## Slide 1: Derivation of RCP/RSP specifications
Where RCP 240 and RSP 180 criteria come from?
Date: 13-14 May 2013
Presented to: ICAO Asia-Pacific RCP/RSP Workshop (Bangkok, Thailand)
By: Tom Kraft tom.kraft@faa.gov

## Slide 2: Introduction
The application of 30 NM and 50 NM longitudinal separation minima are predicated on C, N and S performance
PBCS provides global RCP/RSP specifications for C and S performance supporting this ATM function (GOLD / Doc 9869)
RCP 240 and RSP 180 time criteria were derived from the separation standards for applying these separation minima (contained in Doc 4444)
  This was the “most stringent” scenario
Continuity, availability and integrity criteria were derived from an operational safety assessment (RTCA DO-264/EUROCAE ED-78A)
ATM
RCP
RNP
RSP
S
N
C

## Slide 3: RCP 240 – RSP 180 time requirements
Collision risk modeling (CRM) assumes times for normal means of C and S
Doc 4444 – 30 and 50 NM longitudinal separation
  5.4.2.6.4.3.2 The communication system provided to enable the application of the separation minima in 5.4.2.6.4.3 shall allow a controller, within 4 minutes, to intervene and resolve a potential conflict by contacting an aircraft using the normal means of communication. …
  5.4.2.6.4.3.3 When an ADS-C periodic or waypoint change event report is not received within 3 minutes of the time it should have been sent, the report is considered overdue and the controller shall take action to obtain the report as quickly as possible, normally by ADS-C or CPDLC. …

## Slide 4: Side note – RCP 400 – RSP 400
CRM assumes times for alternative means of C and S based on traditional systems (e.g. HF voice via radio operator); these time criteria can be applied to non-traditional systems (e.g. SATVOICE)
Doc 4444 – 30 and 50 NM longitudinal separation
  5.4.2.6.4.3.2 … An alternative means shall be available to allow the controller to intervene and resolve the conflict within a total time of 10½ minutes, should the normal means of communication fail.
  5.4.2.6.4.3.3 … If a report is not received within 6 minutes of the time the original report should have been sent, and there is a possibility of loss of separation with other aircraft, the controller shall take action to resolve any potential conflict(s) as soon as possible. The communication means provided shall be such that the conflict is resolved within a further 7½ minutes.
  Informal survey of participating ANSPs on when a response is late and when a position report is overdue

## Slide 5: Relationship of RCP/RSP to tau (τ)
CRM uses a communication and controller intervention buffer – referred to as tau (τ) (per Doc 9689, Appendix 5)
RTCA DO-306/EUROCAE ED-122 provides results of analysis to allocate RCP/RSP time criteria from tau (τ) to communication and surveillance components
Tau (τ) for 30 / 50 NM longitudinal separation = 4 minutes (240 seconds); 3 minutes (180 seconds) is derived from Tau (τ)

## Slide 6
Table 5-5 from RTCA DO-306 / EUROCAE ED-122 |  |  | 
Scenario | Normal communication | Non-normal communication | Non-normal surveillance
Value of communication and controller intervention buffer, τ | 240 seconds (4 minutes) | 630 seconds (10½ minutes) | 810 seconds (13½ minutes)
Element related to the PR service Position report delivery time | < 90 seconds Note: Not included in value of τ. | < 90 seconds Note: Not included in value of τ. | 180 seconds Note: Time after which the controller expected the ADS‑C report to have been sent, and was not received.
Time for the controller to recognize the potential conflict and to devise an alternative means of separation | 30 seconds | 30 seconds | Not applicable. Missing report.
Element related to the CRD service Time taken to communicate the instructions to the pilot | Normal means of communication, DCPC (CPDLC) – 105 seconds. Note: Controller message composition -15 seconds; uplink 90 seconds. Normal operations assumes normal means of communication, DCPC (CPDLC) is functioning. Time for the controller to receive and recognize the response to the instruction is not included. | 195 seconds Note: Time after which the controller initiates communication, via normal means, and receives no response. By then, the controller would have initiated communication via alternative means. | 195 seconds Note: Time after which the controller initiates 1st attempt to obtain report, via ADS‑C demand contract and/or CPDLC, and receives no response. By then, the controller would have initiated communication via alternative means.
Time taken to communicate the instructions to the pilot (via alternative means of communication, assumed to be third party voice) | Not applicable | 300 seconds. Note: Time after which the controller initiates communication, via alternative means of communication, and receives no response. By then, the controller would have initiated communication with other aircraft. | 300 seconds Note: Time after which the controller initiates 2nd attempt to obtain report, via alternative means of communication, and receives no response. By then, the controller would have initiated communication with other aircraft.
Time for the pilot to react and initiate an appropriate maneuver | 30 seconds | 30 seconds | 30 seconds
Time for the aircraft to achieve a change of trajectory sufficient to ensure that a collision will be averted | 75 seconds | 75 seconds | 75 seconds
Extra allowance | 0 | 0 | 30 seconds

## Slide 7: CNS/ATM context
Navigation
communications and controller intervention buffer (τ)
Operational communication transaction
ATM context
ATM context
Communication
Surveillance
Surveillance
Communication
Surveillance data
Surveillance data
RSP
RSP
Reduced separation minima
ATM
RCP
RNP
RSP
S
N
C
RNP
RCP
Conflict detectection
Aircraft is safely displaced

## Slide 8: RCP communication transaction time
 | RCP specification (communication transaction time) |  |  |  |  |  |  |  |  | 
RCP | 240 |  |  |  |  |  |  |  |  | RCP
 | Controller composes and sends message | Operational Performance (Monitored) |  |  |  |  |  |  | Controller receives indication and confirms response | 
 |  | Communication transaction time |  |  |  |  |  |  |  | 
99.9% | Part of 30 | 210 |  |  |  |  |  |  | Part of 30 | ET
95% | Part of 30 | 180 |  |  |  |  |  |  | Part of 30 | TT
 |  | RCTP (Ground to Air) |  |  | PORT | RCTP (Air to Ground) |  |  |  | 
99.9% |  | P(150) |  |  | 60 | P(150) |  |  |  | 99.9%
95% |  | P(120) |  |  | 60 | P(120) |  |  |  | 95%
 |  | ATSU system | CSP | Aircraft system |  | Aircraft system | CSP | ATSU system |  | 
99.9% |  | P(15) | P(120) | P(15) |  | P(15) | P(120) | P(15) |  | 99.9%
95% |  | P(10) | P(100) | P(10) |  | P(10) | P(100) | P(10) |  | 95%
Interoperability & functional definition

## Slide 9: RSP surveillance data transit time
 | RSP specification (surveillance data transit time) |  |  |  |  | 
RSP | 180 |  |  |  |  | RSP
 | Time at position (RNP at +/-1 sec UTC) | Operational Performance (Monitored) |  |  | ATSU receives surveillance data | 
 |  | Surveillance data transit time |  |  |  | 
99.9% |  | 180 |  |  |  | OD
95% |  | 90 |  |  |  | DT
 |  | Aircraft system | CSP | ATSU system |  | 
99.9% |  | 5 | 170 | 5 |  | 99.9%
95% |  | 3 | 84 | 3 |  | 95%
X
Event
Interval
Interoperability & functional definition

## Slide 10: RCP continuity
There is no requirement to provide an indication to the controller if a communication transaction exceeds the nominal (TT) time value
If a communication transaction is not completed within the operational (ET) time value, the system is required to provide an indication to the controller for appropriate action
  The frequency at which this indication occurs affects controller workload
  Operational safety assessment classified the effect of “a delayed response to an ATC instruction” as “minor”
  “Minor” equates to a likelihood of occurrence of no greater than 10-3, or a 99.9% success rate

## Slide 11: RSP continuity
There is no requirement to provide an indication to the controller if a surveillance data (position) report exceeds the nominal (DT) time value
If a surveillance data report is overdue (i.e., not delivered within the operational (OD) time value), the system is required to either automatically take action and/or provide an indication to the controller for appropriate action
  The frequency at which this indication occurs affects the latency and accuracy of the surveillance data, which affects conformance monitoring and controller workload
  Operational safety assessment classified the effect of an “overdue surveillance data report” as “minor”
  “Minor” equates to a likelihood of occurrence of no greater than 10-3, or a 99.9% success rate

## Slide 12: RCP – RSP availability (1 of 3)
RCP – RSP availability requirement for aircraft
  Determines number of redundant components; one component can meet 0.999 availability
  Operators can choose different radios (e.g. Iridium SBD, Inmarsat Classic Aero/SBB, HFDL), but the number of radios required is typically specified by operating rules and airspace requirements for voice communications
RCP – RSP availability requirement for communication services
  Assumes that failed data link components within the ANSP would not significantly contribute to loss of the data link service
RCP 240 – RSP 180 availability requirements |  |  | 
Availability parameter | Efficiency | Safety | Compliance means
Service availability (ACSP) | 0.9999 | 0.999 | Contract/service agreement terms
Unplanned outage duration limit (min) | 10 | 10 | 
Maximum number of unplanned outages | 4 | 48 | 
Maximum accumulated unplanned outage time (min/yr) | 52 | 520 | 
Unplanned outage notification delay (min) | 5 | 5 | 
Note.— DO 306/ED 122 specifies a requirement to indicate loss of the service. Unplanned outage notification delay is an additional time value associated with the requirement to indicate the loss to the ATS provider per the RCP/RSP related safety requirement (SR) 4 for the ANSP. |  |  | 

## Slide 13: RCP – RSP availability (2 of 3)
If communication or surveillance service is lost, some form of action will be necessary
  Frequency at which service is lost could affect the application of separation minima being applied when service is lost
  It may be necessary to apply a different form of separation
  Operational safety assessment classified the effect of “loss of service” as “minor”
  “Minor” equates to a likelihood of occurrence of no greater than 10-3, or 99.9% of the time services would be available

## Slide 14: RCP – RSP availability (3 of 3)
The “availability of service” requirement is calculated based on 24/7 operation, given a 12 month period of operation
  24/7 = 168 hours per week x 52 weeks per year = 8736 hours or 524,160 minutes
  99.9% (for safety) available service allows 0.001 “down time” or 524 minutes/year of a 24/7 operation
  99.99% (for efficiency) available service allows 0.01 “down time” or 52.4 minutes/year of a 24/7 operation.
Down time due to planned maintenance is not included

## Slide 15: RCP – RSP integrity (1 of 2)
The operational RCP – RSP integrity requirements are specified in terms of likelihood of malfunction
  Likelihood of failure per flight hour, instead of quality of service
RCP – RSP allocations are specified in terms of safety requirements for the components of the operational system
  Integrity is not allocated like time parameters, since integrity is achieved through system design, architecture and supporting analysis (e.g. cyclic redundancy checks and flight plan correlation with logon, information
  System integrity issues discovered post-implementation should be reported to the appropriate Regional/State monitoring agency and/or authorities for appropriate action
RCP 240 – RSP 180 availability requirements |  | 
Integrity parameter | Integrity value | Compliance means
Integrity (I) | Malfunction = 10-5 (per flight hour) | Analysis, safety requirements, development assurance level commensurate with integrity level, (compliance shown prior to operational implementation). See also RCP related safety requirement SR‑26 for the ATSP. CSP contract/service agreement. See also RCP integrity criteria for CSP, paragraph B.2.1.2.

## Slide 16: RCP – RSP integrity (2 of 2)
There usually is no operational visibility of communication or surveillance services that do not meet integrity requirements
  RCP – RSP integrity ensures that the effects of malfunction of communication or surveillance services are adequately mitigated in design and implementation
  The mitigation strategy take the form of safety and performance requirements allocated to system components, which are qualified prior to operation
  Operational safety assessment classified the effects of undetected message corruption, mis-delivery and other misleading anomalous system behavior as “major”
  “Major” equates to a likelihood of occurrence of no greater than 10-5 probability of malfunction per flight hour
For RSP integrity, in addition to addressing undetected corruption of data in delivery, the requirements include criteria for accuracy of navigation position data and time at the position provided in the surveillance data (e.g., RNP 4 at +/- 1 second UTC)

## Slide 17: Conclusion
Doc 4444, 5.4.2.6.4.3.2 and 5.4.2.6.4.3.3, provide C and S time criteria for applying 30 NM and 50 NM longitudinal separation minima (CRM)
Continuity, availability and integrity criteria are derived from an operational safety assessment (per DO-264/ED-78A)
Based on RCP and RSP specifications, PBCS enables ANSPs to ensure C and S system performance meets these time criteria to safety apply these separation minima