## Slide 1: RCP / RSP
Airbus perspective
Presented by
Jerome CONDIS / FANS Projects (all program)

## Slide 2: Agenda
Demonstration of compliance with RCP/RSP specifications
  Avionics configuration and certification
  Demonstration strategy
    Availability, integrity and continuity
    Time
Configuration Management of FANS certification
Operational notion of RCP/RSP in the cockpit

## Slide 3: Airbus FANS avionics architecture

## Slide 4: Controls & Indications common to
FANS A+ and B+
A320/A330/A340

## Slide 5: Controls & Indications common to
FANS A+ and B+
Commonality with A320/330/340 operating principles
A350/A380 Cockpit interactivity
=
More efficient workflow
A380/A350

## Slide 6: Demonstration of compliance with RCP/RSP
For latest FANS 1/A+ (resp. FANS B+) developments, ED-122/DO-306 (resp. ED-120/DO-290) specifications are used as a basis
  Demonstration that RCP/RSP allocations to the Aircraft are met are part of the aircraft FANS function airworthiness approval
ATC Data Link systems and FANS function certification are required but not sufficient to operate FANS on an aircraft
  Operational approval, under operator responsibility, is required
  Conditions of use may affect the actual performance of the avionics equipment (e.g. if significantly different from assumptions taken for avionics certification)
Tests are made using a representative ground ATC simulation
  Some end-to-end tests are performed with real ground ATC systems, but not exhaustively of course

## Slide 7: Demonstration of compliance with RCP/RSP
Demonstration strategy
    Availability, integrity and continuity requirements
    Basically by demonstrating :
  Fulfilment of the Safety Requirements
  Adherence the minimum required Development Assurance Level process (to meet Safety Objectives)
  FANS function continuity requirement supported by compilation of qualified failure rates for equipment involved in the function

## Slide 8: Demonstration of compliance with RCP/RSP
Demonstration strategy
    Time
    Aircraft contribution to the Transaction Time is allocated to each contributing avionics equipment to the function, e.g.:
  From Comm Means up to Display Systems for uplink processing
  From Generating Systems (e.g. FMS) up to Comm Means for downlink report sending
    Actual time performance of the avionics chain is compiled to ensure compliance with Aircraft requirements from ED-122 / DO-306 and/or ED-120 / DO-290
    Additionally, for major changes to the function, end-to-end tests using real networks (in lab and/or in flight) are performed to ensure overall good behaviour and compliance with expected performance requirements

## Slide 9: Configuration Management of FANS certification
FANS certification is maintained up to date
  Each time an equipment contributing to the function is upgraded
  Each time a new equipment contributing to the function is added
Note: This only applies when the change is supported by an aircraft MOD approved by Airbus.
Any potential effect on Safety, Performance, Interop and/or HMI qualification is assessed
  If any impact is identified, the FANS function airworthiness is reassessed
  New approval is requested including the new or upgraded equipment contribution

## Slide 10: Operational notion of RCP/RSP in the cockpit
NONE
Aircraft is providing the flight crew with alerts in case of equipment/capability failures, e.g.
  Comm Means failure (e.g. SATCOM FAULT)
  Definitive connectivity loss (e.g. VHF3 DATALINK FAULT)
  Failure of ATC Data Link (e.g. ATC DATA LINK FAULT)
  BUT
There is no consolidated RCP/RSP capability directly displayed to the flight crew
  Appropriate procedures (refer to GOLD) and associated training shall be in place to ensure adherence with RCP/RSP monitoring requirements

## Slide 11
QUESTIONS ?