## Slide 1: APAC SIP on ASBU B0-FICE AIDC Implementation Seminar Basic SYSCO Principles and Standard OLDI Communication EUR Environment
ICAO EUR/NAT Office
Celso Figueiredo – Regional Officer ANS - ATM
Bangkok, Thailand
28 to 31 October2014

## Slide 2
By the end of the Presentation you will have a:
  basic understanding of the need for exchange of data in Air Traffic Control (ATC);
  an overview of SYSCO standard co-ordination and basic transfer messages as they are used in most ATM systems;
  understanding of SYSCO terminology;
  definition of Standard OLDI message types;
  purpose of Standard OLDI messages;
  timing of the transmission of Standard OLDI messages;
  system responses to Standard OLDI messages.

## Slide 3
What’s OLDI? 1
  Flights which are being provided with an ATC service are transferred from one ATC unit to the next in a manner designed to ensure complete safety.
  In order to accomplish this, it is a standard procedure that the passage of each flight across the boundary of the areas of responsibility of the two units is co-ordinated between them before the flight reaches the boundary.
  In OLDI, and in the ATM systems, we call this process the Coordination Phase.

## Slide 4
What’s OLDI? 2
  After the receipt of coordination information, the receiving controller uses this information to provide view of the traffic in relation to other aircraft and airspace features.
  When the flight arrives at, or adjacent to, the boundary between the ATC units, control of the flight is transferred to the next unit.
  In OLDI, and in the ATM systems, we call this the Transfer Phase.

## Slide 5
What’s OLDI? 3
When carried out by telephone, the passing of data on individual flights is a major support task at ATC units.
The operational use of connections between Flight Data Processing Systems (FDPS) at ACCs replaces such verbal “estimates”.
This can be achieved using ICAO messages sent by AFTN. This process is supported by most ATM systems.
AFTN messages allow for a limited flow of standard data between ATC units. The requirement for an increase in the data transfer requirements led to the development of On-Line Data Interchange (OLDI) within Europe in the early nineteen eighties.

## Slide 6
What’s OLDI? 4
In order to facilitate implementation, common rules and message formats were elaborated and agreed by the agencies concerned and incorporated in the EUROCONTROL Standard for On-Line Data Interchange.
This process is also referred to as SYSCO (System Assisted Coordination).
The OLDI standard is produced to support the continuing development of such facilities in compliance with the requirements of EATCHIP1.
    1 EUROCONTROL ATC Harmonization and Integration Programme

## Slide 7
SYSCO, brief description
System Assisted Co-ordination (SYSCO) is a EUROCONTROL protocol for co-ordination and transfer between controllers.
In the ATM systems the protocol is used between ATC centers and between ATC sectors.
OLDI stands for: On Line Data Interchange.

## Slide 8
OLDI Messages
OLDI messages are exchanged between ATC units to provide co-ordination and transfer of control information.
We will now look at the terminology used in most ATM systems during the co-ordination and transfer process.

## Slide 9
SYSCO/OLDI Definitions
Co-ordination Entry/Exit Point (COP in/out)
Is the agreed point, on or adjacent to the boundary between ATC areas of responsibility, used in a co-ordination sequence and referred to in co-ordination messages.
In the ATM systems these points are qualified depending on whether they are viewed as an exit ‘COP in’ or entry ‘COP out’ point.
Transfer Flight Level (TFL)
This is the level used in co-ordination messages as the level that the flight will be cleared to when transferring from one controller to another.
In the ATM systems this level is qualified depending on whether it is viewed as the exit ‘XFL’ level or planned entry ‘PEL’ level.

## Slide 10
SYSCO/OLDI Definitions
Cleared flight Level (CFL)
  Is the level that the pilot is currently instructed to fly at. It may be different to the TFL mentioned above, but should normally be the same as the TFL when the flight is handed over to the next controller.
Assigned Speed (ASP)
  Is the speed (indicated airspeed – IAS, or Mach number) that the pilot is currently instructed to fly at. It is used by controllers to maintain the required separation between flights.
Assigned Heading (AHDG) –
  Is the heading, in degrees magnetic, that the pilot is currently instructed to fly.

## Slide 11
We will now look at the OLDI messages and their purpose.

## Slide 12
OLDI Messages Definitions
ABI Advance Boundary Information Message
  Initial notification and updates flight plan information
ACT Activate Message
  Automatic update of FPL data with estimate information
PAC Preliminary Activate Message
  Notification and pre-departure co-ordination where flight time to COP is too short for ACT message
REV Revision Message
  To transmit revisions to co-ordination data (time, level, code, COP)
LAM Logical Acknowledgement Message
  Automatically generated message by receiver to indicate receipt of transmitted message.

## Slide 13
OLDI Messages Definitions
TIM Transfer Initiation Message
  At the end of the co-ordination phase, to signify the change from Coordination to Transfer phase. Includes control data (CFL, AHDG, ASP)
SDM Supplementary Data Message
  To transmit changes to control data during the Transfer Phase (updates TIM data)
COF Change of Frequency Message
  Sent by transferring controller to indicate flight has been instructed to change frequency
MAS Manual Assumption of Communications Message
  Message to the transferring unit to indicate two-way RTF contact has been established with the flight

## Slide 14
Basic OLDI procedure.

## Slide 15
Prior to FIR entry
  At a predefined number of minutes prior to the COP, an ABI is sent.
FIR (first sector)
Provides:
- Missing FPL data
- ABI + revisions
- SSR code to facilitate
early correlation
ABI
SP time
FIR boundary

## Slide 16
  LAM is returned.
If the information sent in the ABI needs to be updated, it is achieved by sending another ABI message containing the revised data.
What is sent in response?

## Slide 17
Prior to FIR entry
  At a predefined number of minutes or distance prior to the COP, an ACT is sent. (coord. phase)
Airspace (sector)
Provides:
- Coordination data
- Performs SSR code
retention check
- code/callsign
correlation
ACT
SP time/
distance
FIR boundary

## Slide 18
  LAM is returned.
What is sent in response?

## Slide 19
What if the aircraft departs from too close to the COP to allow an ACT to be sent?
FIR boundary
SP time/
distance

## Slide 20
Close to FIR entry
  A PAC is used. A PAC replaces the ABI and/or ACT.
Airspace (sector)
Provides:
- notification or pre-departure coordination
- missing flight plan data
Can contain a SSR code request
PAC
ACT time/
distance
FIR boundary

## Slide 21
If the information sent in the PAC message provides an update of ETD but does not include coordination data it is treated like an ABI on reception.
If the PAC message contains coordination data (COP, ETO and TFL) it is treated similar to an ACT on reception.
PAC Messages

## Slide 22
What if revisions to coordination are required?
FIR boundary
FL 290
FL 310
t1
t0

## Slide 23
Revision of coordination required
  A REV is used.
Airspace (sector)
Provides:
Automatic notification of:
- Code/RVSM change
- Transfer level change
- ETO at the COP change
- Can also change route /
COP
REV
FIR boundary

## Slide 24
  LAM is returned and a FPL created if the sector responsible for the control of the flight can be identified.
What is sent in response?

## Slide 25
Transfer of Communication and Control

## Slide 26
Transfer initiation
  At a predefined distance or time prior to the COP, a TIM is sent. If distance and time are set to 0,
  TIM is not automatically sent.
Airspace (sector)
Signifies:
- end of coordination phase
- start of transfer phase
- forwards Executive Control data (AHDG, CFL, ASP) to the accepting controller
TIM
SP time/
distance

## Slide 27
  Not before the flight has been coordinated.
  Automatically at a (SP) distance/time from COP out.
  When the above SP’s are set to ‘0’, the TIM is not automatically sent.
  Regardless of the SP, TIM message sending is also triggered when on certain controller actions that will be covered later.
  A TIM is acknowledged by a LAM.
What is sent?

## Slide 28
Transfer initiation
  After the TIM, any changes to specific FDR fields result in a SDM being sent.
Airspace (sector)
Notifies changes for which approval is not required:
- CFL
- ASP
- AHDG
SDM
SP

## Slide 29
  COF is sent.
What is the last step?

## Slide 30
Transfer Completion
  A COF is sent on controller ‘Transfer’ input (not an automatic function).
Airspace (sector)
- Manually initiated
- A TIM is also sent if COF sent before the automatic TI event or if SPs for TIM sending are set to ‘0’
COF

## Slide 31
  LAM is returned.
What is sent in response?

## Slide 32
  MAS may be manually initiated by the accepting controller.
And finally…
  Not mandatory if a COF is used.
  Acknowledged by a LAM.

## Slide 33
Transfer Completion
  A MAS is sent on controller ‘Assume’ input.
Airspace (sector)
- Manually initiated
MAS

## Slide 34
Standard OLDI Messages
REV
SDM
COF
MAS
ABI/PAC
TIM
ACT/PAC
LAM
LAM
A
B
A
B
LAM
LAM
LAM
LAM
LAM
Transfer Phase
Coordination
Phase
Notification
Phase

## Slide 35
  Here is the process for handling OLDI messages.
OLDI Message Reception

## Slide 36
  On reception a syntax check is performed.
    If error, put in OLDI Queue for manual processing.
  After syntax check a semantic check is performed.
    If error, put in OLDI Queue for manual processing.
  In both cases LAM is not sent.
  When no error, further processing takes place :
    LAM sent: associate with previous message or
    if no previous message, a warning is displayed.
OLDI Message Reception

## Slide 37
  No error - associated processing performed.
    Successful - Acknowledgement message sent.
    Successful: ABI, PAC, ACT - system tries to retrieve first controlling sector.
      sector determined, acknowledgement message sent.
      sector cannot be determined, message put in OLDI Queue, no acknowledgement message sent.
    Unsuccessful Other - put in OLDI Queue, no acknowledgement message sent.
OLDI Message Reception

## Slide 38
  Basic SYSCO Principles and Standard OLDI Communication.
That completes: