Model Regulation on Ground Proximity Warning System (GPWS)

Citation and commencement

1. - 	(1)	These Regulations are made under [insert primary legislation].

(2) 	These Regulations may be cited as [insert name of regulations] and shall come into force on [date].

Applicability

2. - 	(1)	These Regulations shall apply to all operators engaged in international commercial air transport operations or international general aviation operations.

Definitions

3. - 	(1)	In these Regulations, unless the context otherwise requires –

“aeroplane” means a power-driven heavier-than-air aircraft, deriving its lift in flight chiefly from aerodynamic reactions on surfaces which remain fixed under given conditions of flight;

“aircraft” means any machine that can derive support in the atmosphere from the reactions of the air other than the reactions of the air against the earth’s surface;

“commercial air transport operation” means an aircraft operation involving the transport of passengers, cargo or mail for remuneration or hire;

“general aviation operation” means an aircraft operation other than a commercial air transport operation or an aerial work operation;

“Operations manual” means a manual containing procedures, instructions and guidance for use by operational personnel in the execution of their duties;

“operator” means a person, organisation or enterprise engaged in or offering to engage in an aircraft operation.

Aeroplanes to be equipped with ground proximity warning system (GPWS)

4. - 	(1)	No operator shall operate, for the purpose of commercial air transport, a turbine-engined aeroplane of a maximum certificated take-off mass in excess of 5,700kg or that is authorised to carry more than nine passengers unless that aeroplane is equipped with a ground proximity warning system which has a forward looking terrain avoidance function and that meets the requirements in sub-paragraphs (5) and (6).

- No operator shall operate, for the purpose of commercial air transport, a piston-engined aeroplane of a maximum certificated take-off mass in excess of 5,700kg or that is authorised to carry more than nine passengers, unless that aeroplane is equipped with a ground proximity warning system which provides the warnings specified in sub-paragraphs (6)(a) and (6)(c), a warning of unsafe terrain clearance and a forward looking terrain avoidance function.

- No operator shall operate, for the purpose of general aviation, a turbine-engined aeroplane –

(a)	of a maximum certificated take-off mass in excess of 5,700kg; or

(b)	that is authorised to carry more than nine passengers

for which the certificate of airworthiness was first issued on or before 1 January 2011 unless that aeroplane is equipped with a ground proximity warning system which has a forward looking terrain avoidance function and that meets the requirements in sub-paragraph (7).

- No operator shall operate, for the purpose of general aviation, a turbine-engined aeroplane –

(a)	of a maximum certificated take-off mass in excess of 5,700kg; or

(b)	that is authorised to carry more than nine passengers

for which the certificate of airworthiness was first issued after 1 January 2011 unless that aeroplane is equipped with a ground proximity warning system which has a forward looking terrain avoidance function and that meets the requirements in sub-paragraph (6).

- A ground proximity warning system referred to in sub-paragraphs (1), (2), (3) and (4) shall provide automatically a timely and distinctive warning to the flight crew when the aeroplane is in potentially hazardous proximity to the earth’s surface.

- A ground proximity warning system referred to in sub-paragraphs (1), (2) and (4) shall provide, unless otherwise specified in this paragraph, warnings of the following circumstances:

(a)	excessive descent rate;

(b)	excessive terrain closure rate;

(c)	excessive altitude loss after take-off or go-around;

(d)	unsafe terrain clearance while not in landing configuration:

(i)	gear not locked down

(ii)	flaps not in a landing position; and

- excessive descent below the instrument glide path.

(7)	A ground proximity warning system referred to in sub-paragraph (3) shall provide, at a minimum, warnings of at least the following circumstances:

  - excessive descent rate

  - excessive altitude loss after take-off or go-around; and

  - unsafe terrain clearance

(8)	The Operations Manual or Airplane Flight Manual, or both, maintained by the operator shall contain instructions and training requirements, including appropriate procedures for:

- the use of the ground proximity warning system; and

- proper flight crew reaction in response to the ground proximity warning system audio and visual warnings.