## Slide 1: Aviation System Block Upgrades Module N° B0-102 Increased Effectiveness of Ground-Based Safety Nets
SIP/2012/ASBU/Nairobi-WP/24G
Workshop on preparations for ANConf/12 − ASBU methodology
(Nairobi, 13-17 August 2012)

## Slide 2: Module N° B0-102: Increased Effectiveness of Ground-Based Safety Nets
Summary | To monitor the operational environment during airborne phases of flight, safety nets provide timely alerts on the ground. | 
Main Performance Impact | -10 Safety | 
Operating Environment/Phases of Flight | All airborne flight phases | 
Applicability Considerations | Benefits increase whilst traffic density and complexity increase. Not all ground-based safety nets are relevant for each environment. Deployment of this module should be accelerated. | 
Global Concept Component(s) | CM – Conflict Management | 
Global Plan Initiatives | -9 Situational awareness -16 Decision support and alerting systems | 
Main Dependencies | None | 
Global Readiness Checklist |  | Status (ready now or estimated date)
 | Standards Readiness | Not applicable
 | Avionics Availability | Ready now
 | Ground Systems Availability | Ready now
 | Procedures Available | Ready now
 | Operations Approvals | Ready now

## Slide 3: Module N° B0-102 Baseline
None

## Slide 4: Module N° B0-102 – Change Brought by the Module
  Element 1  Short Term Conflict Alert (STCA)
  preventing collision between aircraft by generating an alert of a potential or actual infringement of separation minima
  Element 2  Area Proximity Warning (APW)
  Warn the controller about unauthorised penetration of an airspace volume by generating an alert of a potential or actual
  Element 3  Minimum Safe Altitude Warning (MSAW)
  Warn the controller about risk of controlled flight into terrain accidents by generating an alert of aircraft proximity to terrain or obstacles.

## Slide 5: Module N° B0-102 – Intended Performance Operational Improvement
Safety | Significant reduction of the number of major incidents.
CBA | The business case for this element is entirely made around safety and the application of ALARP (As Low As Reasonably Practicable) in risk management.

## Slide 6: Module N° B0-102 – Necessary Procedures (Air & Ground)
The relevant PANS-ATM (Doc 4444) provisions exist.

## Slide 7: Module N° B0-102 – Necessary System Capability
Avionics
  Aircraft should support cooperative surveillance using existing technology such as Mode C/S transponder or ADS-B Out.
Ground Systems
  Surveillance services must be equipped with Short Term Conflict Alert, Area Proximity Warnings and Minimum Safe Altitude Warnings

## Slide 8: Module N° B0-102 – Training and Qualification Requirements
Controllers must receive specific ground-based safety nets training and be assessed as competent for the use of the relevant ground-based safety nets and recovery techniques.

## Slide 9: Module N° B0-102 – Regulatory/standardization needs and Approval Plan (Air & Ground)
Nil

## Slide 10: Module N° B0-102 – Reference Documents
Standards
  EUROCONTROL Specifications for STCA, APW, MSAW and APM, available at http://www.eurocontrol.int/safety-nets
Procedures
  PANS-ATM (Doc 4444), section 15.7.2 and 15.7.4
Guidance Material
  EUROCONTROL Guidance Material for STCA, APW, MSAW and APM, available at http://www.eurocontrol.int/safety-nets
  Approval Documents- Nil

## Slide 11: Module N° B0-102 Implementation - Benefits and Elements
Increased Effectiveness of Ground-Based Safety Nets
Benefits - Main Key Performance Areas (KPA) |  |  |  |  | 
KPAs | Access | Capacity | Efficiency | Environment | Safety
Applicable | N | N | N | N | Y
Elements
      - Short Term Conflict Alert (STCA)
      - Area Proximity Warning (APW)
      - Minimum Safe Altitude Warning (MSAW)
  To be reflected in ANRF