International Civil Aviation Organization

Caribbean and South America Office

(Presented by USA/FAA)

Interface Control Document

For Aeronautical Telecommunication Network (Atn) Ground-Ground Router in the Caribbean and South America Regions

Version 0.1

Contents

1.0	SCOPE	3

1.1	Reference Documents	3

1.2	Applicable Documents	3

1.2.1	Internet Standards	3

2.0	INTERFACE DESIGN CHARACTERISTICS	4

2.1	General Characteristics	4

2.1.1	Protocol Implementation	4

3.0	Functional Design Characteristics	5

3.1	Functional Design Characteristics	5

3.1.1	Network Interface Layer	5

3.1.2	Internet Layer	5

3.1.3	Transport Layer	6

List of Figures

Figure	Page

Figure 1-2:  TCP/IP Layer Model	5

# SCOPE

This document provides ATN Ground to Ground router ICD guidelines for the routers that form nodes of the CAR/SAM regional network Backbone.  This ICD addresses the Physical, Link, and Internet layers of the ATN G/G router using the TCP/IP model.

## Reference Documents

The following documents are reference documents applicable to the CAR/SAM Regional Router ICD for ATN G/G Router.  These documents do not form a part of this ICD and are not referenced within the document.

## Applicable Documents

The following documents form a part of this ICD to the extent specified herein.  In the event of a conflict between the documents referenced herein and the contents of this ICD, the contents of this ICD shall be the superseding requirements

### Internet Standards

RFC-791 Internet Protocol, September 1981

RFC-796 Address Mappings, September 1981

RFC-793 Transmission Control Protocol, September 1981

RFC 894 Standard for the Transmission of IP Datagrams over Ethernet

Networks, April 1984

RFC-2464 Transmission of IPv6 Packets over Ethernet Networks,

December 1998

RFC-2427 Multiprotocol Interconnect over Frame Relay (FR), September 1998

RFC-2590 Transmission of IPv6 Packets over Frame Relay Networks Specification, May 1999

RFC-2460 Internet Protocol, Version 6 (IPv6) Specification, December 1998

RFC-2373 IP Version 6 Addressing Architecture

RFC-950 Internet Standard Subnetting Procedure, August 1985

RFC-2784 Generic Routing Encapsulation (GRE), March 2000

RFC-2473 Generic Packet Tunneling in IPv6 Specification, December 1998

RFC-3168 The Addition of Explicit Congestion Notification (ECN) to IP, September 2001

# INTERFACE DESIGN CHARACTERISTICS

This section provides the general functional and physical design characteristics for the interfacing communication devices.

## General Characteristics

The ATN G/G routers are Commercial of the Shelf (COTS) routers that can be easily procured and implemented.  The use of these routers with a TCP/IP implementation of the Automatic Message Handling System (AMHS) (RFC1006) will tremendously decrease the time of deployment and final implementation of the AMHS in the CAR/SAM regions.

### Protocol Implementation

The general requirements for the ATN G/G router cover the lower three layers of the TCP/IP four-layer model. The TCP/IP model defines a four-layer network model as shown in Figure 1-2.  Only the lower three layer is cover under this document.

Figure 1-2:  TCP/IP Layer Model

# Functional Design Characteristics

This section describes the functional requirements of this interface.

## Functional Design Characteristics

### Network Interface Layer

The network interface layer handles the hardware details or the physical interfacing to the transmission medium (e.g., cable, radio link). It provides the mechanical, electrical, functional, and procedural methods necessary to activate, maintain, and deactivate physical connections for data links.

The following standards are allowable physical interface implementations in the CAR/SAM regions are described in the following paragraphs.

#### TIA/EIA-232-E/F

The TIA/EIA-232-E/F should be implemented according to TIA/EIA-232-E/F documents.

#### TIA/EIA-530-A

The TIA/EIA-530-A should be implemented according to TIA/EIA-530-A document.

#### V.35

The V.35 should be implemented according to ITU-T V.35 document.

#### Ethernet

Transmission of IPv4 datagrams over Ethernet networks should be in accordance with RFC 894. IPv6 based networks should conform to RFC-2464.

#### Frame Relay (FR)

Transmission of IPv4 datagrams over Frame Relay should be done in accordance with RFC-2427.

Transmission of IPv6 datagrams over Frame Relay should be done in accordance with RFC-2590.

### Internet Layer

The Internet layer specifies the protocols that provide services corresponding to the internet layer. The protocol used in this layer for the CAR/SAM shall be Internet Protocol (IP). IP is designed for use in interconnected packet-switched computer communication networks and provides addressing and fragmentation services.

#### Internet Protocol

Two versions of this protocol shall be allowable for the CAR/SAM – the commonly available IPv4, and the upcoming IPv6 .

IPv4 implementations shall be in accordance with RFC-791.

IPv6 implementations shall be in accordance with RFC-2460.

#### Network addressing

Network addressing should be in accordance with RFC-796 for IPv4 implementations.  IPv6 implementations in the CAR/SAM should be in accordance with RFC-2373.

#### Subnet extensions

Subnet extensions to the addressing architecture for IPv4 networks should be in accordance with RFC-950.

#### Tunneling over IPv4

Tunneling of datagrams (e.g., CLNP, ES-IS) over IPv4 should be done in accordance with RFC-2784.

#### Tunneling over IPv6

Tunneling of datagrams (e.g., CLNP, ES-IS) over IPv6 should be done in accordance with RFC-2473.

### Transport Layer

The transport layer provides communication session management between host computers. It defines the level of service and status of the connection used when transporting data. Transport protocols regulate flow, detect and correct errors, and multiplex data, on an end-to-end basis.

#### Transmission Control Protocol (TCP)

Implementations of TCP shall be in accordance with RFC-793 and RFC-3168.

Appendix A - Acronyms

Acronyms

This appendix defines the acronyms used in this document.

| A/G | Air-Ground |
| --- | --- |
| AAC | Aeronautical Administrative Control |
| ABM | Asynchronous Balanced Mode |
| AIDC | ATS Interfacility Data Communications |
| AMHS | ATS Message Handling System |
| AOC | Aeronautical Operational Control |
| APC | Aeronautical Passenger Communication |
| APRLs | ATN Protocol Requirement Lists |
| ATN | Aeronautical Telecommunications Network |
| ATS | Air Traffic Service |
| ATSC | Air Traffic Service Control |
| CLNP | Connectionless Network Protocol |
| CLNS | Connection-Less Network Service |
| CPDLC | Controller Pilot Data Link Communications |
| DCE | Data Circuit-terminating Equipment |
| DM | Disconnected Mode |
| DTE | Data Terminal Equipment |
| E/R | Error Report |
| EIA | Electrical Industry Association |
| ERD | End Routing Domain |
| ES | End System |
| FIB | Forwarding Information Base |
| FSM | Finite State Machine |
| G-G(G/G) | Ground-Ground |
| ICAO | International Civil Aviation Organization |
| ICD | Interface Control Document |
| IDRP | Inter Domain Routing Protocol |
| IEC | International Electrotechnical Commission |
| ISO | International Standardization Organization |
| ITU | International Telecommunications Union |
| ITU-T | ITU Telecommunications Sector |
| LAPB | Link Access Procedure Balanced |
| NET | Network Entity Title |
| NPDU | Network Protocol Data Unit |
| NSAP | Network Service Access Point |
| OSI | Open Systems Interconnection |
| PDU | Protocol Data Unit |
| PIB | Policy Information Base |
| PICS | Protocol Implementation Compliance Statement |
| PSDN | Public Switched Data Network |
| PSN | Packet Switched Network |
| PVC | Permanent Virtual Circuit |
| QOS | Quality of Service |
| RD | Routing Domain |
| RDC | Routing Domain Confederation |
| RIB | Routing Information Base |
| SARPs | Standards and Recommended Practices |
| SNDCF | Sub Network Dependent Convergence Functions |
| SNPA | Sub Network Point of Attachment |
| SVC | Switched Virtual Circuit |
| TBD | to be Determined |
| TBR | to be Reviewed |