## Slide 1
Regional Activities for ADS-B
ASIA/PAC Region
April 2011
Yeo Cheng Nam
Director (Aeronautical
Telecommunications & Engineering)

## Slide 2: Contents
Applications for ADS-B
Regional Activities Overview
Equipage of Singapore Registered Operators

## Slide 3: Applications for ADS-B
Ground Surveillance Applications
  To enhance ATS in non-radar areas
    Reduce separation
    Enhance situation awareness
  To enhance ATS in radar areas
    Faster update rate available
    Back up existing radars
  Airport surface surveillance
  To support ATC tools
    More timely ATC alerts
  For verification of radar accuracy
  For monitoring of NTZ
Notes: Not all applications are approved as on now. But the potential is there.

## Slide 4: Applications for ADS-B
Aircraft to Aircraft Surveillance Applications
  Enhance traffic situational awareness on the airport surface
  Enhance visual separation on approach
  In trail procedures in oceanic airspace
  Enhance traffic situational awareness during flight operations
  Enhance sequencing operations
Notes: In trail procedure is a procedure whereby ADS-B enabled aircraft can climb and descend through otherwised blocked flight levels.

## Slide 5: Regional Activities Overview
States and ANSPs covered under the overview
  Australia
  Brunei Darussalam
  China
  Fiji
  Hong Kong. China
  Indonesia
  Malaysia
  Myanmar
  New Caledonia
  Pakistan
  The Philippines
  Republic of Korea
  Singapore
  Chinese Taipei
  Thailand
  USA
  Viet Nam

## Slide 6: Australia (Upper Airspace Project)
Installed 29 ADS-B Stations:
  Thursday island, Gove, Doongan, Broome, Karratha, Mornington Island, Tennant creek, Balgo, Telfer, Newman, Meekatherra, Bilabong, Leonora, Warburton, Ayers rock, Alice Spring, Mt Isa, Esperance, Caiguna, Nullabor, Woomera, Birdsville, Broken hill, Jackson, Bourke, Longreach, Bundaberg, Oodnadatta, Lord Howe Island
Receiving data from 4 Indonesian Stations:
  Kintamani, Waignapu, Saumlaki, Merauke

## Slide 7: Australia (Upper Airspace Project)
UAP has been commissioned & operational
Applicable of 5NM separation using ADS-B from operational sites.
Coverage is currently available across the whole continent from 29 ADS-B sites, 1 WAM and 4 from Indonesia.

## Slide 8: Australia (Wide Area Multi-Lateration)
Installed WAM in:
  Tasmania with 14 receivers.
  Sydney with 16 receivers.

## Slide 9
Thursday Island
Doogan
Broome
Karratha
Mornington Island
Tennany Creek
Billabong
Telfer
Newman
Meekatharra
Leonora
Warburton
Ayers Rock
Alice Spring
Mt Isa
Esperance
Caiguna
Birdsville
Jackson
Bourke
Longreach
Broken Hill
Bundaberg
Tasmania
Balgo
Woomera
Nullabor
Oodnadatta
Gove
Merauke
Saumlaki
Waignapu
Kintamani
Lord Howe
Sydney

## Slide 10: Brunei Darussalam
Plan to install an ADS-B station to backup ATC surveillance system
Brunei
Information correct as of Feb 2009

## Slide 11: China
To install ADS-B ground stations at:
  Lhasa Kanbala, Lhasa Airport, Linzhi Airport, Changdu Damala and Kangding Airport
Civil Aviation Flight University of China (CAFUC):
  Installed 7 ADS-B stations
  Equipped ADS-B on about 160 aircrafts
Installed ADS-B trial ground stations in:
  Chengdu and Jiuzhai
Installed ADS-B ground station within Sanya FIR
Information correct as of Apr 2011

## Slide 12
Lhasa Kambala
Linzhi Airport
Kangding Airport
Chengdu
Changdu Damala
Jiuzhai
Xisha
Lhasa Airport

## Slide 13: Fiji
New ATM system (AURORA) installed and in operation in Nadi ATM Centre
Installed 11 ADS-B ground stations (3 of them with interrogators)
Issue ADS-B equipage mandate for aircraft operating in controlled airspace with effect from 20 Dec 2013
Only 3 of the 45 Fiji-registered aircrafts are ADS-B equipped, the rest are expected to be equipped after Dec 2013
Information correct as of Feb 2011

## Slide 14: Hong Kong, China
Plan to install an ADS-B station
Mandate ADS-B carriage by end 2013
  for aircraft flying over L642/M771
Mandate ADS-B carriage by end 2014
  for all aircraft flying within the Hong Kong FIR
Mandate ADS-B carriage after 2015 (TBC)
  for low flying aircraft, including general aviation aircraft and helicopters.
Information correct as of Aug 2010

## Slide 15
Hong Kong

## Slide 16: Indonesia
Installed 30 ADS-B Stations in (as of Feb 2011):
  Banda Aceh, Medan, Pekanbaru, Palembang, Matak, Natuna, Soeta Jakarta, Tarakan, Cilacap, Kintamani, Pontianak, Pangkalan Bun, Palu, Makassar, Waingapu, Kupang, Alor, Ambon, Sorong, Merauke, Saumlaki, Galela, Manado, Biak, Timika, Kendari, Surabaya, Semarang, Banjarmasin and Balikpapan.
Receiving data from 4 Australian ADS-B Stations
  Broome, Doogan, Gove, Thursday Island
Information correct as of Feb 2011

## Slide 17: Indonesia
Plans:
  To set up ADS-B Implementation Team Task Force for ADS-B Planning.
  In short term, DGCA Indonesia has a plan to use ADS-B for ATC Situational Awareness in Makassar Air Traffic Service Center (MATSC).
  Cross FIR Operational Data Sharing as the initial application of ADS-B Services in Indonesia.
  After successful implementation of ADS-B for situational awareness, Indonesia will implement ADS-B for provision of separation services.
Information correct as of Feb 2011

## Slide 18
B Aceh
Medan
Pekanbaru
Palembang
Soeta Jakarta
Cilacap
Surabaya
Pangkalan Bun
Pontianak
Matak
Natuna
Tarakan
Palu
Makassar
Makassar
Waingapu
Kupang
Alor
Kendari
Manado
Galela
Ambon
Sorong
Biak
Saumlaki
Timika
Merauke
Thursday Island
Gove
Doogan
Broome
Banjarmasin
Semarang
Balikpapan

## Slide 19: Malaysia
Installed Multi-lateration and ADS-B in Terengganu Airport (commissioned end-2009).
To upgrade ATM system by Sep 2011 to integrate with ADS-B.
Information correct as of Apr 2011

## Slide 20: Myanmar
Myanmar has plans to install ADS-B stations at
  Lashio
  Sittwe
  Kyaing Tone
  Pathein
  Coco
The Project is expected to start in 2012 and complete by 2015

## Slide 21
Coco
Pathein
Sittwe
Lashio
Kyaing Tone

## Slide 22: Nepal
Replacement of Radar by 2013
Plans to install 1 ADS-B ground station by 2018
  Tribhuvan International Airport
Information correct as of Apr 2011
Tribhuvan

## Slide 23: New Caledonia
ADS-B installation plans as follows:
  Installed 3 ground ADS-B stations in 1H 2010
  ADS-B controller positions available since 30 Jul 2010 at Tontouta and Magenta airports
  For situation awareness & search and rescue
Information correct as of Apr 2011

## Slide 24: Pakistan
Installed 1 trial ADS-B station at Karachi ACC for one year
Information correct as of May 2009

## Slide 25: Papua New Guinea
Commencing ATMS modernisation program including plans to deploy ADS-B as its primary surveillance source
Plans to install 6 ADS-B ground stations by 2013
  Mt Nauwein
  Mt Dimodimo
  Burns Peak
  Mt Mission
  Mt Konokalang
  Lorengau
Information correct as of Apr 2011

## Slide 26
Lorengau
Burns Peak
Mt Nauwein
Mt Dimodimo
Mt Konokalang
Mt Mission

## Slide 27: The Philippines
Installed a new Mode-S SSR radar:
  Capable of processing 1090ES ADS-B reports
  Range of 100NM
  Intend to include ADS-B capability in other Mode S SSR station
Plan to install ADS-B stations by 2012 in:
  Manila and Puerto Princesa
Another possible site is Quezon Palawan*
Information correct as of May 2009
* Information correct as of Aug 2010

## Slide 28
Puerto Princesa
Manila
Quezon Palawan

## Slide 29: Republic of Korea
Installed 4 ADS-B stations at Incheon International Airport.
44 ADS-B vehicle transmitters are installed for vehicle monitoring
6 portable ADS-B vehicle transmitters are available for future use
Information correct as of Apr 2011
Incheon

## Slide 30: Singapore
Installed 1 ADS-B station and ADS-B processor in Singapore
Implementing a new ATM System with ADS-B processing capability by late 2012
Purchased a stand-alone controller position to conduct operational trial starting from 2011
Issued Aeronautical Information Circular on plans to implement ADS-B operations after 2013.

## Slide 31
Singapore

## Slide 32: Sri Lanka
Has plans to install 1 ADS-B ground station by end-2012
  Pidurutalagala (~2500m)
Information correct as of Apr 2011
Pidurutalagala

## Slide 33: Chinese Taipei
Installed 6 ADS-B trial stations at:
  Yang-Ming Mountain (Taipei), Hua Lian, Tai-Tung, Kao-Shung, Tai-Chung and Kin-Men
Installed Airport Multi-lateration at
  Kinmen Airport with 6 sensors
  Taoyuan Airport with 16 sensors
Perform trials on Wide-Area Multi-lateration using the 6 ADS-B trial stations.

## Slide 34
Yang-Ming mountain, Taipei
Hua Lian
Tai Tung
Kao Shung
Tai Chung
Kin-men Island

## Slide 35: Thailand
Planning to install 22 ADS-B ADS-B:
  Ubon Ratchathani, Hat Yai, Udon Thani, Chumphon, Trang, Samui (Surat Thani), Chiang Mai, Chiang Rai, Khon Kaen, Phitsanulok, Doi Inthanon (Chiang Mai), Nakhon Ratchasima, Sakhon Nakhon, Buriram, Suvarnabhumi (Samut Prakan), Donmuang (Bangkok), Hua Hin (Prachuap Khiri Khan), Phuket, Narathiwat, Trad, Nakhon Sawan, and Ranong.
Information correct as of Feb 2009

## Slide 36
Narathiwat
Hat Yai
Trang
Phuket
Surat Thani
Ranong
Chumphon
Hua Hin
Trad
Suvarnabumi
Donmuang
Nakhon Ratchasima
Buriram
Ubon Ratchathani
Khon Kaen
Nakhon Sawan
Phitsanulek
Ubon Thani
Sakhon Nakhoh
Doi Inthanon
Chiang Mai
Chiang Mai

## Slide 37: United States of America
Ground Stations
  Deployment of nearly 800 sites is under way
  Upgrades for the 4 US ATM systems with 1 in operational now.
ADS-B out
  Final Rule published in May 2010
  In general, whereever an SSR transponder is required today, ADS-B out will be required in 2020.
ADS-B in (validation projects)
  In trail procedures
  Visual separation on approach
  Traffic situational awareness on airport surface

## Slide 38
Picture obtained from Air Services Australia

## Slide 39: Viet Nam
Plan to install ADS-B station at Con Son by 2011
Plan to install two ADS-B stations in the Eastern part of Ho Chi Minh FIR
Plan to upgrade ATM system in Ho Chi Minh to integrate with ADS-B
Plan to install new ATM system with ADS-B processing capability in Ha Noi
Information correct as of Dec 2010

## Slide 40
Con Son Island

## Slide 41: Equipage on Singapore Registered Operators
Survey was made with the Singapore registered operators.
Results of the survey are shown in the following slides.
Information is purely based on declaration by operators and should not be construed as Flight Operations Approval.

## Slide 42: ADS-B equipage
 | Singapore Airlines* |  | 
Aircraft Type | No of Aircrafts | ADS-B fitted | (%)
A330 | 19 | 19 | 100%
A345 | 5 | 5 | 100%
A380 | 19 | 19 | 100%
B747 | 9 | 9 | 100%
B777 | 74 | 74 | 100%
 | Singapore Airlines Cargo** |  | 
Aircraft Type | No of Aircrafts | ADS-B fitted | (%)
B744F | 11 | 11 | 100%
* Information correct as of 13 Aug 2010
**Information correct as of 18 Aug 2010

## Slide 43: ADS-B equipage
 | Jetstar** |  | 
Aircraft Type | No of Aircrafts | ADS-B fitted | (%)
A320 | 12 | 10 | 83%
 | Silkair* |  | 
Aircraft Type | No of Aircrafts | ADS-B fitted | (%)
A319 | 11 | 3 | 27%
A320 | 6 | 2 | 33%
*Information correct as of 2 Sep 2010
**Information correct as of 12 Jan 2011

## Slide 44: ADS-B equipage
 | Jett8 |  | 
Aircraft Type | No of Aircrafts | ADS-B fitted | (%)
B747F** | 2 | 0 | 0%
 | Tiger Airways |  | 
Aircraft Type | No of Aircrafts | ADS-B fitted | (%)
A320* | 13 | 13 | 100%
*Information correct as of 24 Feb 2011
**Information correct as of 13 Jan 2011
Total No of Aircrafts | ADS-B fitted | (%)
181 | 165 | 91%

## Slide 45: Thank you