### ATTACHMENT to State letter E 3/5-04/99

### DRAFT ICAO POSTION FOR THE ITU WRC-2007

SUMMARY This paper reviews the agenda for the ITU WRC-2007, discusses points of aeronautical interest and provides the ICAO position for each agenda item. The ICAO position aims at securing availability of radio frequency spectrum to meet civil aviation requirements for current and future safety-of-flight applications. In particular, it stresses that safety considerations dictate that exclusive frequency bands must be allocated to safety critical aeronautical systems and that adequate protection against harmful interference must be ensured. It also includes proposals for new aeronautical allocations for air-ground communications. Support of the ICAO position by Contracting States is required to ensure that the position is supported at the WRC-2007 and that aviation requirements are met.

### CONTENTS

1.	Introduction

2.	Spectrum requirements for international civil aviation

3.	Aeronautical aspects on the agenda for WRC-2007

#### Attachment

Agenda for ITU WRC-2007

1.	INTRODUCTION

  - This paper contains the ICAO position on issues of interest to international civil aviation to be decided at the ITU World Radiocommunication Conference (2007) (WRC-2007), which will be held in October 2007. The agenda of the conference is contained in Attachment 1. The ICAO position should be considered in conjunction with section 7-II of the Handbook on Radio Frequency Spectrum Requirements for Civil Aviation including Statement of Approved ICAO Policies (Doc 9718) (Civil aviation frequency allocations – ICAO policies and related information). A revised version of this section is available on website http://www.icao.int/anb/panels/acp which includes the amendments to the Radio Regulations as agreed at WRC-2003. Also available at the above-mentioned website are the ITU WRC Resolutions referenced in the ICAO position.

2.	SPECTRUM REQUIREMENTS FOR INTERNATIONAL CIVIL AVIATION

2.1	The safety of air operation is vitally dependent on the availability of reliable communications and navigation services. The Eleventh Air Navigation Conference (AN-Conf/11), which was held in Montreal, Canada from 22 September to 3 October 2003, noted that States, international organizations and ICAO had embarked on communication, navigation and surveillance/air traffic management (CNS/ATM) systems planning, intended to improve aircraft operations by making use of modern CNS/ATM technologies. The AN-Conf/11 developed the global air traffic management concept, to be used as guidance for the development of ICAO CNS/ATM related provisions. The planning horizon used for the global ATM concept was up to and beyond the year 2025.

2.2	The development of these CNS/ATM provisions is highly dependent upon the availability of radio frequency spectrum that can support the high integrity and availability requirements associated with aeronautical safety systems and demands special conditions to avoid harmful interference to these systems. It was recognized by the AN-Conf/11 that currently available spectrum for CNS/ATM systems may need to be supplemented with new allocations to enable the introduction of new systems in aviation while the requirements for spectrum for current systems are to be maintained until a future undetermined period. The high integrity and availability requirements associated with aeronautical safety systems demand special conditions to avoid harmful interference to these systems. Article 4.10 of the Radio Regulations states that ITU Member States recognize that the safety aspects of radionavigation and other safety services requires special measures to ensure their freedom from harmful interference. These factors need to be taken into consideration in the allocation, assignment and use of frequencies for aeronautical systems. In particular, the sharing of aeronautical radio services with other aeronautical services or non-aeronautical services must be considered with extreme care. Where sharing conditions are not thoroughly proven, exclusive aeronautical allocations need to be secured to preserve the integrity of aeronautical services.

2.3	The radio frequency spectrum needs for civil aviation, arising from the growth in air transport and from the introduction of new technologies, are increasing. Requirements for additional aviation spectrum and/or for alternative uses of existing aviation spectrum are currently being identified to meet emerging needs. While some of these needs will be addressed by WRC-2007, consideration by future conferences (WRC-2010 and beyond) will be necessary to fully meet the future aviation requirements.

2.4	The ICAO position was developed  in 2003/2004 by the Aeronautical Communications Panel (ACP) and was reviewed by the Air Navigation Commission (ANC) on [21] October  2004. Following the review by the ANC, it was submitted to ICAO Contracting States and international organizations for comments. After final review of the ICAO position and the comments received by the ANC on [xx xxxx 2005], it was approved by Council on [xx xxxx 2005]. It is expected that, during the course of the preparatory activities for the WRC-2007 further updates to the ICAO position may become necessary. States and international organizations in their preparatory activities for the WRC-2007 at the national level, in the activities of the regional telecommunication organizations and in the relevant meetings of the ITU are requested to make use of the ICAO position, to the maximum extend possible.

3.	AERONAUTICAL ASPECTS ON THE AGENDA FOR WRC-2007

Note 1.— The statement of the ICAO position on an agenda item is given in a text box at the end of the section addressing the agenda item, after the introductory background material.

Note 2.— No impact on aeronautical services has been identified from WRC-2007 Agenda Items 1.2, 1.7, 1.8, 1.10, 1.11, 1.12, 1.15, 1.18, 3, 5, 6 and 7.1. which are therefore not addressed in the position:

Note 3.— No ICAO position has been developed on the WRC-2007 agenda items 1.4, 1.9, 1.14 and 1.19. However, any proposal of a technical or regulatory nature on these agenda items needs to be considered carefully to ensure that aeronautical interests are not affected adversely. If required, an ICAO position on these agenda items will be developed in due course.

WRC-2007 Agenda Item 1.1

Agenda Item Title:

Requests from administrations to delete their country footnotes or to have their country name deleted from footnotes, if no longer required, in accordance with Resolution 26 (Rev. WRC-97)

Discussion:

Allocations to the aeronautical services are generally made for all ITU Regions and normally on an exclusive basis. These principles reflect the global process of standardization within ICAO for the promotion of safety and to support the global interoperability of radiocommunication and radionavigation equipment used in civil aircraft. In some instances, however, footnotes to the ITU Table of Frequency Allocations allocate spectrum in one or more countries to other radio services in addition or alternatively to the aeronautical service to which the same spectrum is allocated in the body of the table.

The use of country footnote allocations in aeronautical bands to non-aeronautical services is generally not recommended by ICAO, on safety grounds, as such use may result in harmful interference to safety services. Furthermore, this practice generally leads to an inefficient use of available spectrum to aeronautical services, particularly when the radio systems sharing the band have differing technical characteristics. It also may result in undesirable (sub)-regional variations with respect to the conditions under which the technical conditions under which the aeronautical allocations can be used. This can have serious impact on the safety of aviation.

A number of footnotes in aeronautical bands that should be deleted for safety and efficiency reasons are discussed below.

a)	In the bands used for the ICAO instrument landing system (ILS), (Marker Beacons 74.8 -75.2 MHz; Localizer 108 - 112 MHz and Glide Path 328.6 - 335.4 MHz and the VHF omnidirectional radio range system (VOR); 108-117.975 MHz). Footnotes 5.181, 5.197 and 5.259 allow for the introduction of the mobile service on a secondary basis and subject to agreement obtained under No. 9.21 of the Radio Regulations when these bands are no longer required for the aeronautical radionavigation service. The use of both ILS and VOR is expected to continue. In addition, WRC-2003 has introduced Footnote 5.197A stipulating that the band 108 - 117.975 MHz may also be used by the aeronautical mobile (R) service on a primary basis for navigation and surveillance functions. GNSS ground-based augmentation systems (GBAS) and VDL Mode 4 have been developed and relevant ICAO Standards and Recommended Practices (SARPs) have been adopted by ICAO. As a result, access to these bands by the mobile service is not feasible, in particular since no acceptable sharing criteria that secure the protection of aeronautical systems have been established to date. Footnotes 5.181, 5.197 and 5.259 should now be deleted since they do not represent a realistic expectation for an introduction of the mobile service in these bands.

b)	Footnotes 5.203A and 5.203B allocate the band 136 - 137 MHz in some countries to the fixed and mobile except aeronautical mobile (R)services (5.203) and to the fixed and mobile except aeronautical mobile services (5.203B) both on a secondary basis until 1 January 2005). In addition, this band may also be used by the meteorological satellite service until 1 January 2002 (5.203). The band 136 - 137 MHz was allocated to the aeronautical mobile (route) service (AM(R)S) on a primary basis by the WRC-79. The actual introduction of the AM(R)S could only take place as from 1 January 1990 to enable other users to vacate this band between 1979 and 1990. However, some of the non-aeronautical services continued to operate well beyond 1990. In Europe, the AM(R)S was introduced in 1990 and in North America in 1995 and recently in other ICAO regions. Introduction of aeronautical air-ground data link is primarily concentrated in this sub-band. The band is already heavily used in Europe for AM(R)S for voice and data communications and use is increasing in North America and other parts of the world, thus restricting seriously the operations of the various services mentioned in Footnotes 5.203, 5.203A and 5.203B. The provisions of these footnotes have already expired and should not be extended. As a result, they should be deleted at the WRC-2007.

c)	In the band 1 559 - 1 610 MHz, which is used for elements of the ICAO Global Navigation Satellite System (GNSS), Footnotes 5.362B and 5.362C allow the operation of the fixed service on a primary basis until 1 January 2005 (1 January 2010 in some countries) and on a secondary basis after those dates until 1 January 2015. This band is allocated, on a worldwide, primary basis, to the aeronautical radionavigation service (ARNS) and to the radionavigation-satellite service (RNSS). The band already supports operation of two prime elements of global navigation satellite system (GNSS), i.e. GLObal Navigation Satellite System (GLONASS) and global positioning system (GPS), which have been defined in ICAO SARPs. SARPs for other RNSS systems, such as the European Galileo system, are under development. Studies undertaken in preparation for WRC-2000 indicate that a geographical separation distance exceeding line-of-sight (in the order of 400 km) between aircraft using GNSS and stations of the fixed service is required to ensure safe operation of GNSS. This is a very severe restriction, which can prohibit the safe use of GNSS over wide areas around any fixed service installation. To compensate for these restrictions, retention of current terrestrial radionavigation systems by aviation may be needed, leading to inefficient use of available spectrum. More importantly, harmful interference situations can arise leading to disruption to GNSS, affecting the safety of aircraft in flight. Thus, the WRC-2000 agreement to terminate all use by the fixed service in this band in 2015 still constitutes a severe and unacceptable constraint on the safe and effective use of GNSS in some areas of the world. It is, therefore, recommended that deletion of these allocation be effective as early as possible, preferably from 2007. It is further noted that in Footnote 5.362B the allocation to the fixed service on a primary basis in a number of countries has expired at the timing of WRC-2007. Finally, the alternative allocation to the aeronautical radionavigation service in one country in the band in Footnote 5.363 is redundant in the light of the global allocation already in this frequency band and should be deleted.

d)	In the band 4 200 - 4 400 MHz, which is reserved for use by airborne radio altimeters, Footnote 5.439 allows the operation of the fixed service on a secondary basis in some countries. Radio altimeters are a critical element in aircraft automatic landing systems and serve as a sensor in ground proximity warning systems. Interference from the fixed service has the potential to affect the safety of all weather operations. Deletion of this footnote is recommended.

ICAO Position:

To support deletion of Footnotes 5.181, 5.197 and 5.259, as access to these bands by the mobile service is not feasible and could create the potential for interference to important radionavigation systems used by aircraft at final approach and landing. To support deletion of 5.203, 5.203A and 5.203B at WRC-2007 to enable full use of the band 136 - 137 MHz for AM(R)S communications. To support the cessation of all fixed services in the band 1 559 - 1 610 MHz as of 2007 in order to remove the interference caused by the fixed service to essential aeronautical radionavigation functions and to permit the full utilization of GNSS services to aircraft on a global basis. To support the deletion of 5.363 from the band 1 590 - 1 610 MHz. To support deletion of Footnote 5.439 as a measure to protect safety critical operation of radio altimeters in the band 4 200 - 4 400 MHz.

WRC-2007 Agenda Item 1.3

Agenda Item Title:

In accordance with Resolution 747 (WRC-2003) consider the upgrading of the radiolocation service to primary allocation status in the bands 9 000 - 9 200 MHz and 9 300 - 9 500 MHz and extending by up to 200 MHz the existing primary allocations to the Earth exploration-satellite service (active) and the space research service (active) in the band 9 500 - 9 800 MHz without placing undue constraints to the services to which the bands are allocated.

Discussion:

These three bands are used extensively by aeronautical radar systems (ground and airborne). They cater for short-range surveillance and precision functions up to a 50 km range. In aviation, they find considerable application in precision monitoring, approach and surface detection functions and in airborne weather radar (AWR) systems where their shorter wavelength is suitable for the detection of storm clouds. In this latter role, the frequency band 9 345 - 9 375 MHz has been coordinated with other users within ITU-R as the agreed aeronautical airborne frequencies for this purpose. This band enables for a narrower beam than the AWR operating at 5.3 GHz and it provides a better resolution and less ground clutter. One of the vital safety functions of AWR is to give warning of hazardous weather and ensure safe separation of aircraft from hazardous weather conditions. In most countries the carriage of AWR by aircraft is a mandatory requirement.

These radars are to remain in service for many years into the future. Sharing with maritime radars is manageable and practical because of the different geographical usage and good coordination between the two services. The ongoing protection of the aeronautical uses of these bands needs to be assured. The operation of the radiolocation service in these bands needs to be based upon the results of studies in ITU-R, demonstrating that sharing with the radiolocation service on a primary basis is feasible. These studies should also result in ITU-R recommendations stipulating the conditions of the use of these bands by the radiolocation service. Any upgrade of the radiolocation service to a primary status should be considered with a footnote indicating that the radiolocation service will not cause harmful interference to nor claim protection from the (aeronautical) radionavigation service.

Under this agenda item, WRC-2007 may also consider to allocate additional 200 MHz on a primary basis to the Earth exploration satellite service (EESS) and the space research service (SRS). The band 9 300 - 9 500 MHz identified in the resolves to invite ITU-R of Resolution 747 (WRC-2003) is used by aeronautical radio services. Any suggestions for the sharing of this radionavigation band with EESS and SRS can only be considered on the basis of agreed studies, which take into account the present and expected future use of the band by aviation, and the constraints applied to this use. Such an allocation to EESS and SRS shall not cause harmful interference to, nor claim protection from, or otherwise impose constraints on the operation and future development of the radionavigation service in the band 9 000 - 9 500 MHz.

ICAO Position:

Accept the upgrading of the radiolocation service to primary status in the bands 9 000 - 9 200 MHz and 9 300 - 9 500 MHz, subject to positive results of the studies in ITU-R, on the express condition that no harmful interference is caused to the aeronautical radionavigation service and the radionavigation service and that no protection is required from these radionavigation services. Any suggestions for the sharing of radionavigation band 9 000 - 9 500 MHz with EESS and SRS under this agenda item can only be considered on the basis of agreed studies, which take into account the present and expected future use of the band by aviation, and the constraints applied to this use. An allocation to EESS and SRS shall not cause harmful interference to, not claim protection from, or otherwise impose constraints on the operation and future development of the radionavigation service in the band 9 000 - 9 500 MHz. No change to Footnotes 5.337, 5.427, 5.474 and 5.475. Footnote 5.476 can be deleted since the date indicated has expired.

WRC-2007 Agenda Item 1.5

Agenda Item Title:

To consider spectrum requirements and possible additional spectrum allocations for aeronautical telecommand and high-bit rate aeronautical telemetry, in accordance with Resolution 230 (WRC-2003)

Discussion:

a)	Aeronautical Telemetry

The development of modern aircraft requires a large test flight programme.  These programmes are required to gather a large amount of data on the performance of the airframe under test.  By providing a real-time link between the aircraft and the ground control centre, the amount of testing and the number of flights can be kept to a minimum.  This will result in faster development programmes and hence achieve a significant cost saving.  This agenda item seeks to make provision for the required air-ground telemetry link.

The reduction in aircraft development cycles is important to the future of aviation. Initial estimates presented within ITU Working Party 8B have suggested that 60 MHz will be required to meet the requirements for aeronautical telemetry in the band between 3 - 30 GHz. As stated in Resolution 230, this 60 MHz will have to be found from one of the following methods:

- review, with a view to upgrading to primary, secondary allocations to the mobile service in the frequency range 3 - 16 GHz for the implementation of wideband aeronautical telemetry and associated telecommand;

- consider possible additional allocations to the mobile service, including aeronautical mobile, on a primary basis in the frequency range 3 - 16 GHz for the implementation of wideband aeronautical telemetry and associated telecommand; and

- designate existing mobile allocations between 16 and 30 GHz for wideband aeronautical telemetry and associated telecommand.

The development of telemetry links however must not adversely affect existing and planned aeronautical systems.

b)	Unmanned Aerial Vehicles

There is a significant amount of development work taking place on unmanned aerial vehicles (UAV).  Developments have already demonstrated the capability of large UAVs to operate over long distances (including transcontinental).  There is a need for aviation to consider how to integrate these aircraft into controlled airspace, shared with civil manned aircraft safely, and it may become necessary to develop common global standards for telemetry and telecommand links between the UAV and the UAV ground control centre.  This agenda item seeks to make provision for the required air-ground telemetry/telecommand link for UAVs.

The potential introduction of UAVs into controlled airspace is an important development within aviation. Further, in order to allow UAVs to be fully integrated safely into controlled airspace it is essential that suitable safety of life air ground datalinks, within the frequency range 3 – 30 GHz, are provided.  The development of telemetry and telecommand links to support UAV operations however must not adversely affect existing and planned aeronautical systems.

ICAO Position:

To support the allocation of suitable spectrum to support aeronautical mobile telemetry systems and associated telecommand applications, in the band 3 - 30 GHz, in accordance with the provisions of Resolution 230, provided those allocations have no adverse impact to existing or planned aviation use of the band selected or frequency bands considered in relation to Resolution 414 (see also WRC-2007 Agenda Item 1.6). To support the identification and allocation of suitable spectrum in the band 3 - 30 GHz, to support the safety related aspects of UAV operations provided they do not adversely affect existing or planned aeronautical systems. To support the development of regulatory text to accommodate new service definitions if required. To support the continued use and protection of current aeronautical mobile telemetry applications in the band 1 429 - 1 535 MHz.

WRC-2007 Agenda Item 1.6

Agenda Item Title:

To consider allocations for the aeronautical mobile (R) service in parts of the bands between 108 MHz to 6 GHz, in accordance with Resolution 414 and to study current frequency allocations that will support the modernization of civil aviation telecommunication systems, taking into account Resolution 415 (WRC-2003)

Discussion:

Resolution 414 – Consideration of the frequency range between 108 MHz and 6 GHz for new aeronautical applications

In some regions, in particular in portions of Region 1 (Europe) and Region 2 (North America), the aeronautical VHF communications band 117.975 - 137 MHz is heavily congested. Assignable VHF spectrum for line-of-sight communications to support safety and regularity of flight has become increasingly limited, and in some cases non-existent, even after introduction of more spectrum efficient techniques.

In addition, new applications are foreseen to be globally implemented and mainly making use of data communication systems. These are needed to accommodate expected air traffic growth and to support various new ATM, as well as aviation security requirements. In particular, aviation has identified the need for introducing aeronautical safety systems including those that would:

- overcome limitations of conventional systems and allow ATM to further develop on a global scale;

- provide increased information exchange between aircraft and ground systems as well as between aircraft (e.g. ATC centres, aircraft operating agencies, etc); and

- reduce runway incursions through the use of high integrity, wireless local area networks combined with connected grids of distributed sensors.

For aviation, these new applications support air navigation functions (i.e. either communication, navigation or surveillance or a combination of these) through the transmission or exchange of data.  However, within the terms of the ITU definitions, they require to operate under an allocation to the AM(R)S, thus requiring additional allocations to be made in the relevant bands between 108 MHz to 6 GHz.

The combination of VHF band spectrum congestion, growing air traffic and evolving aeronautical applications drive an urgent need for new AM(R)S allocations. The quantity of spectrum required is under study in ICAO.

Furthermore, an increased use of short-range fixed radio links on or around airports is expected to support the transfer of safety-critical information generated by systems such as air traffic control radars, wind shear radars, remote maintenance control systems, runway lighting, automated weather observation systems, etc., or between nodes of high-integrity airport surface wireless local area networks. Accommodation of the requirements for these aeronautical fixed radio links, foreseen in the band 5 091 - 5 150 MHz, requires an appropriate allocation.

Spectrum currently globally allocated to the aeronautical radionavigation service and having suitable propagation conditions is being considered in ICAO studies to satisfy these current and emerging AM(R)S requirements. These studies focus on additional allocations to the AM(R)S service in the frequency band 5 091 - 5 150 MHz although other frequency bands allocated to aeronautical radionavigation services are also being considered. Introduction of an allocation to the AM(R)S in these bands will require that this service shall not cause harmful interference to, claim protection from, or otherwise impose constraints on operation or development of systems operating in accordance with approved international aeronautical (ICAO) standards. These issues are being addressed in ICAO. Consideration of compatibility of co-band and adjacent band non-aeronautical systems, will be addressed in ITU, as required. Special attention is required for appropriate provisions in the Radio Regulations to allow for the proposed use of the UAT system which operates on the frequency 978 MHz.

With regard to the future use of the band 5 030 - 5 091 MHz by the aeronautical radionavigation service (core band for MLS), protection assignments for MLS require separation distances larger than those assumed to date. Therefore, the current allocation in this band cannot be amended. The impact this may have on the use of the MLS extension band (5 091 - 5 150 MHz) is under consideration in ICAO.

## Resolution 415 - Study of current satellite frequency allocations that will support the modernization of civil aviation telecommunication systems

Resolution 415 (WRC-2003) is addressing possibilities of broadening the services and applications of the use of current satellite frequency allocations to allow the expansion of International Civil Aviation Organization (ICAO) communications, navigation, surveillance and air traffic management (CNS/ATM) systems through using, for aeronautical safety purposes, systems that can also support other, non-aeronautical services.

Ground-ground communications

Satellite communications provide a real possibility to meet the demands of the ICAO CNS/ATM system, especially in areas where a terrestrial communication infrastructure is lacking. The benefits of using in particular very small aperture terminals (VSAT) include the use of the most appropriate and cost-effective technology to improve aeronautical ground-ground communications. VSAT networks have been implemented in a number of ICAO regions and the operation of these networks is well under control. Potential shortcomings, such as interoperability issues between different networks, require a technical or administrative (with administrations and/or service providers) solution. In view of their role in aeronautical safety-of-life communications, aeronautical VSAT systems can be used on a shared basis to offer telecommunication services to non-aeronautical users, subject to appropriate priorities being afforded to aeronautical telecommunications.

VSAT networks operate under an allocation to the fixed satellite service (FSS) which in the ITU is not recognized as a safety service. In this regard, it is necessary to consider in the ITU, through the adoption of a new Resolution at WRC-2007, how to recognize the safety aspects of the aeronautical telecommunications element VSAT networks can carry. Such a Resolution however, should not impose additional constraints on the VSAT operators.

Air-ground communications

AMS(R)S:

Currently, special provisions in the Radio Regulations provide for priority to accommodate the spectrum requirements for the aeronautical mobile satellite (R) service (AMS(R)S) through RR 5.357A and Resolution 222 in the frequency bands 1 545 - 1 559 MHz and 1 646.5 - 1 660.5 MHz. The results of ITU-R studies on the feasibility of real-time pre-emptive access between different networks of mobile-satellite systems, as requested by Resolution 222 and in RR 5.357A seen as a method to ensure priority access and immediate availability AMS(R)S are on the agenda for the WRC-2010.

AMSS:

At WRC-2003, ICAO supported the extension of the allocation to the mobile-satellite (Earth-to-space) on a secondary basis in the band 14 - 14.5 GHz to permit the operation of the aeronautical mobile-satellite service as stipulated in Resolution 216 (Rev. WRC-2000). The ICAO support to this allocation, which was made in 2003, addressed non-safety broadband communications by aircraft operators and passengers of commercial aircraft. This allocation will not form part of the AMS(R)S since any secondary allocation is not acceptable for any aeronautical safety-of-life service. A need to provide complementary spectrum for the space-to-Earth direction has been identified at WRC-2003. Under the provisions of Resolution 415, ICAO would wish to provide support to such allocations on the basis that this service has the potential to promote the general efficiency of aircraft operations.

ICAO Position:

Resolution 414 To support a global allocation to the aeronautical mobile (R) service in the frequency band 5 091 - 5 150 MHz and other bands if shown by aviation studies to meet global CNS/ATM requirements. Use of this AM(R)S allocation shall be limited to systems which operate in accordance with international aeronautical standards. Such use shall be subject to the conditions that the AM(R)S shall not cause harmful interference to, claim protection from, or otherwise impose constraints on the operation and future development of other co-band aeronautical systems operating in accordance with international aeronautical standards. Compatibility with non-aeronautical services that may be affected by these allocations is expected to be addressed in the ITU with the participation of ICAO. To support any necessary additional allocations to the band 5 091 - 5 150 MHz to meet the increasing demand for radio links supporting the transfer of safety-critical information between fixed aeronautical ground facilities. To support appropriate provision allowing the use of frequency 978 MHz by the UAT system subject to its standardization by ICAO. No change to the current allocation in the band 5 030-5 091 MHz since this band is required to satisfy the requirements of the aeronautical radionavigation service (MLS). Resolution 415 To support appropriate regulatory measure, preferably in the format of an ITU Resolution attached to the Radio Regulations which recognizes that VSAT networks operating in the fixed satellite service can also be used for aeronautical safety applications. This includes provisions for the necessary priorities for aeronautical telecommunications when aeronautical VSAT networks are also being used to provide non-aeronautical telecommunications. Support, where applicable, the inclusion of an allocation on a secondary basis for the AMSS (space-to-Earth) to provide for the complimentary component of the secondary allocation to AMSS (Earth-to-space) in the band 14 - 14.5 GHz. This secondary allocation is not intended to be used for aeronautical safety-of-life ICAO CNS/ATM communications.

WRC-2007 Agenda Item 1.13

Agenda Item Title:

Taking into account Resolutions 729 (WRC-97), 351 (WRC-2003) and 544 (WRC-2003) to review the allocations to all services in the HF bands between 4 and 10 MHz, excluding those allocations to services in the frequency range 7 000 - 7 200 kHz and those bands whose allotment plans are in Appendices 25, 26 and 27 and whose channelling arrangements are in Appendix 17, taking into account the impact of new modulation techniques, adaptive control techniques and spectrum requirements for HF broadcasting

Discussion:

Within the frequency range 4 - 10 MHz, various frequency bands are allocated to the aeronautical mobile (R) service and the allotment plan for these frequency bands is in Appendix 27 to the Radio Regulations. Although the aeronautical bands between 4 to 10 MHz have been excluded from consideration under this agenda item, it is of concern to aviation that any change to existing allocation, or new allocation, in particular to the high-powered broadcasting service, will not cause interference to the aeronautical mobile (R) service. In addition, the introduction of any new modulation technique, in particular digital modulation by the broadcasting service, may cause interference to the aeronautical mobile (R) service if these techniques are applied in bands adjacent to or in close proximity of these aeronautical bands.

ICAO Position:

Ensure that new allocations and techniques considered for introduction in the bands between 4 to 10 MHz will not cause harmful interference in the aeronautical HF bands.

WRC-2007 Agenda Item 1.16

Agenda Item Title:

To consider the regulatory and operational provisions for maritime mobile service identities (MMSIs) for equipment other than shipborne mobile equipment, taking into account Resolutions 344 (Rev. WRC-2003) and 353 (WRC-2003)

Discussion:

Maritime mobile service identities (MMSIs) are unique identifiers for individual stations and provide a rapid method of identification. Several ITU-R recommendations cover the assignment and use of these MMSIs for ship and land stations. The need to assign MMSIs for automatic identification systems (AIS) on search and rescue (SAR) aircraft, in accordance with the provision of recommendation ITU-R M.1371 in order to communicate efficiently in the maritime mobile service when engaged in SAR operations. With respect to using AIS on board an aircraft provisions for a standard format of the identification number are necessary. WRC-2007 will consider necessary changes to the Radio Regulations to allow MMSIs to be used on board SAR aircraft.

ICAO supports measures aimed at improving the use of MMSIs on board SAR aircraft. Changes to the Radio Regulations should be made on the condition that these are compatible with ICAO Standards and Recommended Practices (SARPs).

ICAO Position:

Support measures improving the use of MMSIs on board SAR aircraft for automatic identification system (AIS).

WRC-2007 Agenda Item 1.17

Agenda Item Title:

To consider the results of ITU-R studies on compatibility between the fixed-satellite service and other services around 1.4 GHz, in accordance with Resolution 745 (WRC-2003)

Discussion:

This agenda item seeks to complete the studies undertaken in response to Agenda Item 1.16 of WRC-2003 on feeder links for non-geostationary satellite systems. Studies completed to date have shown that there are significant difficulties with an allocation to the fixed-satellite service in this frequency range, in particular if existing (passive) services are to be afforded protection from these feeder links. Of concern to aviation is that the allocation to the radionavigation service in Footnote 5.338 is protected from harmful interference. It is also necessary to secure protection from harmful interference of the band 1 429 - 1 535 MHz. Footnotes 5.342 and 5.343 are stipulating the use of this band for aeronautical telemetry in some countries.

ICAO Position:

Use of the band around 1.4 GHz by the fixed satellite service for feeder links for non-geostationary satellite systems should not be introduced in any of the aeronautical bands in this frequency range; aeronautical usage needs to be protected from harmful interference.

WRC-2007 Agenda Item 1.20

Agenda Item Title:

To consider the results of studies and proposals for regulatory measures, if appropriate, regarding the Earth exploration-satellite service (passive) from unwanted emissions of active services in accordance with Resolution 738

Discussion:

The Earth exploration-satellite service (passive) operates in the frequency band 1 400 – 1 427 MHz and is seeking protection from active services in the adjacent bands.

Of concern to aviation is that the band below 1 400 MHz is used by the aeronautical radionavigation service (radar) through Footnotes 5.334 and 5.338 and their operations should not be unduly constrained. The use of the band 1 429 - 1 535 MHz for aeronautical telemetry is regulated through Footnotes 5.342 and 5.343 for aeronautical telemetry and this usage should not be adversely affected by the wish to improve protection to the Earth exploration-satellite service.

ICAO Position:

Protection of the Earth exploration-satellite service in the band 1 400 - 1 427 MHz should not impose undue constraints to the use of the adjacent bands by aviation.

WRC-2007 Agenda Item 1.21

Agenda Item Title:

To consider the results of studies regarding the compatibility between the radio astronomy service and the active space services in accordance with Resolution 740 (Rev.WRC-2003), in order to review and update, if appropriate, the tables of threshold levels used for consultation that appear in the Annex to Resolution 739 (WRC-2003)

Discussion:

The radio astronomy service uses frequencies in the band 1 610.6 - 1 613.8 MHz and is seeking protection from active services in the adjacent bands.

Of concern to aviation is that the near adjacent band 1 559 - 1 610 MHz is used by the radionavigation satellite service for GNSS (GPS, GLONASS and the future Galileo system) and their operations should not be unduly constrained.

ICAO Position:

Protection of the radio astronomy service in the band 1 610.6 - 1 613.8 MHz should not impose undue constraints to the use of the band 1 559 - 1 610 MHz by aviation.

WRC-2007 - Agenda Item 2

Agenda Item Title:

To examine the revised ITU-R Recommendations incorporated by reference in the Radio Regulations communicated by the Radiocommunication Assembly, in accordance with Resolution 28 (Rev. WRC-2003), and to decide whether or not to update the corresponding references in the Radio Regulations, in accordance with principles contained in the Annex to Resolution 27 (Rev. WRC-2003)

Discussion:

Currently no new or amended ITU-R recommendations referring to aeronautical radio services and incorporated by reference in the ITU Radio Regulations have been identified.

ICAO Position:

No change to the current references in the Radio Regulations to ITU-R recommendations related to aeronautical services.

WRC-2007 Agenda Item 4

Agenda Item Title:

In accordance with Resolution 95 (Rev. WRC-2003), to review the resolutions and recommendations of previous conferences with a view of possible revision, replacement or abrogation.

ICAO Position:

Resolutions:

| Resolution No. | Title | Action recommended |
| --- | --- | --- |
| 18 (MOB-83) | Relating to the procedure for identifying and announcing the position of ships and aircraft of States not parties to an armed conflict | No change |
| 20 (Rev. WRC-2003) | Technical cooperation with developing countries in the field of aeronautical telecommunications | No change |
| 26 (Rev. WRC-97) | Footnotes to the Table of Frequency Allocations in Article 5 of the Radio Regulations | No change |
| 27 (Rev. WRC-2003) | Use of incorporation by reference in the Radio Regulations | No change |
| 28 (Rev. WRC-2003) | Revision of references to the text of ITU-R recommendations incorporated by reference in the Radio Regulations | No change |
| 63 (Rev. WRC-2003) | Protection of radiocommunication services against interference caused by radiation from industrial, scientific and medical (ISM) equipment | No change |
| 95 (Rev. WRC-2003) | General review of the resolutions and recommendations of world administrative radio conferences and world radiocommunication conferences | No change |
| 114 (Rev. WRC-2003) | Studies on compatibility between new systems of the aeronautical radionavigation service and the fixed-satellite service (Earth-to-space) (limited to feeder links of the non-geostationary mobile-satellite systems in the mobile-satellite service) in the frequency band 5 091 - 5 150 MHz | No change |
| 205 (Rev. MOB-87) | Protection of the band 406 - 406.1 MHz allocated to the mobile-satellite service | No change |
| 207 (Rev. WRC-2003) | Measures to address unauthorized use of and interference to frequencies in the bands allocated to the maritime mobile service and to the aeronautical mobile (R) service | No change |
| 217 (WRC-97) | Implementation of wind profiler radars | No change |
| 222 (WRC-2000) | Use of the bands 1 525 - 1 559 MHz and 1 626.5 -1 660.5 MHz by the mobile-satellite service | No change |
| 225 (Rev. WRC-2003) | Use of additional frequency bands for the satellite component of IMT-2000 | No change |
| 228 (Rev. WRC-2003) | Studies on frequency related matters for the future development of IMT-2000 and systems beyond IMT-2000 as defined by ITU-R | Delete after WRC-2007 (WRC-2007, Agenda Item 1.4) |
| 230 (Rev. WRC-2003) | Consideration of mobile allocations for wideband aeronautical telemetry and associated telecommand | Delete after WRC-2007 (WRC-2007, Agenda Item 1.5) |
| 339 (Rev. WRC-2003) | Coordination of NAVTEX services | No change |
| 405 | Relating to the use of frequencies of the aeronautical mobile (R) service | No change |
| 353 (WRC-2003) | Maritime mobile service identities (MMSIs) for equipment other than shipborne equipment | No change |
| 413 (WRC-2003) | Use of the band 108 - 117.975 MHz by aeronautical services | Delete after studies completed |
| 414 (WRC-2003) | Consideration of the frequency range between 108 MHz and 6 GHz for new aeronautical applications | Delete after WRC-2007 (WRC-2007, Agenda Item 1.6) |
| 415 (WRC-2003) | Study of current satellite frequency allocations that will support the modernization of civil aviation telecommunication systems | Delete after WRC-2007 (WRC-2007, Agenda Item 1.6) |
| 544 (WRC-2003) | Identification of additional spectrum for the broadcasting service in the HF bands | Delete after WRC-2007 |
| 608 (WRC-2003) | Use of the frequency band 1 215 – 1 300 MHz by systems of the radionavigation-satellite service | Delete after studies completed |
| 609 (WRC-2003) | Protection of aeronautical radionavigation systems from the equivalent power flux-density produced by radionavigation satellite service networks and systems in the 1 164 - 1 215 MHz band | No change |
| 610 (WRC-2003) | Coordination and bilateral resolution of technical compatibility issues for radionavigation satellite networks and systems in the band 1 164 - 1 300 MHz, 1 559 - 1 610 MHz and 5 010 - 5 030 MHz | No change |
| 644 (Rev. WRC-2000) | Telecommunication resources for disaster mitigation and relief operations | No change |
| 705 (MOB-87) | Mutual protection of radioservices operating in the band 70 - 130 kHz | No change |
| 729 (WRC-97) | Use of frequency adaptive systems in the MF and HF bands | Delete after WRC-2007 |
| 738 (WRC-2003) | Compatibility analysis between the Earth exploration-satellite service and (passive) and active services | Delete after WRC-2007 |
| 740 (WRC-2003) | Future compatibility analyses between the radio astronomy service and active space services in certain adjacent or nearby bands | Delete after WRC-2007 |
| 745 (WRC-2003) | Protection of existing services in all regions from non-geostationary-satellite networks in the fixed satellite service in the fixed-satellite service using the frequency bands around 1.4 GHz on a secondary basis | Delete after WRC-2007 |
| 747 (WRC-2003) | Possible upgrade of the radiolocation service to primary allocation status in the frequency bands 9 000 - 9 200 MHz and 9 300 - 9 500 MHz, and possible extension of the existing primary allocations to the Earth exploration-satellite service (active) in the band 9 500 - 9 800 MHz | Delete after WRC-2007 (WRC-2007, Agenda Item 1.3) |
| 802 (WRC-2003) | Agenda for the 2007 World Radiocommunication Conference | Delete after WRC-2007 |
| 803 (WRC-2003) | Preliminary agenda for the 2010 World Radiocommunication Conference | Modify at WRC-2007 (WRC-2007, Agenda Item 7.2) |
| 951 (WRC-2003) | Options to improve the international spectrum regulatory framework | Delete after WRC-2007 |
| 952 (WRC-2003) | Studies regarding devices using ultra-wideband technology | Delete after studies completed |

Recommendations:

| Recommendation No. | Title | Action recommended |
| --- | --- | --- |
| 7 (Rev. WRC-97) | Adoption of standard forms for ship station and ship earth station licences and aircraft station and aircraft earth station licences | No change |
| 9 | Relating to the measures to be taken to prevent the operation of broadcasting stations on board ships or aircraft outside national territories | No change |
| 71 | Relating to the standardization of the technical and operational characteristics of radio equipment | No change |
| 75 (WRC-2003) | Study on the boundary between the out-of-band and spurious domains of primary radars using magnetrons | No change |
| 401 | Relating to the efficient use of aeronautical mobile (R) worldwide frequencies | No change |
| 604 (Rev. MOB-87) | Future use and characteristics of emergency position-indicating radio beacons (EPIRBs) | No change |
| 606 (MOB-87) | The possibility of reducing the band 4 200 - 4 400 MHz by radio altimeters in the aeronautical radionavigation service | Delete |
| 608 (WRC-2003) | Guidelines for consultation meetings established in Resolution 609 (WRC-2003) | No change |
| 800 (WRC-2003) | Principles for establishing agendas for world radiocommunication conferences | No change |

WRC-2007 - Agenda Item 7.2

Agenda Item Title:

To recommend to the Council items for inclusion in the agenda for the next WRC, and to give its views on the preliminary agenda for the subsequent conference and on possible agenda items for future conferences, taking into account Resolution 802 (WRC-2003)

Discussion:

This agenda item addresses the preliminary agenda for WRC-2010, which will be developed by WRC-2007. Items of aeronautical interest that should appear in the WRC-2010 include:

a)	deletion of country footnotes in aeronautical bands;

b)	review of results of studies conducted in accordance with Resolution 222 (WRC-2000); and

Resolution 222, inter alia, calls for ITU-R studies to ensure spectrum availability and protection for the aeronautical mobile-satellite (R) service in the 1.5 - 1.6 GHz band. The result of such studies should be reviewed by WRC-2010 with a view to assessing the need of changes to the Radio Regulations to satisfy AMS(R)S spectrum requirements in the band. Participation by aviation experts to the relevant ITU-R studies is required.

c)	wireless interactive multimedia. These systems, most likely to be used on an unlicensed basis and on yet undetermined frequencies need to ensure protection to aeronautical services and systems.

ICAO Position:

To support the inclusion in the agenda of WRC-2010 of an item addressing the review of results of studies conducted in accordance with Resolution 222 (WRC-2000).

Attachment 1

ITU COUNCIL RESOLUTION 1227

Agenda for the World Radiocommunication Conference (WRC-2007)

The Council,

Noting

that Resolution 802 of the World Radiocommunication Conference (Geneva, 2003):

- resolved to recommend to the Council that a World Radiocommunication Conference be held in 2007 for a period of four weeks; and

- recommended its agenda, and invited the Council to finalize the agenda and arrange for the convening of WRC-2007 and to initiate, as soon as possible, the necessary consultation with Member States,

resolves

to convene a World Radiocommunication Conference (WRC-2007) in Geneva (Switzerland) from 8 October to 2 November 2007 with the following agenda:

1.	on the basis of proposals from administrations, taking account of the results of WRC-2003 and the Report of the Conference Preparatory Meeting, and with due regard to the requirements of existing and future services in the bands under consideration, to consider and take appropriate action with respect to the following items:

  - requests from administrations to delete their country footnotes or to have their country name deleted from footnotes, if no longer required, in accordance with Resolution 26 (Rev.WRC-97);

1.2	to consider allocations and regulatory issues related to the Earth exploration-satellite (passive) service, space research (passive) service and the meteorological satellite service in accordance with Resolutions 746 (WRC-2003) and 742 (WRC-2003);

1.3	in accordance with Resolution 747 (WRC-03), consider upgrading the radiolocation service to primary allocation status in the bands 9 000 - 9 200 MHz and 9 300 - 9 500 MHz and extending by up to 200 MHz the existing primary allocations to the Earth exploration-satellite service (EESS) (active) and the space research service (SRS) (active) in the band 9 500 - 9 800 MHz without placing undue constraint on the services to which the bands are allocated;

1.4	to consider frequency-related matters for the future development of IMT-2000 and systems beyond IMT-2000 taking into account the results of ITU-R studies in accordance with Resolution 228 (Rev. WRC-2003);

1.5	to consider spectrum requirements and possible additional spectrum allocations for aeronautical telecommand and high bit-rate aeronautical telemetry, in accordance with Resolution 230 (WRC-2003);

1.6	to consider additional allocations for the aeronautical mobile (R) service in parts of the bands between 108 MHz and 6 GHz, in accordance with Resolution 414 (WRC-2003) and, to study current satellite frequency allocations, that will support the modernization of civil aviation telecommunication systems, taking into account Resolution 415 (WRC-2003);

1.7	to consider the results of ITU-R studies regarding sharing between the mobile-satellite service and the SRS (passive) in the band 1 668 - 1 668.4 MHz, and between the mobile-satellite service and the mobile service in the band 1 668.4 - 1 675 MHz in accordance with Resolution 744 (WRC-2003);

1.8	to consider the results of ITU-R studies on technical sharing and regulatory provisions for the application of high altitude platform stations operating in the bands 27.5 - 28.35 GHz and 31 - 31.3 GHz in response to Resolution 145 (WRC-2003), and for high altitude platform stations operating in the bands 47.2 -47.5 GHz and 47.9 - 48.2 GHz in response to Resolution 122 (Rev.WRC-2003);

1.9	to review the technical, operational and regulatory provisions applicable to the use of the band 2 500 - 2 690 MHz by space services in order to facilitate sharing with current and future terrestrial services without placing undue constraint on the services to which the band is allocated;

1.10	to review the regulatory procedures and associated technical criteria of Appendix 30B without any action on the allotments, the existing systems or the assignments in the List of Appendix 30B;

1.11	to review sharing criteria and regulatory provisions for protection of terrestrial services, in particular the terrestrial television broadcasting service, in the band 620 - 790 MHz from broadcasting-satellite service networks and systems, in accordance with Resolution 545 (WRC-2003);

1.12	to consider possible changes in response to Resolution 86 (Rev. Marrakesh, 2002) of the Plenipotentiary Conference: “Advance publication, coordination, notification and recording procedures for frequency assignments pertaining to satellite networks” in accordance with Resolution 86 (WRC-2003);

1.13	taking into account Resolutions 729 (WRC-97), 351 (WRC-2003) and 544 (WRC-2003), to review the allocations to all services in the HF bands between 4 MHz and 10 MHz, excluding those allocations to services in the frequency range 7 000 - 7 200 kHz and those bands whose allotment plans are in Appendices 25, 26 and 27 and whose channelling arrangements are in Appendix 17, taking account of the impact of new modulation techniques, adaptive control techniques and the spectrum requirements for HF broadcasting;

1.14	to review the operational procedures and requirements of the Global Maritime Distress and Safety System (GMDSS) and other related provisions of the Radio Regulations, taking into account Resolutions 331 (Rev.WRC-2003) and 342 (Rev.WRC-2000) and the continued transition to the GMDSS, the experience since its introduction, and the needs of all classes of ships;

1.15	to consider a secondary allocation to the amateur service in the frequency band 135.7 - 137.8 kHz;

1.16	to consider the regulatory and operational provisions for maritime mobile service identities (MMSIs) for equipment other than shipborne mobile equipment, taking into account Resolutions 344 (Rev.WRC-2003) and 353 (WRC-2003);

1.17	to consider the results of ITU-R studies on compatibility between the fixed-satellite service and other services around 1.4 GHz, in accordance with Resolution 745 (WRC-2003);

1.18	to review pfd limits in the band 17.7 - 19.7 GHz for satellite systems using highly inclined orbits, in accordance with Resolution 141 (WRC-2003);

1.19	to consider the results of the ITU-R studies regarding spectrum requirement for global broadband satellite systems in order to identify possible global harmonized fixed-satellite service frequency bands for the use of Internet applications, and consider the appropriate regulatory/technical provisions, taking also into account No. 5.516B;

1.20	to consider the results of studies, and proposals for regulatory measures if appropriate regarding the protection of the EESS (passive) from unwanted emissions of active services in accordance with Resolution 738 (WRC-2003);

1.21	to consider the results of studies regarding the compatibility between the radio astronomy service and the active space services in accordance with Resolution 740 (Rev.WRC-2003), in order to review and update, if appropriate, the tables of threshold levels used for consultation that appear in the Annex to Resolution 739 (WRC-2003);

2.	to examine the revised ITU-R Recommendations incorporated by reference in the Radio Regulations communicated by the Radiocommunication Assembly, in accordance with Resolution 28 (Rev.WRC-2003), and to decide whether or not to update the corresponding references in the Radio Regulations, in accordance with principles contained in the Annex to Resolution 27 (Rev.WRC-2003);

3.	to consider such consequential changes and amendments to the Radio Regulations as may be necessitated by the decisions of the conference;

4.	in accordance with Resolution 95 (Rev.WRC-2003), to review the Resolutions and Recommendations of previous conferences with a view to their possible revision, replacement or abrogation;

5.	to review, and take appropriate action on, the Report from the Radiocommunication Assembly submitted in accordance with Nos. 135 and 136 of the Convention;

6.	to identify those items requiring urgent action by the Radiocommunication Study Groups in preparation for the next world radiocommunication conference;

7.	in accordance with Article 7 of the Convention:

7.1	to consider and approve the Report of the Director of the Radiocommunication Bureau:

–	on the activities of the Radiocommunication Sector since WRC-2003;

–	on any difficulties or inconsistencies encountered in the application of the Radio 	Regulations; and

–	on action in response to Resolution 80 (Rev.WRC-2000);

7.2	to recommend to the Council items for inclusion in the agenda for the next WRC, and to give its views on the preliminary agenda for the subsequent conference and on possible agenda items for future conferences, taking into account Resolution 803 (WRC-2003),

instructs the Director of the Radiocommunication Bureau

to make the necessary arrangements to convene meetings of the Conference Preparatory Meeting and the Special Committee on Regulatory/ Procedural Matters and to prepare a report to WRC-2007,

instructs the Secretary-General

1.	to make all the necessary arrangements, in agreement with the Director of the Radiocommunication Bureau, for the convening of the conference;

2.	to communicate this resolution to international and regional organizations concerned.

- END -

# Footnotes

This paragraph will be inserted in the final version of the ICAO position after being approved by Council.

African Telecommunication Union (ATU), Arab Group, Asia-Pacific Telecommunity (APT), European Conference of Postal and Telecommunications Administrations (CEPT) and the Inter-American Telecommunication Commission (CITEL)