|  | International Civil Aviation Organization WORKING PAPER | ACP-WGF14/WP-5 20/06/05 |
| --- | --- | --- |

AERONAUTICAL COMMUNICATIONS PANEL (ACP)

FOURTEENTH MEETING OF WORKING GROUP F

# Malmo, Sweden 22 – 26 August 2005

| Agenda Item 6: | VDL frequency assignment planning |
| --- | --- |

FREQUENCY ASSIGNMENT PLANNING CRITERIA FOR VDL MODES 2, 3 AND 4

(Presented by the Secretary; updated by Y. Nakatani)

SUMMARY

This paper presents the results of the review of the frequency assignment planning criteria which were reviewed at WG B-17 in October 2004.

ACTION

The WG Whole is invited to approve these criteria

This material is intended to be published in the ICAO Handbook on aviation spectrum requirements; material should be included  in Annex 10 to refer to this Handbook. Also, ICAO Regions should be invited to include this material in their frequency planning process.

# INTERFERENCE THRESHOLDS

  - The interference threshold for the VHF digital link (VDL) is specified (Annex 10, Volume III, Part I, paragraph 6.3.5.1) as follows:

- VDL Mode 2 maximum corrected bit error rate (BER) is 1 in 104;

Note. The uncorrected BER value of 1 in 103 is to be used in the testing of equipment. The forward error correction method used in VDL Mode 2 (Annex 10, Volume III, Part I, paragraph 6.4.3.1.2.1 refers) translates an uncorrected BER of 1 in 103 into a corrected BER of 1 in 104 (See also MOPS for VDL Mode 2).

- VDL Mode 3 maximum uncorrected bit error rate is 1 in 103; and

- VDL Mode 4 maximum uncorrected bit error rate is 1 in 104.

Note.- The BER value for VDL Mode 4 corresponds to a message error rate (MER) of approximately 2 in  102 using the formula MER=1-(1-BER)216 and assuming a one slot message with 216 bits of data. VDL Mode 4 does not provide forward error correction of the data.

# SIGNAL PARAMETERS

  - The values for the radio frequency signal in Table 1 are to be used in the testing of equipment and the development of separation criteria for VDL.

2.2.	The VDL interference immunity criteria (D/U* ratio) which are identified in these VDL frequency assignment planning criteria and developed in accordance with the test methods in Section 4 are defined as follows:

”the protection parameter (as specified in section 3, e.g. an S/P ratio of 6 dB) shall be met with the specified minimum desired signal level (dBm) at the receiver input (as specified in Table 1) and an undesired signal with a signal level (dBm) at the receiver input causing interference not exceeding the protection parameter; the D/U* ratio is the ratio between the two signal levels as measured on their transmitted frequency (either co- or adjacent to the desired frequency).”

Table 1.

| Parameter | DSB-AM | DSB-AM | VDL-M2 | VDL-M2 | VDL-M3 | VDL-M3 | VDL-M4 | VDL-M4 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| TRANSMITTER | Airborne | Ground | Airborne | Ground | Airborne | Ground | Airborne | Ground |
| Output power transmitter | 44 dBm (25 W) | 50 dBm (100 W) | 42 dBm (16 W) | 44 dBm (25 W) | 44 dBm (25 W) | 44 dBm (25 W) | 42 dBm (15 W) | 45 dBm (32 W) |
| Feeder loss (assumed) | -3 dB | -3 dB | -3 dB | -3 dB | -3 dB | -3 dB | -3 dB | -3 dB |
| Antenna gain (assumed) | 0 dB | 2 dB | 0 dB | 2 dB | 0 dB | 2 dB | 0 dB | 2 dB |
| EIRP | 41 dBm (12.5 W) | 49 dBm (80 W) | 39 dBm (8W) | 43 dBm (20 W) | 41 dBm (12.5 W) | 43 dBm (20 W) | 40 dBm (10 W) | 44 dBm (25 W) |
| Adjacent channel emission (Transmitter) for VDL specified in Annex 10, Vol. III, Part I, paragraph 6.3.4 |
| 1st adj ch. (16 kHz bandwidth) | Not specified in Annex 10 | -18 dBm | -18 dBm | -18 dBm | -18 dBm | -18 dBm | -18 dBm |
| 2nd adj ch. (25 kHz bandwidth) | Not specified in Annex 10 | -28 dBm | -28 dBm | -28 dBm | -28 dBm | -28 dBm | -28 dBm |
| 4th adj ch. (25 kHz bandwidth) | Not specified in Annex 10 | -38 dBm | -38 dBm | -38 dBm | -38 dBm | -38 dBm | -38 dBm |
| 8th adj ch. (25 kHz bandwidth) | Not specified in Annex 10 | -43 dBm | -43 dBm | -43 dBm | -43 dBm | -43 dBm | -43 dBm |
| 16th adj ch. (25 kHz bandwidth) | Not specified in Annex 10 | -48 dBm | -48 dBm | -48 dBm | -48 dBm | -48 dBm | -48 dBm |
| 32nd adj ch. (25 kHz bandwidth) | Not specified in Annex 10 | -53.dBm | -53.dBm | -53.dBm | -53.dBm | -53.dBm | -53.dBm |
| RECEIVER |
| Min signal at receiver antenna Annex 10, Vol. III | 75 μV/m (-82 dBm) part II 2.2.1.2 | 20 μV/m (-93 dBm) part II 2.3.1.2 | 75 μV/m (-82 dBm) part I 6.2.2. | 20 μV/m (-93 dBm) part I 6.3.2 | 75 μV/m (-82 dBm) part I 6.2.2. | 20 μV/m (-93 dBm) part I 6.3.2 | 35 μV/m (-88 dBm) part I 6.9.5.1.1.1 | 35 μV/m (-88 dBm) part I 6.9.5.1.1.1 |
| Feeder loss | -3 dB | -3 dB | -3 dB | -3 dB | -3 dB | -3 dB | -3 dB | -3 dB |
| Antenna gain | 0 dB | 2 dB | 0 dB | 2 dB | 0 dB | 2 dB | 0 dB | 2 dB |
| Min. signal at receiver input | -85 dBm | -94 dBm | -85 dBm | -94 dBm | -85 dBm | -94 dBm | -91 dBm | -89 dBm |
| Out-of-band immunity performance of receiver as per Annex 10, Volume III, Part I, paragraph 6.3.5.3.(VDL) and Volume III, Part II, paragraph 2.3.2.8 (DSB-AM). |
| 1st adj. Ch |  |  | -40 dB | -40 dB | -40 dB | -40 dB | -40 dB | -40 dB |
| 4th adj. Ch | -50 dB | -50 dB | -60 dB | -60 dB | -60 dB | -60 dB | -60 dB | -60 dB |

Conversion from input power (dBm) to field strength (μV/m and v.v.) was done on the basis of the following formula: Pr = E - 20logF - 167.2; where Pr is isotropically received power (dB(W)), E is the electric field strength (dB(μV/m) and F is the frequency (GHz) (ITU-R Recommendation PN.525-2 refers).

This formula can be converted in

10logPr = 20logE – 20logF-77.2 where Pr is signal at receiver antenna (in space) in mW, E is the field strength at the antenna in µV/m and F is the frequency f in MHz.

# TESTING PARAMETERS

## Interfered station: DSB-AM (air and ground receiver)

Characteristics of the desired (interfered) DSB-AM station

    - Minimum (desired) signal levels at receiver input to be used in the test measurements are:

- ground stations -94 dBm; and

- aircraft stations -85 dBm.

    - Protection parameters:

Table 2.

| Interfering station | VDL M2 | VDL M3 2) | VDL M4 |
| --- | --- | --- | --- |
| S/P ratio 3) | 6 dB | 18 dB 2) | 12 dB |
| Channel load interferer | 2% | 1 timeslot 1) 4 timeslots 1) | Various (see Table 6 below) |

1)	1 timeslot operation used for all tests, except squelch break for which 4 slots are operating simultaneously.

2)	Only aircraft DSB-AM receivers are to be considered.

3)	Accepted values after evaluation of audio samples of interference.

Note.- Either the 6 dB (S+N)/N ratio needs to be confirmed for VDL Mode 3 and 4 or it needs to be demonstrated that the S/P ratio is more constraining than the required (S+N)/N ratio.

## Interfered (desired) VDL Mode 2 station (air and ground receiver)

Characteristics of the interfered (desired) VDL Mode 2 station

    - Characteristics of the signals level at receiver input to be used in the test measurements are:

- ground stations: -94 dBm;

- aircraft stations: -85 dBm;

- channel loading of the VDL Mode 2 is 20% (for testing with VDL Mode 4 the channel loading of the VDL Mode 2 is 100%).

    - Protection parameter : The bit error rate for VDL Mode 2 shall not exceed 1 in 103 (uncorrected).

For all type of interferers with the characteristics shown in Table 3.

Table 3 Characteristics of the interfering (undesired) signals.

| Interfering station ( | DSB-AM | VDL M2 | VDL M3 | VDL M4 |
| --- | --- | --- | --- | --- |
| Channel load interferer | Voice with 30% modulation depth1) | Channel loading 2% | Maximum loading with 4 time slots | 100%2) |

1)	See paragraph 4.3.a

2)	Correction factors need to be applied to relate these values to particular operational scenarios. These are under development.

Note.- The application of a channel loading of 2% when VDL Mode 2 is the interfering (undesired) signal needs further clarification

## Interfered (desired) station VDL Mode 3 (air and ground receiver)

Characteristics of the interfered (desired) VDL Mode 3 station

    - Minimum (desired) level at receiver input to be used in the measurements are:

- ground stations: -94 dBm; and

- aircraft stations: -85 dBm.

    - Protection parameters

The bit error rate for VDL Mode 3 shall not exceed 1 in 103 (uncorrected) for all type of interferers with the characteristics shown in Table 4.

Table 4 Characteristics of the interfering (undesired) signals.

| Interfering station ( | DSB-AM | VDL M2 | VDL M3 | VDL M4 |
| --- | --- | --- | --- | --- |
| Chanracteristcs of the interfering (undesired) signal | Voice with 90% modulation depth1) |  | Maximum loading with 4 time slots |  |

1)	See paragraph 4.3.a

## Interfered station VDL Mode 4 (air and ground receiver)

Characteristics of the desired (interfered)VDL Mode 4 station

    - Minimum (desired) signal level at receiver input to be used in the measurements are:

- ground stations -89 dBm;

- aircraft stations -91 dBm; and

- channel load: 100 %.

    - Protection parameters

The message error rate (MER) for VDL Mode 4 shall note exceed 2 in 102 (which corresponds to a uncorrected bit error rate of 1 in 104 bit error rate) for all type of interferers (undesired signal) with the characteristics shown in Table 5.

Table 5 Channel loading of the interfering (undesired) signals

| Interfering Station ( | DSB-AM | VDL M2 | VDL M3 | VDL M4 |
| --- | --- | --- | --- | --- |
| Channel loading of the interfering (undesired) signal | Voice with 90% peak modulation depth1) | 2 % |  | Various 2) (see Paragraphs 3.5 and 3.6 below) |

1)	See paragraph 4.3.a

2)	Correction factors need to be applied to relate these values to particular operational scenarios. These are under development.

## VDL Mode 4 interferer channel loading

Table 6.

| Channel type | Channel loading of interferer |
| --- | --- |
|  | Scenario 1 Aircraft on ground vs aircraft on ground | Scenario 2 Aircraft on ground vs ground station | Scenario 4 Aircraft vs aircraft both airborne |
|  |  | Case A ( ground station as interferer | Case B ( aircraft as interferer |  |
| ADS-B | 6.7 % | 3.3 % | 6.7 % | 0.44 % |
|  | 5 x 1-slot per second | 3 x 1-slot plus 1 x 2-slot per two seconds | 5 x 1-slot per second | 1 x 1-slot per three seconds |
| Point-to-point comms | 1.7 % | 40 % | 1.7 % | 0.33 % |
|  | 5 x 1-slot and 5 x 2-slot per 12 seconds | 10 x 1-slot plus 20 x 2-slot per second | 5 x 1-slot and 5 x 2-slot per 12 seconds | 1 x 1-slot and 1 x 2-slot per 12 seconds |
| TIS-B | 0 % | 90 % | 0 % | 0 % |
|  | - | 22 x 3-slot per second | - | - |

## Summary of VM4 victim loadings

Table 7.

| Channel type | Channel loading of victim |
| --- | --- |
|  | Scenario 1 Aircraft on ground vs aircraft on ground | Scenario 2 Aircraft on ground vs ground station | Scenario 4 Aircraft vs aircraft both airborne |
|  |  | Case A - aircraft as victim | Case B - ground station as victim |  |
| ADS-B | 1.3 % | 1.3 % | 3.3 % | 0.44 % |
|  | 1-slot per second | 1-slot per second | 3 x 1-slot and 1 x 2-slot per two seconds | 1 x 1-slot per three seconds |
| Point-to-point comms | 0.33 % | 0.33 % | 40 % | 0.33 % |
|  | 1 x 1-slot and 1 x 2-slot per 12 seconds | 1 x 1-slot and 1 x 2-slot per 12 seconds | 10 x 1-slot and 20 x 2-slot per second | 1 x 1-slot and 1 x 2-slot per 12 seconds |
| TIS-B | 0 % | 0 % | 90 % | 0 % |
|  | - | - | 22 x 3-slot per second | - |

# TEST METHODS

Test setup for testing of interference into a DSB-AM receiver caused by VDL Mode 2, 3 and 4 signals and for testing of interference into a VDL receiver caused by DSB-AM or VDL signals is given in Figure 1.

Figure 1 Test Setup

## Impact of VDL signal on DSB-AM receiver (measuring of D/U ratio)

    - The test methods in 4.2 to 4.6 below can be used to assess the impact of VDL signals into a DSB-AM receiver and are based on measuring the ratio of power of the interfered (desired) and interfering (undesired) signal levels at the receiver input.

    - Tests on adjacent channels were made with 25 kHz increments. Measurements made with 25 kHz equipment at a given frequency separation (kHz) would also apply to 8.33 kHz equipment with the same frequency separation (kHz). The results are presented with reference to the adjacent 25 kHz channel number. Further work is necessary to identify if the frequency separation for 8.33 kHz equipment can be reduced. Also, material needs to be developed with regard to the separation between VDL and DSB-AM with 50 kHz channel spacing.

## Test procedure for measuring the squelch break of the DSB-AM receiver (all VDL modes)

- no desired DSB-AM signal is present; and

- co- and adjacent channel operation. The undesired VDL signal source is tuned to the same frequency as the DSB-AM receiver or the 1st, 2nd, 3rd, 4th, 5th, 10th, 20th and 40th adjacent channel with increments of 25 kHz. The undesired VDL signal level is increased until the squelch is lifted. The level is recorded.

## Test procedure for measuring the D/U signal ratio on the desired DSB-AM channel by the interfering (undesired) VDL Mode 3. (Evaluation of the effect of the interference on the audio output of the receiver)

- the desired DSB-AM signal source is set to produce a signal level of -85dBm (for aircraft receiver testing) or -94dBm (for ground equipment testing) at the DSB-AM receiver input, 90% peak amplitude modulation with ATC phrases at the input of the DSB-AM receiver. This corresponds to 30% modulation with a 1 kHz tone;

- the undesired VDL Mode 3 signal source is set to give a 30 dB D/U at the centre frequency of the desired AM signal (it needs to be checked if this value is correct). The DSB-AM receiver is tuned to the same frequency. A recording is made of the audio output from the receiver for each adjacent channel;

- the undesired VDL Mode 3 signal is then increased to give a 30 dB D/U in the pass band of the DSB-AM receiver on the first and subsequent adjacent channels and a recording is made of the audio output from the receiver for each adjacent channel; and

- a listening panel then assesses the quality of the audio results recorded, scoring each.

Note.- The D/U in this section is the ratio (dB) between the desired and undesired signal in the DSB-AM receiver passband.

## Test procedure for assessing the impact of an undesired VDL signal on a desired DSB-AM receiver. (Signal + noise to noise ratio (S+N)/N and signal to pulse (S/P) ratio)

    - The test methods in 4.4.2 and 4.4.3 below can be used to assess separately the effects of a digital signal on a DSB-AM receiver. By separating the effects of the pulse modulation and continuous modulation of a digital signal on the audio signal, these two objective parameters can be separately measured and tested. In the presence of a desired signal, the signal + noise to noise ((S+N)/N) ratio and signal to pulse (S/P) ratio as specified in Table 2 are considered at the audio output of the receiver. The level of acceptability of these (S+N)/N ratios and S/P ratios was established through varying the ratios level and through conducting subjective tests with audio samples. The various (S+N)/N and S/P ratios in Table 2 were developed with this method.

    - Test method for measuring the (S+N)/N ratio degradation

- the desired DSB-AM signal source is set so as to produce a signal level as indicated in Table 2 of paragraph 3.1 at the DSB-AM receiver input, 30% amplitude modulated with a 1 kHz tone;

- co-and adjacent channel operation. The undesired VDL signal source is set in continuous mode1) with a centre frequency equal to that of the DSB-AM receiver or the 1st, 2nd, 3rd, 4th, 5th, 10th, 20th or 40th adjacent channel. The level of undesired VDL signal source at the input of the DSB-AM receiver is varied until a (S+N)/N degradation consistent with Table 2 is measured at the audio output receiver. The level of the undesired VDL signal at the receiver input is noted. The audio distortion is checked to ensure that it is less than 10%. If this is not the case then the undesired VDL signal which is level required to achieve 10% audio distortion is measured and noted.

- Continuous mode refers to a continuous transmission of data. This is obtained by removing the ramp up and ramp down sequences in the VDL, which results in VDL Mode 3 having the same continuous mode characteristics as VDL Mode 2 since these two systems have the same modulation scheme.

    - Test method for measuring the signal-to-pulse (S/P) ratio

- the desired DSB-AM signal source is set so as to produce a signal level as indicated in paragraph 3.1.1, with a 30% modulated 1 kHz tone at the input of the DSB-AM receiver as reference signal S. The level of this reference signal is measured at the audio output of the receiver;

- after removal of the reference signal, the undesired VDL signal is added to the receiver input and set to achieve S/P ratios not greater than those specified in Table 2, where S is the level of the reference signal and P2) is the peak level of the pulsed signal measured at the audio output of the DSB-AM receiver; and

- co- and adjacent channel operation. The undesired VDL signal source is set in pulse (burst) mode with a centre frequency equal to that of the DSB-AM receiver or the 1st, 2nd, 3rd, 4th, 5th, 10th, 20th or 40th adjacent channel. The level of the undesired VDL signal source at the input of the DSB-AM receiver is varied until the S/P ratios in Table 2 are met. This level is noted.

- Audio pulses are the remaining pulses on the interfered (desired) audio signal and are caused through the ramp up and ramp down sequences of the VDL.

Note.- When testing the interference from VDL Mode 2 into the DSB-AM receiver, it was observed that the D/U* ratio obtained when measuring the (S+N)/N ratio is within the same range or lower than those obtained when measuring the S/P ratio. Therefore only the channel rejection characteristics obtained when measuring S/P ratios were considered when developing protection requirements and separation distances.

## Test procedure for assessing the impact of either a undesired DSB-AM signal or undesired VDL signal on a desired VDL Mode 2, Mode 3 or Mode 4 receiver

Test method for measuring the bit error rate of the VDL

- the desired VDL signal source is set so as to produce a signal level as indicated in paragraph 3.2 (VDL Mode 2), paragraph 3.3 (VDL Mode 3) or paragraph 3.4 (VDL Mode 4) at the input of the desired VDL receiver. The VDL receiver is tuned to the same frequency as the desired VDL signal source;

- co-and adjacent channel operation. The undesired VDL or DSB-AM signal source is tuned to the same frequency as the desired VDL receiver or the 1st, 2nd, 3rd, 4th, 5th, 10th, 20th or 40th adjacent channel. The level of the undesired signal VDL or DSB-AM signal source is increased until the bit error rate, as specified in Annex 10 (see paragraph 1.1) is reached but not exceeded. The level of the undesired signal source at the input of the VDL receiver is noted. The protection parameters of the undesired signal source are as specified in section 3.

## Test procedure for assessing the impact of anundesired VDL Mode 4 signal on VOR or ILS receiver

VOR receiver testing (see test setup below)

- characteristics of the VOR;

- channel spacing for VOR receiver is 50 kHz;

- co- and adjacent channel interference shall be measured (1st, 2nd, 3rd and 4th adjacent VDL Mode 4 channel with 25 kHz increments);

- a change in the VOR bearing of 0.3( due to the interference of VDL Mode 4 shall be considered as interference threshold. (A change of 0.3( in the selected VOR bearing corresponds to a deviation in the VOR course indicator of 4.5 μA);

- VOR frequencies 112 MHz, 115 MHz and 117.975 MHz shall be tested;

- the level of the VOR signal at the input of the VOR receiver shall be set at -79 dBm.

- characteristics of the VDL Mode 4 signal;

- the VDL Mode 4 interference source shall be incremented in steps of 25 kHz;

- the following VDL Mode 4 duty cycles shall be investigated:

- 1.3% duty cycle (one sync burst in one slot every second), simulating the worst case co-site (on-board an aircraft) scenario;

- 2.7% duty cycle (two slot burst transmissions in every second slot), simulating the worst case co-site (on-board) scenario for transmission of e.g. TCP-information;

- 50% duty cycle (sync burst transmissions in very second slot), simulating a medium dense scenario of interferers at equal distance;

- 50% duty cycle (two slot transmissions in every other two slots), simulating a medium dense scenario of interferers at equal distance. The undesired VDL Mode 4 signal is then increased to produce a change in the VOR bearing of 0.3 degree;

- the undesired VDL Mode 4 signal is then increased to produce a change in the VOR bearing of 0.3 degree. This corresponds to a change in the course deflection current of 4.5 μA.

Note.- 50% duty cycle leads to a beat frequency of 37 Hz. VOR's are rather sensitive against low beat frequencies in the order of 30 Hz. This scenario should be considered as a medium dense scenario with interferes at equal distance.

ILS-localizer receiver testing(same test setup as for VOR)

- characteristics of the ILS-localizer;

- channel spacing for ILS-localizer receiver is 50 kHz;

- co- and adjacent channel interference shall be measured (1st, 2nd, 3rd and 4th adjacent VDL Mode 4 channel with 25 kHz increments);

- a change in the ILS-localizer difference in depth of modulation (DDM) of 0.093 due to the interference of VDL Mode 4 shall be considered as interference threshold. (A change of 0.093 in the DDM corresponds to a deviation in the ILS course indicator of 4.5 μA);

- ILS-localizer frequencies 111.95 MHz shall be tested;

- the level of the ILS-localizer signal at the input of the localizer receiver shall be set at -86 dBm.

- characteristics of the VDL Mode 4 signal;

- the VDL Mode 4 interference source shall be incremented in steps of 25 kHz;

- the following VDL Mode 4 duty cycles shall be investigated:

- 1.3% duty cycle (one sync burst in one slot every second), simulating the worst case co-site (on-board an aircraft) scenario;

- 2.7% duty cycle (two slot burst transmissions in every second slot), simulating the worst case co-site (on-board) scenario for transmission of e.g. TCP-information;

- 50% duty cycle (sync burst transmissions in very second slot), simulating a medium dense scenario of interferers at equal distance;

- 50% duty cycle (two slot transmissions in every other two slots), simulating a medium dense scenario of interferers at equal distance;

- the undesired VDL Mode 4 signal is then increased to produce a change in the ILS-localizer bearing of 0.093 DDM. This corresponds to a change in the course deflection current of 4.5 μA.

# OUT-OF-BAND IMMUNITY PERFORMANCE

Note.- When in this section reference is made to adjacent channels, this reference is to the actual adjacent channel with 25 kHz separation.

## VDL Mode 2

VDL Mode 2 and DSB-AM systems

    - The following interference scenarios have been analyzed:

- interference caused by VDL Mode 2 into DSB-AM systems;

- interference caused by DSB-AM systems into VDL Mode 2; and

- interference from VDL Mode 2 into VDL Mode 2.

      - Interference caused by VDL Mode 2 into DSB-AM systems

      - Co-channel interference

No measurements addressing the co-channel interference from DSB-AM into VDL Mode 2 and from VDL Mode 2 into DSB-AM have been developed, as the same channel should not be used for VDL Mode 2 and DSB-AM. To avoid the need for interregional coordination, globally harmonized frequencies should be used for VDL Mode 2. Where possible, the band 136-137 MHz should be reserved for VDL operations. Coordination with ICAO regional office has been conducted to ensure that the band is reserved. Coordination of specific assignments still needs to be conducted in particular regions.

      - Adjacent channel interference

        - Annex 10, Volume III, Part II, paragraph 3.2.8.2 contains the immunity criteria for DSB-AM receiving systems against interference from any VDL station.

        - It has been observed, on the basis of testing results of a number of aircraft DSB-AM receivers in accordance with the test method described in section 4.6, that the immunity performance characteristics in Annex 10 would result in overly pessimistic frequency assignment criteria to protect DSB-AM systems when interfered with a VDL Mode 2 signal. The DSB-AM receivers tested, which were considered to be representative for the airborne receivers currently in use (with 25 kHz characteristics), showed significantly better immunity performance characteristics than those given in Annex 10.

        - Considering the worst case test results for each of these receivers, the following interference immunity performance characteristics for DSB-AM systems when interfered with a VDL Mode 2 signal D/U* ratios were developed:

Table 8. D/U* ratios protection parameter S/P=6dB

(desired DSB-AM and undesired VDL Mode 2)

| Adjacent channel | D/U* ratio (dB) |
| --- | --- |
| 1 | -34 |
| 2 | -53 |
| 3 | -60 |
| 4 | -63 |
| 5 | -65 |
| 10 | <-65 |
| 20 | <-65 |
| 40 | <-65 |

Note.- These interference immunity characteristics need to be incorporated in Annex 10 and their compliance with MOPS needs to be assessed.

      - Interference caused by DSB-AM systems into VDL Mode 2

        - Co-channel interference (see paragraph 5.1.1.2.)

        - Adjacent channel interference

Annex 10, Volume III, Part I paragraph 6.3.5.3 contains the immunity criteria for VDL aircraft receiving systems against interference from any source (VDL or DSB-AM).

It has been observed, on the basis of testing results in accordance with the test method described in section 4.7, that the immunity performance characteristics in Annex 10 would result in overly pessimistic frequency assignment criteria to protect VDL Mode 2 systems when interfered with a DSB-AM signal. The VDL Mode 2 receivers tested showed significantly better immunity performance characteristics than those given in Annex 10.

Considering these test results, the following interference immunity performance characteristics for VDL Mode 2 systems when interfered with a DSB-AM 2 signal D/U* ratios were developed:

Table 9. D/U* ratios Uncorrected BER 1 in 103

for desired VDL Mode 2 and undesired DSB-AM signals

| Adjacent channel | D/U* ratio (dB) |
| --- | --- |
| 1 | -33 |
| 2 | -60 |
| 3 | -60 |
| 4 | -66 |
| 5 | -69 |
| 10 | <-69 |
| 20 | <-69 |
| 40 | <-69 |

Note.- These interference immunity characteristics need to be incorporated in Annex 10; compliance with MOPS needs to be assessed.

        - It was concluded that the D/U* ratio for VDL Mode 2 being interfered with DSB-AM systems is better that when DSB-AM systems are being interfered with VDL Mode 2. Therefore, the calculation of minimum geographical separation distances concentrates on the protection of DSB-AM systems.

Squelch break

The squelch break for DSB-AM receivers was measured with VDL Mode 2 signal levels greater than 0 dBm on the second and beyond adjacent channel. It was therefore considered that squelch break is not a parameter to be considered in frequency assignment planning.

Interference from undesired VDL Mode 2 into desired VDL Mode 2

Co-channel interference. The MOPS for VDL Mode 2 specify that the co-channel D/U protection ratio is 20 dB.

Note.- This needs to be incorporated in Annex 10.

Measurements on an airborne VDL Mode 2 receiver (in accordance with the test method in section 4.7) showed the following D/U*.

Table 10. D/U* ratios (uncorrected BER 1 in 103)

| Adjacent channel | D/U* ratio (dB) |
| --- | --- |
| 1 | -29 |
| 2 | -66 |
| 3 | -68 |
| 4 | -67 |
| 5 | -67 |

The channel loading on the desired signal is defined in paragraph 3.2.1 and on the undesired signal in paragraph 3.2.2.

# FREQUENCY ASSIGNMENT PLANNING CRITERIA

## Propagation model

    - Separation distances shall be calculated on the basis of free space propagation.

    - The transmission loss (Lbf) using free space propagation characteristics can be calculated as follows:

Lbf (dB) = 20log(f) + 20 log(d) +32.4 (Re. ITU R Recommendation 525-2)	(1)

where:	f = MHz

d = km

## Interference model

Pd - Pu = D/U* = Pd - {(Tu +Lu + Gu) -Lbf} where: Pd, Pu and Tu are expressed in dBm 	(2)

Lu, Gu and Lbf are expressed in dB

From (1) and (2) the separation distance can be calculated by:

20log(d) = D/U* - Pd + Tu + Lu + Gu - 20log(f) - 32.4	(3)

The EIRPu of the undesired transmitter equals Tu + Lu + Gu which converts formula (3) into

20log(d) = D/U* - Pd + EIRPu - 20log(f) - 32.4	(4)

The factor 20log(f) introduces a variation of 1.24 dB in the results of calculating 20 log(d). (20log(f) is for the frequency 136 MHz 42.67 and for 118 MHz 41.43; therefore minimum separation distances are at the lower band edge slightly larger than at 136 MHz.

# SEPARATION DISTANCES FOR VDL MODE 2 (VDL Mode 2 vs DSB-AM and VDL Mode 2 vs VDL Mode2)

The tables provided in this chapter cover six (2+2+2) possible interference pairs (VDL2 aircraft into DSB-AM aircraft and ground station (2); DSB-AM aircraft into VDL2 aircraft and ground station (2); VDL2 aircraft into VDL2 aircraft and ground station(2)).

However, in total, there are 16 interference pairs, not six. The table below maps the 16 cases to the separation distance tables provided in this document and provides explanations for the cases not explicitly treated in the tables:

Table11    (U: Undesired; D: Desired; A/C: aircraft; GS:ground  station)

|  | VDL2 A/C D | VDL2 GS D | DSB-AM A/C D | DSB-AM GS D |
| --- | --- | --- | --- | --- |
| VDL2 A/C U | Table 11-C, left | Table 11-C, right | Table 11-A, left | Table 11-A, right |
| VDL2 GS U | Note 1 | Note 2 | Note 3 | Note 2 |
| DSB-AM A/C U | Table 11-B, left | Table 11-B, right | Note 5 | Note 5 |
| DSB-AM GS U | Note 4 | Note 2 | Note 5 | Note 5 |

Note 1: this is the opposite direction of the case treated in (Table 11-C, right). Calculations (not provided in the document) show that the distances calculated in (Table 11-C, right) are more stringent than those calculated in the opposite direction. Hence no data is provided for the opposite direction in the document.

Note 2: ground-to-ground case (no separation distances discussed in the document - only generic statement in 7.2.13)

Note 3: this case is analogous to Note 1, with reference to (Table 11-B, right).

Note 4: this case is analogous to Note 1, with reference to (Table 11-A, right).

Note 5: already covered by Annex 10 (DSB-AM vs DSB-AM)

It is suggested that the above considerations (and in particular the aspects mentioned Notes 1, 3 and 4) be explained at the relevant points in Section 7 (see below). Additionally, considerations should be given to including in the document at least the three sets of distances addressed by Notes 1, 3 and 4.

When using the interference model as in paragraph 6.2 and formula (4), the following separation distances were calculated, using the relevant information from Table 1 and Tables 8, 9 and 10, as follows:

minimum protection distance for interference from VDL Mode 2 aircraft stations (undesired signal) into desired DSB-AM aircraft stations and desired DSB-AM ground stations with the following parameters:

- EIRPu of undesired VDL Mode 2 aircraft station is 39 dBm;

- Pd of desired DSB-AM aircraft station is -82 dBm at the VDL Mode 2 antenna (signal in space); and

- Pd of desired DSB-AM ground station is -93 dBm at the VDL Mode 2 antenna (signal in space)

Table 11-A / VDL2 (air) > DSB-AM (air, ground).

| Channel | D/U* (dB) | Minimum separation distance for protecting DSB-AM aircraft station | Minimum separation distance for protecting DSB-AM ground station |
| --- | --- | --- | --- |
|  |  | 119 MHz | 128 MHz | 136 MHz | 119 MHz | 128 MHz | 136 MHz |
| 1 | -34 | 4 514 m | 4 196 m | 3 949 m | 16 016 m | 14 889 m | 14 013 m |
| 2 | -53 | 507 m | 471 m | 443 m | 1 797 m | 1 671 m | 1 573 m |
| 3 | -60 | 226 m | 210 m | 198 m | 803 m | 747 m | 703 m |
| 4 | -63 | 160 m | 149 m | 140 m | 569 m | 529 m | 497 m |
| 5 | -65 | 127 m | 118 m | 111 m | 452 m | 420 m | 395 m |

minimum protection distance for interference from undesired DSB-AM aircraft stations into desired VDL-Mode 2 aircraft stations and desired VDL Mode 2 ground stations with the following parameters:

- EIRPu from DSB-AM aircraft station is 41 dBm at the VDL Mode 2 antenna (signal in space);

- Pd VDL Mode 2 aircraft station is -82 dBm at the VDL Mode 2 antenna (signal in space); and

- Pd VDL Mode 2 ground station is -93 dBm at the VDL Mode 2 antenna (signal in space)

Table 11-B / DSB-AM (air) > VDL2 (air, ground).

| Channel | D/U* (dB) | Minimum separation distance for protecting VDL Mode 2 aircraft station | Minimum separation distance for protecting VDL Mode 2 ground station |
| --- | --- | --- | --- |
|  |  | 119 MHz | 128 MHz | 136 MHz | 119 MHz | 128 MHz | 136 MHz |
| 1 | -33 | 6 376 | 5 928 | 5 579 | 22 623 | 21 032 | 19 794 |
| 2 | -60 | 285 | 265 | 249 | 1,011 | 940 | 885 |
| 3 | -60 | 285 | 265 | 249 | 1,011 | 940 | 885 |
| 4 | -66 | 143 | 133 | 125 | 507 | 471 | 443 |
| 5 | -69 | 101 | 94 | 88 | 359 | 334 | 314 |

minimum protection distance for interference from undesired VDL Mode 2 aircraft stations into desired VDL-Mode 2 aircraft stations and desired VDL Mode 2 ground stations with the following parameters:

EIRPu from VDL Mode 2 aircraft station is 39 dBm at the VDL Mode 2 antenna (signal in space);

Pd VDL Mode 2 aircraft station is -82 dBm at the VDL Mode 2 antenna (signal in space); and

Pd VDL Mode 2 ground station is -93 dBm at the VDL Mode 2 antenna (signal in space).

Table 11-C VDL2 (air) > VDL2 (air, ground).

| Channel | D/U* (dB) | Minimum separation distance for protecting VDL Mode 2 aircraft station | Minimum separation distance for protecting VDL Mode 2 ground station |
| --- | --- | --- | --- |
|  |  | 119 MHz | 128 MHz | 136 MHz | 119 MHz | 128 MHz | 136 MHz |
| 1 | -29 | 8 027 | 7 462 | 7 023 | 28 480 | 26 477 | 24 920 |
| 2 | -66 | 113 | 105 | 99 | 402 | 374 | 352 |
| 3 | -68 | 90 | 84 | 79 | 320 | 297 | 280 |
| 4 | -67 | 101 | 94 | 88 | 359 | 334 | 314 |
| 5 | -67 | 101 | 94 | 88 | 359 | 334 | 314 |

Note.- DSB-AM aircraft and ground stations are assumed to have the same immunity performance characteristics as well as VDL Mode 2 aircraft and ground stations.

## VDL Mode 2 and DSB-AM systems

Interference to aircraft in flight(air-to-air interference)

    - The minimum separation of aircraft in this scenario is 600 m (2 000 ft). This corresponds to the operational scenario where two aircraft are flying a parallel track in the same direction on flight levels separated by 600 m (2 000 ft). In some cases flight levels are separated by less than 600 m but this is only applied for aircraft flying in opposite directions.

    - On the basis of the separation distances calculated for the case where DSB-AM is interfered by transmissions from VDL Mode 2 (Table 11-A, left-hand columns), which are more stringent than the distances calculated in the opposite direction of interference (Table 11-B, left-hand columns), protection of DSB-AM systems is obtained at the 2nd adjacent (25 kHz) channel.

Aircraft in flight and ground stations

    - Frequency assignment criteria are based on a minimum separation of 600m between a VDL Mode 2 ground station and an aircraft DSB-AM station. When VDL Mode 2 stations are situated in the vicinity of an airport, consideration needs to be given to the need to secure that this distance is met in all operational circumstances between a ground station and an aircraft station.

    - Protection of a desired VDL Mode 2 ground station from interference from an undesired airborne DSB-AM station at a distance of 600 m is obtained at the fourth adjacent channel (Table 11-B, right-hand columns). It should be noted that separation distances are calculated on the basis of interference from airborne DSB-AM transmitter into VDL Mode 2 ground station (see Table 11-B, right-hand columns), as this case provides more stringent requirements than either the case of a VDL Mode 2 airborne transmitter or the case of a ground transmitter (VDL Mode 2 or DSB-AM). Should the separation distance between the two stations be less than 600 m, or the frequency separation be less than four channels, special measures need to be taken to secure protection. These measures could include to maintain larger frequency separation between the two stations if the separation distance is not met, or to introduce special cavity filters to further attenuate the undesired signal at the ground station. Additional mitigations due to the transient nature of this scenario could also be taken into account.

Interference between aircraft on the ground

    - The minimum distance between aircraft on the ground at an airport can be expected to be between 50 and 100 m. However, the interference immunity performance of DSB-AM and VDL Mode 2 systems, as specified in the SARPs (respectively 50 dB and 60 dB rejection at the 4th channel and beyond), is not sufficient to protect a desired signal at minimum power of -82 dBm at the aircraft antenna from an interfering signal at short distance. For example 72 dB (50 m) to 66 dB (100 m) would be required, using the model in Section 6.

    - Using the same model, and based on the interference immunity performance as specified in the SARPs, it can be seen protection can be guaranteed with a minimum separation distance of 210 m, with a minimum power of -82 dBm at the aircraft antenna. Therefore the reference distance to assess compatibility between VDL Mode 2 and DSB-AM or another VDL Mode 2 station has been set at 210 m.

    - In practice protection at 50 m distance can be achieved with a desired minimum signal level of -70dBm at the aircraft receiver input. It was concluded from measurements on a number of representative airports that this level is achievable in most operational conditions on the ground.

    - In the case of DSB-AM being interfered with VDL Mode 2, all aircraft receivers were found to offer the required interference immunity at the 3rd adjacent channel. However, initially a separation of 5 channels (125 kHz) is to be used when DSB-AM and VDL Mode 2 are operated at the same airport, in order to accommodate for receiver design variations.

    - For 2nd adjacent and higher channels, the D/U* in the reverse case and would result in smaller separation distance than when DSB-AM is interfered by VDL Mode 2. Therefore the separation criteria for VDL Mode 2 interfering to DSB-AM have been used (Table 11-A, right hand columns).

Interference between aircraft onthe ground and ground-station

    - Through a similar reasoning as for in 7.2.5 above, applying both DSB-AM and VDL SARPS immunity performance specifications, it can be found that the interference immunity performance of VDL Mode 2 and DSB-AM systems rejection capability is protecting only a desired signal with a minimum power of -93 dBm at the ground receiver only at a separation (protection) distance of at least 750 m.

    - The protection distance of 750 m is reached from the 4th adjacent channel. (Table 11-B, left-hand side).

    - Special installation and filtering techniques may be applied to ground-stations operating at a fixed frequency with a high sensitivity whereas aircraft radios can not benefit of such mitigation means. In particular, large improvement in interference rejection may be obtained through the addition in the ground receiver station of a cavity filter or a quartz filter.

Interference between ground transmissionstations and ground receiver stations

    - Normally, ground transmitters are geographically separated from ground receiver stations. Transmissions from ground DSB-AM stations may interfere with the (ground) reception of VDL Mode 2 signals and transmission from ground VDL Mode 2 signals may interfere with the (ground) reception of DSB-AM signals. This should be considered in the design of ground station characteristics. Also here, the use of special cavity filters may assist in securing proper functioning of the various communication systems.

## VDL Mode 2 versus VDL Mode 2

Using the propagation model in section 6, minimum separation distances were calculated in Table 11C above.

Interference to aircraft in flight(air-to-air interference)

The required protection distance for 2 aircraft in flight is 600 m. Table 11-C shows that this distance is reached at the 2nd adjacent channel with a very large margin. Therefore, to assign a VDL Mode 2 channel in the same service volume as another VDL Mode 2 channel, a single channel guard band is necessary.

Aircraft on the ground versus aircraft on the ground

With the requirements to protect a minimum power at the antenna input of -82dBm, the reference distance of 210 m is used as in the corresponding DSB-AM. The calculation results show that protection at this distance is achieved at the 2nd adjacent channel. A single channel guard band is necessary for this scenario.

Aircraft on the ground versus ground station

The minimum protection distance at the second adjacent channel for the ground receiver with a power input at the ground receiver of -93 dBm (without additive filtering techniques) is well below the recommended 750 m reference distance and would further get down to less than 100 m with the addition of dedicated filters.

Therefore, to assign a VDL Mode 2 channel for use at an airport in the vicinity of the ground receiver station where another VDL Mode 2 channel is used, a single channel guard band is sufficient.

## Summary of VDL frequency assignment planning constraints

Table 13. 25 kHz guard band channels between different services

| Vs. | Interference Source |
| --- | --- |
|  | DSB-AM | VDL 2 |
|  | A | G | A | G |
| Victim | DSB-AM | - | - | 1 | 1 |
|  | VDL 2 | 1 | 4 | 1 | 1 |

Note: the numbers provided in table 12 are guard channels. The next channel that can be used without frequency assignment planning constraints is 1 higher (e.g.: A desired DSB-AM station that is interfered by a VDL Mode 2 aircraft station, requires one 25 kHz guard band channel. The next channel, 50 kHz away, can be used in the same designated operational coverage without constraints.

- END -

# Footnotes

Values for the out-of-band immunity performance in section 5 (interference susceptibility of the receiver tested) are based upon actual measurements on a number of receivers. Where receivers are used with different characteristics, adjustments in the separation distances are required. For VDL Mode 2, reference is made to working paper 5 submitted to the 11th meeting of WG B of the Aeronautical (Mobile) Communications Panel A(M)CP which is available on http://www.icao.int/anb/panels/acp

For calculating separation distances in section 7, 100W was assumed for the output power of the DSB-AM (voice) ground based transmitter. Typical values of these stations of 25W or 50W will result in smaller separation distances.