|  | International Civil Aviation Organization WORKING PAPER | ACP-WGF14/WP-21 22/08/05 |
| --- | --- | --- |

AERONAUTICAL COMMUNICATIONS PANEL (ACP)

FOURTEENTH MEETING OF WORKING GROUP F

Malmo, Sweden 22 – 26 August 2005

| Agenda Item 3 | : WRC’07 Agenda Item 1.6 |
| --- | --- |

Feasibility of VOR/DME replanning  in Europe to free the sub-band 116 –118 MHz for AM(R)S usage

(Presented by Alain DELRIEU)

SUMMARY

In the frame of the WRC-07 Agenda Item 1.6, besides the identification of new spectrum allocation for AM(R)S in view of introducing a future ground cellular mobile communication system, one potential way forward is to try to expand the current VHF AM(R)S band within the ARNS band below 118 MHz (VOR band). Such potential solution could provide within the European region several hundreds of 8.33 kHz DSB AM channels that could bridge the time gap between 2010 and the actual deployment of the new mobile radio communication component, under study by ICAO/ACP/WGC that is now foreseen by 2020 at the earliest. This paper summarizes a simulation conducted by France to assess the feasibility of this scenario from a strict spectrum management point of view. It indicates that it could possible to free between 1 and 2 MHz below 118 MHz to be allocated to AM(R)S while keeping all the current VOR and VOR/DME assignments through a direct frequency change of all the existing assignments within the VOR upper frequency band (116 MHz – 118 MHz).

ACTION

It is recommended to use this material to ensure that proper decision are taken at ITU WRC 07 to allocate a part of the ARNS band (108 –118 MHz) to AM(R)S to extend the frequency band dedicated to VHF DSB AM communication assignments

# 1.Introduction

One potential way forward identified in Europe to cope with the current and foreseeable frequency congestion within 118 – 137 MHz VHF band, despite the wide introduction of the new 8.33 kHz channel spacing, is to try to reassign the VOR frequencies above 116 MHz within the frequency band below 116 MHz without withdrawing any of those assignments.

A simulation has been conducted by France in order to study the feasibility of this scenario from a point of view strictly limited to  spectrum management

The document in annex provides the complete description of the simulations with the various scenario implemented. The scenario implemented based upon the European Air Navigation Plan COM 3 table, are the following:

- Freeing part of the VOR sub-band

With four sub scenario:

  - 1 MHz vacated

  - 1.5 MHz vacated

  - 2 MHz vacated

  - 2 MHz vacated with a special condition (removing of all MLS associated DME existing  assignments)

- Identification  of the impact of the 2 MHz reduction of the ARNS band on the GBAS deployment capability in Europe through a comparison between :

  - 1775 GBAS requirements assigned within the whole existing ARNS band

  - 1775 GBAS requirements assigned within the reduced ARNS band (108 – 116 MHz)

- Quantification of the gain for AM(R)S after the release of  2 MHz within the ARNS band

# 2. Synthesis of results

## 2.1 VOR reassignment simulation

The following table provides the results of the first set of scenario dealing with existing VOR re-assignments:

| Width of sub-band vacated | 1 MHz | 1.5 MHz | 2 MHz | 2 MHz without MLS-DME |
| --- | --- | --- | --- | --- |
| Nr of VOR and VOR-DME in the sub-band having to be replanned | 133 | 201 | 264 | 264 |
| Successfully replanned VORs | 120 | 178 | 232 | 244 |
| Replanning failures, including: | 13 | 23 | 32 | 20 |
| - Failures (All Land VOR-DME) | 3 | 6 | 10 | 10 |
| - Failures (other VOR-DME) | 8 | 16 | 21 | 9 |
| - Failures (All Land VOR) | 1 | 1 | 1 | 1 |
| - Failures (other VOR) | 0 | 0 | 0 | 0 |

Those tables show that if we consider separately the All Land assignments (that are usually associated with implementation of mobile station during existing VOR renewing) that could probably be reduced in number in the foreseeable future, only 8 assignments were not reassignable in the scenario 1a and only 21 in the scenario 1b. If the MLS/DME constraint is removed the number of blocking assignments is reduced to 9 for the 2 MHz vacation scenario.

Those results shows that depending on specific technical and institutional arrangements the release of up to 2MHz in the ARNS band is feasible

## 2.3. GBAS assignments

The following table provides the result of two comparative exercises of assignments of 1775 GBAS stations within the region within the nominal ARNS band and within the reduced ARNS band (minus 2 MHz). The 1775 GBAS needs are indeed generated by using the existing ILS assignment and generating 50% increase by random duplication of existing ILS assignments.

| Scenario | Destination band | moved VORs | New GBASs | Re-planned GBASs | Failures |
| --- | --- | --- | --- | --- | --- |
| 2A | 108.000 - 116.000 MHz | 178 | 1,775 | 1,668 | 107 |
| 2B | 108.000 - 118.000 MHz | 0 | 1,775 | 1,702 | 73 |

This table shows that the impact of reducing the ARNS band on the flexibility of GBAS deployment in Europe is very limited even in a very demanding scenario in terms of GBAS needs. This second scenario confirms that the reduction of the ARNS band is not a serious issue for the GBAS deployment in Europe.

# Spectrum gain for the AM(R)S VHF assignments

The last part of the simulation concerns the quantification of the gain for the VHF AM(R)S assignments. The freeing of 2 MHz below 118 MHz provides 240 new 8.33 kHz channels that could be used to provide communication services in the upper airspace. The simulation was not really assessing this scenario but the usage of this extra spectrum allocation to satisfy both 25 kHz and 8.33 kHz needs without any discrimination between the nature of the services and including also ATIS and VOLMET services. It shows that the gain was significant even the proposed segregation (usage only for en route upper airspace and for 8.33 kHz assignments). In conclusion it shows that if completely feasible (that is to say that all the other aspects need to be analysed) the spectrum gain will be very significant and will certainly facilitate the filling of the current gap between now and the implementation of the future components of the air/ground mobile communication system.

# 3. Conclusion

The study conducted by France indicates that it could be feasible  from  a pure spectrum management point of view to release  part of the current ARNS band between 108 – 118 MHz to provide extra spectrum for the VHF AM(R)S in conjunction with the use of 8.33 kHz channels, within this new extension of the AM(R)S VHF band, in order to release pressure on the  congested VHF 118-137 MHz usage

PT3 is invited to:

    - take note of the study and of its encouraging results

    - take the appropriate measure to ensure that the allocation of the 116 -  118 MHz part of the ARNS band is also given to AM(R)S on a co-primary basis at the next ITU WRC07, in addition to the existing allocation (since WRC’03, ref. 5.197A) limited for use by VDL Mode 4

encourage the investigation of the other aspects of the use of this part of the ARNS band to cope with the VHF frequency congestion in Europe (e.g. aircraft radio retrofit issue, including flight deck frequency selector,  economical aspect of the VOR frequency changes, timescale of implementation, FM broadcasting compatibility, etc..…)

Version 1.0 - 15 March 2005

PARTIAL REPLANNING

OF THE VOR BAND

DSNA/DTI/SO3      SYSTEX 2

TABLE OF CONTENTS

1.	INTRODUCTION	3

2.	CONTENT OF THE STUDY	3

3.	SCENARIOS STUDIED	4

4.	DATABASES	5

4.1	COM3 database	5

4.2	COM2 database	5

5.	SCENARIO 1: Vacation of the VOR sub-band	6

5.1	Scenario 1A: 1MHz vacated between 117.000 and 118.000	6

5.1.1	Assignments processed	6

5.1.2	Location of the VORs processed	6

5.1.3	List of failures	7

5.2	Scenario 1B: 1.5 MHz vacated between 116.500 and 118.000	8

5.2.1	Assignments processed	8

5.2.2	Location of the VORs processed	8

5.2.3	List of failures	9

5.3	Scenario 1C : 2 MHz vacated between 116.000 and 118.000	10

5.3.1	Assignments processed	10

5.3.2	Location of the VORs processed	10

5.3.3	List of failures	11

5.4	Scenario 1D: 2MHz vacated between 116.000 and 118.000, with MLS-DMEs deleted	12

5.4.1	Assignments deleted	12

5.4.2	Assignments processed	12

5.4.3	Location of the VORs processed	12

5.4.4	List of failures	13

5.5	Scenario 1A, 1B, 1C and 1D: consolidated results	14

6.	SCENARIO 2: Verification of GBAS	15

6.1	Scenario 2A: Planning of 1,775 GBASs between 108.000 and 116.000	15

6.1.1	Assignments processed	15

6.1.2	Location of the failed GBASs	15

6.1.3	List of failures	16

6.2	Scenario 2B: Planning of 1,775 GBASs between 108.000 and 118.000	18

6.2.1	Assignments processed	18

6.2.2	Location of the failed GBASs	18

6.2.3	List of failures	19

6.3	Scenario 2A, 2B: consolidated results	20

7.	SCENARIO 3: Spectrum gains for voice communication	21

7.1	Scenario 3A: Gains associated with the use of a supplementary 2 MHz band	21

7.1.1	Assignments processed	21

7.1.2	Successful assignments	22

7.1.3	Percentage of assignments satisfied	23

7.1.4	List of successful assignments	24

# INTRODUCTION

As part of the preparations for the forthcoming World Radiocommunications Conference (WRC) of the International Telecommuncation Union (ITU) scheduled for 2007, Civil Aviation is studying the possibilities of using the frequency bands allocated to other civil aviation services (mainly the radio navigation service) for the mobile aeronautical communication service in order to find an answer to the current congestion of the VHF band.

One of the options studied involves reassigning the VORs in the higher range (116 – 118 MHz) in the VHF radio navigation band (108 – 118 MHz) to be able to use the higher range for the mobile communication service.

# CONTENT OF THE STUDY

The study involves simulating, on the basis of COM2 and COM3 data from the European Air Navigation Plan, three scenarios for the re-planning of VOR services. These services, whose frequencies are in the band to be vacated (e.g. between 116 and 118 MHz) will be transferred to frequencies elsewhere in the band (e.g. between 108 and 116 MHz).

The objective of the scenarios examined is to make it possible to:

- evaluate the feasibility of reassigning the VHF OmniRange (VOR) from the 116-118 MHz band to elsewhere in the radio navigation band,

- to assess the capacity gained in this way with a view to assigning to it the mobile radio communication services using 8.33 kHz channel spacing,

- to evaluate the capacity for assigning to the lower part of the radio navigation band (108 - 116 MHz) VHF Data Broadcast stations (VDB: system for broadcasting GPS differentials via VHF) associated with the Ground Based Augmentation System (GBAS).

The COM2 and COM3 tables and the planning criteria will conform to those used by EUROCONTROL for the compatibility and re-planning studies in the radio navigation frequency (VOR, ILS, GBAS and DME)  and mobile radio communication bands.

# SCENARIOS STUDIED

Three scenarios will be studied:

The first scenario involves evaluating the possibility of reallocating a frequency to the VOR and VOR/DME services currently in the band to be vacated and identifying the services for which it is impossible to find directly (without using “shift” techniques) a new frequency elsewhere in the band.

This scenario will be examined for three bandwidths to be vacated: 1 MHz, 1.5 MHz and 2 MHz.

The objective of this scenario is to evaluate, for each bandwidth examined, the outstanding difficulties which might require specific action (of the “shift” type).

The second scenario involves verifying that the allocation of new GBAS services is still possible elsewhere in the band. The GBAS services are obtained by copying and “transforming into GBAS” a certain percentage (between 100 and 200%) of existing ILS.

NB:	STNA’s wish to use a percentage of 100% for category I ILS and a percentage of category II/III cannot be fulfilled because no category is indicated in the COM3 table supplied by EUROCONTROL.

The third scenario involves determining the voice communication services (ACC, APP, etc.) which could be accommodated in the higher part of the band, once it has been vacated in this way (1 MHz, 1.5 MHZ et 2 MHz respectively). The services planned will be defined by duplicating the existing services for which it is currently impossible to find a new frequency in the 118 - 137 MHz band. In this scenario, an attempt will be made to assess the actual capacity freed up in the radio navigation bands in order to be able to assess the usefulness of such an initiative.

# DATABASES

The databases were provided by EUROCONTROL on the basis of ICAO’s COM tables, with a number of amendments which make it possible to process assignments with incorrect or missing data for a planning exercise.

## COM3 database

The table below presents a breakdown by service of the assignments of the COM3 table used.

| Code | ILS | ID | VOR | VD | DME | MLS | IDM | NPM | Total |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Services matched | ILS | ILS DME MLS | VOR | VOR DME | DME | MLS DME | ILS DME MLS | MLS |  |
|  | 649 | 525 | 178 | 910 | 523 | 896 | 74 | 17 | 3 772 |

## COM2 database

This is the COM2 database used for block planning.

# SCENARIO 1: Vacation of the VOR sub-band

## Scenario 1A: 1MHz vacated between 117.000 and 118.000

### Assignments processed

| Width of sub-band vacated | 1MHz |
| --- | --- |
| VOR and VOR-DME in the sub-band | 133 |
| Re-planned VORs | 120 |
| Failures, including: | 13 |
| - Failures (All Land VOR-DME) | 3 |
| - Failures (other VOR-DME) | 8 |
| - Failures (All Land VOR) | 1 |
| - Failures (other VOR) | 0 |

### Location of the VORs processed

The failures are shown in red. The VORs, VORTACs and VOR-DMEs which it was possible to re-plan are shown in green.

The icons indicate type of service, as set out below:

|  | : VOR |  | : VOR-TAC |  | : VOR-DME |
| --- | --- | --- | --- | --- | --- |

The large icons identify the “ALL LAND” mobile services.

### List of failures

| Cty | Location | Poly | Type | VHF freq | DOC | VHF pwr | DME pwr |
| --- | --- | --- | --- | --- | --- | --- | --- |
| ED | ALL GERMANY | LAND | VOR | 117.950 | 25/100 | 80L |  |
| ED | BRUNKENDORF |  | VD | 117.700 | 80/500 | 200L | 39 |
| ED | HEHLINGEN |  | VD | 117.300 | 80/500 | 200L | 39 |
| ED | NOERDLINGEN |  | VD | 117.550 | 60/500 | 50 | 37 |
| ED | SAARBRUCKEN |  | VD | 117.000 | 60/500 | 400L | 42 |
| EH | ALL NETHERLANDS | LAND | VD | 117.650 | 100/500 | 50L | 37 |
| EH | PAMPUS |  | VD | 117.800 | 120NT,150TC,80/500 | 50L | 37 |
| EN | ALL NORWAY | LAND | VD | 117.200 | 100/500 | 50L | 37 |
| ES | ALL SWEDEN | LAND | VD | 117.900 | 80/400 | 50L | 29 |
| LF | ALL FRANCE | LAND | VD | 117.200 | 40/250 | 50L | 37 |
| LF | CHATILLON-SUR-MARNE |  | VD | 117.600 | 70VE,100/500 | 50L | 37 |
| LF | PARIS/CH.DE GAULLE |  | VD | 117.050 | 110/500 | 50L | 37 |
| LF | ROLAMPONT |  | VD | 117.300 | 120HL,60/500 | 50L | 36 |

## Scenario 1B: 1.5 MHz vacated between 116.500 and 118.000

### Assignments processed

| Width of sub-band vacated | 1.5 MHz |
| --- | --- |
| VOR and VOR-DME in the sub-band | 201 |
| Re-planned VORs | 178 |
| Failures, including: | 23 |
| - Failures (All Land VOR-DME) | 6 |
| - Failures (other VOR-DME) | 16 |
| - Failures (All Land VOR) | 1 |
| - Failures (other VOR) | 0 |

### Location of the VORs processed

The failures are shown in red. The VORs, VORTACs and VOR-DMEs which it was possible to re-plan are shown in green.

The icons indicate type of service, as set out below:

|  | : VOR |  | : VOR-TAC |  | : VOR-DME |
| --- | --- | --- | --- | --- | --- |

The large icons identify the “ALL LAND” mobile services.

### List of failures

| Cty | Location | Poly | Type | VHF freq | DOC | VHF pwr | DME pwr |
| --- | --- | --- | --- | --- | --- | --- | --- |
| ED | ALL GERMANY | LAND | VOR | 117.950 | 25/100 | 80L |  |
| ED | BRUNKENDORF |  | VD | 117.700 | 80/500 | 200L | 39 |
| ED | HEHLINGEN |  | VD | 117.300 | 80/500 | 200L | 39 |
| ED | NOERDLINGEN |  | VD | 117.550 | 60/500 | 50 | 37 |
| ED | SAARBRUCKEN |  | VD | 117.000 | 60/500 | 400L | 42 |
| ED | TAUNUS |  | VD | 116.700 | 60SA,40/250 | 400L | 42 |
| EG | ALL UK | LAND | VD | 116.900 | 100/500 | 50L | 37 |
| EG | ALL UK | LAND | VD | 116.950 | 100/500 | 50L | 37 |
| EG | DETLING |  | VD | 117.300 | 60/500 | 50L | 39 |
| EH | ALL NETHERLANDS | LAND | VD | 117.650 | 100/500 | 50L | 37 |
| EH | PAMPUS |  | VD | 117.800 | 120NT,150TC,80/500 | 50L | 37 |
| EH | REKKEN |  | VD | 116.800 | 80/500 | 25L | 37 |
| EK | VESTA |  | VD | 116.600 | 200PX,160XE,100/500 | 50L | 36 |
| EN | ALL NORWAY | LAND | VD | 117.200 | 100/500 | 50L | 37 |
| EP | SUBI/SLUBICE |  | VD | 116.700 | 150/500 | 100L | 39 |
| ES | ALL SWEDEN | LAND | VD | 117.900 | 80/400 | 50L | 29 |
| LF | ALL FRANCE | LAND | VD | 117.200 | 40/250 | 50L | 37 |
| LF | BOURSONNE |  | VD | 116.750 | 60/500 | 50L | 37 |
| LF | CHATILLON-SUR-MARNE |  | VD | 117.600 | 70VE,100/500 | 50L | 37 |
| LF | PARIS/CH.DE GAULLE |  | VD | 117.050 | 110/500 | 50L | 37 |
| LF | ROLAMPONT |  | VD | 117.300 | 120HL,60/500 | 50L | 36 |
| LI | BOLZANO |  | VD | 116.800 | 100/500 | 50L | 39 |
| LS | PASSEIRY |  | VD | 116.600 | 120GS,80/500 | 50L | 37 |

## Scenario 1C : 2 MHz vacated between 116.000 and 118.000

### Assignments processed

| Width of sub-band vacated | 2 MHz |
| --- | --- |
| VOR and VOR-DME in the sub-band | 264 |
| Replanned VORs | 232 |
| Failures, including: | 32 |
| - Failures (All Land VOR-DME) | 10 |
| - Failures (other VOR-DME) | 21 |
| - Failures (All Land VOR) | 1 |
| - Failures (other VOR) | 0 |

### Location of the VORs processed

The failures are shown in red. The VORs, VORTACs and VOR-DMEs which it was possible to re-plan are shown in green.

The icons indicate type of service, as set out below:

|  | : VOR |  | : VOR-TAC |  | : VOR-DME |
| --- | --- | --- | --- | --- | --- |

The large icons identify the “ALL LAND” mobile services.

### List of failures

| Cty | Location | Poly | Type | VHF freq | DOC | VHF pwr | DME pwr |
| --- | --- | --- | --- | --- | --- | --- | --- |
| ED | ALL GERMANY | LAND | VOR | 117.950 | 25/100 | 80L |  |
| ED | ALL GERMANY | LAND | VD | 116.050 | 100/500 | 200L | 40 |
| ED | ALL GERMANY | LAND | VD | 116.350 | 100/500 | 200L | 40 |
| ED | ALL GERMANY | LAND | VD | 116.150 | 40/250 | 200L | 39 |
| ED | BRUNKENDORF |  | VD | 117.700 | 80/500 | 200L | 39 |
| ED | HEHLINGEN |  | VD | 117.300 | 80/500 | 200L | 39 |
| ED | MAGDEBURG |  | VD | 117.350 | 80/500 | 400L | 37 |
| ED | MOOSBURG |  | VD | 117.150 | 60/500 | 200L | 37 |
| ED | NOERDLINGEN |  | VD | 117.550 | 60/500 | 50 | 37 |
| ED | NORVENICH |  | VD | 116.200 | 60/500 | 200L | 40 |
| ED | SAARBRUCKEN |  | VD | 117.000 | 60/500 | 400L | 42 |
| ED | TAUNUS |  | VD | 116.700 | 60SA,40/250 | 400L | 42 |
| EG | ALL UK | LAND | VD | 116.900 | 100/500 | 50L | 37 |
| EG | ALL UK | LAND | VD | 116.950 | 100/500 | 50L | 37 |
| EG | DAVENTRY |  | VD | 116.400 | 75TX,60/500 | 50L | 39 |
| EG | DETLING |  | VD | 117.300 | 60/500 | 50L | 39 |
| EH | ALL NETHERLANDS | LAND | VD | 117.650 | 100/500 | 50L | 37 |
| EH | PAMPUS |  | VD | 117.800 | 120NT,150TC,80/500 | 50L | 37 |
| EH | REKKEN |  | VD | 116.800 | 80/500 | 25L | 37 |
| EK | VESTA |  | VD | 116.600 | 200PX,160XE,100/500 | 50L | 36 |
| EN | ALL NORWAY | LAND | VD | 117.200 | 100/500 | 50L | 37 |
| EP | SUBI/SLUBICE |  | VD | 116.700 | 150/500 | 100L | 39 |
| ES | ALL SWEDEN | LAND | VD | 117.900 | 80/400 | 50L | 29 |
| GE | ALL SPAIN | LAND | VD | 116.100 | 60/250 | 50L | 37 |
| LF | ALL FRANCE | LAND | VD | 117.200 | 40/250 | 50L | 37 |
| LF | BOURSONNE |  | VD | 116.750 | 60/500 | 50L | 37 |
| LF | CHATILLON-SUR-MARNE |  | VD | 117.600 | 70VE,100/500 | 50L | 37 |
| LF | LE LUC/LE CANNET |  | VD | 117.600 | 100/250 | 50L | 37 |
| LF | PARIS/CH.DE GAULLE |  | VD | 117.050 | 110/500 | 50L | 37 |
| LF | ROLAMPONT |  | VD | 117.300 | 120HL,60/500 | 50L | 36 |
| LI | BOLZANO |  | VD | 116.800 | 100/500 | 50L | 39 |
| LS | PASSEIRY |  | VD | 116.600 | 120GS,80/500 | 50L | 37 |

## Scenario 1D: 2MHz vacated between 116.000 and 118.000, with MLS-DMEs deleted

### Assignments deleted

| MLS-DMEs deleted | 870 |
| --- | --- |

### Assignments processed

| Width of sub-band vacated | 2 MHz |
| --- | --- |
| VOR and VOR-DME in the sub-band | 264 |
| Replanned VORs | 244 |
| Failures, including: | 20 |
| - Failures (All Land VOR-DME) | 10 |
| - Failures (other VOR-DME) | 9 |
| - Failures (All Land VOR) | 1 |
| - Failures (other VOR) | 0 |

### Location of the VORs processed

The failures are shown in red. The VORs, VORTACs and VOR-DMEs which it was possible to re-plan are shown in green.

The icons indicate type of service, as set out below:

|  | : VOR |  | : VOR-TAC |  | : VOR-DME |
| --- | --- | --- | --- | --- | --- |

The large icons identify the “ALL LAND” mobile services.

### List of failures

| Cty | Location | Poly | Type | VHF freq | DOC | VHF pwr | DME pwr |
| --- | --- | --- | --- | --- | --- | --- | --- |
| ED | ALL GERMANY | LAND | VD | 116.150 | 40/250 | 200L | 39 |
| ED | ALL GERMANY | LAND | VOR | 117.950 | 25/100 | 80L |  |
| ED | ALL GERMANY | LAND | VD | 116.050 | 100/500 | 200L | 40 |
| ED | ALL GERMANY | LAND | VD | 116.350 | 100/500 | 200L | 40 |
| ED | HELGOLAND |  | VD | 116.300 | 200MD,60/500 | 400L | 42 |
| EG | ALL UK | LAND | VD | 116.900 | 100/500 | 50L | 37 |
| EG | ALL UK | LAND | VD | 116.950 | 100/500 | 50L | 37 |
| EH | ALL NETHERLANDS | LAND | VD | 117.650 | 100/500 | 50L | 37 |
| EH | PAMPUS |  | VD | 117.800 | 120NT,150TC,80/500 | 50L | 37 |
| EH | REKKEN |  | VD | 116.800 | 80/500 | 25L | 37 |
| EK | VESTA |  | VD | 116.600 | 200PX,160XE,100/500 | 50L | 36 |
| EN | ALL NORWAY | LAND | VD | 117.200 | 100/500 | 50L | 37 |
| EP | SUBI/SLUBICE |  | VD | 116.700 | 150/500 | 100L | 39 |
| ES | ALL SWEDEN | LAND | VD | 117.900 | 80/400 | 50L | 29 |
| GE | ALL SPAIN | LAND | VD | 116.100 | 60/250 | 50L | 37 |
| LF | ALL FRANCE | LAND | VD | 117.200 | 40/250 | 50L | 37 |
| LF | BOURSONNE |  | VD | 116.750 | 60/500 | 50L | 37 |
| LF | CHATILLON-SUR-MARNE |  | VD | 117.600 | 70VE,100/500 | 50L | 37 |
| LF | PARIS/CH.DE GAULLE |  | VD | 117.050 | 110/500 | 50L | 37 |
| LS | PASSEIRY |  | VD | 116.600 | 120GS,80/500 | 50L | 37 |

## Scenario 1A, 1B, 1C and 1D: consolidated results

| Width of sub-band vacated | 1 MHz | 1.5 MHz | 1.5 MHz | 2 MHz | 2 MHz without MLS-DME |
| --- | --- | --- | --- | --- | --- |
| VOR and VOR-DME in the sub-band | 133 | 201 | 202 | 264 | 264 |
| Replanned VORs | 120 | 178 | 182 | 232 | 244 |
| Failures, including: | 13 | 23 | 20 | 32 | 20 |
| - Failures (All Land VOR-DME) | 3 | 6 | 5 | 10 | 10 |
| - Failures (other VOR-DME) | 8 | 16 | 14 | 21 | 9 |
| - Failures (All Land VOR) | 1 | 1 | 1 | 1 | 1 |
| - Failures (other VOR) | 0 | 0 | 0 | 0 | 0 |

List of countries where failures are located:

| Code | Country | Number of failures |
| --- | --- | --- |
|  |  | Minimum | Maximum |
| ED | GERMANY | 5 | 12 |
| EG | UNITED KINGDOM | 0 | 4 |
| EH | NETHERLANDS | 2 | 3 |
| EK | DENMARK | 0 | 1 |
| EN | NORWAY | 1 | 1 |
| EP | POLAND | 0 | 1 |
| ES | SWEDEN | 1 | 1 |
| GE | SPAIN | 0 | 1 |
| LF | FRANCE | 4 | 6 |
| LI | ITALY | 0 | 1 |
| LS | SWITZERLAND | 0 | 1 |

# SCENARIO 2: Verification of GBAS

## Scenario 2A: Planning of 1,775 GBASs between 108.000 and 116.000

The “new” GBASs are planned in the COM3 band which was reorganised following the migration of the VORs from the 116-118 MHz band to the 108-116MHz band. These “new” GBASs (considered to be future requirements) are created by copying all the ILSs and ILS-DMEs existing in EUROPE, applying a factor of 150%.

The coverage defined for the GBASs corresponds to a circular coverage with a radius:

- of 25NM, in the case of a copied ILS,

- equivalent to the DOC of the DME, for copies of ILS-DME.

The height of the airspace is equal to :

- FL100, for the ILSs,

- maximum FL of the DME service for copies of ILS-DME.

It was assumed that each GBAS service would use all the frequency slots allocated to it.

Prior to re-planning, the spectrum corresponds to that obtained from scenario 2C, i.e. following transfer between 108.000 and 116.000 MHz of 239 VOR and VOR/DME assignments whose frequency was between 116.000 and 118.000 MHz.

### Assignments processed

| Destination band | New GBASs | Re-planned GBASs | Failures |
| --- | --- | --- | --- |
| 108.000 – 116.000 Mhz | 1,775 | 1,668 | 107 |

### Location of the failed GBASs

The failures are shown in red. The successfully re-planned GBASs are shown in green.

### List of failures

| Cty | Location | DOC |  | Cty | Location | DOC |
| --- | --- | --- | --- | --- | --- | --- |
| EB | BRUXELLES/NATIONAL | 25/100 |  | EP | MIROSLAWIEC | 200/250 |
|  | BRUXELLES/NATIONAL | 25/250 |  | LF | BRETIGNY | 25/100 |
|  | BRUXELLES/NATIONAL | 25/100 |  |  | BRETIGNY | 25/100 |
|  | CHARLEROI/BRUSSELS | 25/250 |  |  | CHARLEVILLE/MEZIER | 25/100 |
|  | CHARLEROI/BRUSSELS | 25/250 |  |  | CREIL | 25/100 |
|  | KORTRIJK/WEVELGEM | 25/250 |  |  | EPINAL/MIRECOURT | 25/100 |
|  | KORTRIJK/WEVELGEM | 25/250 |  |  | EPINAL/MIRECOURT | 25/100 |
|  | LIEGE/LIEGE | 25/250 |  |  | ETAIN/ROUVRES | 25/250 |
|  | LIEGE/LIEGE | 25/250 |  |  | ETAIN/ROUVRES | 25/250 |
|  | LIEGE/LIEGE | 25/250 |  |  | MELUN/VILLAROCHE | 25/250 |
|  | LIEGE/LIEGE | 25/250 |  |  | NANCY/OCHEY | 25/100 |
|  | OOSTENDE/OOSTENDE | 25/250 |  |  | NANCY/OCHEY | 25/100 |
| ED | ALL GERMANY | 25/100 |  |  | PARIS/CH.DE GAULLE | 25/100 |
|  | DUSSELDORF/DUSSELD | 25/100 |  |  | PARIS/CH.DE GAULLE | 25/250 |
|  | FRANKFURT/MAIN | 25/100 |  |  | PARIS/CH.DE GAULLE | 25/250 |
|  | FRANKFURT/MAIN | 25/100 |  |  | PARIS/CH.DE GAULLE | 25/250 |
|  | FRANKFURT/MAIN | 25/100 |  |  | PARIS/CH.DE GAULLE | 25/100 |
|  | FRANKFURT/MAIN | 25/100 |  |  | PARIS/CH.DE GAULLE | 25/100 |
|  | FRANKFURT/MAIN | 25/100 |  |  | PARIS/CH.DE GAULLE | 25/250 |
|  | FRANKFURT/MAIN | 25/100 |  |  | PARIS/CH.DE GAULLE | 25/100 |
|  | FRANKFURT/MAIN | 25/100 |  |  | PARIS/LE BOURGET | 25/250 |
|  | FRANKFURT/MAIN | 25/100 |  |  | PARIS/LE BOURGET | 25/100 |
|  | FRANKFURT/MAIN | 25/100 |  |  | PARIS/LE BOURGET | 25/100 |
|  | FRANKFURT/MAIN | 25/100 |  |  | PARIS/LE BOURGET | 25/100 |
|  | HAHN | 25/100 |  |  | PARIS/LE BOURGET | 25/250 |
|  | HAHN | 25/100 |  |  | PARIS/LE BOURGET | 25/100 |
|  | KOLN/KOLN-BONN | 25/100 |  |  | PARIS/LE BOURGET | 25/100 |
|  | MUNSTER/OSNABRUCK | 25/100 |  |  | PARIS/ORLY | 25/250 |
|  | NIEDERRHEIN | 25/100 |  |  | PARIS/ORLY | 25/100 |
|  | SIEGERLAND | 25/100 |  |  | PHALSBOURG | 25/250 |
|  | SPANGDAHLEM | 25/100 |  |  | PONTOISE | 25/100 |
|  | SPANGDAHLEM | 25/100 |  |  | STRASBOURG/ENTZHEIN | 25/100 |
| EG | FARNBOROUGH | 25/250 |  |  | TOUL | 25/100 |
|  | GATWICK (TEE) | 25/100 |  |  | TOUSSUS-LE-NOBLE | 25/250 |
|  | LONDON/GATWICK | 25/250 |  |  | TOUSSUS-LE-NOBLE | 25/100 |
|  | LONDON/GATWICK | 25/250 |  |  | TOUSSUS-LE-NOBLE | 25/250 |
|  | MANSTON | 25/750 |  |  | TOUSSUS-LE-NOBLE | 25/100 |
|  | MANSTON | 25/750 |  |  | VILLACOUBLAY | 25/250 |
|  | MANSTON | 25/750 |  | LI | ALL ITALY | 25/100 |
|  | MILDENHALL | 25/100 |  |  |  |  |
|  | MILDENHALL | 25/100 |  |  |  |  |
|  | NORTHOLT | 25/250 |  |  |  |  |
|  | ODIHAM | 25/100 |  |  |  |  |
|  | ODIHAM | 25/100 |  |  |  |  |
|  | SOUTHEND | 25/250 |  |  |  |  |
| EH | AMSTERDAM/SCHIPHOL | 25/250 |  |  |  |  |
|  | AMSTERDAM/SCHIPHOL | 25/250 |  |  |  |  |
|  | AMSTERDAM/SCHIPHOL | 25/100 |  |  |  |  |
|  | AMSTERDAM/SCHIPHOL | 25/100 |  |  |  |  |
|  | AMSTERDAM/SCHIPHOL | 25/100 |  |  |  |  |
|  | EINDHOVEN | 25/250 |  |  |  |  |
|  | EINDHOVEN | 25/250 |  |  |  |  |
|  | EINDHOVEN | 25/100 |  |  |  |  |
|  | GILZE-RIJEN | 25/250 |  |  |  |  |
|  | GILZE-RIJEN | 25/250 |  |  |  |  |
|  | GILZE-RIJEN | 25/250 |  |  |  |  |
|  | MAASTRICHT | 25/250 |  |  |  |  |
|  | MAASTRICHT/ZUID-LI | 25/100 |  |  |  |  |
|  | MAASTRICHT/ZUID-LI | 25/100 |  |  |  |  |
|  | VALKENBURG | 25/250 |  |  |  |  |
|  | VALKENBURG | 25/250 |  |  |  |  |
|  | VALKENBURG | 25/250 |  |  |  |  |
|  | VALKENBURG | 25/250 |  |  |  |  |
|  | VOLKEL | 25/250 |  |  |  |  |
|  | VOLKEL | 25/250 |  |  |  |  |
|  | VOLKEL | 25/250 |  |  |  |  |
|  | WOENSDRECHT | 25/250 |  |  |  |  |
|  | WOENSDRECHT | 25/250 |  |  |  |  |

A large part of these failures correspond to multiple GBAS requests at a single airport. These requests are based on initial hypotheses determining requirements.  GBASs by copy/transformation of 1.5  times the ILS and ILS-DMEs at that airport are set out in the COM3 table.

For example, at FRANKFURT/MAIN, the GBAS requirement determined on the basis of these hypotheses was 18 services. Of these 18 services, there were 10 failures, yet 8 GBAS requirements were satisfactory for this airport alone.

Similarly, at PARIS/CDG, 8 requirements were considered, with 6 failures and 2 successes.

## Scenario 2B: Planning of 1,775 GBASs between 108.000 and 118.000

The "new" GBASs are planned in the current COM3 band between 108 and 118Hz, with no migration of the VORs located between 116 and 118 MHz.

The objective of this scenario is to provide a basis of comparison reflecting a measure of current GBAS capacity. A comparison of the results of this scenario 2B with the preceding scenario 2A makes it possible to evaluate the deterioration caused by scenario 2A to the GBAS capacity of the spectrum. The deterioration observed results both from the use of a reduced  2MHz band and from the migration of the VOR services to a reduced band.

### Assignments processed

| Destination band | New GBASs | Re-planned GBASs | Failures |
| --- | --- | --- | --- |
| 108.000 - 118.000 Mhz | 1,775 | 1,702 | 73 |

### Location of the failed GBASs

The failures are shown in red. The successfully re-planned GBASs are shown in green.

### List of failures

| Cty | Location | DOC |  | Cty | Location | DOC |
| --- | --- | --- | --- | --- | --- | --- |
| EB | CHARLEROI/BRUSSELS | 25/250 |  | EP | MIROSLAWIEC | 200/250 |
|  | CHARLEROI/BRUSSELS | 25/250 |  | LF | BRETIGNY | 25/100 |
|  | KORTRIJK/WEVELGEM | 25/250 |  | LF | BRETIGNY | 25/100 |
|  | OOSTENDE/OOSTENDE | 25/250 |  | LF | CHARLEVILLE/MEZIER | 25/100 |
|  |  |  |  | LF | CREIL | 25/100 |
|  |  |  |  | LF | NANCY/OCHEY | 25/100 |
|  |  |  |  | LF | PARIS/CH.DE GAULLE | 25/100 |
|  |  |  |  | LF | PARIS/CH.DE GAULLE | 25/250 |
|  |  |  |  | LF | PARIS/CH.DE GAULLE | 25/250 |
|  |  |  |  | LF | PARIS/CH.DE GAULLE | 25/250 |
|  |  |  |  | LF | PARIS/CH.DE GAULLE | 25/100 |
|  |  |  |  | LF | PARIS/CH.DE GAULLE | 25/100 |
| ED | ALL GERMANY | 25/100 |  | LF | PARIS/CH.DE GAULLE | 25/250 |
|  | FRANKFURT/MAIN | 25/100 |  | LF | PARIS/CH.DE GAULLE | 25/100 |
|  | FRANKFURT/MAIN | 25/100 |  | LF | PARIS/LE BOURGET | 25/250 |
|  | FRANKFURT/MAIN | 25/100 |  | LF | PARIS/LE BOURGET | 25/100 |
|  | FRANKFURT/MAIN | 25/100 |  | LF | PARIS/LE BOURGET | 25/100 |
|  | FRANKFURT/MAIN | 25/100 |  | LF | PARIS/LE BOURGET | 25/100 |
|  | FRANKFURT/MAIN | 25/100 |  | LF | PARIS/LE BOURGET | 25/100 |
|  | FRANKFURT/MAIN | 25/100 |  | LF | PARIS/ORLY | 25/250 |
|  | FRANKFURT/MAIN | 25/100 |  | LF | TOUSSUS-LE-NOBLE | 25/250 |
|  | FRANKFURT/MAIN | 25/100 |  | LF | TOUSSUS-LE-NOBLE | 25/100 |
|  | FRANKFURT/MAIN | 25/100 |  | LF | TOUSSUS-LE-NOBLE | 25/250 |
|  | FRANKFURT/MAIN | 25/100 |  | LF | TOUSSUS-LE-NOBLE | 25/100 |
|  | FRANKFURT/MAIN | 25/100 |  | LF | VILLACOUBLAY | 25/250 |
|  | HAHN | 25/100 |  |  |  |  |
|  | KOLN/KOLN-BONN | 25/100 |  |  |  |  |
|  | MUNSTER/OSNABRUCK | 25/100 |  |  |  |  |
|  | MUNSTER/OSNABRUCK | 25/100 |  |  |  |  |
|  | NIEDERRHEIN | 25/100 |  |  |  |  |
|  | SIEGERLAND | 25/100 |  |  |  |  |
| EG | BIGGIN HILL | 25/250 |  |  |  |  |
|  | LONDON/GATWICK | 25/250 |  |  |  |  |
|  | LONDON/GATWICK | 25/250 |  |  |  |  |
|  | MANSTON | 25/750 |  |  |  |  |
|  | MANSTON | 25/750 |  |  |  |  |
|  |  |  |  | LI | ALL ITALY | 25/100 |
| EH | AMSTERDAM/SCHIPHOL | 25/250 |  |  |  |  |
|  | AMSTERDAM/SCHIPHOL | 25/100 |  |  |  |  |
|  | AMSTERDAM/SCHIPHOL | 25/100 |  |  |  |  |
|  | AMSTERDAM/SCHIPHOL | 25/100 |  |  |  |  |
|  | EINDHOVEN | 25/250 |  |  |  |  |
|  | EINDHOVEN | 25/100 |  |  |  |  |
|  | GILZE-RIJEN | 25/250 |  |  |  |  |
|  | GILZE-RIJEN | 25/250 |  |  |  |  |
|  | MAASTRICHT | 25/250 |  |  |  |  |
|  | MAASTRICHT/ZUID-LI | 25/100 |  |  |  |  |
|  | SOESTERBERG | 25/250 |  |  |  |  |
|  | SOESTERBERG | 25/250 |  |  |  |  |
|  | VALKENBURG | 25/250 |  |  |  |  |
|  | VALKENBURG | 25/250 |  |  |  |  |
|  | VALKENBURG | 25/250 |  |  |  |  |
|  | VOLKEL | 25/250 |  |  |  |  |
|  | VOLKEL | 25/250 |  |  |  |  |
|  | VOLKEL | 25/250 |  |  |  |  |
|  | WOENSDRECHT | 25/250 |  |  |  |  |

## Scenario 2A, 2B: consolidated results

| Scenario | Destination band | moved VORs | New GBASs | Re-planned GBASs | Failures |
| --- | --- | --- | --- | --- | --- |
| 2A | 108.000 - 116.000 MHz | 178 | 1,775 | 1,668 | 107 |
| 2B | 108.000 - 118.000 MHz | 0 | 1,775 | 1,702 | 73 |

The reduction in GBAS capacity caused by the migration of the VORs to the 108-116 band would appear to be marginal: 34 extra GBAS failures on the basis of a scenario of introducing 1,775 GBASs.

# SCENARIO 3: Spectrum gains for voice communication

## Scenario 3A: Gains associated with the use of a supplementary 2 MHz band

### Assignments processed

The requirements processed correspond to the COM2 assignments for which it is impossible to find an additional frequency without having to use a permutation mechanism. Assignments of the type  “NATIONAL AERODROMES” were removed from the list of assignments processed.

The assignments were classified by country, based on the type of channel spacing (8.33 or 25 MHz) and type of service (AV corresponds to the ATIS and Volmet “Broadcast” services”).

| Channel type |  |  |  | 25 |  |  |  |  |  |  |  |  |  | 8.33 | 8.33 & 25 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| FL |  | <150 |  |  |  | >=150 | and | <300 |  | >=300 |  |  |  | >=300 |  |
| Country | A/G | TWR AFIS | APP | ACC F | A/G | AV | APP | ACC F | A/G | AV | APP | ACC F | Total | ACC | Total |
| AUT |  |  |  |  |  | 5 | 11 | 2 |  | 1 |  | 10 | 29 | 5 | 34 |
| BEL |  | 3 | 4 |  | 1 | 3 | 3 | 15 | 1 | 1 |  |  | 31 | 9 | 40 |
| CZE |  |  |  |  | 4 |  | 7 | 4 | 1 | 1 |  | 3 | 20 | 4 | 24 |
| D |  | 3 | 4 | 8 | 11 | 9 | 14 | 81 |  | 4 |  | 18 | 152 | 32 | 184 |
| DNK |  |  |  |  |  |  |  | 5 |  | 1 |  | 4 | 10 |  | 10 |
| F | 7 | 7 | 19 | 1 | 17 | 18 | 23 | 49 | 14 | 7 |  | 47 | 209 | 42 | 251 |
| G | 13 | 11 | 28 | 6 |  | 14 | 26 | 49 | 4 | 5 | 2 | 86 | 244 | 6 | 250 |
| HNG |  |  |  | 1 | 1 |  |  | 2 |  | 1 |  | 5 | 10 | 1 | 11 |
| HOL | 3 |  |  | 1 |  | 3 | 8 | 9 |  | 1 |  | 11 | 36 | 4 | 40 |
| HRV |  |  |  |  |  |  | 5 | 7 | 1 | 1 |  | 9 | 23 |  | 23 |
| I |  |  |  | 3 | 3 |  | 5 | 21 | 2 | 3 |  | 22 | 59 | 4 | 63 |
| IRL |  |  |  |  |  |  |  |  | 2 |  |  | 9 | 11 |  | 11 |
| LUX |  | 2 | 1 |  |  |  | 1 |  |  |  |  |  | 4 |  | 4 |
| POL |  |  |  |  |  |  |  | 3 | 1 | 1 |  | 12 | 17 |  | 17 |
| S |  |  |  |  |  |  |  |  | 1 | 1 |  | 7 | 9 |  | 9 |
| SUI |  |  |  |  |  | 6 |  | 9 |  | 2 |  | 8 | 25 | 5 | 30 |
| SVK |  |  | 1 |  | 1 |  |  | 4 |  | 1 |  | 6 | 13 |  | 13 |
| SVN |  |  |  |  |  |  | 1 | 4 | 1 |  |  | 1 | 7 |  | 7 |
| UKR |  |  |  |  |  |  |  |  |  |  |  | 4 | 4 |  | 4 |
| YUG |  |  |  |  |  |  |  | 7 |  |  |  | 10 | 17 |  | 17 |
| Total | 23 | 26 | 57 | 20 | 38 | 58 | 104 | 271 | 28 | 31 | 2 | 272 | 930 | 112 | 1042 |
| Country | A/G | TWR AFIS | APP | ACC F | A/G | AV | APP | ACC F | A/G | AV | APP | ACC F | Total | ACC | Total |
| FL |  | <150 |  |  |  | >=150 | and | <300 |  | >=300 |  |  |  | >=300 |  |
| Channel type |  |  |  | 25 |  |  |  |  |  |  |  |  |  | 8.33 | 8.33 & 25 |

### Successful assignments

The table shows the successful assignments, classified in the same way as in the table of assignments processed.

AV corresponds to the ATIS and Volmet “Broadcast” services

| Channel type |  |  |  | 25 |  |  |  |  |  |  |  |  |  | 8.33 | 8.33 & 25 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| FL |  | <150 |  |  |  | >=150 | and | <300 |  | >=300 |  |  |  | >=300 |  |
| Country | A/G | TWR AFIS | APP | ACC F | A/G | AV | APP | ACC F | A/G | AV | APP | ACC F | Total | ACC | Total |
| AUT |  |  |  |  |  | 2 | 2 | 1 |  | 1 |  | 1 | 7 | 2 | 9 |
| BEL |  | 2 | 0 |  | 1 | 2 | 2 | 2 | 0 | 1 |  |  | 10 | 2 | 12 |
| CZE |  |  |  |  | 2 |  | 3 | 0 | 0 | 0 |  | 1 | 6 | 1 | 7 |
| D |  | 2 | 1 | 1 | 2 | 0 | 2 | 17 |  | 2 |  | 2 | 29 | 3 | 32 |
| DNK |  |  |  |  |  |  |  | 0 |  | 1 |  | 0 | 1 |  | 1 |
| F | 1 | 2 | 2 | 0 | 2 | 0 | 3 | 11 | 2 | 3 |  | 7 | 33 | 5 | 38 |
| G | 4 | 1 | 9 | 1 |  | 3 | 7 | 7 | 0 | 0 | 0 | 12 | 44 | 0 | 44 |
| HNG |  |  |  | 1 | 1 |  |  | 2 |  | 1 |  | 0 | 5 | 1 | 6 |
| HOL | 1 |  |  | 1 |  | 0 | 2 | 1 |  | 1 |  | 1 | 7 | 2 | 9 |
| HRV |  |  |  |  |  |  | 3 | 3 | 0 | 1 |  | 1 | 8 |  | 8 |
| I |  |  |  | 3 | 2 |  | 1 | 4 | 0 | 1 |  | 8 | 19 | 0 | 19 |
| IRL |  |  |  |  |  |  |  |  | 1 |  |  | 2 | 3 |  | 3 |
| LUX |  | 0 | 0 |  |  |  | 1 |  |  |  |  |  | 1 |  | 1 |
| POL |  |  |  |  |  |  |  | 0 | 1 | 1 |  | 6 | 8 |  | 8 |
| S |  |  |  |  |  |  |  |  | 1 | 1 |  | 4 | 6 |  | 6 |
| SUI |  |  |  |  |  | 1 |  | 2 |  | 0 |  | 1 | 4 | 1 | 5 |
| SVK |  |  | 1 |  | 0 |  |  | 3 |  | 1 |  | 0 | 5 |  | 5 |
| SVN |  |  |  |  |  |  | 0 | 0 | 0 |  |  | 0 | 0 |  | 0 |
| UKR |  |  |  |  |  |  |  |  |  |  |  | 4 | 4 |  | 4 |
| YUG |  |  |  |  |  |  |  | 6 |  |  |  | 5 | 11 |  | 11 |
| Total | 6 | 7 | 13 | 7 | 10 | 8 | 26 | 59 | 5 | 15 | 0 | 55 | 211 | 17 | 228 |
| Country | A/G | TWR AFIS | APP | ACC F | A/G | AV | APP | ACC F | A/G | AV | APP | ACC F | Total | ACC | Total |
| FL |  | <150 |  |  |  | >=150 | and | <300 |  | >=300 |  |  |  | >=300 |  |
| Channel type |  |  |  | 25 |  |  |  |  |  |  |  |  |  | 8.33 | 8.33 & 25 |

The result shows that with one frequency (25 MHz) it will be possible to satisfy around 3 requirements for which it is currently impossible to find a frequency.

### Percentage of assignments satisfied

AV corresponds to the ATIS and Volmet “Broadcast” services

| Channel type |  |  |  | 25 |  |  |  |  |  |  |  |  |  | 8.33 | 8.33 & 25 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| FL |  | <150 |  |  |  | >=150 | and | <300 |  | >=300 |  |  |  | >=300 |  |
| Country | A/G | TWR AFIS | APP | ACC F | A/G | AV | APP | ACC F | A/G | AV | APP | ACC F | Total | ACC | Total |
| AUT |  |  |  |  |  | 40% | 18% | 50% |  | 100% |  | 10% | 24% | 40% | 26% |
| BEL |  | 66% | 0% |  | 100% | 66% | 66% | 13% | 0% | 100% |  |  | 32% | 22% | 30% |
| CZE |  |  |  |  | 50% |  | 42% | 0% | 0% | 0% |  | 33% | 30% | 25% | 29% |
| D |  | 66% | 25% | 12% | 18% | 0% | 14% | 20% |  | 50% |  | 11% | 19% | 9% | 17% |
| DNK |  |  |  |  |  |  |  | 0% |  | 100% |  | 0% | 10% |  | 10% |
| F | 14% | 28% | 10% | 0% | 11% | 0% | 13% | 22% | 14% | 42% |  | 14% | 15% | 11% | 15% |
| G | 30% | 9% | 32% | 16% |  | 21% | 26% | 14% | 0% | 0% | 0% | 13% | 18% | 0% | 17% |
| HNG |  |  |  | 100% | 100% |  |  | 100% |  | 100% |  | 0% | 50% | 100% | 54% |
| HOL | 33% |  |  | 100% |  | 0% | 25% | 11% |  | 100% |  | 9% | 19% | 50% | 22% |
| HRV |  |  |  |  |  |  | 60% | 42% | 0% | 100% |  | 11% | 34% |  | 34% |
| I |  |  |  | 100% | 66% |  | 20% | 19% | 0% | 33% |  | 36% | 32% | 0% | 30% |
| IRL |  |  |  |  |  |  |  |  | 50% |  |  | 22% | 27% |  | 27% |
| LUX |  | 0% | 0% |  |  |  | 100% |  |  |  |  |  | 25% |  | 25% |
| POL |  |  |  |  |  |  |  | 0% | 100% | 100% |  | 50% | 47% |  | 47% |
| S |  |  |  |  |  |  |  |  | 100% | 100% |  | 57% | 66% |  | 66% |
| SUI |  |  |  |  |  | 16% |  | 22% |  | 0% |  | 12% | 16% | 20% | 16% |
| SVK |  |  | 100% |  | 0% |  |  | 75% |  | 100% |  | 0% | 38% |  | 38% |
| SVN |  |  |  |  |  |  | 0% | 0% | 0% |  |  | 0% | 0% |  | 0% |
| UKR |  |  |  |  |  |  |  |  |  |  |  | 100% | 100% |  | 100% |
| YUG |  |  |  |  |  |  |  | 85% |  |  |  | 50% | 64% |  | 64% |
| Total | 26% | 26% | 22% | 35% | 26% | 13% | 25% | 21% | 17% | 48% | 0% | 20% | 22% | 15% | 21% |
| Country | A/G | TWR AFIS | APP | ACC F | A/G | AV | APP | ACC F | A/G | AV | APP | ACC F | Total | ACC | Total |
| FL |  | <150 |  |  |  | >=150 | and | <300 |  | >=300 |  |  |  | >=300 |  |
| Channel type |  |  |  | 25 |  |  |  |  |  |  |  |  |  | 8.33 | 8.33 & 25 |

### List of successful assignments

| Country | Site | 8/25 | Service | DOC in NM | FL | POLY |
| --- | --- | --- | --- | --- | --- | --- |
| AUT | WIEN ACC | 8 | ACC/U |  | 450 | POLY |
| AUT | WIEN ACC | 8 | ACC/U |  | 450 | POLY |
| AUT | WIEN ACC | 25 | VOLMET | 261 | 450 |  |
| AUT | WIEN ACC | 25 | ACC/U |  | 450 | POLY |
| AUT | LINZ/LINZ | 25 | ATIS | 60 | 200 |  |
| AUT | WIEN ACC | 25 | ACC/L |  | 200 | POLY |
| AUT | WIEN/SCHWECHAT | 25 | VOLMET | 100 | 200 |  |
| AUT | WIEN/SCHWECHAT | 25 | APP/I | 40 | 200 |  |
| AUT | SALZBURG/SALZBURG | 25 | APP/I | 40 | 150 |  |
| BEL | BRUXELLES ACC | 8 | ACC/U |  | 450 | POLY |
| BEL | BRUXELLES ACC | 8 | ACC/U |  | 450 | POLY |
| BEL | BRUXELLES ACC | 25 | VOLMET | 261 | 450 |  |
| BEL | BRUXELLES ACC | 25 | ACC/L |  | 250 | POLY |
| BEL | BRUXELLES ACC | 25 | ACC/L |  | 250 | POLY |
| BEL | SEMMERZAKE | 25 | A/G | 50 | 250 |  |
| BEL | LIEGE/LIEGE | 25 | ATIS | 60 | 200 |  |
| BEL | BRUXELLES/NATIONAL | 25 | ATIS | 60 | 200 |  |
| BEL | BRUXELLES/NATIONAL | 25 | APP/I | 40 | 150 |  |
| BEL | BRUXELLES/NATIONAL | 25 | APP/I | 40 | 150 |  |
| BEL | CHARLEROI/BRUSSELS S | 25 | TWR | 25 | 40 |  |
| BEL | NAMUR/SUARLEE | 25 | AFIS | 15 | 30 |  |
| CZE | PRAHA ACC | 8 | ACC/U |  | 450 | POLY |
| CZE | PRAHA ACC | 25 | ACC/U |  | 450 | POLY |
| CZE | BRNO/TURANY | 25 | A/G | 50 | 250 |  |
| CZE | KUNOVICE | 25 | APP/H | 50 | 250 |  |
| CZE | PLZEN | 25 | APP/I | 40 | 150 |  |
| CZE | ZATEC | 25 | A/G | 40 | 150 |  |
| CZE | PRAHA/RUZYNE | 25 | APP/I | 40 | 150 |  |
| D | RHEIN UAC | 8 | ACC/U |  | 450 | POLY |
| D | RHEIN UAC | 8 | ACC |  | 450 | POLY |
| D | RHEIN UAC | 8 | ACC/U |  | 450 | POLY |
| D | FRANKFURT ACC | 25 | VOLMET | 261 | 450 |  |
| D | RHEIN UAC | 25 | ACC/U |  | 450 | POLY |
| D | BERLIN ACC | 25 | VOLMET | 261 | 450 |  |
| D | HANNOVER ACC | 25 | ACC/U |  | 450 | POLY |
| D | BERLIN ACC | 25 | ACC/L |  | 295 | POLY |
| D | BERLIN ACC | 25 | ACC/L |  | 295 | POLY |
| D | BERLIN ACC | 25 | ACC |  | 295 | POLY |
| D | DUSSELDORF ACC | 25 | ACC/L |  | 285 | POLY |
| D | MUNCHEN ACC | 25 | ACC/L |  | 280 | POLY |
| D | MUNCHEN ACC | 25 | ACC |  | 280 | POLY |
| D | MUNCHEN ACC | 25 | ACC |  | 275 | POLY |
| D | FRANKFURT ACC | 25 | ACC/L |  | 250 | POLY |
| D | FRANKFURT ACC | 25 | ACC/L |  | 250 | POLY |
| D | MUNCHEN ACC | 25 | F |  | 250 | POLY |
| D | BREMEN ACC | 25 | ACC/L |  | 250 | POLY |
| D | BREMEN ACC | 25 | ACC |  | 250 | POLY |
| D | FRANKFURT ACC | 25 | ACC/L |  | 250 | POLY |
| D | FRANKFURT ACC | 25 | ACC/L |  | 250 | POLY |
| D | FRANKFURT ACC | 25 | ACC/L |  | 250 | POLY |
| D | LEIPZIG/LEIPZIG | 25 | A/G | 50 | 250 |  |
| D | BERLIN ACC | 25 | ACC/L |  | 250 | POLY |
| D | BERLIN/BERLIN | 25 | APP/H | 60 | 200 |  |
| D | DRESDEN | 25 | APP/H | 50 | 200 |  |
| D | DUSSELDORF ACC | 25 | ACC |  | 155 | POLY |
| D | DRESDEN | 25 | A/G | 40 | 150 |  |
| D | FRANKFURT ACC | 25 | F |  | 100 | POLY |
| D | NURNBERG/NURNBERG | 25 | APP/L | 60 | 100 |  |
| D | MANNHEIM/NEUOSTHEIM | 25 | ATIS | 50 | 100 |  |
| D | FRANKFURT/FRANKFURT | 25 | AS | 25 | 0 |  |
| DNK | KOBENHAVN ACC | 25 | VOLMET | 261 | 450 |  |
| F | BREST ACC | 8 | ACC/U |  | 450 | POLY |
| F | BREST ACC | 8 | ACC/U |  | 450 | POLY |
| F | PARIS/REIMS ACC | 8 | ACC/U |  | 450 | POLY |
| F | BREST ACC | 8 | ACC |  | 430 | POLY |
| F | BREST ACC | 8 | ACC |  | 380 | POLY |
| F | PARIS/REIMS ACC | 25 | ACC/U |  | 450 | POLY |
| F | PARIS/REIMS ACC | 25 | VOLMET | 261 | 450 |  |
| F | BORDEAUX ACC | 25 | ACC/U |  | 450 | POLY |
| F | BREST ACC | 25 | ACC/U |  | 450 | POLY |
| F | BREST/LOPERHET | 25 | A/G |  | 450 | POLY |
| F | MARSEILLE ACC | 25 | VOLMET | 261 | 450 |  |
| F | MARSEILLE ACC | 25 | VOLMET | 261 | 450 |  |
| F | MARSEILLE ACC | 25 | ACC/I |  | 350 | POLY |
| F | MARSEILLE ACC | 25 | ACC/I |  | 350 | POLY |
| F | MARSEILLE ACC | 25 | ACC/I |  | 350 | POLY |
| F | MARSEILLE ACC | 25 | ACC/I |  | 350 | POLY |
| F | TOURS/ST-SYMPHORIEN | 25 | A/G |  | 300 | POLY |
| F | PARIS ACC | 25 | ACC/L |  | 250 | POLY |
| F | PARIS ACC | 25 | ACC/L |  | 250 | POLY |
| F | PARIS ACC | 25 | F |  | 250 | POLY |
| F | PARIS/REIMS ACC | 25 | ACC/L |  | 250 | POLY |
| F | PARIS/REIMS ACC | 25 | ACC/L |  | 250 | POLY |
| F | PARIS/REIMS ACC | 25 | ACC/L |  | 250 | POLY |
| F | PARIS/REIMS ACC | 25 | F |  | 250 | POLY |
| F | VILLACOUBLAY | 25 | A/G | 50 | 250 |  |
| F | NICE/COTE D'AZUR | 25 | APP/H | 50 | 250 |  |
| F | ISTRES | 25 | ACC |  | 250 | POLY |
| F | BORDEAUX ACC | 25 | F |  | 250 | POLY |
| F | MARSEILLE ACC | 25 | ACC/L |  | 250 | POLY |
| F | MARSEILLE ACC | 25 | F |  | 250 | POLY |
| F | NICE/COTE D'AZUR | 25 | APP/H | 50 | 250 |  |
| F | TOULOUSE/BLAGNAC | 25 | A/G |  | 250 | POLY |
| F | METZ/NANCY-LORRAINE | 25 | APP | 50 | 195 |  |
| F | LILLE/LESQUIN | 25 | APP |  | 115 | POLY |
| F | BEAUVAIS/TILLE | 25 | APP/L | 25 | 100 |  |
| F | LE TOUQUET/PARIS-PLA | 25 | TWR | 25 | 40 |  |
| F | MERVILLE/CALONNE | 25 | TWR | 25 | 40 |  |
| F | TOULOUSE | 25 | A/G |  | 40 | POLY |
| G | SCOTTISH ACC | 25 | ACC/U |  | 460 | POLY |
| G | SCOTTISH ACC | 25 | ACC/U |  | 460 | POLY |
| G | LONDON ACC | 25 | ACC/U |  | 450 | POLY |
| G | LONDON MIL ACC | 25 | ACC/U |  | 450 | POLY |
| G | LONDON ACC | 25 | ACC/U |  | 450 | POLY |
| G | LONDON ACC | 25 | ACC/U |  | 450 | POLY |
| G | SCOTTISH ACC | 25 | ACC/U |  | 450 | POLY |
| G | LONDON ACC | 25 | ACC/U |  | 430 | POLY |
| G | MANCHESTER ACC | 25 | ACC/I |  | 310 | POLY |
| G | MANCHESTER ACC | 25 | ACC/L |  | 300 | POLY |
| G | SCOTTISH ACC | 25 | ACC/I |  | 300 | POLY |
| G | MANCHESTER ACC | 25 | ACC/I |  | 300 | POLY |
| G | MANCHESTER ACC | 25 | ACC/I |  | 290 | POLY |
| G | MANCHESTER ACC | 25 | ACC/I |  | 270 | POLY |
| G | LONDON ACC | 25 | ACC/L |  | 250 | POLY |
| G | LONDON ACC | 25 | F |  | 250 | POLY |
| G | HUMBERSIDE/HUMBERSID | 25 | APP/H | 50 | 250 |  |
| G | LONDON ACC | 25 | ACC/L |  | 245 | POLY |
| G | MANCHESTER/MANCHESTE | 25 | APP/H | 40 | 240 |  |
| G | MANCHESTER/MANCHESTE | 25 | APP/H | 40 | 240 |  |
| G | EAST MIDLANDS/EAST M | 25 | ATIS | 60 | 200 |  |
| G | HUMBERSIDE/HUMBERSID | 25 | ATIS | 60 | 200 |  |
| G | LONDON ACC | 25 | ACC/L |  | 200 | POLY |
| G | COVENTRY | 25 | ATIS | 60 | 200 |  |
| G | CARDIFF/CARDIFF | 25 | APP/L |  | 190 | POLY |
| G | CARDIFF/CARDIFF | 25 | APP | 40 | 190 |  |
| G | BRISTOL/LULSGATE | 25 | APP/L | 60 | 150 |  |
| G | MANCHESTER/MANCHESTE | 25 | APP/I | 40 | 150 |  |
| G | MANCHESTER FIR | 25 | ACC |  | 150 | POLY |
| G | SHOREHAM | 25 | APP/L | 25 | 100 |  |
| G | NORTHOLT | 25 | ATIS | 100 | 100 |  |
| G | MANSTON | 25 | APP/I | 40 | 100 |  |
| G | WATTISHAM | 25 | APP/L | 30 | 100 |  |
| G | BOSCOMBE DOWN | 25 | APP/I | 40 | 100 |  |
| G | COLTISHALL | 25 | APP/I | 40 | 80 |  |
| G | PORTLAND | 25 | APP/I | 40 | 80 |  |
| G | NORWICH | 25 | APP/L | 40 | 70 |  |
| G | FARNBOROUGH | 25 | APP/L | 25 | 60 |  |
| G | SOUTHAMPTON/SOUTHAMP | 25 | APP/L | 50 | 55 |  |
| G | FARNBOROUGH | 25 | A/G | 50 | 50 |  |
| G | NORTH SEA | 25 | A/G |  | 50 | POLY |
| G | CHALGROVE | 25 | A/G | 25 | 40 |  |
| G | NORTH SEA | 25 | ACC |  | 30 | POLY |
| G | NORTH SEA | 25 | A/G |  | 0 | POLY |
| HNG | BUDAPEST ACC | 8 | ACC/U |  | 450 | POLY |
| HNG | BUDAPEST ACC | 25 | VOLMET | 261 | 450 |  |
| HNG | VESZPREM | 25 | A/G | 50 | 250 |  |
| HNG | BUDAPEST ACC | 25 | ACC |  | 250 | POLY |
| HNG | BUDAPEST ACC | 25 | ACC |  | 250 | POLY |
| HNG | BUDAPEST ACC | 25 | F |  | 95 | POLY |
| HOL | MAASTRICHT UAC | 8 | ACC/U |  | 450 | POLY |
| HOL | MAASTRICHT UAC | 8 | ACC/U |  | 450 | POLY |
| HOL | NIEUW MILLIGEN ACC | 25 | ACC/U |  | 450 | POLY |
| HOL | AMSTERDAM ACC | 25 | VOLMET | 261 | 450 |  |
| HOL | AMSTERDAM ACC | 25 | ACC/L |  | 250 | POLY |
| HOL | AMSTERDAM/SCHIPHOL | 25 | APP/I | 40 | 150 |  |
| HOL | GILZE-RIJEN | 25 | APP/I | 40 | 150 |  |
| HOL | NIEUW MILLIGEN ACC | 25 | F |  | 120 | POLY |
| HOL | NORTH SEA | 25 | A/G |  | 40 | POLY |
| HRV | ZAGREB ACC | 25 | ACC |  | 450 | POLY |
| HRV | ZAGREB ACC | 25 | VOLMET | 261 | 450 |  |
| HRV | PULA/PULA | 25 | APP/H | 50 | 250 |  |
| HRV | SPLIT TMA | 25 | APP/H | 50 | 250 | POLY |
| HRV | PULA TMA | 25 | F |  | 250 | POLY |
| HRV | ZAGREB ACC | 25 | ACC/L |  | 250 | POLY |
| HRV | ZAGREB TMA | 25 | F |  | 250 | POLY |
| HRV | SPLIT TMA | 25 | APP/H | 50 | 200 | POLY |
| I | BRINDISI ACC | 25 | ACC/U |  | 450 | POLY |
| I | PADOVA ACC | 25 | ACC/U |  | 450 | POLY |
| I | ITALIA UAC | 25 | ACC/U |  | 450 | POLY |
| I | BRINDISI ACC | 25 | ACC/U |  | 450 | POLY |
| I | ITALIA UAC | 25 | ACC/U |  | 450 | POLY |
| I | ITALIA UAC | 25 | ACC/U |  | 450 | POLY |
| I | ROMA ACC | 25 | VOLMET | 261 | 450 |  |
| I | ITALIA UAC | 25 | ACC/U |  | 450 | POLY |
| I | BRINDISI ACC | 25 | ACC/U |  | 365 | POLY |
| I | GENOVA/SESTRI | 25 | A/G | 50 | 250 |  |
| I | ROMA ACC | 25 | F |  | 250 | POLY |
| I | MILANO ACC | 25 | ACC/L |  | 250 | POLY |
| I | MILANO ACC | 25 | F |  | 250 | POLY |
| I | ROMA ACC | 25 | F |  | 250 | POLY |
| I | ROMA/CIAMPINO | 25 | A/G |  | 250 | POLY |
| I | VERONA/VILLAFRANCA | 25 | APP/I | 40 | 150 |  |
| I | MILANO ACC | 25 | ACC/L |  | 100 | POLY |
| I | MILANO ACC | 25 | ACC/L |  | 100 | POLY |
| I | MILANO ACC | 25 | ACC/L |  | 95 | POLY |
| IRL | SHANNON ACC | 25 | ACC/U |  | 450 | POLY |
| IRL | SHANNON ACC | 25 | ACC/U |  | 450 | POLY |
| IRL | CASEMENT | 25 | A/G |  | 450 | POLY |
| LUX | LUXEMBOURG/LUXEMBOUR | 25 | APP/I | 40 | 150 |  |
| POL | WARSZAWA ACC | 25 | ACC/U |  | 460 | POLY |
| POL | WARSZAWA ACC | 25 | ACC/U |  | 450 | POLY |
| POL | SZCZECIN | 25 | A/G | 80 | 450 |  |
| POL | POZNAN | 25 | ACC/U |  | 450 | POLY |
| POL | WARSZAWA ACC | 25 | ACC/U |  | 450 | POLY |
| POL | WARSZAWA ACC | 25 | VOLMET | 261 | 450 |  |
| POL | WARSZAWA ACC | 25 | ACC/U |  | 450 | POLY |
| POL | WARSZAWA ACC | 25 | ACC |  | 410 | POLY |
| S | MALMO ACC | 25 | ACC/U |  | 450 | POLY |
| S | MALMO ACC | 25 | ACC/U |  | 450 | POLY |
| S | MALMO ACC | 25 | A/G |  | 450 | POLY |
| S | MALMO ACC | 25 | ACC/U |  | 450 | POLY |
| S | JONKOPING | 25 | VOLMET | 261 | 450 |  |
| S | MALMO ACC | 25 | ACC/U |  | 350 | POLY |
| SUI | ZURICH ACC | 8 | ACC |  | 330 | POLY |
| SUI | ZURICH ACC | 25 | ACC/U |  | 450 | POLY |
| SUI | GENEVE ACC | 25 | ACC/L |  | 260 | POLY |
| SUI | ZURICH ACC | 25 | ACC/L |  | 250 | POLY |
| SUI | SAMEDAN | 25 | ATIS | 60 | 200 |  |
| SVK | BRATISLAVA ACC | 25 | VOLMET | 261 | 450 |  |
| SVK | BRATISLAVA ACC | 25 | ACC/L |  | 250 | POLY |
| SVK | BRATISLAVA ACC | 25 | F |  | 250 | POLY |
| SVK | BRATISLAVA ACC | 25 | ACC |  | 150 | POLY |
| SVK | BRATISLAVA | 25 | APP/I | 45 | 125 |  |
| UKR | IZMAIL ACC | 25 | ACC/U |  | 450 | POLY |
| UKR | VINNYTSIA ACC | 25 | ACC/U |  | 450 | POLY |
| UKR | DNIPROPETROVS'K ACC | 25 | ACC/U |  | 450 | POLY |
| UKR | KYIV/BORYSPIL' ACC | 25 | ACC/U |  | 450 | POLY |
| YUG | BEOGRAD ACC | 25 | ACC |  | 450 | POLY |
| YUG | BEOGRAD ACC | 25 | ACC |  | 450 | POLY |
| YUG | BEOGRAD ACC | 25 | ACC/U |  | 450 | POLY |
| YUG | PODGORICA/GOLUBOVCI | 25 | ACC/U |  | 450 | POLY |
| YUG | BEOGRAD ACC | 25 | ACC |  | 315 | POLY |
| YUG | BEOGRAD ACC | 25 | ACC |  | 285 | POLY |
| YUG | BEOGRAD ACC | 25 | ACC |  | 285 | POLY |
| YUG | BEOGRAD ACC | 25 | ACC/L |  | 250 | POLY |
| YUG | BEOGRAD ACC | 25 | F |  | 250 | POLY |
| YUG | BEOGRAD ACC | 25 | ACC/L |  | 245 | POLY |
| YUG | BEOGRAD ACC | 25 | ACC |  | 245 | POLY |