AERONAUTICAL COMMUNICATIONS PANEL (ACP)

Working Group F – 15th meeting

Cairo, Egypt

7th – 13th June 2006

Unmanned Aerial Vehicles

Update on the Progress with the UK

Presented by John Mettrop

1.0	Background

Un-manned Aerial Vehicles (UAVs) have been used for some time by the military, operating either in theatres of war, defined test ranges where segregated airspace can be provided or on one off missions where an appropriate moving corridor of segregated airspace can be provided along the intended flight path of the aircraft .  Vehicles size varying form a few centimeters in length to Global Hawk with a wingspan of 35 metres and an overall length of 13 metres (737 size).  With the growing capability of these aircraft so there is an increasing demand from the military to allow these aircraft to fly in non-segregated airspace.

Additionally the civil community can see applications for the technology being developed as a replacement for traditional manned aircraft as well as opening up new opportunities.  Work on this has already commenced and is looking at both extremes of the market in terms of size with serious consideration being given to the use of the technology to initially allow reduced manning of the flight deck with an eventual goal to remove the pilot totally from the aircraft, especially on freight flights.

Whilst initially ICAO kept a watching brief on developments, concerned that this was either a military or national issue, as discussions have progress so they have taken a greater interest and realize that ICAO do have a part to play.  This being re-enforced by the results of a recent ICAO explanatory meeting on UAV’s held in Montreal on the 23rd & 24th May 2006 at which a number of key issues including spectrum and sense& avoid were discussed.

- PROGRESS WITHIN THE UK

Along with a number of other countries the UK has started work on understanding the implications of UAV technology and what it will require in terms of regulation, additional systems and spectrum in order to allow it to fly within non-segregated airspace.

In 2001 work on CAP 722 “Unmanned Aerial Vehicle Operations in UK Airspace – Guidance” was started as a joint civil/military document and a first iteration of the document being produced in that year with a update being produced in 2004 (See Attachment 1).  This document provides guidance on all aspects of UAV operations within UK airspace and is seen as regulation in waiting.

The UK realized that spectrum was a clear issue for both the safety functionality of the aircraft as well as the payload and ensured that at least one agenda item for the World Radio Conference 2007 would allow for an allocation of spectrum to made for the UAV use.  Although the CAA has made a number of presentations to various bodies/conferences within the UK and Europe including The Royal Aeronautical Society and UVSI (See Attachment 2 for a copy of the latest) little concrete action has been taken by the industry.  What has been generated is a matrix of all of the links and additional radio systems required to support the safety functionality of the aircraft (See Attachment 3) however little information has been made available to the CAA that would allow for this matrix to be turned into a fact based spectrum requirement that could be submitted to the ITU.

### 3.0	REQUIRED ACTION

Whilst the UK CAA can continue to work pro-actively within the UK there is a need for a concerted international effort to ensure that the regulation and spectrum resources are in place in a timely manner to allow the industry to develop.

With respect to spectrum there is a clear need for aviation to work together to ensure that there is a common understanding of the requirements and a focus on achieving them.  Whether a suitable spectrum allocation(s) can be achieved at WRC 07 to meet all UAV requirements is questionable and hence there is a need to determine how to ensure that a suitable agenda item is placed on the agenda of WRC-10

Attachment 1

CAP 722

Attachment 2

###### UAV Spectrum Presentation to the Royal Aeronautical Society

Attachment 3

Radio Link Matricies

| UAV LINKS - EN ROUTE ENVIRONMENT |
| --- |
|  |  |  |  |  |  | To GCS |  |  |  |  |
|  |  | ATC voice | ATC data | flight control | system control | platform health monitoring | navigation info | automatic collision avoidance system | situational awareness (sensors) | flight plan | automatic dependance surveillance |
|  | Sense data |  |  |  |  |  |  |  | 1.2 kbps @ 0.1% |  |  |
|  | Flight control |  |  | 1.2 kbps @ 0.1% |  |  |  |  |  |  |  |
|  | system control |  |  |  | 1.2 kbps @ 0.1% |  |  |  |  |  |  |
| From UAV | flight monitoring |  |  |  |  | 1.2 kbps @ 0.1% |  |  |  |  |  |
|  | secondary surveillance radar |  |  |  |  |  |  |  |  |  |  |
|  | navigation |  |  |  |  |  | 1.2 kbps @ 1% |  |  |  |  |
|  | ATC voice & data | 2.4 kbps @ 10% | 32 kbps @ 0.1% |  |  |  |  |  |  |  |  |
|  | UAV Pilot voice & data |  |  |  |  |  |  |  |  |  |  |
|  | primary radar signature |  |  |  |  |  |  |  |  |  |  |
|  | situational awareness |  |  |  |  |  |  | x | 2.4 kbps @ 25% |  |  |
|  | automatic dependance surveillance |  |  |  |  |  |  |  |  |  | 8 kbps |
|  | Forward view |  |  |  |  |  |  |  |  |  |  |

| UAV LINKS - EN ROUTE ENVIRONMENT |
| --- |
|  |  |  |  |  | To UAV |  |  |  |  |  |  |  |
|  |  | Sense data | Flight control | system control | flight monitoring | secondary surveillance radar | navigation | ATC voice & data | UAV Pilot voice & data | primary radar signature | situational awareness | automatic dependance surveillance | Forward view |
|  | ATC voice |  |  |  |  |  |  |  | 2.4 kbps @ 1% |  |  |  |  |
|  | ATC data |  |  |  |  |  |  |  | 32 kbps @ 0.1% |  |  |  |  |
|  | flight control |  | 1.2 kbps @ 0.1% |  |  |  |  |  |  |  |  |  |  |
| From GCS | system control |  |  | 1.2 kbps @ 0.1% |  |  |  |  |  |  |  |  |  |
|  | platform health monitoring |  |  |  |  |  |  |  |  |  |  |  |  |
|  | navigation info |  |  |  |  |  |  |  |  |  |  |  |  |
|  | automatic collision avoidance system |  |  |  |  |  |  |  |  |  |  |  |  |
|  | situational awareness (sensors) |  |  |  |  |  |  |  |  |  |  |  |  |
|  | flight plan |  |  |  |  |  |  |  |  |  |  |  |  |
|  | automatic dependance surveillance |  |  |  |  |  |  |  |  |  |  |  |  |

| UAV LINKS - POINT TO POINT ENVIRONMENT |
| --- |
|  |  |  |  |  |  | To GCS |  |  |  |  |
|  |  | ATC voice | ATC data | flight control | system control | platform health monitoring | navigation info | automatic collision avoidance system | situational awareness (sensors) | flight plan | automatic dependance surveillance |
|  | Sense data |  |  |  |  |  |  |  | 1.2 kbps @ 0.1% |  |  |
|  | Flight control |  |  | 1.2 kbps @ 0.1% |  |  |  |  |  |  |  |
|  | system control |  |  |  | 1.2 kbps @ 0.1% |  |  |  |  |  |  |
| From UAV | flight monitoring |  |  |  |  | 1.2 kbps @ 0.1% |  |  |  |  |  |
|  | secondary surveillance radar |  |  |  |  |  |  |  |  |  |  |
|  | navigation |  |  |  |  |  | 1.2 kbps @ 1% |  |  |  |  |
|  | ATC voice & data | 2.4 kbps @ 25% | 32 kbps @ 0.1% |  |  |  |  |  |  |  |  |
|  | UAV Pilot voice & data |  |  |  |  |  |  |  |  |  |  |
|  | primary radar signature |  |  |  |  |  |  |  |  |  |  |
|  | situational awareness |  |  |  |  |  |  | x | 2.4 kbps @ 25% |  |  |
|  | automatic dependance surveillance |  |  |  |  |  |  |  |  |  | 80 kbps |
|  | Forward view |  |  |  |  |  |  |  |  |  |  |

| UAV LINKS - POINT TO POINT ENVIRONMENT |
| --- |
|  |  |  |  |  | To UAV |  |  |  |  |  |  |  |
|  |  | Sense data | Flight control | system control | flight monitoring | secondary surveillance radar | navigation | ATC voice & data | UAV Pilot voice & data | primary radar signature | situational awareness | automatic dependance surveillance | Forward view |
|  | ATC voice |  |  |  |  |  |  |  | 2.4 kbps @ 10% |  |  |  |  |
|  | ATC data |  |  |  |  |  |  |  | 32 kbps @ 0.1% |  |  |  |  |
|  | flight control |  | 1.2 kbps @ 0.1% |  |  |  |  |  |  |  |  |  |  |
| From GCS | system control |  |  | 1.2 kbps @ 0.1% |  |  |  |  |  |  |  |  |  |
|  | platform health monitoring |  |  |  |  |  |  |  |  |  |  |  |  |
|  | navigation info |  |  |  |  |  |  |  |  |  |  |  |  |
|  | automatic collision avoidance system |  |  |  |  |  |  |  |  |  |  |  |  |
|  | situational awareness (sensors) |  |  |  |  |  |  |  |  |  |  |  |  |
|  | flight plan |  |  |  |  |  |  |  |  |  |  |  |  |
|  | automatic dependance surveillance |  |  |  |  |  |  |  |  |  |  |  |  |