|  | International Civil Aviation Organization INFORMATION PAPER | ACP-WGF 19/IP01 18/07/08 |
| --- | --- | --- |

AERONAUTICAL COMMUNICATIONS PANEL (ACP)

WORKING GROUP F # 19

Montreal, Canada 15 – 19 September 2008

| Agenda Item 7: | Any other business |
| --- | --- |

CLASSIFICATION OF THE AIR TRAFFIC SERVICES AND SAFETY RELATED AERONAUTICAL OPERATION CONTROL COMMUNICATIONS ACCORDING TO THE ITU PRIORITY LEVEL

(Presented by A. Frizon, EADS)

(Prepared by H. Boithias, A. Frizon, X. Ibos, A. Martin, EADS)

SUMMARY

This paper proposes to identify the possible order(s) of priority of AMS(R)S communications as well as a classification of air traffic services and aeronautical operational control communications as defined in COCR with respect to priority level defined at ITU.

ACTION

The meeting notes this paper and uses it as appropriate for drafting a commonly agreed cross-classification between ITU and COCR nomenclatures.

INTRODUCTION

The issue of AMS(R)S is to be debated in ITU-R, notably during the studies called under agenda item 1.7 of WRC-11. It is felt appropriate to better understand how AMS(R)S fits with the order of priority for communications in the AMSS, and to illustrate the applications that can be provided using AMS(R)S allocations. This document aims at contributing to this purpose.

Article 44 of ITU Radio Regulations defines the order of priority for communications in the aeronautical mobile service and the aeronautical mobile-satellite service. In this Article (depicted in Annex A of this document) aeronautical services are shared out among 10 categories (from 1 to 10 respectively from the highest priority to the lowest priority).

In addition, it is clearly stated in Article 43 of Radio Regulations that “frequencies in any band allocated to the aeronautical mobile (R) service and the aeronautical mobile-satellite (R) service are reserved for communications relating to safety and regularity of flight”. In footnotes No. 5.357A and 5.362A of ITU Radio Regulations, references are made to aeronautical mobile-satellite (R) service communications with priority 1 to 6.

This document aims at clearing up the situation regarding the entire aeronautical services, as currently identified by the aeronautical organisms, and their classification into the ITU categories defined in Article 44.

Background

The aim of this contribution was to gather as exhaustive material as possible and to use commonly agreed description of aeronautical services in order to provide a possible baseline for further discussions.

The European Organisation for the Safety of Air Navigation (EUROCONTROL) and the Federal Aviation Administration (FAA) have initiated a joint study to identify potential future communications technologies to meet safety and regularity of flight communications requirements, i.e., those supporting Air Traffic Services (ATS) and safety related Aeronautical Operational Control (AOC) communications. As a preliminary task EUROCONTROL and FAA have focused on identifying and defining the ATS and AOC required services to cope with data communication requirements in terms of future air traffic growth and seamless air traffic management.

This list of services agreed at civil aviation community level in the COCR has been used as main input to that document.

ANALYSIS

It is understood that AMS(R)S can cover any communications falling under priority orders from 1 to 6.

As ATS services are communications governing traffic management, most of those services are perceived as to be classified as Flight Safety Messages, with priority 4 according to Article 44 of ITU Radio Regulations. Furthermore some services could be classified as distress calls or distress messages since they would be used in case all other ways of communications have failed. Those services namely Data Link Alert and Urgent Contact should have the highest priority and are rated as ITU Category 1 messages.

Regarding AOC services, those are communications established between the aircraft (either on ground or in flight) and its airline. Data transferred are mainly driven by exchange of information regarding status of flight and/or aircraft with the view to be capable of ensuring prompt departure for the following flight. Those messages could largely be classified as flight regularity messages in ITU Category 6. However the safety aspect of some of them could cover the domain of Flight safety messages and Meteorological messages, respectively with priority 4 and 5.

Beyond these safety messages, a few could be rated as non-safety messages and classified in ITU Category 10. Those are Free Text messages and Software Loading messages.

The identified services and a proposed classification with respect to ITU priority level are provided in Annex B.

Recommendation

This paper stands for a preliminary work basis for cross-classification of aeronautical services according to ITU and COCR nomenclatures.

We would like to invite ICAO and competent authorities / administrations to comment on this and provide their expertise with the view to improve the proposed classification of aeronautical services as defined in the COCR with respect to ITU categories as defined in Article 44 of RR.

ITU Article 44

ARTICLE  44

Order of priority of communications

44.1	§ 1	The order of priority for communications1 in the aeronautical mobile service and the aeronautical mobile-satellite service shall be as follows, except where impracticable in a fully automated system in which, nevertheless, Category 1 shall receive priority:

1	Distress calls, distress messages and distress traffic.

2	Communications preceded by the urgency signal.

3	Communications relating to radio direction-finding.

4	Flight safety messages.

5	Meteorological messages.

6	Flight regularity messages.

7	Messages relating to the application of the United Nations Charter.

8	Government messages for which priority has been expressly requested.

9	Service communications relating to the working of the telecommunication service or to communications previously exchanged.

10	Other aeronautical communications.

44.2	§ 2	Categories 1 and 2 shall receive priority over all other communications irrespective of any agreement under the provisions of No. 35.1.

Mapping ITU / COCR

| ITU Priority Level | COCR |
| --- | --- |
|  | ATS | AOC |
| 1 | Distress calls, distress message and distress trafic | Data Link Alert |  |
|  |  | Urgent Contact |  |
| 2 | Communications preceded by the urgency signal |  |  |
| 3 | Communications related to radio direction-finding |  |  |
| 4 | Flight safety messages | ATC Clearance | Notice to Airmen |
|  |  | Departure Clearance | Flight Plan Data |
|  |  | Downstream Clearance | Load Sheet Request/Transfer |
|  |  | ATC Microphone Check | Update Electronic Library |
|  |  | Data Link Taxi Clearance |  |
|  |  | Common Trajectory Coordination |  |
|  |  | Data Link Automatic Runway Visual Range |  |
|  |  | Data Link Automatic Terminal Information Service |  |
|  |  | Data Link Operational Terminal Information Service |  |
|  |  | Data Link Operational En Route Information Service |  |
|  |  | Dynamic Route Availability |  |
|  |  | Air Traffic Control Surveillance |  |
|  |  | Flight Plan Consistency |  |
|  |  | Flight Plan Intent |  |
|  |  | System Acces Parameters |  |
|  |  | Traffic Information Service |  |
|  |  | In-Trail Procedures |  |
|  |  | Merging and Spacing |  |
|  |  | Crossing and Passing |  |
|  |  | Paired Approach |  |
|  |  | Air-to-Air Self Separation |  |
|  |  | Air Traffic Control Surveillance |  |
|  |  | Data Link Surface Information and Guidance |  |
|  |  | Wake Service |  |
|  |  | Data Link Significant Meteorological Information |  |
|  |  | Pilot Preferences Downlinks |  |
|  |  | Data Link Logon |  |
|  |  | ATC Communication Management |  |
|  |  | Auto Execute |  |
| 5 | Meteorological messages |  | Textual Weather Reports |
|  |  |  | Real-time Weather Reports for Met Offices |
|  |  |  | Graphical Weather Information |
| 6 | Flight regularity messages | Data Link Flight Update | Flight Status |
|  |  | Arrival Manager Information Delivery | Maintenance Problem Resolution |
|  |  |  | Real-Time Maintenance Information |
|  |  |  | AOC Data Link Logon |
|  |  |  | Position Report |
|  |  |  | Out-Off-On-In |
|  |  |  | Cabin Log Book Transfer |
|  |  |  | Technical Log Book Update |
|  |  |  | Fuel Status |
|  |  |  | Gate and Connecting Flight Status |
|  |  |  | Engine Performance Reports |
|  |  |  | Flight Log Transfer |
| 7 | Messages related to the application of the United Nations Charter |  |  |
| 8 | Government messages for which priority has been expressly requested |  |  |
| 9 | Service communications related to the working of the telecommunication service or to communications previously exchanged |  |  |
| 10 | Other aeronautical communications |  | Free Text |
|  |  |  | Software Loading |

ATS Services

| Name of Service | Description |
| --- | --- |
| Data Link Logon | The DLL service exchanges information between an aircraft and an ATSU to support other addressed data communications services. The DLL service is executed prior to any other addressed data communications service. It is used to uniquely identify an aircraft and to provide version and address information for all data communications services. Once initiated, DLL provides the flight identification to the avionics, and the remainder of the DLL takes place automatically without Flight Crew involvement. |
| ATC Communication Management | The ACM service is used for the following: To manage the transfer of data communication authority between sectors and/or ATSUs To terminate data communications with an ATSU To issue a change of voice frequency |
| ATC Clearance | A Flight Crew under the control of an ATSU transmits reports; makes requests; and receives clearances, instructions, and notifications using ACL. The ACL service specifies dialogue exchanges via air-ground addressed communications between Flight Crews and Controllers working the specific position/sector associated with the aircraft’s physical location. The ACL service may be initiated by either the ground automation/Controller or the avionics/Flight Crew. |
| Departure Clearance | A flight due to depart from an airfield must obtain a departure clearance from the Controlling ATSU (C-ATSU). The DCL service enables a Flight Crew to receive their departure clearance and related route-of-flight information by data communications. The DCL service provides automated assistance to Controllers and Flight Crews to perform these communication exchanges. |
| Downstream Clearance | A Flight Crew may need to obtain clearances or information from an ATSU not yet in control of the aircraft but that will be responsible for control of the aircraft later during the flight, i.e., a downstream ATSU (D-ATSU). |
| ATC Microphone Check | When the voice channel is blocked, such as when an aircraft has a stuck microphone, the AMC service is used to contact some or all aircraft under control of that sector/position. The AMC message instructs a Flight Crew to check the aircraft’s communication equipment to determine if the cause of the problem is a stuck microphone on their aircraft and, when required, take corrective action. |
| Data Link Taxi Clearance | The Flight Crew of an aircraft preparing to depart from an airport or of an aircraft that has just landed must obtain a series of clearances from the C-ATSU in order to proceed from a gate/stand to the runway or from the runway to a gate/stand. The DTAXI service provides automated assistance to Controllers and Flight Crews to perform these communication exchanges for ground-movement operations. D-TAXI clearances are usually provided in response to a Flight Crew request but may also be initiated by the Controller/ATSU automation. D-TAXI clearances may be amended. D-TAXI clearances require a response from the Flight Crew. |
| Common Trajectory Coordination | The COTRAC service is used to establish and coordinate trajectory agreements in real-time using graphical interfaces and automation systems, in particular the Flight Management System (FMS). COTRAC provides trajectory agreements involving multiple constraints, e.g., latitude/longitude, altitude, and airspeed. |
| Data Link Automatic Terminal Information Service | D-ATIS provides automated assistance in requesting and delivering air traffic information including: meteorological conditions, operating procedures, runways and approaches in use, and various other information which may affect the departure, approach, and landing flight phases as well as surface operations relevant to a specified airport(s) in any phase of flight (except in the AOA domain outside of the buffer zone). |
| Data Link Operational Terminal Information Service | D-OTIS provides Flight Crews with compiled meteorological and operational flight information derived from ATC, ATIS, Meteorological Aerodrome Report (METAR), Notice to Airmen (NOTAM), and Pilot Report (PIREP) information tailored to the departure, approach and landing phases of flight. |
| Data Link Operation En Route Information Service | D-ORIS provides Flight Crews with compiled meteorological and operational flight information, derived from ATC, En Route weather information, NOTAMs, and other sources, specifically relevant to an area to be over-flown by the aircraft. |
| Data Link Significant Meteorological Information | The D-SIGMET service provides Flight Crews with advisories of the occurrence, or expected occurrence, of weather phenomena that may affect the safety of aircraft operations. The preparation and issue of SIGMET reports is the prime responsibility of meteorological watch offices. SIGMET information messages are distributed on ground initiative to aircraft in flight through associated ATSUs. |
| Data Link Surface Information and Guidance | D-SIG provides current airport elements necessary for ground movements (e.g., taxiway closures, runway re-surfacing) to the Flight Crew. |
| Arrival Manager Information Delivery | The ARMAND service transmits relevant advisories directly from the ground automation to Flight Crews that are within the optimum-planning horizon of the AMAN (Arrival Manager). The ARMAND service transmits target, expected, or revised controlled arrival time advisories relevant to the destination airport or points in space along the aircraft’s route. The ARMAND service only offers advisories, not clearances, and thus is consistent with the principle of not modifying the route of an aircraft that is in another sector’s airspace. |
| Dynamic Route Availability | The DYNAV service is used by an ATSU to offer a Flight Crew alternative routes as they become available during the course of a flight. DYNAV may be initiated automatically by the automation or manually by the Controller. The ATSU does not need to be in control of the aircraft when providing the DYNAV service. |
| Data Link Flight Update | The D-FLUP service provides ATM-related operational data and information to optimise flight operations. Examples of D-FLUP data include flight-specific information related to the departure sequence, slot-time allocations, flow management advisories, airspace/airport configurations, and special operations such as de-icing. D-FLUP operates on a demand, periodic, or event basis and is available in any phase of flight. |
| Air Traffic Control Surveillance | The SURV service uses Automatic Dependent Surveillance (ADS) positional information provided by equipped aircraft for separation or monitoring purposes. The information can be provided via broadcast, (i.e., ADS – Broadcast [ADS-B]), or via addressed contracts, (i.e., ADS – Contract [ADS-C]). This service can be conducted in all domains independent of radar support. When SURV uses ADS-B, the aircraft providing the data must have the capability to broadcast out, and the recipient for the ADS data (either another aircraft or a ground system) must have the capability to receive and process ADS-B reports. |
| Flight Plan Consistency | The FLIPCY service provides information to an ATSU for the detection of inconsistencies between the ATC flight plan and the flight plan activated in the aircraft’s Flight Management System (FMS). |
| Flight Plan Intent | The FLIPINT service provides information to an ATSU for the detection of inconsistencies between the ATC flight plan and the flight plan activated in the aircraft’s FMS. |
| System Acces Parameters | The SAP service consists of the extraction, transmission, and provision to the Controller or ground automation of specific airborne avionics tactical flight information (e.g., indicated heading, indicated air speed or mach, vertical rate, selected level, and wind vector). The ground system uses the SAP service to provide enhancements to ATC surveillance and trajectory prediction functions. The SAP service is initiated by ATSU automation and conducted on a periodic or event driven basis. |
| Wake Service | The WAKE service provides information enabling encounter-specific separation based on wake vortex characteristics. Ground automation uses the WAKE parameters (e.g., aircraft type, weight, and flap and speed settings) and other environmental data to determine the required minimum separation between a pair of aircraft to avoid a wake vortex encounter. The WAKE service is available in all domains except ORP and AOA. |
| Pilot Preferences Downlink | The PPD service provides automated support for ground automation/Controller trajectory and traffic flow planning. It is used by a Flight Crew to express flight preferences or limitations. The PPD service allows the Flight Crew, in all phases of a flight, to provide the ground automation/Controller with a set of preferences beyond what is available in the filed flight plan (e.g., maximum acceptable flight level) and request modification of some flight plan elements (e.g., desired route or speed limitations). |
| Traffic Information Service | The TIS-B service is used by a ground system to broadcast sensor-based traffic information and/or re-broadcast received air-ground ADS-B information. TIS-B information is displayed on aircraft avionics to provide the Flight Crew with situational awareness of proximate traffic. |
| Data Link Alert | The D-ALERT service enables a Flight Crew to notify appropriate ground authorities when the aircraft is in a state of emergency or in an abnormal situation. |
| Urgent Contact | The Urgent Contact (URCO) service enables an ATSU to establish urgent voice or data communications contact with a Flight Crew or for a Flight Crew to contact an ATSU when other forms of communications have failed. |
| In-Trail Procedures | The ITP service requires both the ACL and SURV services. The ITP service is initiated by issuing an ACL instruction to one aircraft to perform a climb, descent, or station-keep relative to a target aircraft. The aircraft performing the ITP instruction receives the SURV data from the target aircraft and displays the position information on the Cockpit Display of Traffic Information (CDTI). The Flight Crew receiving the ITP instruction identifies the target aircraft using the CDTI and assumes separation responsibility with the target aircraft during the procedure. |
| Merging and Spacing | The M&S service requires both the ACL and SURV services. The M&S service is initiated by a Controller issuing an ACL instruction to one aircraft to perform a merging and spacing manoeuvre relative to a target aircraft. The aircraft performing the M&S instruction receives the SURV data from the target aircraft and displays position information on the CDTI. The Flight Crew receiving the M&S instruction assumes separation responsibility with the target aircraft during the procedure. |
| Crossing and Passing | The C&P service requires both the ACL and SURV services. The C&P service is initiated by a Controller issuing an ACL instruction to one aircraft to perform a crossing and passing manoeuvre relative to a target aircraft. The aircraft performing the C&P instruction then receives the SURV data from the target aircraft and displays the position information on the CDTI. The Flight Crew receiving the C&P instruction assumes separation responsibility with the target aircraft during the procedure. |
| Paired Approach | The PAIRAPP service requires both the ACL and SURV services. The PAIRAPP service is initiated by an ACL instruction to a pair of aircraft to perform a simultaneous approach. Both aircraft performing the simultaneous approach exchange SURV data and display position data on the CDTI. The Flight Crews assume separation responsibility with the partner aircraft during the procedure. |
| Air-to-Air Self Separation | The Air-to-Air Self Separation (AIRSEP) service exchanges data between aircraft to ensure separation in the AOA domain, without the aid of ground ATC support. AIRSEP requires automated airborne algorithms that detect or estimate the probability of conflicts with other flight trajectories, airspace, or weather restrictions along the intended route of flight. |
| Auto Execute | The A-EXEC service provides an automated safety net to capture situations where encounter-specific separation is being used and a non-conformance FLIPINT event occurs with minimal time remaining to resolve the conflict. Subject to local implementations, aircraft that support the A-EXEC service are separated based on encounter-specific conditions. When non-conformance occurs, triggering an imminent loss of separation, the ground automation system generates and sends a resolution to the aircraft for automatic execution without the Flight Crew or Controller in the loop. |
| Data Link Runway Visual Range | The D-RVR service provides Flight Crews with up-to-date RVR information related to an airport’s runway(s). Flight Crews can request RVR information related to any airport’s runway(s) during any phase of flight. The D-RVR information is updated when the specified components of the D-RVR message change by specified criteria. |
| Air Traffic Control Surveillance | The SURV service uses Automatic Dependent Surveillance (ADS) positional information provided by equipped aircraft for separation or monitoring purposes. The information can be provided via broadcast, (i.e., ADS – Broadcast [ADS-B]), or via addressed contracts, (i.e., ADS – Contract [ADS-C]). This service can be conducted in all domains independent of radar support. |

AOC Services

| Name of Service | Description |
| --- | --- |
| AOC Data Link Logon | The Flight Crew activates the data communication system and enters the required flight identification information into the logon page in order for AOC to respond with the correct information. The AOCDLL provides an indication to AOC that the Flight Crew has arrived on-board the aircraft and are prepared to receive AOC generated information in order to conduct the flight. |
| Out-Off-On-In | Movement Service messages including Out-Off-On-In (OOOI) report data are automatically routed to the AOC Movement Control System. This service is a oneway downlink from the aircraft to AOC to report significant points in the flight’s progress. |
| Notice to Airmen | The NOTAM service provides information to alert the Flight Crew in the event of the following: - Hazards such as air-shows and parachute jumps - Closed runways - Inoperable radio navigational aids - Military exercises with resulting airspace restrictions - Inoperable lights on tall obstructions - Temporary erection of obstacles near airfields (e.g., cranes) |
| Free Text | The FREETEXT service includes miscellaneous uplinks and downlinks via textual messages between the cockpit and AOC or other ground based units. This service does not include cockpit-to-cockpit exchanges. |
| Textual Weather Report | The WXTEXT service is initiated by Flight Crew requests for airport weather information. The WXTEXT service includes Meteorological Aerodrome Reports (METARs) and Terminal Area Forecasts (TAFs). The AOC responds to Flight Crew requests by delivering the requested weather information to the cockpit. |
| Position Report | The POSRPT service includes automatic downlink of position during the climb, cruise, and descent portions of the flight. The primary purpose of this service is delivery of position reports at required waypoints for use in AOC tracking systems. During all phases of flight, but principally En Route, the Flight Crew can also manually initiate the POSRPT service for such things as in-range reporting. |
| Flight Status | The FLTSTAT service includes, for example, malfunction reports including fault reporting codes that allow maintenance and spares to be pre-positioned at the parking stand after landing. Fault reporting can be done manually or can be automatically sent when triggered by an event. |
| Fuel Status | The FUEL service downlinks fuel status En Route and prior to landing. This service allows ground services to dispatch refuelling capability promptly after landing. The Flight Crew also reports the fuel status upon specific request from the AOC. |
| Gate and Connecting Flights Status | The GATES service for passengers and Flight Crew includes manual and automatic uplink of connecting flights, estimated time of departure (ETD), and gate assignments before landing. Information about rebooking may also be included in case of late arrival or cancelled flights. |
| Engine Performance Reports | The ENGINE service is used to downlink aircraft condition monitoring system (engine and systems) reports in real time, automatically and on request. This is usually done in the En Route phase. |
| Maintenance Problem Resolution | Using the MAINTPR service, maintenance personnel and a Flight Crew are able to discuss and correct technical problems while the aircraft is still airborne. Although voice is customarily used for the discussion of the problem, this service may be used to provide the instructions for problem resolution as a text message between maintenance personnel and Flight Crew. |
| Flight Plan Data | The FLTPLAN service provides the operators with the ability to request and receive the AOC-developed flight plan for comparison to that assigned by ATC and for loading into avionics. AOC flight plans have more information than flight plans filed with ATS. |
| Load Sheet Request/Transfer | Upon downlink request, the Load Sheet Control System uplinks planned load sheet and cargo documentation in the LOADSHT service. A number of data calculations relating to aircraft loading, takeoff, and landing are required to enhance safety and/or meet aviation regulations. The load sheet includes weight and balance information which insures resultant weights and centre of gravity are within the performance limits of the aircraft. A preliminary load sheet is transferred right after an AOCDLL. A final load sheet is typically transferred just before pushback, but can be transmitted as late as just before takeoff. The load sheet will also include a passenger manifest & fuel status. |
| Flight Log Transfer | The FLTLOG service is used to track the aircraft’s flight times, departure and destination information, etc. Flight log information may be manually requested by the AOC or automatically downlinked. |
| Real-Time Maintenance Information | The MAINTRT service allows aircraft parameters to be sent to the airline maintenance base in real-time to monitor the operational status of the aircraft and to troubleshoot problems identified during the flight. Information could include engine data, airframe systems, etc. This service allows information to be obtained more quickly than the normal maintenance data acquisition via on-board recorders. It is typically event driven, triggering a flow of information until resolution is achieved. The maintenance personnel may request other parameters to be downlinked in addition to those triggered by the event. |
| Graphical Weather Information | The WXGRAPH service sends weather information to the aircraft in a form that is suitable for displaying graphically on displays in the cockpit (e.g., vector graphics). This service provides advisory information which supplements or replaces the textual weather information available in current AOC services. Graphical weather information is expected to be more strategic in nature and will supplement on-board tactical weather radar which has inherent range and display limitations. |
| Real-time Weather Reports for Met Offices | With the WXRT service, information derived by the aircraft on the environment in which it is flying (e.g., wind speed and direction, temperature) can be sent automatically in real-time to weather forecasting agencies to help improve predictions. |
| Technical Log Book Update | The TECHLOG service allows the Flight Crew to complete the aircraft’s technical log electronically and send the updated log to the maintenance base. Information regarding the technical status, physical condition, and trouble reports of the aircraft can therefore be obtained much more quickly so that any remedial action can be taken at an early stage. |
| Cabin Log Book Transfer | The CABINLOG service allows the cabin crew to complete the aircraft’s cabin equipment log electronically and send the updated log to the AOC. Information regarding the status of the cabin equipment can therefore be obtained much more quickly so that any remedial action can be taken at an early stage. |
| Update Electronic Library | The Electronic Library will replace many of the paper documents currently required to be carried in the cockpit (e.g., Aircraft Manual, Standard Instrument Departures (SIDs), Standard Terminal Arrival Routes (STARs), and Airspace Charts). The UPLIB service enables this information to be updated electronically either by request or automatically. The transmitted information will be used to update various avionic systems (e.g., an Electronic Flight Bag [EFB] device). As such, this service carries safety-related information used for navigational purposes by the Flight Crew/Aircraft. |
| Software Loading | The SWLOAD service allows new versions of software to be uploaded to non-safety related aircraft systems whilst the aircraft is at the gate. |

# Footnotes

1 	44.1.1	The term communications as used in this Article includes radiotelegrams, radiotelephone calls and radiotelex calls.

Taken from COCR. For complete definitions, please refer to COCR.

Taken from COCR. For complete definitions, please refer to COCR.