|  | International Civil Aviation Organization WORKING PAPER | ACP-WGF19/IP5 |
| --- | --- | --- |

| ASCFG - Interference Group – 4th Meeting Toulouse, DSNA 11th to 12th December 2007 |  |
| --- | --- |

Information Paper IP7

Agenda Item 7: ECC Project Team FM22

Measurement campaign on the MPX Power of VHF band FM Broadcasting Stations by ECC Project Team FM22

Presented/prepared by: Eurocontrol

| Project Team FM22 |  |
| --- | --- |
| 28th Meeting of FM22 Riga, 04 – 07 September 2007 | FM22(07)57 |
| Date issued: 29 August 2007 Source: Hungary Subject: Measurement campaign on the MPX Power of VHF band FM Broadcasting Stations |
| Summary Listening to the radios in the recent years, almost everywhere in Europe could have been experienced a loudness battle amongst (mainly commercial) terrestrial FM broadcasting stations operated in the 88 – 108 MHz frequency band. They apply audio processing on the modulation signal that can result in the MPX** power exceeds significantly the maximum 0 dBr value of the relevant ITU-R BS.412-9 recommendation. According to this recommendation, the increased MPX power can result in protection ratio degradation (interference, signal/noise deterioration) of the reception of other broadcasts. It means, the coverage area of the broadcasting stations operated in adjacent channels decreases that makes the previous network planning calculations of the coverage area unreliable and false. The 27th meeting of PT22 in Timisoara decided to organise a measurement campaign on the MPX power and FM deviation of European FM broadcasting stations. The goal of the campaign was to get a general overview about; how the MPX powers of the FM broadcasting stations comply with (or exceed) the relevant ITU regulations in the different countries, whether is it necessary to keep the rule of ITU-Rec., if yes, how can be achieved that the limitation on MPX power must be stated in all licensing documents and each broadcasting stations equally comply with this regulation. |
| Proposal The Riga meeting of PT22 will evaluate the acquired measurement data detailed in the ANNEX of this document and specifies the needed next steps. If the meeting needs further data, the second phase of the campaign can begin after the autumn meeting in 2007 and lasts until the next spring meeting of P22. |
| Background Rec. ITU-R BS.412-9 ‘Planning standards for terrestrial FM sound broadcasting at VHF’ |

* ECC policy is that in general all documents should be publicly available unless the author of the document requires that it be restricted to ECC family participants only.

** MPX: Signal containing all information, including pilot tone and any supplemental signal which is used to frequency modulate the VHF FM transmitter [Reference ETSI ETS 300484]

#### 1.	Introduction

By processing the modulation signal of the FM audio broadcasting stations, the studios desire to achieve louder sound effects, whereby they expect the increasing number of their listeners. In order to achieve a louder sound they apply an external audio signal processor unit, which amplifies the softer sounds but by clipping, lets the louder sounds unchanged.

When applying an audio processor unit at the modulator input of FM transmitters, the momentary values of MPX deviation approach the maximum ( 75 kHz deviation more frequently. The audio processor allows to increasing the modulation power without exceeding the frequency deviation limit.

However, increasing the loudness (together with the increasing MPX power) can result in radio noise in adjacent radio channels. The radio noise that is made by a neighbouring FM station is proportional to its increased MPX power, in case of the receivers are operated at the edges of their radio coverage area. In consequence, the boundary-line of the protected coverage area of an adjacent channel broadcasting station will shrink in this case.

Recommendation ITU-R BS.412, § 2.3 provides protection ratios for interference free FM receptions. (must be at least 33 dB, in cases of stereophonic, max. (75 kHz modulation and 100 kHz carrier frequency spacing)

The § 2.5.1 of this Recommendation assumes that the maximum peak deviation must not exceed (75 kHz at any time and the power of a complete multiplex signal integrated over any interval of 60 s, shall not be higher than the power of a multiplex signal, which is modulated with a sinusoidal tone, which causes a peak deviation of 19 kHz ( 0dBr).

Similarly to the increased FM deviation, the exceeded MPX power can results in protection ratio degradation (interference, signal/noise deterioration) in the reception of adjacent channels. The § 2.5.1 of the ITU-R also states: ‘It is important that the limits for modulation levels should not be exceeded, otherwise the radiated power of the transmitter has to be reduced …’. (?)

#### 2.	The monitoring campaign

The 27th meeting of PT22 in Timisoara decided to organise a measurement campaign on the MPX power and FM deviation of FM broadcasting stations to get an overview about the compliance of FM broadcasting stations of European countries with the relevant ITU regulations. The results of campaign will be reported to WG FM for subsequent action, if required.

Originally, the monitoring campaign was planned to be performed in 2 phases. The first phase started from the end of April until the next FM22 meeting in September 2007. This phase of the campaign has been finished by now.

Although only a few countries joined in the campaign (Austria, Czech Rep., Germany, Hungary and Portugal), but they measured not only their home broadcasting stations but also some foreign stations of their neighbouring countries operated near their common borders, so their acquired measurement data seem relatively sufficient for assessing the observance of ITU-R regulations on MPX power and deviation, in the European countries. On the bases of the detailed results in ANNEX of this document, the Riga meeting of PT22 can evaluate the results and specifies the needed next steps.

If the meeting needs further data, the second phase of the campaign can begin after the autumn meeting 2007 and lasts until the spring meeting of P22.

#### 3.	Conclusions

By the statistical assessment of measured data and received answers on the questions of the document FM22(07)09, the following conclusions can be drown:

3.1 Assessment of the measured data:

In the course of the campaign, the monitoring services of 5 participant countries (Austria, Czech Republic, Germany, Hungary and Portugal) measured the maximum multiplex power and deviation of 546 FM broadcasting stations of 18 European countries (the Austrian, Belgian, Croatian, Czech, French, German, Hungarian, Luxembourgian, Polish, Rumanian, Serbian, Slovakian, Slovenian, Spanish, Swiss, Portuguese and Ukrainian broadcasting stations).

- Austrian measurement

|  | Austrian stations (107 tested BS) | Foreign stations (53 tested BS) |
| --- | --- | --- |
| MPX power | Broadcasting stations | Broadcasting stations |
| ≤ 0 dBr | 2 | (2%) | -- | -- |
| ( 0…(3 dBr | 99 | (92%) | 18 | (34%) |
| ( 3 dBr | 6 | (6%) | 35 | (66%) |
| Max. dBr | 7.17 dBr | 7.6 dBr |

- Measurement of Czech Republic

|  | Stations of Czech Republic (25 tested BS) | Slovak stations (5 tested BS) |
| --- | --- | --- |
| MPX power | Broadcasting stations | Broadcasting stations |
| ≤ 0 dBr | -- | -- | 1 | (20%) |
| ( 0…(3 dBr | 3 | (12%) | 1 | (20%) |
| ( 3 dBr | 22 | (88%) | 3 | (60%) |
| Max. dBr | 7.5 dBr | 5.5 dBr |

- Measurement of Germany

|  | Stations of Germany (78 tested BS) | Foreign stations (42 tested BS) |
| --- | --- | --- |
| MPX power | Broadcasting stations | Broadcasting stations |
| ≤ 0 dBr | 23 | (30%) | 1 | (3%) |
| ( 0…(3 dBr | 47 | (60%) | 17 | (40%) |
| ( 3 dBr | 8 | (10%) | 24 | (57%) |
| Max. dBr | 5.5 dBr | 9.1 dBr |

- Measurement of Hungary

|  | Hungary (92 tested BS) | Foreign stations (79 tested BS) |
| --- | --- | --- |
| MPX power | Broadcasting stations | Broadcasting stations |
| ≤ 0 dBr | 4 | (4%) | 11 | (14%) |
| ( 0…(3 dBr | 26 | (28%) | 29 | (37%) |
| ( 3 dBr | 62 | (68%) | 39 | (49%) |
| Max. dBr | 8.2 dBr | 11.03 dBr |

- Measurement of Portugal (60 home and 5 foreign stations)

|  | Portugal (60 tested BS) | Spain (5 tested BS) |
| --- | --- | --- |
| MPX power | Broadcasting station(s) | Broadcasting stations |
| ≤ 0 dBr | 1 | (2%) | - | -- |
| ( 0…(3 dBr | 3 | (5%) | - | -- |
| ( 3 dBr | 56 | (93%) | 5 | (100%) |
| Max. dBr | 8.1 dBr | 9.77 dBr |

Summary of the measure result:

Almost the half (47.9 %) of the tested 546 FM broadcasting stations exceeded the +3 dBr MPX power.

Less then the half (44.7 %) of the MPX power of the tested 546 FM broadcasting stations were between 0 … +3 dBr.

Only 7.9 % of the tested 546 FM broadcasting stations complied with the relevant ≤ 0 dBr regulation of ITU-R § 2.5.1. on modulation power.

3.2	Conclusions from the answers on the questionnaire of doc. FM22(07)09:

By the questions of the document FM22(07)09 submitted to our previous meeting, we asked the participants of PT22 for their answers on their domestic application of the relevant part of ITU-R recommendation, the official control and the observation of the maximum MPX power and deviation by their broadcasting stations, and the experienced occurrence of interference cases from the increased MPX powers in their country.

Some answers on the questionnaire of FM22(07)09 document indicated that some countries do not control the MPX power of FM broadcasting station, because they had no received complaint about interference cases from the higher-level modulation power. It is really imaginable, since the listeners usually do not complain because of the reasons as follows:

- The increased modulation power not always and not everywhere causes reception degradation, not even in the adjacent channels. On the sites, where a transmission wanted to be listened to can be received with high field strength, the quality of the reception is not influenced even by an adjacent channel broadcasting station operated with increased MPX power. (In this case, there is no reason to complain on disturbance.)

- A broadcasting station operated with increased MPX power has only impact on the reception quality if the receiver tuned on an adjacent channel, is operated although within-, but near the margin of the coverage area. In such a case the listener may think, he tries to receive an inaccessible, distant broadcasting station so he tunes further his radio, looking for another broadcast with better reception quality. In this case the jamming station reduces the coverage area of an adjacent channel broadcast, whereas only the transmission with higher modulation power makes the reception inaccessible for the potential listener. (No complaint, because the listener does not know his reception is spoilt on account of an over modulated jamming station in the adjacent channel.)

- Inside large countries or in case of a country partially or entirely bordering on see, there is no need to share the utilizable radio frequencies (co-ordination) with more foreign countries, consequently there is no need to use the adjacent channel in the vicinity of each other. In such a case of course, there is no chance of they diminish the coverage area of each other, by their overstepped MPX power.

The demand on free radio channels is increasing and increasing. Nowadays newer and newer broadcasting stations want to start their radio emission in the FM radio band, therefore it must be taken into account that where is no problem with radio reception today, it will be possible tomorrow.

Having a look at the acquired measurement data of the campaign and on the bases of the answers of the above mentioned questionnaire, it can be stated that to less (( +3dBr) or larger extent (( +3dBr), but the overwhelming majority of MPX power of the FM broadcasting stations have ignored (exceeded) the limit of the relevant ITU recommendation, therefore there is a need to revise the importance of this regulation.

If this regulation is important, it is impossible that only a few countries must control the modulation power of their FM stations, since the jamming crosses the border. It must be achieved that each communications authority must strictly control the compliance with this regulation.

ANNEX

Campaign on MPX Power and MPX deviation control

of FM Sound Broadcasting Stations

Detailed measurement results

|  | FM deviation and MPX power measurements of Germany (Hubmessungen) |  |  |  |
| --- | --- | --- | --- | --- |
|  |  | Germany |  |  |  |  |  |  |  |
| Date of measurement | Name of transmitter | Country | Frequency | RF level * | Max. MPX power | Max. FM deviation | Remarks | MPX power exceeded | Deviation exceeded |
| 2007.08.02 | Bad Reichenhall | D | 103,7 | 89,0 | 5,5 | 125 | Antenne Bayern | X | X |
| 2007.07.11 | Langenberg | D | 96,5 | 84,0 | 1,5 | 120 | BFBS | X | X |
| 2007.07.25 | Guben | D | 92,1 | 84,8 | 5,2 | 116 |  | X | X |
| 2007.08.14 | Aurich | D | 103,1 | 85,5 | 2,0 | 103 | FFN | X | X |
| 2007.07.17 | Merkur | D | 99,6 | 99,8 | 0,8 | 100 | SWR 3 | X | X |
| 2007.08.08 | Münster | D | 92,0 | 70,0 | -0,5 | 100 | WDR 5 |  | X |
| 2007.08.01 | Waldshut | D | 91,8 | 109,4 | 2,9 | 99 | Argovia | X | X |
| 2007.07.25 | Forst | D | 102,7 | 83,6 | 4,0 | 97 |  | X | X |
| 2007.07.12 | Dresden | D | 97,3 | 98,5 | 1,7 | 94 |  | X | X |
| 2007.07.30 | Freiburg | D | 94,7 | 109,8 | 1,5 | 93 | Antenne 106.0 | X | X |
| 2007.07.12 | Dresden | D | 92,2 | 99,9 | 2,2 | 90 |  | X | X |
| 2007.08.15 | Meppen | D | 99,0 | 85,5 | 1,8 | 90 | NDR-Info | X | X |
| 2007.07.18 | München | D | 93,3 | 73,8 | 0,0 | 90 | Radio ENERGY |  | X |
| 2007.07.26 | Eisenhüttenstadt | D | 103,7 | 88,4 | 3,9 | 86 |  | X | X |
| 2007.07.09 | Grosser Feldberg Taunus | D | 105,9 | 87,0 | 1,6 | 86 | FFH | X | X |
| 2007.07.25 | Konstanz | D | 101,8 | 119,9 | -0,2 | 86 | Seefunk |  | X |
| 2007.07.12 | Garmisch-Partenk. | D | 106,2 | 80,1 | 4,0 | 85 | Radio OBERLAND | X | X |
| 2007.08.08 | Münster | D | 97,5 | 87,0 | 3,0 | 85 | Deutschlandradio | X | X |
| 2007.08.03 | Simbach | D | 103,0 | 71,2 | 3,0 | 85 | Radio Trausnitz | X | X |
| 2007.08.02 | Högl | D | 100,3 | 98,4 | 2,0 | 85 | Deutschlandfunk | X | X |
| 2007.07.18 | München | D | 89,0 | 75,1 | 1,0 | 85 | Radio 2-Day | X | X |
| 2007.07.11 | Langenberg | D | 101,3 | 86,0 | 0,0 | 85 | WDR 4 |  | X |
| 2007.07.26 | Lindlar | D | 105,2 | 70,0 | 0,0 | 85 | Radio Berg |  | X |
| 2007.07.20 | Aachen | D | 100,8 | 76,0 | -0,5 | 85 | WDR 2 |  | X |
| 2007.07.12 | Dresden | D | 100,2 | 79,8 | 2,9 | 84 |  | X | X |
| 2007.08.13 | Freienwill | D | 103,3 | 87,1 | 0,6 | 83 | DLF | X | X |
| 2007.07.30 | Freiburg | D | 99,2 | 106,7 | 0,4 | 82 | SWR 3 | X | X |
| 2007.08.16 | Süderlügum | D | 91,5 | 89,3 | 0,4 | 82 | N-Joy | X | X |
| 2007.07.11 | Langenberg | D | 106,7 | 85,0 | 0,0 | 82 | 1 Live |  | X |
| 2007.07.12 | Langenberg | D | 103,3 | 86,0 | -0,5 | 82 | WDR 5 |  | X |
| 2007.08.01 | Moers | D | 91,7 | 78,0 | 2,0 | 80 | Radio KW | X | X |
| 2007.07.26 | Köln | D | 105,8 | 80,0 | 1,5 | 80 | Radio Erft | X | X |
| 2007.08.01 | Oberhausen | D | 106,2 | 101,0 | 1,5 | 80 | Antenne Ruhr | X | X |
| 2007.07.11 | Landsberg | D | 101,7 | 114,2 | 0,5 | 80 | DLF / FM-dev in peaks | X | X |
| 2007.07.12 | Langenberg | D | 88,8 | 85,0 | 0,0 | 80 | WDR 5 |  | X |
| 2007.07.20 | Aachen | D | 106,4 | 80,0 | 0,0 | 80 | 1 Live |  | X |
| 2007.08.08 | Münster | D | 100,0 | 75,0 | -0,5 | 80 | WDR 4 |  | X |
| 2007.07.25 | Ermatingen (Reichenau) | D | 92,9 | 112,8 | 2,0 | 79 | DRS1 | X | X |
| 2007.07.10 | Grosser Feldberg Taunus | D | 102,5 | 89,0 | -0,3 | 79 | HR4 |  | X |
| 2007.07.25 | Ermatingen (Reichenau) | D | 99,1 | 113,8 | 0,2 | 78 | DRS2 | X | X |
| 2007.07.12 | Dresden | D | 103,5 | 82,5 | 4,0 | 77 |  | X | X |
| 2007.07.10 | Krehberg | D | 105,0 | 85,0 | 2,0 | 77 | FFH | X | X |
| 2007.07.12 | Langenberg | D | 95,1 | 86,0 | -2,0 | 77 | WDR 3 |  | X |
| 2007.07.17 | Fremersberg | D | 91,7 | 96,9 | 0,3 | 76 | DASDING | X | X |
| 2007.08.14 | Aurich | D | 101,8 | 91,1 | -0,6 | 76 | DLF |  | X |
| 2007.07.31 | Oberaudorf | D | 104,2 | 88,9 | 2,0 | 75 | Radio CHARIVARI | X |  |
| 2007.07.26 | Köln | D | 107,1 | 76,0 | 1,5 | 75 | Radio Köln | X |  |
| 2007.08.02 | Unterau/Untersberg | D | 96,1 | 75,3 | 1,0 | 75 | Bayern 3 | X |  |
| 2007.07.17 | Wendelstein | D | 98,5 | 72,3 | 1,0 | 75 | Bayern 3 | X |  |
| 2007.07.26 | Nordhelle | D | 102,7 | 75,0 | 0,5 | 75 | DLF | X |  |
| 2007.07.17 | Fremersberg | D | 103,8 | 103,4 | 0,4 | 75 | Big FM | X |  |
| 2007.07.11 | Wesel | D | 102,8 | 86,0 | 0,0 | 75 | DLF |  |  |
| 2007.07.11 | Langenberg | D | 99,2 | 87,0 | -1,0 | 75 | WDR 2 |  |  |
| 2007.08.02 | Helpterberg | D | 105,8 | 102,4 | 2,8 | 74 |  | X |  |
| 2007.08.15 | Lingen | D | 104,3 | 85,0 | 2,0 | 73 | Hit-Radio | X |  |
| 2007.07.12 | Grosser Feldberg Taunus | D | 98,7 | 85,0 | 1,0 | 73 | AFN | X |  |
| 2007.07.18 | Lahr | D | 107,4 | 125,0 | 3,8 | 71 | Radio Ohr | X |  |
| 2007.08.14 | Darmstadt | D | 92,4 | 78,0 | 0,3 | 71 | Sky Radio | X |  |
| 2007.08.03 | Unterau/Untersberg | D | 87,8 | 79,5 | 0,0 | 70 | Bayern 5 |  |  |
| 2007.07.17 | Wendelstein | D | 102,3 | 70,7 | -0,5 | 70 | Bayern 4 |  |  |
| 2007.07.09 | Grosser Feldberg Taunus | D | 89,3 | 84,0 | 1,7 | 69 | HR3 | X |  |
| 2007.08.02 | Helpterberg | D | 99,1 | 99,9 | 0,8 | 69 |  | X |  |
| 2007.07.12 | Grosser Feldberg Taunus | D | 96,7 | 84,0 | -1,2 | 69 | HR2 |  |  |
| 2007.07.10 | Darmstadt | D | 107,0 | 93,0 | -2,7 | 69 | HRinfo |  |  |
| 2007.07.18 | Oberachern | D | 90,5 | 106,5 | 2,6 | 68 | Radio Ohr | X |  |
| 2007.07.12 | Grosser Feldberg Taunus | D | 94,4 | 82,0 | 0,8 | 68 | HR1 | X |  |
| 2007.08.01 | Duisburg | D | 92,2 | 72,0 | 0,5 | 65 | Radio Duisburg | X |  |
| 2007.08.13 | Flensburg | D | 93,2 | 86,0 | 1,0 | 64 | NDR 2 | X |  |
| 2007.08.14 | Emden | D | 93,4 | 94,1 | 1,0 | 63 | DLR-Kultur | X |  |
| 2007.08.02 | Helpterberg | D | 103,8 | 103,2 | 2,1 | 60 |  | X |  |
| 2007.08.15 | Lingen | D | 97,8 | 85,4 | 1,8 | 60 | NDR 2 | X |  |
| 2007.07.18 | München | D | 96,3 | 74,7 | 1,0 | 60 | Radio GONG 96,3 | X |  |
| 2007.08.08 | Münster | D | 95,4 | 80,0 | 0,5 | 60 | Antenne Münster | X |  |
| 2007.07.17 | Merkur | D | 100,9 | 95,3 | 1,0 | 58 | Neue Welle | X |  |
| 2007.08.13 | Freienwill | D | 101,4 | 81,0 | -0,3 | 56 | RSH |  |  |
| 2007.07.18 | München | D | 95,5 | 72,4 | 0,0 | 53 | Radio CHARIVARI |  |  |
| 2007.08.14 | Darmstadt | D | 103,4 | 86,0 | 2,0 | 47 | Radio Darmstadt | X |  |
| 2007.07.18 | München | D | 92,4 | 73,2 | -3,5 | 40 | Radio HOREB |  |  |
| 2007.07.12 | Zugspitze/Ehrwald | D/AUT | 100,7 | 62,7 | 2,5 | 75 |  | X | 2007.07.12 |

|  |  | Austria |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2007.07.31 | Kufstein | AUT | 104,9 | 71,3 | 3,0 | 100 | Life Radio - Possible unknown TX on 104,8 MHz with 30 dbµV | X | X |
| 2007.08.02 | Salzburg | AUT | 90,9 | 100,0 | 1,5 | 75 | Österreich 1 | X |  |
| 2007.08.02 | Salzburg | AUT | 104,6 | 91,0 | 2,0 | 73 | FM 4 | X |  |
| 2007.08.01 | Hallein | AUT | 88,6 | 88,5 | 2,0 | 70 | Österreich 3 | X |  |
| 2007.08.01 | Hallein | AUT | 95,6 | 92,3 | 2,0 | 70 | Radio Salzburg | X |  |
| 2007.08.02 | Salzburg | AUT | 106,2 | 68,7 | 2,0 | 70 | Welle 1 | X |  |
|  |  | Belgium |  |  |  |  |  |  |  |
| 2007.07.31 | Beho | BEL | 106,4 | 75,0 | 2,9 | 91 | 7FM | X | X |
| 2007.07.31 | Recht | BEL | 104,1 | 82,0 | 3,2 | 89 | Belgischer Rundfunk | X | X |
|  |  | Czech Rep. |  |  |  |  |  |  |  |
| 2007.07.11 | Liberec | CZE | 101,4 | 84,2 | 4,5 | 80 |  | X | X |
|  |  | France |  |  |  |  |  |  |  |
| 2007.08.02 | Metz | F | 106,8 | 86,0 | 4,3 | 120 | France Info | X | X |
| 2007.07.16 | Straßburg-Nordheim | F | 97,3 | 107,9 | 5,2 | 112 | France Inter | X | X |
| 2007.07.16 | Straßburg-Nordheim | F | 104 ,4 | 107,9 | 4,6 | 112 | France Info | X | X |
| 2007.07.16 | Straßburg-Nordheim | F | 101,4 | 108,4 | 4,3 | 98 | Bleu Alsace | X | X |
| 2007.07.30 | Mulhouse | F | 95,3 | 108,4 | 7,2 | 81 | Phare FM | X | X |
| 2007.08.02 | Sarreguemines | F | 88,4 | 84,0 | 6,6 | 79 | RTL | X | X |
| 2007.07.19 | Colmar 2 | F | 100,1 | 102,6 | 6,0 | 77 | Florival | X | X |
| 2007.07.30 | Mulhouse | F | 94,8 | 114,9 | 4,2 | 75 | Europe 1 | X |  |
| 2007.07.18 | Colmar-Ingersheim | F | 88,0 | 103,2 | 9,1 | 73 | Sky Rock | X |  |
| 2007.07.19 | Colmar 2 | F | 107,3 | 108,5 | 6,3 | 73 | RTL | X |  |
| 2007.07.18 | Colmar-Ingersheim | F | 103,5 | 101,3 | 5,8 | 73 | Radio Dreyeckland | X |  |
| 2007.07.17 | Wissembourg | F | 94,6 | 89,0 | -2,6 | 31 | France Bleu Alsace |  |  |

|  |  | Holland |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2007.07.20 | Roermond | HOL | 100,3 | 76,0 | 6,0 | 105 | Radio 1 Limburg, average deviation 75 kHz | X | X |
| 2007.07.20 | Roermond | HOL | 88,2 | 75,0 | 7,0 | 100 | Radio 2, average deviation 75 kHz | X | X |
| 2007.07.20 | Roermond | HOL | 104,8 | 76,0 | 2,0 | 80 | Radio 1, 75 kHz deviation exceeded during commercials | X | X |
|  |  | Luxemburg |  |  |  |  |  |  |
| 2007.08.01 | Hosingen | LUX | 97,0 | 107,0 | 5,0 | 77 | RTL (deutsch) | X | X |
| 2007.08.01 | Hosingen | LUX | 92,5 | 105,0 | 4,7 | 77 | RTL (letzebuergisch) | X | X |
|  |  | Poland |  |  |  |  |  |  |  |
| 2007.07.11 | Luban | POL | 99,0 | 84,3 | 4,7 | 118 |  | X | X |
| 2007.08.01 | Szczecin | POL | 92,0 | 82,7 | 3,3 | 84 |  | X | X |
| 2007.08.01 | Szczecin | POL | 88,9 | 71,1 | 4,2 | 82 |  | X | X |
| 2007.07.31 | Zielona Gora | POL | 105,0 | 78,4 | 1,5 | 80 |  | X | X |
| 2007.08.01 | Szczecin | POL | 106,7 | 65,6 | 2,2 | 75 |  | X |  |
| 2007.07.11 | Luban | POL | 89,4 | 82,9 | 4,6 | 73 |  | X |  |
| 2007.07.10 | Luban | POL | 93,8 | 88,5 | 5,1 | 72 |  | X |  |
| 2007.08.01 | Szczecin | POL | 95,2 | 71,8 | 3,2 | 65 |  | X |  |
| 2007.07.31 | Zielona Gora | POL | 88,3 | 78,6 | 3,6 | 62 |  | X |  |
| 2007.07.26 | Zielona Gora | POL | 106,4 | 78,6 | 2,7 | 62 |  | X |  |
|  |  | Switzerland |  |  |  |  |  |  |
| 2007.07.31 | St. Chrischona | SUI | 94,5 | 90,3 | 2,9 | 78 | Radio X | X | X |
| 2007.07.31 | St. Chrischona | SUI | 101,7 | 104,9 | 2,6 | 76 | Basel 1 | X | X |
| 2007.07.31 | St. Chrischona | SUI | 107,6 | 101,5 | 2,1 | 76 | Basilisk | X | X |
| 2007.07.31 | St. Chrischona | SUI | 103,6 | 111,6 | 1,9 | 76 | DRS 3 | X | X |
| 2007.08.01 | Tägerwillen | SUI | 99,5 | 112,1 | 2,7 | 73 | Top | X |  |

|  | FM deviation and MPX power measurements of Austria |  |
| --- | --- | --- |
| Date of measurement | Name of transmitter | Country | Frequency | RF level * | Max. MPX power | Max. FM deviation | Remarks Cumulated MPX deviation 0,001% (kHz) |
|  |  | Austria |  |  |  |  |  |
| 2007.06.27 | WIEN 1 Kahlenberg / OE3 |  | 92,9 | 94,0 | 3,6 | ±77,9 | 73,2 |
| 2007.06.27 | WIEN 1 Kahlenberg / Kronehit |  | 94,0 | 80,0 | 0,2 | ±124,8 | 76,8 |
| 2007.06.27 | WIEN 1 Kahlenberg / 88,6 |  | 107,3 | 80,0 | -0,1 | ±150 | 82,6 |
| 2007.06.27 | WIEN 1 Kahlenberg / OE2-B |  | 92,9 | 94,0 | 3,6 | ±77,9 | 73,2 |
| 2007.07.26 | WIEN 4 Donauturm / Arabella |  | 92,9 | 94,0 | 3,6 | ±77,9 | 73,2 |
| 2007.07.26 | WIEN 4 Donauturm / Orange |  | 94,0 | 80,0 | 0,2 | ±124,8 | 76,8 |
| 2007.07.26 | WIEN 4 Donauturm / Stephansdom |  | 107,3 | 80,0 | -0,1 | ±150 | 82,6 |
| 2007.07.16 | WIEN 5 Arsenal / Energy |  | 104,2 | 91,0 | 2,3 | ±80,9 | 75,6 |
| 2007.07.17 | WAIDHOFEN YB 1 Sonntagberg / OE3 |  | 88,2 | 89,0 | 1,6 | ±66,8 | 61,5 |
| 2007.07.17 | WAIDHOFEN YB 1 Sonntagberg / OE2-N |  | 93,5 | 89,0 | 2,3 | ±70,9 | 67,4 |
| 2007.07.17 | WAIDHOFEN YB 1 Sonntagberg / OE1 |  | 99,6 | 90,0 | 0,6 | ±70,3 | 65,6 |
| 2007.07.17 | WAIDHOFEN YB 3 Basilika / R.Maria |  | 104,7 | 89,0 | -2,9 | ±70,9 | 56,8 |
| 2007.07.17 | WAIDHOFEN YB 5 / Kronehit |  | 101,3 | 73,0 | 2,3 | ±80,9 | 65,0 |
| 2007.06.26 | WR NEUSTADT Sonnenberg / Party FM |  | 106,7 | 76,0 | 3,0 | ±77,9 | 73,2 |
| 2007.07.03 | MATTERBURG Heuberg / OE1 |  | 89,0 | 94,0 | 1,3 | ±72,1 | 69,1 |
| 2007.07.03 | MATTERBURG Heuberg / OE2-B |  | 96,2 | 98,0 | 3,0 | ±77,3 | 73,2 |
| 2007.07.03 | MATTERBURG Heuberg / OE3 |  | 100,9 | 95,0 | 2,2 | ±70,9 | 66,8 |

| 2007.07.03 | MATTERBURG Heuberg / Kronehit |  | 103,4 | 93,0 | 2,5 | ±103,7 | 68,0 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 2007.07.03 | MATTERBURG Heuberg / HIT FM |  | 106,3 | 90,0 | 2,8 | ±83,8 | 68,6 |
| 2007.07.18 | RECHNITZ Hirschenstein / OE3 |  | 87,9 | 90,0 | 3,0 | ±76,2 | 72,1 |
| 2007.07.18 | RECHNITZ Hirschenstein / OE1 |  | 90,6 | 88,0 | 2,5 | ±75,0 | 72,7 |
| 2007.07.18 | RECHNITZ Hirschenstein / OE2-B |  | 93,5 | 89,0 | 2,7 | ±73,8 | 70,9 |
| 2007.07.18 | RECHNITZ Hirschenstein / FM4 |  | 97,4 | 90,0 | 2,7 | ±75,6 | 72,7 |
| 2007.07.18 | RECHNITZ Hirschenstein / Kronehit |  | 104,1 | 89,0 | 3,0 | ±76,2 | 72,1 |
| 2007.07.18 | RECHNITZ 2 Hirschenstein / HIT FM |  | 105,5 | 85,0 | 1,5 | ±68,6 | 63,3 |
| 04.07.2007 | BREGENZ 1 Pfänder / Ö1 |  | 93,3 | 101 | 2 | 76,8 | 73,8 |
| 04.07.2007 | BREGENZ 1 Pfänder / Ö3 |  | 89,6 | 101 | 2,55 | 76,2 | 69,7 |
| 04.07.2007 | BREGENZ 1 Pfänder / Ö2 |  | 98,2 | 101 | 2,58 | 74,4 | 68,6 |
| 04.07.2007 | BREGENZ 1 Pfänder / FM4 |  | 102,1 | 102 | 2,71 | 81,4 | 74,4 |
| 04.07.2007 | BREGENZ 1 Pfänder / Antenne |  | 106,5 | 100 | 2,68 | 77,3 | 71,5 |
| 04.07.2007 | BREGENZ 3 Gebhardsberg / Kronehit |  | 91,5 | 85 | 2,76 | 82,6 | 76,8 |
| 2007.06.29 | SALZBURG Gaisberg / Ö1 |  | 90,9 | 102,0 | 2,4 | 74,4 | 71,5 |
| 2007.06.29 | SALZBURG Gaisberg / Ö2-S |  | 94,8 | 102,0 | 2,6 | 71,5 | 68,6 |
| 2007.06.29 | SALZBURG Gaisberg / Ö2-OÖ |  | 101,2 | 98,0 | 2,5 | 79,7 | 71,5 |
| 2007.06.29 | SALZBURG Gaisberg / Ö3 |  | 99,0 | 101,0 | 2,7 | 72,1 | 69,1 |
| 2007.06.29 | SALZBURG Gaisberg / FM4 |  | 104,6 | 101,0 | 2,6 | 75,0 | 72,1 |
| 2007.06.29 | SALZBURG Gaisberg / Antenne |  | 101,8 | 86,0 | 2,4 | 73,8 | 70,3 |

| 2007.06.29 | SALZBURG Gaisberg / Kronehit |  | 94,0 | 80,0 | 2,7 | 83,8 | 77,3 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 2007.06.29 | SALZBURG Gaisberg / Welle 1 |  | 106,2 | 84,0 | 3,0 | 73,8 | 66,2 |
| 2007.07.16 | SALZBURG 4 Wartberg / Radio Arabella |  | 102,5 | 102,0 | 1,0 | 80,3 | 74,4 |
| 2007.07.13 | HOEGL / Untersberg live |  | 89,0 | 80,0 | 3,7 | 97,3 | 79,1 |
| 2007.07.13 | HOEGL / Deutschlandfunk |  | 100,3 | 85,0 | 2,3 | 98,4 | 76,8 |
| 2007.06.28 | S GILGEN Zwölferhorn / Antenne Salzburg |  | 106,700 | 82,0 | 1,60 | 75,00 | 66,2 |
| 2007.07.03 | LEND Luxkogel / Ö1 |  | 89,8 | 80,0 | 1,3 | 76,8 | 73,8 |
| 2007.07.03 | LEND Luxkogel / Ö2-S |  | 93,9 | 80,0 | 2,6 | 73,2 | 69,1 |
| 2007.07.03 | LEND Luxkogel / Ö3 |  | 99,7 | 80,0 | 2,6 | 70,3 | 68,0 |
| 2007.07.03 | LEND Luxkogel / FM4 |  | 97,7 | 80,0 | 2,2 | 72,1 | 69,1 |
| 2007.06.19 | GRAZ 1 Schoeckl / OE3 |  | 89,2 | 73,0 | 2,5 | 72,7 | 69,1 |
| 2007.06.19 | GRAZ 1 Schoeckl / OE1 |  | 91,2 | 76,0 | -1,6 | 68,6 | 55,1 |
| 2007.06.29 | GRAZ 1 Schoeckl / OE2-ST |  | 95,4 | 83,0 | 2,4 | 72,7 | 69,7 |
| 2007.07.26 | GRAZ 1 Schoeckl / ANTENNE |  | 99,1 | 70,0 | 2,4 | 72,1 | 68,6 |
| 2007.07.26 | GRAZ 1 Schoeckl / FM4 |  | 101,7 | 74,0 | 2,5 | 75,0 | 72,1 |
| 2007.07.16 | RECHNITZ Hirschenstein / OE2-ST |  | 100,1 | 74,0 | 2,8 | 80,3 | 73,8 |
| 2007.07.24 | RECHNITZ Hirschenstein / ANTENNE |  | 106,1 | 81,0 | 2,3 | 73,2 | 68,6 |
| 2007.06.27 | LINZ 1 Lichtenberg / Arabella |  | 96,7 | 96,0 | 3,2 | 77,3 | 72,1 |
| 2007.06.27 | LINZ 1 Lichtenberg / Ö3 |  | 88,8 | 96,0 | 2,6 | 75,0 | 69,7 |
| 2007.07.03 | SCHAERDING Schardenberg / Kronehit |  | 104,9 | 94,0 | 1,7 | 82,0 | 74,4 |
| 2007.06.26 | INNSBRUCK 1 Patscherkofel / OE3 |  | 88,5 | 73,0 | 2,7 | 97,9 |  |
| 2007.07.04 | INNSBRUCK 1 Patscherkofel / OE1 |  | 92,5 | 88,0 | 0,0 | 73,2 |  |

| 2007.07.03 | INNSBRUCK 1 Patscherkofel / OE2T |  | 96,4 | 85,0 | 2,5 | 74,4 |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 2007.07.04 | INNSBRUCK 1 Patscherkofel / FM 4 |  | 101,4 | 79,0 | 2,6 | 89,1 |  |
| 2007.07.04 | INNSBRUCK 1 Patscherkofel / Kronehit |  | 106,5 | 91,0 | 1,8 | 82,6 |  |
| 2007.07.04 | INNSBRUCK 2 Seegrube / OE1 |  | 87,6 | 77,0 | 1,5 | 75,0 |  |
| 2007.07.04 | INNSBRUCK 2 Seegrube / OE2T |  | 94,6 | 75,0 | 2,5 | 73,2 |  |
| 2007.06.26 | INNSBRUCK 2 Seegrube / OE3 |  | 99,5 | 73,0 | 2,8 | 77,3 |  |
| 2007.07.04 | INNSBRUCK 2 Seegrube / FM 4 |  | 102,5 | 74,0 | 2,7 | 76,2 |  |
| 03.08.2007 | FLATSCHSPITZE / Radio Maria |  | 104,8 | 77 | 6,68 | 77,3 | 69,7 |
| 03.08.2007 | FLATSCHSPITZE / Radio Dolomiti |  | 88,85 | 67 | 6,34 | 147,7 | 102,0 |
| 03.08.2007 | FLATSCHSPITZE / Die Antenne |  | 100,8 | 73 | 4,46 | 131,2 | 82,6 |
| 16.07.2007 | EHRWALD 1 Zugspitze / OE 1 |  | 91,6 | 71 | 1,6 | 75 | 72,1 |
| 16.07.2007 | EHRWALD 1 Zugspitze / OE2T |  | 95,3 | 78 | 2,62 | 72,1 | 69,1 |
| 16.07.2007 | EHRWALD 1 Zugspitze / Hitradio OE 3 |  | 97,1 | 79 | 2,62 | 72,7 | 69,1 |
| 16.07.2007 | EHRWALD 1 Zugspitze / FM4 |  | 100,7 | 78 | 2,53 | 75 | 72,1 |
| 14.07.2007 | S ANTON ARLB 1 / OE 2T |  | 95,1 | 77 | 2,5 | 76,2 |  |
| 14.07.2007 | S ANTON ARLB 1 / OE 1 |  | 92,1 | 80 | 1,77 | 75,6 |  |
| 14.07.2007 | S ANTON ARLB 1 / OE 3 |  | 88,5 | 77 | 2,45 | 72,1 |  |
| 24.07.2007 | HOPFGARTEN DEF 2 / Radio Osttirol |  | 100,0 | 94 | 0,95 | 150,0 | 62,1 |
| 24.07.2007 | KALS / Radio Osttirol |  | 105,7 | 79 | 2,22 | 110,7 | 64,5 |
| 25.07.2007 | KOETSCHACH / Radio Osttirol |  | 102,2 | 52 | 1,88 | 108,4 | 63,9 |
| 25.07.2007 | LIENZ 2 Hochstein / Antenne Tirol |  | 106,4 | 71 | -3,75 | 93,2 | 55,1 |
| 25.07.2007 | LIENZ 2 Hochstein / Kronehit |  | 107,1 | 72 | 1,36 | 82,0 | 70,9 |

| 25.07.2007 | LIENZ 2 Hochstein / Life |  | 104,4 | 75 | 1,82 | 115,4 | 72,7 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 25.07.2007 | LIENZ Rauchkofel / FM 4 |  | 101,0 | 83 | 2,55 | 77,3 | 72,7 |
| 25.07.2007 | LIENZ Rauchkofel / OE 1 |  | 89,3 | 84 | 1,18 | 75,6 | 73,2 |
| 25.07.2007 | LIENZ Rauchkofel / OE 2T |  | 95,9 | 83 | 2,68 | 73,8 | 70,9 |
| 25.07.2007 | LIENZ Rauchkofel / OE3 |  | 99,3 | 83 | 2,72 | 74,4 | 69,7 |
| 25.07.2007 | LIENZ Stronach / Radio Osttirol |  | 107,8 | 70 | 1,12 | 150,0 | 60,9 |
| 24.07.2007 | MATREI OSTTIR 2 / Radio Osttirol |  | 101,7 | 78 | 1,77 | 113,7 | 63,3 |
| 24.07.2007 | MATREI OSTTIROL / OE 3 |  | 98,6 | 67 | 2,84 | 77,9 | 72,7 |
| 24.07.2007 | SILLIAN Hollbruck / Radio Osttirol |  | 103,9 | 80 | 2,02 | 150,0 | 63,9 |
| 22.07.2007 | KUFSTEIN Kitzbueheler Horn / OE 2T |  | 95,4 | 82 | 2,34 | 70,3 | 66,8 |
| 22.07.2007 | KUFSTEIN Kitzbueheler Horn / OE 1 |  | 97,5 | 84 | 0,97 | 75,0 | 71,5 |
| 22.07.2007 | KUFSTEIN Kitzbueheler Horn / OE3 |  | 103,9 | 85 | 2,49 | 73,8 | 69,1 |
| 22.07.2007 | KUFSTEIN Kitzbueheler Horn / FM 4 |  | 99,9 | 85 | 2,45 | 74,4 | 70,9 |
| 22.07.2007 | KITZBUEHEL 3 Hahnenkamm / U 1 |  | 106,0 | 68 | -0,01 | 106,6 | 71,5 |
| 22.07.2007 | KITZBUEHEL2 Hahnenkamm/Kronehit |  | 102,9 | 71 | 0,05 | 79,1 | 57,4 |
| 22.07.2007 | KUFSTEIN Kitzb.Hahnenkamm / Life |  | 106,8 | 70 | 7,17 | 137,7 | 126,6 |
| 22.07.2007 | S JOHANN TIR Harschbichl / U 1 |  | 87,7 | 67 | 0,29 | 108,4 | 68,0 |
| 17.07.2007 | IMST 3 Arzl / Welle |  | 104,7 | 109 | 5,57 | 124,8 | 87,9 |
| 13.07.2007 | LANDECK 1 Krahberg / Life |  | 106 | 83 | 0,07 | 113,7 | 71,5 |
| 13.07.2007 | LANDECK 1 Krahberg / OE3 |  | 102,6 | 66 | 2,58 | 73,2 |  |
| 13.07.2007 | LANDECK 1 Krahberg / OE2T |  | 93,9 | 75 | 2,7 | 74,4 | 70,9 |
| 13.07.2007 | LANDECK 1 Krahberg / OE1 |  | 90,1 | 72 | 0,16 | 74,4 | 71,5 |
| 16.07.2007 | REUTTE 1 Hahnenkamm / OE1 |  | 87,8 | 78 | 1,64 | 76,2 | 71,5 |

| 16.07.2007 | REUTTE 1 Hahnenkamm / OE 2T |  | 94,7 | 78 | 2,66 | 72,7 | 69,7 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 16.07.2007 | REUTTE 1 Hahnenkamm / OE3 |  | 99,7 | 70 | 2,7 | 73,8 | 69,7 |
| 16.07.2007 | REUTTE 3 Hahnenkamm / Ausserferner Welle |  | 104,0 | 83 | 4,79 | 150,0 | 150,0 |
| 16.07.2007 | REUTTE 1 Hahnenkamm / LIFE Radio |  | 89,9 | 73 | -0,37 | 94,3 | 64,5 |
| 2007.07.04 | INZING Rangger Koepfel / Life - Radio |  | 103,4 | 89,0 | 2,4 | 127,7 |  |
| 2007.07.04 | INZING Rangger Koepfel / Oberländer - Welle |  | 104,3 | 73,0 | -1,2 | 72,7 |  |
| 2007.07.03 | KLAGENFURT 1 Dobratsch / FM4 |  | 102,9 | 79,0 | 2,37 | 74,4 | 70,3 |
| 2007.07.03 | KLAGENFURT 1 Dobratsch / OE3 |  | 90,4 | 84,0 | 2,37 | 70,3 | 67,4 |
|  |  | Germany |  |  |  |  |  |
| 27.07.2007 | WENDELSTEIN / Bayern 3 |  | 98,5 | 90 | 1,5 | 79,7 | 70,3 |
| 27.07.2007 | WENDELSTEIN / Bayern 2 |  | 89,5 | 80 | 0,5 | 78,5 | 63,9 |
| 27.07.2007 | WENDELSTEIN / Bayern 1 |  | 93,7 | 88 | 1,78 | 80,9 | 66,8 |
|  |  | Czech Republic |  |  |  |  |  |
| 2007.07.04 | C BUDEJOVICE / CR1 |  | 91,1 | 84,0 | 6,0 | 75,6 | 69,7 |
| 2007.07.04 | C BUDEJOVICE / F1 94,1 |  | 94,1 | 82,0 | 7,3 | 80,3 | 77,3 |
| 2007.07.04 | C BUDEJOVICE / IMPULS |  | 102,9 | 86,0 | 5,4 | 106,1 | 84,4 |
| 2007.07.04 | C BUDEJOVICE / Cro CB |  | 106,4 | 85,0 | 3,7 | 100,8 | 78,5 |
| 2007.07.04 | PRAHA / EVROPA2 |  | 105,5 | 81,0 | 7,6 | 75,6 | 70,9 |
|  |  | Slovenia |  |  |  |  |  |
| 2007.07.02 | POHORJE / SLO 1 |  | 88,5 | 88,0 | 1,7 | 77,9 | 63,3 |
| 2007.07.05 | POHORJE / MARIBOR |  | 93,1 | 76,0 | 2,0 | 84,4 | 75,0 |
| 2007.07.02 | POHORJE / VAL 202 |  | 96,9 | 88,0 | 3,1 | 89,1 | 71,5 |

| 2007.07.10 | MARIBOR 3 / NET FM |  | 100,2 | 62,0 | 6,9 | 109,6 | 87,3 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 2007.07.05 | MELJSKY HRIB / CITY |  | 100,6 | 72,0 | 6,8 | 85,5 | 74,4 |
| 2007.07.02 | POHORJE / RADIO SI |  | 102,8 | 92,0 | 5,7 | 80,9 | 76,2 |
| 2007.07.02 | POHORJE / ARS |  | 105,3 | 83,0 | -1,4 | 69,7 | 59,2 |
| 2007.07.17 | KAMANSCAK / Maxi |  | 90,0 | 72,0 | 7,5 | 124,2 | 87,9 |
| 2007.07.02 | MUSKA SOBOTA / MURS.VAL |  | 87,6 | 65,0 | 2,7 | 104,3 | 77,9 |
| 2007.07.23 | MUSKA SOBOTA / MURS.VAL |  | 94,6 | 66,0 | 2,2 | 89,1 | 79,1 |
| 2007.07.04 | PLESIVEC / ALPHA |  | 107,8 | 75,0 | 6,11 | 74,4 | 67,4 |
| 2007.07.04 | PLESIVEC / ARS |  | 101,4 | 85,0 | 1,65 | 79,1 | 71,5 |
| 2007.07.04 | PLESIVEC / KOROSKI |  | 97,2 | 76,0 | 5,74 | 82,0 | 76,2 |
| 2007.07.04 | PLESIVEC / SLO1 |  | 90,0 | 78,0 | 3,77 | 78,5 | 73,8 |
| 2007.07.04 | PLESIVEC / VAL202 |  | 92,4 | 81,0 | 2,58 | 82,6 | 75,0 |
|  |  | Croatia |  |  |  |  |  |
| 2007.06.26 | SLJEME / HRT-HR 1 |  | 92,1 | 69,0 | 3,5 | 96,7 | 73,8 |
| 2007.07.23 | SLJEME / HRT-HR 2 |  | 98,5 | 72,0 | 4,5 | 87,3 | 67,4 |
| 2007.06.26 | SLJEME / Radio101 |  | 101,0 | 66,0 | 5,5 | 82,6 | 76,2 |
| 2007.07.23 | IVANCICA / HRT-HR 2 |  | 106,4 | 74,0 | 4,8 | 93,2 | 75,0 |
| 2007.07.10 | IVANCICA / HRT-HR 1 |  | 102,4 | 64,0 | 2,0 | 69,1 | 60,4 |
| 2007.07.10 | IVANCICA / HRT-HR 3 |  | 96,1 | 62,0 | 2,9 | 86,7 | 68,0 |
| 2007.06.26 | SLJEME / HRT-HR 1 |  | 92,1 | 69,0 | 3,5 | 96,7 | 73,8 |
|  |  | Slovakia |  |  |  |  |  |
| 2007.07.02 | BRATISLAVA Kamzik / Expres |  | 107,6 | 68,0 | 7,4 | ±89,1 | 82,6 |
| 2007.07.02 | BRATISLAVA Kamzik / FUNRADIO |  | 94,3 | 84,0 | 6,8 | ±78,5 | 72,7 |
| 2007.07.02 | BRATISLAVA Kamzik / SRO 1 |  | 96,6 | 84,0 | 5,7 | ±80,9 | 74,4 |
| 2007.07.02 | BRATISLAVA Kamzik / VIVA |  | 101,8 | 85,0 | 3,2 | ±79,1 | 62,1 |
| 2007.07.02 | BRATISLAVA Kamzik / OKEY |  | 104,8 | 80,0 | 6,4 | ±84,4 | 78,5 |

|  |  | Hungary |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 2007.06.28 | SOPRON / Slager |  | 96,8 | 64,0 | 5,6 | ±92,0 | 72,7 |
| 2007.06.28 | SOPRON / Petofi |  | 99,5 | 66,0 | 5,6 | ±74,4 | 69,1 |
| 2007.06.28 | SOPRON / Bartok |  | 107,9 | 67,0 | 3,5 | ±73,8 | 69,1 |
| 2007.06.28 | SOPRON / Danubius |  | 102,0 | 71,0 | 3,3 | ±79,7 | 72,1 |
|  |  | Germany |  |  |  |  |  |
| 04.07.2007 | WITTHOH / SWR1 BW |  | 92,4 | 65 | 1,26 | 109,6 | 70,9 |
| 04.07.2007 | WITTHOH / SWR2 BW |  | 90,4 | 65 | -2,6 | 99 | 75 |
|  |  | Switzerland |  |  |  |  |  |
| 02.07.2007 | SAENTIS / DRS 1 |  | 101,50 | 57,00 | 1,45 | 76,20 | 60,4 |
| 02.07.2007 | SAENTIS / DRS 3 |  | 105,6 | 55,00 | 2,11 | 75,60 | 63,9 |
| 2007.07.02 | SAENTIS / RSR - 1ERE |  | 99,9 | 52,00 | 0,65 | 76,8 | 60,4 |
|  |  | Italy |  |  |  |  |  |
| 2007.07.06 | MT S LUSSARI / DEEJAY |  | 101,9 | 71,0 | 5,94 | 75,6 | 69,1 |
| 2007.07.06 | MT S LUSSARI / RADIO24 |  | 106,4 | 84,0 | 3,38 | 69,7 | 62,7 |
| 2007.07.13 | MT S LUSSARI / RTL 102,5 |  | 102,5 | 67,0 | 5,59 | 103,1 | 83,2 |
| 2007.07.13 | MONTE FORNO / RADIO MARIA |  | 99,1 | 84,0 | 5,76 | 114,3 | 104,3 |
| 2007.07.13 | MONTE FORNO / RTL 102,5 |  | 104,5 | 74,0 | 5,35 | 95,5 | 80,3 |

| Measurement performed by the authority: ICP-ANACOM |  |  |  | Number of page: | 1 of 2 |
| --- | --- | --- | --- | --- | --- |
| Country where the broadcasting stations are operated: Portugal |  |  |  |  |
| Remark: | *To ensure a sufficient AF signal-to-noise ratio, the wanted signal input level for the receiver should be at least 43 dBpW (60 dBV), |  |
|  | as recommended in Recommendation ITU-R SM.1268-1, 2.3§ |  |  |  |  |  |
|  | Date of measurement | Name of transmitter | Frequency | RF level * | Max. MPX Power | Max. FM deviation | Remarks |
|  |  |  | (MHz) | (dBV) | (dBr) | (kHz) |  |
|  | 2007.06.11 | KISS FM | 93,700 | 87 | 8,10 | 73,0 |  |
|  | 2007.06.11 | ROMÂNTICA FM | 107,200 | 86 | 3,96 | 79,1 |  |
|  | 2007.06.12 | ANTENA 2 | 88,900 | 70 | 4,05 | 66,0 |  |
|  | 2007.06.12 | TSF (Lisboa) | 89,500 | 83 | 5,09 | 84,4 |  |
|  | 2007.06.12 | RPL | 90,400 | 79 | 5,90 | 85,0 |  |
|  | 2007.06.12 | CIDADE FM | 91,600 | 81 | 6,04 | 77,0 |  |
|  | 2007.06.12 | MEGA FM | 92,400 | 75 | 7,69 | 82,6 |  |
|  | 2007.06.12 | RFM (Lisboa) | 93,200 | 87 | 6,37 | 86,1 |  |
|  | 2007.06.12 | ANTENA 2 (Lisboa) | 94,400 | 94 | 2,90 | 72,0 |  |
|  | 2007.06.12 | MIRAMAR | 95,000 | 82 | 5,57 | 81,0 |  |
|  | 2007.06.12 | ANTENA 1 (Lisboa) | 95,700 | 92 | 6,67 | 77,0 |  |
|  | 2007.06.12 | M80 | 96,600 | 83 | 5,73 | 77,5 |  |
|  | 2007.06.12 | RÁDIO COMERCIAL (Lisboa) | 97,400 | 93 | 5,24 | 75,0 |  |
|  | 2007.06.12 | ANTENA 3 (Lisboa) | 100,300 | 92 | 7,80 | 80,0 |  |
|  | 2007.06.12 | PAL FM | 102,200 | 70 | 6,04 | 75,0 |  |
|  | 2007.06.12 | OXIGENIO | 102,600 | 84 | 6,67 | 73,0 |  |
|  | 2007.06.12 | R CLUB P | 104,300 | 93 | 4,06 | 77,5 |  |
|  | 2007.06.13 | RFM | 89,900 | 78 | 6,76 | 79,7 |  |
|  | 2007.06.13 | RADAR | 97,800 | 87 | 7,60 | 77,0 |  |
|  | 2007.06.13 | MARGINAL | 98,100 | 88 | 6,12 | 78,0 |  |
|  | 2007.06.13 | ANTENA 1 | 99,400 | 72 | 3,74 | 73,0 |  |
|  | 2007.06.13 | CAPITAL | 100,800 | 90 | 5,26 | 85,0 |  |
|  | 2007.06.15 | MEGA FM | 88,000 | 89 | 6,24 | 64,5 |  |
|  | 2007.06.15 | RCSINTRA | 91,200 | 84 | 5,86 | 77,9 |  |
|  | 2007.06.15 | CSB RADIO | 105,400 | 69 | 2,37 | 77,0 |  |
|  | 2007.06.15 | NOSSA FM | 107,700 | 78 | 7,45 | 99,0 |  |
|  | 2007.06.19 | FONÓGRAFO | 90,100 | 78 | -1,38 | 53,5 |  |
|  | 2007.06.19 | ANTENA 2 (Elvas) | 93,200 | 72 | 2,73 | 68,0 |  |
|  | 2007.06.19 | ANTENA 3 (Elvas) | 101,600 | 76 | 6,62 | 72,0 |  |
|  | 2007.06.19 | RÁDIO PERNES | 101,700 | 85 | 6,45 | 90,5 |  |
|  | 2007.06.19 | ANTENA 1 (Elvas) | 103,800 | 77 | 6,12 | 76,0 |  |
|  | 2007.06.19 | RC ALMEIRIM | 104,000 | 76 | 5,61 | 77,9 |  |
|  | 2007.06.19 | RFM (Elvas) | 107,100 | 63 | 6,25 | 90,2 |  |
|  | 2007.06.20 | RÁDIO CIDADE TOMAR | 90,500 | 97 | 5,23 | 75,0 |  |
|  | 2007.06.20 | RÁDIO TÁGIDE | 96,700 | 91 | 4,62 | 91,0 |  |
|  | 2007.06.20 | RÁDIO CLUBE OURÉM | 103,700 | 78 | 3,43 | 76,0 |  |
|  | 2007.06.21 | RÁDIO CIDADE RIO MAIOR | 104,600 | 83 | 7,77 | 103,5 |  |
|  | 2007.06.30 | Rádio Clube | 90,000 | 78 | 4,71 | 76,5 |  |
|  | 2007.06.30 | Mega FM | 90,600 | 60 | 4,79 | 66,5 |  |
|  | 2007.06.30 | Rádio Comercial (Porto) | 97,700 | 76 | 4,96 | 79,0 |  |
|  | 2007.06.30 | TSF (Porto) | 105,300 | 83 | 3,51 | 74,0 |  |
|  | 2007.06.30 | Best FM | 105,800 | 74 | 6,75 | 79,5 |  |
|  | 2007.07.01 | RDP2 (Porto) | 92,500 | 85 | 4,44 | 72,5 |  |
|  | 2007.07.01 | RR CANAL1 (Porto) | 93,700 | 77 | 5,82 | 82,0 |  |
|  | 2007.07.01 | Rádio Festival | 94,800 | 82 | 7,39 | 85,5 |  |
|  | 2007.07.01 | Gaia FM | 95,500 | 77 | 3,91 | 82,5 |  |
|  | 2007.07.01 | RDP1 (Porto) | 96,700 | 87 | 6,32 | 83,0 |  |
|  | 2007.07.01 | Rádio Nova | 98,900 | 78 | 6,28 | 78,0 |  |
|  | 2007.07.01 | Nova Era | 101,300 | 67 | 6,51 | 75,0 |  |
|  | 2007.07.01 | Capital | 102,700 | 64 | 4,31 | 91,0 |  |
|  | 2007.07.02 | Rádio Clube Matosinhos | 91,000 | 72 | 3,26 | 83,0 |  |
|  | 2007.07.02 | RFM (Porto) | 104,100 | 75 | 5,83 | 79,5 |  |
|  | 2007.07.02 | Rádio Cidade | 107,200 | 71 | 5,67 | 76,5 |  |
|  | 2007.07.03 | M80 Rádio | 89,500 | 88 | 4,96 | 77,5 |  |
|  | 2007.07.03 | Lidador | 94,300 | 69 | 6,18 | 80,0 |  |
|  | 2007.07.03 | RDP3 (Porto) | 100,400 | 80 | 7,17 | 84,0 |  |
|  | 2007.07.03 | Romana FM | 100,800 | 68 | 4,05 | 79,0 |  |
|  | 2007.07.03 | Jornal FM | 103,600 | 61 | 6,11 | 79,5 |  |
|  | 2007.07.04 | Rádio Voz Santo Tirso | 98,400 | 61 | 5,11 | 76,0 |  |
|  | 2007.07.04 | Nova Era | 100,100 | 59 | 7,44 | 79,0 |  |
|  |  |  |  | Av. MPX power | 5,47 | dBr |  |

|  | Measurement performed by the authority: | CZECH Republic |
| --- | --- | --- |
|  | Country where the broadcasting stations are operated: | CZECH Republic |
| Date of measurement | Name of transmitter | Frequency [MHz] | RF level * [dBµV] | Max. MPX Power [dBr] ¹ | Max. FM deviation [kHz] ² | Remarks Cumulated MPX deviation 0,001% [kHz] |
| 15.5.2007 | Hodonin - Radio Palava - CZ | 88,9 | 79 | 5,92 | 70 |  |
| 15.5.2007 | Hodonin – CRo5 -CZ | 93,6 | 80 | 4,22 | 77 |  |
| 15.5.2007 | Hodonin – CRo3 –CZ | 100,4 | 89 | 3,12 | 80 |  |
| 15.5.2007 | Hodonin – CRo1 -CZ | 106,2 | 88 | 6,52 | 75 |  |
| 15.5.2007 | Hodonin – CRo2 –CZ | 107,8 | 87 | 1,92 | 75 |  |
| 15.5.2007 | Hodonin – Radio Dyje –CZ | 91,4 | 81 | 6,02 | 78 |  |
| 28.6.2007 | Uh. Hradiste – CRo5 –CZ | 99,1 | 88 | 7,66 | 76 |  |
| 28.6.2007 | Uh. Hradiste – Radio Kiss -CZ Publikum | 96,5 | 74 | 6,38 | 76 |  |
| 28.6.2007 | Breclav – Radio Dyje –CZ | 93,2 | 84 | 5,15 | 75 |  |
| 19.7.2007 | Uh. Brod –Radio Proglas –CZ | 105,7 | 78 | 2,37 | 70 |  |
| 19.7.2007 | Uh. Brod –CRo5 –CZ | 107,5 | 83 | 7,01 | 74 |  |
| 19.7.2007 | Uh. Brod – CRo1 –CZ | 93,0 | 81 | 2,84 | 75 |  |
| 19.7.2007 | Uh. Brod –Radio Zlin –CZ | 96,2 | 83 | 6,39 | 77 |  |
| 19.7.2007 | Uh. Brod –Radio Kiss Publikum –CZ | 98,9 | 80 | 6,38 | 75 |  |
| 24.7.2007 | Breclav – CR1 –CZ | 101,2 | 89 | 6,22 | 76 |  |
| 24.7.2007 | Breclav – Radio Blanik –CZ | 104,2 | 76 | 7,18 | 75 |  |
| 24.7.2007 | Breclav – Evropa 2 –CZ | 106,7 | 83 | 5,63 | 75 |  |
| 24.7.2007 | Breclav – Proglas –CZ | 107,2 | 66 | 3,81 | 79 |  |
| 24.7.2007 | Breclav – CR2 –CZ | 89,6 | 89 | 4,88 | 76 |  |
| 24.7.2007 | Breclav – Radio Kiss Hady –CZ | 90,9 | 81 | 7,5 | 79 |  |
| 24.7.2007 | Breclav – Radio Krokodyl –CZ | 96,2 | 80 | 3,43 | 75 |  |
| 24.7.2007 | Breclav – CRo5 –CZ | 97,3 | 88 | 4,73 | 77 |  |
| 24.7.2007 | Breclav – CRo3 –CZ | 99,2 | 89 | 4,31 | 80 |  |
| 1.8.2007 | Olomouc – Radio Hana –CZ | 92,3 | 88 | 6,52 | 75 |  |
| 1.8.2007 | Olomouc – Radio BBC –CZ | 105,6 | 75 | 3,83 | 71 |  |

|  | Measurement performed by the authority: | CZECH Republic |
| --- | --- | --- |
|  | Country where the broadcasting stations are operated: | Slovakia |
| Date of measurement | Name of transmitter | Frequency [MHz] | RF level * [dBµV] | Max. MPX Power [dBr] ¹ | Max. FM deviation [kHz] ² | Remarks Cummulated MPX deviation 0,001% [kHz] |
| 17.6.2007 | Banska Bystrica RadioR1 – SK | 90,1 | 67 | 4,85 | 77 |  |
| 17.6.2007 | Zilina - RadioR3 – SK | 97,2 | 79 | -2,25 | 70 |  |
| 17.6.2007 | Banska Bystrica Radio HEY – SK | 97,6 | 73 | 4,06 | 70 |  |
| 17.6.2007 | Zilina – RadioR2 – SK | 100,1 | 78 | 2,55 | 82 |  |
| 17.6.2007 | Banska Bystrica Radio OKEY – SK | 106,0 | 66 | 5,51 | 75 |  |

Measurement performed by the authority:  National Communications Authority of Hungary

Country where the broadcasting stations are operated:	Hungary

Average of max. MPX powers: 4.1 dBr (92 stations)

| Date of measurement | Name of transmitter | Frequency (MHz) | RF level * (dB(V) | Max. MPX Power (dBr) | Max. FM deviation (kHz) | Remarks Cumulated MPX deviation 0,001% [kHz] |
| --- | --- | --- | --- | --- | --- | --- |
| 2007.06.07 | Rádió 88 | 92.5 | 67.37 | +5.95 | -75.6/+77.3 | 77,3 |
| 2007.06.07 | Kossuth Rádió | 93.0 | 89.89 | +1.70 | -67.4/+69.1 | 69,1 |
| 2007.06.07 | Kossuth Rádió | 106.4 | 61.87 | +1.97 | -68.6/+69.7 | 69,7 |
| 2007.06.08 | Mária Rádió | 106.3 | 83.41 | +7.18 | -122.5/+78.5 | 78,5 |
| 2007.06.10 | Rádió 2000 | 90.4 | 75.91 | +6.55 | -83.2/+84.4 | 84,4 |
| 2007.06.10 | Rádió Aktív | 92.2 | 65.85 | +6.31 | -72.7/+73.8 | 73,8 |
| 2007.06.10 | Kossuth Rádió | 94.3 | 84.63 | +1.26 | -68.6/+66.2 | 66,2 |
| 2007.06.10 | MR Szolnok | 101.2 | 79.89 | -0.52 | -68.6/+68.0 | 68,0 |
| 2007.06.13 | Gong Rádió | 96.5 | 84.58 | +6.55 | -77.9/+79.1 | 79,1 |
| 2007.06.13 | Klub Rádió | 97.7 | 83.67 | +4.58 | -76.8/+77.3 | 77,3 |
| 2007.06.14 | Gong Rádió | 87.6 | 83.04 | -1.86 | -65.6/+71.5 | 71,5 |
| 2007.06.14 | Sirius Rádió | 91.1 | 82.36 | +4.33 | -69.1/+70.3 | 70,3 |
| 2007.06.15 | Sláger Rádió | 88.4 | 86.82 | +4.55 | -69.1/+70.3 | 70,3 |
| 2007.06.15 | Kunság Rádió | 91.7 | 86.76 | +5.76 | -76.8/+77.3 | 77,3 |
| 2007.06.15 | Petőfi Rádió | 95.1 | 85.43 | +5.08 | -68.6/+69.1 | 69,1 |
| 2007.06.15 | Bartók Rádió | 105.9 | 86.04 | +0.66 | -67.4/+68.0 | 68,0 |
| 2007.06.18 | Party FM | 92.9 | 70.47 | +5.48 | -76.8/+77.3 | 77,3 |
| 2007.06.18 | Kossuth Rádió | 102.7 | 61.83 | +1.53 | -68.0/+68.6 | 68,6 |
| 2007.06.19 | Rádió Majsa | 88.2 | 67.14 | +4.54 | -93.2/+94.3 | 94,3 |
| 2007.06.19 | Rádió 7 | 107.0 | 83.73 | +8.2 | -92,0/+93,2 | 150,0 |
| 2007.06.24 | Plusz Rádió | 100.2 | 70.15 | +7.67 | -91.4/+92.0 | 92,0 |
| 2007.06.25 | Sláger Rádió | 90.3 | 71.34 | +4.67 | -68.0/+68.6 | 68,6 |
| 2007.06.25 | Danubius Rádió | 94.9 | 68.94 | +2.06 | -65.0/+66.2 | 66,2 |
| 2007.06.25 | Kossuth Rádió | 101.9 | 71.26 | +0.12 | -67.4/+64.5 | 64,5 |
| 2007.06.25 | Petőfi Rádió | 104.6 | 71.60 | +5.26 | -75.1/+72.1 | 72,1 |
| 2007.06.25 | Bartók Rádió | 105.7 | 71.31 | -1.33 | -63.3/+62.7 | 62,7 |
| 2007.06.26 | Juventus Rádió | 88.6 | 73.29 | +5.88 | -77.9/+78.5 | 78,5 |
| 2007.06.26 | Rádió 1 | 90.2 | 70.16 | +5.55 | -72.7/+73.2 | 73,2 |
| 2007.06.26 | FM 90.8 | 90.8 | 74.83 | +6.59 | -76.2/+76.2 | 76,2 |
| 2007.06.26 | Rádió 7 | 97.6 | 74.41 | +5.79 | -101.4/+102.5 | 102,5 |
| 2007.06.26 | Rádió X | 105.4 | 60.13 | +7.28 | -96.7/+97.3 | 97,3 |
| 2007.06.27 | Plusz Rádió | 95.7 | 61.54 | +3.46 | -72.7/+70.9 | 70,9 |
| 2007.06.27 | Kossuth Rádió | 91.6 | 73.87 | +1.94 | -69.7/+70.9 | 70,9 |
| 2007.06.27 | Árkádia Rádió | 96.8 | 75.52 | +1.03 | -66.8/+63.3 | 63,3 |
| 2007.06.27 | Petőfi Rádió | 98.8 | 84.62 | +5.38 | -71.5/+72.1 | 72,1 |
| 2007.06.27 | Sláger Rádió | 100.4 | 90.55 | +4.92 | -69.1/+70.3 | 70,3 |
| 2007.06.27 | Rádió Szentes | 106.1 | 60.44 | +2.30 | -68.6/+69.7 | 69,7 |
| 2007.06.27 | Bartók Rádió | 107.3 | 89.46 | +2.43 | -69.7/+69.1 | 69,1 |
| 2007.06.28 | Rádió 1 | 101.8 | 63.18 | +8.01 | -77.3/+77.9 | 77,9 |
| 2007.06.29 | Junior Rádió | 101.3 | 91.17 | +6.36 | -76.2/+77.9 | 77,9 |
| 2007.06.30 | Mária Rádió | 91.7 | 62.43 | +7.68 | -76.8/+120.7 | 120,7 |
| 2007.06.30 | Kossuth Rádió | 105.4 | 68.80 | +1.15 | -68.0/+69.1 | 69,1 |
| 2007.07.01 | Alisca Rádió | 91.3 | 89.50 | +1.03 | -66.8/+67.4 | 67,4 |
| 2007.07.01 | Kossuth Rádió | 92.0 | 83.44 | +0.76 | -69.1/+70.3 | 70,3 |
| 2007.07.01 | Alisca Rádió | 92.8 | 77.54 | +2.64 | -68.6/+75.6 | 75,6 |
| 2007.07.01 | Fortuna Rádió | 94.0 | 82.64 | +1.23 | -73.8/+75.0 | 75,0 |
| 2007.07.01 | Alisca Rádió | 106.5 | 88.62 | +4.42 | -65.0/+70.3 | 70,3 |
| 2007.07.02 | Rádió 1 | 87.9 | 69.20 | +7.28 | -72.1/+74.4 | 74,4 |
| 2007.07.02 | Petőfi Rádió | 90.3 | 89.51 | +5.11 | -70.3/+70.9 | 70,9 |
| 2007.07.02 | Juventus Rádió | 92.6 | 65.14 | +6.13 | -74.4/+75.6 | 75,6 |
| 2007.07.02 | Kossuth Rádió | 93.6 | 64.80 | +2.00 | -68.6/+68.6 | 68,6 |
| 2007.07.02 | Sláger Rádió | 101.5 | 76.86 | +4.90 | -70.3/+71.5 | 71,5 |
| 2007.07.02 | Bartók Rádió | 106.9 | 83.16 | +1.43 | -69.7/+65.6 | 65,6 |
| 2007.07.03 | Alisca Rádió | 101.9 | 75.00 | +3.67 | -67.4/+65.6 | 65,6 |
| 2007.07.03 | N-Joy | 98.7 | 82.62 | +6.19 | -76.8/+79.1 | 79,1 |
| 2007.07.04 | N-Joy | 91.2 | 82.82 | +4.54 | -72.7/+73.2 | 53,2 |
| 2007.07.04 | Kossuth Rádió | 96.7 | 88.91 | -0.65 | -55.1/+58.0 | 58,0 |
| 2007.07.04 | Kapos Rádió | 99.9 | 75.80 | +4.45 | -72.1/+72.1 | 72,1 |
| 2007.07.04 | N-Joy Classic | 102.6 | 90.16 | +5.92 | -76.8/+77.9 | 77,9 |
| 2007.07.05 | Rádió 1 | 90.6 | 66.41 | +7.21 | -74.4/+75.6 | 75,6 |
| 2007.07.05 | Rádió Aktív | 94.6 | 60.23 | +4.41 | -73.8/+83.8 | 83,8 |
| 2007.07.05 | Sláger Rádió | 95.9 | 85.03 | +4.87 | -68.6/+69.7 | 69,7 |
| 2007.07.05 | Régió Rádió | 101.7 | 74.36 | +4.87 | -67.4/+70.9 | 70,9 |
| 2007.07.05 | Petőfi Rádió | 103.7 | 88.14 | +5.40 | -70.3/+70.9 | 70,9 |
| 2007.07.06 | Sláger Rádió | 90.2 | 84.85 | +4.41 | -66.2/+67.4 | 67,4 |
| 2007.07.06 | Petőfi Rádió | 94.3 | 71.24 | +5.06 | -70.3/+70.9 | 70,9 |
| 2007.07.06 | Kanizsa Rádió | 98.6 | 91.86 | +3.90 | -59.2/+60.9 | 60,9 |
| 2007.07.06 | Bartók Rádió | 104.7 | 82.12 | +1.12 | -67.4/+67.4 | 67,4 |
| 2007.07.06 | Kossuth Rádió | 106.7 | 75.21 | +1.87 | -68.6/+69.1 | 69,1 |
| 2007.07.07 | N-Joy | 98.9 | 98.57 | +5.89 | -77.3/+78.5 | 78,5 |
| 2007.07.07 | Mediterrán Rádió | 101.2 | 71.40 | +5.30 | -74.4/+76.2 | 76,2 |
| 2007.07.07 | Kossuth Rádió | 104.6 | 86.66 | +1.62 | -67.4/+69.1 | 69,1 |
| 2007.07.07 | Danubius Rádió | 105.5 | 87.25 | +2.12 | -65.6/+66.8 | 66,8 |
| 2007.07.07 | Bartók Rádió | 107.6 | 85.89 | +0.22 | -66.8/+66.2 | 66,2 |
| 2007.07.08 | Klub Rádió | 92.2 | 63.07 | +4.27 | -78.5/+77.9 | 77,9 |
| 2007.07.08 | Egerszeg Rádió | 92.9 | 81.58 | +5.06 | -71.5/+73.8 | 73,8 |
| 2007.07.08 | Helikon Rádió | 99.4 | 64.88 | +5.17 | -72.1/+70.9 | 70,9 |
| 2007.07.08 | 101.8 | 101.8 | 84.35 | +3.83 | -76.2/+77.9 | 77,9 |
| 2007.07.09 | Yo Rádió | 97.1 | 85.04 | +6.33 | -74.4/+76.2 | 76,2 |
| 2007.07.13 | Rádió 1 | 99.4 | 69.23 | +6.68 | -83.2/+82.6 | 82,6 |
| 2007.07.13 | Aqua Rádió | 102.7 | 76.57 | +5.80 | -75.0/+77.3 | 77,3 |
| 2007.07.14 | N-Joy | 94.8 | 87.21 | +5.67 | -76.8/+78.5 | 78,5 |
| 2007.07.14 | Kossuth Rádió | 103.8 | 64.29 | +0.66 | -68.0/+69.1 | 69,1 |
| 2007.07.27 | Klub 88.8 | 88.8 | 69.42 | +3.58 | -80.9/+79.7 | 79,7 |
| 2007.07.27 | Kossuth Rádió | 92.3 | 71.27 | +0.17 | -68.0/+69.1 | 69,1 |
| 2007.07.27 | Fehérvár Rádió | 94.5 | 76.46 | +7.54 | -76.2/+76.2 | 76,2 |
| 2007.07.27 | Vörösmarty | 99.2 | 76.09 | +3.53 | -77.9/+79.1 | 79,1 |
| 2007.07.27 | Rádió 1 | 101.8 | 63.18 | +8.01 | -77.3/+77.9 | 77,9 |
| 2007.07.28 | Klub 90.6 | 90.6 | 83.29 | +4.24 | -74.4/+74.4 | 74,4 |
| 2007.07.28 | Rádió 1 | 94.6 | 91.51 | +4.89 | -78.5/+79.7 | 79,7 |
| 2007.07.29 | Tenkes Rádió | 88.6 | 89.18 | +5,64 | -75.6/+76.2 | 76,2 |
| 2007.07.29 | Tenkes Rádió | 100.9 | 85.51 | +6.99 | -94.3/+96.1 |  |

Measurement performed by the authority:  National Communications Authority of Hungary

Country where the broadcasting stations are operated:	Austria

Average of max. MPX powers:	2.37 dBr (15 stations)

| Date of measurement | Name of transmitter | Frequency (MHz) | RF level * (dB(V) | Max. MPX Power (dBr) | Max. FM deviation (kHz) | Remarks Cumulated MPX deviation 0,001% [kHz] |
| --- | --- | --- | --- | --- | --- | --- |
| 2007-07-18 | Rechnitz (Ö-3) | 87,9 | 74 | 2,87 | 76,2 | 72,1 |
| 2007-07-18 | Graz 1 (Ö-3) | 89,2 | 74 | 2,53 | 75,0 | 69,7 |
| 2007-07-24 | Wien 1 (Ö2-W) | 89,9 | 62 | 2,01 | 73,2 | 66,2 |
| 2007-07-18 | Rechnitz (Ö-1) | 90,6 | 74 | 2,12 | 75,6 | 73,2 |
| 2007-07-18 | Graz 1 (Ö-1) | 91,2 | 75 | 1,69 | 74,4 | 70,3 |
| 2007-07-18 | Rechnitz (Ö-2B) | 93,5 | 74 | 2,73 | 73,8 | 71,5 |
| 2007-07-18 | Graz 1 (Ö-2ST) | 95,4 | 76 | 2,60 | 74,4 | 70,9 |
| 2007-07-18 | Rechnitz (Blue Danube) | 97,4 | 73 | 2,45 | 74,4 | 72,1 |
| 2007-07-24 | Wien 1 (Ö2-N) | 97,9 | 63 | 1,98 | 72,1 | 67,4 |
| 2007-07-18 | Graz 1 (STMK) | 99,1 | 77 | 2,49 | 73,8 | 69,7 |
| 2007-07-24 | Wien 1 (Ö-3) | 99,9 | 64 | 2,29 | 74,4 | 69,7 |
| 2007-07-18 | Graz 1 (Blue Danube) | 101,7 | 76 | 2,49 | 76,8 | 72,7 |

Measurement performed by the authority:  National Communications Authority of Hungary

Country where the broadcasting stations are operated:	Slovenia

Average of max. MPX powers:	0.37 dBr (3 stations)

| Date of measurement | Name of transmitter | Frequency (MHz) | RF level * (dB(V) | Max. MPX Power (dBr) | Max. FM deviation (kHz) | Remarks Cumulated MPX deviation 0,001% [kHz] |
| --- | --- | --- | --- | --- | --- | --- |
| 2007-07-19 | Pohorje (SLO 1) | 88,5 | 77 | 0,16 | 73,8 | 64,5 |
| 2007-07-18 | Pohorje (VAL 202) | 96,9 | 80 | 2,57 | 91,4 | 72,1 |
| 2007-07-18 | Pohorje (SLO 3) | 105,3 | 79 | -1,62 | 70,3 | 58,6 |

Measurement performed by the authority:  National Communications Authority of Hungary

Country where the broadcasting stations are operated:	Serbia

Average of max. MPX powers:	-0,23 dBr (4 stations)

| Date of measurement | Name of transmitter | Frequency (MHz) | RF level * (dB(V) | Max. MPX Power (dBr) | Max. FM deviation (kHz) | Remarks Cumulated MPX deviation 0,001% [kHz] |
| --- | --- | --- | --- | --- | --- | --- |
| 2007-07-25 | Subotica (NS3) | 88,9 | 73 | 0,21 | 150,0 | 93,8 |
| 2007-07-25 | Subotica (NS2) | 92,5 | 73 | -0,05 | 141,8 | 66,8 |
| 2007-07-25 | Subotica (NS1) | 99,3 | 68 | -0,77 | 141,8 | 62,7 |
| 2007-07-25 | Subotica (RTS BG2) | 101,1 | 75 | -0,29 | 128,9 | 82,6 |

Measurement performed by the authority:  National Communications Authority of Hungary	Number of page: 15

Country where the broadcasting stations are operated:	 Slovakia

Average of max. MPX powers: 4.3 dBr (30 stations)

| Date of measurement | Name of transmitter | Frequency (MHz) | RF level * (dB(V) | Max. MPX Power (dBr) | Max. FM deviation (kHz) | Remarks Cumulated MPX deviation 0,001% [kHz] |
| --- | --- | --- | --- | --- | --- | --- |
| 2007-07-26 | Kosice 1 (Fun Radio) | 87,7 | 84 | 5,39 | 65,0 | 62,7 |
| 2007-07-25 | Banska Bystrica (Rebeca /jemne/) | 87,7 | 62 | 4,86 | 75,0 | 70,3 |
| 2007-07-24 | Bratislava (Radio FM) | 89,3 | 71 | 3,88 | 87,3 | 74,4 |
| 2007-07-25 | Banska Bystrica (SRO1) | 90,1 | 71 | 4,63 | 83,8 | 75,6 |
| 2007-07-25 | Nitra (SRO1) | 91,2 | 62 | 4,36 | 82,0 | 74,4 |
| 2007-07-27 | Sturovo (Regina) | 91,7 | 74 | 2,76 | 80,9 | 75,0 |
| 2007-07-25 | Poprad (SRO1) | 92,2 | 71 | 4,07 | 75,0 | 69,1 |
| 2007-07-25 | Banska Stiavnica (Lumen) | 93,3 | 75 | 3,52 | 74,4 | 71,5 |
| 2007-07-25 | Poprad (RTI-SK) | 94,2 | 67 | 6,16 | 77,3 | 73,8 |
| 2007-07-24 | Bratislava (Fun Radio) | 94,3 | 79 | 6,74 | 75,0 | 72,1 |
| 2007-07-25 | Nitra (N-Radio) | 95,2 | 61 | 5,05 | 107,2 | 90,8 |
| 2007-07-27 | Sturovo (SRO1) | 96,3 | 81 | 4,60 | 78,5 | 73,2 |
| 2007-07-26 | Kosice 1 (SRO1) | 96,6 | 87 | 3,87 | 76,2 | 70,3 |
| 2007-07-24 | Bratislava (SRO1) | 96,6 | 81 | 6,05 | 77,9 | 73,2 |
| 2007-07-25 | Banska Bystrica (Hey) | 97,6 | 72 | 4,65 | 68,6 | 63,9 |
| 2007-07-26 | Kosice 1 (Jemne) | 98,6 | 85 | 2,39 | 70,9 | 66,2 |
| 2007-07-25 | Banska Stiavnica (SRO1) | 99,0 | 80 | 4,07 | 76,2 | 70,3 |
| 2007-07-24 | Bratislava (Regina) | 99,3 | 74 | 2,29 | 73,2 | 66,8 |
| 2007-07-27 | Sturovo (Expres) | 99,4 | 69 | 6,47 | 89,6 | 83,8 |
| 2007-07-26 | Kosice 1 (Regina) | 100,3 | 84 | 0,32 | 75,6 | 55,1 |
| 2007-07-25 | Banska Bystrica (Regina) | 101,5 | 68 | 1,39 | 48,0 | 45,7 |
| 2007-07-24 | Bratislava (Viva) | 101,8 | 81 | 3,27 | 85,0 | 68,6 |
| 2007-07-26 | Kosice 1 (Okey) | 102,0 | 67 | 4,99 | 93,8 | 88,5 |
| 2007-07-25 | Banska Stiavnica (Devin) | 102,6 | 80 | -2,11 | 135,9 | 92,0 |
| 2007-07-27 | Sturovo (Radio FM) | 103,7 | 80 | 3,59 | 76,8 | 70,3 |
| 2007-07-24 | Bratislava (Okey) | 104,8 | 79 | 6,41 | 82,6 | 76,8 |
| 2007-07-25 | Banska Stiavnica (Viva) | 105,1 | 79 | 3,35 | 92,0 | 71,5 |
| 2007-07-25 | Banska Bystrica (Okey) | 106,0 | 66 | 5,90 | 77,9 | 72,7 |
| 2007-07-26 | Kosice 1 (Expres) | 106,2 | 74 | 8,26 | 90,2 | 83,8 |
| 2007-07-24 | Bratislava (Expres) | 107,6 | 76 | 7,43 | 83,2 | 78,5 |
| 2007-07-24 | Bratislava (SRO1) | 96,6 | 81 | 6,05 | 77,9 | 73,2 |
| 2007-07-25 | Banska Bystrica (Hey) | 97,6 | 72 | 4,65 | 68,6 | 63,9 |
| 2007-07-26 | Kosice 1 (Jemne) | 98,6 | 85 | 2,39 | 70,9 | 66,2 |
| 2007-07-25 | Banska Stiavnica (SRO1) | 99,0 | 80 | 4,07 | 76,2 | 70,3 |
| 2007-07-24 | Bratislava (Regina) | 99,3 | 74 | 2,29 | 73,2 | 66,8 |
| 2007-07-27 | Sturovo (Expres) | 99,4 | 69 | 6,47 | 89,6 | 83,8 |
| 2007-07-26 | Kosice 1 (Regina) | 100,3 | 84 | 0,32 | 75,6 | 55,1 |
| 2007-07-25 | Banska Bystrica (Regina) | 101,5 | 68 | 1,39 | 48,0 | 45,7 |

Measurement performed by the authority:  National Communications Authority of Hungary

Country where the broadcasting stations are operated:	Croatia

Average of max. MPX powers:	3.46 dBr (17 stations)

| Date of measurement | Name of transmitter | Frequency (MHz) | RF level * (dB(V) | Max. MPX Power (dBr) | Max. FM deviation (kHz) | Remarks Cumulated MPX deviation 0,001% [kHz] |
| --- | --- | --- | --- | --- | --- | --- |
| 2007-07-24 | Belje (R. Baranja) | 88,0 | 62 | 7,40 | 113,1 | 101,4 |
| 2007-07-19 | Sljeme (HR 1) | 92,1 | 78 | 3,13 | 93,8 | 75,6 |
| 2007-07-24 | Belje (HR 1) | 93,3 | 89 | 4,20 | 93,8 | 75,0 |
| 2007-07-24 | Papuk (HR 1) | 94,9 | 68 | 3,35 | 94,9 | 74,4 |
| 2007-07-19 | Ivanscica (HR 3) | 96,1 | 82 | 1,06 | 87,3 | 72,1 |
| 2007-07-24 | - | 96,9 | 66 | -3,27 | 85,0 | 62,7 |
| 2007-07-24 | Psunj (HR 1) | 97,3 | 62 | 0,69 | 70,3 | 55,1 |
| 2007-07-24 | Papuk (HR 3) | 97,7 | 67 | 2,03 | 80,9 | 68,0 |
| 2007-07-24 | Belje (HR 2) | 98,1 | 87 | 5,21 | 111,9 | 87,3 |
| 2007-07-19 | Sljeme (HR 2) | 98,5 | 78 | 4,16 | 93,2 | 69,7 |
| 2007-07-19 | Sljeme (HR 3) | 101,0 | 77 | 4,85 | 83,2 | 77,3 |
| 2007-07-24 | Psunj (R. Osijek) | 102,0 | 59 | 4,75 | 150,0 | 131,2 |
| 2007-07-19 | Ivanscica (HR 1) | 102,4 | 83 | 0,13 | 64,5 | 55,7 |
| 2007-07-24 | Belje (R. Osijek) | 102,8 | 87 | 4,48 | 150,0 | 134,2 |
| 2007-07-24 | Osijek (Slavonski Radio) | 106,2 | 78 | 6,01 | 150,0 | 113,1 |
| 2007-07-24 | Papuk (HR 2) | 106,8 | 63 | 4,66 | 98,4 | 79,7 |
| 2007-07-18 | - (Otvoreni) | 107,5 | 78 | 6,07 | 140,6 | 96,7 |

Measurement performed by the authority:  National Communications Authority of Hungary

Country where the broadcasting stations are operated:	 Rumania

Average of max. MPX powers: 2.46 dBr (8stations)

| Date of measurement | Name of transmitter | Frequency (MHz) | RF level * (dB(V) | Max. MPX Power (dBr) | Max. FM deviation (kHz) | Remarks Cumulated MPX deviation 0,001% [kHz] |
| --- | --- | --- | --- | --- | --- | --- |
| 2007-07-31 | Rractual | 89,4 | 60 | 0,17 | 150,0 | 107,8 |
| 2007-07-26 | Cultural | 96,1 | 73 | 0,91 | 82,6 | 73,8 |
| 2007-07-31 | Cultural | 100,1 | 68 | -0,78 | 76,8 | 69,7 |
| 2007-07-31 | Rractual | 102,5 | 66 | 3,93 | 80,3 | 75,0 |
| 2007-07-25 | Rractual | 103,8 | 66 | 3,12 | 85,0 | 79,1 |
| 2007-07-26 | Rractual | 104,1 | 71 | 3,25 | 85,5 | 77,3 |
| 2007-07-25 | Cultural | 106,8 | 65 | -1,91 | 79,1 | 63,9 |
| 2007-07-25 | Infopro | 107,6 | 68 | 11,03 | 118,9 | 111,3 |
| 2007-07-31 | Rractual | 89,4 | 60 | 0,17 | 150,0 | 107,8 |
| 2007-07-26 | Cultural | 96,1 | 73 | 0,91 | 82,6 | 73,8 |

Measurement performed by the authority:  National Communications Authority of Hungary

Country where the broadcasting stations are operated:	 Ukraina

Average of max. MPX powers: 6.16 dBr (2 stations)

| Date of measurement | Name of transmitter | Frequency (MHz) | RF level * (dB(V) | Max. MPX Power (dBr) | Max. FM deviation (kHz) | Remarks Cumulated MPX deviation 0,001% [kHz] |
| --- | --- | --- | --- | --- | --- | --- |
| 2007-08-01 | Zakarpattya | 101,9 | 69 | 6,42 | 140,6 | 117,2 |
| 2007-08-01 | Tisza | 103,0 | 63 | 5,89 | 134,2 | 117,2 |