| Radiocommunication Study Groups |  |
| --- | --- |
| Source: Documents 5B/209 and 5B/317 | Document 5B/TEMP/184-E |
|  | 1 December 2009 |
|  | English only |
| Working Party 5B |
| Liaison Statement to ICAO, with copy to ITU-R WP 4C |
| Potential interference between the ICAO standard microwave landing system (MLS) operating above 5 030 MHz and planned radionavigation-satellite service (RNSS) in the band 5 000-5 030 MHz |

At its November meeting, Working Party 5B considered the different reference documents addressing the question of the modelling of MLS unwanted emissions.

The document attached to 5B/317 has interpreted the guidance given by ICAO in 5B/209 such that the MLS worst-case transmit spectrum can be modelled as :
“ spectrum attenuation in dBc decaying as ”  with f the frequency offset from the considered MLS on-tune frequency, Bw the reference bandwidth and fd the MLS DPSK modulation rate.

However, following guidance of 5B/209 Table 1, one can assess MLS spectrum attenuation at much lower values than shown in Fig. 3-6 of the Attachment to 5B/317, by more than 10 dB. Furthermore, information from the ICAO ACP website – document ACP-WGF20-WP 13 refers – suggests the possibility of using the formulation  to derive worst-case MLS spectrum attenuations in line with those obtained using this 5B/209 Table 1 guidance.

Working Party 5B kindly invites ICAO to advise Working Party 4C and Working Party 5B on what should be the appropriate formulation of the MLS unwanted emissions model to be used unambiguously in its future work.

Attachment: 5B/209, 5B/317

| Status: | For action |
| --- | --- |
| Contact: | Loftur Jonasson, ICAO, (ljonasson@icao.int) |
| Deadline: | WP 4C March 2010 meeting |

______________