|  | International Civil Aviation Organization WORKING PAPER | ACP WG-F/25 WP09 07/06/05 |
| --- | --- | --- |

AERONAUTICAL COMMUNICATIONS PANEL (ACP)

25th MEETING OF WORKING GROUP F

Dakar, Senegal, 6 – 14 October 2011

| Agenda Item 2: | Review, update and development of the ICAO Frequency Spectrum Handbook |
| --- | --- |

Handbook on radio frequency spectrum requirements for civil aviation; Part II Frequency assignment planning criteria for aeronautical communication and navigation systems

(Presented by the Secretary)

SUMMARY

This paper presents the results of the coordination of frequency assignment planning criteria for air/ground VHF communication systems in the band 117.975 – 137 MHz

ACTION

Action by the meeting is in paragraph xxx

INTRODUCTION

At ACP WG F 24 (17 – 25 March 2011, Paris, France) the first version of Part II of the ICAO Handbook on radio frequency spectrum requirements for civil aviation was presented and referred for further review and completion by the email correspondence group.

discussion

Part II of the Handbook was reviewed by the members of the email correspondence group. In principle, all participants agreed with the principles for establishing separation distances between co-frequency and adjacent frequency assignments based on either a 20 dB D/U protection ratio (14 dB in Regions where agreed) or the radio line-of-sight separation whichever is smaller.

The results of the coordination are in Appendix A .

ACTION BY THE MEETING

ACP WG F is invited to agree that the material presented in Appendix A should be used to be incorporated in an appropriate format in Part II of the ICAO Handbook on radio frequency spectrum requirements for civil aviation

DRAFT  (4 October 2011)

# HANDBOOK ON RADIO FREQUENCY SPECTRUM REQUIREMENTS FOR CIVIL AVIATION

PART II _ Frequency assignment planning criteria for aeronautical radio communication and navigation systems

## Chapter 1 	General methodology for compatibility analysis of aeronautical radio systems

1.1		Introduction

1.1.1		This chapter describes a general methodology, which can be used in interference analysis for different radio systems. The general methodology is mainly based on ITU-R Recommendation SM.337-4 which is logically combining currently available models and parameters of both desired and undesired systems, e.g. signal power and spectral distribution, receiver selectivity, antenna patterns, propagation attenuation etc. Recommendation ITU-R SM.337-6 provides the procedures for calculating distance and frequency separation for an acceptable (agreed) interference level.

1.1.2		The following primary factors, which quantify the interactive effects between interfering transmitters and victim receivers for various combinations of frequency or distance separation, are:

### -	the frequency dependent rejection (FDR) which is a measure of the rejection produced by a receiver selectivity curve on an unwanted transmitter emission, and

### -	frequency / distance (FD) which is a measure of the minimum distance separation that is required between a victim receiver and an interfering transmitter as a function of difference between their tuned frequencies.

1.1.3		The frequency/distance rules are an important part of the frequency management process in most radio services. In channelized services, these rules take the following form:

### co-channel or co-frequency transmitters must be separated by at least d0 (NM),

### first adjacent frequency transmitters (separated by one channel or the applicable frequency separation (e.g. 25 kHz) ) must be separated by at least d1 (NM),

### second adjacent frequency transmitters (separated by two channels or two times the applicable frequency separation (e.g. 2 times 25 kHz) ) must be at least d2 (NM) away and so on.

1.1.4		For the purpose of frequency assignment planning appropriate frequency / distance rules should be applied when similar or dissimilar systems occupy the same (or adjacent) frequency band.

### FD and FDR can provide solutions to co- and adjacent frequency sharing and adjacent band interference problems by providing estimates of minimum required frequency and geographic separation between interfering transmitters and victim receivers which are required for an adequate receiver performance.

### Note: Throughout this document, capital letters are used to denote logarithmic values (dB) of the corresponding quantities designated with lower-case type, e.g. PD = 10 log pD. PD is the input power to the transmitting antenna (dB) relative to 1 W when pD is the input power (W).

1.2		Methodology

The electromagnetic compatibility of radio equipment should be calculated by the following method:

- Step 1:		determine the desired signal level at the victim receiver front end;

- Step 2:		determine the resulting level of interference at the victim receiver’s front end;

- Step 3:		determine the interactive effects among wanted signals, interference and receiver 		characteristics for various frequency or distance separations;

- Step 4:		determine the appropriate ITU-R propagation model to be used; and

- Step 5:		determine, from these data, a relationship between the frequency separation and

distance separation that the interference is considered tolerable.

1.3		Procedure

The compatibility analysis between an undesired transmitter and a victim receiver can be performed as follows (see Figure 1-1):

- Step 1:	a. 	Generic method:

- Determine the desired signal level PD (dBW) at the desired (victim) receiver front end.

|  |  | (1) |
| --- | --- | --- |

where:

- PD :	desired signal level PD (dBW) at the victim receiver front end

- PTx_D :	output power of the desired transmitter (dBW)

- GTx_D(():	gain of the desired transmitting antenna in direction of victim receiver with respect to an isotropic antenna (dBi)

- LTX_D_FL :	feeder link losses between output of the desired transmitter and the input of the desired transmitting antenna (dB)

- GRx((D) :	gain of the receiving antenna in direction of desired transmitter with respect to an isotropic antenna (dBi)

- LRX_FL :	feeder link losses between output of the receiving antenna and the input receiver (dB)

- LPOL_Rx_D :	loss due to polarization mismatch of receiving antenna with respect to desired transmitted signal (dB)

- Lb (dD ) :	basic transmission loss for a separation distance dD between desired transmitter and receiver (dB) (see Recommendation ITU-R P.341)

- ( :	angle between boresight of desired transmitting antenna in the direction of the desired receiving antenna

- (D 	angle between boresight of the desired receiving antenna in the direction of the desired transmitting antenna

This formula calculates the level of the desired signal at the (desired) receiver input based on the characteristics of the (desired) transmitter.

Figure 1 – 1 Elements of desired and undesired signal

b.	Method when the minimum signal strength of the desired signal has been specified:

As an alternative approach the desired signal power level PD (dBW) at the victim receiver front end can be determined based on the minimum required field strength at the receiver antenna (signal in space) within the service volume. In most cases, Annex 10 contains SARPs for radiocommunication and radionavigation systems where the minimum fieldstrength at the antenna (signal in space) is determined in the format of e = xx µV/m or as a power flux density of S = yy dBW/m2. The field strength in µV/m can be converted into dB(W/m2) as follows:

xx (µV/m) =     or  S = E – 145.8  where S = dB(W/m2) and E = dB (µV/m).

The power of the desired signal at the input of the receiver can be calculated as follows (see also Figure 1-2):

Figure 1 – 2 Calculation of PD at receiver input

|  |  | (1a) |
| --- | --- | --- |

where:

- PD :	desired signal level PD (dBW) at the victim receiver front end

- E :	minimum required electric field strength at the edge of the service area (dB((V/m))

- f:	frequency (MHz)

- GRx((D) :	gain of the receiving antenna in direction of desired transmitter with respect to an isotropic antenna (dBi)

- LRX_FL :	feeder link losses between output of the receiving antenna and the receiver input (dB)

- LPOL_Rx_D :	loss due to polarization mismatch of receiving antenna with respect to desired transmitted signal (dB)

- (D 	angle between boresight of receiving antenna and desired transmitting antenna

Note: 	When assuming the minimum field strength throughout the service volume than this approach is slightly more conservative since it does not take into account actual field strength values.

In aeronautical frequency assignment planning, typical (worst case) values are:

= 0 dB

= -3 dB

= 0 dB

And turns formula (1a) into

- Step 2:	Calculate the resulting level of interference at the victim receiver’s front end using the formula:

|  |  | (2) |
| --- | --- | --- |

where:

- PU :	undesired signal level PU (dBW) at the victim receiver front end

- PTx_U :	output power of the undesired transmitter (dBW)

- LTX_U_FL :	feeder link losses between output of the undesired transmitter and the input of the undesired transmitting antenna (dB)

- GTx_U(():	gain of the undesired transmitting antenna in direction of victim receiver with respect to an isotropic antenna (dBi)

- GRx((U) :	gain of the receiving antenna in direction of undesired transmitter with respect to an isotropic antenna (dBi)

- LRX_FL :	feeder link losses between output of the receiving antenna and the input of the receiver (dB)

- LPOL_Rx_U :	loss due to polarization mismatch of receiving antenna with respect to undesired transmitted signal (dB)

- Lb (dU ) :	basic transmission loss for a separation distance dU between the undesired transmitter and the receiver (dB) (see Recommendation ITU-R P.341)

- FDR (Δf ) :	frequency dependent rejection for a frequency separation Δf as expressed by equation (3)

- ψ :	angle between boresight of undesired transmitting antenna in the direction of the receiving antenna

- (U 	angle between boresight of receiving antenna in the direction of the undesired transmitting antenna

FDR is the rejection provided by a receiver to a transmitted signal as a result of the limited bandwidth of the receiver with respect to the transmitted signal and the detuning between the receiver and the transmitter.

|  | dB | (3) |
| --- | --- | --- |

where:

- p( f ) :		power spectral density of the interfering signal (W/Hz); and

- h( f ) :		normalized frequency response of the receiver.

|  |  | (4) |
| --- | --- | --- |

where:

- fRx :			receiver tuned frequency; and

- fTx_U :		interferer tuned frequency.

The FDR can be divided into two terms, the on-tune rejection (OTR) and the off-frequency rejection (OFR). The OTR is the rejection provided by a receiver selectivity characteristic to a co-tuned transmitter as a result of a transmitted signal exceeding the receiver bandwidth. The OFR is an additional rejection that results from off-tuning between interferer and receiver.

The FDR can also be described in the format of the receiver out-of-band immunity performance.

Note: FDR, OTR and OFR are considered as losses and defined below in a manner to ensure positive values.

|  |  | (5) |
| --- | --- | --- |

And in logarithmic values:

|  | dB | (6) |
| --- | --- | --- |

where:

|  | dB | (7) |
| --- | --- | --- |
|  | dB | (8) |

The on-tune rejection also called the bandwidth correction factor can often be approximated by:

|  | BR ≤ BT | (9) |
| --- | --- | --- |

where:

- BR :	interfered receiver 3 dB bandwidth (Hz)

- BT :	interferer transmitter 3 dB bandwidth (Hz)

- K =	10 for non-coherent signals

- =K	20 for pulse signals.

Note: OTR = 0        if BR  (  BT

- Step 3:	The interference will be considered tolerable if the following inequality is satisfied:

|  |  | (10) |
| --- | --- | --- |

where:

- PD :	desired signal level PD (dBW) at the victim receiver front end

- PU :	undesired signal level PU (dBW) at the victim receiver front end

- (	protection ratio (dB)

- ASF	aviation safety factor (dB) (see Part I of this Handbook (9.2.22). General material is in Recommendation ITU-R SM.1535 on “The protection of safety services from unwanted emissions”

In some cases it is required to calculate the interference-to-noise ratio (I/N) at the IF output or demodulation input of the victim receiver. The interference will be considered tolerable if the following inequality is satisfied:

|  |  | (11) |
| --- | --- | --- |

where:

- I/N :	calculated interference-to-noise ration at the victim receiver input referred to the IF bandwidth (dB)

- (I/N)req :	required interference-to-noise ration at the victim receiver input referred to the IF bandwidth (dB)

- ASF	aviation safety factor (dB)

The noise at the receiver input referred to the IF bandwidth is given by:

|  |  | (12) |
| --- | --- | --- |

where:

- N:	receiver noise power (dBm)

- k:	Boltzmann’s constant

- T0	absolute temperature (K)

- BIF	receiver’s intermediate frequency bandwidth (Hz)

- NF	receiver noise figure (dB)

The I/N ratio is then given by:

|  |  | (13) |
| --- | --- | --- |

Step 4: 		Determine the appropriate ITU-R propagation model to be used

See paragraph 1.3 for propagation models.

Step 5: 		Determine a relationship between the frequency separation and distance separation that the interference is considered tolerable

- Substitute PD and PU of steps 1 and 2 above into equation (10) to derive or numerically compute a relationship between the frequency separation f and the distance separation dU such that the interference is considered tolerable.

1.3		Propagation Model

1.3.1		Free – Space Propagation Model

- The propagation loss that would occur if the antennas were replaced by isotropic antennas located in a perfectly dielectric, homogeneous, isotropic and unlimited environment, the distance between the antennas being retained (see Recommendation ITU-R P.525).

|  |  | (14) |
| --- | --- | --- |

- where:

- Lbf :	free-space basic transmission loss (dB)

- d :	distance

- ( :	wavelength

- where d and ( are expressed in the same unit.

- Equation (14) can also be written using the frequency instead of the wavelength.

|  |  | (15) |
| --- | --- | --- |

where:

- f :	frequency (MHz)

- d :	distance (km).

or

|  |  | (16) |
| --- | --- | --- |

where:

- f :	frequency (MHz)

- d :	distance (NM)

1.3.2		Propagation of radio waves in the atmosphere

The propagation of radio waves, typical VHF and UHF frequencies, is subject to a number of conditions, compare to the free space propagation. These conditions include:

- Refraction – refraction of radio waves in the atmosphere along the Earth’s surface bend slightly towards the Earth. The effect is that radio waves can propagate beyond the horizon with no other (significant) loss than the free space loss. This phenomenon is corrected in radio propagation by using a 4/3 Earth radius. The radio horizon (radio path until it reaches the radio horizon) is calculated using a 4/3 Earth.

- Ducting – Unusual weather conditions (or other phenomena such as sand storms) can bend the radio waves more than normal and VHF or UHF radio frequencies can be received without significant attenuation over longer distances. In aeronautical frequency assignment planning this phenomenon is not normally taken into account.

The standard propagation model calculates the propagation loss along the radio path as follows:

Figure 1 - 3

Radio signals from transmitter Tx in Figure 3 propagate until the radio horizon over the distance dRH under free space propagation conditions. Beyond the radio horizon the radio signals are attenuated with a constant factor a, which is depending on the actual frequency as follows

- in the band 108 – 137 MHz a is 0.5 dB/NM

- in the band 960 – 1215 MHz a is 1.6 dB/NM

- in the band 5030 – 5091 MHz a is 2.7 dB/NM

Note: The constant attenuation factor a was derived from ITU-R Recommendation P.528 for 125 MHz, 1200 MHz and 5100 MHz for 50 % of the time. These curves are reproduced in Appendix A and are based on the IF 77 electromagnetic wave propagation model. The IF-77 model was developed by the Institute for Telecommunication Sciences and the FAA (US). A Windows version of this model is contained in the ICAO frequency assignment planning program Search Frequency and can be used for assessing more precise signal parameters. Normally, for radio paths up to the radio horizon, aeronautical frequency assignment planning is based on free space propagation. Applying the IF-77 model may result in a more accurate prediction of the actual radio wave propagation characteristics.

The distance to the radio horizon can be calculated with the formula:

dRH = 1.23√hTx where			(17)

dRH is the distance of the station to the radio horizon (NM)

hTx is the height of the station above the Earth’s surface

In Figure 1 – 3 the factor (d – dRH) is the distance of the receiver beyond the radio horizon from the transmitter Tx.

If d ≤ dRH the basic transmission (or propagation) loss between the transmitter Tx and the receiver Rx is

37.8 + 20.log d + 20.log f   (re. (16))

In this case, the receiver is within direct line of (radio) sight of the transmitter.

If d > dRH, the basic transmission loss between the transmitter Tx and the receiver Rx is

37.8 + 20.logdRH + 20 log f + (d-dRH).a    (re. (17)

In this case, the receiver is beyond the radio horizon of the transmitter. The distance dRH is calculated with formula (17). (d is in NM)

1.3.3	Aeronautical Standard Propagation Model

Aeronautical standard propagation model (ASPM) is derived from the ITU-R Recommendation P.528. For distances up to the radio horizon, free space propagation is assumed. Beyond the radio horizon, a constant attenuation factor a, which depends on the frequency band under consideration, is used.

The distance to the radio horizon can be calculated using the following formula:

|  |  | (18) |
| --- | --- | --- |

where:

- dRH :	distance to the radio horizon

- k :	effective Earth radius factor

- RE	Earth radius

- hTX	height of transmitting antenna above Earth’s surface

- hRX	height of receiving antenna above Earth’s surface

If heights hTX and hRX are expressed in feet (ft) and the distance d in Nautical Miles (NM), the Earth radius RE = 6360 km and if the atmospheric conditions are assumed to be normal (effective Earth radius factor k = 4/3) the following practical formula can be used:

|  |  | (19) |
| --- | --- | --- |

where:

- dRH :	distance to the radio horizon (NM)

- hTX	height of transmitting antenna above Earth’s surface (ft)

- hRX	height of receiving antenna above Earth’s surface (ft)

Figure 1 – 4

The situation as depicted in Figure 1 – 4 is typical applied in frequency assignment planning for air-ground communication systems (e.g. operating in the VHF band 112 – 137 MHz. In this situation, the minimum separation distance is between two aircraft each operating within their respective designated operational coverage (DOC) (see also Chapter 2).

1.3.4		Separation distance ratio

## In particular for air-ground voice communication systems, the minimum separation distance can be expressed in terms of a distance ratio. This is the ratio of the distance from the (desired ground based) transmitter to the desired (victim) aircraft receiver to the distance of the nearest interfering transmitter (another aircraft).

## Formula (1) calculates the desired signal level at the receiver input as follows:

## and formula (2) calculates the undesired (interfering) signal level at the receiver input:

## D/U ratio is 20 dB

## The D/U ratio for voice communication systems PD – PU = 20 dB ((re (10) and as specified in Annex 10).

## Assuming that    PTx_D = PTx-U; LTx_D_FL = LTx_U_FL; GTx_D(Ψ) = GTx_U(Ψ); LPol_Rx_U = 0 and FDR (∆f) = 0

## (the desired and undesired transmitter have the same power output; the same cable losses and the same antenna gain, they have the same antenna gain in the direction of the desired (victim) receiver, have the same polarization and operate on the same frequency)  PD – PU can be re-written using the formulas (1) and (2) as:

PD – PU =(- Lb(dD)) – (-Lb(dU)) = 20 dB.

Lb(dD) is the distance from the (desired) aircraft to the (desired) ground transmitter and Lb(dU) is the distance from the (desired) aircraft to the (undesired or interfering) aircraft.

Under free space propagation conditions, using formula 16 gives:

Lb(dU) – Lb(dD) =   = 20

or

-  = 20     >> = 20   >>= 1   >>= 10

D/U ratio is 14 dB

## If the D/U ratio for voice communication systems PD – PU = 14 dB (as specified in Annex 10 and used in congested areas) the separation distance ratio can be calculated as follows:

PD – PU = =(- Lb(dD)) – (-Lb(dU)) = 14 dB.

Lb(dU) – Lb(dD) =  -() =14

or

-  = 14     >> = 14   >>= 0.7   >>= 5

In many cases, applying the separation distance 1 : 10 leads to separation distances which are (far) beyond the radio horizon.

1.3.4.1		The effect of the radio horizon

The effect of the radio horizon is demonstrated in the following example. (Re Figure 1 – 5)

Figure 1 – 5 Separation distances (aircraft are not within line of sight)

In order to protect (aircraft) station a from interference from (aircraft) station b (with the same characteristics as in 1.3.4.1), Lb(dU) needs to be 142.6 dB

When aircraft station a is at an altitude of FL 250 (25000 ft) and aircraft b is at an altitude of FL 450 (45000 ft) the minimum separation between the two aircraft can be calculated as follows:

For station a the distance to the radio horizon (RLOSa) is 194 NM

For station b the distance to the radio horizon (RLOSb) is 261 NM

Lb(dU) 	=  37.8 + 20.log(f) + 20.log(RLOSa + RLOSb) + 0.5.drh  (dB)

= 79.7 + 455 +0.5 drh = 142.6           drh = 19.5 NM

The total minimum distance required between the two aircraft stations a and b is 474.5 NM.

In aeronautical frequency assignment planning, the distance drh is normally not taken into consideration; protection is sufficient when the two aircraft are separated by the sum of their distances to the radio horizon. The probability that two aircraft at the same time are at the maximum altitude and the maximum range of the closest point of the designated operational coverage can be ignored. Although 20 dB may be used in frequency assignment planning in Regions where frequency congestion is not severe or is not anticipated to become severe, Annex 10 stipulates that a desired to undesired protection ratio of 14 dB is sufficient to protect air/ground communication systems from harmful interference.(Re. Annex 10, Volume 5, paragraph 4.1.5.1)

The minimum separation distance between two ground stations “A” and “B”, which have a designated operational range of RA and RB respectively becomes:

RA + RLOSa +RLOSb + RB 			(20)

This separation distance protects two aircraft, operating on the same frequency and which are at the same time at the closest point and the maximum altitude of their respective designated operational coverage areas. These criteria are implemented in the ICAO frequency assignment planning program “Search Frequency” and are in conformity with the provisions in Annex 10, Volume 5.

When applying the 20 dB D/U protection ratio, the method for calculating the minimum separation distance described in this paragraph results (in almost all cases) in a minimum separation distance which is less than the separation distance calculated with the 1 :10 distance ratio; therefore using the 1 : 10 separation distance ratio method is not recommended or practical.

1.3.4.2		In (congested) areas cases where the 14 dB D/U ratio is applied, the separation distance ratio 5 as shown in paragraph 1.3.4 can be used.

In some cases (depending on the size of the designated operational coverage), applying a 1 : 5 distance ratio may result in smaller minimum separation distances compared to using the line-of-sight criterion.

Using formula (20) (line-of-sight criterion) calculates a minimum separation distance between the closest point at the edge of the designated operational coverage for each service of:

Dsep = RLOSa + RLOSb = 1.23√Ha +1.23√Hb

(Ha and Hb are the maximum altitude of the different designated operational coverage areas).

Using the 1 : 5 distance ratio will give a minimum separation distance between the closest point at the edge of the designated operational coverage for each service of

Dsep = 5RA or 5RB, whichever of these two is the largest distance (RA and RB are the ranges of the different designated operational coverage areas).

Note 1: the line-of-sight criterion should be applied where this provides a smaller minimum separation distance compared to the 1 : 5 separation distance ratio method.

The 1 : 5 separation distance criterion assumes that both the (desired) ground transmitter and the (undesired) aircraft transmitter have the same e.i.r.p. Typical value for aircraft e.i.r.p. is 43 dBm or 12.5 W (with a 25 W transmitter, 0 dB antenna gain and 3 dB cable losses). When the ground station e.i.r.p. is less than 12.5 W, the 14 dB protection ratio is not provided. In case the interfering ground station is within line-of-sight of the (desired) aircraft station and has an e.i.r.p greater than 12.5 W, the 14 dB protection ratio is not provided. Therefore, the 1 : 5 distance ratio should be used with caution.

Example calculations:

- a.	Application of the line-of-sight criterion gives a minimum separation distance between two designated operational coverage areas for a TWR service (25 NM / 4000ft) of 156 NM (the radio horizon for 4000 ft is 78 NM).

b.	Application of the 1 : 5 distance ratio gives a minimum separation between the two designated operational coverage areas of a TWR service of 5*25 NM or 125 NM.

In this case, the 1 : 5 separation distance criterion could be applied.

- a. 	For two APP/U services (250 NM/45000 ft), using the line of sight criterion, the minimum separation distance between the designated operational coverage areas is 520 NM (the radio horizon for 45000 ft is 260 NM)

b.	 Application of the 1:5 distance ratio would give a minimum separation distance 0f 5*250 NM or 1250 NM.

In this case, the line-of-sight criterion should be applied.

Application of the 5:1 distance ratio gives only marginal relief in frequency assignment planning.

Note: 	The ICAO frequency assignment planning program SEARCH FREQUENCY has implemented the frequency assignment planning criteria based on the line-of-sight (radio horizon) criterion (D/U ratio is 20dB.)

The program SEARCH FREQUENCY also includes the regional frequency assignment  planning criteria as these are currently used in the AFI, APAC, CAR, MID and SAM Regions. Until such time that the Regional frequency assignment planning criteria have been updated and in line with the planning criteria are per Annex 10, the current regional frequency assignment planning criteria should be used.

Implementation of the 14 dB D/U ratio with the 1 : 5 distance ratio  is applied in the EUR Region.

## Chapter 2

## Aeronautical VHF radio air-ground radio communication systems operating in the band 117.975 – 137 MHz

## 2.1		Introduction

2.1.1		The frequency band 108 – 137 MHz is allocated by the International Telecommunication Union (ITU) to the Aeronautical Mobile (Route) Service (AM(R)S) and used for air-ground voice as well as air-ground and air-air data link communications. The ITU has published details concerning the allocation of radio frequency spectrum for all radio services in its Radio Regulations and relevant Resolutions and Recommendations to the Radio Regulations. Technical material on the use of this band is contained in ITU-R Recommendations and Reports. Part I of this Handbook includes details pertinent to this allocation as agreed within the ITU. The use of the band 102 – 137 MHz by aviation for air/ground communication systems (aeronautical mobile (R) service) is in full accordance with the provisions of the ITU, as contained in the ITU Radio Regulations.  This chapter contains technical and operational material pertaining to the assignment and use of frequencies in the band 117.975 – 137 MHz.

Note: The allocation to the aeronautical mobile (R) service in the band 108 – 117.975 is subject to the conditions as contained in ITU Resolution 413 (WRC-07).

2.1.2		ICAO documents relevant to frequency assignment planning include:

  - Annex 10 Volume III (Communication systems),

    - Part I (Digital data communication systems) – Chapter 6 – VHF air-ground digital link

    - Part II (Voice communication systems) – Chapter 2 – Aeronautical Mobile Service

  - Annex 10 Volume V, Chapter 4 – Utilization of frequencies above 30 MHz and Attachment A – Considerations affecting the deployment of VHF communication frequencies

Note: This material is reproduced in Appendix B

  - ICAO Regional Air Navigation Plans and relevant ICAO Regional Air Navigation Agreements.

## 2.2		Interference model

2.2.1		General

2.2.1.1		An aircraft can be subject to interference caused by transmissions from other (nearby) aircraft and from ground stations. These transmissions can be generated on the desired frequency (co-frequency) or on frequencies adjacent to the desired frequency (adjacent frequency). Communications between aircraft and ground stations, operating on the same frequency within the same designated operational coverage of a particular frequency is not considered as harmful interference as indeed all relevant aircraft and ground stations are expected to use the communication services provided on this frequency (all transmissions from aircraft and ground station(s) within either area A or area B in Figure 2-1). Other co-frequency communications (from outside the designated operational coverage of the desired station / service, e.g. transmissions from within area B in Figure 2-1 may interfere with communications within area A in Figure 2-1 and vice versa ) may cause interference which may be harmful. Similarly, the use of frequencies adjacent to the frequency in use may cause harmful interference.

2.2.2		Interference model used in aeronautical frequency assignment planning for air/ground VHF communication systems.

2.2.2.1		The model used for establishing co-frequency separation distances in aeronautical frequency assignment planning for systems used for both air-ground and ground-air communications is shown in Figure 2 – 1. When the (protection) distance between aircraft a and aircraft b is equal or greater than the sum of the radio horizon (line-of-sight) of each aircraft, the aircraft stations are mutually protected from interference from each other (see also paragraph 1.3.4).

Note: The calculation of minimum separation distances is described in paragraph 2.7.

When the minimum protection distance has been established between the closest points of the respective designated operational coverage (DOC) areas, all aircraft (and the ground station) operating within the DOC area “A” are protected from harmful interference from all aircraft (and the ground station) operating within DOC area “B” as these are operating well beyond the radio horizon of each other.

This method also protects aircraft if the e.i.r.p of the ground stations is different because the ground station is normally situated well beyond the radio horizon if the minimum separation distance between aircraft stations is met.  Paragraph 2 – 7 describes in detail the different interference mechanisms that need to be considered in frequency assignment planning to protect frequency assignments from co-frequency interference (paragraph 2.7.3)  and adjacent frequency interference (paragraph 2.7.4).

Figure 2 – 1 Model for establishing separation distances

In VHF air/ground communication frequency assignment planning, the following three interference models, based on the model in Figure 2 – 1 apply:

- Both the desired and the undesired transmitting / receiving stations involve aircraft stations communicating with a ground station (see paragraph 2.7.3.1)

- The desired ground station is transmitting (broadcasting) from the ground and the desired aircraft station  is being interfered by another aircraft communicating with (transmitting) another ground station (see paragraph 2.7.3.2)

- The desired ground station is transmitting (broadcasting) from the ground and the desired aircraft station  is being interfered by a undesired transmitting (broadcasting) ground station (see paragraph 2.7.3.3)

2.3		Protection requirements for air/ground voice communication systems operating in the band 117.975 – 137 MHz.

2.3.1		Provisions concerning the deployment of VHF frequencies and the avoidance of harmful interference are contained in Annex 10, Volume V, Chapter 4 (4.1.5) and are reproduced in Appendix B for information and reference.

2.3.2		In summary, Annex 10 Volume V stipulates in paragraph 4.1.5.1 that:

a.	The D/U protection ratio between the desired (wanted) and the undesired (interfering) signal shall be 14 dB. (This provision is to be implemented on the bases of a regional air navigation agreement)

b. 	The D/U protection ratio may be 20 dB in areas where frequency congestion is not severe

c.	These protection ratios are to be achieved at the limit of the designated operational coverage (DOC) which automatically protects all aircraft within the DOC.

The requirement for a D/U ratio of 14 dB has been implemented through a regional agreement in Europe and is used in North America. Other Regions apply the 20 dB protection ratio (which is equivalent to the radio line-of sight criterion as described in paragraph 2.2.1).

2.3.3		Protection of signals in space.

2.3.3.1		Annex 10 has established minimum field strength levels (signal in space) for the various air/ground communication systems that can operate in the frequency band 112 – 137 MHz. These field strength levels, together with other relevant data such as typical values for ground and airborne transmitter power, are reproduced in Tables 2 – 1a and 2 – 1b.  Protection of aeronautical VHF air/ground communication systems is based on the principle that these minimum field strength levels are not subject to harmful interference if the interfering (undesired) signal is either more than 14 dB (re. paragraph 2.3.2 a) or more than 20 dB (re. paragraph 2.3.2. b) below the specified minimum field strength (of the desired signal).

Protection is achieved by securing that the potential interferer is located at a distance that will allow for the interfering signal to sufficiently below the minimum field strength (see paragraph 1.3.3 which describes the line-of-sight method or paragraph 1.3.4 which describers the separation distance ratio method).  The line-of-sight method is used in all ICAO Regions, except Europe and [parts of[ North America, where a combination of the two methods is being used.

- Table 2 – 1a also contains typical values for ground and airborne transmitter power that can be used in interference assessment.

| Parameter | DSB-AM | DSB-AM | VDL-M2 | VDL-M2 | VDL-M3 | VDL-M3 | VDL-M4 | VDL-M4 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| TRANSMITTER | Airborne | Ground | Airborne | Ground | Airborne | Ground | Airborne | Ground |
| Output power transmitter (typical ground station output power is 25 or 50 W (44 or 47 dBm) | 44 dBm (25 W) | 50 dBm (100 W) | 42 dBm (16 W) | 44 dBm (25 W) | 44 dBm (25 W) | 44 dBm (25 W) | 42 dBm (15 W) | 45 dBm (32 W) |
| Feeder loss (assumed) | -3 dB | -3 dB | -3 dB | -3 dB | -3 dB | -3 dB | -3 dB | -3 dB |
| Antenna gain (assumed) | 0 dB | 2 dB | 0 dB | 2 dB | 0 dB | 2 dB | 0 dB | 2 dB |
| EIRP | 41 dBm (12.5 W) | 49 dBm (80 W) | 39 dBm (8W) | 43 dBm (20 W) | 41 dBm (12.5 W) | 43 dBm (20 W) | 40 dBm (10 W) | 44 dBm (25 W) |
| Adjacent frequency emission (Transmitter) for VDL specified in Annex 10, Vol. III, Part I, paragraph 6.3.4 |
| 1st adj fr. (16 kHz bandwidth) | Not specified in Annex 10 | -18 dBm | -18 dBm | -18 dBm | -18 dBm | -18 dBm | -18 dBm |
| 2nd adj fr. (25 kHz bandwidth) | Not specified in Annex 10 | -28 dBm | -28 dBm | -28 dBm | -28 dBm | -28 dBm | -28 dBm |
| 4th adj fr. (25 kHz bandwidth) | Not specified in Annex 10 | -38 dBm | -38 dBm | -38 dBm | -38 dBm | -38 dBm | -38 dBm |
| 8th adj fr. (25 kHz bandwidth) | Not specified in Annex 10 | -43 dBm | -43 dBm | -43 dBm | -43 dBm | -43 dBm | -43 dBm |
| 16th adj fr. (25 kHz bandwidth) | Not specified in Annex 10 | -48 dBm | -48 dBm | -48 dBm | -48 dBm | -48 dBm | -48 dBm |
| 32nd adj fr. (25 kHz bandwidth) | Not specified in Annex 10 | -53.dBm | -53.dBm | -53.dBm | -53.dBm | -53.dBm | -53.dBm |

- Table 2 – 1a   Typical values for various parameters for VHF communication systems (transmitter)

| Parameter | DSB-AM | DSB-AM | VDL-M2 | VDL-M2 | VDL-M3 | VDL-M3 | VDL-M4 | VDL-M4 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| RECEIVER |
| Min signal at receiver antenna (Annex 10, Vol. III) | 75 μV/m (-82 dBm) part II 2.2.1.2 | 20 μV/m (-93 dBm) part II 2.3.1.2 | 75 μV/m (-82 dBm) part I 6.2.2. | 20 μV/m (-93 dBm) part I 6.3.2 | 75 μV/m (-82 dBm) part I 6.2.2. | 20 μV/m (-93 dBm) part I 6.3.2 | 35 μV/m (-88 dBm) part I 6.9.5.1.1.1 | 35 μV/m (-88 dBm) part I 6.9.5.1.1.1 |
| Feeder loss | -3 dB | -3 dB | -3 dB | -3 dB | -3 dB | -3 dB | -3 dB | -3 dB |
| Antenna gain | 0 dB | 2 dB | 0 dB | 2 dB | 0 dB | 2 dB | 0 dB | 2 dB |
| Min. signal at receiver input | -85 dBm | -94 dBm | -85 dBm | -94 dBm | -85 dBm | -94 dBm | -91 dBm | -89 dBm |
| Out-of-band immunity performance of receiver as per Annex 10, Volume III, Part I, paragraph 6.3.5.3.(VDL) and Volume III, Part II, paragraph 2.3.2.8 (DSB-AM). |
| 1st adj. Ch |  |  | -40 dB | -40 dB | -40 dB | -40 dB | -40 dB | -40 dB |
| 4th adj. Ch | -50 dB | -50 dB | -60 dB | -60 dB | -60 dB | -60 dB | -60 dB | -60 dB |

- Table 2 – 1b   Typical values for various parameters for VHF communication systems (receiver)

Conversion from input power (dBm) to field strength (μV/m and v.v.) was done on the basis of the following formula:

Pr = E - 20logF - 167.2;

Where:

Pr is isotropically received power (dB(W))

E is the electric field strength (dB(μV/m) and

F is the frequency (GHz)

(ITU-R Recommendation PN.525-2 refers).

dBm is power relative to 1 milliwatt.

This formula can be converted in

10logPr = 20logE – 20logF-77.2

where Pr is signal at receiver antenna (in space) in mW, E is the field strength at the antenna in µV/m and F is the frequency f in MHz.

[dB(µV/m) = 20log(µV/m)]

2.4		Allotment of the frequency band 117.975 – 137 MHz.

2.4.1		Annex 10, Volume V, Chapter 4, paragraph 4.1.1 and Table 4 – 1 has established a general allotment of the frequency band 117.975 – 137 MHz. The main sub-divisions of this band are the frequency bands allocated to both international and national services and frequency bands solely allocated to national services. The provisions of this paragraph are reproduced in Appendix B.

2.4.2		Annex 10, Volume V includes provisions for the use of specific frequencies as follows:

121.5 MHz – Emergency frequency; the guard band for this frequency includes the band 121.425 – 121.575 MHz. (See also Annex 10, Volume V, paragraph 4.1.3.1)

121.6 – 121.9917 MHz (121.975 where 25 kHz frequency separation is deployed) – This band is reserved for ground movement communications, pre-flight checking and ATS clearance services.

123.1 MHz – Auxiliary frequency for SAR purposes. The guard band for this frequency includes the band 123.075 – 123.125 MHz. (See also Annex 10, Volume V, paragraph 4.1.4)

123.450 MHz – Air to air communications channel; to be used when the aircraft is out of the range of VHF ground stations. (See also Annex 10, Volume V, paragraph 4.1.3.2)

136.975 MHz – Common signaling frequency for VDL; this frequency uses the VDL Mode 2 modulation scheme. (See also Annex 10, Volume 5, paragraph 4.1.3.3)

Frequencies in the band 136.500 – 137 MHz are not available for assignment to frequencies with a bandwidth of less than 25 kHz (See Annex 10, Volume V, paragraph 4.1.8.1.1, note 1).

2.4.3		In addition to the general allotment plan, all Regions have developed a more detailed allotment plan through which operational services are allotted to certain frequency bands and included these in the relevant ICAO Air Navigation Plans (ANP).  The prime goal of these allotment plans is to accommodate new frequency assignments in the sub-bands allotted to a particular service. Appendix E contains a detailed overview of these allotment plans. The Regional allotment plans are incorporated in the ICAO frequency assignment planning program SEARCH FREQUENCY.

2.4.4		Frequency assignments should preferably be made in accordance with the provisions of the Regional allotment table. However, in case a particular requirement for a frequency assignment cannot be made from within the sub-band that is allotted to a particular service, other sub-bands  can be considered to satisfy the requirement.  The Regional frequency allotment plans also include provisions for sub-bands for aeronautical operational control (AOC) communications.

2.5		Frequency separation and channeling

2.5.1		Annex 10 stipulates that the minimum separation between assignable frequencies in the aeronautical mobile (R) service shall be 8.33 kHz. (Annex 10, Volume V, paragraph 4.1.2.1.)

2.5.2		Currently, 8.33 kHz frequency separation has only been introduced in the EUR Region. All other Regions have agreed to base frequency assignment planning on 25 kHz frequency separation. This implies that radio equipment designed for 50 kHz or 100 kHz frequency separation may not always be protected from harmful interference that can be caused by stations operating on adjacent 25 kHz or 8.33 kHz frequencies.

2.5.3		The ICAO program for frequency assignment planning SEARCH FREQUENCY has implemented compatibility calculations for all frequency assignments with 25 kHz frequency separation. In this program the user can select to search for frequencies on multiples of 50 kHz and 100 kHz; however, the planning and protection criteria that are applied relate to 25 kHz frequency separation only.

Note: Criteria for frequency assignment planning in a mixed 8.33 kHz/25 kHz environment is being implemented in the program SEARCH FREQUENCY.

2.5.4		Annex 10, Volume V, Chapter 4 (Utilization of frequencies above 30 MHz), Paragraph 4.1.2 (Utilization in the band 117.975 – 137 MHz; Frequency separation and limits of assignable frequencies) contains more material regarding the frequency separation and the protection dates of the different systems that can operate in the band 117.975 – 137 MHz.

Note: the protection dates specified in the relevant SARPs require updating.

2.5.5		Protection of 25 kHz frequency assignments

2.5.5.1		In Regions that continue operation with a frequency separation of  25 kHz, frequency assignments are protected from harmful interference from the use of frequencies operating on multiples of 8.33 kHz in (adjacent) Regions (see Annex 10, Volume V, paragraph 4.1.2.2.1, note and 4.1.8.1.1, note 2).

2.5.6		Channeling

2.5.6.1		Normally, in aviation the frequency in use is identified through the frequency (and not a channel number) (e.g. frequency 118.150 (as used in radio telephony) is the frequency 118.850 MHz and frequency 118.975 is the frequency 118.975 MHz.) For the use of 8.33 kHz frequencies in one single radio that can operate in 8.33 kHz frequency separation mode as well as in 25 kHz frequency separation mode, the frequency identification for 8.33 kHz frequencies was replaced with a channel identification similar to the method used for identifying frequencies. The channel/frequency identification is in accordance with Table 2 – 2. (See also Appendix C).

| Frequency (MHz) | Frequency separation (kHz) | Channel # |
| --- | --- | --- |
| 118.0000 | 25 | 118.000 |
| 118.0000 | 8.33 | 118.005 |
| 118.0083 | 8.33 | 118.010 |
| 118.0167 | 8.33 | 118.015 |
| 118.0250 | 25 | 118.025 |
| 118.0250 | 8.33 | 118.030 |
| 118.0333 | 8.33 | 118.035 |
| 118.0417 | 8.33 | 118.040 |
| 118.0500 | 25 | 118.050 |
| 118.0500 | 8.33 | 118.055 |
| 118.0583 | 8.33 | 118.060 |
| 118.0667 | 8.33 | 118.065 |
| 118.0750 | 25 | 118.075 |
| 118.0750 | 8.33 | 118.080 |
| 118.0833 | 8.33 | 118.085 |
| 118.0917 | 8.33 | 118.090 |
| 118.1000 | 25 | 118.100 |
| etc. |  |  |

Table 2 – 2 Channeling / frequency pairing for frequencies with 25 kHz and 8.33 kHz separation

2.6		Services and designated operational coverage

2.6.1		Frequency assignments are made to implement specific aeronautical services as follows:

Aerodrome

TWR	Aerodrome control service

AS	Aerodrome surface communications

AFIS	Aerodrome flight information service

Approach

APP	Approach control service

ATIS	Automatic terminal information service

En route

FIS	Flight information service

ACC	Area control service

Other functions

A/A		Air-to-air

A/G		Air-to-ground

AOC		Aeronautical operational control

VOLMET	Meteorological broadcast for aircraft in flight

GPS		VHF En-Route General Purpose System

EMERGENCY	Emergency

SAR		Search and rescue

2.6.1.1		No frequency coordination of frequency assignment planning is necessary for the emergency frequency (121.500 MHz) and the SAR frequency (123.100 MHz) as these services are available globally at each station where this service is required. Also, no specific frequency assignment planning is required for the air-to-air communication channel 123.450 MHz as this channel is to be used only in remote and oceanic areas when the aircraft is outside VHF coverage and does not involve ground stations.

2.6.2	Table of uniform values for designated operational coverage (DOC)

Frequencies for aeronautical radio communication services are (normally) implemented to satisfy the operational need for specific services. These services, and their uniform designated operational coverage areas, are as in Table 2 – 3.

| Service | Designated Operational Coverage |  |  |
| --- | --- | --- | --- |
|  | Range (NM) | Height (ft) | Comments |  |
| Aerodrome |  |  |  |  |
| TWR | 25 | 4000* |  |  |
| PAR | 25 | 4000* | Also APP-PAR |  |
| AFIS | 25 | 4000* |  |  |
| AS | Limits of aerodrome | surface |  |  |
| Approach |  |  |  |  |
| APP–L | 50 | 12000 | Also APP-SR-L |  |
| APP–I | 75 | 25000 | Also APP-SR-I |  |
| APP–U | 150 | 45000 | Also APP-SR-U |  |
| En-Route |  |  |  |  |
| ACC–L | Area | 25000 | Within specified area; also ACC-SR-L |  |
| ACC-I | Area | 25000 | Within specified area; also ACC-SR-I |  |
| ACC–U | Area | 45000 | Within specified area; also ACC-SR-U |  |
| FIS | Area | 45000 | Within specified area |  |
| FIS-L | Area | 25000 | Within specified area |  |
| FIS-U | Area | 45000 | Within specified area |  |
| VOLMET | 260 | 45000 | Maximum coverage |  |
| Other functions |  |  |  |  |
| ATIS | 260 | 45000 | In EUR the uniform DOC is 60/200 |  |
| A-A | - | - | DOC to be determined by States |  |
| A-G | - | - | DOC to be determined by States |  |
| AOC | Not protected | Not protected |  |  |
| EMERG | N/A | N/A |  |  |
| SAR | N/A | N/A |  |  |
| GPS |  |  | To be determined by States |  |

Table 2 – 3 Table of uniform designated operational coverage

Notes:	* Height above ground

Additional functionality in the column “comments” may be added to the services as follows:

CD	Clearance delivery

CTA	CTA

DF 	Direction finding

ER	Extended range

RCAG	Remote controlled air-ground communications

SR	Surveillance Radar

These additions do not alter the basic service or the DOC for which the frequency is required and should be included as a remark to the frequency assignment in the COM list in the global table of frequency assignments and the program SEARCH FREQUENCY.

2.6.3 		Non-standard DOC (Range and Height) may be implemented as and when required. Reduced DOC may alleviate frequency congestion.

2.6.4		The use of common frequencies, preferably Region wide, to satisfy requirements for specific non-protected applications such as light aviation, gliding and balloon activities is recommended as such use increases the efficiency in frequency assignment planning. Normally, these applications operate on a non-protected basis.

2.6.5		Frequencies for aeronautical operational control are not protected through frequency planning. These frequencies are normally assigned on the basis of the traffic loading that is expected. (E.g. within the same area, smaller airlines can share the same frequency for operational control purposes).

2.6.6		The risk of interference from FM broadcasting stations operating in the band 87 – 108 MHz is generally not considered for frequency assignments in the band 117.975 – 137 MHz.

2.6.7		ICAO frequency assignment planning does not include protection against interference that may be caused in case facilities are co-located (e.g. interference due to intermodulation products)

2.6.8		Frequency coordination must take place with all States which may be affected by a proposal for a new frequency assignment or where the characteristics of an existing assignment are modified. Normally, such coordination is effected through the ICAO Regional Offices which have a central and coordinating role in frequency assignment planning.

2.7		Calculation of separation distances

Note: The material contained in this section can be used in areas where frequency assignment planning is based solely on 25 kHz or 8.33 kHz frequency separation. Paragraph 2.7.5 contains material to be considered when establishing separation distances in a mixed 25 kHz and 8.33 kHz environment

2.7.1		Protection of frequency assignments from harmful interference is achieved through frequency and/or distance separation. Normally, the determining factor in frequency assignment planning is the risk of interference between two aircraft, operating within different DOC areas at the closest point. As normally the ground station is located well within the DOC area, the ground station is protected when the aircraft (receiver) is protected from harmful interference.

2.7.2	The separation distances provided in this paragraph are the minimum distances that need to be maintained between the ground stations that provide the relevant service. The separation distances have been established using the method in paragraph 1.3 and 2.2 and the protection requirements as in paragraph 2.3.

2.7.3		Co-frequency separation distances

2.7.3.1		Air/ground communication services. Protection of co-frequency assignments for air/ground communication services (involving aircraft transmissions) is obtained by securing that the D/U ratio is in accordance with the regionally agreed value. The D/U ratio can be either 14 dB or 20 dB. (Re. paragraph 2.3.2).

2.7.3.1.1	Co-frequency  separation distance for air/ground communications

D/U is 20 dB (radio line-of-sight)

As described in 1.3.4.2 and 2.2.1, in Regions where a protection ratio (desired over undesired signal, D/U) of 20 dB has been agreed, the minimum separation distance from the edge of the DOC (of the desired) ground station A to another (undesired) aircraft, operating on the same frequency (and outside the desired DOC), should be the sum of the distance to the radio horizon from each aircraft station. As shown in Figure 2 - 2, when the ground stations have a designated operational range of RA and RB respectively and RHA and RB is the distance from the respective aircraft to the radio horizon, the minimum separation distance between the ground stations should be

RA + RHA + RHB +RB.

Figure 2 – 2 Separation distance based on Radio line-of-sight

Separation distance for D/U is 14 dB (1 : 5 separation distance ratio)

As described in 1.3.4, where a D/U protection ration of 14 dB is applied, the 1:5 distance ratio is to be used. To meet the 14 dB protection requirement, the distance between the aircraft receiver and the (interfering) aircraft transmitter needs to be at least 5 times the distance between the aircraft receiver and the desired ground station. This assumes that the e.i.r.p of both the [desired] station and the [undesired; interfering] station is the same. Where the e.i.r.p of the transmitters is different, adjustments to this formula are necessary (see paragraph 1.3.4).

Figure 2 – 3 Separation distance based on 5 to 1 distance ratio

In Figure 2 – 3 the designated operational range for ground station A is RA and for ground station B is RB. If the (minimum separation) distance from aircraft station a to aircraft station b is at least 5 times the distance from aircraft station a to ground station A (5*RA) aircraft station a is protected from interference from aircraft station b. Vice versa, if the distance from aircraft station b to aircraft station a is at least 5 times the distance from aircraft station b to ground station B (5*RB) aircraft station b is protected from interference from aircraft station a.  The minimum separation distance between the two aircraft stations a and b is the largest of 5*RA and 5*RB. The minimum separation between the ground stations is the larger value of

RA + 5RA + RB or RA + 5RB + RB.

In cases where this value is larger than RA + RHSA +RHB +RB (as described in paragraph 2.7.3.1.1 above) the line-of-sight criterion should be used.

2.7.3.1.2	Area services

For area services (such as ACC or FIS) the minimum separation distance that should be applied is the minimum distance between the closest point between the limit of the area services at maximum height (and, if applicable, also circular). The distance between these points at the limit of the DOC shall be at least the sum of the radio horizon of each aircraft at maximum protected flight level. The minimum separation distance between area services (and in cases where one service is an area service and the other service is a circular service) is RHA + RHB between the closest points of the respective service area. (See also paragraph 2.7.6)

The ICAO frequency assignment planning program SEARCH FREQUENCY currently has implemented planning criteria applicable to the 20 dB D/U protection ratio  (radio line-of-sight), as established in paragraph 2.7.3.1.1. In line with current practice in many Regional Offices, area services are protected as a circular service, with a maximum operational range to the radio horizon for the specified height (e.g. 260 NM for an ACC/U service with a maximum flight level of 450 (45000 ft). The program plots on a map any potential interference that can be predicted within the designated operational coverage of the area service.

2.7.3.1.3	Co-frequency separation distances – broadcast services (ATIS and VOLMET)

Broadcast services such as ATIS and VOLMET are characterized by ground-to-air transmissions only and do not involve airborne transmissions. As a consequence, the separation distance between broadcast (ground) stations can be smaller compared to the case where aircraft transmissions are involved.

To protect an aircraft which is receiving broadcasts from an aeronautical ground broadcast station from interference from another aeronautical ground broadcast station, the minimum co-frequency separation distance between the (wanted) aircraft to the (unwanted) ground station is the distance to the radio horizon from the (wanted) aircraft plus 30 NM. This separation distance secures that the undesired VOLMET or ATIS station is located well beyond the radio horizon of the (desired) aircraft and accommodates a normally higher e.i.r.p for VOLMET (or ATIS) transmitters (typically 100 W). The designated operational coverage for these broadcast stations is normally the maximum that can be achieved (260 NM at flight level 450). The interference mechanism is shown in Figure 2 –45.

Figure 2 – 4 Interference mechanism between broadcast services

The minimum separation distance between two (ground) broadcast stations is

RA+RHA+30 (NM)

To secure compatibility when station B is the wanted broadcast station and aircraft B is the desired receving aircraft station, the minimum separation distance between the (ground) broadcast stations A and B is

RB+RHB+30 (NM)

To secure compatibility between the two broadcast stations the minimum separation distance to be maintained between the ground broadcast stations A and B respectively is the larger value of:

(Max) RHA + RA + 30 or RHB + RB + 30

Where: RA is the designated operational range for ground broadcasting station “A”

RB is the designated operational range for ground broadcasting station “B”

RHA is the distance to the radio horizon of aircraft A

RHB is the distance to the radio horizon of aircraft B

(Distances in NM)

Note: these values are specified for VOLMET in Annex 10, Volume V, Attachment A paragraph 5.

[In the EUR Region, where the protection requirement of 14 dB D/U is used, the minimum separation distance to the (undesired) broadcast station is 5 times the designated operational range of the (desired) broadcast service or the distance to the radio horizon from the edge of the range of the (desired) broadcast signal, whichever distance is less].

2.7.3.1.4	Co-frequency separation distances – broadcast and air-ground services

To protect an aircraft station receiving broadcasts from a ground station from another station providing air/ground communications the mechanism as shown in Figure 2  - 5 applies

Figure 2-5 Interference mechanism between broadcast service and air/ground service

In order to protect aircraft B, which is receiving (only) broadcast information from ground broadcast station B (e.g. VOLMET or ATIS), from interference that can be caused by transmissions from aircraft station B, the minimum separation between the two aircraft stations needs to be the sum of the radio horizon of aircraft station A (RHA) and the radio horizon of aircraft station B (RHB).  The minimum separation distance between the two ground stations then becomes:

RA + RHA + RHB +RB

Where: RA is the designated operational range for station “A”

RB is the designated operational range for broadcasting station “B”

RHA is the distance to the radio horizon of aircraft A

RHB is the distance to the radio horizon of aircraft B

(Distances in NM)

This distance is the same as in the case where both services are air/ground communication services (see paragraph 2.7.3.1.1).

To protect aircraft A from interference that can be caused by (ground ) broadcast station B, the minimum separation between the two ground stations needs to be (see paragraph 2.7.3.1.3):

RA+RHA+30 NM

To protect both stations from interference that can be caused by each other, the maximum of the distances to be applied is

(Max) RA + RHA + RHB +RB or RA+RHA+30 NM

2.7.3.4		Unprotected services.

2.7.3.4.1	Certain services are not protected from interference and in many cases, no coverage has been determined for these services. An example is the use of frequencies for aeronautical operational control or for special uses such as for gliders and balloons.

2.7.3.4.2	Assignment of frequencies to stations is in these cases normally determined on the basis of the traffic loading that can be expected by the users of these -unprotected- frequencies.  As long as these frequencies are in operation exclusively for unprotected use, these assignments are not subject to interference calculations. When these frequencies are shared with protected services, consideration needs to be given whether the use of the unprotected frequencies may cause interference to frequencies (co- and adjacent frequency) which do require protection from harmful interference and an assessment of potential interference should be undertaken. This may result in a situation that while the protected service is to be protected from interference from the unprotected service, the unprotected service is in turn also protected from interference from the protected service.

2.7.3.4.4	 In the interest of efficient frequency assignment planning it is important to realize that when frequency assignments to unprotected services are being made, these should preferably be concentrated in one (or more) sub-bands solely reserved for unprotected services. Where feasible, such sub-bands should be established.

2.7.3.4.5	The program SEARCH FREQUENCY calculates the potential interference between frequency assignments for unprotected services as well as between frequency assignments for unprotected and for protected services. When presenting the calculation results, interference into unprotected services (or between unprotected services) can omitted from the calculation results.

2.7.4		Adjacent frequency separation distances

2.7.4.1		Air/ground communication services (25 kHz frequency separation).

2.7.4.1.1	The minimum separation between aircraft operating on the first adjacent (25 kHz) frequency is 10 NM (Re. Figure 2 – 6). An effective (first) adjacent frequency rejection of 60 dB is assumed which may lead to interference in cases where 50 kHz equipment is still in use.   Annex 10 shows that, for aircraft receivers designed for operation in an environment where the minimum frequency separation is 25 kHz and assuming an effective adjacent frequency rejection of 60 dB or better, the minimum separation to be maintained between aircraft operating on adjacent frequencies is 3 NM. This also applies for receivers operating with a frequency separation of 8.33 kHz and to the first adjacent (8.33 kHz) frequency. These criteria protect the receiver by muting. A 20 dB D/U ratio is considered with this separation distance.  Current practice is to use a value of 10 NM instead of 3 NM to secure adjacent frequency protection through frequency assignment planning.

Figure 2 – 6 Adjacent frequency separation for air-ground services.

The minimum separation between two ground stations operating on the first adjacent 25 kHz frequency is:

RA +10 NM +RB

This minimum separation distance prevents adjacent frequency interference between two aircraft and applies when one (or both) aircraft stations provides air/ground communications

2.7.4.2		Adjacent frequency separation distances between broadcast services (ATIS, VOLMET).

2.7.4.2.1	In case both ground stations are broadcast (VOLMET, ATIS) stations, the minimum adjacent frequency separation distance between the aircraft and an unwanted (interfering) ground broadcasting station is 13 NM as shown in Figure 2 – 7.

Figure 2 – 7 Adjacent frequency separation between broadcast services

The minimum separation between two ground broadcast stations, operating on adjacent frequency, is

RA + 13 NM

where: RA is the designated operational range for ground broadcast station A

Similarly, for broadcast station B, the minimum separation distance between the two ground stations is

RB + 13 NM

where: RB is the designated operational range for ground broadcast station B (not shown in Figure 2 – 7)

The minimum separation distance that needs to be secured between the broadcast stations A and B is the larger value of:

(Max)  RA + 13 NM or RB + 13 NM

2.7.4.3 		Adjacent frequency separation distances – broadcast and air-ground services

2.7.4.3.1	In this case, two different interference mechanisms need to be analyzed. The minimum separation distance can be calculated as follows:

Aircraft a is involved in air/ground communications with ground station A (Range RA)

Aircraft b is receiving broadcast messages only from ground station B (Range RB)

a. 	minimum separation distance between the two ground stations to protect the aircraft station a from interference from the (broadcasting) ground station b,  as described in paragraph 2.7.4.2, is

RA +13 NM

where RA is the designated operational range of the station providing air/ground communications.

b.	minimum separation distance between the two ground stations to protect the broadcast receiver (aircraft station b) from interference from aircraft station a. With the method as described in paragraph 2.7.4.1, the minimum distance between the aircraft stations is 10 NM. The minimum distance between the ground stations is

RA +10 + RB

where: 	RA is the designated operational range of the air-ground communication service

RB is the designated operational range of the broadcast service

To secure protection of both services, the minimum separation between the ground stations is the larger value of:

(Max)	RA +13 NM or RA +10 + RB

2.7.5 		Co – and adjacent frequency consideration in a mixed environment where 8.33 kHz and 25 kHz frequency separation is being used.

Note: The following criteria are contained in the EUR Frequency management manual and require further consideration, in particular with regard to the protection of frequencies using off-set carrier (CLIMAX) systems.

2.7.5.1		Co-frequency separation criteria should be used when the 8.33 kHz frequency and the 25 kHz frequency are the same (e.g. channel 119.000 and 119.005 operate both on the frequency 119.000 MHz). Co-frequency  separation criteria should also be applied between an 8.33 kHz frequency and a 25 kHz frequency which are separated by 8.33 kHz MHz. (e.g. channels 119.010 and 118.990, using frequencies 119.0083 MHz and 118.9917 MHz respectively) are considered both co-frequency to the [25 kHz] frequency 119.000 (119.000 MHz))

2.7.5.2		At least [33] NM should be the separation distance between the edges of the DOC’s when the 8.33 kHz and a 25 kHz frequencies are separated by 16.67 MHz (e.g. channels 119.015 and 118.985, using frequencies 119.0167 MHz and 118.9833 MHz).

Note: These frequencies are considered co-frequency to the next 25 kHz frequency (e.g. co-frequency to 119.025 MHz and 118.975 MHz.

2.7.5.3		At least 10 NM should be the separation between the edges of the DOC’s when the 8.33 KHz frequency and the 25 kHz frequency are separated by 20 kHz (i.e. the same criteria as for a 25 kHz adjacent frequency.

2.7.5.4		At least 4 NM should be the separation distance between an 8.33 kHz frequency and a 25 kHz frequency which are separated by 25 kHz (e.g. channel 118.000 (25 kHz) and 118.030 (8.33 kHz) which use the frequency 118.000 MHz and the frequency 118.025 MHz respectively)

2.7.5.5	Table 2 – 4 gives an overview of the separation distances to be maintained in a mixed 25 / 8.33 kHz environment. The values for the adjacent frequency separation are in NM. “C” indicates that the co-frequency separation criteria (line-of-sight or the 1 : 5 distance ratio needs to be applied.

|  | 118.0000 118.000 | 118.0000 118.005 | 118.0083 118.010 | 118.0167 118.015 | 118.0250 118.025 | 118.0250 118.030 | 118.0333 118.035 | 118.0417 118.040 | 118.0500 118.050 | 118.0500 118.055 | 118.0583 118.060 | 118.0667 118.065 | 118.0750 118.075 | 118.0750 118.080 | 118.0833 118.085 | 118.0917 118.090 | 118.1000 118.100 | 118.1000 118.105 | 118.0000 | 118.0000 | 118.0000 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 118.0000 118.000 | C | C | C | 33 | 10 | 4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 118.0000 118.005 | C | C | 10 |  | 4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 118.0083 118.010 | C | 10 | C | 10 | 33 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 118.0167 118.015 | 33 |  | 10 | C | C | 10 |  |  | 4 |  |  |  |  |  |  |  |  |  |  |  |  |
| 118.0250 118.025 | 10 | 4 | 33 | C | C | C | C | 33 | 10 |  |  |  |  |  |  |  |  |  |  |  |  |
| 118.0250 118.030 | 4 |  |  | 10 | C | C | 10 |  | 4 |  |  |  |  |  |  |  |  |  |  |  |  |
| 118.0333 118.035 |  |  |  |  | C | 10 | C | 10 | 33 |  |  |  |  |  |  |  |  |  |  |  |  |
| 118.0417 118.040 |  |  |  |  | 33 |  | 10 | C | C | 10 |  |  | 4 |  |  |  |  |  |  |  |  |
| 118.0500 118.050 |  |  |  | 4 | 10 | 4 | 33 | C | C | C | C | 33 | 10 |  |  |  |  |  |  |  |  |
| 118.0500 118.055 |  |  |  |  | 4 |  |  | 10 | C | C | 10 |  | 4 |  |  |  |  |  |  |  |  |
| 118.0583 118.060 |  |  |  |  |  |  |  |  | C | 10 | C | 10 | 33 |  |  |  |  |  |  |  |  |
| 118.0667 118.065 |  |  |  |  |  |  |  |  | 33 |  | 10 | C | C | 10 |  |  |  |  |  |  |  |
| 118.0750 118.075 |  |  |  |  |  |  |  |  | 10 | 4 | 33 | C | C | C | C | 33 | 10 |  |  |  |  |
| 118.0750 118.080 |  |  |  |  |  |  |  |  | 4 |  |  | 10 | C | C | 10 |  | 4 |  |  |  |  |
| 118.0833 118.085 |  |  |  |  |  |  |  |  |  |  |  |  | C | 10 | C | 10 | 33 |  |  |  |  |
| 118.0917 118.090 |  |  |  |  |  |  |  |  |  |  |  |  | 33 |  | 10 | C | C | 10 |  |  |  |
| 118.1000 118.100 |  |  |  |  |  |  |  |  |  |  |  |  | 10 | 4 | 33 | C | C | C | C |  |  |
| 118.1000 118.105 |  |  |  |  |  |  |  |  |  |  |  |  | 4 |  |  | 10 | C | C |  |  |  |

Table 2 – 4 Adjacent frequency separation distances for a mixed 25 kHz/8.33 kHz environment

2.7.6		Frequency planning criteria for area services

2.7.6.1		For area services, the separation distance is measured from the edge of the coverage of the area service. When the two services considered include a circular service, the separation distance is from the station providing the circular service to the closest point of the edge of coverage of the area service.

Figure 2 – 8 Minimum separation of area services

Note: RLOS is radio line-of-sight

2.7.6.2		Co-frequency separation

The minimum separation between the designated operational coverage of two area services is equal to the sum of the radio line-of-sight for each area service at the limit of the DOC (coverage). This method provides frequency protection throughout the DOC of the area service. In Figure 2 – 8 around the each of the area services a buffer zone equal to the distance to the radio horizon for an aircraft at maximum altitude of the relevant DOC has been established. The minimum separation to protect the two area services from harmful interference is established at the closest point between the service areas.

2.7.6.2.1		In many cases, for large designated operational coverage areas of area services, a single ground station cannot provide coverage throughout the service area. In these cases, where required, additional coverage is provided through installing extended range stations (forward relay). These stations can operate on the same frequency (using the off-set carrier system as specified in Annex 10, Volume III) or on a discrete frequency. Not in all cases full VHF coverage is provided, in particular for lower flight levels. The program SEARCH FREQUENCY can display these coverage areas for Flight Information Regions on a map.

2.7.6.2.2		Frequency protection is being calculated in the program SEARCH FREQUENCY for the circular coverage area at the maximum altitude of the station providing the area service. This may lead to overprotection in cases where the coverage of these stations extends outside the area service.

2.7.6.2.3		When the same frequency used by an area service is also used by a broadcasting service (which is a circular service), the minimum separation is the larger value of the following:

a.	to protect the aircraft receiver at the edge of the area coverage, the minimum distance to the ground broadcast transmitter should be at least the distance to the radio horizon  + 30 NM from the limit of the DOC of the area service

b.	the minimum distance from the aircraft broadcast receiver to the airborne transmitter at the edge of the area service should be at least the sum of the distance to the radio horizon (radio line-of-sight) for each aircraft. The minimum distance from the edge of the DOC of the area service to the broadcast transmitter should be at least the sum of the distance to the radio horizon for each aircraft plus the range of the broadcast station.

The methodology for establishing the minimum separation distances is the same as provided in paragraphs 2.7.3 and 2.7.4. However, in order to secure protection of area services throughout the DOC, separation distances are measured from the limit of the DOC rather than from the ground station(s) providing the area service.

2.7.6.3		Adjacent frequency separation for area services.

2.7.6.3.1		The minimum separation distance between the designated operational coverage of two area services are to be separated (at the edge of coverage) by at least 10 NM when in each of the two areas the first adjacent frequencies is being used. (In this case, in figure 2 – 8 the buffer zone around the area service is 10 NM)

2.7.6.3.2		The same condition applies when one of the services is a circular service. In this case, the minimum separation between the edge of the designated operational coverage of the area service and the ground station of the circular service is the range of the circular service + 10 NM

2.7.6.3.3		When the adjacent frequency used by an area service is used by a broadcasting service (which is a circular service), the minimum separation is the larger value of the following:

a.	to protect the aircraft receiver at the edge of coverage, the minimum distance to the ground broadcast transmitter from the edge of coverage should be at least 13 NM.

b.	the minimum distance from the aircraft broadcast receiving to the airborne transmitter at the edge of the area service should be at least the sum of the distance to the radio horizon (radio line-of-sight) for each aircraft plus 13 NM. The minimum distance from the edge of the DOC of the area service to the broadcast transmitter should be at least 13 NM plus the range of the broadcast station.

2.8		Separation distances for VDL (VDL Mode 2 and VDL Mode 4)

2.8.1		VDL operating co-frequency with other VDL or DSB-AM air/ground communication systems.

The same planning criteria as used between VHF voice systems (20 dB protection ratio) should be used. The separation criteria are those as described in paragraph 2.7.3 above.

Note: This applies to VDL vs. DSB-AM as well as between VDL assignments)

2.8.2		VDL operating on adjacent frequencies:

The 1st frequency, adjacent to either a DSB-AM frequency or a VDL frequency should not be used in the same airspace.

The 2nd frequency, adjacent to a DSB-AM frequency should not be used in the same airspace for VDL Mode 4.

| Vs. | Interference source |
| --- | --- |
|  | DSB-AM | VDL 2 | VDL 4 |
| Victim | DSB-AM |  | 1 | 2 |
|  | VDL 2 | 1 | 1 | 1 |
|  | VDL 4 | 2 | 1 | 1 |

Table 2 – 5 25 kHz guard band (channels) between DSB-AM, VDL mode 2 and VDL mode 4

Note: The numbers in Table 4 are guard-bands (channels). The next frequency that can be used without frequency planning constrain is 1 channel higher (e.g. a desired DSB-AM station that is interfered by a VDL Mode 2 aircraft station requires one 25 kHz guard band.. The next frequency, 50 kHz away, can be used in the same designated operational coverage without any frequency assignment planning constraint.

2.8.3.		Attention is drawn to the possibility of interference between DSB-AM and VDL Mode 2/4 when these systems are used on the surface of an airport. Interference can occur if the frequency separation (guard band) is four channels (25 kHz) or less. In this case interference between aircraft stations can be prevented through securing that the minimum field strength of these systems is 70 dBm at the antenna. Any interference that may be caused in ground based receiving stations (i.e. not aircraft stations) can be mitigated through using cavity filters that block in these receivers the reception of unwanted signals from transmissions from aircraft operating on the surface of an airport.

2.9 		Separation distances (air ground communication services and ground based broadcasting services)

2.9.1		Applying the methodology as described in paragraph 2.7, separation distances between the edges of the DOC have been calculated using the distance to the radio horizon (RLOS) as below:

| Symbol | Service range (NM) | Service height | Radio horizon |
| --- | --- | --- | --- |
| TWR | 25 NM | 4000 ft | 78 NM |
| AFIS | 25 NM | 4000 ft | 78 NM |
| AS | Limits of aerodrome | Surface | N/A |
| APP-U | 150 NM | 45000 ft | 260 NM |
| APP-I | 75 NM | 25000 ft | 195 NM |
| APP-L | 50 NM | 12000 ft | 134 NM |
| ACC-U | Specified area | 45000 ft | 260 NM |
| ACC-L | Specified area | 25000 ft | 195 NM |
| FIS-U | Specified area | 45000 ft | 260 NM |
| FIS-L | Specified area | 25000 ft | 195 NM |
| VOLMET | 260 NM | 45000 ft | 260 NM |
| ATIS | 260 NM | 45000 ft | 260 NM |

Table 2 – 6 Distance to radio horizon with aircraft at maximum altitude

Note:	Radio horizon of the aircraft from the edge of DOC.

The minimum separation distances between the ground stations are summarized in Table 2 – 7 and are in accordance with the methods described in paragraph 2.7.3.

2.9.1.1		Automatic Terminal Information Service, or ATIS, is a continuous broadcast of recorded information in busier terminal (i.e. airport) areas. ATIS broadcasts contain essential information, such as weather information, which runways are active, available approaches, and any other information required by the pilots, such as important NOTAMs. As a terminal service, ATIS may not require a DOC greater than APP/U.(to be confirmed). In Tables 2 – 6 and 2 – 7 the designated operational coverage for ATIS is assumed to be the maximum achievable (260 NM / 45000 ft.), in accordance with current practice in various Regions.

|  | VICTIM |
| --- | --- |
|  | Service | TWR 25/40 | AFIS 25/40 | AS 10/1.5 | APP-U 150/450 | APP- I 75/250 | APP-L 50/120 | ACC-U 260/260 | ACC-L 195/195 | FIS-U 260/260 | FIS- L 195/195 | VOLMET 260/260 | ATIS 260/260 |
| INTERFER | TWR | 206 | 206 | 128 | 513 | 373 | 287 | 623 | 493 | 623 | 493 | 623 | 623 |
|  | AFIS | 206 | 206 | 128 | 513 | 373 | 287 | 623 | 493 | 623 | 493 | 623 | 623 |
|  | AS (Note 2) | 128 | 128 | 50 | 435 | 295 | 209 | 545 | 415 | 545 | 415 | 545 | 545 |
|  | APP-U | 513 | 513 | 435 | 820 | 680 | 594 | 930 | 800 | 930 | 800 | 930 | 930 |
|  | APP-I | 373 | 373 | 295 | 680 | 540 | 454 | 790 | 660 | 790 | 660 | 790 | 790 |
|  | APP-L | 287 | 287 | 209 | 594 | 454 | 368 | 704 | 574 | 704 | 574 | 704 | 704 |
|  | ACC-U (Note 1) | 623 | 623 | 545 | 930 | 790 | 704 | 1040 | 910 | 1040 | 910 | 1040 | 1040 |
|  | ACC-L (Note 1) | 493 | 493 | 415 | 800 | 660 | 574 | 910 | 780 | 910 | 780 | 910 | 910 |
|  | FIS-U (Note 1) | 623 | 623 | 545 | 930 | 790 | 704 | 1040 | 910 | 1040 | 910 | 1040 | 1040 |
|  | FIS-L (Note 1) | 493 | 493 | 415 | 800 | 660 | 574 | 910 | 780 | 910 | 780 | 910 | 910 |
|  | VOLMET | 133* | 133* | 55* | 440* | 300* | 214* | 550* | 420* | 550* | 420* | 550 | 550 |
|  | ATIS | 133* | 133* | 55* | 440* | 300* | 214* | 550* | 420* | 550* | 420* | 550 | 550 |

Table 2 -7 – Minimum geographical co-frequency separation distances between stations

Note 1:		 All distances are in NM. Separation distances are between the facilities (ground stations) for (circular) services. For area services, the separation distance between the ground stations has been calculated on the basis of the maximum circular coverage that can be obtained at the maximum flight level or the relevant service. Different combinations of the designated operational range and height will result in minimum separation distances that differ from those in Table 2 – 7. The program SEARCH FREQENCY calculates the minimum required separation distance on the actual designated operational coverage as specified in the relevant COM List.

Note 2: 		For Aerodrome Surface communications, a co-frequency separation distance of 50 NM between two stations has been used. (A DOC of 10 NM / 150 ft. has been assumed). Frequencies for aerodrome surface communications should be selected from the band 121.600 – 121.975 MHz. This band is reserved exclusively for aerodrome surface communications.

Note 3:		The designated operational coverage for area services (ACC and FIS) in Table 2 – 7 is assumed to be circular with the following values:

ACC/L and FIS/L: 	194 NM / 25000 ft.

ACC/U and FIS/U:	360 NM / 45000 ft.

Note 4:		Separation distances marked with an asterix (*) are sufficient to protect an air/ground communication service from interference that can be caused by a (ground) broadcasting station (VOLMET, ATIS). (ATIS/VOLMET stations are the interferer and the air/ground communication service (at the aircraft) is the victim.  However, to protect also the broadcasting service, the separation distances for the air/ground communication services as interferer need to be used. (See also 2.7.3.3, 2.9.1.2 and 2.9.1.2.1.)

(Table2-7A – separation distances based on 5:1 distance ratio (14 dB D/U) to be added)

2.9.1.2		VOLMET and ATIS are one-way transmissions from a ground transmitter to the aircraft. Since the VOLMET DOC has been calculated upon the maximum coverage that can be obtained at 45000 ft  (260 NM), protection between VOLMET stations can be secured if the separation distance between these DOC  is 30 NM, assuming a VOLMET transmitter height of 100ft and results in a VOLMET/VOLMET co-frequency separation distance of 260 + 30 + 260 = 550 NM. This distance would also be sufficient for the protection of ATIS from interference from VOLMET transmissions.

2.9.1.2.1	Not in all cases where interference can be caused by an air/ground communication service into the on-board reception of ATIS/VOLMET broadcast transmission, the ATIS/VOLMET broadcast transmissions will, vice versa, interfere with the (on-board) reception of the air/ground communication service transmission (see 2.7.3.3).

For example, to protect the reception of a TWR service from interference from the transmission of a (ground) VOLMET station (the VOLMET station is the interfere) , the minimum separation distance between the ground TWR station and the ground VOLMET station is the sum of the DOC-range and the radio horizon for the TWR service and 30 NM:

25 NM + 78 NM +30 NM = 133 NM.

To protect also the reception of the VOLMET service from interference from the transmission of the (airborne) TWR station, the minimum separation between the ground VOLMET station and the ground TWR stations is the sum of the DOC range and the radio horizon of the VOLMET station and the sum of the DOC range and the radio horizon of the TWR service:

260 NM + 260 NM +25 NM +78 NM = 623 NM.

To secure compatibility between both stations / services, the minimum separation distance between the two stations needs to be 633 NM.

Note: In these cases the program SEARCH FREQUENCY shows the interference caused by the TWR service into the VOLMET service. The TWR service is printed on the map as a protected service.

2.9.1.3		Minimum separation distances for aerodrome surface communications (AS) are calculated assuming a designated operational range for AS communications of 10 NM and a designated operational height of 150 ft. This results in a minimum co-frequency separation distance of 50 NM. Should the difference in height between the two aerodromes be significantly different, additional margins may need to be added. Separation distances (between facilities) providing air/ground communications operating on the same frequency as the aerodrome communications service have been calculated as the sum of 25 NM (AS) plus the radio horizon plus DOC-range of the air/ground communication service; (see paragraph 2.7.3.1.1). In case the airborne service is an area service (ACC or FIS), only the distance of the radio horizon to the nearest limit of the airborne service has been provided (25 NM (AS plus DOC range airborne service) should apply. Sharing of frequencies with aerodrome surface communications and air/ground communication services is unlikely to occur since an (exclusive) sub-band has been allotted by ICAO for AS communication (121.600-121.975 MHz).

---------------

Appendix A	Aeronautical propagation curves for 125 MHz,  300 MHz, 1200 MHz and 5100 MHz (Source: Recommendation ITU-R P.528)

Appendix B	Deleted

Appendix C	Deleted

Appendix D	Terms and definitions

Appendix E	Regional frequency allotment plans

Appendix F	Deleted

Appendix G 	Regional frequency utilization table

- Appendix A

Appendix A

Appendix A

Appendix A

Appendix D

Terms and definitions

Designated operational range or height (DOR or DOH) – The range or height to which an aid is needed operationally in order to provide a particular service and within which the facility is afforded frequency protection.

Note 1 – The designated value for range or height is determined in accordance with the criteria for the deployment of the aid in question.

Note 2 – The designated value for range or height forms the basis for the technical planning of aids.

Designated operational coverage (DOC) – The combination of the designated operational range and the designated operational height (e.g. 200NM/FL500 is the designated operational coverage for an aid with a designated operational range of 500 NM and a designated operational height of 50.000 ft (Flight Level 500).

Appendix E

Appendix E

Appendix E

Appendix E

Appendix E

Appendix F

Regional frequency utilization table

| Frequency | Channel | AFI | APAC | CAR | EUR | MID | Appendix G SAM |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 118.0000 | 118.005 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.0000 | 118.000 | TWR | TWR | TWR | TWR, APP | TWR | TWR |
| 118.0083 | 118.010 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.0167 | 118.015 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.0250 | 118.025 | TWR | TWR | TWR | TWR, APP | TWR | TWR |
| 118.0250 | 118.030 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.0333 | 118.035 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.0417 | 118.040 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.0500 | 118.055 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.0500 | 118.050 | TWR | TWR | TWR | TWR, APP | TWR | TWR |
| 118.0583 | 118.060 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.0667 | 118.065 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.0750 | 118.080 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.0750 | 118.075 | TWR | TWR | TWR | TWR, APP | TWR | TWR |
| 118.0833 | 118.085 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.0917 | 118.090 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.1000 | 118.100 | TWR | TWR | TWR | TWR, APP | TWR | TWR |
| 118.1000 | 118.105 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.1083 | 118.110 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.1167 | 118.115 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.1250 | 118.125 | TWR | TWR | TWR | TWR, APP | TWR | TWR |
| 118.1250 | 118.130 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.1333 | 118.135 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.1417 | 118.140 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.1500 | 118.150 | TWR | TWR | TWR | TWR, APP | TWR | TWR |
| 118.1500 | 118.155 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.1583 | 118.160 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.1667 | 118.165 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.1750 | 118.175 | TWR | TWR | TWR | TWR, APP | TWR | TWR |
| 118.1750 | 118.180 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.1833 | 118.185 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.1917 | 118.190 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.2000 | 118.200 | TWR | TWR | TWR | TWR, APP | TWR | TWR |
| 118.2000 | 118.205 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.2083 | 118.210 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.2167 | 118.215 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.2250 | 118.230 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.2250 | 118.225 | TWR | TWR | TWR | TWR, APP | TWR | TWR |
| 118.2333 | 118.235 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.2417 | 118.240 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.2500 | 118.250 | TWR | TWR | TWR | TWR, APP | TWR | TWR |
| 118.2500 | 118.255 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.2583 | 118.260 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.2667 | 118.265 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.2750 | 118.275 | TWR | TWR | TWR | TWR, APP | TWR | TWR |
| 118.2750 | 118.280 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.2833 | 118.285 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.2917 | 118.290 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.3000 | 118.300 | TWR | TWR | TWR | TWR, APP | TWR | TWR |
| 118.3000 | 118.305 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.3083 | 118.310 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.3167 | 118.315 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.3250 | 118.330 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.3250 | 118.325 | TWR | TWR | TWR | TWR, APP | TWR | TWR |
| 118.3333 | 118.335 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.3417 | 118.340 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.3500 | 118.355 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.3500 | 118.350 | TWR | TWR | TWR | TWR, APP | TWR | TWR |
| 118.3583 | 118.360 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.3667 | 118.365 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.3750 | 118.380 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.3750 | 118.375 | TWR | TWR | TWR | TWR, APP | TWR | TWR |
| 118.3833 | 118.385 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.3917 | 118.390 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.4000 | 118.400 | TWR | TWR | TWR | TWR, APP | TWR | TWR |
| 118.4000 | 118.405 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.4083 | 118.410 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.4167 | 118.415 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.4250 | 118.425 | TWR | TWR | TWR | TWR, APP | TWR | TWR |
| 118.4250 | 118.430 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.4333 | 118.435 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.4417 | 118.440 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.4500 | 118.450 | TWR | TWR | TWR | TWR, APP | TWR | TWR |
| 118.4500 | 118.455 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.4583 | 118.460 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.4667 | 118.465 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.4750 | 118.475 | TWR | TWR | TWR | TWR, APP | TWR | TWR |
| 118.4750 | 118.480 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.4833 | 118.485 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.4917 | 118.490 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.5000 | 118.500 | ACC-U | TWR | TWR | TWR, APP | TWR | TWR |
| 118.5000 | 118.505 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.5083 | 118.510 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.5167 | 118.515 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.5250 | 118.525 | ACC-U | TWR | TWR | TWR, APP | TWR | TWR |
| 118.5250 | 118.530 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.5333 | 118.535 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.5417 | 118.540 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.5500 | 118.550 | ACC-U | TWR | TWR | TWR, APP | TWR | TWR |
| 118.5500 | 118.555 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.5583 | 118.560 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.5667 | 118.565 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.5750 | 118.575 | ACC-U | TWR | TWR | TWR, APP | TWR | TWR |
| 118.5750 | 118.580 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.5833 | 118.585 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.5917 | 118.590 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.6000 | 118.600 | TWR | TWR | TWR | TWR, APP | TWR | TWR |
| 118.6000 | 118.605 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.6083 | 118.610 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.6167 | 118.615 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.6250 | 118.625 | TWR | TWR | TWR | TWR, APP | TWR | TWR |
| 118.6250 | 118.630 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.6333 | 118.635 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.6417 | 118.640 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.6500 | 118.650 | TWR | TWR | TWR | TWR, APP | TWR | TWR |
| 118.6500 | 118.655 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.6583 | 118.660 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.6667 | 118.665 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.6750 | 118.675 | TWR | TWR | TWR | TWR, APP | TWR | TWR |
| 118.6750 | 118.680 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.6833 | 118.685 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.6917 | 118.690 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.7000 | 118.700 | TWR | TWR | TWR | TWR, APP | TWR | TWR |
| 118.7000 | 118.705 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.7083 | 118.710 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.7167 | 118.715 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.7250 | 118.725 | TWR | TWR | TWR | TWR, APP | TWR | TWR |
| 118.7250 | 118.730 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.7333 | 118.735 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.7417 | 118.740 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.7500 | 118.750 | TWR | TWR | TWR | TWR, APP | TWR | TWR |
| 118.7500 | 118.755 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.7583 | 118.760 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.7667 | 118.765 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.7750 | 118.775 | TWR | TWR | TWR | TWR, APP | TWR | TWR |
| 118.7750 | 118.780 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.7833 | 118.785 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.7917 | 118.790 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.8000 | 118.800 | TWR | TWR | TWR | TWR, APP | TWR | TWR |
| 118.8000 | 118.805 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.8083 | 118.810 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.8167 | 118.815 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.8250 | 118.825 | TWR | TWR | TWR | TWR, APP | TWR | TWR |
| 118.8250 | 118.830 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.8333 | 118.835 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.8417 | 118.840 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.8500 | 118.850 | TWR | TWR | TWR | TWR, APP | TWR | TWR |
| 118.8500 | 118.855 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.8583 | 118.860 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.8667 | 118.865 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.8750 | 118.875 | TWR | TWR | TWR | TWR, APP | TWR | TWR |
| 118.8750 | 118.880 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.8833 | 118.885 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.8917 | 118.890 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.9000 | 118.900 | TWR | ACC-L, ACC-U | TWR | TWR, APP | ACC-L, ACC-U | TWR |
| 118.9000 | 118.905 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.9083 | 118.910 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.9167 | 118.915 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.9250 | 118.925 | TWR | ACC-L, ACC-U | TWR | TWR, APP | ACC-L, ACC-U | TWR |
| 118.9250 | 118.930 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.9333 | 118.935 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.9417 | 118.940 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.9500 | 118.950 | TWR | ACC-L, ACC-U | Not allotted | TWR, APP | ACC-L, ACC-U | Not allotted |
| 118.9500 | 118.955 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.9583 | 118.960 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.9667 | 118.965 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.9750 | 118.975 | TWR | ACC-L, ACC-U | Not allotted | TWR, APP | ACC-L, ACC-U | Not allotted |
| 118.9750 | 118.980 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.9833 | 118.985 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 118.9917 | 118.990 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.0000 | 119.000 | APP-L | APP-L, APP-I | APP | TWR, APP | APP-L, APP-I | APP |
| 119.0000 | 119.005 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.0083 | 119.010 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.0167 | 119.015 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.0250 | 119.025 | APP-L | APP-L, APP-I | APP | TWR, APP | APP-L, APP-I | APP |
| 119.0250 | 119.030 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.0333 | 119.035 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.0417 | 119.040 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.0500 | 119.050 | APP-L | APP-L, APP-I | APP | TWR, APP | APP-L, APP-I | APP |
| 119.0500 | 119.055 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.0583 | 119.060 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.0667 | 119.065 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.0750 | 119.075 | APP-L | APP-L, APP-I | APP | TWR, APP | APP-L, APP-I | APP |
| 119.0750 | 119.080 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.0833 | 119.085 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.0917 | 119.090 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.1000 | 119.100 | APP-L | APP-L, APP-I | APP | TWR, APP | APP-L, APP-I | APP |
| 119.1000 | 119.105 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.1083 | 119.110 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.1167 | 119.115 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.1250 | 119.125 | APP-L | APP-L, APP-I | APP | TWR, APP | APP-L, APP-I | APP |
| 119.1250 | 119.130 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.1333 | 119.135 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.1417 | 119.140 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.1500 | 119.150 | APP-L | APP-L, APP-I | APP | TWR, APP | APP-L, APP-I | APP |
| 119.1500 | 119.155 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.1583 | 119.160 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.1667 | 119.165 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.1750 | 119.175 | APP-L | APP-L, APP-I | APP | TWR, APP | APP-L, APP-I | APP |
| 119.1750 | 119.180 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.1833 | 119.185 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.1917 | 119.190 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.2000 | 119.200 | APP-L | APP-L, APP-I | APP | TWR, APP | APP-L, APP-I | APP |
| 119.2000 | 119.205 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.2083 | 119.210 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.2167 | 119.215 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.2250 | 119.225 | APP-L | APP-L, APP-I | APP | TWR, APP | APP-L, APP-I | APP |
| 119.2250 | 119.230 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.2333 | 119.235 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.2417 | 119.240 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.2500 | 119.250 | APP-L | APP-L, APP-I | APP | TWR, APP | APP-L, APP-I | APP |
| 119.2500 | 119.255 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.2583 | 119.260 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.2667 | 119.265 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.2750 | 119.275 | APP-L | APP-L, APP-I | APP | TWR, APP | APP-L, APP-I | APP |
| 119.2750 | 119.280 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.2833 | 119.285 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.2917 | 119.290 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.3000 | 119.300 | ACC-U | ACC-L, ACC-U | APP | TWR, APP | ACC-L, ACC-U | APP |
| 119.3000 | 119.305 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.3083 | 119.310 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.3167 | 119.315 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.3250 | 119.325 | ACC-U | ACC-L, ACC-U | APP | TWR, APP | ACC-L, ACC-U | APP |
| 119.3250 | 119.330 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.3333 | 119.335 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.3417 | 119.340 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.3500 | 119.350 | ACC-U | ACC-L, ACC-U | APP | TWR, APP | ACC-L, ACC-U | APP |
| 119.3500 | 119.355 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.3583 | 119.360 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.3667 | 119.365 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.3750 | 119.375 | ACC-U | ACC-L, ACC-U | APP | TWR, APP | ACC-L, ACC-U | APP |
| 119.3750 | 119.380 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.3833 | 119.385 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.3917 | 119.390 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.4000 | 119.400 | APP-L | APP-L, APP-I | APP | TWR, APP | APP-L, APP-I | APP |
| 119.4000 | 119.405 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.4083 | 119.410 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.4167 | 119.415 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.4250 | 119.425 | APP-L | APP-L, APP-I | APP | TWR, APP | APP-L, APP-I | APP |
| 119.4250 | 119.430 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.4333 | 119.435 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.4417 | 119.440 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.4500 | 119.450 | APP-L | APP-L, APP-I | APP | TWR, APP | APP-L, APP-I | APP |
| 119.4500 | 119.455 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.4583 | 119.460 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.4667 | 119.465 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.4750 | 119.475 | APP-L | APP-L, APP-I | APP | TWR, APP | APP-L, APP-I | APP |
| 119.4750 | 119.480 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.4833 | 119.485 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.4917 | 119.490 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.5000 | 119.505 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.5000 | 119.500 | APP-PAR | APP-PAR | APP | TWR, APP | APP-PAR | APP |
| 119.5083 | 119.510 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.5167 | 119.515 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.5250 | 119.525 | APP-PAR | APP-PAR | APP | TWR, APP | APP-PAR | APP |
| 119.5250 | 119.530 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.5333 | 119.535 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.5417 | 119.540 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.5500 | 119.550 | APP-PAR | APP-PAR | APP | TWR, APP | APP-PAR | APP |
| 119.5500 | 119.555 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.5583 | 119.560 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.5667 | 119.565 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.5750 | 119.575 | APP-PAR | APP-PAR | APP | TWR, APP | APP-PAR | APP |
| 119.5750 | 119.580 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.5833 | 119.585 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.5917 | 119.590 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.6000 | 119.600 | APP-L | APP-PAR | APP | TWR, APP | APP-PAR | APP |
| 119.6000 | 119.605 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.6083 | 119.610 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.6167 | 119.615 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.6250 | 119.625 | APP-L | APP-PAR | APP | TWR, APP | APP-PAR | APP |
| 119.6250 | 119.630 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.6333 | 119.635 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.6417 | 119.640 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.6500 | 119.650 | APP-L | APP-PAR | APP | TWR, APP | APP-PAR | APP |
| 119.6500 | 119.655 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.6583 | 119.660 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.6667 | 119.665 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.6750 | 119.675 | APP-L | APP-PAR | APP | TWR, APP | APP-PAR | APP |
| 119.6750 | 119.680 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.6833 | 119.685 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.6917 | 119.690 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.7000 | 119.700 | APP-L | APP-L, APP-I | APP | RGA (TWR, APP) | APP-L, APP-I | APP |
| 119.7000 | 119.705 | Not used | Not used | Not used | RGA (TWR, APP) | Not used | Not used |
| 119.7083 | 119.710 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.7167 | 119.715 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.7250 | 119.725 | APP-L | APP-L, APP-I | APP | TWR, APP | APP-L, APP-I | APP |
| 119.7250 | 119.730 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.7333 | 119.735 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.7417 | 119.740 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.7500 | 119.750 | APP-L | APP-L, APP-I | APP | TWR, APP | APP-L, APP-I | APP |
| 119.7500 | 119.755 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.7583 | 119.760 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.7667 | 119.765 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.7750 | 119.775 | APP-L | APP-L, APP-I | APP | TWR, APP | APP-L, APP-I | APP |
| 119.7750 | 119.780 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.7833 | 119.785 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.7917 | 119.790 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.8000 | 119.800 | APP-L | APP-PAR | APP | TWR, APP | APP-PAR | APP |
| 119.8000 | 119.805 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.8083 | 119.810 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.8167 | 119.815 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.8250 | 119.825 | APP-L | APP-PAR | APP | TWR, APP | APP-PAR | APP |
| 119.8250 | 119.830 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.8333 | 119.835 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.8417 | 119.840 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.8500 | 119.850 | APP-L | APP-PAR | APP | TWR, APP | APP-PAR | APP |
| 119.8500 | 119.855 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.8583 | 119.860 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.8667 | 119.865 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.8750 | 119.875 | APP-L | APP-PAR | APP | TWR, APP | APP-PAR | APP |
| 119.8750 | 119.880 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.8833 | 119.885 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.8917 | 119.890 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.9000 | 119.900 | APP-PAR | APP-PAR | APP | TWR, APP | APP-PAR | APP |
| 119.9000 | 119.905 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.9083 | 119.910 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.9167 | 119.915 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.9250 | 119.930 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.9250 | 119.925 | APP-PAR | APP-PAR | APP | TWR, APP | APP-PAR | APP |
| 119.9333 | 119.935 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.9417 | 119.940 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.9500 | 119.950 | APP-PAR | APP-PAR | APP | TWR, APP | APP-PAR | APP |
| 119.9500 | 119.955 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.9583 | 119.960 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.9667 | 119.965 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.9750 | 119.975 | APP-PAR | APP-PAR | APP | TWR, APP | APP-PAR | APP |
| 119.9750 | 119.980 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.9833 | 119.985 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 119.9917 | 119.990 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.0000 | 120.000 | APP-I | APP-L, APP-I | APP | TWR, APP | APP-L, APP-I | APP |
| 120.0000 | 120.005 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.0083 | 120.010 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.0167 | 120.015 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.0250 | 120.025 | APP-I | APP-L, APP-I | APP | TWR, APP | APP-L, APP-I | APP |
| 120.0250 | 120.030 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.0333 | 120.035 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.0417 | 120.040 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.0500 | 120.055 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.0500 | 120.050 | APP-I | APP-L, APP-I | APP | TWR, APP | APP-L, APP-I | APP |
| 120.0583 | 120.060 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.0667 | 120.065 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.0750 | 120.075 | APP-I | APP-L, APP-I | APP | TWR, APP | APP-L, APP-I | APP |
| 120.0750 | 120.080 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.0833 | 120.085 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.0917 | 120.090 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.1000 | 120.100 | APP-PAR | FIS-L, FIS-U | APP | TWR, APP | FIS-L, FIS-U | APP |
| 120.1000 | 120.105 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.1083 | 120.110 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.1167 | 120.115 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.1250 | 120.125 | APP-PAR | FIS-L, FIS-U | APP | TWR, APP | FIS-L, FIS-U | APP |
| 120.1250 | 120.130 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.1333 | 120.135 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.1417 | 120.140 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.1500 | 120.150 | APP-PAR | FIS-L, FIS-U | APP | TWR, APP | FIS-L, FIS-U | APP |
| 120.1500 | 120.155 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.1583 | 120.160 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.1667 | 120.165 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.1750 | 120.175 | APP-PAR | FIS-L, FIS-U | APP | TWR, APP | FIS-L, FIS-U | APP |
| 120.1750 | 120.180 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.1833 | 120.185 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.1917 | 120.190 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.2000 | 120.200 | Not allotted | APP-L, APP-I | APP | TWR, APP | APP-L, APP-I | APP |
| 120.2000 | 120.205 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.2083 | 120.210 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.2167 | 120.215 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.2250 | 120.225 | Not allotted | APP-L, APP-I | APP | TWR, APP | APP-L, APP-I | APP |
| 120.2250 | 120.230 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.2333 | 120.235 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.2417 | 120.240 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.2500 | 120.250 | Not allotted | APP-L, APP-I | APP | TWR, APP | APP-L, APP-I | APP |
| 120.2500 | 120.255 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.2583 | 120.260 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.2667 | 120.265 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.2750 | 120.275 | Not allotted | APP-L, APP-I | APP | TWR, APP | APP-L, APP-I | APP |
| 120.2750 | 120.280 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.2833 | 120.285 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.2917 | 120.290 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.3000 | 120.300 | APP-I | APP-U | APP | TWR, APP | APP-U | APP |
| 120.3000 | 120.305 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.3083 | 120.310 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.3167 | 120.315 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.3250 | 120.325 | APP-I | APP-U | APP | TWR, APP | APP-U | APP |
| 120.3250 | 120.330 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.3333 | 120.335 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.3417 | 120.340 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.3500 | 120.350 | APP-I | APP-U | APP | TWR, APP | APP-U | APP |
| 120.3500 | 120.355 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.3583 | 120.360 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.3667 | 120.365 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.3750 | 120.375 | APP-I | APP-U | APP | TWR, APP | APP-U | APP |
| 120.3750 | 120.380 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.3833 | 120.385 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.3917 | 120.390 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.4000 | 120.400 | APP-I | APP-L, APP-I | APP | TWR, APP | APP-L, APP-I | APP |
| 120.4000 | 120.405 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.4083 | 120.410 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.4167 | 120.415 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.4250 | 120.425 | APP-I | APP-L, APP-I | APP | TWR, APP | APP-L, APP-I | APP |
| 120.4250 | 120.430 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.4333 | 120.435 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.4417 | 120.440 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.4500 | 120.450 | APP-I | APP-L, APP-I | APP | TWR, APP | APP-L, APP-I | APP |
| 120.4500 | 120.455 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.4583 | 120.460 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.4667 | 120.465 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.4750 | 120.475 | APP-I | APP-L, APP-I | APP | TWR, APP | APP-L, APP-I | APP |
| 120.4750 | 120.480 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.4833 | 120.485 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.4917 | 120.490 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.5000 | 120.500 | ACC-U | ACC-L, ACC-U | APP | TWR, APP | ACC-L, ACC-U | APP |
| 120.5000 | 120.505 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.5083 | 120.510 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.5167 | 120.515 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.5250 | 120.525 | ACC-U | ACC-L, ACC-U | APP | TWR, APP | ACC-L, ACC-U | APP |
| 120.5250 | 120.530 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.5333 | 120.535 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.5417 | 120.540 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.5500 | 120.550 | ACC-U | ACC-L, ACC-U | APP | TWR, APP | ACC-L, ACC-U | APP |
| 120.5500 | 120.555 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.5583 | 120.560 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.5667 | 120.565 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.5750 | 120.575 | ACC-U | ACC-L, ACC-U | APP | TWR, APP | ACC-L, ACC-U | APP |
| 120.5750 | 120.580 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.5833 | 120.585 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.5917 | 120.590 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.6000 | 120.600 | ACC-U | APP-L, APP-I | APP | TWR, APP | APP-L, APP-I | APP |
| 120.6000 | 120.605 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.6083 | 120.610 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.6167 | 120.615 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.6250 | 120.625 | ACC-U | APP-L, APP-I | APP | TWR, APP | APP-L, APP-I | APP |
| 120.6250 | 120.630 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.6333 | 120.635 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.6417 | 120.640 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.6500 | 120.650 | ACC-U | APP-L, APP-I | APP | TWR, APP | APP-L, APP-I | APP |
| 120.6500 | 120.655 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.6583 | 120.660 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.6667 | 120.665 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.6750 | 120.675 | ACC-U | APP-L, APP-I | APP | TWR, APP | APP-L, APP-I | APP |
| 120.6750 | 120.680 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.6833 | 120.685 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.6917 | 120.690 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.7000 | 120.700 | APP-I | ACC-L, ACC-U | APP | TWR, APP | ACC-L, ACC-U | APP |
| 120.7000 | 120.705 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.7083 | 120.710 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.7167 | 120.715 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.7250 | 120.725 | APP-I | ACC-L, ACC-U | APP | TWR, APP | ACC-L, ACC-U | APP |
| 120.7250 | 120.730 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.7333 | 120.735 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.7417 | 120.740 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.7500 | 120.750 | APP-I | ACC-L, ACC-U | APP | TWR, APP | ACC-L, ACC-U | APP |
| 120.7500 | 120.755 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.7583 | 120.760 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.7667 | 120.765 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.7750 | 120.775 | APP-I | ACC-L, ACC-U | APP | TWR, APP | ACC-L, ACC-U | APP |
| 120.7750 | 120.780 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.7833 | 120.785 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.7917 | 120.790 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.8000 | 120.800 | TWR | APP-L, APP-I | APP | TWR, APP | APP-L, APP-I | APP |
| 120.8000 | 120.805 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.8083 | 120.810 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.8167 | 120.815 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.8250 | 120.825 | TWR | APP-L, APP-I | APP | TWR, APP | APP-L, APP-I | APP |
| 120.8250 | 120.830 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.8333 | 120.835 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.8417 | 120.840 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.8500 | 120.850 | TWR | APP-L, APP-I | APP | TWR, APP | APP-L, APP-I | APP |
| 120.8500 | 120.855 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.8583 | 120.860 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.8667 | 120.865 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.8750 | 120.875 | TWR | APP-L, APP-I | APP | TWR, APP | APP-L, APP-I | APP |
| 120.8750 | 120.880 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.8833 | 120.885 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.8917 | 120.890 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.9000 | 120.900 | ACC-U | ACC-L, ACC-U | APP | TWR, APP | ACC-L, ACC-U | APP |
| 120.9000 | 120.905 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.9083 | 120.910 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.9167 | 120.915 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.9250 | 120.925 | ACC-U | ACC-L, ACC-U | APP | TWR, APP | ACC-L, ACC-U | APP |
| 120.9250 | 120.930 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.9333 | 120.935 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.9417 | 120.940 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.9500 | 120.950 | ACC-U | ACC-L, ACC-U | APP | TWR, APP | ACC-L, ACC-U | APP |
| 120.9500 | 120.955 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.9583 | 120.960 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.9667 | 120.965 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.9750 | 120.980 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.9750 | 120.975 | ACC-U | ACC-L, ACC-U | APP | TWR, APP | ACC-L, ACC-U | APP |
| 120.9833 | 120.985 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 120.9917 | 120.990 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 121.0000 | 121.000 | Not allotted | APP-L, APP-I | APP | TWR, APP | APP-L, APP-I | APP |
| 121.0000 | 121.005 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 121.0083 | 121.010 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 121.0167 | 121.015 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 121.0250 | 121.025 | Not allotted | APP-L, APP-I | APP | TWR, APP | APP-L, APP-I | APP |
| 121.0250 | 121.030 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 121.0333 | 121.035 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 121.0417 | 121.040 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 121.0500 | 121.050 | Not allotted | APP-L, APP-I | APP | TWR, APP | APP-L, APP-I | APP |
| 121.0500 | 121.055 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 121.0583 | 121.060 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 121.0667 | 121.065 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 121.0750 | 121.075 | Not allotted | APP-L, APP-I | APP | TWR, APP | APP-L, APP-I | APP |
| 121.0750 | 121.080 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 121.0833 | 121.085 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 121.0917 | 121.090 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 121.1000 | 121.100 | APP-I | APP-L, APP-I | APP | TWR, APP | APP-L, APP-I | APP |
| 121.1000 | 121.105 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 121.1083 | 121.110 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 121.1167 | 121.115 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 121.1250 | 121.125 | APP-I | APP-L, APP-I | APP | TWR, APP | APP-L, APP-I | APP |
| 121.1250 | 121.130 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 121.1333 | 121.135 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 121.1417 | 121.140 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 121.1500 | 121.150 | APP-I | APP-L, APP-I | APP | TWR, APP | APP-L, APP-I | APP |
| 121.1500 | 121.155 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 121.1583 | 121.160 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 121.1667 | 121.165 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 121.1750 | 121.175 | APP-I | APP-L, APP-I | APP | TWR, APP | APP-L, APP-I | APP |
| 121.1750 | 121.180 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 121.1833 | 121.185 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 121.1917 | 121.190 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 121.2000 | 121.200 | APP-I | APP-L, APP-I | APP | TWR, APP | APP-L, APP-I | APP |
| 121.2000 | 121.205 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 121.2083 | 121.210 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 121.2167 | 121.215 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 121.2250 | 121.225 | APP-I | APP-L, APP-I | APP | TWR, APP | APP-L, APP-I | APP |
| 121.2250 | 121.230 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 121.2333 | 121.235 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 121.2417 | 121.240 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 121.2500 | 121.250 | APP-I | APP-L, APP-I | APP | TWR, APP | APP-L, APP-I | APP |
| 121.2500 | 121.255 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 121.2583 | 121.260 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 121.2667 | 121.265 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 121.2750 | 121.275 | APP-I | APP-L, APP-I | APP | TWR, APP | APP-L, APP-I | APP |
| 121.2750 | 121.280 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 121.2833 | 121.285 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 121.2917 | 121.290 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 121.3000 | 121.300 | APP-I | APP-U | APP | TWR, APP | APP-U | APP |
| 121.3000 | 121.305 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 121.3083 | 121.310 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 121.3167 | 121.315 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 121.3250 | 121.325 | APP-I | APP-U | APP | TWR, APP | APP-U | APP |
| 121.3250 | 121.330 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 121.3333 | 121.335 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 121.3417 | 121.340 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 121.3500 | 121.350 | APP-I | APP-U | APP | TWR, APP | APP-U | APP |
| 121.3500 | 121.355 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 121.3583 | 121.360 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 121.3667 | 121.365 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 121.3750 | 121.375 | APP-I | APP-U | APP | TWR, APP | APP-U | APP |
| 121.3750 | 121.380 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 121.3833 | 121.385 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 121.3917 | 121.390 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 121.4000 | 121.405 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 121.4000 | 121.400 | APP-I | APP-L, APP-I | Not allotted | TWR, APP | APP-L, APP-I | Not allotted |
| 121.4083 | 121.410 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 121.4167 | 121.415 | Not used | Not used | Not used | TWR, APP | Not used | Not used |
| 121.4250 | 121.425 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 121.4250 | 121.430 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 121.4333 | 121.435 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 121.4417 | 121.440 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 121.4500 | 121.450 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 121.4500 | 121.455 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 121.4583 | 121.460 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 121.4667 | 121.465 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 121.4750 | 121.475 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 121.4750 | 121.480 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 121.4833 | 121.485 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 121.4917 | 121.490 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 121.5000 | 121.500 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 121.5000 | 121.505 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 121.5083 | 121.510 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 121.5167 | 121.515 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 121.5250 | 121.525 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 121.5250 | 121.530 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 121.5333 | 121.535 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 121.5417 | 121.540 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 121.5500 | 121.550 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 121.5500 | 121.555 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 121.5583 | 121.560 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 121.5667 | 121.565 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 121.5750 | 121.575 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 121.5750 | 121.580 | Not used | Not used | Not used | AS | Not used | Not used |
| 121.5833 | 121.585 | Not used | Not used | Not used | AS | Not used | Not used |
| 121.5917 | 121.590 | Not used | Not used | Not used | AS | Not used | Not used |
| 121.6000 | 121.600 | AS | AS | AS | AS | AS | AS |
| 121.6000 | 121.605 | Not used | Not used | Not used | AS | Not used | Not used |
| 121.6083 | 121.610 | Not used | Not used | Not used | AS | Not used | Not used |
| 121.6167 | 121.615 | Not used | Not used | Not used | AS | Not used | Not used |
| 121.6250 | 121.630 | Not used | Not used | Not used | AS | Not used | Not used |
| 121.6250 | 121.625 | AS | AS | AS | AS | AS | AS |
| 121.6333 | 121.635 | Not used | Not used | Not used | AS | Not used | Not used |
| 121.6417 | 121.640 | Not used | Not used | Not used | AS | Not used | Not used |
| 121.6500 | 121.650 | AS | AS | AS | AS | AS | AS |
| 121.6500 | 121.655 | Not used | Not used | Not used | AS | Not used | Not used |
| 121.6583 | 121.660 | Not used | Not used | Not used | AS | Not used | Not used |
| 121.6667 | 121.665 | Not used | Not used | Not used | AS | Not used | Not used |
| 121.6750 | 121.675 | AS | AS | AS | AS | AS | AS |
| 121.6750 | 121.680 | Not used | Not used | Not used | AS | Not used | Not used |
| 121.6833 | 121.685 | Not used | Not used | Not used | AS | Not used | Not used |
| 121.6917 | 121.690 | Not used | Not used | Not used | AS | Not used | Not used |
| 121.7000 | 121.700 | AS | AS | AS | AS | AS | AS |
| 121.7000 | 121.705 | Not used | Not used | Not used | AS | Not used | Not used |
| 121.7083 | 121.710 | Not used | Not used | Not used | AS | Not used | Not used |
| 121.7167 | 121.715 | Not used | Not used | Not used | AS | Not used | Not used |
| 121.7250 | 121.725 | AS | AS | AS | AS | AS | AS |
| 121.7250 | 121.730 | Not used | Not used | Not used | AS | Not used | Not used |
| 121.7333 | 121.735 | Not used | Not used | Not used | AS | Not used | Not used |
| 121.7417 | 121.740 | Not used | Not used | Not used | AS | Not used | Not used |
| 121.7500 | 121.750 | AS | AS | AS | AS | AS | AS |
| 121.7500 | 121.755 | Not used | Not used | Not used | AS | Not used | Not used |
| 121.7583 | 121.760 | Not used | Not used | Not used | AS | Not used | Not used |
| 121.7667 | 121.765 | Not used | Not used | Not used | AS | Not used | Not used |
| 121.7750 | 121.775 | AS | AS | AS | AS | AS | AS |
| 121.7750 | 121.780 | Not used | Not used | Not used | AS | Not used | Not used |
| 121.7833 | 121.785 | Not used | Not used | Not used | AS | Not used | Not used |
| 121.7917 | 121.790 | Not used | Not used | Not used | AS | Not used | Not used |
| 121.8000 | 121.800 | AS | AS | AS | AS | AS | AS |
| 121.8000 | 121.805 | Not used | Not used | Not used | AS | Not used | Not used |
| 121.8083 | 121.810 | Not used | Not used | Not used | AS | Not used | Not used |
| 121.8167 | 121.815 | Not used | Not used | Not used | AS | Not used | Not used |
| 121.8250 | 121.825 | AS | AS | AS | AS | AS | AS |
| 121.8250 | 121.830 | Not used | Not used | Not used | AS | Not used | Not used |
| 121.8333 | 121.835 | Not used | Not used | Not used | AS | Not used | Not used |
| 121.8417 | 121.840 | Not used | Not used | Not used | AS | Not used | Not used |
| 121.8500 | 121.850 | AS | AS | AS | AS | AS | AS |
| 121.8500 | 121.855 | Not used | Not used | Not used | AS | Not used | Not used |
| 121.8583 | 121.860 | Not used | Not used | Not used | AS | Not used | Not used |
| 121.8667 | 121.865 | Not used | Not used | Not used | AS | Not used | Not used |
| 121.8750 | 121.875 | AS | AS | AS | AS | AS | AS |
| 121.8750 | 121.880 | Not used | Not used | Not used | AS | Not used | Not used |
| 121.8833 | 121.885 | Not used | Not used | Not used | AS | Not used | Not used |
| 121.8917 | 121.890 | Not used | Not used | Not used | AS | Not used | Not used |
| 121.9000 | 121.900 | AS | AS | AS | AS | AS | AS |
| 121.9000 | 121.905 | Not used | Not used | Not used | AS | Not used | Not used |
| 121.9083 | 121.910 | Not used | Not used | Not used | AS | Not used | Not used |
| 121.9167 | 121.915 | Not used | Not used | Not used | AS | Not used | Not used |
| 121.9250 | 121.925 | AS | AS | AS | AS | AS | AS |
| 121.9250 | 121.930 | Not used | Not used | Not used | AS | Not used | Not used |
| 121.9333 | 121.935 | Not used | Not used | Not used | AS | Not used | Not used |
| 121.9417 | 121.940 | Not used | Not used | Not used | AS | Not used | Not used |
| 121.9500 | 121.950 | AS | AS | AS | AS | AS | AS |
| 121.9500 | 121.955 | Not used | Not used | Not used | AS | Not used | Not used |
| 121.9583 | 121.960 | Not used | Not used | Not used | AS | Not used | Not used |
| 121.9667 | 121.965 | Not used | Not used | Not used | AS | Not used | Not used |
| 121.9750 | 121.975 | AS | AS | AS | AS | AS | AS |
| 121.9750 | 121.980 | Not used | Not used | Not used | AS | Not used | Not used |
| 121.9833 | 121.985 | Not used | Not used | Not used | AS | Not used | Not used |
| 121.9917 | 121.990 | Not used | Not used | Not used | AS | Not used | Not used |
| 122.0000 | 122.000 | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted |
| 122.0000 | 122.005 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.0083 | 122.010 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.0167 | 122.015 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.0250 | 122.025 | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted |
| 122.0250 | 122.030 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.0333 | 122.035 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.0417 | 122.040 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.0500 | 122.050 | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted |
| 122.0500 | 122.055 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.0583 | 122.060 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.0667 | 122.065 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.0750 | 122.075 | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted |
| 122.0750 | 122.080 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.0833 | 122.085 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.0917 | 122.090 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.1000 | 122.100 | Not allotted | Not allotted | Not allotted | RGA TWR, APP | Not allotted | Not allotted |
| 122.1000 | 122.105 | Not used | Not used | Not used | RGA TWR, APP | Not used | Not used |
| 122.1083 | 122.110 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.1167 | 122.115 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.1250 | 122.125 | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted |
| 122.1250 | 122.130 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.1333 | 122.135 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.1417 | 122.140 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.1500 | 122.150 | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted |
| 122.1500 | 122.155 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.1583 | 122.160 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.1667 | 122.165 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.1750 | 122.175 | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted |
| 122.1750 | 122.180 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.1833 | 122.185 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.1917 | 122.190 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.2000 | 122.200 | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted |
| 122.2000 | 122.205 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.2083 | 122.210 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.2167 | 122.215 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.2250 | 122.225 | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted |
| 122.2250 | 122.230 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.2333 | 122.235 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.2417 | 122.240 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.2500 | 122.250 | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted |
| 122.2500 | 122.255 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.2583 | 122.260 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.2667 | 122.265 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.2750 | 122.275 | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted |
| 122.2750 | 122.280 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.2833 | 122.285 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.2917 | 122.290 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.3000 | 122.300 | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted |
| 122.3000 | 122.305 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.3083 | 122.310 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.3167 | 122.315 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.3250 | 122.325 | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted |
| 122.3250 | 122.330 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.3333 | 122.335 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.3417 | 122.340 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.3500 | 122.350 | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted |
| 122.3500 | 122.355 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.3583 | 122.360 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.3667 | 122.365 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.3750 | 122.375 | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted |
| 122.3750 | 122.380 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.3833 | 122.385 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.3917 | 122.390 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.4000 | 122.400 | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted |
| 122.4000 | 122.405 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.4083 | 122.410 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.4167 | 122.415 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.4250 | 122.425 | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted |
| 122.4250 | 122.430 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.4333 | 122.435 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.4417 | 122.440 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.4500 | 122.450 | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted |
| 122.4500 | 122.455 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.4583 | 122.460 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.4667 | 122.465 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.4750 | 122.475 | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted |
| 122.4750 | 122.480 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.4833 | 122.485 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.4917 | 122.490 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.5000 | 122.500 | Not allotted | Not allotted | Not allotted | RLA | Not allotted | Not allotted |
| 122.5000 | 122.505 | Not used | Not used | Not used | RLA | Not used | Not used |
| 122.5083 | 122.510 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.5167 | 122.515 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.5250 | 122.525 | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted |
| 122.5250 | 122.530 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.5333 | 122.535 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.5417 | 122.540 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.5500 | 122.550 | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted |
| 122.5500 | 122.555 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.5583 | 122.560 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.5667 | 122.565 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.5750 | 122.575 | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted |
| 122.5750 | 122.580 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.5833 | 122.585 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.5917 | 122.590 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.6000 | 122.600 | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted |
| 122.6000 | 122.605 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.6083 | 122.610 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.6167 | 122.615 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.6250 | 122.625 | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted |
| 122.6250 | 122.630 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.6333 | 122.635 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.6417 | 122.640 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.6500 | 122.650 | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted |
| 122.6500 | 122.655 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.6583 | 122.660 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.6667 | 122.665 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.6750 | 122.675 | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted |
| 122.6750 | 122.680 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.6833 | 122.685 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.6917 | 122.690 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.7000 | 122.700 | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted |
| 122.7000 | 122.705 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.7083 | 122.710 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.7167 | 122.715 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.7250 | 122.725 | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted |
| 122.7250 | 122.730 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.7333 | 122.735 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.7417 | 122.740 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.7500 | 122.750 | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted |
| 122.7500 | 122.755 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.7583 | 122.760 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.7667 | 122.765 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.7750 | 122.775 | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted |
| 122.7750 | 122.780 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.7833 | 122.785 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.7917 | 122.790 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.8000 | 122.800 | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted |
| 122.8000 | 122.805 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.8083 | 122.810 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.8167 | 122.815 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.8250 | 122.825 | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted |
| 122.8250 | 122.830 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.8333 | 122.835 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.8417 | 122.840 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.8500 | 122.850 | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted |
| 122.8500 | 122.855 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.8583 | 122.860 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.8667 | 122.865 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.8750 | 122.875 | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted |
| 122.8750 | 122.880 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.8833 | 122.885 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.8917 | 122.890 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.9000 | 122.900 | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted |
| 122.9000 | 122.905 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.9083 | 122.910 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.9167 | 122.915 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.9250 | 122.925 | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted |
| 122.9250 | 122.930 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.9333 | 122.935 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.9417 | 122.940 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.9500 | 122.950 | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted |
| 122.9500 | 122.955 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.9583 | 122.960 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.9667 | 122.965 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.9750 | 122.975 | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted |
| 122.9750 | 122.980 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.9833 | 122.985 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 122.9917 | 122.990 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 123.0000 | 123.000 | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted |
| 123.0000 | 123.005 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 123.0083 | 123.010 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 123.0167 | 123.015 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 123.0250 | 123.025 | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted |
| 123.0250 | 123.030 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 123.0333 | 123.035 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 123.0417 | 123.040 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 123.0500 | 123.050 | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted |
| 123.0500 | 123.055 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 123.0583 | 123.060 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 123.0667 | 123.065 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 123.0750 | 123.075 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 123.0750 | 123.080 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 123.0833 | 123.085 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 123.0917 | 123.090 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 123.1000 | 123.100 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 123.1000 | 123.105 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 123.1083 | 123.110 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 123.1167 | 123.115 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 123.1250 | 123.125 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 123.1250 | 123.130 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 123.1333 | 123.135 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 123.1417 | 123.140 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 123.1500 | 123.150 | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted |
| 123.1500 | 123.155 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 123.1583 | 123.160 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 123.1667 | 123.165 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 123.1750 | 123.175 | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted |
| 123.1750 | 123.180 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 123.1833 | 123.185 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 123.1917 | 123.190 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 123.2000 | 123.200 | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted |
| 123.2000 | 123.205 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 123.2083 | 123.210 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 123.2167 | 123.215 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 123.2250 | 123.225 | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted |
| 123.2250 | 123.230 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 123.2333 | 123.235 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 123.2417 | 123.240 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 123.2500 | 123.255 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 123.2500 | 123.250 | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted |
| 123.2583 | 123.260 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 123.2667 | 123.265 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 123.2750 | 123.275 | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted |
| 123.2750 | 123.280 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 123.2833 | 123.285 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 123.2917 | 123.290 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 123.3000 | 123.300 | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted |
| 123.3000 | 123.305 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 123.3083 | 123.310 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 123.3167 | 123.315 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 123.3250 | 123.325 | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted |
| 123.3250 | 123.330 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 123.3333 | 123.335 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 123.3417 | 123.340 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 123.3500 | 123.350 | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted |
| 123.3500 | 123.355 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 123.3583 | 123.360 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 123.3667 | 123.365 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 123.3750 | 123.375 | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted |
| 123.3750 | 123.380 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 123.3833 | 123.385 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 123.3917 | 123.390 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 123.4000 | 123.400 | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted |
| 123.4000 | 123.405 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 123.4083 | 123.410 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 123.4167 | 123.415 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 123.4250 | 123.425 | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted |
| 123.4250 | 123.430 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 123.4333 | 123.435 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 123.4417 | 123.440 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 123.4500 | 123.450 | Air-Air | Air-Air | Air-Air | Not allotted | Air-Air | Air-Air |
| 123.4500 | 123.455 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 123.4583 | 123.460 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 123.4667 | 123.465 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 123.4750 | 123.475 | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted |
| 123.4750 | 123.480 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 123.4833 | 123.485 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 123.4917 | 123.490 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 123.5000 | 123.500 | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted |
| 123.5000 | 123.505 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 123.5083 | 123.510 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 123.5167 | 123.515 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 123.5250 | 123.525 | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted |
| 123.5250 | 123.530 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 123.5333 | 123.535 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 123.5417 | 123.540 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 123.5500 | 123.550 | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted |
| 123.5500 | 123.555 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 123.5583 | 123.560 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 123.5667 | 123.565 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 123.5750 | 123.575 | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted |
| 123.5750 | 123.580 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 123.5833 | 123.585 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 123.5917 | 123.590 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 123.6000 | 123.600 | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted |
| 123.6000 | 123.605 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 123.6083 | 123.610 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 123.6167 | 123.615 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 123.6250 | 123.625 | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted |
| 123.6250 | 123.630 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 123.6333 | 123.635 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 123.6417 | 123.640 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 123.6500 | 123.650 | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted |
| 123.6500 | 123.655 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 123.6583 | 123.660 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 123.6667 | 123.665 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 123.6750 | 123.675 | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted | Not allotted |
| 123.6750 | 123.680 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 123.6833 | 123.685 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 123.6917 | 123.690 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 123.7000 | 123.700 | APP-I | ACC-L, ACC-U | ACC | APP, ACC-L | ACC-L, ACC-U | ACC |
| 123.7000 | 123.705 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 123.7083 | 123.710 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 123.7167 | 123.715 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 123.7250 | 123.725 | APP-I | ACC-L, ACC-U | ACC | APP, ACC-L | ACC-L, ACC-U | ACC |
| 123.7250 | 123.730 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 123.7333 | 123.735 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 123.7417 | 123.740 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 123.7500 | 123.750 | APP-I | ACC-L, ACC-U | ACC | APP, ACC-L | ACC-L, ACC-U | ACC |
| 123.7500 | 123.755 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 123.7583 | 123.760 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 123.7667 | 123.765 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 123.7750 | 123.775 | APP-I | ACC-L, ACC-U | ACC | APP, ACC-L | ACC-L, ACC-U | ACC |
| 123.7750 | 123.780 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 123.7833 | 123.785 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 123.7917 | 123.790 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 123.8000 | 123.800 | ACC-L | APP-L, APP-I | ACC | APP, ACC-L | APP-L, APP-I | ACC |
| 123.8000 | 123.805 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 123.8083 | 123.810 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 123.8167 | 123.815 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 123.8250 | 123.825 | ACC-L | APP-L, APP-I | ACC | APP, ACC-L | APP-L, APP-I | ACC |
| 123.8250 | 123.830 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 123.8333 | 123.835 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 123.8417 | 123.840 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 123.8500 | 123.850 | ACC-L | APP-L, APP-I | ACC | APP, ACC-L | APP-L, APP-I | ACC |
| 123.8500 | 123.855 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 123.8583 | 123.860 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 123.8667 | 123.865 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 123.8750 | 123.875 | ACC-L | APP-L, APP-I | ACC | APP, ACC-L | APP-L, APP-I | ACC |
| 123.8750 | 123.880 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 123.8833 | 123.885 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 123.8917 | 123.890 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 123.9000 | 123.900 | APP-U | FIS-L, FIS-U | ACC | APP, ACC-L | FIS-L, FIS-U | ACC |
| 123.9000 | 123.905 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 123.9083 | 123.910 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 123.9167 | 123.915 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 123.9250 | 123.925 | APP-U | FIS-L, FIS-U | ACC | APP, ACC-L | FIS-L, FIS-U | ACC |
| 123.9250 | 123.930 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 123.9333 | 123.935 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 123.9417 | 123.940 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 123.9500 | 123.950 | APP-U | FIS-L, FIS-U | ACC | APP, ACC-L | FIS-L, FIS-U | ACC |
| 123.9500 | 123.955 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 123.9583 | 123.960 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 123.9667 | 123.965 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 123.9750 | 123.975 | APP-U | FIS-L, FIS-U | ACC | APP, ACC-L | FIS-L, FIS-U | ACC |
| 123.9750 | 123.980 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 123.9833 | 123.985 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 123.9917 | 123.990 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.0000 | 124.000 | APP-I | APP-L, APP-I | ACC | APP, ACC-L | APP-L, APP-I | ACC |
| 124.0000 | 124.005 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.0083 | 124.010 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.0167 | 124.015 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.0250 | 124.025 | APP-I | APP-L, APP-I | ACC | APP, ACC-L | APP-L, APP-I | ACC |
| 124.0250 | 124.030 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.0333 | 124.035 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.0417 | 124.040 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.0500 | 124.050 | APP-I | APP-L, APP-I | ACC | APP, ACC-L | APP-L, APP-I | ACC |
| 124.0500 | 124.055 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.0583 | 124.060 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.0667 | 124.065 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.0750 | 124.075 | APP-I | APP-L, APP-I | ACC | APP, ACC-L | APP-L, APP-I | ACC |
| 124.0750 | 124.080 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.0833 | 124.085 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.0917 | 124.090 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.1000 | 124.100 | Not allotted | FIS-L, FIS-U | ACC | APP, ACC-L | FIS-L, FIS-U | ACC |
| 124.1000 | 124.105 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.1083 | 124.110 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.1167 | 124.115 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.1250 | 124.125 | Not allotted | FIS-L, FIS-U | ACC | APP, ACC-L | FIS-L, FIS-U | ACC |
| 124.1250 | 124.130 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.1333 | 124.135 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.1417 | 124.140 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.1500 | 124.150 | Not allotted | FIS-L, FIS-U | ACC | APP, ACC-L | FIS-L, FIS-U | ACC |
| 124.1500 | 124.155 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.1583 | 124.160 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.1667 | 124.165 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.1750 | 124.175 | Not allotted | FIS-L, FIS-U | ACC | APP, ACC-L | FIS-L, FIS-U | ACC |
| 124.1750 | 124.180 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.1833 | 124.185 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.1917 | 124.190 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.2000 | 124.200 | FIS-L | APP-U | ACC | APP, ACC-L | Not allotted | ACC |
| 124.2000 | 124.205 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.2083 | 124.210 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.2167 | 124.215 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.2250 | 124.225 | FIS-L | APP-U | ACC | APP, ACC-L | Not allotted | ACC |
| 124.2250 | 124.230 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.2333 | 124.235 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.2417 | 124.240 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.2500 | 124.250 | FIS-L | APP-U | ACC | APP, ACC-L | Not allotted | ACC |
| 124.2500 | 124.255 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.2583 | 124.260 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.2667 | 124.265 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.2750 | 124.275 | FIS-L | APP-U | ACC | APP, ACC-L | Not allotted | ACC |
| 124.2750 | 124.280 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.2833 | 124.285 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.2917 | 124.290 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.3000 | 124.300 | APP-I | TWR | ACC | APP, ACC-L | TWR | ACC |
| 124.3000 | 124.305 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.3083 | 124.310 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.3167 | 124.315 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.3250 | 124.325 | APP-I | TWR | ACC | APP, ACC-L | TWR | ACC |
| 124.3250 | 124.330 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.3333 | 124.335 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.3417 | 124.340 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.3500 | 124.350 | APP-I | TWR | ACC | APP, ACC-L | TWR | ACC |
| 124.3500 | 124.355 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.3583 | 124.360 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.3667 | 124.365 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.3750 | 124.375 | APP-I | TWR | ACC | APP, ACC-L | TWR | ACC |
| 124.3750 | 124.380 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.3833 | 124.385 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.3917 | 124.390 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.4000 | 124.400 | APP-U | APP-U | ACC | APP, ACC-L | APP-U | ACC |
| 124.4000 | 124.405 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.4083 | 124.410 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.4167 | 124.415 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.4250 | 124.425 | APP-U | APP-U | ACC | APP, ACC-L | APP-U | ACC |
| 124.4250 | 124.430 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.4333 | 124.435 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.4417 | 124.440 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.4500 | 124.450 | APP-U | APP-U | ACC | APP, ACC-L | APP-U | ACC |
| 124.4500 | 124.455 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.4583 | 124.460 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.4667 | 124.465 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.4750 | 124.475 | APP-U | APP-U | ACC | APP, ACC-L | APP-U | ACC |
| 124.4750 | 124.480 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.4833 | 124.485 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.4917 | 124.490 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.5000 | 124.500 | APP-U | ACC-L, ACC-U | ACC | APP, ACC-L | ACC-L, ACC-U | ACC |
| 124.5000 | 124.505 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.5083 | 124.510 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.5167 | 124.515 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.5250 | 124.525 | APP-U | ACC-L, ACC-U | ACC | APP, ACC-L | ACC-L, ACC-U | ACC |
| 124.5250 | 124.530 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.5333 | 124.535 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.5417 | 124.540 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.5500 | 124.550 | APP-U | ACC-L, ACC-U | ACC | APP, ACC-L | ACC-L, ACC-U | ACC |
| 124.5500 | 124.555 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.5583 | 124.560 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.5667 | 124.565 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.5750 | 124.575 | APP-U | ACC-L, ACC-U | ACC | APP, ACC-L | ACC-L, ACC-U | ACC |
| 124.5750 | 124.580 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.5833 | 124.585 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.5917 | 124.590 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.6000 | 124.600 | ACC-U | APP-U | ACC | APP, ACC-L | APP-U | ACC |
| 124.6000 | 124.605 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.6083 | 124.610 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.6167 | 124.615 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.6250 | 124.625 | ACC-U | APP-U | ACC | APP, ACC-L | APP-U | ACC |
| 124.6250 | 124.630 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.6333 | 124.635 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.6417 | 124.640 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.6500 | 124.650 | ACC-U | APP-U | ACC | APP, ACC-L | APP-U | ACC |
| 124.6500 | 124.655 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.6583 | 124.660 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.6667 | 124.665 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.6750 | 124.675 | ACC-U | APP-U | ACC | APP, ACC-L | APP-U | ACC |
| 124.6750 | 124.680 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.6833 | 124.685 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.6917 | 124.690 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.7000 | 124.700 | ACC-U | APP-L, APP-I | ACC | APP, ACC-L | APP-L, APP-I | ACC |
| 124.7000 | 124.705 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.7083 | 124.710 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.7167 | 124.715 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.7250 | 124.725 | ACC-U | APP-L, APP-I | ACC | APP, ACC-L | APP-L, APP-I | ACC |
| 124.7250 | 124.730 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.7333 | 124.735 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.7417 | 124.740 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.7500 | 124.750 | ACC-U | APP-L, APP-I | ACC | APP, ACC-L | APP-L, APP-I | ACC |
| 124.7500 | 124.755 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.7583 | 124.760 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.7667 | 124.765 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.7750 | 124.775 | ACC-U | APP-L, APP-I | ACC | APP, ACC-L | APP-L, APP-I | ACC |
| 124.7750 | 124.780 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.7833 | 124.785 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.7917 | 124.790 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.8000 | 124.800 | FIS-U (GPS) | APP-U | ACC | APP, ACC-L | APP-U | ACC |
| 124.8000 | 124.805 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.8083 | 124.810 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.8167 | 124.815 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.8250 | 124.825 | FIS-U (GPS) | APP-U | ACC | APP, ACC-L | APP-U | ACC |
| 124.8250 | 124.830 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.8333 | 124.835 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.8417 | 124.840 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.8500 | 124.850 | FIS-U (GPS) | APP-U | ACC | APP, ACC-L | APP-U | ACC |
| 124.8500 | 124.855 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.8583 | 124.860 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.8667 | 124.865 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.8750 | 124.875 | FIS-U (GPS) | APP-U | ACC | APP, ACC-L | APP-U | ACC |
| 124.8750 | 124.880 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.8833 | 124.885 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.8917 | 124.890 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.9000 | 124.900 | APP-U | FIS-L, FIS-U | ACC | APP, ACC-L | FIS-L, FIS-U | ACC |
| 124.9000 | 124.905 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.9083 | 124.910 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.9167 | 124.915 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.9250 | 124.925 | APP-U | FIS-L, FIS-U | ACC | APP, ACC-L | FIS-L, FIS-U | ACC |
| 124.9250 | 124.930 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.9333 | 124.935 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.9417 | 124.940 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.9500 | 124.950 | APP-U | FIS-L, FIS-U | ACC | APP, ACC-L | FIS-L, FIS-U | ACC |
| 124.9500 | 124.955 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.9583 | 124.960 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.9667 | 124.965 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.9750 | 124.975 | APP-U | FIS-L, FIS-U | ACC | APP, ACC-L | FIS-L, FIS-U | ACC |
| 124.9750 | 124.980 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.9833 | 124.985 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 124.9917 | 124.990 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.0000 | 125.000 | Not allotted | APP-U | ACC | APP, ACC-L | APP-U | ACC |
| 125.0000 | 125.005 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.0083 | 125.010 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.0167 | 125.015 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.0250 | 125.025 | Not allotted | APP-U | ACC | APP, ACC-L | APP-U | ACC |
| 125.0250 | 125.030 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.0333 | 125.035 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.0417 | 125.040 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.0500 | 125.050 | Not allotted | APP-U | ACC | APP, ACC-L | APP-U | ACC |
| 125.0500 | 125.055 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.0583 | 125.060 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.0667 | 125.065 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.0750 | 125.075 | Not allotted | APP-U | ACC | APP, ACC-L | APP-U | ACC |
| 125.0750 | 125.080 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.0833 | 125.085 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.0917 | 125.090 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.1000 | 125.100 | ACC-U | APP-L, APP-I | ACC | APP, ACC-L | APP-L, APP-I | ACC |
| 125.1000 | 125.105 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.1083 | 125.110 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.1167 | 125.115 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.1250 | 125.125 | ACC-U | APP-L, APP-I | ACC | APP, ACC-L | APP-L, APP-I | ACC |
| 125.1250 | 125.130 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.1333 | 125.135 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.1417 | 125.140 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.1500 | 125.150 | ACC-U | APP-L, APP-I | ACC | APP, ACC-L | APP-L, APP-I | ACC |
| 125.1500 | 125.155 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.1583 | 125.160 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.1667 | 125.165 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.1750 | 125.175 | ACC-U | APP-L, APP-I | ACC | APP, ACC-L | APP-L, APP-I | ACC |
| 125.1750 | 125.180 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.1833 | 125.185 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.1917 | 125.190 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.2000 | 125.200 | FIS-L | APP-U | ACC | APP, ACC-L | APP-U | ACC |
| 125.2000 | 125.205 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.2083 | 125.210 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.2167 | 125.215 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.2250 | 125.225 | FIS-L | APP-U | ACC | APP, ACC-L | APP-U | ACC |
| 125.2250 | 125.230 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.2333 | 125.235 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.2417 | 125.240 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.2500 | 125.250 | FIS-L | APP-U | ACC | APP, ACC-L | APP-U | ACC |
| 125.2500 | 125.255 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.2583 | 125.260 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.2667 | 125.265 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.2750 | 125.275 | FIS-L | APP-U | ACC | APP, ACC-L | APP-U | ACC |
| 125.2750 | 125.280 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.2833 | 125.285 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.2917 | 125.290 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.3000 | 125.300 | APP-I | ACC-L, ACC-U | ACC | APP, ACC-L | ACC-L, ACC-U | ACC |
| 125.3000 | 125.305 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.3083 | 125.310 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.3167 | 125.315 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.3250 | 125.325 | APP-I | ACC-L, ACC-U | ACC | APP, ACC-L | ACC-L, ACC-U | ACC |
| 125.3250 | 125.330 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.3333 | 125.335 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.3417 | 125.340 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.3500 | 125.350 | APP-I | ACC-L, ACC-U | ACC | APP, ACC-L | ACC-L, ACC-U | ACC |
| 125.3500 | 125.355 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.3583 | 125.360 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.3667 | 125.365 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.3750 | 125.375 | APP-I | ACC-L, ACC-U | ACC | APP, ACC-L | ACC-L, ACC-U | ACC |
| 125.3750 | 125.380 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.3833 | 125.385 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.3917 | 125.390 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.4000 | 125.400 | ACC-L | APP-U | ACC | APP, ACC-L | APP-U | ACC |
| 125.4000 | 125.405 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.4083 | 125.410 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.4167 | 125.415 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.4250 | 125.425 | ACC-L | APP-U | ACC | APP, ACC-L | APP-U | ACC |
| 125.4250 | 125.430 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.4333 | 125.435 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.4417 | 125.440 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.4500 | 125.450 | ACC-L | APP-U | ACC | APP, ACC-L | APP-U | ACC |
| 125.4500 | 125.455 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.4583 | 125.460 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.4667 | 125.465 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.4750 | 125.475 | ACC-L | APP-U | ACC | APP, ACC-L | APP-U | ACC |
| 125.4750 | 125.480 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.4833 | 125.485 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.4917 | 125.490 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.5000 | 125.500 | ACC-U | APP-L, APP-I | ACC | APP, ACC-L | APP-L, APP-I | ACC |
| 125.5000 | 125.505 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.5083 | 125.510 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.5167 | 125.515 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.5250 | 125.525 | ACC-U | APP-L, APP-I | ACC | APP, ACC-L | APP-L, APP-I | ACC |
| 125.5250 | 125.530 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.5333 | 125.535 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.5417 | 125.540 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.5500 | 125.550 | ACC-U | APP-L, APP-I | ACC | APP, ACC-L | APP-L, APP-I | ACC |
| 125.5500 | 125.555 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.5583 | 125.560 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.5667 | 125.565 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.5750 | 125.575 | ACC-U | APP-L, APP-I | ACC | APP, ACC-L | APP-L, APP-I | ACC |
| 125.5750 | 125.580 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.5833 | 125.585 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.5917 | 125.590 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.6000 | 125.600 | ACC-U | APP-U | ACC | APP, ACC-L | APP-U | ACC |
| 125.6000 | 125.605 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.6083 | 125.610 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.6167 | 125.615 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.6250 | 125.625 | ACC-U | APP-U | ACC | APP, ACC-L | APP-U | ACC |
| 125.6250 | 125.630 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.6333 | 125.635 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.6417 | 125.640 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.6500 | 125.650 | ACC-U | APP-U | ACC | APP, ACC-L | APP-U | ACC |
| 125.6500 | 125.655 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.6583 | 125.660 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.6667 | 125.665 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.6750 | 125.675 | ACC-U | APP-U | ACC | APP, ACC-L | APP-U | ACC |
| 125.6750 | 125.680 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.6833 | 125.685 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.6917 | 125.690 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.7000 | 125.700 | APP-U | ACC-L, ACC-U | ACC | APP, ACC-L | ACC-L, ACC-U | ACC |
| 125.7000 | 125.705 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.7083 | 125.710 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.7167 | 125.715 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.7250 | 125.725 | APP-U | ACC-L, ACC-U | ACC | APP, ACC-L | ACC-L, ACC-U | ACC |
| 125.7250 | 125.730 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.7333 | 125.735 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.7417 | 125.740 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.7500 | 125.750 | APP-U | ACC-L, ACC-U | ACC | APP, ACC-L | ACC-L, ACC-U | ACC |
| 125.7500 | 125.755 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.7583 | 125.760 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.7667 | 125.765 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.7750 | 125.775 | APP-U | ACC-L, ACC-U | ACC | APP, ACC-L | ACC-L, ACC-U | ACC |
| 125.7750 | 125.780 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.7833 | 125.785 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.7917 | 125.790 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.8000 | 125.800 | FIS-U (GPS) | APP-U | ACC | APP, ACC-L | APP-U | ACC |
| 125.8000 | 125.805 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.8083 | 125.810 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.8167 | 125.815 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.8250 | 125.825 | FIS-U (GPS) | APP-U | ACC | APP, ACC-L | APP-U | ACC |
| 125.8250 | 125.830 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.8333 | 125.835 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.8417 | 125.840 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.8500 | 125.850 | FIS-U (GPS) | APP-U | ACC | APP, ACC-L | APP-U | ACC |
| 125.8500 | 125.855 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.8583 | 125.860 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.8667 | 125.865 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.8750 | 125.875 | FIS-U (GPS) | APP-U | ACC | APP, ACC-L | APP-U | ACC |
| 125.8750 | 125.880 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.8833 | 125.885 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.8917 | 125.890 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.9000 | 125.900 | ACC-U | ACC-L, ACC-U | ACC | APP, ACC-L | ACC-L, ACC-U | ACC |
| 125.9000 | 125.905 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.9083 | 125.910 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.9167 | 125.915 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.9250 | 125.925 | ACC-U | ACC-L, ACC-U | ACC | APP, ACC-L | ACC-L, ACC-U | ACC |
| 125.9250 | 125.930 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.9333 | 125.935 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.9417 | 125.940 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.9500 | 125.950 | ACC-U | ACC-L, ACC-U | ACC | APP, ACC-L | ACC-L, ACC-U | ACC |
| 125.9500 | 125.955 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.9583 | 125.960 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.9667 | 125.965 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.9750 | 125.975 | ACC-U | ACC-L, ACC-U | ACC | APP, ACC-L | ACC-L, ACC-U | ACC |
| 125.9750 | 125.980 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.9833 | 125.985 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 125.9917 | 125.990 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.0000 | 126.000 | APP-L | APP-U | ACC | APP, ACC-L | APP-U | ACC |
| 126.0000 | 126.005 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.0083 | 126.010 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.0167 | 126.015 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.0250 | 126.025 | APP-L | APP-U | ACC | APP, ACC-L | APP-U | ACC |
| 126.0250 | 126.030 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.0333 | 126.035 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.0417 | 126.040 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.0500 | 126.050 | APP-L | APP-U | ACC | APP, ACC-L | APP-U | ACC |
| 126.0500 | 126.055 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.0583 | 126.060 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.0667 | 126.065 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.0750 | 126.075 | APP-L | APP-U | ACC | APP, ACC-L | APP-U | ACC |
| 126.0750 | 126.080 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.0833 | 126.085 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.0917 | 126.090 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.1000 | 126.100 | ACC-U | ACC-L | ACC | APP, ACC-L | ACC-L | ACC |
| 126.1000 | 126.105 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.1083 | 126.110 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.1167 | 126.115 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.1250 | 126.125 | ACC-U | ACC-L | ACC | APP, ACC-L | ACC-L | ACC |
| 126.1250 | 126.130 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.1333 | 126.135 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.1417 | 126.140 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.1500 | 126.150 | ACC-U | ACC-L | ACC | APP, ACC-L | ACC-L | ACC |
| 126.1500 | 126.155 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.1583 | 126.160 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.1667 | 126.165 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.1750 | 126.175 | ACC-U | ACC-L | ACC | APP, ACC-L | ACC-L | ACC |
| 126.1750 | 126.180 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.1833 | 126.185 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.1917 | 126.190 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.2000 | 126.200 | VOLMET, ATIS | VOLMET, ATIS | ACC | APP, ACC-L | VOLMET, ATIS | ACC |
| 126.2000 | 126.205 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.2083 | 126.210 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.2167 | 126.215 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.2250 | 126.225 | VOLMET, ATIS | VOLMET, ATIS | ACC | APP, ACC-L | VOLMET, ATIS | ACC |
| 126.2250 | 126.230 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.2333 | 126.235 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.2417 | 126.240 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.2500 | 126.250 | VOLMET, ATIS | VOLMET, ATIS | ACC | APP, ACC-L | VOLMET, ATIS | ACC |
| 126.2500 | 126.255 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.2583 | 126.260 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.2667 | 126.265 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.2750 | 126.275 | VOLMET, ATIS | VOLMET, ATIS | ACC | APP, ACC-L | VOLMET, ATIS | ACC |
| 126.2750 | 126.280 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.2833 | 126.285 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.2917 | 126.290 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.3000 | 126.300 | FIS-U (GPS) | APP-U | ACC | APP, ACC-L | APP-U | ACC |
| 126.3000 | 126.305 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.3083 | 126.310 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.3167 | 126.315 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.3250 | 126.325 | FIS-U (GPS) | APP-U | ACC | APP, ACC-L | APP-U | ACC |
| 126.3250 | 126.330 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.3333 | 126.335 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.3417 | 126.340 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.3500 | 126.350 | FIS-U (GPS) | APP-U | ACC | APP, ACC-L | APP-U | ACC |
| 126.3500 | 126.355 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.3583 | 126.360 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.3667 | 126.365 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.3750 | 126.375 | FIS-U (GPS) | APP-U | ACC | APP, ACC-L | APP-U | ACC |
| 126.3750 | 126.380 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.3833 | 126.385 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.3917 | 126.390 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.4000 | 126.400 | VOLMET, ATIS | VOLMET, ATIS | ACC | APP, ACC-L | VOLMET, ATIS | ACC |
| 126.4000 | 126.405 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.4083 | 126.410 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.4167 | 126.415 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.4250 | 126.425 | VOLMET, ATIS | VOLMET, ATIS | ACC | APP, ACC-L | VOLMET, ATIS | ACC |
| 126.4250 | 126.430 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.4333 | 126.435 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.4417 | 126.440 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.4500 | 126.450 | VOLMET, ATIS | VOLMET, ATIS | ACC | APP, ACC-L | VOLMET, ATIS | ACC |
| 126.4500 | 126.455 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.4583 | 126.460 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.4667 | 126.465 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.4750 | 126.475 | VOLMET, ATIS | VOLMET, ATIS | ACC | APP, ACC-L | VOLMET, ATIS | ACC |
| 126.4750 | 126.480 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.4833 | 126.485 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.4917 | 126.490 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.5000 | 126.500 | ACC-U | APP-L, APP-I | ACC | APP, ACC-L | APP-L, APP-I | ACC |
| 126.5000 | 126.505 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.5083 | 126.510 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.5167 | 126.515 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.5250 | 126.525 | ACC-U | APP-L, APP-I | ACC | APP, ACC-L | APP-L, APP-I | ACC |
| 126.5250 | 126.530 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.5333 | 126.535 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.5417 | 126.540 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.5500 | 126.550 | ACC-U | APP-L, APP-I | ACC | APP, ACC-L | APP-L, APP-I | ACC |
| 126.5500 | 126.555 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.5583 | 126.560 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.5667 | 126.565 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.5750 | 126.575 | ACC-U | APP-L, APP-I | ACC | APP, ACC-L | APP-L, APP-I | ACC |
| 126.5750 | 126.580 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.5833 | 126.585 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.5917 | 126.590 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.6000 | 126.600 | VOLMET, ATIS | VOLMET, ATIS | ACC | APP, ACC-L | VOLMET, ATIS | ACC |
| 126.6000 | 126.605 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.6083 | 126.610 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.6167 | 126.615 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.6250 | 126.625 | VOLMET, ATIS | VOLMET, ATIS | ACC | APP, ACC-L | VOLMET, ATIS | ACC |
| 126.6250 | 126.630 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.6333 | 126.635 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.6417 | 126.640 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.6500 | 126.650 | VOLMET, ATIS | VOLMET, ATIS | ACC | APP, ACC-L | VOLMET, ATIS | ACC |
| 126.6500 | 126.655 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.6583 | 126.660 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.6667 | 126.665 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.6750 | 126.675 | VOLMET, ATIS | VOLMET, ATIS | ACC | APP, ACC-L | VOLMET, ATIS | ACC |
| 126.6750 | 126.680 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.6833 | 126.685 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.6917 | 126.690 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.7000 | 126.700 | ACC-U | FIS-L, FIS-U | GPS | APP, ACC-L | FIS-L, FIS-U | GPS |
| 126.7000 | 126.705 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.7083 | 126.710 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.7167 | 126.715 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.7250 | 126.725 | ACC-U | FIS-L, FIS-U | GPS | APP, ACC-L | FIS-L, FIS-U | GPS |
| 126.7250 | 126.730 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.7333 | 126.735 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.7417 | 126.740 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.7500 | 126.750 | ACC-U | FIS-L, FIS-U | GPS | APP, ACC-L | FIS-L, FIS-U | GPS |
| 126.7500 | 126.755 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.7583 | 126.760 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.7667 | 126.765 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.7750 | 126.775 | ACC-U | FIS-L, FIS-U | GPS | APP, ACC-L | FIS-L, FIS-U | GPS |
| 126.7750 | 126.780 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.7833 | 126.785 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.7917 | 126.790 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.8000 | 126.800 | VOLMET, ATIS | VOLMET, ATIS | GPS | APP, ACC-L | VOLMET, ATIS | GPS |
| 126.8000 | 126.805 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.8083 | 126.810 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.8167 | 126.815 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.8250 | 126.825 | VOLMET, ATIS | VOLMET, ATIS | GPS | APP, ACC-L | VOLMET, ATIS | GPS |
| 126.8250 | 126.830 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.8333 | 126.835 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.8417 | 126.840 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.8500 | 126.850 | VOLMET, ATIS | VOLMET, ATIS | GPS | APP, ACC-L | VOLMET, ATIS | GPS |
| 126.8500 | 126.855 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.8583 | 126.860 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.8667 | 126.865 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.8750 | 126.875 | VOLMET, ATIS | VOLMET, ATIS | GPS | APP, ACC-L | VOLMET, ATIS | GPS |
| 126.8750 | 126.880 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.8833 | 126.885 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.8917 | 126.890 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.9000 | 126.900 | FIS-U (GPS) | FIS-L, FIS-U | GPS | APP, ACC-L | FIS-L, FIS-U | GPS |
| 126.9000 | 126.905 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.9083 | 126.910 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.9167 | 126.915 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.9250 | 126.925 | FIS-U (GPS) | FIS-L, FIS-U | GPS | APP, ACC-L | FIS-L, FIS-U | GPS |
| 126.9250 | 126.930 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.9333 | 126.935 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.9417 | 126.940 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.9500 | 126.950 | FIS-U (GPS) | FIS-L, FIS-U | GPS | APP, ACC-L | FIS-L, FIS-U | GPS |
| 126.9500 | 126.955 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.9583 | 126.960 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.9667 | 126.965 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.9750 | 126.975 | FIS-U (GPS) | FIS-L, FIS-U | GPS | APP, ACC-L | FIS-L, FIS-U | GPS |
| 126.9750 | 126.980 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.9833 | 126.985 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 126.9917 | 126.990 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.0000 | 127.000 | VOLMET, ATIS | VOLMET, ATIS | GPS | APP, ACC-L | VOLMET, ATIS | GPS |
| 127.0000 | 127.005 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.0083 | 127.010 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.0167 | 127.015 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.0250 | 127.025 | VOLMET, ATIS | VOLMET, ATIS | GPS | APP, ACC-L | VOLMET, ATIS | GPS |
| 127.0250 | 127.030 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.0333 | 127.035 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.0417 | 127.040 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.0500 | 127.050 | VOLMET, ATIS | VOLMET, ATIS | GPS | APP, ACC-L | VOLMET, ATIS | GPS |
| 127.0500 | 127.055 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.0583 | 127.060 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.0667 | 127.065 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.0750 | 127.075 | VOLMET, ATIS | VOLMET, ATIS | GPS | APP, ACC-L | VOLMET, ATIS | GPS |
| 127.0750 | 127.080 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.0833 | 127.085 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.0917 | 127.090 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.1000 | 127.100 | ACC-U | FIS-L, FIS-U | GPS | APP, ACC-L | FIS-L, FIS-U | GPS |
| 127.1000 | 127.105 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.1083 | 127.110 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.1167 | 127.115 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.1250 | 127.125 | ACC-U | FIS-L, FIS-U | GPS | APP, ACC-L | FIS-L, FIS-U | GPS |
| 127.1250 | 127.130 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.1333 | 127.135 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.1417 | 127.140 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.1500 | 127.150 | ACC-U | FIS-L, FIS-U | GPS | APP, ACC-L | FIS-L, FIS-U | GPS |
| 127.1500 | 127.155 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.1583 | 127.160 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.1667 | 127.165 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.1750 | 127.175 | ACC-U | FIS-L, FIS-U | GPS | APP, ACC-L | FIS-L, FIS-U | GPS |
| 127.1750 | 127.180 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.1833 | 127.185 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.1917 | 127.190 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.2000 | 127.200 | APP-U | VOLMET, ATIS | GPS | APP, ACC-L | VOLMET, ATIS | GPS |
| 127.2000 | 127.205 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.2083 | 127.210 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.2167 | 127.215 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.2250 | 127.225 | APP-U | VOLMET, ATIS | GPS | APP, ACC-L | VOLMET, ATIS | GPS |
| 127.2250 | 127.230 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.2333 | 127.235 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.2417 | 127.240 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.2500 | 127.250 | APP-U | VOLMET, ATIS | GPS | APP, ACC-L | VOLMET, ATIS | GPS |
| 127.2500 | 127.255 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.2583 | 127.260 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.2667 | 127.265 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.2750 | 127.275 | APP-U | VOLMET, ATIS | GPS | APP, ACC-L | VOLMET, ATIS | GPS |
| 127.2750 | 127.280 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.2833 | 127.285 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.2917 | 127.290 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.3000 | 127.300 | ACC-U | FIS-L, FIS-U | GPS | APP, ACC-L | FIS-L, FIS-U | GPS |
| 127.3000 | 127.305 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.3083 | 127.310 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.3167 | 127.315 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.3250 | 127.325 | ACC-U | FIS-L, FIS-U | GPS | APP, ACC-L | FIS-L, FIS-U | GPS |
| 127.3250 | 127.330 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.3333 | 127.335 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.3417 | 127.340 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.3500 | 127.350 | ACC-U | FIS-L, FIS-U | GPS | APP, ACC-L | FIS-L, FIS-U | GPS |
| 127.3500 | 127.355 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.3583 | 127.360 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.3667 | 127.365 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.3750 | 127.375 | ACC-U | FIS-L, FIS-U | GPS | APP, ACC-L | FIS-L, FIS-U | GPS |
| 127.3750 | 127.380 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.3833 | 127.385 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.3917 | 127.390 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.4000 | 127.400 | FIS-U (GPS) | VOLMET, ATIS | GPS | APP, ACC-L | VOLMET, ATIS | GPS |
| 127.4000 | 127.405 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.4083 | 127.410 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.4167 | 127.415 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.4250 | 127.425 | FIS-U (GPS) | VOLMET, ATIS | GPS | APP, ACC-L | VOLMET, ATIS | GPS |
| 127.4250 | 127.430 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.4333 | 127.435 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.4417 | 127.440 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.4500 | 127.450 | FIS-U (GPS) | VOLMET, ATIS | GPS | APP, ACC-L | VOLMET, ATIS | GPS |
| 127.4500 | 127.455 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.4583 | 127.460 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.4667 | 127.465 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.4750 | 127.475 | FIS-U (GPS) | VOLMET, ATIS | GPS | APP, ACC-L | VOLMET, ATIS | GPS |
| 127.4750 | 127.480 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.4833 | 127.485 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.4917 | 127.490 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.5000 | 127.500 | FIS-L | ACC-L | GPS | APP, ACC-L | ACC-L | GPS |
| 127.5000 | 127.505 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.5083 | 127.510 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.5167 | 127.515 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.5250 | 127.525 | FIS-L | ACC-L | GPS | APP, ACC-L | ACC-L | GPS |
| 127.5250 | 127.530 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.5333 | 127.535 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.5417 | 127.540 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.5500 | 127.550 | FIS-L | ACC-L | GPS | APP, ACC-L | ACC-L | GPS |
| 127.5500 | 127.555 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.5583 | 127.560 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.5667 | 127.565 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.5750 | 127.575 | FIS-L | ACC-L | GPS | APP, ACC-L | ACC-L | GPS |
| 127.5750 | 127.580 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.5833 | 127.585 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.5917 | 127.590 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.6000 | 127.600 | VOLMET, ATIS | VOLMET, ATIS | VOLMET, ATIS | APP, ACC-L | VOLMET, ATIS | VOLMET, ATIS |
| 127.6000 | 127.605 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.6083 | 127.610 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.6167 | 127.615 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.6250 | 127.625 | VOLMET, ATIS | VOLMET, ATIS | VOLMET, ATIS | APP, ACC-L | VOLMET, ATIS | VOLMET, ATIS |
| 127.6250 | 127.630 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.6333 | 127.635 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.6417 | 127.640 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.6500 | 127.650 | VOLMET, ATIS | VOLMET, ATIS | VOLMET, ATIS | APP, ACC-L | VOLMET, ATIS | VOLMET, ATIS |
| 127.6500 | 127.655 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.6583 | 127.660 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.6667 | 127.665 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.6750 | 127.675 | VOLMET, ATIS | VOLMET, ATIS | VOLMET, ATIS | APP, ACC-L | VOLMET, ATIS | VOLMET, ATIS |
| 127.6750 | 127.680 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.6833 | 127.685 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.6917 | 127.690 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.7000 | 127.700 | ACC-U | APP-L, APP-I | VOLMET, ATIS | APP, ACC-L | APP-L, APP-I | VOLMET, ATIS |
| 127.7000 | 127.705 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.7083 | 127.710 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.7167 | 127.715 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.7250 | 127.725 | ACC-U | APP-L, APP-I | VOLMET, ATIS | APP, ACC-L | APP-L, APP-I | VOLMET, ATIS |
| 127.7250 | 127.730 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.7333 | 127.735 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.7417 | 127.740 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.7500 | 127.750 | ACC-U | APP-L, APP-I | VOLMET, ATIS | APP, ACC-L | APP-L, APP-I | VOLMET, ATIS |
| 127.7500 | 127.755 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.7583 | 127.760 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.7667 | 127.765 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.7750 | 127.775 | ACC-U | APP-L, APP-I | VOLMET, ATIS | APP, ACC-L | APP-L, APP-I | VOLMET, ATIS |
| 127.7750 | 127.780 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.7833 | 127.785 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.7917 | 127.790 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.8000 | 127.800 | APP-U | VOLMET, ATIS | VOLMET, ATIS | APP, ACC-L | VOLMET, ATIS | VOLMET, ATIS |
| 127.8000 | 127.805 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.8083 | 127.810 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.8167 | 127.815 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.8250 | 127.825 | APP-U | VOLMET, ATIS | VOLMET, ATIS | APP, ACC-L | VOLMET, ATIS | VOLMET, ATIS |
| 127.8250 | 127.830 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.8333 | 127.835 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.8417 | 127.840 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.8500 | 127.850 | APP-U | VOLMET, ATIS | VOLMET, ATIS | APP, ACC-L | VOLMET, ATIS | VOLMET, ATIS |
| 127.8500 | 127.855 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.8583 | 127.860 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.8667 | 127.865 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.8750 | 127.875 | APP-U | VOLMET, ATIS | VOLMET, ATIS | APP, ACC-L | VOLMET, ATIS | VOLMET, ATIS |
| 127.8750 | 127.880 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.8833 | 127.885 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.8917 | 127.890 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.9000 | 127.900 | Not allotted | APP-L, APP-I | VOLMET, ATIS | APP, ACC-L | APP-L, APP-I | VOLMET, ATIS |
| 127.9000 | 127.905 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.9083 | 127.910 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.9167 | 127.915 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.9250 | 127.925 | Not allotted | APP-L, APP-I | Not allotted | APP, ACC-L | APP-L, APP-I | Not allotted |
| 127.9250 | 127.930 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.9333 | 127.935 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.9417 | 127.940 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.9500 | 127.950 | Not allotted | APP-L, APP-I | ACC | APP, ACC-L | APP-L, APP-I | ACC |
| 127.9500 | 127.955 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.9583 | 127.960 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.9667 | 127.965 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.9750 | 127.975 | Not allotted | APP-L, APP-I | ACC | APP, ACC-L | APP-L, APP-I | ACC |
| 127.9750 | 127.980 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.9833 | 127.985 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 127.9917 | 127.990 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.0000 | 128.000 | APP-U | VOLMET, ATIS | ACC | APP, ACC-L | VOLMET, ATIS | ACC |
| 128.0000 | 128.005 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.0083 | 128.010 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.0167 | 128.015 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.0250 | 128.025 | APP-U | VOLMET, ATIS | ACC | APP, ACC-L | VOLMET, ATIS | ACC |
| 128.0250 | 128.030 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.0333 | 128.035 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.0417 | 128.040 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.0500 | 128.050 | APP-U | VOLMET, ATIS | ACC | APP, ACC-L | VOLMET, ATIS | ACC |
| 128.0500 | 128.055 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.0583 | 128.060 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.0667 | 128.065 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.0750 | 128.075 | APP-U | VOLMET, ATIS | ACC | APP, ACC-L | VOLMET, ATIS | ACC |
| 128.0750 | 128.080 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.0833 | 128.085 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.0917 | 128.090 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.1000 | 128.100 | ACC-U | ACC-L, ACC-U | ACC | APP, ACC-L | ACC-L, ACC-U | ACC |
| 128.1000 | 128.105 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.1083 | 128.110 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.1167 | 128.115 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.1250 | 128.125 | ACC-U | ACC-L, ACC-U | ACC | APP, ACC-L | ACC-L, ACC-U | ACC |
| 128.1250 | 128.130 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.1333 | 128.135 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.1417 | 128.140 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.1500 | 128.150 | ACC-U | ACC-L, ACC-U | ACC | APP, ACC-L | ACC-L, ACC-U | ACC |
| 128.1500 | 128.155 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.1583 | 128.160 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.1667 | 128.165 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.1750 | 128.175 | ACC-U | ACC-L, ACC-U | ACC | APP, ACC-L | ACC-L, ACC-U | ACC |
| 128.1750 | 128.180 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.1833 | 128.185 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.1917 | 128.190 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.2000 | 128.200 | APP-U | VOLMET, ATIS | ACC | APP, ACC-L | VOLMET, ATIS | ACC |
| 128.2000 | 128.205 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.2083 | 128.210 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.2167 | 128.215 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.2250 | 128.225 | APP-U | VOLMET, ATIS | ACC | APP, ACC-L | VOLMET, ATIS | ACC |
| 128.2250 | 128.230 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.2333 | 128.235 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.2417 | 128.240 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.2500 | 128.250 | APP-U | VOLMET, ATIS | ACC | APP, ACC-L | VOLMET, ATIS | ACC |
| 128.2500 | 128.255 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.2583 | 128.260 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.2667 | 128.265 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.2750 | 128.275 | APP-U | VOLMET, ATIS | ACC | APP, ACC-L | VOLMET, ATIS | ACC |
| 128.2750 | 128.280 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.2833 | 128.285 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.2917 | 128.290 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.3000 | 128.300 | ACC-U | ACC-L | ACC | APP, ACC-L | ACC-L | ACC |
| 128.3000 | 128.305 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.3083 | 128.310 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.3167 | 128.315 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.3250 | 128.325 | ACC-U | ACC-L | ACC | APP, ACC-L | ACC-L | ACC |
| 128.3250 | 128.330 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.3333 | 128.335 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.3417 | 128.340 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.3500 | 128.350 | ACC-U | ACC-L | ACC | APP, ACC-L | ACC-L | ACC |
| 128.3500 | 128.355 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.3583 | 128.360 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.3667 | 128.365 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.3750 | 128.375 | ACC-U | ACC-L | ACC | APP, ACC-L | ACC-L | ACC |
| 128.3750 | 128.380 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.3833 | 128.385 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.3917 | 128.390 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.4000 | 128.400 | ACC-L | VOLMET, ATIS | ACC | APP, ACC-L | VOLMET, ATIS | ACC |
| 128.4000 | 128.405 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.4083 | 128.410 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.4167 | 128.415 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.4250 | 128.425 | ACC-L | VOLMET, ATIS | ACC | APP, ACC-L | VOLMET, ATIS | ACC |
| 128.4250 | 128.430 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.4333 | 128.435 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.4417 | 128.440 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.4500 | 128.450 | ACC-L | VOLMET, ATIS | ACC | APP, ACC-L | VOLMET, ATIS | ACC |
| 128.4500 | 128.455 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.4583 | 128.460 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.4667 | 128.465 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.4750 | 128.475 | ACC-L | VOLMET, ATIS | ACC | APP, ACC-L | VOLMET, ATIS | ACC |
| 128.4750 | 128.480 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.4833 | 128.485 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.4917 | 128.490 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.5000 | 128.500 | ACC-U | FIS-L, FIS-U | ACC | APP, ACC-L | FIS-L, FIS-U | ACC |
| 128.5000 | 128.505 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.5083 | 128.510 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.5167 | 128.515 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.5250 | 128.525 | ACC-U | FIS-L, FIS-U | ACC | APP, ACC-L | FIS-L, FIS-U | ACC |
| 128.5250 | 128.530 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.5333 | 128.535 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.5417 | 128.540 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.5500 | 128.550 | ACC-U | FIS-L, FIS-U | ACC | APP, ACC-L | FIS-L, FIS-U | ACC |
| 128.5500 | 128.555 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.5583 | 128.560 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.5667 | 128.565 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.5750 | 128.575 | ACC-U | FIS-L, FIS-U | ACC | APP, ACC-L | FIS-L, FIS-U | ACC |
| 128.5750 | 128.580 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.5833 | 128.585 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.5917 | 128.590 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.6000 | 128.600 | APP-U | VOLMET, ATIS | ACC | APP, ACC-L | VOLMET, ATIS | ACC |
| 128.6000 | 128.605 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.6083 | 128.610 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.6167 | 128.615 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.6250 | 128.625 | APP-U | VOLMET, ATIS | ACC | APP, ACC-L | VOLMET, ATIS | ACC |
| 128.6250 | 128.630 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.6333 | 128.635 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.6417 | 128.640 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.6500 | 128.650 | APP-U | VOLMET, ATIS | ACC | APP, ACC-L | VOLMET, ATIS | ACC |
| 128.6500 | 128.655 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.6583 | 128.660 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.6667 | 128.665 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.6750 | 128.675 | APP-U | VOLMET, ATIS | ACC | APP, ACC-L | VOLMET, ATIS | ACC |
| 128.6750 | 128.680 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.6833 | 128.685 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.6917 | 128.690 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.7000 | 128.700 | ACC-U | ACC-L | ACC | APP, ACC-L | ACC-L | ACC |
| 128.7000 | 128.705 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.7083 | 128.710 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.7167 | 128.715 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.7250 | 128.725 | ACC-U | ACC-L | ACC | APP, ACC-L | ACC-L | ACC |
| 128.7250 | 128.730 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.7333 | 128.735 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.7417 | 128.740 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.7500 | 128.750 | ACC-U | ACC-L | ACC | APP, ACC-L | ACC-L | ACC |
| 128.7500 | 128.755 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.7583 | 128.760 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.7667 | 128.765 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.7750 | 128.775 | ACC-U | ACC-L | ACC | APP, ACC-L | ACC-L | ACC |
| 128.7750 | 128.780 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.7833 | 128.785 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.7917 | 128.790 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.8000 | 128.800 | ACC-U | VOLMET, ATIS | ACC | APP, ACC-L | VOLMET, ATIS | ACC |
| 128.8000 | 128.805 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.8083 | 128.810 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.8167 | 128.815 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.8250 | 128.825 | ACC-U | VOLMET, ATIS | Not allotted | APP, ACC-L | VOLMET, ATIS | Not allotted |
| 128.8250 | 128.830 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.8333 | 128.835 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.8417 | 128.840 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.8500 | 128.850 | ACC-U | VOLMET, ATIS | APP | APP, ACC-L | VOLMET, ATIS | APP |
| 128.8500 | 128.855 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.8583 | 128.860 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.8667 | 128.865 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.8750 | 128.875 | ACC-U | VOLMET, ATIS | APP | APP, ACC-L | VOLMET, ATIS | APP |
| 128.8750 | 128.880 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.8833 | 128.885 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.8917 | 128.890 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.9000 | 128.900 | ACC-U | AOC | APP | APP, ACC-L | AOC | APP |
| 128.9000 | 128.905 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.9083 | 128.910 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.9167 | 128.915 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.9250 | 128.925 | ACC-U | AOC | APP | APP, ACC-L | AOC | APP |
| 128.9250 | 128.930 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.9333 | 128.935 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.9417 | 128.940 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.9500 | 128.950 | ACC-U | AOC | APP | APP, ACC-L | AOC | APP |
| 128.9500 | 128.955 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.9583 | 128.960 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.9667 | 128.965 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.9750 | 128.975 | ACC-U | AOC | APP | APP, ACC-L | AOC | APP |
| 128.9750 | 128.980 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.9833 | 128.985 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 128.9917 | 128.990 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.0000 | 129.000 | ACC-L | AOC | APP | APP, ACC-L | AOC | APP |
| 129.0000 | 129.005 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.0083 | 129.010 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.0167 | 129.015 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.0250 | 129.025 | ACC-L | AOC | APP | APP, ACC-L | AOC | APP |
| 129.0250 | 129.030 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.0333 | 129.035 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.0417 | 129.040 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.0500 | 129.050 | ACC-L | AOC | APP | APP, ACC-L | AOC | APP |
| 129.0500 | 129.055 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.0583 | 129.060 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.0667 | 129.065 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.0750 | 129.075 | ACC-L | AOC | APP | APP, ACC-L | AOC | APP |
| 129.0750 | 129.080 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.0833 | 129.085 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.0917 | 129.090 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.1000 | 129.100 | ACC-U | AOC | APP | APP, ACC-L | AOC | APP |
| 129.1000 | 129.105 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.1083 | 129.110 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.1167 | 129.115 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.1250 | 129.125 | ACC-U | AOC | APP | APP, ACC-L | AOC | APP |
| 129.1250 | 129.130 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.1333 | 129.135 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.1417 | 129.140 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.1500 | 129.150 | ACC-U | AOC | APP | APP, ACC-L | AOC | APP |
| 129.1500 | 129.155 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.1583 | 129.160 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.1667 | 129.165 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.1750 | 129.175 | ACC-U | AOC | APP | APP, ACC-L | AOC | APP |
| 129.1750 | 129.180 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.1833 | 129.185 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.1917 | 129.190 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.2000 | 129.200 | ACC-U | AOC | APP | APP, ACC-L | AOC | APP |
| 129.2000 | 129.205 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.2083 | 129.210 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.2167 | 129.215 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.2250 | 129.225 | ACC-U | AOC | APP | APP, ACC-L | AOC | APP |
| 129.2250 | 129.230 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.2333 | 129.235 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.2417 | 129.240 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.2500 | 129.250 | ACC-U | AOC | APP | APP, ACC-L | AOC | APP |
| 129.2500 | 129.255 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.2583 | 129.260 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.2667 | 129.265 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.2750 | 129.275 | ACC-U | AOC | APP | APP, ACC-L | AOC | APP |
| 129.2750 | 129.280 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.2833 | 129.285 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.2917 | 129.290 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.3000 | 129.300 | ACC-U | AOC | APP | APP, ACC-L | AOC | APP |
| 129.3000 | 129.305 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.3083 | 129.310 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.3167 | 129.315 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.3250 | 129.325 | ACC-U | AOC | APP | APP, ACC-L | AOC | APP |
| 129.3250 | 129.330 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.3333 | 129.335 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.3417 | 129.340 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.3500 | 129.350 | ACC-U | AOC | APP | APP, ACC-L | AOC | APP |
| 129.3500 | 129.355 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.3583 | 129.360 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.3667 | 129.365 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.3750 | 129.375 | ACC-U | AOC | APP | APP, ACC-L | AOC | APP |
| 129.3750 | 129.380 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.3833 | 129.385 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.3917 | 129.390 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.4000 | 129.400 | ACC-U | AOC | APP | APP, ACC-L | AOC | APP |
| 129.4000 | 129.405 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.4083 | 129.410 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.4167 | 129.415 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.4250 | 129.425 | ACC-U | AOC | APP | APP, ACC-L | AOC | APP |
| 129.4250 | 129.430 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.4333 | 129.435 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.4417 | 129.440 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.4500 | 129.450 | ACC-U | AOC | APP | APP, ACC-L | AOC | APP |
| 129.4500 | 129.455 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.4583 | 129.460 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.4667 | 129.465 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.4750 | 129.475 | ACC-U | AOC | APP | APP, ACC-L | AOC | APP |
| 129.4750 | 129.480 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.4833 | 129.485 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.4917 | 129.490 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.5000 | 129.500 | ACC-U | AOC | APP | APP, ACC-L | AOC | APP |
| 129.5000 | 129.505 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.5083 | 129.510 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.5167 | 129.515 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.5250 | 129.525 | ACC-U | AOC | APP | APP, ACC-L | AOC | APP |
| 129.5250 | 129.530 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.5333 | 129.535 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.5417 | 129.540 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.5500 | 129.550 | ACC-U | AOC | APP | APP, ACC-L | AOC | APP |
| 129.5500 | 129.555 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.5583 | 129.560 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.5667 | 129.565 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.5750 | 129.575 | ACC-U | AOC | APP | APP, ACC-L | AOC | APP |
| 129.5750 | 129.580 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.5833 | 129.585 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.5917 | 129.590 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.6000 | 129.600 | ACC-L | AOC | APP | APP, ACC-L | AOC | APP |
| 129.6000 | 129.605 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.6083 | 129.610 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.6167 | 129.615 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.6250 | 129.625 | ACC-L | AOC | APP | APP, ACC-L | AOC | APP |
| 129.6250 | 129.630 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.6333 | 129.635 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.6417 | 129.640 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.6500 | 129.650 | ACC-L | AOC | APP | APP, ACC-L | AOC | APP |
| 129.6500 | 129.655 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.6583 | 129.660 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.6667 | 129.665 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.6750 | 129.675 | ACC-L | AOC | APP | APP, ACC-L | AOC | APP |
| 129.6750 | 129.680 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.6833 | 129.685 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.6917 | 129.690 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 129.7000 | 129.700 | Not allotted | AOC | APP | Not allotted | AOC | APP |
| 129.7000 | 129.705 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 129.7083 | 129.710 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 129.7167 | 129.715 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 129.7250 | 129.725 | Not allotted | AOC | APP | Not allotted | AOC | APP |
| 129.7250 | 129.730 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 129.7333 | 129.735 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 129.7417 | 129.740 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 129.7500 | 129.750 | Not allotted | AOC | APP | Not allotted | AOC | APP |
| 129.7500 | 129.755 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 129.7583 | 129.760 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 129.7667 | 129.765 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 129.7750 | 129.775 | Not allotted | AOC | APP | Not allotted | AOC | APP |
| 129.7750 | 129.780 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 129.7833 | 129.785 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 129.7917 | 129.790 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 129.8000 | 129.800 | Not allotted | AOC | APP | Not allotted | AOC | APP |
| 129.8000 | 129.805 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 129.8083 | 129.810 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 129.8167 | 129.815 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 129.8250 | 129.825 | Not allotted | AOC | APP | Not allotted | AOC | APP |
| 129.8250 | 129.830 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 129.8333 | 129.835 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 129.8417 | 129.840 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 129.8500 | 129.850 | Not allotted | AOC | APP | Not allotted | AOC | APP |
| 129.8500 | 129.855 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 129.8583 | 129.860 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 129.8667 | 129.865 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 129.8750 | 129.875 | Not allotted | AOC | Not allotted | Not allotted | AOC | Not allotted |
| 129.8750 | 129.880 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 129.8833 | 129.885 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 129.8917 | 129.890 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 129.9000 | 129.900 | Not allotted | AOC | AOC | Not allotted | AOC | AOC |
| 129.9000 | 129.905 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 129.9083 | 129.910 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 129.9167 | 129.915 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 129.9250 | 129.925 | Not allotted | AOC | AOC | Not allotted | AOC | AOC |
| 129.9250 | 129.930 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 129.9333 | 129.935 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 129.9417 | 129.940 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 129.9500 | 129.950 | Not allotted | AOC | AOC | Not allotted | AOC | AOC |
| 129.9500 | 129.955 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 129.9583 | 129.960 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 129.9667 | 129.965 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 129.9750 | 129.975 | Not allotted | AOC | AOC | Not allotted | AOC | AOC |
| 129.9750 | 129.980 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 129.9833 | 129.985 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 129.9917 | 129.990 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.0000 | 130.000 | Not allotted | AOC | AOC | Not allotted | AOC | AOC |
| 130.0000 | 130.005 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.0083 | 130.010 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.0167 | 130.015 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.0250 | 130.025 | Not allotted | AOC | AOC | Not allotted | AOC | AOC |
| 130.0250 | 130.030 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.0333 | 130.035 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.0417 | 130.040 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.0500 | 130.050 | Not allotted | AOC | AOC | Not allotted | AOC | AOC |
| 130.0500 | 130.055 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.0583 | 130.060 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.0667 | 130.065 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.0750 | 130.075 | Not allotted | AOC | AOC | Not allotted | AOC | AOC |
| 130.0750 | 130.080 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.0833 | 130.085 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.0917 | 130.090 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.1000 | 130.100 | Not allotted | AOC | AOC | Not allotted | AOC | AOC |
| 130.1000 | 130.105 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.1083 | 130.110 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.1167 | 130.115 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.1250 | 130.125 | Not allotted | AOC | AOC | Not allotted | AOC | AOC |
| 130.1250 | 130.130 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.1333 | 130.135 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.1417 | 130.140 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.1500 | 130.150 | Not allotted | AOC | AOC | Not allotted | AOC | AOC |
| 130.1500 | 130.155 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.1583 | 130.160 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.1667 | 130.165 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.1750 | 130.175 | Not allotted | AOC | AOC | Not allotted | AOC | AOC |
| 130.1750 | 130.180 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.1833 | 130.185 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.1917 | 130.190 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.2000 | 130.200 | Not allotted | AOC | AOC | Not allotted | AOC | AOC |
| 130.2000 | 130.205 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.2083 | 130.210 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.2167 | 130.215 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.2250 | 130.225 | Not allotted | AOC | AOC | Not allotted | AOC | AOC |
| 130.2250 | 130.230 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.2333 | 130.235 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.2417 | 130.240 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.2500 | 130.250 | Not allotted | AOC | AOC | Not allotted | AOC | AOC |
| 130.2500 | 130.255 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.2583 | 130.260 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.2667 | 130.265 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.2750 | 130.275 | Not allotted | AOC | AOC | Not allotted | AOC | AOC |
| 130.2750 | 130.280 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.2833 | 130.285 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.2917 | 130.290 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.3000 | 130.300 | Not allotted | AOC | AOC | Not allotted | AOC | AOC |
| 130.3000 | 130.305 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.3083 | 130.310 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.3167 | 130.315 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.3250 | 130.325 | Not allotted | AOC | AOC | Not allotted | AOC | AOC |
| 130.3250 | 130.330 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.3333 | 130.335 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.3417 | 130.340 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.3500 | 130.350 | Not allotted | AOC | AOC | Not allotted | AOC | AOC |
| 130.3500 | 130.355 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.3583 | 130.360 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.3667 | 130.365 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.3750 | 130.375 | Not allotted | AOC | AOC | Not allotted | AOC | AOC |
| 130.3750 | 130.380 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.3833 | 130.385 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.3917 | 130.390 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.4000 | 130.400 | Not allotted | AOC | AOC | Not allotted | AOC | AOC |
| 130.4000 | 130.405 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.4083 | 130.410 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.4167 | 130.415 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.4250 | 130.425 | Not allotted | AOC | AOC | Not allotted | AOC | AOC |
| 130.4250 | 130.430 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.4333 | 130.435 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.4417 | 130.440 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.4500 | 130.450 | Not allotted | AOC | AOC | Not allotted | AOC | AOC |
| 130.4500 | 130.455 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.4583 | 130.460 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.4667 | 130.465 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.4750 | 130.475 | Not allotted | AOC | AOC | Not allotted | AOC | AOC |
| 130.4750 | 130.480 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.4833 | 130.485 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.4917 | 130.490 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.5000 | 130.500 | Not allotted | AOC | AOC | Not allotted | AOC | AOC |
| 130.5000 | 130.505 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.5083 | 130.510 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.5167 | 130.515 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.5250 | 130.525 | Not allotted | AOC | AOC | Not allotted | AOC | AOC |
| 130.5250 | 130.530 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.5333 | 130.535 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.5417 | 130.540 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.5500 | 130.550 | Not allotted | AOC | AOC | Not allotted | AOC | AOC |
| 130.5500 | 130.555 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.5583 | 130.560 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.5667 | 130.565 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.5750 | 130.575 | Not allotted | AOC | AOC | Not allotted | AOC | AOC |
| 130.5750 | 130.580 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.5833 | 130.585 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.5917 | 130.590 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.6000 | 130.600 | Not allotted | AOC | AOC | Not allotted | AOC | AOC |
| 130.6000 | 130.605 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.6083 | 130.610 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.6167 | 130.615 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.6250 | 130.625 | Not allotted | AOC | AOC | Not allotted | AOC | AOC |
| 130.6250 | 130.630 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.6333 | 130.635 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.6417 | 130.640 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.6500 | 130.650 | Not allotted | AOC | AOC | Not allotted | AOC | AOC |
| 130.6500 | 130.655 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.6583 | 130.660 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.6667 | 130.665 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.6750 | 130.675 | Not allotted | AOC | AOC | Not allotted | AOC | AOC |
| 130.6750 | 130.680 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.6833 | 130.685 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.6917 | 130.690 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.7000 | 130.700 | Not allotted | AOC | AOC | Not allotted | AOC | AOC |
| 130.7000 | 130.705 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.7083 | 130.710 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.7167 | 130.715 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.7250 | 130.725 | Not allotted | AOC | AOC | Not allotted | AOC | AOC |
| 130.7250 | 130.730 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.7333 | 130.735 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.7417 | 130.740 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.7500 | 130.750 | Not allotted | AOC | AOC | Not allotted | AOC | AOC |
| 130.7500 | 130.755 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.7583 | 130.760 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.7667 | 130.765 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.7750 | 130.775 | Not allotted | AOC | AOC | Not allotted | AOC | AOC |
| 130.7750 | 130.780 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.7833 | 130.785 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.7917 | 130.790 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.8000 | 130.800 | Not allotted | AOC | AOC | Not allotted | AOC | AOC |
| 130.8000 | 130.805 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.8083 | 130.810 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.8167 | 130.815 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.8250 | 130.825 | Not allotted | AOC | AOC | Not allotted | AOC | AOC |
| 130.8250 | 130.830 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.8333 | 130.835 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.8417 | 130.840 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.8500 | 130.850 | Not allotted | AOC | AOC | Not allotted | AOC | AOC |
| 130.8500 | 130.855 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.8583 | 130.860 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.8667 | 130.865 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.8750 | 130.875 | Not allotted | AOC | AOC | Not allotted | AOC | AOC |
| 130.8750 | 130.880 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.8833 | 130.885 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.8917 | 130.890 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 130.9000 | 130.900 | ACC-U | AOC | AOC | APP, ACC-L | AOC | AOC |
| 130.9000 | 130.905 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 130.9083 | 130.910 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 130.9167 | 130.915 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 130.9250 | 130.925 | ACC-U | AOC | AOC | APP, ACC-L | AOC | AOC |
| 130.9250 | 130.930 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 130.9333 | 130.935 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 130.9417 | 130.940 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 130.9500 | 130.950 | ACC-U | AOC | AOC | APP, ACC-L | AOC | AOC |
| 130.9500 | 130.955 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 130.9583 | 130.960 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 130.9667 | 130.965 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 130.9750 | 130.975 | ACC-U | AOC | AOC | APP, ACC-L | AOC | AOC |
| 130.9750 | 130.980 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 130.9833 | 130.985 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 130.9917 | 130.990 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 131.0000 | 131.000 | Not allotted | AOC | AOC | APP, ACC-L | AOC | AOC |
| 131.0000 | 131.005 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 131.0083 | 131.010 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 131.0167 | 131.015 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 131.0250 | 131.025 | Not allotted | AOC | AOC | APP, ACC-L | AOC | AOC |
| 131.0250 | 131.030 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 131.0333 | 131.035 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 131.0417 | 131.040 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 131.0500 | 131.050 | Not allotted | AOC | AOC | APP, ACC-L | AOC | AOC |
| 131.0500 | 131.055 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 131.0583 | 131.060 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 131.0667 | 131.065 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 131.0750 | 131.075 | Not allotted | AOC | AOC | APP, ACC-L | AOC | AOC |
| 131.0750 | 131.080 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 131.0833 | 131.085 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 131.0917 | 131.090 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 131.1000 | 131.100 | FIS-L | AOC | AOC | APP, ACC-L | AOC | AOC |
| 131.1000 | 131.105 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 131.1083 | 131.110 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 131.1167 | 131.115 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 131.1250 | 131.125 | FIS-L | AOC | AOC | APP, ACC-L | AOC | AOC |
| 131.1250 | 131.130 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 131.1333 | 131.135 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 131.1417 | 131.140 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 131.1500 | 131.150 | FIS-L | AOC | AOC | APP, ACC-L | AOC | AOC |
| 131.1500 | 131.155 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 131.1583 | 131.160 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 131.1667 | 131.165 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 131.1750 | 131.175 | FIS-L | AOC | AOC | APP, ACC-L | AOC | AOC |
| 131.1750 | 131.180 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 131.1833 | 131.185 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 131.1917 | 131.190 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 131.2000 | 131.200 | ACC-L | AOC | AOC | APP, ACC-L | AOC | AOC |
| 131.2000 | 131.205 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 131.2083 | 131.210 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 131.2167 | 131.215 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 131.2250 | 131.225 | ACC-L | AOC | AOC | APP, ACC-L | AOC | AOC |
| 131.2250 | 131.230 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 131.2333 | 131.235 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 131.2417 | 131.240 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 131.2500 | 131.250 | ACC-L | AOC | AOC | APP, ACC-L | AOC | AOC |
| 131.2500 | 131.255 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 131.2583 | 131.260 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 131.2667 | 131.265 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 131.2750 | 131.275 | ACC-L | AOC | AOC | APP, ACC-L | AOC | AOC |
| 131.2750 | 131.280 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 131.2833 | 131.285 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 131.2917 | 131.290 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 131.3000 | 131.300 | FIS-U (GPS) | AOC | AOC | APP, ACC-L | AOC | AOC |
| 131.3000 | 131.305 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 131.3083 | 131.310 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 131.3167 | 131.315 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 131.3250 | 131.325 | FIS-U (GPS) | AOC | AOC | APP, ACC-L | AOC | AOC |
| 131.3250 | 131.330 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 131.3333 | 131.335 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 131.3417 | 131.340 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 131.3500 | 131.350 | FIS-U (GPS) | AOC | AOC | APP, ACC-L | AOC | AOC |
| 131.3500 | 131.355 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 131.3583 | 131.360 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 131.3667 | 131.365 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 131.3750 | 131.375 | FIS-U (GPS) | AOC | AOC | APP, ACC-L | AOC | AOC |
| 131.3750 | 131.380 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 131.3833 | 131.385 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 131.3917 | 131.390 | Not used | Not used | Not used | APP, ACC-L | Not used | Not used |
| 131.4000 | 131.400 | AOC | AOC | AOC | AOC | AOC | AOC |
| 131.4000 | 131.405 | Not used | Not used | Not used | AOC | Not used | Not used |
| 131.4083 | 131.410 | Not used | Not used | Not used | AOC | Not used | Not used |
| 131.4167 | 131.415 | Not used | Not used | Not used | AOC | Not used | Not used |
| 131.4250 | 131.425 | AOC | AOC | AOC | AOC | AOC | AOC |
| 131.4250 | 131.430 | Not used | Not used | Not used | AOC | Not used | Not used |
| 131.4333 | 131.435 | Not used | Not used | Not used | AOC | Not used | Not used |
| 131.4417 | 131.440 | Not used | Not used | Not used | AOC | Not used | Not used |
| 131.4500 | 131.450 | AOC | AOC | AOC | AOC | AOC | AOC |
| 131.4500 | 131.455 | Not used | Not used | Not used | AOC | Not used | Not used |
| 131.4583 | 131.460 | Not used | Not used | Not used | AOC | Not used | Not used |
| 131.4667 | 131.465 | Not used | Not used | Not used | AOC | Not used | Not used |
| 131.4750 | 131.475 | AOC | AOC | AOC | AOC | AOC | AOC |
| 131.4750 | 131.480 | Not used | Not used | Not used | AOC | Not used | Not used |
| 131.4833 | 131.485 | Not used | Not used | Not used | AOC | Not used | Not used |
| 131.4917 | 131.490 | Not used | Not used | Not used | AOC | Not used | Not used |
| 131.5000 | 131.500 | AOC | AOC | AOC | AOC | AOC | AOC |
| 131.5000 | 131.505 | Not used | Not used | Not used | Blocked | Not used | Not used |
| 131.5083 | 131.510 | Not used | Not used | Not used | Blocked | Not used | Not used |
| 131.5167 | 131.515 | Not used | Not used | Not used | Blocked | Not used | Not used |
| 131.5250 | 131.525 | AOC | AOC | AOC | AOC | AOC | AOC |
| 131.5250 | 131.530 | Not used | Not used | Not used | Blocked | Not used | Not used |
| 131.5333 | 131.535 | Not used | Not used | Not used | Blocked | Not used | Not used |
| 131.5417 | 131.540 | Not used | Not used | Not used | Blocked | Not used | Not used |
| 131.5500 | 131.550 | AOC | AOC | AOC | AOC | AOC | AOC |
| 131.5500 | 131.555 | Not used | Not used | Not used | AOC | Not used | Not used |
| 131.5583 | 131.560 | Not used | Not used | Not used | AOC | Not used | Not used |
| 131.5667 | 131.565 | Not used | Not used | Not used | AOC | Not used | Not used |
| 131.5750 | 131.575 | AOC | AOC | AOC | AOC | AOC | AOC |
| 131.5750 | 131.580 | Not used | Not used | Not used | AOC | Not used | Not used |
| 131.5833 | 131.585 | Not used | Not used | Not used | AOC | Not used | Not used |
| 131.5917 | 131.590 | Not used | Not used | Not used | AOC | Not used | Not used |
| 131.6000 | 131.600 | AOC | AOC | AOC | AOC | AOC | AOC |
| 131.6000 | 131.605 | Not used | Not used | Not used | AOC | Not used | Not used |
| 131.6083 | 131.610 | Not used | Not used | Not used | AOC | Not used | Not used |
| 131.6167 | 131.615 | Not used | Not used | Not used | AOC | Not used | Not used |
| 131.6250 | 131.625 | AOC | AOC | AOC | AOC | AOC | AOC |
| 131.6250 | 131.630 | Not used | Not used | Not used | AOC | Not used | Not used |
| 131.6333 | 131.635 | Not used | Not used | Not used | AOC | Not used | Not used |
| 131.6417 | 131.640 | Not used | Not used | Not used | AOC | Not used | Not used |
| 131.6500 | 131.650 | AOC | AOC | AOC | AOC | AOC | AOC |
| 131.6500 | 131.655 | Not used | Not used | Not used | AOC | Not used | Not used |
| 131.6583 | 131.660 | Not used | Not used | Not used | AOC | Not used | Not used |
| 131.6667 | 131.665 | Not used | Not used | Not used | AOC | Not used | Not used |
| 131.6750 | 131.675 | AOC | AOC | AOC | AOC | AOC | AOC |
| 131.6750 | 131.680 | Not used | Not used | Not used | AOC | Not used | Not used |
| 131.6833 | 131.685 | Not used | Not used | Not used | AOC | Not used | Not used |
| 131.6917 | 131.690 | Not used | Not used | Not used | AOC | Not used | Not used |
| 131.7000 | 131.700 | AOC | AOC | AOC | AOC | AOC | AOC |
| 131.7000 | 131.705 | Not used | Not used | Not used | Blocked | Not used | Not used |
| 131.7083 | 131.710 | Not used | Not used | Not used | Blocked | Not used | Not used |
| 131.7167 | 131.715 | Not used | Not used | Not used | Blocked | Not used | Not used |
| 131.7250 | 131.725 | AOC | AOC | AOC | AOC | AOC | AOC |
| 131.7250 | 131.730 | Not used | Not used | Not used | Blocked | Not used | Not used |
| 131.7333 | 131.735 | Not used | Not used | Not used | Blocked | Not used | Not used |
| 131.7417 | 131.740 | Not used | Not used | Not used | Blocked | Not used | Not used |
| 131.7500 | 131.750 | AOC | AOC | AOC | AOC | AOC | AOC |
| 131.7500 | 131.755 | Not used | Not used | Not used | Blocked | Not used | Not used |
| 131.7583 | 131.760 | Not used | Not used | Not used | Blocked | Not used | Not used |
| 131.7667 | 131.765 | Not used | Not used | Not used | Blocked | Not used | Not used |
| 131.7750 | 131.775 | AOC | AOC | AOC | AOC | AOC | AOC |
| 131.7750 | 131.780 | Not used | Not used | Not used | Blocked | Not used | Not used |
| 131.7833 | 131.785 | Not used | Not used | Not used | Blocked | Not used | Not used |
| 131.7917 | 131.790 | Not used | Not used | Not used | Blocked | Not used | Not used |
| 131.8000 | 131.800 | AOC | AOC | AOC | AOC | AOC | AOC |
| 131.8000 | 131.805 | Not used | Not used | Not used | Blocked | Not used | Not used |
| 131.8083 | 131.810 | Not used | Not used | Not used | Blocked | Not used | Not used |
| 131.8167 | 131.815 | Not used | Not used | Not used | Blocked | Not used | Not used |
| 131.8250 | 131.825 | AOC | AOC | AOC | AOC | AOC | AOC |
| 131.8250 | 131.830 | Not used | Not used | Not used | Blocked | Not used | Not used |
| 131.8333 | 131.835 | Not used | Not used | Not used | Blocked | Not used | Not used |
| 131.8417 | 131.840 | Not used | Not used | Not used | Blocked | Not used | Not used |
| 131.8500 | 131.850 | AOC | AOC | AOC | AOC | AOC | AOC |
| 131.8500 | 131.855 | Not used | Not used | Not used | AOC | Not used | Not used |
| 131.8583 | 131.860 | Not used | Not used | Not used | AOC | Not used | Not used |
| 131.8667 | 131.865 | Not used | Not used | Not used | AOC | Not used | Not used |
| 131.8750 | 131.875 | AOC | AOC | AOC | AOC | AOC | AOC |
| 131.8750 | 131.880 | Not used | Not used | Not used | AOC | Not used | Not used |
| 131.8833 | 131.885 | Not used | Not used | Not used | AOC | Not used | Not used |
| 131.8917 | 131.890 | Not used | Not used | Not used | AOC | Not used | Not used |
| 131.9000 | 131.900 | AOC | AOC | AOC | AOC | AOC | AOC |
| 131.9000 | 131.905 | Not used | Not used | Not used | AOC | Not used | Not used |
| 131.9083 | 131.910 | Not used | Not used | Not used | AOC | Not used | Not used |
| 131.9167 | 131.915 | Not used | Not used | Not used | AOC | Not used | Not used |
| 131.9250 | 131.925 | AOC | AOC | AOC | AOC | AOC | AOC |
| 131.9250 | 131.930 | Not used | Not used | Not used | AOC | Not used | Not used |
| 131.9333 | 131.935 | Not used | Not used | Not used | AOC | Not used | Not used |
| 131.9417 | 131.940 | Not used | Not used | Not used | AOC | Not used | Not used |
| 131.9500 | 131.950 | AOC | AOC | AOC | AOC | AOC | AOC |
| 131.9500 | 131.955 | Not used | Not used | Not used | AOC | Not used | Not used |
| 131.9583 | 131.960 | Not used | Not used | Not used | AOC | Not used | Not used |
| 131.9667 | 131.965 | Not used | Not used | Not used | AOC | Not used | Not used |
| 131.9750 | 131.975 | AOC | AOC | AOC | AOC | AOC | AOC |
| 131.9750 | 131.980 | Not used | Not used | Not used | AOC | Not used | Not used |
| 131.9833 | 131.985 | Not used | Not used | Not used | AOC | Not used | Not used |
| 131.9917 | 131.990 | Not used | Not used | Not used | AOC | Not used | Not used |
| 132.0000 | 132.000 | Not allotted | AOC | AOC | ACC-U | AOC | AOC |
| 132.0000 | 132.005 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.0083 | 132.010 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.0167 | 132.015 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.0250 | 132.025 | Not allotted | AOC | AOC | ACC-U | AOC | AOC |
| 132.0250 | 132.030 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.0333 | 132.035 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.0417 | 132.040 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.0500 | 132.050 | Not allotted | Not allotted | VOLMET, ATIS | ACC-U | Not allotted | VOLMET, ATIS |
| 132.0500 | 132.055 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.0583 | 132.060 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.0667 | 132.065 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.0750 | 132.075 | Not allotted | Not allotted | VOLMET, ATIS | ACC-U | Not allotted | VOLMET, ATIS |
| 132.0750 | 132.080 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.0833 | 132.085 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.0917 | 132.090 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.1000 | 132.100 | ACC-U | ACC-L, ACC-U | VOLMET, ATIS | ACC-U | ACC-L, ACC-U | VOLMET, ATIS |
| 132.1000 | 132.105 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.1083 | 132.110 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.1167 | 132.115 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.1250 | 132.125 | ACC-U | ACC-L, ACC-U | VOLMET, ATIS | ACC-U | ACC-L, ACC-U | VOLMET, ATIS |
| 132.1250 | 132.130 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.1333 | 132.135 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.1417 | 132.140 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.1500 | 132.150 | ACC-U | ACC-L, ACC-U | VOLMET, ATIS | ACC-U | ACC-L, ACC-U | VOLMET, ATIS |
| 132.1500 | 132.155 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.1583 | 132.160 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.1667 | 132.165 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.1750 | 132.175 | ACC-U | ACC-L, ACC-U | VOLMET, ATIS | ACC-U | ACC-L, ACC-U | VOLMET, ATIS |
| 132.1750 | 132.180 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.1833 | 132.185 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.1917 | 132.190 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.2000 | 132.200 | Not allotted | ACC-L, ACC-U | VOLMET, ATIS | ACC-U | ACC-L, ACC-U | VOLMET, ATIS |
| 132.2000 | 132.205 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.2083 | 132.210 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.2167 | 132.215 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.2250 | 132.225 | Not allotted | ACC-L, ACC-U | VOLMET, ATIS | ACC-U | ACC-L, ACC-U | VOLMET, ATIS |
| 132.2250 | 132.230 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.2333 | 132.235 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.2417 | 132.240 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.2500 | 132.250 | Not allotted | ACC-L, ACC-U | VOLMET, ATIS | ACC-U | ACC-L, ACC-U | VOLMET, ATIS |
| 132.2500 | 132.255 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.2583 | 132.260 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.2667 | 132.265 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.2750 | 132.275 | Not allotted | ACC-L, ACC-U | VOLMET, ATIS | ACC-U | ACC-L, ACC-U | VOLMET, ATIS |
| 132.2750 | 132.280 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.2833 | 132.285 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.2917 | 132.290 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.3000 | 132.300 | FIS-U (GPS) | ACC-L, ACC-U | VOLMET, ATIS | ACC-U | ACC-L, ACC-U | VOLMET, ATIS |
| 132.3000 | 132.305 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.3083 | 132.310 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.3167 | 132.315 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.3250 | 132.325 | FIS-U (GPS) | ACC-L, ACC-U | VOLMET, ATIS | ACC-U | ACC-L, ACC-U | VOLMET, ATIS |
| 132.3250 | 132.330 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.3333 | 132.335 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.3417 | 132.340 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.3500 | 132.350 | FIS-U (GPS) | ACC-L, ACC-U | VOLMET, ATIS | ACC-U | ACC-L, ACC-U | VOLMET, ATIS |
| 132.3500 | 132.355 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.3583 | 132.360 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.3667 | 132.365 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.3750 | 132.375 | FIS-U (GPS) | ACC-L, ACC-U | VOLMET, ATIS | ACC-U | ACC-L, ACC-U | VOLMET, ATIS |
| 132.3750 | 132.380 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.3833 | 132.385 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.3917 | 132.390 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.4000 | 132.400 | Not allotted | ACC-L, ACC-U | VOLMET, ATIS | ACC-U | ACC-L, ACC-U | VOLMET, ATIS |
| 132.4000 | 132.405 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.4083 | 132.410 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.4167 | 132.415 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.4250 | 132.425 | Not allotted | ACC-L, ACC-U | VOLMET, ATIS | ACC-U | ACC-L, ACC-U | VOLMET, ATIS |
| 132.4250 | 132.430 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.4333 | 132.435 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.4417 | 132.440 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.4500 | 132.450 | Not allotted | ACC-L, ACC-U | VOLMET, ATIS | ACC-U | ACC-L, ACC-U | VOLMET, ATIS |
| 132.4500 | 132.455 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.4583 | 132.460 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.4667 | 132.465 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.4750 | 132.475 | Not allotted | ACC-L, ACC-U | VOLMET, ATIS | ACC-U | ACC-L, ACC-U | VOLMET, ATIS |
| 132.4750 | 132.480 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.4833 | 132.485 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.4917 | 132.490 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.5000 | 132.500 | Not allotted | ACC-L, ACC-U | VOLMET, ATIS | ACC-U | ACC-L, ACC-U | VOLMET, ATIS |
| 132.5000 | 132.505 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.5083 | 132.510 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.5167 | 132.515 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.5250 | 132.525 | Not allotted | ACC-L, ACC-U | VOLMET, ATIS | ACC-U | ACC-L, ACC-U | VOLMET, ATIS |
| 132.5250 | 132.530 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.5333 | 132.535 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.5417 | 132.540 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.5500 | 132.550 | Not allotted | ACC-L, ACC-U | VOLMET, ATIS | ACC-U | ACC-L, ACC-U | VOLMET, ATIS |
| 132.5500 | 132.555 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.5583 | 132.560 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.5667 | 132.565 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.5750 | 132.575 | Not allotted | ACC-L, ACC-U | VOLMET, ATIS | ACC-U | ACC-L, ACC-U | VOLMET, ATIS |
| 132.5750 | 132.580 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.5833 | 132.585 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.5917 | 132.590 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.6000 | 132.600 | Not allotted | ACC-L, ACC-U | VOLMET, ATIS | ACC-U | ACC-L, ACC-U | VOLMET, ATIS |
| 132.6000 | 132.605 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.6083 | 132.610 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.6167 | 132.615 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.6250 | 132.625 | Not allotted | ACC-L, ACC-U | VOLMET, ATIS | ACC-U | ACC-L, ACC-U | VOLMET, ATIS |
| 132.6250 | 132.630 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.6333 | 132.635 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.6417 | 132.640 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.6500 | 132.650 | Not allotted | ACC-L, ACC-U | VOLMET, ATIS | ACC-U | ACC-L, ACC-U | VOLMET, ATIS |
| 132.6500 | 132.655 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.6583 | 132.660 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.6667 | 132.665 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.6750 | 132.675 | Not allotted | ACC-L, ACC-U | VOLMET, ATIS | ACC-U | ACC-L, ACC-U | VOLMET, ATIS |
| 132.6750 | 132.680 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.6833 | 132.685 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.6917 | 132.690 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.7000 | 132.700 | Not allotted | ACC-L, ACC-U | VOLMET, ATIS | ACC-U | ACC-L, ACC-U | VOLMET, ATIS |
| 132.7000 | 132.705 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.7083 | 132.710 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.7167 | 132.715 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.7250 | 132.725 | Not allotted | ACC-L, ACC-U | VOLMET, ATIS | ACC-U | ACC-L, ACC-U | VOLMET, ATIS |
| 132.7250 | 132.730 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.7333 | 132.735 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.7417 | 132.740 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.7500 | 132.750 | Not allotted | ACC-L, ACC-U | VOLMET, ATIS | ACC-U | ACC-L, ACC-U | VOLMET, ATIS |
| 132.7500 | 132.755 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.7583 | 132.760 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.7667 | 132.765 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.7750 | 132.775 | Not allotted | ACC-L, ACC-U | VOLMET, ATIS | ACC-U | ACC-L, ACC-U | VOLMET, ATIS |
| 132.7750 | 132.780 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.7833 | 132.785 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.7917 | 132.790 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.8000 | 132.800 | Not allotted | ACC-L, ACC-U | VOLMET, ATIS | ACC-U | ACC-L, ACC-U | VOLMET, ATIS |
| 132.8000 | 132.805 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.8083 | 132.810 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.8167 | 132.815 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.8250 | 132.825 | Not allotted | ACC-L, ACC-U | VOLMET, ATIS | ACC-U | ACC-L, ACC-U | VOLMET, ATIS |
| 132.8250 | 132.830 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.8333 | 132.835 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.8417 | 132.840 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.8500 | 132.850 | Not allotted | ACC-L, ACC-U | VOLMET, ATIS | ACC-U | ACC-L, ACC-U | VOLMET, ATIS |
| 132.8500 | 132.855 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.8583 | 132.860 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.8667 | 132.865 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.8750 | 132.875 | Not allotted | ACC-L, ACC-U | VOLMET, ATIS | ACC-U | ACC-L, ACC-U | VOLMET, ATIS |
| 132.8750 | 132.880 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.8833 | 132.885 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.8917 | 132.890 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.9000 | 132.900 | Not allotted | ACC-L, ACC-U | VOLMET, ATIS | ACC-U | ACC-L, ACC-U | VOLMET, ATIS |
| 132.9000 | 132.905 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.9083 | 132.910 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.9167 | 132.915 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.9250 | 132.925 | Not allotted | ACC-L, ACC-U | VOLMET, ATIS | ACC-U | ACC-L, ACC-U | VOLMET, ATIS |
| 132.9250 | 132.930 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.9333 | 132.935 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.9417 | 132.940 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.9500 | 132.950 | Not allotted | ACC-L, ACC-U | VOLMET, ATIS | ACC-U | ACC-L, ACC-U | VOLMET, ATIS |
| 132.9500 | 132.955 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.9583 | 132.960 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.9667 | 132.965 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.9750 | 132.975 | Not allotted | ACC-L, ACC-U | ACC | ACC-U | ACC-L, ACC-U | ACC |
| 132.9750 | 132.980 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.9833 | 132.985 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 132.9917 | 132.990 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.0000 | 133.000 | Not allotted | ACC-L, ACC-U | ACC | ACC-U | ACC-L, ACC-U | ACC |
| 133.0000 | 133.005 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.0083 | 133.010 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.0167 | 133.015 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.0250 | 133.025 | Not allotted | ACC-L, ACC-U | ACC | ACC-U | ACC-L, ACC-U | ACC |
| 133.0250 | 133.030 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.0333 | 133.035 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.0417 | 133.040 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.0500 | 133.050 | Not allotted | ACC-L, ACC-U | ACC | ACC-U | ACC-L, ACC-U | ACC |
| 133.0500 | 133.055 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.0583 | 133.060 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.0667 | 133.065 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.0750 | 133.075 | Not allotted | ACC-L, ACC-U | ACC | ACC-U | ACC-L, ACC-U | ACC |
| 133.0750 | 133.080 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.0833 | 133.085 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.0917 | 133.090 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.1000 | 133.100 | Not allotted | ACC-L, ACC-U | ACC | ACC-U | ACC-L, ACC-U | ACC |
| 133.1000 | 133.105 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.1083 | 133.110 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.1167 | 133.115 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.1250 | 133.125 | Not allotted | ACC-L, ACC-U | ACC | ACC-U | ACC-L, ACC-U | ACC |
| 133.1250 | 133.130 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.1333 | 133.135 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.1417 | 133.140 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.1500 | 133.150 | Not allotted | ACC-L, ACC-U | ACC | ACC-U | ACC-L, ACC-U | ACC |
| 133.1500 | 133.155 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.1583 | 133.160 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.1667 | 133.165 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.1750 | 133.175 | Not allotted | ACC-L, ACC-U | ACC | ACC-U | ACC-L, ACC-U | ACC |
| 133.1750 | 133.180 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.1833 | 133.185 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.1917 | 133.190 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.2000 | 133.200 | Not allotted | ACC-L, ACC-U | ACC | ACC-U | ACC-L, ACC-U | ACC |
| 133.2000 | 133.205 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.2083 | 133.210 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.2167 | 133.215 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.2250 | 133.225 | Not allotted | ACC-L, ACC-U | ACC | ACC-U | ACC-L, ACC-U | ACC |
| 133.2250 | 133.230 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.2333 | 133.235 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.2417 | 133.240 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.2500 | 133.250 | Not allotted | ACC-L, ACC-U | ACC | ACC-U | ACC-L, ACC-U | ACC |
| 133.2500 | 133.255 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.2583 | 133.260 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.2667 | 133.265 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.2750 | 133.275 | Not allotted | ACC-L, ACC-U | ACC | ACC-U | ACC-L, ACC-U | ACC |
| 133.2750 | 133.280 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.2833 | 133.285 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.2917 | 133.290 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.3000 | 133.300 | Not allotted | ACC-L, ACC-U | ACC | ACC-U | ACC-L, ACC-U | ACC |
| 133.3000 | 133.305 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.3083 | 133.310 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.3167 | 133.315 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.3250 | 133.325 | Not allotted | ACC-L, ACC-U | ACC | ACC-U | ACC-L, ACC-U | ACC |
| 133.3250 | 133.330 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.3333 | 133.335 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.3417 | 133.340 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.3500 | 133.350 | Not allotted | ACC-L, ACC-U | ACC | ACC-U | ACC-L, ACC-U | ACC |
| 133.3500 | 133.355 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.3583 | 133.360 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.3667 | 133.365 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.3750 | 133.375 | Not allotted | ACC-L, ACC-U | ACC | ACC-U | ACC-L, ACC-U | ACC |
| 133.3750 | 133.380 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.3833 | 133.385 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.3917 | 133.390 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.4000 | 133.400 | Not allotted | ACC-L, ACC-U | ACC | ACC-U | ACC-L, ACC-U | ACC |
| 133.4000 | 133.405 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.4083 | 133.410 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.4167 | 133.415 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.4250 | 133.425 | Not allotted | ACC-L, ACC-U | ACC | ACC-U | ACC-L, ACC-U | ACC |
| 133.4250 | 133.430 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.4333 | 133.435 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.4417 | 133.440 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.4500 | 133.450 | Not allotted | ACC-L, ACC-U | ACC | ACC-U | ACC-L, ACC-U | ACC |
| 133.4500 | 133.455 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.4583 | 133.460 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.4667 | 133.465 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.4750 | 133.475 | Not allotted | ACC-L, ACC-U | ACC | ACC-U | ACC-L, ACC-U | ACC |
| 133.4750 | 133.480 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.4833 | 133.485 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.4917 | 133.490 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.5000 | 133.500 | Not allotted | ACC-L, ACC-U | ACC | ACC-U | ACC-L, ACC-U | ACC |
| 133.5000 | 133.505 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.5083 | 133.510 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.5167 | 133.515 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.5250 | 133.525 | Not allotted | ACC-L, ACC-U | ACC | ACC-U | ACC-L, ACC-U | ACC |
| 133.5250 | 133.530 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.5333 | 133.535 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.5417 | 133.540 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.5500 | 133.550 | Not allotted | ACC-L, ACC-U | ACC | ACC-U | ACC-L, ACC-U | ACC |
| 133.5500 | 133.555 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.5583 | 133.560 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.5667 | 133.565 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.5750 | 133.575 | Not allotted | ACC-L, ACC-U | ACC | ACC-U | ACC-L, ACC-U | ACC |
| 133.5750 | 133.580 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.5833 | 133.585 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.5917 | 133.590 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.6000 | 133.600 | Not allotted | ACC-L, ACC-U | ACC | ACC-U | ACC-L, ACC-U | ACC |
| 133.6000 | 133.605 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.6083 | 133.610 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.6167 | 133.615 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.6250 | 133.625 | Not allotted | ACC-L, ACC-U | ACC | ACC-U | ACC-L, ACC-U | ACC |
| 133.6250 | 133.630 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.6333 | 133.635 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.6417 | 133.640 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.6500 | 133.650 | Not allotted | ACC-L, ACC-U | ACC | ACC-U | ACC-L, ACC-U | ACC |
| 133.6500 | 133.655 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.6583 | 133.660 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.6667 | 133.665 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.6750 | 133.675 | Not allotted | ACC-L, ACC-U | ACC | ACC-U | ACC-L, ACC-U | ACC |
| 133.6750 | 133.680 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.6833 | 133.685 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.6917 | 133.690 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.7000 | 133.700 | Not allotted | ACC-L, ACC-U | ACC | ACC-U | ACC-L, ACC-U | ACC |
| 133.7000 | 133.705 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.7083 | 133.710 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.7167 | 133.715 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.7250 | 133.725 | Not allotted | ACC-L, ACC-U | ACC | ACC-U | ACC-L, ACC-U | ACC |
| 133.7250 | 133.730 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.7333 | 133.735 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.7417 | 133.740 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.7500 | 133.750 | Not allotted | ACC-L, ACC-U | ACC | ACC-U | ACC-L, ACC-U | ACC |
| 133.7500 | 133.755 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.7583 | 133.760 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.7667 | 133.765 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.7750 | 133.775 | Not allotted | ACC-L, ACC-U | ACC | ACC-U | ACC-L, ACC-U | ACC |
| 133.7750 | 133.780 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.7833 | 133.785 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.7917 | 133.790 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.8000 | 133.800 | Not allotted | ACC-L, ACC-U | ACC | ACC-U | ACC-L, ACC-U | ACC |
| 133.8000 | 133.805 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.8083 | 133.810 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.8167 | 133.815 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.8250 | 133.825 | Not allotted | ACC-L, ACC-U | ACC | ACC-U | ACC-L, ACC-U | ACC |
| 133.8250 | 133.830 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.8333 | 133.835 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.8417 | 133.840 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.8500 | 133.850 | Not allotted | ACC-L, ACC-U | ACC | ACC-U | ACC-L, ACC-U | ACC |
| 133.8500 | 133.855 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.8583 | 133.860 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.8667 | 133.865 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.8750 | 133.875 | Not allotted | ACC-L, ACC-U | ACC | ACC-U | ACC-L, ACC-U | ACC |
| 133.8750 | 133.880 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.8833 | 133.885 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.8917 | 133.890 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.9000 | 133.900 | Not allotted | ACC-L, ACC-U | ACC | ACC-U | ACC-L, ACC-U | ACC |
| 133.9000 | 133.905 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.9083 | 133.910 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.9167 | 133.915 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.9250 | 133.925 | Not allotted | ACC-L, ACC-U | ACC | ACC-U | ACC-L, ACC-U | ACC |
| 133.9250 | 133.930 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.9333 | 133.935 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.9417 | 133.940 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.9500 | 133.950 | Not allotted | ACC-L, ACC-U | ACC | ACC-U | ACC-L, ACC-U | ACC |
| 133.9500 | 133.955 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.9583 | 133.960 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.9667 | 133.965 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.9750 | 133.975 | Not allotted | ACC-L, ACC-U | ACC | ACC-U | ACC-L, ACC-U | ACC |
| 133.9750 | 133.980 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.9833 | 133.985 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 133.9917 | 133.990 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.0000 | 134.000 | Not allotted | ACC-L, ACC-U | ACC | ACC-U | ACC-L, ACC-U | ACC |
| 134.0000 | 134.005 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.0083 | 134.010 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.0167 | 134.015 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.0250 | 134.025 | Not allotted | ACC-L, ACC-U | ACC | ACC-U | ACC-L, ACC-U | ACC |
| 134.0250 | 134.030 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.0333 | 134.035 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.0417 | 134.040 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.0500 | 134.050 | Not allotted | ACC-L, ACC-U | ACC | ACC-U | ACC-L, ACC-U | ACC |
| 134.0500 | 134.055 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.0583 | 134.060 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.0667 | 134.065 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.0750 | 134.075 | Not allotted | ACC-L, ACC-U | ACC | ACC-U | ACC-L, ACC-U | ACC |
| 134.0750 | 134.080 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.0833 | 134.085 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.0917 | 134.090 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.1000 | 134.100 | Not allotted | ACC-L, ACC-U | ACC | ACC-U | ACC-L, ACC-U | ACC |
| 134.1000 | 134.105 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.1083 | 134.110 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.1167 | 134.115 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.1250 | 134.125 | Not allotted | ACC-L, ACC-U | ACC | ACC-U | ACC-L, ACC-U | ACC |
| 134.1250 | 134.130 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.1333 | 134.135 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.1417 | 134.140 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.1500 | 134.150 | Not allotted | ACC-L, ACC-U | ACC | ACC-U | ACC-L, ACC-U | ACC |
| 134.1500 | 134.155 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.1583 | 134.160 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.1667 | 134.165 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.1750 | 134.175 | Not allotted | ACC-L, ACC-U | ACC | ACC-U | ACC-L, ACC-U | ACC |
| 134.1750 | 134.180 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.1833 | 134.185 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.1917 | 134.190 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.2000 | 134.200 | Not allotted | ACC-L, ACC-U | ACC | ACC-U | ACC-L, ACC-U | ACC |
| 134.2000 | 134.205 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.2083 | 134.210 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.2167 | 134.215 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.2250 | 134.225 | Not allotted | ACC-L, ACC-U | ACC | ACC-U | ACC-L, ACC-U | ACC |
| 134.2250 | 134.230 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.2333 | 134.235 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.2417 | 134.240 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.2500 | 134.250 | Not allotted | ACC-L, ACC-U | ACC | ACC-U | ACC-L, ACC-U | ACC |
| 134.2500 | 134.255 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.2583 | 134.260 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.2667 | 134.265 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.2750 | 134.275 | Not allotted | ACC-L, ACC-U | ACC | ACC-U | ACC-L, ACC-U | ACC |
| 134.2750 | 134.280 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.2833 | 134.285 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.2917 | 134.290 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.3000 | 134.300 | Not allotted | ACC-L, ACC-U | ACC | ACC-U | ACC-L, ACC-U | ACC |
| 134.3000 | 134.305 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.3083 | 134.310 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.3167 | 134.315 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.3250 | 134.325 | Not allotted | ACC-L, ACC-U | ACC | ACC-U | ACC-L, ACC-U | ACC |
| 134.3250 | 134.330 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.3333 | 134.335 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.3417 | 134.340 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.3500 | 134.350 | Not allotted | ACC-L, ACC-U | ACC | ACC-U | ACC-L, ACC-U | ACC |
| 134.3500 | 134.355 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.3583 | 134.360 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.3667 | 134.365 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.3750 | 134.375 | Not allotted | ACC-L, ACC-U | ACC | ACC-U | ACC-L, ACC-U | ACC |
| 134.3750 | 134.380 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.3833 | 134.385 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.3917 | 134.390 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.4000 | 134.400 | Not allotted | ACC-L, ACC-U | ACC | ACC-U | ACC-L, ACC-U | ACC |
| 134.4000 | 134.405 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.4083 | 134.410 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.4167 | 134.415 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.4250 | 134.425 | Not allotted | ACC-L, ACC-U | ACC | ACC-U | ACC-L, ACC-U | ACC |
| 134.4250 | 134.430 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.4333 | 134.435 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.4417 | 134.440 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.4500 | 134.450 | Not allotted | ACC-L, ACC-U | ACC | ACC-U | ACC-L, ACC-U | ACC |
| 134.4500 | 134.455 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.4583 | 134.460 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.4667 | 134.465 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.4750 | 134.475 | Not allotted | ACC-L, ACC-U | ACC | ACC-U | ACC-L, ACC-U | ACC |
| 134.4750 | 134.480 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.4833 | 134.485 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.4917 | 134.490 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.5000 | 134.500 | Not allotted | ACC-L, ACC-U | ACC | ACC-U | ACC-L, ACC-U | ACC |
| 134.5000 | 134.505 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.5083 | 134.510 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.5167 | 134.515 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.5250 | 134.525 | Not allotted | Not allotted | ACC | ACC-U | Not allotted | ACC |
| 134.5250 | 134.530 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.5333 | 134.535 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.5417 | 134.540 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.5500 | 134.550 | Not allotted | Not allotted | ACC | ACC-U | Not allotted | ACC |
| 134.5500 | 134.555 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.5583 | 134.560 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.5667 | 134.565 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.5750 | 134.575 | Not allotted | Not allotted | ACC | ACC-U | Not allotted | ACC |
| 134.5750 | 134.580 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.5833 | 134.585 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.5917 | 134.590 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.6000 | 134.600 | Not allotted | FIS-U (GPS) | ACC | ACC-U | FIS-U (GPS) | ACC |
| 134.6000 | 134.605 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.6083 | 134.610 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.6167 | 134.615 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.6250 | 134.625 | Not allotted | FIS-U (GPS) | ACC | ACC-U | FIS-U (GPS) | ACC |
| 134.6250 | 134.630 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.6333 | 134.635 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.6417 | 134.640 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.6500 | 134.650 | Not allotted | FIS-U (GPS) | ACC | ACC-U | FIS-U (GPS) | ACC |
| 134.6500 | 134.655 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.6583 | 134.660 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.6667 | 134.665 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.6750 | 134.675 | Not allotted | FIS-U (GPS) | ACC | ACC-U | FIS-U (GPS) | ACC |
| 134.6750 | 134.680 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.6833 | 134.685 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.6917 | 134.690 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.7000 | 134.700 | Not allotted | FIS-U (GPS) | ACC | ACC-U | FIS-U (GPS) | ACC |
| 134.7000 | 134.705 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.7083 | 134.710 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.7167 | 134.715 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.7250 | 134.725 | Not allotted | FIS-U (GPS) | ACC | ACC-U | FIS-U (GPS) | ACC |
| 134.7250 | 134.730 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.7333 | 134.735 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.7417 | 134.740 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.7500 | 134.750 | Not allotted | FIS-U (GPS) | ACC | ACC-U | FIS-U (GPS) | ACC |
| 134.7500 | 134.755 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.7583 | 134.760 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.7667 | 134.765 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.7750 | 134.775 | Not allotted | FIS-U (GPS) | ACC | ACC-U | FIS-U (GPS) | ACC |
| 134.7750 | 134.780 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.7833 | 134.785 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.7917 | 134.790 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.8000 | 134.800 | Not allotted | FIS-U (GPS) | ACC | ACC-U | FIS-U (GPS) | ACC |
| 134.8000 | 134.805 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.8083 | 134.810 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.8167 | 134.815 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.8250 | 134.825 | Not allotted | FIS-U (GPS) | ACC | ACC-U | FIS-U (GPS) | ACC |
| 134.8250 | 134.830 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.8333 | 134.835 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.8417 | 134.840 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.8500 | 134.850 | Not allotted | FIS-U (GPS) | ACC | ACC-U | FIS-U (GPS) | ACC |
| 134.8500 | 134.855 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.8583 | 134.860 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.8667 | 134.865 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.8750 | 134.875 | Not allotted | FIS-U (GPS) | ACC | ACC-U | FIS-U (GPS) | ACC |
| 134.8750 | 134.880 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.8833 | 134.885 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.8917 | 134.890 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.9000 | 134.900 | Not allotted | FIS-U (GPS) | ACC | ACC-U | FIS-U (GPS) | ACC |
| 134.9000 | 134.905 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.9083 | 134.910 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.9167 | 134.915 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.9250 | 134.925 | Not allotted | FIS-U (GPS) | ACC | ACC-U | FIS-U (GPS) | ACC |
| 134.9250 | 134.930 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.9333 | 134.935 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.9417 | 134.940 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.9500 | 134.950 | Not allotted | FIS-U (GPS) | ACC | ACC-U | FIS-U (GPS) | ACC |
| 134.9500 | 134.955 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.9583 | 134.960 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.9667 | 134.965 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.9750 | 134.975 | Not allotted | FIS-U (GPS) | ACC | ACC-U | FIS-U (GPS) | ACC |
| 134.9750 | 134.980 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.9833 | 134.985 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 134.9917 | 134.990 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.0000 | 135.000 | Not allotted | FIS-U (GPS) | ACC | ACC-U | FIS-U (GPS) | ACC |
| 135.0000 | 135.005 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.0083 | 135.010 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.0167 | 135.015 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.0250 | 135.025 | Not allotted | FIS-U (GPS) | ACC | ACC-U | FIS-U (GPS) | ACC |
| 135.0250 | 135.030 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.0333 | 135.035 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.0417 | 135.040 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.0500 | 135.050 | Not allotted | FIS-U (GPS) | ACC | ACC-U | FIS-U (GPS) | ACC |
| 135.0500 | 135.055 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.0583 | 135.060 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.0667 | 135.065 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.0750 | 135.075 | Not allotted | FIS-U (GPS) | ACC | ACC-U | FIS-U (GPS) | ACC |
| 135.0750 | 135.080 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.0833 | 135.085 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.0917 | 135.090 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.1000 | 135.100 | Not allotted | FIS-U (GPS) | ACC | ACC-U | FIS-U (GPS) | ACC |
| 135.1000 | 135.105 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.1083 | 135.110 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.1167 | 135.115 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.1250 | 135.125 | Not allotted | FIS-U (GPS) | ACC | ACC-U | FIS-U (GPS) | ACC |
| 135.1250 | 135.130 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.1333 | 135.135 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.1417 | 135.140 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.1500 | 135.150 | Not allotted | FIS-U (GPS) | ACC | ACC-U | FIS-U (GPS) | ACC |
| 135.1500 | 135.155 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.1583 | 135.160 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.1667 | 135.165 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.1750 | 135.175 | Not allotted | FIS-U (GPS) | ACC | ACC-U | FIS-U (GPS) | ACC |
| 135.1750 | 135.180 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.1833 | 135.185 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.1917 | 135.190 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.2000 | 135.200 | Not allotted | FIS-U (GPS) | ACC | ACC-U | FIS-U (GPS) | ACC |
| 135.2000 | 135.205 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.2083 | 135.210 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.2167 | 135.215 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.2250 | 135.225 | Not allotted | FIS-U (GPS) | ACC | ACC-U | FIS-U (GPS) | ACC |
| 135.2250 | 135.230 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.2333 | 135.235 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.2417 | 135.240 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.2500 | 135.250 | Not allotted | FIS-U (GPS) | ACC | ACC-U | FIS-U (GPS) | ACC |
| 135.2500 | 135.255 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.2583 | 135.260 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.2667 | 135.265 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.2750 | 135.275 | Not allotted | FIS-U (GPS) | ACC | ACC-U | FIS-U (GPS) | ACC |
| 135.2750 | 135.280 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.2833 | 135.285 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.2917 | 135.290 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.3000 | 135.300 | Not allotted | FIS-U (GPS) | ACC | ACC-U | FIS-U (GPS) | ACC |
| 135.3000 | 135.305 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.3083 | 135.310 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.3167 | 135.315 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.3250 | 135.325 | Not allotted | FIS-U (GPS) | ACC | ACC-U | FIS-U (GPS) | ACC |
| 135.3250 | 135.330 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.3333 | 135.335 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.3417 | 135.340 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.3500 | 135.350 | Not allotted | FIS-U (GPS) | ACC | ACC-U | FIS-U (GPS) | ACC |
| 135.3500 | 135.355 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.3583 | 135.360 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.3667 | 135.365 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.3750 | 135.375 | Not allotted | FIS-U (GPS) | ACC | ACC-U | FIS-U (GPS) | ACC |
| 135.3750 | 135.380 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.3833 | 135.385 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.3917 | 135.390 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.4000 | 135.400 | Not allotted | FIS-U (GPS) | ACC | ACC-U | FIS-U (GPS) | ACC |
| 135.4000 | 135.405 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.4083 | 135.410 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.4167 | 135.415 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.4250 | 135.425 | Not allotted | FIS-U (GPS) | ACC | ACC-U | FIS-U (GPS) | ACC |
| 135.4250 | 135.430 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.4333 | 135.435 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.4417 | 135.440 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.4500 | 135.450 | Not allotted | FIS-U (GPS) | ACC | ACC-U | FIS-U (GPS) | ACC |
| 135.4500 | 135.455 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.4583 | 135.460 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.4667 | 135.465 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.4750 | 135.475 | Not allotted | FIS-U (GPS) | ACC | ACC-U | FIS-U (GPS) | ACC |
| 135.4750 | 135.480 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.4833 | 135.485 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.4917 | 135.490 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.5000 | 135.500 | Not allotted | FIS-U (GPS) | ACC | ACC-U | FIS-U (GPS) | ACC |
| 135.5000 | 135.505 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.5083 | 135.510 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.5167 | 135.515 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.5250 | 135.525 | Not allotted | FIS-U (GPS) | ACC | ACC-U | FIS-U (GPS) | ACC |
| 135.5250 | 135.530 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.5333 | 135.535 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.5417 | 135.540 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.5500 | 135.550 | Not allotted | FIS-U (GPS) | ACC | ACC-U | FIS-U (GPS) | ACC |
| 135.5500 | 135.555 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.5583 | 135.560 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.5667 | 135.565 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.5750 | 135.575 | Not allotted | FIS-U (GPS) | ACC | ACC-U | FIS-U (GPS) | ACC |
| 135.5750 | 135.580 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.5833 | 135.585 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.5917 | 135.590 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.6000 | 135.600 | Not allotted | FIS-U (GPS) | ACC | ACC-U | FIS-U (GPS) | ACC |
| 135.6000 | 135.605 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.6083 | 135.610 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.6167 | 135.615 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.6250 | 135.625 | Not allotted | FIS-U (GPS) | ACC | ACC-U | FIS-U (GPS) | ACC |
| 135.6250 | 135.630 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.6333 | 135.635 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.6417 | 135.640 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.6500 | 135.650 | Not allotted | FIS-U (GPS) | ACC | ACC-U | FIS-U (GPS) | ACC |
| 135.6500 | 135.655 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.6583 | 135.660 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.6667 | 135.665 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.6750 | 135.675 | Not allotted | FIS-U (GPS) | ACC | ACC-U | FIS-U (GPS) | ACC |
| 135.6750 | 135.680 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.6833 | 135.685 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.6917 | 135.690 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.7000 | 135.700 | Not allotted | FIS-U (GPS) | ACC | ACC-U | FIS-U (GPS) | ACC |
| 135.7000 | 135.705 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.7083 | 135.710 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.7167 | 135.715 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.7250 | 135.725 | Not allotted | FIS-U (GPS) | ACC | ACC-U | FIS-U (GPS) | ACC |
| 135.7250 | 135.730 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.7333 | 135.735 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.7417 | 135.740 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.7500 | 135.750 | Not allotted | FIS-U (GPS) | ACC | ACC-U | FIS-U (GPS) | ACC |
| 135.7500 | 135.755 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.7583 | 135.760 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.7667 | 135.765 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.7750 | 135.775 | Not allotted | FIS-U (GPS) | ACC | ACC-U | FIS-U (GPS) | ACC |
| 135.7750 | 135.780 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.7833 | 135.785 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.7917 | 135.790 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.8000 | 135.800 | Not allotted | FIS-U (GPS) | ACC | ACC-U | FIS-U (GPS) | ACC |
| 135.8000 | 135.805 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.8083 | 135.810 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.8167 | 135.815 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.8250 | 135.825 | Not allotted | Not allotted | ACC | ACC-U | Not allotted | ACC |
| 135.8250 | 135.830 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.8333 | 135.835 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.8417 | 135.840 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.8500 | 135.850 | Not allotted | Not allotted | ACC | ACC-U | Not allotted | ACC |
| 135.8500 | 135.855 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.8583 | 135.860 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.8667 | 135.865 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.8750 | 135.875 | Not allotted | Not allotted | ACC | ACC-U | Not allotted | ACC |
| 135.8750 | 135.880 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.8833 | 135.885 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.8917 | 135.890 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.9000 | 135.900 | Not allotted | Not allotted | ACC | ACC-U | Not allotted | ACC |
| 135.9000 | 135.905 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.9083 | 135.910 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.9167 | 135.915 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.9250 | 135.925 | Not allotted | Not allotted | ACC | ACC-U | Not allotted | ACC |
| 135.9250 | 135.930 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.9333 | 135.935 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.9417 | 135.940 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.9500 | 135.950 | Not allotted | Not allotted | ACC | ACC-U | Not allotted | ACC |
| 135.9500 | 135.955 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.9583 | 135.960 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.9667 | 135.965 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.9750 | 135.975 | Not allotted | Not allotted | Not allotted | ACC-U | Not allotted | Not allotted |
| 135.9750 | 135.980 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.9833 | 135.985 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 135.9917 | 135.990 | Not used | Not used | Not used | ACC-U | Not used | Not used |
| 136.0000 | 136.000 | Not allotted | VDL | Not allotted | Not allotted | Not allotted | Not allotted |
| 136.0000 | 136.005 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 136.0083 | 136.010 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 136.0167 | 136.015 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 136.0250 | 136.025 | Not allotted | VDL | Not allotted | Not allotted | Not allotted | Not allotted |
| 136.0250 | 136.030 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 136.0333 | 136.035 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 136.0417 | 136.040 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 136.0500 | 136.050 | Not allotted | VDL | Not allotted | Not allotted | Not allotted | Not allotted |
| 136.0500 | 136.055 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 136.0583 | 136.060 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 136.0667 | 136.065 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 136.0750 | 136.075 | Not allotted | VDL | Not allotted | Not allotted | Not allotted | Not allotted |
| 136.0750 | 136.080 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 136.0833 | 136.085 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 136.0917 | 136.090 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 136.1000 | 136.100 | Not allotted | VDL | Not allotted | Not allotted | Not allotted | Not allotted |
| 136.1000 | 136.105 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 136.1083 | 136.110 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 136.1167 | 136.115 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 136.1250 | 136.125 | Not allotted | VDL | Not allotted | Not allotted | Not allotted | Not allotted |
| 136.1250 | 136.130 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 136.1333 | 136.135 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 136.1417 | 136.140 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 136.1500 | 136.150 | Not allotted | VDL | Not allotted | Not allotted | Not allotted | Not allotted |
| 136.1500 | 136.155 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 136.1583 | 136.160 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 136.1667 | 136.165 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 136.1750 | 136.175 | Not allotted | VDL | Not allotted | Not allotted | Not allotted | Not allotted |
| 136.1750 | 136.180 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 136.1833 | 136.185 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 136.1917 | 136.190 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 136.2000 | 136.200 | Not allotted | VDL | Not allotted | Not allotted | Not allotted | Not allotted |
| 136.2000 | 136.205 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 136.2083 | 136.210 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 136.2167 | 136.215 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 136.2250 | 136.225 | Not allotted | VDL | Not allotted | Not allotted | Not allotted | Not allotted |
| 136.2250 | 136.230 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 136.2333 | 136.235 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 136.2417 | 136.240 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 136.2500 | 136.250 | Not allotted | VDL | Not allotted | Not allotted | Not allotted | Not allotted |
| 136.2500 | 136.255 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 136.2583 | 136.260 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 136.2667 | 136.265 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 136.2750 | 136.275 | Not allotted | VDL | Not allotted | Not allotted | Not allotted | Not allotted |
| 136.2750 | 136.280 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 136.2833 | 136.285 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 136.2917 | 136.290 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 136.3000 | 136.300 | Not allotted | VDL | Not allotted | Not allotted | Not allotted | Not allotted |
| 136.3000 | 136.305 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 136.3083 | 136.310 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 136.3167 | 136.315 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 136.3250 | 136.325 | Not allotted | VDL | Not allotted | Not allotted | Not allotted | Not allotted |
| 136.3250 | 136.330 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 136.3333 | 136.335 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 136.3417 | 136.340 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 136.3500 | 136.350 | Not allotted | VDL | Not allotted | Not allotted | Not allotted | Not allotted |
| 136.3500 | 136.355 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 136.3583 | 136.360 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 136.3667 | 136.365 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 136.3750 | 136.375 | Not allotted | VDL | Not allotted | Not allotted | Not allotted | Not allotted |
| 136.3750 | 136.380 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 136.3833 | 136.385 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 136.3917 | 136.390 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 136.4000 | 136.400 | Not allotted | VDL | Not allotted | Not allotted | Not allotted | Not allotted |
| 136.4000 | 136.405 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 136.4083 | 136.410 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 136.4167 | 136.415 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 136.4250 | 136.425 | Not allotted | VDL | Not allotted | Not allotted | Not allotted | Not allotted |
| 136.4250 | 136.430 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 136.4333 | 136.435 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 136.4417 | 136.440 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 136.4500 | 136.450 | Not allotted | VDL | Not allotted | Not allotted | Not allotted | Not allotted |
| 136.4500 | 136.455 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 136.4583 | 136.460 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 136.4667 | 136.465 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 136.4750 | 136.475 | Not allotted | VDL | Not allotted | Not allotted | Not allotted | Not allotted |
| 136.4750 | 136.480 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 136.4833 | 136.485 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 136.4917 | 136.490 | Not used | Not used | Not used | Not allotted | Not used | Not used |
| 136.5000 | 136.500 | Not allotted | VDL | Not allotted | Not allotted | Not allotted | Not allotted |
| 136.5000 | 136.505 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 136.5083 | 136.510 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 136.5167 | 136.515 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 136.5250 | 136.525 | Not allotted | VDL | Not allotted | VDL | Not allotted | Not allotted |
| 136.5250 | 136.530 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 136.5333 | 136.535 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 136.5417 | 136.540 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 136.5500 | 136.550 | Not allotted | VDL | Not allotted | VDL | Not allotted | Not allotted |
| 136.5500 | 136.555 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 136.5583 | 136.560 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 136.5667 | 136.565 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 136.5750 | 136.575 | Not allotted | VDL | Not allotted | VDL | Not allotted | Not allotted |
| 136.5750 | 136.580 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 136.5833 | 136.585 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 136.5917 | 136.590 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 136.6000 | 136.600 | Not allotted | VDL | Not allotted | VDL | Not allotted | Not allotted |
| 136.6000 | 136.605 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 136.6083 | 136.610 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 136.6167 | 136.615 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 136.6250 | 136.625 | Not allotted | VDL | Not allotted | VDL | Not allotted | Not allotted |
| 136.6250 | 136.630 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 136.6333 | 136.635 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 136.6417 | 136.640 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 136.6500 | 136.650 | Not allotted | VDL | Not allotted | VDL | Not allotted | Not allotted |
| 136.6500 | 136.655 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 136.6583 | 136.660 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 136.6667 | 136.665 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 136.6750 | 136.675 | Not allotted | VDL | Not allotted | VDL | Not allotted | Not allotted |
| 136.6750 | 136.680 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 136.6833 | 136.685 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 136.6917 | 136.690 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 136.7000 | 136.700 | Not allotted | VDL | Not allotted | VDL | Not allotted | Not allotted |
| 136.7000 | 136.705 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 136.7083 | 136.710 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 136.7167 | 136.715 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 136.7250 | 136.725 | Not allotted | VDL | Not allotted | VDL | Not allotted | Not allotted |
| 136.7250 | 136.730 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 136.7333 | 136.735 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 136.7417 | 136.740 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 136.7500 | 136.750 | Not allotted | VDL | Not allotted | VDL | Not allotted | Not allotted |
| 136.7500 | 136.755 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 136.7583 | 136.760 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 136.7667 | 136.765 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 136.7750 | 136.775 | Not allotted | VDL | Not allotted | VDL | Not allotted | Not allotted |
| 136.7750 | 136.780 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 136.7833 | 136.785 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 136.7917 | 136.790 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 136.8000 | 136.800 | Not allotted | VDL | Not allotted | VDL | Not allotted | Not allotted |
| 136.8000 | 136.805 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 136.8083 | 136.810 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 136.8167 | 136.815 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 136.8250 | 136.825 | Not allotted | VDL | Not allotted | VDL | Not allotted | Not allotted |
| 136.8250 | 136.830 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 136.8333 | 136.835 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 136.8417 | 136.840 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 136.8500 | 136.850 | Not allotted | VDL | Not allotted | VDL | Not allotted | Not allotted |
| 136.8500 | 136.855 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 136.8583 | 136.860 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 136.8667 | 136.865 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 136.8750 | 136.875 | Not allotted | VDL | Not allotted | VDL | Not allotted | Not allotted |
| 136.8750 | 136.880 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 136.8833 | 136.885 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 136.8917 | 136.890 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 136.9000 | 136.900 | VDL | VDL | VDL | VDL | VDL | VDL |
| 136.9000 | 136.905 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 136.9083 | 136.910 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 136.9167 | 136.915 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 136.9250 | 136.925 | VDL | VDL | VDL | VDL | VDL | VDL |
| 136.9250 | 136.930 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 136.9333 | 136.935 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 136.9417 | 136.940 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 136.9500 | 136.950 | VDL | VDL | VDL | VDL | VDL | VDL |
| 136.9500 | 136.955 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 136.9583 | 136.960 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 136.9667 | 136.965 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 136.9750 | 136.975 | VDL | VDL | VDL | VDL | VDL | VDL |
| 136.9750 | 136.980 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 136.9833 | 136.985 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 136.9917 | 136.990 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |
| 137.0000 | 137.000 | Blocked | Blocked | Blocked | Blocked | Blocked | Blocked |