AERONAUTICAL COMMUNICATIONS PANEL (ACP)

TWENTYSEVENTH MEETING OF WORKING GROUP F

Montreal, Canada 17 – 26 September 2012

| Agenda Item: 2 | Development of ICAO position for WRC-15 |
| --- | --- |

X-Band sharing of EESS with PAR, ASDE, ASR

(Prepared by /Presented by Joachim Wollweber)

SUMMARY

WRC 15 Agenda Item 1.12 with possibly impact to aeronautical services is the proposed extension of the range 9000 to 9200 MHz for Earth exploration satellite Service (EESS), currently used e.g. for Precision Approach Radar (PAR), Airport Surface Detection Equipment (ASDE), Airport Surface Movement Radar (ASMR) sometimes combined with Airport Surface Radar (ASR) with Range up to 25 NM. It is argued during the last ITU-R WP5B meeting, that the impact on the aeronautical services has already been proven since the technical data is mainly identical to those equipments dealt with at previous sharing studies performed during past allocation for the EESS above 9200 MHz. While it is true that some Radar types used by ARNS also operate above 9200 MHz, others like PAR do not. Furthermore the equipment types considered in the past were only un-modulated pulse Radars, having short pulses around 40 ns and PRF in excess of 8000 Hz. In lieu of magnetron-based designs manufacturers offer now solid-state-based Radars that utilize pulse-compression modulation. The compatibility of these new Radar technologies with the aforementioned aeronautical systems have not yet been analyzed. Therefore in addition to studying the compatibility of EESS with aeronautical Radars in the band 9000 to 9200 MHz also the compatibility in the band 9200 to 9500 MHz band needs to be studied.

# Introduction to X-Band RADAR used for ARNS:

WRC-15 Agenda Item 1.12 calls to consider an extension of the current worldwide allocation to the Earth exploration-satellite (active) service in the frequency band 9 300-9 900 MHz by up to 600 MHz within the frequency bands 8 700-9 300 MHz and/or 9 900-10 500 MHz.

In this context it should be emphasized, that for ARNS the following RADAR applications are in use in the Band 900 to 9200 MHz:

- PAR (Precision Approach Radar)

- ASDE or ASMR (Airport Surface Detection Equipment, Airport Surface Movement Radar)

- ASR combined with PAR or ASDE

All of these systems operate either using two scanning antennas, one for azimuth and elevation guidance in case of a PAR, or rotating antennas for ASDE, ASMR and ASR. While originally only single frequency design, for redundancy and to improve the probability of detection dual frequency designs are now commonly used. Short pulses of about 40 ns in duration are transmitted with a PRF of 8000 Hz or higher, while the antenna rotates with about 60 RPM. Antenna gains are around 38 dBi The Magnetrons used for the generation of the pulses have a transmitter output of up to 40 kW. The occupied bandwidth and therefore receiver bandwidth is sufficiently large to allow for drift of the Magnetron during operation, for the systems known to the author about 70 MHz. Radar with short-pulses allow sharing of multiple Radar in the same aerodrome due to the Pulse Width, PRF, and RPM commonly used.

Moreover, for PAR, ASDE and ASMR solid state transmitter are replacing magnetrons. Since about ten years frequency agile PAR were introduced that employ 4 or more frequencies and now more ASDE and ASMR are available.

The solid state technology allows pulse compression by means of modulation.  Furthermore it became common to transmit multiple pulses in succession (e.g. 3) which differ in length and frequency they are transmitted on, thus requiring different frequencies for each pulse  in order not to interfere with a previously used frequency in the available frequency range 9000 to 9200 MHz or 9200 MHz to 9500 MHz. Attachment I provides a comparison of three different modern radio determination Radars manufactured Terma. The principle of frequency hopping using pulse-compressed signals of different duration are shown in Att. II 6.2 Radar Settings, which documents transmitter testing. However the, receiver requirements and their interference susceptibility are yet unknown.

Technical details differ from design to design, from manufacturer to manufacturer confidential and are mostly viewed as confidential. Manufacturers offer only basic information like transmitter output power, antenna gain, beam- or pulse-width, but not the for sharing studies relevant information on the receiver nor the post processing needed to evaluate the interference sensitivity to other signal types, like the ones proposed by EESS. The pulse-compression used for signals, their duration, modulation type or hopping sequence are not universally harmonized.

It has to be noted that without the information of technical and operational equipments of these Radar types ITU will not include them in their studies and therefore no protection is provided.

At the time of preparation of this paper, neither technical nor operational details about the signals to be transmitted by EESS are available. Therefore no evaluation of the electromagnetic compatibility with the aforementioned aeronautical systems is possible.

# Conclusion:

Without that manufacturer will provide the required technical and operational equipments no sharing studies will be performed for this Radar types within ITU.

While it may not be impossible to allow sharing with the restrictions that e.g. operation of EESS is limited to night times when airport in the area of transmission of the EESS are not in operation for aerodrome control or APP and DEP services, it is advised not to agree to a sharing until actual interference studies on the currently available RADAR designs have been performed.

Furthermore it is advised/cautioned that any future designs of RADAR for ARNS purposes require similar measurements and may require further restriction for the EESS operator,

Prior accepting shall be subjected to a similar detailed interference susceptibility measurement before allowing their use, and that additional restrictions can be imposed to EESS, allowing ARNS RADAR to maintain improvement in operation as technical evolution allows.

# Recommendation:

- Based on the lack of information no positive statements for a sharing with EESS the present draft ICAO position on WRC-15 agenda item 1.12.

- To obtain an overview of the aeronautical use of the relevant frequency bands, a questionnaire to civil and military ANSP should identify the RADAR systems currently in operation or planned to be procured for operation

- Manufacturers of the equipment identified in the questionnaire above should be questioned by ANSP that procured the equipment, to provide a feedback on conducted  interference compatibility studies

- EESS providers shall provide signal generators capable of generating the signals to be used for EESS upon request to ANSP and manufacturer to allow interference compatibility tests.

- ANSPs to inform their national representatives within ITU of the need to establish the allowable interference values for the band 9000 to 9200 MHz and also for those equipment employing pulse compressed signal in the band 9200 to 9500 MHz.

- Urge states to provide any available relevant progress report to WG-F

- Urge ANSP that already employ or plan to procure Radar utilizing  pulse compression, to lean on their manufacturer to provide the required technical and operational information, to allow sharing studies within WRC, and in consequence ensure protection of ARNS equipment

Acknowledgement:

The author would like to acknowledge the support of his colleague Felix Butsch in proofreading and streamlining this paper.

Apendix I:  Draft ICAO Position on WRC 15 Agenda Item 1.12 (May 2012)

Oppose any allocation to the Earth exploration-satellite service in the frequency band 9 000 – 9 200 MHz unless:-

- unless it has been demonstrated through agreed studies that there will be no impact on aviation use.

- no additional constraints are place on the use of the frequency band by aeronautical systems

No change to Nos. 5.337, 5.427, 5.474 and 5.475.

Attachment I:

Characteristics of modern radio determination radars in the 8 700-9 300 MHz band

provided by Terma A/S,  Lystrup, Denmark, June 2012

| Characteristics |  | Scanter 5000 system | Scanter 5000 system | Scanter 4000 System |
| --- | --- | --- | --- | --- |
| Function |  | Airport Surface movement Radar | Coastal Surveillance / Vessel Traffic System Radar | Coastal Surveillance / Vessel Traffic System Radar |
| Tuning range | MHz | 9 000-9 200 | 9 225-9 500 | 8800-9450 |
| Modulation |  | Pulse Compression | Pulse Compression | Pulse Compression |
| Peak power | kW | 0.05 | 0.05 or 0.2 | 12 |
| Pulse widths | μs | 0.08 - 100 | 0.08 – 100 | 40 (2x) |
| Pulse repetition rate | pps | 1000 - 10.000 | 1000 - 10.000 | 3900 (short pulse) 700 (long pulse) |
| Max. duty cycle |  | 0.2 | 0.2 | 0.05 |
| Pulse rise times | (s | 0.02 | 0.02 | 0.02 |
| Pulse fall times | μs | 0.02 | 0.02 | 0.02 |
| Antenna pattern type |  | Fan | Fan | Fan |
| Antenna type |  | Slotted Waveguide | Slotted Waveguide | Slotted Waveguide |
| Antenna polarisation |  | Circular | Circular | Circular / Horizontal |
| Main beam gain | dBi | 38 | 38 | 42 |
| Elev. beamwidth | ° | 11 | 11 | 4 |
| Azim. beamwidth | ° | 0.36 | 0.36 | 0.36 |
| Horiz. scan rate | °/s | 60 - 288 | 60 – 288 | 24 - 90 |
| Horiz. scan type |  | Continuous or sectors | Continuous or sectors | Continuous or sectors |
| Vert. scan rate | °/s | N/A | N/A | N/A |
| Vert. scan type |  | N/A | N/A | N/A |
| Side lobe levels (antenna) |  | 28dB | 28dB | 26dB |
| Antenna height | m | Normally 30-75 | Normally 30-100 | Normally 50-100 |
| Receiver IF 3dB bandwidth | MHz | 180 | 180 | 40 |
| Receiver noise figure | dB | 2.5 | 2.5 | 2.5 dB |
| Min. discernible signal | dBm | -130 | -130 | -121 |
| Dynamic range | dB | 90 (140 incl STC) | 90 (140 incl STC) | 140 |
| Min. number of processed pulses |  | 8 | 8 | 8 |
| Total chirp width | MHz | Normally 4*35MHz | Normally 6*35MHz | Normally 8*20MHz |
| RF emission bandwidth 3 dB | MHz | 170 | 240 | 600 |
| RF emission bandwidth 20 dB | MHz | 200 | 275 | 700 |

Attachment II:

Embedded File “Scanter 50006000 200W Spectrum Measurements (RPT - 386300-RL - 1 - B).pdf”