|  | International Civil Aviation Organization WORKING PAPER | ACP-WGF28/WP-12 2013-03-11 |
| --- | --- | --- |

AERONAUTICAL COMMUNICATIONS PANEL (ACP)

28TH MEETING OF THE WORKING GROUP F

Lima, Peru, 11 – 22 March 2013

| Agenda Item X : | Any Other Business |
| --- | --- |

Proposal from ITU-R WP5A for the Public Mobile Communications with aircraft

(Presented by India)

SUMMARY

This paper provides information to WG-F members on the preliminary draft report developed by ITU-R WP-5A on systems for public mobile communication with aircraft.

ACTION

WG-F to note the paper and consider developing suitable input before next WP-5A meeting to assist states.

INTRODUCTION

At its November 2012 Meeting, ITU-R WP5A has developed a preliminary draft report (Document 5A/198-E) on systems for public mobile communication with aircraft. This report deals with the general principles, technical characteristics and operational features of terrestrial systems for public mobile communication services onboard aircraft in each Region separately.

discussion

Of late, there is a growing demand to provide for various types of telecommunications services such as broadband internet communication access and mobile multimedia services during flights. The proposed systems are intended to support non-safety related Aeronautical Passenger Communications (APC) and also Aeronautical Administrative Communication (AAC) Services to meet increasing capacity demand by passenger and airline related services by establishing high performance radio links to aircrafts.

It should be mentioned that the proposals on technical characteristics and operational features of the system for public communications with aircrafts are finalized in some countries of Region1, 2 & 3 separately. WP5A has annexed all the three proposals in its draft report. (Please see the attachment).

In Region-3, it is understood that China has already developed such a system and successfully tested its Air-to-Ground broadband communication capability. Hence, the proposal developed by WP5A for Region-3 is based on China’s input.

It should be emphasized that the stakeholders in India are keen to know the views of civil aviation on the draft proposal for Region 3 and has sought necessary inputs for consideration in the next WP-5A meeting to be held in June 2013.

It is therefore proposed that Working Group F conduct a detailed review and initiate work on developing suitable views/inputs on the proposal and enlighten the states and particularly the civil aviation community to suitably respond to the stakeholders prior to next WP5A meeting.

Aside from looking into the aspects of the spectrum needs and frequency range, such a study by WGF has to meticulously consider inter alia the systems concept and equipment compliance for relevant ICAO regulations and ITU-R regulatory regime for compatibility with aeronautical systems (both ground and airborne) supporting safety and regularity of flights.

ACTION BY THE MEETING

The ACP WGF is invited to take the proposal in to account during its deliberations and start development of suitable input prior to next WP5A meeting.

ATTACHMENT embedded:

Annex 14 to Working Party 5A Chairman’s Report

PRELIMINARY DRAFT NEW REPORT ITU-R [LMS.ATG]

Systems for public mobile communications with aircraft