Handbook  on Radio Frequency

Spectrum Requirements

for Civil  Aviation

(Doc 9718-AN/957 Ed.2)

Amendments to Chapter 7

Summary

The ICAO "Handbook on radio frequency spectrum requirements for civil aviation and statement of approved ICAO policies" (Doc 9718-AN/957) contains material relating to the radio frequency spectrum requirements for civil aviation. In this Handbook all of the frequency bands used by civil aviation for air-ground communication and radionavigation are reviewed in detail. For each band a statement of the ICAO policy approved by the Council is included. The Handbook requires periodic amendment meet evolving aviation requirements and to reflect changes to the ITU Radio Regulations as approved by World Radiocommunication Conference and developments in the study groups of the ITU-R sector and other standardization activities. Chapter 7 addresses the frequency allocations to aeronautical radio services, including the details of use, and the approved ICAO Policy for each band

This paper contains amendments to Chapter 7 of the Handbook arising from the following:

- Changes to the Radio Regulations that were agreed at WRC-2000

- Update to ICAO Policy statements as a result of these changes and the approved ICAO position for the WRC-2003

- Update of narrative text and removal of obsolete material

- Textural enhancements to improve presentation.

It is intended that the third Edition of the Handbook will be published during the second half of 2001 and will incorporate these amendments.

Chapter 7

STATEMENT OF FREQUENCY ALLOCATIONS,

TECHNICAL DETAILS AND

ICAO POLICY

This chapter addresses the main subject matter in detail, structured as follows:

Section 7-I. List of frequency bands.

Section 7-II. Civil aviation frequency allocations — ICAO policies and related information including a composite statement for each frequency band:

·	allocation table;

·	footnotes;

·	ICAO policy;

·	aviation use;

·	commentary;

·	technical and other information;

·	interference from non-aeronautical sources.

Section 7-III. Radio Regulations and other ITU material of importance to aeronautical services and Appendices including:

·	identification of chapter and regulations of interest;

·	ICAO policy.

Section 7-IV. ITU Resolutions and Recommendations, including:

·	reference to all resolutions and recommendations of the Radio Regulations affecting aeronautical services;

·	 ICAO policy for each Resolution and Recommendation of the Radio Regulations

— — — — — — — — —

SECTION 7-I.  LIST OF FREQUENCY BANDS

Note.— The numbering of the provisions of the Radio Regulations conforms to the  numbering scheme adopted at WRC-95.

| Band | Service | Aviation use | Section 7-II page no. |
| --- | --- | --- | --- |
| 90–110 kHz | RN | Loran-C |  |
| 130–535 kHz | ARN | NDB/location |  |
| 1 800–2000 kHz | RN | Loran-A |  |
| 2 850–22000 kHz | AM(R)S | Air-ground communications (HF voice and data) |  |
| 3023 and 5680 kHz | AM(R)S | Search and rescue |  |
| 74.8–75.2 MHz | ARN | Marker beacon |  |
| 108–117.975 MHz | ARN | VOR/ILS localizer |  |
| 117.975–137 MHz | AM(R)S | Air-ground and air-air communications (VHF voice and data) |  |
| 121.5, 123.1 and 243 MHz | AM(R)S/mobile | Emergency frequencies |  |
| 328.6–335.4 MHz | ARN | ILS glide path |  |
| 406–406.1 MHz | MSS | Search and rescue |  |
| 960–1215 MHz | ARN RNS | DME GNSS |  |
| 1030 and 1090 MHz | ARN | SSR/ACAS |  |
| 1215–1260 MHz | RL/RNS | GNSS Surveillance radar |  |
| 1260–1400 MHz | ARN/RL | Surveillance radar |  |
| 1525–1559 MHz 1626.5–1660.5 MHz | MSS | Satellite communications |  |
| 1559–1626.5 MHz | ARN/RNS/MSS | GNSS |  |
| 1610–1626.5 MHz | ARN/RDS/MSS | GLONASS |  |
| 2700–3300 MHz | ARN/RL | Surveillance radar |  |
| 4200–4400 MHz | ARN | Radio altimeter |  |
| 5000–5250 MHz | ARN | MLS |  |
| 5350–5470 MHz | ARN | Airborne weather radar |  |
| 8750–8850 MHz | ARN/RL | Airborne Doppler radar |  |
| 9000–9500 MHz | ARN/RN/RL | Precision approach radar |  |
| 13.25–13.4 GHz | ARN | Airborne Doppler radar |  |
| 15.4–16.6 GHz | ARN | ASDE/other systems |  |
| 24.25–24.65 GHz | RN | ASDE |  |
| 31.8–33.4 GHz | RN | ASDE |  |
| RN: Radionavigation RL: Radiolocation ARN: Aeronautical radionavigation RNS: Radionavigation satellite service RDS: Radio determination satellite service AM(R)S: Aeronautical mobile (route) service MSS: Mobile satellite service AMS(R)S: Aeronautical mobile satellite (route) service |

— — — — — — —

SECTION 7-II.  CIVIL AVIATION FREQUENCY

ALLOCATIONS — ICAO POLICIES AND

RELATED INFORMATION

(including a composite statement for each frequency band)

The following material is reproduced from Article S5 of the ITU Radio Regulations to provide necessary information  the regulatory basis of the Table of Frequency Allocations below .

Note 1.— Extracts from the ITU Radio Regulations are presented against a shaded background.

Note 2.— The numbering of the provisions of the Radio Regulations conforms to the new numbering scheme adopted at WRC-95.

Note 3    This Edition 3 incorporates the changes to the Radio Regulations adopted at WRC-2000.

ARTICLE S5 FREQUENCY ALLOCATIONS S5.1In all documents of the Union where the terms allocation, allotment and assignment are to be used, they shall have the meaning given them in Nos. S1.16 to S1.18, the terms used in the three working languages being as follows:

| Frequency distribution to: | French | English | Spanish |
| --- | --- | --- | --- |
| Services | Attribution (attribuer) | Allocation (to allocate) | Atribución (atribuir) |
| Areas or countries | Allotissement (allotir) | Allotment (to allot) | Adjudicación (adjudicar) |
| Stations | Assignation (assigner) | Assignment (to assign) | Asignación (asignar) |

Section I. Regions and Areas S5.2For the allocation of frequencies the world has been divided into three Regions* as shown on the following map and described in Nos. S5.3 to S5.9.

Note 1.— The map is reproduced in Figure 3-1 of this handbook.

Note 2.— S5.3 to S5.9 are not included in this handbook.

*S5.2.1It should be noted that where the words “regions” or “regional” are without a capital “R” in these Regulations, they do not relate to the three Regions here defined for purposes of frequency allocation. . . . . . Section II. Categories of Services and Allocations S5.23Primary and Secondary Services S5.24(1)Where, in a box of the Table in Section IV of this Article, a band is indicated as allocated to more than one service, either on a worldwide or Regional basis, such services are listed in the following order: S5.25 a) services the names of which are printed in “capitals” (example: FIXED); these are called “primary” services; S5.26 b) services the names of which are printed in “normal characters” (example: Mobile); these are called “secondary” services (see Nos. S5.28 to S5.31). S5.27(2)Additional remarks shall be printed in normal characters (example: MOBILE except aeronautical mobile). S5.28(3)Stations of a secondary service: S5.29 a) shall not cause harmful interference to stations of primary services to which frequencies are already assigned or to which frequencies may be assigned at a later date; S5.30 b) cannot claim protection from harmful interference from stations of a primary service to which frequencies are already assigned or may be assigned at a later date; S5.31 c) can claim protection, however, from harmful interference from stations of the same or other secondary service(s) to which frequencies may be assigned at a later date. S5.32(4)Where a band is indicated in a footnote of the Table as allocated to a service “on a secondary basis” in an area smaller than a Region, or in a particular country, this is a secondary service (see Nos. S5.28 to S5.31). S5.33(5)Where a band is indicated in a footnote of the Table as allocated to a service “on a primary basis”, in an area smaller than a Region, or in a particular country, this is a primary service only in that area or country.

S5.34Additional Allocations S5.35(1)Where a band is indicated in a footnote of the Table as “also allocated” to a service in an area smaller than a Region, or in a particular country, this is an “additional” allocation, i.e. an allocation which is added in this area or in this country to the service or services which are indicated in the Table (see No. S5.36). S5.36(2)If the footnote does not include any restriction on the service or services concerned apart from the restriction to operate only in a particular area or country, stations of this service or these services shall have equality of right to operate with stations of the other primary service or services indicated in the Table. S5.37(3)If restrictions are imposed on an additional allocation in addition to the restriction to operate only in a particular area or country, this is indicated in the footnote of the Table. S5.38Alternative Allocations S5.39(1)Where a band is indicated in a footnote of the Table as “allocated” to one or more services in an area smaller than a Region, or in a particular country, this is an “alternative” allocation, i.e. an allocation which replaces, in this area or in this country, the allocation indicated in the Table (see No. S5.40 (432)). S5.40(2)If the footnote does not include any restriction on stations of the service or services concerned, apart from the restriction to operate only in a particular area or country, these stations of such a service or services shall have an equality of right to operate with stations of the primary service or services, indicated in the Table, to which the band is allocated in other areas or countries. S5.41(3)If restrictions are imposed on stations of a service to which an alternative allocation is made, in addition to the restriction to operate only in a particular country or area, this is indicated in the footnote. S5.42Miscellaneous Provisions S5.43(1)Where it is indicated in these Regulations that a service or stations in a service may operate in a specific frequency band subject to not causing harmful interference to another service or to another station in the same service, this means also that the service which is subject to not causing interference cannot claim protection from harmful interference caused by the other service or other station in the same service. S5.43A (1) bis Where it is indicated in these Regulations that a service or stations in a service may operate in a specific frequency band subject to not claiming protection from another service or from another station in the same service, this means also that the service which is subject to not claiming protection shall not cause harmful interference to the other service or other station in the same service.

S5.44(2)Except if otherwise specified in a footnote, the term “fixed service”, where appearing in Section IV of this Article, does not include systems using ionospheric scatter propagation. S5.45Not used. Section III. Description of the Table of Frequency Allocations S5.46(1)The heading of the Table in Section IV of this Article includes three columns, each of which corresponds to one of the Regions (see No. S5.2). Where an allocation occupies the whole of the width of the Table or only one or two of the three columns, this is a worldwide allocation or a Regional allocation, respectively. S5.47(2)The frequency band referred to in each allocation is indicated in the left-hand top corner of the part of the Table concerned. S5.48(3)Within each of the categories specified in Nos. S5.25 to S5.26, services are listed in alphabetical order according to the French language. The order of listing does not indicate relative priority within each category. S5.49(4)In the case where there is a parenthetical addition to an allocation in the Table, that service allocation is restricted to the type of operation so indicated. S5.50(5)The footnote references which appear in the Table below the allocated service or services apply to more than one of the allocated services, or to the whole of the allocation concerned. S5.51(6)The footnote references which appear to the right of the name of a service are applicable only to that particular service. S5.52(7)In certain cases, the names of countries appearing in the footnotes have been simplified in order to shorten the text.

— — — — — — — —

This page deliberately left blank.

Delete the section on Omega since all Omega stations ceased to operate as from 30 September 1997. No future aeronautical requirements for the use of this band have been identified.

Band: 90–110 kHz

Service: Radionavigation (Loran-C)

Allocation:

kHz 90–110

| Allocation to Services |
| --- |
| Region 1 | Region 2 | Region 3 |
| 90–110 | RADIONAVIGATION S5.62 Fixed |
|  | S5.64 |  |

Footnotes: S5.62Administrations which operate stations in the radionavigation service in the band 90–110 kHz are urged to coordinate technical and operating characteristics in such a way as to avoid harmful interference to the services provided by these stations. S5.64Only classes A1A or F1B, A2C, A3C, F1C or F3C emissions are authorized for stations of the fixed service in the bands allocated to this service between 90 kHz and 160 kHz (148.5 kHz in Region 1) and for stations of the maritime mobile service in the bands allocated to this service between 110 kHz and 160 kHz (148.5 kHz in Region 1). Exceptionally, class J2B or J7B emissions are also authorized in the bands between 110 kHz and 160 kHz (148.5 kHz in Region 1) for stations of the maritime mobile service.

ICAO  POLICY

- Retain the allocation to the Aeronautical Radionavigation Service and S5.62

- Support deletion of the fixed service and S5.64 as envisaged in Resolution 706.

AVIATION USE: Long-range hyperbolic navigation for specialized purposes other than flight along national airways and air routes.

COMMENTARY: The hyperbolic navigation systems which operate in this band are provided by commercial operators for special purpose use, which also includes maritime use. There is no deployment for use on the organized airway structure. The civil aviation use is  mainly  for general aviation users in certain ICAO Contracting States using the LORAN C system.

Loran C services are continuing as a requirement by certain elements in the air transport community such as general aviation.  In this situation it is necessary to secure a safe radio environment, free from interference.   Other users of the adionavigation service, in particular maritime services, are concerned also and are joint authors of Resolution 706 (Rev. WRC-2000) calling for a review of the allocation to the fixed service with a view of its possible deletion. This matter is not placed on the Agenda for the WRC-2003 nor on the draft agenda for the WRC-2006.

This page deliberately left blank.

Band: 130–535 kHz

Service: Aeronautical radionavigation (NDB/locator)

Allocation:

kHz 130–315

| Allocation to Services |
| --- |
| Region 1 | Region 2 | Region 3 |
| 130–148.5 | 130–160 | 130–160 |
| MARITIME MOBILE | FIXED | FIXED |
| FIXED | MARITIME MOBILE | MARITIME MOBILE |
| S5.64 S5.67 |  | RADIONAVIGATION |
| 148.5–255 | S5.64 | S5.64 |
| BROADCASTING | 160–190 | 160–190 |
|  | FIXED | FIXED |
|  |  | Aeronautical Radionavigation |
|  | 190–200 |
|  | AERONAUTICAL RADIONAVIGATION |
| S5.68 S5.69 S5.70 | 200–275 | 200–285 |
| 255–283.5 | AERONAUTICAL | AERONAUTICAL |
| BROADCASTING | RADIONAVIGATION | RADIONAVIGATION |
| AERONAUTICAL | Aeronautical Mobile | Aeronautical Mobile |
| RADIONAVIGATION | 275–285 |  |
| S5.70 S5.71 | AERONAUTICAL |  |
| 283.5–315 | RADIONAVIGATION |  |
| AERONAUTICAL | Aeronautical Mobile |  |
| RADIONAVIGATION | Maritime Radionavigation |  |
| MARITIME | (radiobeacons) |  |
| RADIONAVIGATION | 285–315 |
| (radiobeacons) S5.73 | MARITIME RADIONAVIGATION |
|  | (radiobeacons) S5.73 |
| S5.72 S5.74 | AERONAUTICAL RADIONAVIGATION |

kHz 315–505

| Allocation to Services |
| --- |
| Region 1 | Region 2 | Region 3 |
| 315–325 | 315–325 | 315–325 |
| AERONAUTICAL | MARITIME | AERONAUTICAL |
| RADIONAVIGATION | RADIONAVIGATION | RADIONAVIGATION |
| Maritime Radionavigation | (radiobeacons) S5.73 | MARITIME |
| (radiobeacons) S5.73 | Aeronautical | RADIONAVIGATION |
|  | Radionavigation | (radiobeacons) S5.73 |
| S5.72 S5.75 |  |  |
| 325–405 | 325–335 | 325–405 |
| AERONAUTICAL | AERONAUTICAL | AERONAUTICAL |
| RADIONAVIGATION | RADIONAVIGATION | RADIONAVIGATION |
|  | Aeronautical Mobile | Aeronautical Mobile |
|  | Maritime Radionavigation |  |
|  | (radiobeacons) |  |
|  | 335–405 |  |
|  | AERONAUTICAL |  |
|  | RADIONAVIGATION |  |
| S5.72 | Aeronautical Mobile |  |
| 405–415 | 405–415 |
| RADIONAVIGATION S5.76 | RADIONAVIGATION S5.76 |
| S5.72 | Aeronautical Mobile |
| 415–435 | 415–495 |
| AERONAUTICAL | MARITIME MOBILE S5.79 S5.79A |
| RADIONAVIGATION | Aeronautical Radionavigation S5.80 |
| MARITIME MOBILE S5.79 |  |
| S5.72 |  |
| 435–495 |  |
| MARITIME MOBILE S5.79 S5.79A |  |
| Aeronautical |  |
| Radionavigation |  |
| S5.72 S5.82 | S5.77 S5.78 S5.82 |
| 495–505 | MOBILE (DISTRESS AND CALLING) |
|  | S5.83 |

kHz 505–535

| Allocation to Services |
| --- |
| Region 1 | Region 2 | Region 3 |
| 505–526.5 | 505–510 | 505–526.5 |
| MARITIME MOBILE S5.79 S5.79A S5.84 | MARITIME MOBILE S5.79 | MARITIME MOBILE S5.79 S5.79A |
| AERONAUTICAL |  | S5.84 |
| RADIONAVIGATION | 510–525 | AERONAUTICAL RADIONAVIGATION |
|  | MOBILE S5.79A S5.84 |  |
|  | AERONAUTICAL | Aeronautical mobile |
|  | RADIONAVIGATION | Land mobile |
| S5.72 | 525–535 |  |
| 526.5–1606.5 | BROADCASTING S5.86 | 526.5–535 |
| BROADCASTING | AERONAUTICAL | BROADCASTING |
|  | RADIONAVIGATION | Mobile |
| S5.87 S5.87A |  | S5.88 |

Footnotes: S5.64Only classes A1A or F1B, A2C, A3C, F1C or F3C emissions are authorized for stations of the fixed service in the bands allocated to this service between 90 kHz and 160 kHz (148.5 kHz in Region 1) and for stations of the maritime mobile service in the bands allocated to this service between 110 kHz and 160 kHz (148.5 kHz in Region 1). Exceptionally, class J2B or J7B emissions are also authorized in the bands between 110 kHz and 160 kHz (148.5 kHz in Region 1) for stations of the maritime mobile service. S5.67Additional allocation: in Armenia, Azerbaijan, Belarus, Bulgaria, Kazakhstan, Moldova, Mongolia, Kyrgyzstan, Romania, Russia, Tajikistan, Turkmenistan and Ukraine, the band 130–148.5 kHz is also allocated to the radionavigation service on a secondary basis. Within and between these countries this service shall have an equal right to operate. S5.68Alternative allocation: in Angola, Botswana, Burundi, the Congo, Malawi, Rwanda, South Africa and Zaire, the band 160–200 kHz is allocated to the fixed service on a primary basis. S5.69Additional allocation: In Somalia, the band 200–255 kHz is also allocated to the aeronautical radionavigation service on a primary basis.

S5.70Alternative allocation: In Angola, Botswana, Burundi, Cameroon, the Central African Republic, the Congo, Ethiopia, Kenya, Lesotho, Madagascar, Malawi, Mozambique, Namibia, Nigeria, Oman, Rwanda, South Africa, Swaziland, Tanzania, Chad, Zaire, Zambia and Zimbabwe, the band 200– 283.5 kHz is allocated to the aeronautical radionavigation service on a primary basis. S5.71Alternative allocation: In Tunisia, the band 255–283.5 kHz is allocated to the broadcasting service on a primary basis. S5.72Norwegian stations of the fixed service situated in northern areas (north of 60° N) subject to auroral disturbances are allowed to continue operation on four frequencies in the bands 283.5–490 kHz and 510–526.5 kHz. S5.73The band 285–325 kHz (283.5–325 kHz in Region 1), in the maritime radionavigation service may be used to transmit supplementary navigational information using narrow-band techniques, on condition that no harmful interference is caused to radiobeacon stations operating in the radionavigation service. S5.74Additional Allocation: In Region 1, the frequency band 285.3– 285.7 kHz is also allocated to the maritime radionavigation service (other than radiobeacons) on a primary basis. S5.75Different category of service: in Armenia, Azerbaijan, Belarus, Georgia, Moldova, Kyrgyzstan, the Russian Federation, Tajikistan, Turkmenistan, Ukraine and the Black Sea areas of Bulgaria and Romania, the allocation of the band 315–325 kHz to the maritime radionavigation service is on a primary basis under the conditions: that in the Baltic Sea area, the assignment of frequencies in this band to new stations in the maritime or aeronautical radionavigation services shall be subject to prior consultation between the administrations concerned. S5.76The frequency 410 kHz is designated for radio direction-finding in the maritime radionavigation service. The other radionavigation services to which the band 405–415 kHz is allocated shall not cause harmful interference to radio direction-finding in the band 406.5–413.5 kHz. S5.77Different category of service: in Australia, China, the French Overseas Territories of Region 3, India, Indonesia (until 1 January 2005), Iran ( Islamic Republic of), Japan, Pakistan, Papua New Guinea and Sri Lanka, the allocation of the band 415–495 kHz to the aeronautical radionavigation service is on a primary basis. Administrations in these countries shall take all practical steps necessary to ensure that aeronautical radionavigation stations in the band 435–495 kHz do not cause interference to reception by coast stations of ship stations transmitting on frequencies designated for ship stations on a worldwide basis (see No. S52.39).

S5.78Different category of service: in Cuba, the United States of America, and Mexico the allocation of the band 415–435 kHz to the aeronautical radionavigation service is on a primary basis. S5.79The use of the bands 415–495 kHz and 505–526.5 kHz (505–510 kHz in Region 2) by the maritime mobile service is limited to radiotelegraphy. S5.79AWhen establishing coast stations in the NAVTEX service on the frequencies 490 kHz, 518 kHz and 4209.5 kHz, administrations are strongly recommended to coordinate the operating characteristics in accordance with the procedures of the International Maritime Organization (IMO) (see Resolution 339 (Rev. WRC-97)). S5.80In Region 2, the use of the band 435–495 kHz by the aeronautical radionavigation service is limited to non-directional beacons not employing voice transmission. S5.82In the maritime mobile service, the frequency 490 kHz is, from the date of full implementation of the GMDSS (see Resolution 331 (Rev. WRC-97)), to be used exclusively for the transmission by coast stations of navigational and meteorological warnings and urgent information to ships, by means of narrow-band direct-printing telegraphy. The conditions for use of the frequency 490 kHz are prescribed in Articles S31 and S52. In using the band 415–495 kHz for the aeronautical radionavigation service, administrations are requested to ensure that no harmful interference is caused to the frequency 490 kHz. S5.83The frequency 500 kHz is an international distress and calling frequency for Morse radiotelegraphy. The conditions for its use are prescribed in Articles S31 and S52 in Appendix S13. S5.84The conditions for the use of the frequency 518 kHz by the maritime mobile service are prescribed in Articles S31 and S52 and in Appendix S13. S5.85Not used. S5.86In Region 2, in the band 525–535 kHz the carrier power of broadcasting stations shall not exceed 1 kW during the day and 250 W at night. S5.87Additional allocation: in Angola, Botswana, Lesotho, Malawi, Mozambique, Namibia, South Africa, Swaziland, Zambia and Zimbabwe, the band 526.5–535 kHz is also allocated to the mobile service on a secondary basis.

S5.87AAdditional allocation: in Uzbekistan, the band 526.5–1606.5 kHz is also allocated to the radionavigation service on a primary basis. Such use is subject to agreement obtained under Article 14/S9.21 with administrations concerned and limited to ground-based radiobeacons in operation on 27 October 1997 until the end of its lifetime. S5.88Additional allocation: in China, the band 526.5–535 kHz is also allocated to the aeronautical radionavigation service on a secondary basis.

ICAO POLICY Until at least 2015, the current allocations to the aeronautical radionavigation service for use by non-directional radio beacons (NDB) need to be safeguarded. · National requirements may need to extend this period. · No change to S5.70, S5.80 and S5.86. · In regions where GNSS is implemented and NDB assignments are withdrawn from international and national usage, aviation requirements for spectrum may be reduced.

AVIATION USE: These bands support non-directional radio beacons (NDB)  for short- and medium-range navigation. Used with automatic direction finder (ADF) equipment in aircraft, the NDB provides a bearing with moderate accuracy (in modern terms). The NDB is used by larger aircraft over sea or over land routes and is extensively deployed at general aviation aerodromes where it provides an economic and easily installed facility. Aeronautical NDB's at coastal locations are also used by the maritime service, and, in the reverse sense, beacons provided for maritime purposes are potentially usable by aviation.

NDBs are assigned frequencies on the basis of daytime propagation conditions. NDBs are prone to night effects, when due to ionosphere propagation (reflection)  significant errors due to the reception of signals from distant NDB's. This night effect increases with frequency.

Frequency scarcity in some geographical areas has been a cause for concern in the past. The 1979 ITU World Administrative Radio Conference  (WARC-79) hence recognized a demand in Europe and Africa and allocated in Region 1 the band 415–435 kHz, shared with the maritime mobile service, at that time on a permitted basis. An ITU frequency assignment plan for Region 1 was prepared for this band in 1985 giving priority access to the aeronautical service (Final Actsof the Regional Administrative Conference for the planning of the MF Maritime Mobile and Aeronautical Radionavigation Service (Region 1), Geneva, 1985).  Regional Conference 1985 refer). At present  the requirement for NDB's has stabilized and aviation can meet its requirement from the present allocations. Allocations made on a permitted bases were removed from the Radio Regulations at WRC-95 and replaced with an allocation on a primary basis.

Interference from broadcasting in the band 255–283.5 kHz has been reported, which render this band  unusable in much of Region 1.

COMMENTARY: For international purposes, the future air navigation systems (FANS) scenario foresees a reduction in the role of NDB in the future, inter alia, due to the emergence of the global navigation satellite system (GNSS) as the future  system for a range of navigation services, including those  for oceanic and low-density continental airspace.

The NAT SPG discussions in June 1995 produced Conclusion 31/10 (NAT SPG/31) which foresaw a continuing requirement for NDBs for “at least five years” in the North Atlantic Region. The same conclusion called for the development of a policy for gradual withdrawal, as new technology becomes available. It is foreseen that, in other areas of the world, the requirement for NDB spectrum will remain for the next twenty years, at least.

At a national level where the majority of NDB services are provided, frequency demand for NDB will depend to a large extent on national policies. The last world-wide ICAO review in 1985 (Appendix C to Agenda Item 8 of the Communications/Operations (COM/OPS) Divisional Meeting (1985) (Doc 9464)) considered the retention of NDB allocations essential, including the need for assignments for national purposes.  General aviation use of NDB will continue well beyond their withdrawal from internationally agreed routes.

Footnotes: Footnotes of particular importance are:

S5.76: Designation of 410 kHz for radio direction finding

S5.80: The prohibition of the use of voice in Region 2 in the band 435–495 kHz

S5.84: Designation of 518 kHz for special use in the maritime mobile service

TECHNICAL AND OTHER INFORMATION

Band: 130–535 kHz (selected bands)

Service: Aeronautical radionavigation

Aviation use: Non-directional beacons, locator beacons

Annex 10:

SARPs: Annex 10, Volume I, Chapter 3, 3.4 and 3.9

Frequency plan: Regional plan

Channelization: 1 kHz spacing; in EUR Region 0.5 kHz assignments

may also be used.

Planning criteria:

Annex 10, Volume V, Chapter 3, 3.2

Annex 10, Volume I, Attachment C, paragraph 6

Annex 10, Volume V, Attachment B

Air Navigation Plan

European Area Regional Plan, Part X, Table COM-4

Other regions to be added

RTCA MOPS: DO-179; MOPS for airborne ADF equipment (1982)

Eurocae MPS: 712-7

ARINC characteristic: ED-51

ITU Res/Rec:

ITU-R:

Other material:

·	CCIR Report No. 910 — Sharing between the Maritime Mobile Service and the Aeronautical Radionavigation Service in the band 415–526.5 kHz. Note: this report is published in Annex 3 to Volume VIII of the report of the XVII of the plenary assembly of the International Radio Consultative Committee (CCIR) (Dusseldorf, 1990)

·	Final Acts of the Regional Administrative Conference for the Planning of the MF Maritime Mobile and Aeronautical Radionavigation Service (Region 1), Geneva 1985.

---------------------------------------------------------------------------------------------------------------------

INTERFERENCE FROM

NON-AERONAUTICAL SOURCES

FREQUENCY SHARING BETWEEN NDB AND

MARITIME MOBILE SERVICES IN BANDS

BETWEEN 415 and 435 kHz

General: The MF frequency bands allocated to aeronautical radionavigation service  between 415 and 495 kHz and and used for NDB's is in all three ITU Regions with the maritime mobile service. In Region 1  in the band 415 - 435 kHz the sharing is on a joint primary basis In Regions 2 and 3, and in the band 435 - 495 kHz in Region 1, the aeronautical Radionavigation service  is on a secondary basis although in some countries the aeronautical Radionavigation service enjoys a primary status (S5.77 and S5.78). With careful planning and coordination acceptable arrangements  can be achieved,  facilitated by the partially geographically different areas of operation of the two services.

The  protection of aeronautical beacons from  transmissions of coast and ship stations of the maritime mobile service can be assured by the application of the criteria contained in Appendix S12 to the Radio Regulations. Additional  Guidance Material is contained in Annex 10. Some ICAO Regions, notably the European Region, have also agreed to apply supplementary criteria to NDB frequency assignments in their area. An overview of these provisions is given below:

ITU Radio Regulations::

Appendix S12 Special Rules Applicable to Radiobeacons Section 1 Aeronautical Radiobeacons (1) The assignment of frequencies to aeronautical radiobeacons operating in the bands between 160 kHz and 535 kHz shall be based on a protection ratio against interference of at least 15 dB for each beacon throughout its service area. (2) The radiated power should be kept to the minimum value necessary to give the desired field strength at the service range. (3) The daylight service range of radiobeacons referred to in (1) above shall be based on the following field strengths: (4) Regions 1 and 2 — 70 microvolts per metre for radiobeacons North of 30 N; — 120 microvolts per metre for radiobeacons between 30 N and 30 S; — 70 microvolts per metre for radiobeacons south of 30 S; (5) Region 3 — 70 microvolts per metre for radiobeacons North of 40 N; — 120 microvolts per metre for radiobeacons between 40 N and 50 S; — 70 microvolts per metre for radiobeacons south of 50 S.

The above provisions have the status of Regulations through the linked reference at Articles S28, S28.23 and S28.24, which specifies the above as special rules which must be complied with.

ICAO Annex 10: Frequency planning material relevant for NDB assignments is also contained in:

(i)	Annex 10, Volume I, 3.4 — Specification for non-directional radio beacon (NDB); and

(ii)	Annex 10 ,Volume V, Att. B — Considerations affecting the deployment of LF/MF frequencies and the avoidance of harmful interference.

The planning guidance in Attachment B of Annex 10, Volume V, is related to the RF-filtering  characteristics of ADF receivers used in in aircraft.These characteristics  are used for developing  adjacent channel NDB planning parameters  for establishing the required separation distance in the case where the NDB and maritime service frequencies operate on adjacent channels .

Propagation Model: Daytime propagation  at LF and MF  are greatly affected by the conductivity amd permittivity characteristics of the ground. Nighttime propagation of transmissions from NDB are prone to ionospheric relection and  do not generally provide a reliable service and are not recommended. The appropriate ground wave transmission model used for frequency assignment planning is contained in ITU-R Recommendation P.368. . This recommendation provides ground wave propagation data for frequencies from 10 kHz up to 30 MHz. In the frequency range of interest for NDB, there are separate curves for the frequencies of 200, 300, 400 and 500 kHz. Separate propagation curves are provided for sea and for eight different values of ground conductivity and permittivity, which must be ascertained from local knowledge to enable accurate application.

CCIR Report 910-1 — Sharing between MMS and NDB in Band 415 - 526.5 kHz

Parts of the frequency band 415 - 526.5 kHz are allocated to both the maritime mobile service and the aeronautical radionavigation service. Because of differences in operational use, i.e. frequency planning characteristics radiated power, etc., the coexistence of these two radio services in the same bands may present problems. Particular attention is required with respect to the problems which have their origin in the power levels used. In general, the  coast stations of the maritime mobile Service operate at  power levels of the order of 20 - 30 dB higher than short and medium range NDB. For example, coast station operation at e.r.p. of 10 to 50 Watts is typical as is ship station operation at 40 Watts e.r.p., whereas an NDB with a range of 50 NM would have an e.r.p. of less than 1 Watt (taking into account the relative antenna efficiencies which may be as low as 10 to 30 per cent).

This highly important report examines in detail some of the important parameters to be addressed in any analysis of these situations. The required protection to both maritime (NAVTEX services on 518 kHz) and NDB is examined for the full range of conditions of propagation. Two annexes provide detailed analysis for particular cases: Annex I for protection of NAVTEX services and Annex II for protection of NDB services.

Bands: 1800–2000 kHz

Service: Radionavigation (Regions 2 and 3) (Loran-A)

Allocation:

kHz 1800–2000

| Allocation to Services |
| --- |
| Region 1 | Region 2 | Region 3 |
| 1800–1810 | 1800–1850 | 1800–2000 |
| RADIOLOCATION S5.95 | AMATEUR | AMATEUR |
| S5.93 S5.94 |  | FIXED |
| 1810–1850 |  | MOBILE except |
| AMATEUR |  | aeronautical mobile |
| S5.98 S5.99 S5.100 |  | RADIONAVIGATION |
| S5.101 |  | Radiolocation |
| 1850–2000 | 1850–2000 |  |
| FIXED | AMATEUR |  |
| MOBILE except | FIXED |  |
| aeronautical mobile | MOBILE except |  |
|  | aeronautical mobile |  |
|  | RADIOLOCATION |  |
|  | RADIONAVIGATION |  |
| S5.92 S5.96 S5.103 | S5.102 | S5.97 |

Footnotes: S5.92Some countries of Region 1 use radiodetermination systems in the bands 1606.5–1.625 kHz, 1635–1800 kHz, 1850–2160 kHz, 2194– 2300 kHz, 2502–2850 kHz and 3500–3800 kHz, subject to agreement obtained under No. S9.21. The radiated mean power of these stations shall not exceed 50 W. S5.93Additional allocation: in Angola, Armenia, Azerbaijan, Belarus, , Georgia, Hungary, Kazakstan, Latvia, Lithuania, Moldova, Mongolia, Nigeria, Uzbekistan, Poland, Kyrgyzstan, Slovakia, the Czech Republic, the Russian Federation , Tajikistan, Chad, Turkmenistan and Ukraine, the bands 1625– 1635 kHz, 1800–1810 kHz and 2160–2170 kHz and, in Bulgaria, the bands 1625-1635 kHz and 1800-1810 kHz are also allocated to the fixed and land mobile services on a primary basis, subject to agreement obtained under No. S9.21. S5.94Not used

S5.95Not used S5.96In Germany, Armenia, Austria, Azerbaijan, Belarus, Denmark, Estonia, Finland, Georgia, Hungary, Ireland, Israel, Jordan, Kazakhstan, Latvia, Liechtenstein, Lithuania, Malta, Moldova, Norway, Uzbekistan, Poland, Kyrgyzstan, Slovakia, the Czech Republic, the United Kingdom, the Russian Federation , Sweden, Switzerland, Tajikistan, Turkmenistan and Ukraine, administrations may allocate up to 200 kHz to their amateur service in the bands 1715–1800 kHz and 1850–2000 kHz. However, when allocating the bands within this range to their amateur service, administrations shall, after prior consultation with administrations of neighbouring countries, take such steps as may be necessary to prevent harmful interference from their amateur service to the fixed and mobile services of other countries. The mean power of any amateur station shall not exceed 10 W. S5.97In Region 3, the Loran system operates either on 1850 kHz or 1950 kHz, the bands occupied being 1825–1875 kHz and 1925–1975 kHz, respectively. Other services to which the band 1800–2000 kHz is allocated may use any frequency therein on condition that no harmful interference is caused to the Loran system operating on 1850 kHz or 1950 kHz. S5.98Alternative allocation: in Angola, Armenia, , Azerbaijan, Belarus, Belgium, Bulgaria, Cameroon, the Congo, Denmark, Egypt, Eritrea, Spain, Ethiopia, Georgia, Greece, Italy, Kazakhstan, Lebanon, Lithuania, Moldova, the Netherlands, Syria, Kyrgyzstan, the Russian Federation , Somalia, Tajikistan, Tunisia, Turkmenistan, Turkey and Ukraine, the band 1810–1830 kHz is allocated to the fixed and mobile, except aeronautical mobile, services on a primary basis. S5.99Additional allocation: in Saudi Arabia, Austria, Bosnia and Herzegovina, Iraq, Libya, Uzbekistan, Slovakia, the Czech Republic, Romania, Slovenia, Chad, Togo and Yugoslavia, the band 1810–1830 kHz is also allocated to the fixed and mobile, except aeronautical mobile, services on a primary basis. S5.100In Region 1, the authorization to use the band 1810–1830 kHz by the amateur service in countries situated totally or partially north of 40° N shall be given only after consultation with the countries mentioned in Nos. S5.98 and S5.99 to define the necessary steps to be taken to prevent harmful interference between amateur stations and stations of other services operating in accordance with Nos. S5.98 and S5.99. S5.101Alternative allocation: in Burundi and Lesotho, the band 1810– 1850 kHz is allocated to the fixed and mobile, except aeronautical mobile, services on a primary basis. S5.102Alternative allocation: in Argentina, Bolivia, Chile, Mexico, Paraguay, Peru, Uruguay and Venezuela, the band 1850–2000 kHz is allocated to the fixed and mobile, except aeronautical mobile, radiolocation and radionavigation services on a primary basis.

S5.103In Region 1, in making assignments to stations in the fixed and mobile services in the bands 1850–2045 kHz, 2194–2498 kHz, 2502– 2625 kHz and 2650–2850 kHz, administrations should bear in mind the special requirements of the maritime mobile service.

ICAO POLICY · No firm international civil requirement for LORAN A has been identified. However, the allocation to radionavigation in the bands between 1800 and 2000 kHz should be maintained until regional agreements for the cessation of LORAN services are made. · No change to S5.97.

AVIATION USE: The frequencies 1850 kHz or 1950 kHz are used in Region 3 for LORAN A.

COMMENTARY: LORAN has been recognized by FANS as a system which will eventually be replaced by GNSS. The allocation at 1800–2000 kHz for radionavigation is necessary.

LORAN A is provided primarily for use by military aircraft and is not covered by any NOTAM action in regard to its state of serviceability.

TECHNICAL AND OTHER INFORMATION

Band: 1800–2000 kHz (Region 3)

Service: Radionavigation

Aviation use: LORAN A

Annex 10

SARPs:  None

Frequency plan:  None

Channelization:  Two frequencies — 1850 kHz and 1950 kHz

Planning criteria:  None

RTCA MOPS: DO-194 MOPS for airborne area navigation equipment

using LORAN A (1986)

Eurocae MPS:

ARINC characteristic:

ITU Res/Rec: None

ITU-R: None

Other material: None

This page deliberately left blank.

Band: 2850–22000 kHz

Service: AM(R)S, air-ground communications (HF voice and data)

Allocation: In nine sub-bands

kHz 2850–22000

| Allocation to Services |
| --- |
| Region 1 | Region 2 | Region 3 |
| 2 850–3025 | AERONAUTICAL MOBILE (R) S5.111 S5.115 |
| 3400–3500 AERONAUTICAL MOBILE (R) |
| 4650–4700 | AERONAUTICAL MOBILE (R) |
| 5450–5480 | 5450–5480 | 5450–5480 |
| FIXED | AERONAUTICAL | FIXED |
| AERONAUTICAL | MOBILE (R) | AERONAUTICAL |
| MOBILE (OR) |  | MOBILE (OR) |
| LAND MOBILE |  | LAND MOBILE |
| 5480–5680 AERONAUTICAL MOBILE (R) |
| S5.111 S5.115 |
| 6525–6685 AERONAUTICAL MOBILE (R) |
| 8815–8965 AERONAUTICAL MOBILE (R) |
| 10005–10100 AERONAUTICAL MOBILE (R) S5.111 |
| 11275–11400 AERONAUTICAL MOBILE (R) |
| 13260–13360 AERONAUTICAL MOBILE (R) |
| 17900–17970 AERONAUTICAL MOBILE (R) |
| 21924–22000 AERONAUTICAL MOBILE (R) |

Footnotes: S5.111The carrier frequencies 2182 kHz, 3023 kHz, 5680 kHz, 8364 kHz and the frequencies 121.5 MHz, 156.8 MHz and 243 MHz may also be used, in accordance with the procedures in force for terrestrial radiocommunication services, for search and rescue operations concerning manned space vehicles. The conditions for the use of the frequencies are prescribed in Article S31 and Appendix S13. The same applies to the frequencies 10003 kHz, 14993 kHz and 19993 kHz, but in each of these cases emissions must be confined in a band of ±3 kHz about the frequency. S5.115The carrier (reference) frequencies 3 023 kHz and 5 680 kHz may also be used, in accordance with Article S31 and Appendix S13 by stations of the maritime mobile service engaged in coordinated search and rescue operations.

ICAO  POLICY

- to retain the current allocations in the HF bands to the aeronautical mobile (route) service (AM(R)S) bands for the foreseeable future for HF voice and HF data.

- To investigate possibilities for expansion into aeronautical mobile (off-route) service (AM(OR)S) bands or other bands.

- To support measures facilitating the introduction of HF data links in conformity with ICAO SARPS. Provisional estimates of a further expansion of 30 kHz in the bands above 5 MHz for this use have been stated.

- T o protect the use of the aeronautical HF bands in accordance with the provisions of Appendix S27 as necessary.  The introduction of non-aeronautical services in these bands cannot be accepted.

- No change to S5.111 and S5.115.

To support the measures, and participate in the technical studies, addressed in Resolution 207 (Rev. WRC-2000)  addressing the   unauthorized use of and interference to frequencies in the bands allocated to the aeronautical mobile (R) service.  Consider technical solutions which can be implemented without changes to aircraft equipment, or disruption to operational services.

AVIATION USE: HF communications provide the main long distance air-ground communication system in areas where VHF is not practicable, e.g. oceanic and remote areas, low-level overseas paths, area coverage where the area is large, etc. Single sideband amplitude modulation voice is the modulation used. Data transmission over HF frequencies is permissible and has increasing applications.

Appendix S27 to the Radio Regulations contains the allotment plan and system parameters and was agreed to at the ITU WARC-78. The ICAO Communications Divisional Meeting (1976) carried out the ICAO coordination prior to the ITU Conference. The ICAO Communications Divisional Meeting (1981) discussed and agreed to the necessary amendments to Annex 10, which included the change of specification from double sideband (DSB) to single sideband (SSB).

Allotments in the Appendix S27 plan are made to major world air route areas (MWARA) for long-distance international services where more than one country is affected. Regional and domestic air route areas (RDARA) allotments are made in other cases. The structure of Appendix S27 conforms to the operational requirement for aeronautical HF voice communication for the foreseeable future.

The registration of assignments in the Master International Frequency Register is a requirement covered by the Radio Regulations and effected through ITU member Administrations.

A proportion of the allotments are also made on a worldwide basis for assignment by administrations to aircraft operating agencies for regularity of flight purposes (see No.S27/194A) i.e. long-range operational control (see definition S27/8A in this section).

The carrier frequencies 3023 kHz and 5650 kHz are designated in  S27/208 to S27/214 for common use on a worldwide basis.  S27/212 further permits these frequencies to be used by other mobile services for air-surface search and rescue operations. Radio Regulations Footnotes S5.111 and S5.115 and Appendix S15 also specify these frequencies for distress and safety purposes.

Appendix S27  S27/20 specifically recognizes the coordination role of ICAO, with particular reference to the operational use of frequencies in the plan. This activity is coordinated at Regional Air Navigation Meetings where regional requirements for long range communications are agreed.

S27/21 permits the assignment of frequencies to other sharing possibilities additional to the plan where they do not reduce the protection to the same frequencies allotted in the Appendix S27 plan. These frequencies are accorded the same protection as those in the plan after registration in the MIFR.

COMMENTARY:

The ICAO Communications/Meteorology/Operations (COM/MET/OPS) Divisional Meeting (1990) discussed future HF needs. The ITU plan, which was created in 1978, significantly failed at that time to meet all requirements which wereput forward to the WARC-78  and could only satisfy requirements planned for operation before 1990. A revision of the plan is therefore due. However, further discussions on the future role of HF are continuing. A decision on a revision of Appendix S27 should be made after completion of these discussions. Also, the ability of the current regulations to accommodate the new requirements needs to be investigated.

The Frequency Management Study Group (FMSG), at its meetings in November 1994 and August 1995, carried out the review and analysis of current use of the HF bands. Data link has been considered by the Aeronautical Mobile Communications Panel (AMCP) and by the Automatic Dependent Surveillance Panel (ADSP). A study on this matter, including the development of SARPs for Annex 10,   has been completed and relevant SARPs  have now been incorporated in Annex 10 Vol III.  . An estimate of the possible number of families for a worldwide HF data link service has been given (six families each of six frequencies), which remains to be considered and accepted.

The present policy, in line with the findings of the COM/MET/OPS/90, is that no change be made to the allocation to the bands between 2–22 MHz allocated to the aeronautical mobile (route) service (Report of COM/MET/OPS/90, Appendix A to the Report on Agenda Item 3, paragraph 2.3 — Future aviation use — refers). This policy recognizes that current requirements are increasing. The transition to satellite-based communication would occur over an extended period. Coverage of polar regions would be likely to remain as a requirement for HF spectrum even after full implementation of satellite communication, although implementation of non-geostationary satellite systems, if used in aviation, might also provide the missing coverage over Polar areas.

USE OF DATA IN THE HF AM(R)S:

SARPs for HF data link (HFDL) have  been incorporated in Annex 10 in 1999.

The existing technical provisions in  Appendix S27 already permit data modulations, and the Rules of Procedure relating to this were approved by the ITU Radio Regulations Board at its meeting in July 1998. This has been communicated to ITU member administrations. The text of these rules is reproduced below:

Ref. S27/15: This provision specifies that the use of channels derived from the frequencies indicated in No. S27/18 for the various classes of emissions other than J3E and H2B will be subject to special arrangements by the administrations concerned and affected. In this connection, and having in mind the spirit of Resolution 713 (WRC-95), the Board considers as a valid “special arrangement by the administrations concerned” any formal action by the International Civil Aviation Organization (ICAO) which results in Standards and Recommended Practices (SARPs), which are approved by the ICAO in accordance with its procedures and which are communicated to the ITU accordingly.

Ref. S27/19: This provision specifies the role of ICAO in performing voluntary coordination (“should”) in the operational use of the frequencies. The Board considers such a coordination as an internal ICAO activity, intended to concluding operational agreements between the international operators (e.g., timesharing arrangements). Therefore the Bureau will not take into account such agreements between operators, unless they are communicated to the Bureau by their national telecommunications administration. Ref. S27/58: This provision lists the permissible classes of emission on the channels of Appendix S27 and stipulates, amongst other emissions, the possibility of using “other transmissions such as data transmission, single sideband, suppressed carrier”. The class of transmission listed against this latter description is JXX (former designation A9J). In this respect, the Board considers that any SSB (suppressed carrier) class of emission is authorized on the channels in Appendix S27 (e.g. J2B, J2D, J7B, J7D, J9B, J9D, etc.), provided that the following conditions are satisfied: · the reference frequency of the concerned transmission coincides with a reference frequency listed in the list of carrier (reference) frequencies (S27/18); · the occupied bandwidth of other authorized emissions does not exceed the upper limit of J3E emissions (No. S27/12), i.e. 2 700 Hz; · the assigned frequency is at a value 1 400 Hz above the carrier (reference) frequency (S27/75).

In frequency assignment planning, it is important to realize that the geographical disposition of allotments to MWARA and RDARA may need adjustment to accommodate the area of application of the new data services. HF data link is anticipated to operate in a different operational configuration than that for radio telephony. In accordance with Appendix S27, Rule S27/52, the frequency assignments for data must be made so as not to cause harmful interference to the allotments in Appendix S27. While some assignments may be identified using the possibilities covered by Rule S27/21 (see below), the additional requirements for dedicated families for data, as specified by AMCP, cannot be met from the present Appendix S27 Allotment Plan without affecting the provisions (allotments) for HF voice.

Harmful Interference to HF Services in Certain Areas

ITU Conferences in 1997 and 2000 have discussed the increase in harmful interference to air ground communications (and to maritime communications) in the HF bands.  This is more prevalent in some areas in the Western part of the South Pacific, and is believed to arise from the use of non-licensed, non-authorized equipment often installed on marine craft.  The ITU discussions have encompassed both administrative measures i.e better control and regulation, and technical measures, which can reduce the effect.   The latter are only regarded with favour in aviation if they can be implemented without  changes to current operational aircraft equipment.  Resolution 207 (Rev. WRC-2000) was amended at WRC-2000 to draw attention to this threat and to ensure studies by ITU-R to continue.

Appendix S27 to the Radio Regulations

The assignment of HF frequencies in the AM(R)S service for air ground communications are  governned and planned by the ITU. The Frequency Allotment Plan for the Aeronautical Mobile (R) Service and related information is contained in Appendix S27 to the ITU Radio Regulations and was last revised (to replace DSB with SSB) at the ITU World Administrative Radio Conference on the Aeronautical Mobile (R) Service in 1978 (WARC-78) Some important provisions of a regulatory character extracted from Appendix S27 are given below.

S 27/20  which recognizes the special role of ICAO,

S27/21 which permits the use of new allotments under specified conditions, and

S27/194A which permits AOC use on World-Wide frequencies as specified in Appendix 27.

Appendix S27 can only be amended by a competent ITU World Radiocommunication Conference where this subject is placed on the Agenda.  Any major replanning of allotments has traditionally in the past been preceded by an ICAO Divisional Meeting to agree and put forward the requirements of international civil aviation for MWARA and in some cases RDARA allotments. There are currently no requirements identified for a review of the allotment plan.

Definitions 1.Frequency Allotment Plan S27/1A plan which shows the frequencies to be used in particular areas without specifying the stations to which the frequencies are to be assigned. S27/22.The terms to express the different methods of frequency distribution as used in this Appendix have the following meanings:

| Frequency distribution to: | French | English | Spanish |
| --- | --- | --- | --- |
| Services | Attribution (attribuer) | Allocation (to allocate) | Atribución (atribuir) |
| Areas | Allotissement (allotir) | Allotment (to allot) | Adjudicación (adjudicar) |
| Stations | Assignation (assigner) | Assignment (to assign) | Asignación (asignar) |

S27/33.A Major World Air Route is a long-distance route, made up of one or more segments, essentially international in character, extending through more than one country and requiring long-distance communication facilities. S27/44.A Major World Air Route Area (MWARA) is an area embracing a certain number of Major World Air Routes, which generally follow the same traffic pattern and are so related geographically that the same frequency families may logically be applied. S27/55.Regional and Domestic Air Routes are all those using the Aeronautical Mobile (R) Service not covered by the definition of a Major World Air Route in No. S27/3. S27/66.A Regional and Domestic Air Route Area (RDARA) is an area embracing a certain number of the air routes defined in No. S27/5. S27/77.A VOLMET Allotment Area is an area encompassing all points where an HF broadcast facility might be required to operate on a family of frequencies common to the area. S27/88.A VOLMET Reception Area is an area within which aircraft should be able to receive broadcasts from one or more stations in the associated VOLMET Allotment Area. S27/99.A Worldwide Allotment Area is one in which frequencies are allotted to provide long-distance communication between an aeronautical station within that allotment area and aircraft operating anywhere in the world.

S27/1010.A Family of Frequencies in the Aeronautical Mobile (R) Service contains two or more frequencies selected from different aeronautical mobile (R) bands and is intended to permit communication at any time within the authorized area of use (see Nos. S27/213 to S27/231) between aircraft stations and appropriate aeronautical stations. ........ S27/193.The International Civil Aviation Organization (ICAO) coordinates radiocommunications of the aeronautical mobile (R) service with international aeronautical operations and this Organization should be consulted in all appropriate cases in the operational use of the frequencies in the Plan. 4.Adaptation of Allotment Procedure S27/20It is recognized that not all the sharing possibilities have been exhausted in the Allotment Plan contained in this Appendix. Therefore, in order to satisfy particular operational requirements which are not otherwise met by this Allotment Plan, Administrations may assign frequencies from the aeronautical mobile (R) bands in areas other than those to which they are allotted in this Plan. However, the use of the frequencies so assigned must not reduce the protection to the same frequencies in the areas where they are allotted by the Plan below that determined by the application of the procedure defined in Part I, Section II B of this Appendix. S27/215.When necessary to satisfy the needs of international air operations Administrations may adapt the allotment procedure for the assignment of aeronautical mobile (R) frequencies, which assignments shall then be the subject of prior agreement between Administrations affected. S27/226.The coordination described in No. S27/21 shall be effected where appropriate and desirable for the efficient utilization of the frequencies in question, and especially when the procedures of No. S27/19 are unsatisfactory. Note secr. The numbering in this paragraph may be in error S27/67e)That, in accordance with the Radio Regulations, all details of the assignment(s), including the transmitting antenna characteristics shall be notified to the IFRB. S27/2174.The worldwide frequency allotments appearing in the tables at No. S27/213 and Nos. S27/218 to S27/231, except for carrier (reference) frequencies 3023 kHz and 5680 kHz, are reserved for assignment by administrations to stations operating under authority granted by the administration concerned, for the purpose of serving one or more aircraft operating agencies. Such assignments are to provide communications between an appropriate aeronautical station and an aircraft station anywhere in the world for exercising control over regularity of flight and for safety of aircraft. Worldwide frequencies are not to be assigned by administrations for MWARA, RDARA and VOLMET purposes. Where the operational area of an aircraft lies wholly within a RDARA or Sub-RDARA boundary, frequencies allotted to those RDARAs and Sub-RDARAs shall be used.

TECHNICAL AND OTHER INFORMATION

Band: 2850–22000 kHz (selected bands)

Service: AM(R)S

Aviation use: Air-ground communications (HF voice and data)

Annex 10:

SARPs: 		Annex 10, Volume III, Part II, Chapter 2, 2.4

Frequency plan: 	Appendix S27 (see ITU below)

Channelization: 	3 kHz spacing SSB

Planning criteria: 	see ITU below

RTCA MOPS: DO-163 MOPS for airborne HF radio communication

transmitting/receiving equipment (1976).

Eurocae MPS:

ARINC characteristic: 719-5

ITU Res/Rec:

·	Appendix S27 to Radio Regulations (Frequency Allotment Plan, Planning Criteria).

·	Res. No. 207.

·	Res. No. 405: Relating to the use of frequencies of the aeronautical mobile (R) service.

·	Res. No. 406: Relating to the use of frequency bands higher than the HF bands in the aeronautical mobile (R) service and the aeronautical mobile-satellite (R) service for communications and for meteorological broadcasts.

·	Rec. No. 401: Relating to the efficient use of aeronautical mobile (R) worldwide frequencies.

·	Rec. No. 402: Relating to cooperation in the efficient use of the worldwide frequencies in the aeronautical mobile (R) service.

Other material: The reports of AMCP/3, AMCP/4, AMCP/5 and ADSP/3 contain ICAO material relevant to the development of SARPs for HF data link.

Band: 3023 kHz and 5680 kHz

Service: AM(R)S (search and rescue)

Aviation use: The frequencies 3023 and 5650 kHz are intended for common use on a worldwide basis as indicated in Appendix S27.

S27/2321.The carrier (reference) frequencies 3023 kHz and 5680 kHz are intended for common use on a worldwide basis. S27/2332.The use of these frequencies in any part of the world is authorized: 2.1 aboard aircraft for: a) communications with approach and aerodrome control; b) communication with an aeronautical station when other frequencies of the station are either unavailable or unknown; 2.2 at aeronautical stations for aerodrome and approach control under the following conditions: a) with mean power limited to a value of not more than 20 watts in the antenna circuit; b) special attention must be given in each case to the type of antenna used in order to avoid harmful interference; c) the power of aeronautical stations which use these frequencies in accordance with the above conditions may be increased to the extent necessary to meet certain operational requirements subject to coordination between the administrations directly concerned and those whose services may be adversely affected. S27/2343.Notwithstanding these provisions, the frequency 5680 kHz may also be used at aeronautical stations for communication with aircraft stations when other frequencies of the aeronautical stations are either unavailable or unknown. However, this use shall be restricted to such areas and conditions that harmful interference cannot be caused to other authorized operations of stations in the aeronautical mobile service. S27/2354.Additional particulars regarding the use of these channels for the above purposes may be recommended by the meetings of ICAO. S27/2365.Frequencies 3023 kHz and 5680 kHz may also be used by stations of other mobile services participating in coordinated air-surface search and rescue operations, including communications between these stations and participating land stations. Aeronautical stations are authorized to use these frequencies to establish communications with such stations.

See also S5.111 and S5.115

TECHNICAL AND OTHER INFORMATION

Bands: 3023 and 5680 kHz

Service: AM(R)S

Aviation use: Search and rescue (SAR) frequencies in HF

Annex 10

SARPs: None

Frequency plan: Annex 10, Volume V, Chapter 2, 2.2

Channelization: None

Planning criteria: None

RTCA MOPS:

DO-163. MOPS for airborne radio communication transmitting/receiving equipment.

ARINC characteristic: None

Eurocae MPS: None

ITU Res/Rec: Res. No. 403: Relating to the use of frequencies 3023 kHz and 5680 kHz common to the aeronautical mobile (route) and (OR) services

ITU-R:

Other material:

· Radio Regulations, Chapter SVII and Appendix S13

· Appendix S27

Band: 74.8–75.2 MHz

Service: Aeronautical radionavigation (marker beacon)

Allocation:

MHz 74.8–75.2

| Allocation to Services |
| --- |
| Region 1 | Region 2 | Region 3 |
| 74.8–75.2 AERONAUTICAL RADIONAVIGATION |
|  | S5.180 S5.181 |  |

Footnotes: S5.180The frequency 75 MHz is assigned to marker beacons. Administrations shall refrain from assigning frequencies close to the limits of the guardband to stations of other services which, because of their power or geographical position, might cause harmful interference or otherwise place a constraint on marker beacons. Every effort should be made to improve further the characteristics of airborne receivers and to limit the power of transmitting stations close to the limits 74.8 MHz and 75.2 MHz. S5.181Additional allocation: in , Egypt, Israel, Japan, and Syria, the band 74.8–75.2 MHz is also allocated to the mobile service on a secondary basis, subject to agreement obtained under S9.21. In order to ensure that harmful interference is not caused to stations of the aeronautical radionavigation service, stations of the mobile service shall not be introduced in the band until it is no longer required for the aeronautical radionavigation service by any administration which may be identified in the application of the procedure invoked under No. S9.21.

ICAO  POLICY

- No change to the current allocations.

- No change to S5.180.

- Deletion of S5.181

AVIATION USE: The frequency of 75 MHz is assigned to marker beacon for use with ILS to define specific points in the approach path. The outer marker is nominally at 7.5 km from the runway threshold, the middle marker at 1050 m from threshold, and, where installed, the inner marker is located just prior to threshold. In addition, markers may also be used to mark significant points on air routes.

COMMENTARY: There is a continuing and essential requirement for this allocation. (see also ILS localizer in band 108–111.975 MHz ).

ILS will continue to be used for the foreseeable future. Marker beacons are an indispensable element of the ILS system. Marker beacons are also used as en-route waypoint markers.

Footnote S5.181 relating to future use of this band by the mobile service was introduced at WARC-87.   At WRC-2000 aviation was successful  in removing 15 European and Middle Eastern country names from this footnote.   With the continuing use of ILS systems and markers this  footnote is not only ineffective but risks the addition of new names at future conferences and should  be deleted in its entirety. Any use of this band by the mobile service is incompatible with the allocation to the aeronautical Radionavigation service

TECHNICAL AND OTHER INFORMATION

Band: 74.8–75.2 MHz

Service: Aeronautical radionavigation

Aviation use: Marker beacon

Annex 10

SARPs: Annex 10, Volume I, Chapter 3, 3.1.7 and 3.6

Frequency plan: Fixed frequency of 75 MHz

Channelization: None

Planning criteria: Annex 10, Volume I, Attachment C, Section 5

RTCA MOPS: DO 143 MOPS for airborne radio marker receiving

equipment operating on 75 MHz (1970).

Eurocae MPS: 1/W67/70

ARINC characteristic:

ITU Res/Rec:

ITU-Rec:

CCIR:

Other material:

Band: 108–117.975 MHz

Service: Aeronautical radionavigation (VOR/ILS localizer)

Allocation:

MHz 108–117.975

| Allocation to Services |
| --- |
| Region 1 | Region 2 | Region 3 |
| 108–117.975 AERONAUTICAL RADIONAVIGATION |
|  | S5.197 |  |

Footnotes: S5.197Additional allocation: in , Japan, Pakistan, and Syria the band 108–111.975 MHz is also allocated to the mobile service on a secondary basis, subject to agreement obtained under No. S9.21. In order to ensure that harmful interference is not caused to stations of the aeronautical radionavigation service, stations of the mobile service shall not be introduced in the band until it is no longer required for the aeronautical radionavigation service by any administration which may be identified in the application of the procedures invoked under No. S9.21.

ICAO POLICY

- No change to the current allocation to the aeronautical radionavigation service

- Support an allocation enabling the use of the band 108-117.975 MHz for the transmissions of ICAO standard GNSS ground based augmentation system (GBAS) on a non-interference basis to aeronautical radionavigation systems (ILS/VOR).

- Ensure by appropriate measures conformity with ITU-R Recommendation IS.1009 regarding the compatibility of the aeronautical use with the FM Broadcast services in the band 87.5-108 MHz.

AVIATION USE: ILS localizer and VOR.

The instrument landing system (ILS) is one of the ICAO standard approach and landing systems. The use of ILS is protected in Annex 10 to at least the year 2010. The VHF omnidirectional radio range (VOR) is the short/medium range navigation aid.

The sub-band 108–111.975 MHz is shared between ILS and VOR in an interleaved 50 kHz and 100 kHz spaced frequency arrangement (108.1 and 108.15 MHz for ILS, 108, 108.05, 108.2 and 108.25 MHz for VOR, etc.)

The sub-band 112–117.975 MHz is used exclusively for VOR, with 50 kHz or 100 kHz channel spacing,depending on regional requirements.

The ILS localizer is coupled with the glide path frequencies from the band 328.6– 335.4 MHz and, where possible, with MLS from the band 5030–5150 MHz. DME/N or DME/P from the band 960–1215 MHz are also  frequency coupled with ILS and/or MLS, respectively.

VOR is normally associated with DME and is frequency coupled. Short-range airport VOR frequencies are usually taken from the sub-band 108–111.975 MHz.

Receivers operating  at the lower end of this frequency band, and particularly the ILS, are vulnerable to intermodulation and saturation effects from FM broadcast transmissions from the band 87–108 MHz. Material providing guidelines for States when assessing compatibility between assignments for FM broadcasting and aeronautical radionavigation (ILS/VOR) has been agreed in the ITU-R (ITU-R.IS 1009 refers).

Frequency congestion  for ILS and VOR exists in some high density areas, such as Western Europe and North America. This applies to ILS and VOR and arises, partially,  from the coupling and planning constraints exercised from MLS and DME.

The band has been used by aviation since 1947. At two occasions, the channel spacing was reduced. From 200 kHz to 100 kHz, and from 100 kHz to 50 kHz in 1972 (at the 7th Air Navigation Conference ).

Footnote S5.197  introduced at WARC-87 in anticipation that  ILS would be withdrawn from international service in 1998 and the use of the ILS/Localizer  would be terminated (see footnote section below).

COMMENTARY (ILS):

The comprehensive discussion under Agenda Items 1 to 3 of the Special Communications/Operations Divisional Meeting (1995) (SP COM/OPS/95) examined the future of ILS in the context of transition to MLS and to GNSS as envisaged in the FANS scenarios. MLS already had the capability for all categories of all weather operations, and GNSS would possibly achieve Category II in the early years after 2000 and Category III possibly in the year 2015 or later.

Most States indicated an intention to retain ILS in service (SP COM/OPS/95, Agenda Item 1, paragraph 1.3.4 refers) for the foreseeable future. In this regard, it is noted that Annex 10 requires all ILS and VOR receivers to improve immunity standards against interference from FM broadcasts.

ILS sustainability is addressed in Appendix B to the Report on Agenda Item 3. The meeting agreed on Recommendation 3/2 calling for a review of ILS SARPs and guidance material to ensure adequate provision for ILS beyond the year 2000. Other recommendations have called for studies and examinations of various scenarios for transition from ILS to either MLS or GNSS, with important emphasis on the economics of operation.

The introduction of the mobile service, in accordance with the provision of S5.197, is not possible in the foreseeable future. In light of the above, it is clear that the ILS allocation will be needed until probably well beyond 2010., t.

COMMENTARY (VOR):

The continuing deployment of VOR is dependent on the progress, development and implementation of GNSS; aviation may continue to require VOR for sometime after implementing GNSS. The GNSS Panel has developed the Guidelines for the Introduction and Operational use of the Global Navigation Satellite System (GNSS) published by ICAO as Circular 267 and will continue with developing the measures and principles necessary to evolve towards the use of GNSS as a  means of en-route navigation.

Section 6 of the reference document addresses the timescales and steps necessary for the implementation of GNSS, and Section 7 addresses the future prospects for GNSS. Different world regions will have different emphasis on their need for GNSS in the near and medium terms, and decisions will be taken at a regional level.

No definite or tentative dates have been agreed to for the GNSS programmes. It is therefore necessary to maintain the allocation for VOR until, at least, the year 2010.

Use of the band 108-117.975 MHz for GBAS and GRAS

ICAO has identified the band 108 - 117.975 to support spectrum for GBAS and GRAS. WRC-2003 will review the need for an allocation to this band enabling the introduction of this service. It has been argued that, from the radio-regulatory point of view, GBAS/GRAS needs to be considered as an aeronautical mobile (R) service since these augmentation systems only transmit data. The type of allocation to be made is still discussed in ICAO although there are strong arguments in favour of an allocation to the aeronautical mobile (R) service.  The development of SARPs relating to frequency assignment planning to ensure technical compatibility between ILS/VOR services and GNSS augmentation signals has been undertaken within ICAO. This is required to meet the proposed ITU regulatory basis whereby GNSS augmentation signals must operate without causing interference to ILS/VOR installations.

Allocations to Other Services

Footnote S5.197 was added by the ITU WARC-87 for mobile services. On present expectations for the use of the  band 108–117.975 MHz, it is improbable that his footnote can be considered for implementation for many years (possibly post 2010) in most of the countries in the note. The footnote is not meaningful in practical terms and carries the risk that further country names will be added at future conferences,   Hence it should be deleted in its entirety.   Furthermore, it should be noted , that no guidance exists on how S5.197 would be applied, or what essential prior agreements are necessary within aviation for mobile service operations to commence on any single frequency, or within particular sub-bands.  This inexactness compounds the problem, as it leaves room for undesirable interpretations that could be used to allow entry of the mobile service.

TECHNICAL AND OTHER INFORMATION

Band: 108–117.975 MHz

Service: Aeronautical radionavigation

Aviation use:

VOR (108–117.975 MHz )

ILS localizer (108–111.975 MHz )

Annex 10

SARPs: Annex 10, Volume I, Chapter 3, 3.1 (ILS) and 3.3 (VOR)

Frequency plan: Annex 10, Volume I, Chapter 3, 3.1.6 (ILS)

Channelization: 100 kHz/50 kHz spacing

Planning criteria:

Annex 10, Volume V, Chapter 4, 4.2

Annex 10, Volume I, Attachment C, 2.6 (ILS)

Annex 10, Volume I, Attachment C, 3.5 (VOR/ILS)

DO-195 MOPS from airborne ILS localizer equipment operating within the radio frequency range of 108–112 MHz.

RTCA MOPS:

ILS:

VOR: DO-196 MOPS for airborne VOR receiving equipment operating within the radio frequency range of 108–117.95 MHz.

Eurocae MPS:

ILS: ED-46B, ED-74 (combined ILS/MLS)

VOR: ED-22B, ED-52 (ground equipment)

ARINC characteristic:

ILS: 710-9

VOR: 711-9

ITU Res/Rec:

Rec. No. 704: Relating to the Compatibility between the broadcasting service in the band 100–108 MHz and the aeronautical radionavigation service in the band 108–117.975 MHz.

ITU-R:

·	ITU-R M44-1: Signal-to-interference ratios and minimum field strengths required in the aeronautical-mobile (route) service above 30 MHz

·	ITU-R.IS 1009: Compatibility between the sound broadcasting service in the band 87–108 MHz and the aeronautical services in the band 108– 137 MHz

Other material:

·	Receiver susceptibility to FM broadcast

·	DO 176: FMBC interference related to airborne ILS/VOR and VHF communication (1981)

·	Annex 10, Volume I, Chapter 3, 3.1.4 (ILS)

·	Annex 10, Volume I, Attachment C, 2.2.10 (ILS)

·	Annex 10, Volume I, Chapter 3, 3.3.8 (VOR)

·	Annex 10, Volume I, Attachment C, 3.6.5 (VOR)

·	DO-217 MASPS for DGNSS instrument approach system Special Category SCAT 1D (1993)

·	Change 1 to DO-217 (1994), change 2 to DO-217 (1990)

INTERFERENCE FROM

NON-AERONAUTICAL SOURCES

COMPATIBILITY BETWEEN ILS/VOR AND

FM BROADCASTING

General:  The ITU WARC in 1979 allocated the band at 100 –108 MHz to broadcasting services in Region 1. This band was  previously allocated in that way only in  Regions 2 and 3. The band is adjacent to the VOR/ILS band at 108 to 117.975 MHz, and interference effects have been  experienced due to transmissions of broadcast stations, particularly those operating on frequencies close to the band edge and in areas  where there is a high density of both FM stations and ILS or VOR. In many countries, FM sound broadcasting services of both low and high power are operated in this band. In some other countries, the broadcast services include analogue television transmissions. Compatibility problems due to intermodulation products, generated by both FM transmitter stations and in ILS/VOR receivers as well as overloading of the front end of aircraft ILS/VOR receivers became apparent when broadcast stations commenced use of the frequencies in the band 100 -108 MHz in the mid-seventies in Region 2.  Studies on a suitable planning methodology initiated by the CCIR (now ITU-R) in a joint aeronautical/broadcasting group have documented a viable methodology for  broadcast and aeronautical frequency assignment planning with a view to ensuring  a safe situation for air operations.

Any resolution of this problem through planning and coordination automatically restricts both services. In high-density areas, such as Western Europe and North America, the full potential of the frequency band for either service cannot be realized. Both services tend to be at their greatest density in areas of high population, which places a severe constraint on the full utilization of the potential of the 40 channels available  for use by ILS (see Annex 10, Volume I, 3.1.6). VOR services are also affected but not to the same critical degree. VHF communications, because of their greater frequency separation, are also affected, but to a lesser degree than ILS/VOR.

ITU-R Studies: After many studies on the compatibility between ILS/VOR and FM Broadcasting were  initiated in ITU  (, ITU-R approved Recommendation 1S.1009 in 1994.

The three Annexes of Recommendation IS.1009 deal comprehensively with the subject and are:

Annex 1:	Interference mechanism, system parameters and compatibility assessment criteria

Annex 2:	General assessment method

Annex 3:	Detailed compatibility assessment and practical verification.

The report comprehensively covers the treatment of conflict situations for the four interference modes:

Type A:	FM broadcasting-transmitter-generated interference products falling within the ILS/VOR bands. The two sub-types are:

Type A1:	spurious or harmonic intermodulation products generated by one or more FM transmitters within the aeronautical band

Type A2:	non-negligible components of the FM broadcasting signal, operating near the band edge 108 MHz, within the aeronautical band  (affecting only aeronautical frequencies near the 108 MHz band edge).

Type B:	ILS/VOR-receiver-generated interference caused by high-level broadcast signals operating outside the ILS/VOR band. The two sub-types are:

Type B1:	interference that may be generated in the aeronautical receiver being driven into non-linearity due to high-power broadcasting signals outside the aeronautical band. The effect on receiver resulting in  the generation of  intermodulation products in the receiver;

Type B2:	performance degradation due to high-power overload and desensitization without any frequency relationship.

This Recommendation, with its three detailed Annexes, provides the essential requirements for the identification and analysis of interference  situations and for the coordination between broadcasting and aeronautical interests within a country, or between countries. The criteria and methods have been developed and reviewed by a group of experts and represent the best available information on the subject. Furthermore, the Recommendation  is recognized by aeronautical and telecommunication authorities as the definitive guidance for planning and coordination purposes.

ICAO Studies

Handbook for evaluation of electromagnetic compatibility (EMC) between ILS and FM broadcasting stations using flight tests (1997)

This ICAO handbook is the result of considerable flight testing programmes and provides detailed guidance on this activity. It addresses the methods of flight testing for analyzing and resolving cases of FM interference to aircraft ILS localizer receivers. It describes test equipment, test procedures and interference assessment criteria. The material is also generally applicable to VOR or communications systems. The areas covered in the handbook are:

a)Description and operation of airborne equipment;

b)Interference assessment methodology; and

c)Flight test procedures

with six explanatory appendices.

Note.— This handbook is available from the Secretariat on request

SARPs on FM-immunity for ILS, VOR and VHF-communications

Since 1984, Annex 10 incorporates provisions covering the FM-immunity  performance of airborne receivers. These performance requirements are a considerable improvement compared to those of unmodified receivers. In many cases, compliance with these SARPs will require equipment replacement. These  SARPs were  incorporated to standardize the FM-immunity  performance of ILS, VOR and VHF com receivers to FM broadcast signals. Whilst the SARPs were incorporated in the Annex with Amendment No. 65 in 1984, implementation was not required until 1998, allowing fourteen years for modification or refit. In some areas of the world, implementation is not necessary due to the lower level of implementation of both ILS/VOR and FM broadcasting stations. However, full scale implementation of these SARPs is foreseen in Europe by 2001.

The FM-immunity SARPs are contained:

(i)	for ILS:			Annex 10, Volume I, 3.1.4, Interference immunity performance for ILS localizer receiving systems and Annex 10, Volume I, Att. C, 2.2.9, guidance material on above;

(ii)	for VOR:		Annex 10, Volume I, 3.3.8, Interference immunity performance for VOR receiving systems;

(iii)	for VHF Com:	Annex 10, Volume III, Part II, 2.3.3, Interference immunity performance and Annex 10, Volume III, Part II, Att. A, 1.3.

LEGBAC consultative arrangements

In Europe, the Limited European Group on Broadcasting Aeronautical Compatibility (LEGBAC) has developed a methodology, including computer programmes, to assess compatibility of assignments to FM broadcasting stations and ILS/VOR assignments. This methodology has been  accepted as the European-wide assessment method. It is compliant with the provisions of the Final Acts of the 1984 ITU Broadcasting Conference  the ITU-R Recommendation IS.1009 and the relevant SARPs.

This page deliberately left blank.

Band:	117.975–136 MHz

136–137 MHz

Service: Aeronautical mobile (R) service (air-ground and

air-air communications, VHF voice and data)

Allocation:

MHz 117.975–137

| Allocation to Services |
| --- |
| Region 1 | Region 2 | Region 3 |
| 117.975–136 | AERONAUTICAL MOBILE (R) |
|  | S5.111 S5.198 S5.199 S5.200 S5.201 |
| 136–137 | AERONAUTICAL MOBILE (R) |
|  | S5.202 S5.203 S5.203A S5.203B |

Footnotes: S5.111The carrier frequencies 2182 kHz, 3023 kHz, 5680 kHz, 8364 kHz and the frequencies 121.5 MHz, 156.8 MHz and 243 MHz may also be used, in accordance with the procedures in force for terrestrial radiocommunication services, for search and rescue operations concerning manned space vehicles. The conditions for the use of the frequencies are prescribed in Articles S31 and in Appendix S13. The same applies to the frequencies 10003 kHz, 14993 kHz and 19993 kHz, but in each of these cases emissions must be confined in a band of ±3 kHz about the frequency. S5.198Additional allocation: the band 117.975–136 MHz is also allocated to the aeronautical mobile-satellite (R) service on a secondary basis, subject to agreement obtained under No. S9.21. S5.199The bands 121.45–121.55 MHz and 242.95–243.05 MHz are also allocated to the mobile-satellite service for the reception on board satellites of emissions from emergency position-indicating radio beacons transmitting at 121.5 MHz and 243 MHz (see Appendix S13). S5.200In the band 117.975–136 MHz, the frequency 121.5 MHz is the aeronautical emergency frequency and, where required, the frequency 123.1 MHz is the aeronautical frequency auxiliary to 121.5 MHz. Mobile stations of the maritime mobile service may communicate on these frequencies under the conditions laid down in Article S31 and Appendix S13 for distress and safety purposes with stations of the aeronautical mobile service.

S5.201Additional allocation: in Angola, Armenia, Azerbaijan, Belarus, Bulgaria, Estonia, Georgia, Hungary, the Islamic Republic of Iran, Iraq, Japan, Kazakhstan, Latvia, Moldova, Mongolia, Mozambique, Uzbekistan, Papua New Guinea, Poland, Kyrgyzstan, Slovakia, the Czech Republic, Romania, Russia, Tajikistan, Turkmenistan, and Ukraine, the band 132–136 MHz is also allocated to the aeronautical mobile (OR) service on a primary basis. In assigning frequencies to stations of the aeronautical mobile (OR) service, the administration shall take account of the frequencies assigned to stations in the aeronautical mobile (R) service. S5.202Additional allocation: in Saudi Arabia, Armenia, Azerbaijan, Belarus, Bulgaria, the United Arab Emirates, Georgia, Iran ( Islamic Republic of ), Jordan, , Latvia, Moldova, Oman, Uzbekistan, Poland, Syria, Kyrgyzstan, Slovakia, the Czech Republic, Romania, the Russian Federation a, Tajikistan, Turkmenistan, and Ukraine, the band 136–137 MHz is also allocated to the aeronautical mobile (OR) service on a primary basis. In assigning frequencies to stations of the aeronautical mobile (OR) service, the administration shall take account of the frequencies assigned to stations in the aeronautical mobile (R) service. S5.203In the band 136–137 MHz, existing operational meteorological satellites may continue to operate, under the conditions defined in No. S4.4 with respect to the aeronautical mobile service, until 1 January 2002. Administrations shall not authorize new frequency assignments in this band to stations in the meteorological-satellite service. S5.203AAdditional allocation: in Israel, Mauritania, Qatar and Zimbabwe, the band 136–137 MHz is also allocated to the fixed and mobile, except aeronautical mobile (R), services on a secondary basis until 1 January 2005. S5.203BAdditional allocation: in Saudi Arabia, United Arab Emirates, Jordan, Oman and Syria, the band 136–137 MHz is also allocated to the fixed and mobile, except aeronautical mobile, services on a secondary basis until 1 January 2005.

ICAO POLICY

- No change to the allocations to the Aeronautical Mobile (route) Service in this band.

- No changes to S.5199, S5.200

- No changes to the provisions relating to the use of the emergency channels 121.5 and 123.1 MHz.

- Delete S5.198

- Delete S5.203,S5.203A, and S5.203B

- Promote measures for the deletion of S5.201 and S5.202.

AVIATION USE: The  band 117.975 - 137 MHz is the main communications band for line-of-sight range air-ground communications and is used at all airports, for en route, approach and landing phases of flight and for a variety of short-range tasks for general aviation and recreational flying activities (e.g. gliders, balloons).

The band 118–132 MHz was first allocated to aviation in 1947, the extension of the band to 136 MHz was made in 1959, and the extension to 137 MHz was made in 1979.

To satisfy increased demand and frequency congestion in high-density traffic areas, the channel width has been reduced on four occasions. From 200 kHz to 100 kHz in the 1950s, to 50 kHz in the 1960s, to 25 kHz in 1972 (Seventh Air Navigation Conference refers) and finally to 8.33 kHz in 1995 (SP COM/OPS/95 refers). Frequency assignments and equipment standards may be chosen by regional agreement to suit local demand patterns.

Single channel simplex is the mode of operation.  Double sideband amplitude modulation voice is the major modulation method. FANS recommendations envisage a transition to data in the future in this band for routine communications. Voice capability, however, will remain to be required for non-routine communication.

ICAO has allotted the band  to national and international services (see Annex 10, Volume V, Chapter 4, Table 4-1).

The aeronautical mobile (route) service is defined in S1.33 and in S43.1 (see Attachment A) as “reserved for communications related to safety and regularity of flight between any aircraft and those aeronautical stations and aeronautical earth stations primarily concerned with flight along national or international civil air routes”. Public correspondence, as defined in S1.116, is prohibited under S43.4.

Frequencies for aeronautical operational control (AOC) use are covered by the Recommendation at Annex 10, Volume V, Chapter 4, 4.1.8.1.3, which prescribes that frequencies will be selected from the band 128.825–132.05 MHz for this purpose, subject to regional agreement in areas where a scarcity exists. Control of communications content rests with the licensing authority in accordance with Annex 10, Volume II, Chapter 5, 5.1.8.6 and 5.1.8.6.1 together with the note to 5.1.8.6.

Frequency 121.5 MHz is the aeronautical emergency frequency (Annex 10, Volume V, Chapter 4, 4.1.3.1) and is designated in the Radio Regulations (Chapter SVII and Appendix S13) for general distress and safety and emergency location transmitter (ELT) purposes. It is used in the space system for search of vessels in distress/search and rescue satellite-aided tracking (COSPAS/SARSAT) system for search and rescue purposes. This use is being phased out and new COSPAS/SARSAT tracking is concentrated on 406.1 MHz

Frequency 123.1 MHz is the frequency designated as the auxiliary to 121.5 MHz (Annex 10, Volume V, Chapter 4, 4.1.4 refers). This frequency is to be used as auxiliary saerch and rescue frequency. The Radio Regulations also designate 123.1 MHz for general scene of search purposes.

Frequency 123.450 MHz is the frequency designated for air-to-air communications between aircraft engaged in flights over remote and oceanic areas and while out of range of VHF ground stations

To give low level coverage over a large area, offset carrier operation is employed in some areas (see paragraph 1.2, Annex 10, Volume III, Attachment A to Part II). Such systems using up to five carriers in one channel are possible with channel spacing of at least 25 kHz Offset carrier systems shall not be used with 8.33 kHz channel spacing.

VHF receivers are susceptible to interference from FM broadcast signals in the band 87–108 MHz. Annex 10, Volume III, Part II, specifies performance requirements to provide protection from this possibility (see Section 7-III.) ITU-R.IS.1009 provides technical planning guidance.

COMMENTARY:

The SP COM/OPS/95 discussed the shortage of assignable VHF channels necessary to support the growth in air traffic in the years ahead. This scarcity situation occurred in 1992 in the core area of Europe and is expected to occur in North America around 2002. The Communications/Meteorology/Operations (COM/MET/OPS) Divisional Meeting (1990) had earlier developed Recommendation 2/4 calling for  a review and study of the congestion in the VHF band, and the AMCP, as tasked by the Air Navigation Commission, had examined and reported the situation in 1994 (AMCP/3 refers).

Note.— The core area in Europe includes Austria, Belgium, Denmark, France, Germany, Ireland, Luxembourg, Netherlands, Switzerland and the United Kingdom.

Channel Spacing

The SP COM/OPS/95 foresaw a near-term improvement phase using a VHF voice system based on 8.33 kHz channel spacing. Not all ICAO Regions  would need to apply this new Standard. Recommendation 6/1 from this Divisional Meeting, endorsed by the Air Navigation Commission, called for  SARPs for 8.33 kHz channel spacing DSB AM to be incorporated in Annex 10 (ref. in Appendix B to the Report on Agenda Item 6). These SARPs  were adopted by the Council in 1996.  Implementation is subject to Regional agreement.

Implementation of 8.33 kHz spacing in a limited form, i.e. for upper airspace services initially, is proceeding in Europe under the aegis of ICAO, assisted by the European Organization for the Safety of Air Navigation (EUROCONTROL) in a coordination/planning role. In 2000, a number of countries in the core area of Europe had implemented 8.33 kHz channel spacing. Possible extension to the upper airspace of other countries in this Region, and to the lower airspace is likely to be agreed also.  Full implementation of en route and  later airport use (approach and landing) is likely to take a number of years - and possibly be effectively completed in the later years of this decade.

Many other Regions  can continue to meet their requirements for VHF channels using 25 kHz spacing for some years ahead without  the compelling requirement  to convert to other systems.

Use of Data in Air/Ground Communications

The CNS/ATM concept placed considerable reliance on the use of air-ground data for pilot/controller exchange of data  to supplement the use of  voice for certain categories of messages,  primarily for routine communications  between pilots and ATC. SARPs for VDL Mode 2 have been incorporated in Annex 10. Mode 2 will become the prime data system for the immediate future. The SARPs for VDL Mode 3 and Mode4  .  have now also been finalized, adopted and incorporated in Annex 10. Frequency planning guidance is being developed in AMCP for use in frequency assignment planning.

.

Band Capacity Issues

In high density congested areas such as Europe and N.America, the requirement for VHF channels continues to increase. In normal regular ATC use the maximimum utilization of a channel dedicated to an ATC sector is around 10 - 20 per cent due to other essential tasks performed by the controller. The use of air/ground data should enable an improvement  in utilization of the spectrum which should be beneficial and delay the time point of spectrum exhaustion.   Further expansion of spectrum for short range line of sight communications as demand increases will meet problems due to the general shortage of frequencies in alll parts of the radio frequency spectrum. The strategy and options to deal with this situation require early attention.

Use of the Band by Other Services

The band extensions at 132-136 MHz, and 136-137 MHz were agreed many years ago in ITU but still support other services (such as the aeronautical mobile (OR) service) existing at that time and now operating under footnote provisions. Other footnotes relate to anticipated use (such as the aeronautical mobile satellite (R) service) which did not materialize and is now not longer realistic, or practicable.  With increasing band congestion these non-AM(R)S uses can create difficulties in frequency assignment planning, and may lead to an inability to make full effective use of the available frequencies. A policy of band clearance to provide unrestricted use is now essential.

Footnote S5.198 relates to use for the AMS(R)S on a secondary basis for satellite communications for ATC.. Its origin dates from a period when the use of the VHF band for aeronautical mobile satellite was considered. There is no longer any known requirement for this use; therefore, this footnote should  be deleted.

Footnote S5.199 was included to cater for COSPAS/SARSAT use.  Retention of this footnote for the present is recommended.

Footnote S5.202 relates to use for national purposes, for off-route (OR) services, which were widespread prior to the agreement in 1959 to release 132–136 MHz in most countries for exclusive use by the (route) service.  In areas where the (OR) service operates on these frequencies co-ordination procedures agreed in the past have been satisfactory up to now. With increasing and intensive use of the frequencies in the band for AM(R)S purposes, it is likely that this (OR) use may become a problem in which case it will become essential to press for a cessation of this use.

Footnotes S5.203, S5.203A and S5.203B address the use of the band 136 – 137 MHz by the meteorological satellite service and fixed and mobile service on a secondary basis.  The ITU agreement in 1979 for AM(R)S services to be operated in this band foresaw the cessation of its use by other services by 1990 as expressed in Resolution 408 (Rev. Mob. 87) which in the mean time has been suppressed. The intervening years have seen some reductions, but also some new country names were added. Despite the secondary status of these services, this remains as a continuing risk which can not be defeated under ITU rules. Non-aviation use affects the safe use of frequencies by the AM(R)S, and prohibits full development of the use of this band  in these areas.   Tthese footnotes  must therefore be deleted at the earliest opportunity. No extension beyond the presently quoted date of 2005 should be permitted.

TECHNICAL AND OTHER INFORMATION

Band: 117.975–137 MHz

Service: AM(R)S

Aviation use: Air-ground and air-air communication (VHF voice and data)

Annex 10

SARPs:  Annex 10, Volume III, Part II, Chapter 2, 2.1, 2.2 and 2.3

Frequency plan: Annex 10, Volume V, Chapter 4, 4.1

Channelization: 25 kHz /8.33 kHz

Planning criteria:  Annex 10, Volume V, Attachment A

RTCA MOPS: DO 186A - MOPS for airborne radio communications equipment operating within the frequency range 117.975–137 MHz (1995).

Eurocae MPS: ED-23B

ARINC characteristic: 716-7, 750 (Data)

ITU Res/Rec:

·

·	Rec. No. 714 (Mob-87): Compatibility between the aeronautical mobile (R) service in the band 117.975–137 MHz and sound broadcasting stations in the band 87.5–108 MHz.

ITU-R: ITU-R IS.1009: Compatibility between the sound broadcasting service in the band 87–108 MHz and the aeronautical services in the band 108–137 MHz

Other material:

·	RTCA DO-225: VHF air-ground communication systems improvements alternative studies and selection of proposals for future action (1994)

·	RTCA DO-224: Signal in space MASPS for advanced VHF digital data communications, including compatibility with digital voice techniques (1994).

·	DO 176 - FM BC: Interference related to airborne ILS, VDR and VHF communications (1981).

Band: 121.5 MHz, 123.1 MHz and 243 MHz (mobile)

Service: AM(R)S

Aviation use: Emergency frequencies for use in aircraft emergencies and in ELT (121.5 MHz ) and for scene of search communication (123.1 MHz ).

Emergency frequency in mobile service (243 MHz): The frequency 243 MHz (twice that of the aeronautical emergency frequency 121.5 MHz ) is designated by the Radio Regulations (see Annex 10, Volume V, Chapter 2 — Distress frequencies and Radio Regulation S5.256) for use in distress situations. Survival craft stations using VHF (ELT and EPIRB) are normally fitted with both 121.5 MHz and 243 MHz.

Commentary: None

Footnotes: S5.256.

ICAO POLICY No change to the provisions in Chapter SVII and Appendix S13 relating to the use of 121.5 MHz, 123.1 MHz and 243 MHz.

TECHNICAL AND OTHER INFORMATION

Frequency: 121.5 MHz, 123.1 MHz, and 243 MHz

Annex 10

SARPs:  Annex 10, Volume III, Part II, Chapter 5

Frequency plan:  Annex 10, Volume V, Chapter 4

Channelization:  None

Planning criteria:  None

RTCA MOPS:

DO 183 MOPS for emergency locator transmitters operating on 121.5 and 243 MHz.

DO-204

Eurocae MPS: None

ARINC characteristic: None

ITU Res/Rec:

·	Res. No. 601 (Rev. Mob-87) Recommendations and Standards for emergency position-indicating radio beacons operating on the frequencies 121.5 MHz and 243 MHz

·	Rec. 604 (Rev. Mob-87): Future use and characteristics of emergency position-indicating radio beacons (EPIRBs)

·	Resolution 18 (MOB-83) relating to the procedure for identifying and announcing the position of ships and aircraft of States not parties to an armed conflict.

ITU-R Rec: ITU-RM 690: Technical characteristics of emergency position indicating radio beacons (EPIRBs) operating on carrier frequencies 121.5 MHz and 243 MHz

Other material:

·	ITU Radio Regulations, Chapter SVII and Appendix S13

·	DO-182 ELT equipment and installation performance (1982)

Band: 328.6–335.4 MHz

Service: Aeronautical radionavigation (ILS glide path)

Allocation:

MHz 328.6–335.4

| Allocation to Services |
| --- |
| Region 1 | Region 2 | Region 3 |
| 328.6–335.4 | AERONAUTICAL RADIONAVIGATION |
|  | S5.258 S5.259 |

Footnotes: S5.258The use of the band 328.6–335.4 MHz by the aeronautical radionavigation service limited to Instrument Landing Systems (glide path). S5.259Additional allocation: in Egypt, Israel, Japan, and Syria the band 328.6–335.4 MHz is also allocated to the mobile service on a secondary basis, subject to agreement obtained under No. S9.21. In order to ensure that harmful interference is not caused to stations of the aeronautical radionavigation service, stations of the mobile service shall not be introduced in the band until it is no longer required for the aeronautical radionavigation service by any administration which may be identified in the application of the procedure invoked under No. S9.21.

ICAO   POLICY

- No change to current allocation to the Aeronautical Radionavigation Service.

- No change to S5.258

- Deletion of S5.197

AVIATION USE: Footnote S5.258 limits the use of this band to ILS glide path. Frequencies are used at a spacing of 150 kHz (Annex 10, Volume I, Chapter 3, 3.1.6.1) and are paired with those of the ILS localizer.

COMMENTARY: ICAO policy for the future need and use of this allocation is described in detail in the general policy for the use of ILS (see ILS localizer at 108–117.975 MHz ).

USE of the band by other services

Footnote S5.259 was inserted by the ITU WARC-87. This footnote uses the same text (except for the list of countries) as Footnote S5.197 for the ILS localizer and VOR band at 108-117.975 MHz. At WRC-2000, most of the countires listed removed their name from this footnote. The remaining country names must now also be deleted to protect ILS glide path services in these areas, and to avoid the possibility of new names being added at a future conference.

TECHNICAL AND OTHER INFORMATION

Band: 328.6–335.4 MHz

Service: Aeronautical radionavigation

Aviation use: ILS glide path

Annex 10

SARPs:  Annex 10, Volume I, Chapter 3, 3.1.5

Frequency plan:  Annex 10, Volume I, Chapter 3, 3.1.6

Channelization:  300 kHz or 150 kHz spacing

Planning criteria:  as for ILS — localizer

RTCA MOPS: DO-192 MOPS for airborne ILS glide slope receiving equipment operating within the radio frequency range of 328.6–335.4 MHz (1986)

Eurocae MPS:

ARINC characteristic: 551

ITU Res/Rec:

ITU-R:

Other material:

Band: 406–406.1 MHz

Service: Mobile satellite (Earth-to-space) (search and rescue)

Allocation:

MHz 406–406.1

| Allocation to Services |
| --- |
| Region 1 | Region 2 | Region 3 |
| 406–406.1 MOBILE-SATELLITE (Earth-to-space) |
|  | S5.266 S5.267 |  |

Footnotes: S5.266The use of the band 406–406.1 MHz by the mobile-satellite service is limited to low power satellite emergency position-indicating radiobeacons (see also Article S31 and Appendix S13). S5.267Any emission capable of causing harmful interference to the authorized uses of the band 406–406.1 MHz is prohibited.

ICAO POLICY · No change as long as 406.05 MHz plays a role in the global maritime distress and safety service (GMDSS). · No change to S5.266 and S5.267

AVIATION USE: This one-way (Earth-to-space) satellite service is for the use with satellite EPIRB operating on the nominal frequency of 406.05 MHz. The COSPAS/SARSAT service, part of the global maritime distress and safety service (GMDSS) which receives the distress transmissions and relays back to Earth, is a joint enterprise operated on a multi-national basis for the benefit of all users.

COMMENTARY: ICAO participates with the International Maritime Organization (IMO) and other international bodies in discussions on the global aspects of search and rescue which encompass the use and deployment of this frequency.

Recent cases of serious interference from non-emergency sources have caused concern on the effectiveness of COSPAS/SARSAT services (see also ITU Resolution 205 (Rev. Mob 87)).

TECHNICAL AND OTHER INFORMATION

Band: 406–406.1 MHz

Service: Mobile satellite (Earth-to-space)

Aviation use: Search and rescue

Annex 10

SARPs: Annex 10, Volume III, Part II, Appendix 1 to Chapter 5

Frequency plan: Annex 10, Volume V

Channelization: None

Planning criteria: 	None

RTCA MOPS: DO-204 MOPS for 406 MHz emergency locator transmitters (ELT) 1994. Change 1 to DO-204 (1994)

Eurocae MPS:

ARINC characteristic:

ITU Res/Rec: Res. No. 205 (Rev. Mob-87): Protection of the band 406–406.1 MHz allocated to the mobile-satellite service

ITU-R: ITU-RM 633 Transmission characteristics of a satellite position indicating radio beacon (satellite EPIRB) system operating through a low polar orbiting satellite system in the 406 MHz band.

CCIR:

Other material:

Band: 960–1215 MHz

Service: Aeronautical radionavigation (DME/SSR/ACAS)

Allocation:

MHz 960–1 215

| Allocation to Services |
| --- |
| Region 1 | Region 2 | Region 3 |
| 960–1215 AERONAUTICAL RADIONAVIGATION S5.328 |
|  | S5.328A |  |

Footnotes: S5.328The use of the band 960–1215 MHz by the aeronautical radionavigation service is reserved on a worldwide basis for the operation and development of airborne electronic aids to air navigation and any directly associated ground-based facilities. S5.328A Additional allocation : the band 1164-1215 MHz is also allocated to the radionavigation-satellite service (space-to-Earth)(space-space) on a primary basis. The aggregate power flux density produced by all the space stations of all radionavigation-satellite systems at the Earths surface shall not exceed the provisional value of -115 dB(W/m2 ) in any 1 MHz band for all angles of arrival. Stations in the radionavigation-satellite service shall not cause interference to, nor claim protection from, stations of the aeronautical radionavigation service. The provisions of Resolution 605 (WRC-2000) apply.

ICAO  POLICY

- No change to the current allocation to the aeronautical radionavigation service in the band 960-1215 MHz.

- No change to S5.328.

- No change to the regulatory provisions contained in footnote S5.328A

- Support the studies under ITU-R Resolution 605 (WRC-2000) and for the inclusion of an appropriate PFD limit value agreed by ICAO in S5.328A.

- Support agreement on any additional regulatory measures in ITU Resolutions and ITU-R Recommendations, which promotes the protection of DME.

AVIATION USE: The band 960–1215 MHz is a prime radionavigation band which is used intensively, and extensively, to support a number of aviation systems, for both civil and military purposes. The civil systems are:

Distance measuring equipment (DME): DME is the ICAO Standard system for the determination of the distance between an aircraft and a -ground based- DME beacon  within radio line of sight. The DME is using pulse techniques and time measurement. DME/N is the standard system used for en-route and terminal navigation.  It can be  co-located with VHF omnidirectional radio range (VOR) enabling the aircrafts position to be determined through a measurement of its bearing and the distance relative to the VOR/DME. Alterntively, the aircrafts position can be determined through measurement of the distances from two DME's  and the flight management system (FMS) equipment in the aircraft. DME/P is a precision version of DME with an enhanced precision measurement capability which is  used in conjunction with   MLS to provide accurate distance to touch down. TACAN is the military equivalent of DME which also has a bearing capability and  uses the same channel plan as for DME.

The channel plan (Annex 10, Volume I, Chapter 3, Table A) employs discrimination in both pulse length and pulse spacing, generating four possible modes (X,Y,W,Z) as a means of creating additional channels

Secondary surveillance radar (SSR): SSR is the ICAO Standard system for  secondary surveillance radar . It is used either as a stand alone system  or co-located and synchronized with primary radar. The ground equipment is an interrogator and the aircraft equipment is a transponder responding to signals from the interrogator. SSR employs Mode A for transmitting identification  and Mode C for transmitting, in addition, pressure-altitude information. Mode S employs selective addressing of the airvraft and has a limited data link capability. SSR Mode S is a continuing requirement, in particular in high density airspace.

All SSR installations operate on 1030 MHz for the ground-to-air interrogation signal, and 1090 MHz for the air-ground reply. Extensive use of pulse repetition frequency (PRF) discrimination and plot plan processing techniques assists in reducing the number of unvalidated responses being processed by the ground receiving system.

Airborne collision avoidance system (ACAS): ACAS is the ICAO Standard system for detection and avoidance of airborne conflict situations. ACAS operates as a supplementary system to SSR using the same frequency pair of 1030 MHz and 1090 MHz. 1030 MHz is used for the air-to-air interrogation and 1090 MHz for the air-to-air reply. The three modes, I, II and III, provide increased capability at each level of functional implementation. Provision is made for air-ground communication with ground stations using the Mode S data link. A diagram of the use of the band by air and ground elements of SSR is at Figure 7-1 .

COMMENTARY:

The present internationally agreed channel plans occupy the full band 960–1215 MHz.   The DME channel Plan is displayed at Table A of Annex 10 Chapter 3. The arrangement of air-ground interrogations, and ground to air replies showing the standard 63 MHz separation and the interleaving of X and Y channels is shown at Fig. 7/1 below.      Both X and Y channels are currently deployed in the higher density areas where the implementation of DME (and TACAN) is extensive. W and Z channels are intended for use with MLS, employing an interrogation pulse pair with a different pulse length on the X and Y channels respectively.

Some world areas are prone to frequency scarcity.   Pairing of DME  with VOR or ILS and triple pairing  of DME with ILS and with microwave landing system (MLS), a necessary operational technique for air safety, or for the transition to MLS where this system is brought in to use, and co-channel TACAN use, are factors often creating difficulties in frequency planning which are not easily overcome.

Figure 7-1.  Channeling DME band (960 - 1 215 MHz)

VOR/DME could be replaced by GNSS, or supplemented by the use of area navigation based on DME/DME. The latter system, where it becomes established , is likely to extend beyond the year 2015.

The use of DME/P will provide essential support to higher Category ILS and MLS operations. Present expectations are that no Category III operations other than with ILS or MLS are foreseen in the period up to and beyond the year 2015.

SSR and SSR Mode S are the main technique for surveillance in high traffic density areas (FANS II/4 refers).

SSR Mode S is a tool for air traffic management mainly in  high traffic density continental airspaces.

Carriage of ACAS systems may be mandatory in some airspace by national regulation or by regional agreement.

The overall situation in this band is one of a continuing exploitation of current systems. The realistic probability is that some important uses of the band, such as DME/DME, DME/P with MLS, and SSR Mode S, will continue as the main ATS tool in high density airspace well beyond 2015, and may be only slowly reduced after that date.

The use of the band for GNSS

The frequencies in the band 1164-1215  MHz have been identified as suitable to support components for the future development of GNSS, in addition to GNSS components operating on other  frequencies. Currently, a main component of GNSS is operating in the GNSS band at 1559-1610 MHz. Proposed schemes include an additional frequency for GPS with higher signal levels and a more robust interference rejection characteristic at 1172.xxxMHz, and a European initiative (Gallileo) for an independent radionavigation satellite system.operating under civil auspicies.  Both systems, if implemented, are considered for recognition in the GNSS Panel as elements of the ICAO GNSS   The time scales for first use in both cases is in the frame 2008-2012.

The ITU World Radiocommunication Conference in 2000 (WRC-2000) adopted footnote S5.328A which includes an allocation to the radionavigation satellite service (RNSS, the ITU terminology for GNSS systems) in the band 1164-1215 MHz. It is expected that the two proposed systems (GPS L5 and Galileo) will operate in separate parts of this allocation without any overlap.  Protection of the DME channels 79X to 101X, the use of which can be affected by this allocation, is to be assured by the imposition of a power flux density limitation for the space to earth signals of the RNSS service, and by a regulatory provision requiring the RNSS service neither to cause interference to, nor claim protection from the stations of the ARNS service operating in this band.

Aviation support and agreement to this new allocation was an essential element in the ITU discussions.  The precise value for the PFD limit remains as an issue to be reviewed and finalized at WRC-2003 following study in ITU-R under Resolution 605 of WRC-2000.  Earlier studies by ICAO had concluded that the PFD limit should be between minus 115 and minus 119 dBW/M2/MHz in order to protect DME under all operational conditions. This remains as a contentious issue, to be further addressed in ICAO and ITU-R studies. The final value has to permit a continued unrestricted use of existing DME, and additionally permit future additions of DME assignments and possible new aeronautical radionavigation systems, which may become necessary.

Use of the 960-1215 MHz band by other services

In some countries the band is also used by national communications systems  (e.g. JTIDS) on a compatible basis with DME/SSR. Such systems are permitted to operate on a strict basis of non-interference to the radionavigation systems using the band in accordance with the ITU allocation.

TECHNICAL AND OTHER INFORMATION (DME)

Band: 960–1215 MHz

Service: Aeronautical radionavigation

Aviation use: DME

Annex 10

SARPs:

DME: Annex 10, Volume I, Chapter 3, 3.5

Frequency plan:

DME: Annex 10, Volume I, Chapter 3, Table A

DME: Annex 10, Volume V, Chapter 4, 4.3

Planning criteria:

DME, Annex 10, Volume I, Attachment C, Section 7

EUR ANP COM/3

RTCA MOPS:

DO 189, MOPS for airborne DME operations within the frequency range of 960–1215 MHz (1995).

Eurocae MPS:

ARINC characteristic: 709, 709A (DME/P)

ITU Res/Rec:

ITU-R Rec: Res. No. 605 (WRC-2000): Use of the frequency band 1164 - 1215 MHz by systems of the Radionavigation satellite service (space-to-Earth)

CCIR:

Other material:

TECHNICAL AND OTHER INFORMATION (SSR)

Band: 1030 MHz and 1090 MHz

Service: Aeronautical radionavigation

Aviation use: SSR/ACAS

Annex 10

SARPs: Annex 10, Volume IV, Chapters 3 and 4

Frequency plan: Two frequency 1030 MHz for  ground-air interrogations.  1090 MHz for air-ground reply

Channelization:   N/A

Planning criteria:  Coordination of the pulse repetition frequency (PRF) on a national basis is required for overlapping coverage areas of SSR.

RTCA MOPS:

·	DO 181A (Mode S), DO 185 (TCAS)

·	DO 185 MOPS for traffic alert and collision avoidance systems; airborne equipment consolidated edition (1983/1990)

·	Change 1 to DO-185 (1994)

·	DO 218 MOPS for the Mode S airborne data link processor

·	Change 1 to DO 218

Eurocae MPS: 718 (Mode S transponder and ACAS)

ARINC characteristic:

ITU Res/Rec:

·	Res. No. 18 (Mob-83): Relating to the procedure for identifying and  announcing the position of ships and aircraft of States not parties to an armed conflict

·	Rec. No. 601: Concerning the matter of providing a suitable frequency allocation for a collision avoidance system in the aeronautical radionavigation service

ITU-R:

Other material: DO-197A MOPS for active traffic alert and collision avoidance system 1 (active TCAS 1) (1994)

Band: 1215–1260 MHz

Service: Radiolocation/radionavigation satellite (GNSS/surveillance radar)

Allocation:

MHz 1215–1260

| Allocation to Services |
| --- |
| Region 1 | Region 2 | Region 3 |
| 1215–1240 | RADIOLOCATION |
|  | RADIONAVIGATION-SATELLITE (space-to-Earth) (space-space) S5.329, S5.329A EARTH EXPLORATION-SATELLITE (active) |
|  | SPACE RESEARCH (active) S5.330 S5.331 S5.332 |
| 1240–1260 | RADIOLOCATION |
|  | RADIONAVIGATION-SATELLITE (space-to-Earth) (space-space) S5.329, S5.329A EARTH EXPLORATION-SATELLITE (active) SPACE RESEARCH (active) Amateur S5.330 S5.331 S5.332 S5.334 S5.335 |

Footnotes: S5.329Use of the radionavigation-satellite service in the band 1215– 1300 MHz shall be subject to the condition that no harmful interference is caused to, and no protection claimed from, the radionavigation service authorized under No. S5.331. See also Resolution 606 (WRC-2000)] S5.329A Use of systems in the radionavigation-satellite service (space-space) operating in the bands 1215-1300 MHz and 1559-1560 MHz is not intended to provide safety service applications, and shall not impose any additional constraints on other systems or services operating in accordance with the Table of Frequency Allocations. S5.330Additional allocation: in Angola, Saudi Arabia, Bahrain, Bangladesh, Cameroon, China, the United Arab Emirates, Eritrea, Ethiopia, Guyana, India, Indonesia, the Islamic Republic of Iran, Iraq, Israel, Japan, Jordan, Kuwait, Lebanon, Libya, Morocco, Mozambique, Nepal, Nigeria, Pakistan, the Philippines, Qatar, Syria, Somalia, Sudan, Sri Lanka, Chad, Togo and Yemen, the band 1215–1300 MHz is also allocated to the fixed and mobile services on a primary basis. S5.331Additional allocation: in Algeria, Germany, Austria, Bahrain, Belgium, Benin, Bosnia and Herzegovina, Burundi, Cameroon, China, Croatia, Denmark, the United Arab Emirates, France, Greece, India,Iran (the Islamic Republic of ),

Iraq, Kenya, The Former Yugoslav Republic of Macedonia, Liechtenstein, Luxembourg, Mali, Mauritania, Norway, Oman, the Netherlands, Portugal, Qatar, Senegal, Slovenia, Somalia, Sudan, Sri Lanka, Sweden, Switzerland, Turkey and Yugoslavia, the band 1215–1300 MHz is also allocated to the radionavigation service on a primary basis. S5.332In the band 1215– 1260 MHz, active spaceborne sensors in the earth exploration-satellite and space research services shall not cause harmful interference to, claim protection from, or otherwise impose constraints on operation or development of the radiolocation service, the radionavigation -satellite service and other services allocated on a primary basis.S5.333 (SUP - WRC-97) S5.334Additional allocation: in Canada and the United States, the bands 1240–1300 MHz and 1350–1370 MHz are also allocated to the aeronautical radionavigation service on a primary basis. S5.335 In Canada and the United States in the band 1 240-1 300 MHz, active spaceborne sensors in the earth exploration-satellite and space research services shall not cause interference to, claim protection from, or otherwise impose constraints on operation or development of the aeronautical radionavigation service. (WRC-97)

ICAO  POLICY

- No change to the allocation to the radionavigation Service contained in the   footnotes.

- No change to the regulatory provisions of S5.329 and S5.329A.

- Support the incorporation in S5.329 of an appropriate, aggregate PFD limit for the Radionavigation Satellite Service to protect radar stations.

- Support the adoption of a regulatory framework having full mandatory force to implement the protection measures for the terrestrial Radionavigation Services operating in this band.

- Support the ITU-R studies under Resolution 606 (WRC-2000)

AVIATION USE: The band is primarily used for ground-based primary radar (long range) as part of the band 1215–1350 MHz. The band is also used for the L2 frequencies (initially 1246 MHz + 24 ´ 437.5 kHz ) of GLONASS. This frequency is expected to be shifted in the near future (1243.5 MHz + 14 ´ 437.5 kHz. The frequency of 1227.6 MHz is used for the precision positioning service (PPS, L2) of GPS, extending the accuracy of GPS. L2 (PPS) will become available for civil use. Techniques have been developed for use of ground stations to correct for ionospheric delays (see also commentary on GNSS usage of the band 1559–1610 MHz).

COMMENTARY: WRC-2000 adopted an allocation to the radionavigation satellite service in the space-to-space direction in this band. GPS and GLONASS already operate in this band in the spae-to-Earth direction. The allocation improves reception of GNSS signals on board space-vehicles.

Studies in ITU-R SG 8 are underway to establish the need for (and , if necessary, the level of) a power flux density limitation on the spaceborne transmissions of the RNSS with a view to protect radar systems from harmful interference (Ref. Resolution 606 (WRC-2000)).

Band: 1260–1400 MHz

Service: Aeronautical radionavigation; radiolocation (surveillance radar)

Allocation:

MHz 1260–1400

| Allocation to Services |
| --- |
| Region 1 | Region 2 | Region 3 |
| 1 260–1 300 | RADIOLOCATION RADIONAVIGATION -SATELLITE (space-earth) (space-space) S5.329, S5.329A EARTH EXPLORATION-SATELLITE (active) SPACE RESEARCH (active) Amateur S5.282 S5.330 S5.331 S5.334 S5.335 S5.335A |
| 1 300–1 350 | AERONAUTICAL RADIONAVIGATION S5.337 RADIONAVIGATION-SATELLITE (Earth-space) S5.149 S5.337A RADIOLOCATION S5.149 S5.337A |
| 1 350–1400 FIXED MOBILE RADIOLOCATION S5.149 S5.338 S5.339 | 1 350–1 400 RADIOLOCATION S5.149 S5.334 S5.339 |  |

Footnotes: S5.149In making assignments to stations of other services to which the bands: ..... 1330–1400 MHz * ..... are allocated (* indicates radio astronomy use for spectral line observations), administrations are urged to take all practicable steps to protect the radio astronomy service from harmful inter-ference. Emissions from spaceborne or airborne stations can be particularly serious sources of interference to the radio astronomy service (see Nos. S4.5 and S4.6 and Article S29).

S5.282 In the bands 435–438 MHz, 1260–1270 MHz, 2400–2450 MHz, 3400–3410 MHz (in Regions 2 and 3 only) and 5650–5670 MHz, the amateur-satellite service may operate subject to not causing harmful interference to other services operating in accordance with the Table (see No. S5.43). Administrations authorizing such use shall ensure that any harmful interference caused by emissions from a station in the amateur-satellite service is immediately eliminated in accordance with the provisions of No. S25.11. The use of the bands 1260–1270 MHz and 5650–5670 MHz by the amateur- satellite service is limited to the Earth-to-space direction. S5.329Use of the radionavigation-satellite service in the band 1215– 1300 MHz shall be subject to the condition that no harmful interference is caused to, and no protection claimed from, the radionavigation service authorized under No. S5.331. See also Resolution 606 (WRC-2000)] S5.329A Use of systems in the radionavigation-satellite service (space-space) operating in the bands 1215-1300 MHz and 1559-1560 MHz is not intended to provide safety service applications, and shall not impose any additional constraints on other systems or services operating in accordance with the Table of Frequency Allocations. S5.330Additional allocation: in Angola, Saudi Arabia, Bahrain, Bangladesh, Cameroon, China, the United Arab Emirates, Eritrea, Ethiopia, Guinea, Guyana, India, Indonesia, the Islamic Republic of Iran, Iraq, Israel, Japan, Jordan, Kuwait, Lebanon, Libya, Malawi, Morocco, Mozambique, Nepal, Nigeria, Pakistan, the Philippines, Qatar, Syria, Somalia, Sudan, Sri Lanka, Chad, Thailand, Togo and Yemen, the band 1215–1300 MHz is also allocated to the fixed and mobile services on a primary basis. S5.331Additional allocation: in Algeria, Germany, Austria, Bahrain, Belgium, Benin, Bosnia and Herzegovina, Burundi, Cameroon, China, Croatia, Denmark, the United Arab Emirates, France, Greece, India, the Islamic Republic of Iran, Iraq, Kenya, the former Yugoslav Republic of Macedonia, Liechtenstein, Luxembourg, Mali, Mauritania, Norway, Oman, Pakistan, the Netherlands, Portugal, Qatar, Senegal, Slovenia, Somalia, Sudan, Sri Lanka, Sweden, Switzerland, Turkey and Yugoslavia, the band 1215–1300 MHz is also allocated to the radionavigation service on a primary basis. S5.332 In the band 1215-1260 MHz , active spaceborne sensors in the earth exploration-satellite service and space research services shall not cause harmful interference to, claim protection from, or otherwise impose constraints on the operation or development of the radiolocation service, the radionavigation-satellite service, and other services allocated on a primary basis.. S5.335AIn the band 1260–1300 MHz, active spaceborne sensors in the earth exploration-satellite and space research services shall not cause harmful interference to, claim protection from or otherwise impose constraints on the operation and development of the radiolocation service and other services allocated by footnotes on a primary basis. S5.334Additional allocation: in Canada and the United States, the bands 1240–1300 MHz and 1350–1370 MHz are also allocated to the aeronautical radionavigation service on a primary basis. S5.335In Canada and the United States in the band 1240–1300 MHz, active spaceborne sensors in the earth exploration-satellite and space research services shall not cause interference to, claim protection from, or otherwise impose constraints on operation or development of the aeronautical radionavigation service. S5.336Not used. S5.337The use of the bands 1300–1350 MHz, 2700–2900 MHz and 9000–9200 MHz by the aeronautical radionavigation service is restricted to ground-based radars and to associated airborne transponders which transmit only on frequencies in these bands and only when actuated by radars operating in the same band. S5.337A The use of the band 1300-1350 MHz by earth stations in the radionavigation-satellite service and by stations in the radiolocation service shall not cause harmful interference to, nor constrain the operation and development of the aeronautical radionavigation service.

S5.338In Azerbaijan, Bulgaria, Mongolia, Kyrgyzstan, Slovakia, the Czech Republic, Romania, and Ukraine, the existing installations of the radionavigation service may continue to operate in the band 1350– 1400 MHz. S5.339The bands 1370–1400 MHz, 2640–2655 MHz, 4950–4990 MHz and 15.20–15.35 GHz are also allocated to the space research (passive) and earth exploration-satellite (passive) services on a secondary basis.

ICAO  POLICY

- No change to the allocations to the aeronautical radionavigation service.

- No change to S5.331, S5.334 and S5.337.

- Support the inclusion of a PFD limit on the radionavigation satellite service, as a necessary protection for en route radar surveillance services to aircraft.

- Support regulatory and technical measures which complement the allocation provisions and give these important radar services full assurance that their safety case will not be infringed.

- Support the ITU-R studies under Resolutions 606 (WRC-2000) and 607 (WRC-2000).

AVIATION USE: These bands are used extensively for 23 cm (L-band) primary surveillance radar (PSR), for both en-route and terminal surveillance tasks. Modern systems employing digitized plot extraction often operate on multiple frequency and use pulse repetitio frequency discrimination  (PRF) where up to four or even six frequencies may be used by   a single radar spaced over a band of 100 MHz. For these requirements, the band from around 1215 to 1370 MHz (as for example in Footnote S5.334) must be available. The band is also used extensively by other users for the long-range detection of aircraft targets. Co-located SSR and primary surveillance radar are often employed with combined plot extraction, electronic processing and display. Electronically generated labels displaying flight number and other data, i.e. altitude reported from SSR Mode C, are often added to provide a complete radar data picture.

23 cm is the preferred wave length for long-range radar where a sufficiently large antenna can be installed to provide narrow beams in azimuth and phased arrays for beam switching for multi-purpose mode operation. This frequency range also provides less weather clutter and is hence less affected by cold weather frontals and thunderstorm effects.

COMMENTARY: Under FANS Recommendations, the use of primary radar is expected, in the long term, to diminish in both en-route and terminal areas [Report on Agenda Item 7 of the Tenth Air Navigation Conference (1991) (Doc 9583) refers]. The recommended replacement system is SSR Mode S, or some form of ADS using air-ground data link. Future possible use of ADS or ADS-B may affect the requirements for primary or secondary radar. Primary radar with its high level investments is however expected to continue to be utilized in civil aviation for many years into the future and beyond the year 2015. One of the important features of primary radar is the independent role it plays in surveillance of airspace.

The Communications/Meteorology/Operations (COM/MET/OPS) Divisional Meeting (1990) (Attachment 4 to Appendix B to the Report on Agenda Item 1 refers) reported the wide use of this band (and also of the band 2700–2900 MHz) for en-route and terminal surveillance. Table 1 in this attachment provides estimates of the use amounting to 583 radars worldwide. Paragraph 4 proposes the ICAO position of no change to the allocation at 1300–1350 MHz and adjoining bands.

The conclusion which appears from these considerations is that these bands should be retained and protected for the foreseeable future for the operation of radar systems.

Use of the band by the Radionavigation-satellite service

WRC-2000 introduced an allocation to the radionavigation satellite service (RNSS) in the frequency bands 1260-1300 MHz for space-Earth and space-to-space direction, and 1300-1350 MHz for the Earth-to-space direction to meet the requirements of a proposed European civil operated satellite radionavigation system (Galileo). The service is not expected to be operational before about 2010. The use of the band 1260-1300 MHz is not intended to support safety service applications. The components in these bands are not being considered as a part of the ICAO GNSS system.

The Galileo system may also use frequency components in the DME band at 1164-1215 MHz, the GNSS band at 1559-1610 MHz, and the MLS band at 5000-5030 MHz. RNSS will operate in the band 1260 - 1350 MHz on a non-protection basis with respect to existing and future ARNS services. Aviation policy is to seek protection from RNSS spaceborne transmissions through the establishment of a PFD limitation on the RNSS service in the band 1260 - 1300 MHz. Studies under WRC-2000 Resolution 606 on this matter will be reported to WRC-2003 and are expected include the terms of the protection needed to protect the aeronautical radionavigation service in the band 1260-1300 MHz.

Studies under Resolution 607 are necessary to establish criteria on the compatibility between the radiolocation service in the band 1300-1350 MHz which has been upgraded to a primary status at WRC-2000. Although no specific studies are requested to protect the aeronautical radionavigation service from interference from the Earth-to-space transmissions of the RNNS service, geographical separation criteria between radar and RNSS Earth stations are to be developed.

TECHNICAL AND OTHER INFORMATION

Band: 1260–1400 MHz

Service: Radio location/aeronautical radionavigation/radionavigation-satellite

Aviation use: Medium- and long-range surveillance radar

Annex 10

SARPs:   None

Frequency plan:  Nationally produced

Channelization:  Nationally produced

Planning criteria:  Nationally produced

RTCA MOPS: None

Eurocae MPS: None

ARINC characteristic: None

ITU Res/Rec: Rec. No. 701: Relating to the use of frequency band

1330–1400 MHz by the radio astronomy service

Res. No. 606 (WRC-2000) relating to the use of the frequency band 1215 - 1300 MHz by systems of the radionavigation-satellite service (space-to-Earth)

Res. No. 607 (WRC-2000) relating to studies on compatibility between stations of the radionavigation-satellite service (Earth-to-space) and the radiolocation service operating in the frequency band 1300 - 1350 MHz.

ITU-R:

Other material:

Bands: Mobile satellite bands 1525–1559 MHz and 1626.5–1660.5 MHz

Service: AMS(R)S (satellite communications)

1. Space-Earth MHz 1525–1559 and 1626.5–1660.5

| Allocation to Services |
| --- |
| Region 1 | Region 2 | Region 3 |
| 1525–1530 SPACE OPERATION (space-to-Earth) FIXED MOBILE-SATELLITE (space-to-Earth) S5.351A Earth Exploration-Satellite Mobile except aeronautical mobile S5.349 S5.341 S5.342 S5.350 S5.351 S5.352A S5.354 | 1525–1530 SPACE OPERATION (space-to-Earth) MOBILE-SATELLITE (space-to-Earth) S5.351A Earth Exploration-Satellite Fixed Mobile S5.343 S5.341 S5.351 S5.354 | 1525–1530 SPACE OPERATION (space-to-Earth) FIXED MOBILE-SATELLITE (space-to-Earth) S5.351A Earth Exploration-Satellite Mobile S5.349 S5.341 S5.351 S5.352A S5.354 |
| 1530–1533 SPACE OPERATION (space-to-Earth) MOBILE-SATELLITE (space-to-Earth) S5.353A Earth Exploration-Satellite Fixed Mobile except aeronautical mobile S5.341 S5.342 S5.351 S5.354 | 1530–1533 SPACE OPERATION (space-to-Earth) MOBILE-SATELLITE (space-to-Earth) S5.353A Earth Exploration-Satellite Fixed Mobile S5.343 S5.341 S5.351 S5.354 |
| 1533–1535 SPACE OPERATION (space-to-Earth) MOBILE-SATELLITE (space-to-Earth) S5.353A Earth Exploration-Satellite Fixed Mobile except aeronautical mobile S5.341 S5.342 S5.351 S5.354 | 1533–1535 SPACE OPERATION (space-to-Earth) MOBILE-SATELLITE (space-to-Earth) S5.353A Earth Exploration-Satellite Fixed Mobile S5.343 S5.341 S5.351 S5.354 |
| 1535–1544 | MOBILE-SATELLITE (space-to-Earth) S5.341 S5.351 S5.353A S5.354 S5.355 |
| 1544–1545 | MOBILE-SATELLITE (space-to-Earth) S5.341 S5.354 S5.355 S5.356 |
| 1545–1555 | MOBILE-SATELLITE (space-to-Earth) S5.341 S5.351 S5.354 S5.355 S5.357 S5.359 S5.357A |
| 1555–1559 | MOBILE-SATELLITE (space-to-Earth) S5.341 S5.351 S5.354 S5.355 S5.359 S5.362A |

2. Earth-space

| Allocation to Services |
| --- |
| Region 1 | Region 2 | Region 3 |
| 1626.5–1631.5 MOBILE-SATELLITE (Earth-to-space) S5.341 S5.351 S5.354 S5.355 S5.359 S5.353A | 1626.5–1631.5 MOBILE-SATELLITE (Earth-to-space) S5.341 S5.351 S5.354 S5.355 S5.359 S5.353A |
| 1631.5–1636.5 | MOBILE-SATELLITE (Earth-to-space) S5.341 S5.351 S5.354 S5.355 S5.359 MOD S5.374 S5.353A |
| 1636.5–1645.5 | MOBILE-SATELLITE (Earth-to-space) S5.341 S5.351 S5.353A S5.354 S5.355 S5.359 |
| 1645.5–1646.5 | MOBILE-SATELLITE (Earth-to-space) S5.341 S5.354 S5.375 |
| 1646.5–1656.5 | MOBILE-SATELLITE (Earth-to-space) S5.357A S5.341 S5.351 S5.354 S5.355 S5.359 S5.376 |
| 1656.5–1660 | MOBILE-SATELLITE (Earth-to-space) S5.341 S5.351 S5.354 S5.355 S5.359 S5.374 S5.362A |
| 1660–1660.5 | MOBILE-SATELLITE (Earth-to-space) RADIO ASTRONOMY S5.149 S5.341 S5.351 S5.354 S5.376A S5.362B |

Footnotes: S5.149In making assignments to stations of other services to which the bands: ..... 1660–1670 MHz..... are allocated, administration are urged to take all practicable steps to protect the radio astronomy from harmful interference. Emissions from spaceborne or airborne stations can be particularly serious sources of interference to the radio astronomy service (see Nos. S4.5 and S4.6 and Article S29). S5.341In the bands 1 400–1 727 MHz, 101–120 GHz and 197–220 GHz, passive research is being conducted by some countries in a programme for the search for intentional emissions of extra-terrestrial origin. S5.342Additional allocation: in Armenia, Azerbaijan, Belarus, Bulgaria, Uzebekistan, Kyrgystan, the Russian Federation, and Ukraine, the band 1429–1535 MHz is also allocated to the aeronautical mobile service on a primary basis exclusively for the purposes of aeronautical telemetry within the national territory. As of 1 April 2007, the use of the band 1452–1492 MHz is subject to agreement between the administrations concerned. S5.343In Region 2, the use of the band 1435–1535 MHz by the aeronautical mobile service for telemetry has priority over other uses by the mobile service.

S5.349Different category of service: in Saudi Arabia, Azerbaijan, Bahrain, Bosnia and Herzegovina, Cameroon, Egypt, the United Arab Emirates, France, the Islamic Republic of Iran, Iraq, Israel, Kazakhstan, Kuwait, The former Yugoslav Republic of Macedonia, Lebanon, Morocco, , Qatar, Syria, Kyrgyzstan, Romania, Turkmenistan, , Yemen and Yugoslavia, the allocation of the band 1525–1530 MHz to the mobile, except aeronautical mobile,service is on a primary basis (see No. S5.33). S5.350Additional allocation: in Azerbaijan, Kyrgyzstan, and Turkmenistan , the band 1525–1530 MHz is also allocated to the aeronautical mobile service on a primary basis. S5.351A For the use of the bands 1525-1544 MHz, 1545-1559 MHz, 1610-1626.5 MHz,1626.5-1645.5 MHz, 1646.5-1660.5 MHz, 1980-2010 MHz, 2170-2200 MHz, 2483.5-2500 MHz, 2500-2520 MHz, and 2670-2690 MHz by the mobile-satellite service, see Resolution 212 (Rev WRC-97) and 225 (WRC-2000). S5.351The bands 1525–1544 MHz, 1545–1559 MHz, 1626.5– 1645.5 MHz and 1646.5–1660.5 MHz shall not be used for feeder links of any service. In exceptional circumstances, however, an earth station at a specified fixed point in any of the mobile-satellite services may be authorized by an administration to communicate via space stations using these bands. S5.352AIn the band 1525–1530 MHz, stations in the mobile-satellite service, except stations in the maritime mobile-satellite service, shall not cause harmful interference to, or claim protection from, stations of the fixed service in France and French overseas territories in Region 3, Algeria, Saudi Arabia, Egypt, Guinea, India, Israel, Italy, Jordan, Kuwait, Mali, Malta, Morocco, Mauritania, Nigeria, Oman, Pakistan, Philippines, Qatar, Syria, Tanzania, Viet Nam and Yemen notified prior to 1 April 1998. S5.353AIn applying the procedures of Section II of Article S9 to the mobile-satellite service in the bands 1530–1544 MHz and 1626.5–1645.5 MHz, priority shall be given to accommodating the spectrum requirements for distress, urgency and safety communications of the Global Maritime Distress and Safety System (GMDSS). Maritime mobile-satellite distress, urgency and safety communi-cations shall have priority access and immediate availability over all other mobile satellite communications operating within a network. Mobile-satellite systems shall not cause unacceptable interference to, or claim protection from, distress, urgency and safety communications of the GMDSS. Account shall be taken of the priority of safety-related communications in the other mobile-satellite services. ( The provisions of Resolution 222(WRC-2000) shall apply.) S5.354The use of bands 1525–1559 MHz and 1626.5–1660.5 MHz by the mobile-satellite services is subject to coordination under Resolution 46 (Res. WRC-95)/No. S9.11A. S5.355Additional allocation: In Bahrain, Bangladesh, Congo, Egypt, , Eritrea, the Islamic Republic of Iran, Iraq, Israel, Jordan, Kuwait, Lebanon, Malta, Morocco, , Qatar, Syria, Somalia, Sudan, , Chad, Togo, and Yemen , the bands 1540–1559 MHz, 1610- 1645.5 MHz and 1646.5–1660 MHz are also allocated to the fixed service on a secondary basis.

S5.356The use of the band 1544-1545 MHz by the mobile-satellite service (space-to-Earth) is limited to distress and safety communications (see Article S31). S5.357Transmission in the band 1545-1555 MHz from terrestrial aeronautical stations directly to aircraft stations, or between aircraft stations, in the aeronautical mobile (R) service are also authorized when such transmissions are used to extend or supplement the satellite-to-aircraft links. S5.357AIn applying the procedures of Section II of Article S 9 to the mobile-satellite service in the bands 1545–1555 MHz and 1646.5–1656.5 MHz, priority shall be given to accommodating the spectrum requirements of the aeronautical mobile-satellite (R) service (AMS(R)S) providing transmission of messages with priority 1 to 6 in Article S44. AMS(R)S communications with priority 1 to 6 in Article S44 shall have priority access and immediate availability, by pre-emption if necessary, over all other mobile-satellite communications operating within a network. Mobile-satellite systems shall not cause unacceptable interference to, or claim protection from, AMS(R)S communications with priority 1 to 6 in Article S44. Account shall be taken of the priority of safety-related communications in the other mobile-satellite services. ( The provisions of Resolution 222 (WRC-2000)] shall apply. S5.359Additional allocations: in Germany, Saudi Arabia, Armenia, Austria, Azerbaijan, Belarus, Benin, Bosnia and Herzegovina, Bulgaria, Cameroon, Spain, France, Gabon, Georgia, Greece, Guinea, Guinea-Bissau, Hungary, Jordan, Kazakhstan, Kuwait, Latvia, Lebanon, Libya, Lithunia, Mali, Morocco Mauritania, Moldova, Mongolia, Nigeria, Uganda, Uzbekistan, Pakistan, Poland, Syria, Kyrgyzstan, the Democratic People's Republic of Korea, Romania, the Russian Federation, Senegal, Swaziland, Tajikistan, Tunisia, Tanzania, Turkmenistan, and Ukraine, the bands 1550– 1559 MHz, 1610-1645.5 MHz and 1646.5–1660 MHz are also allocated to the fixed service on a primary basis. Administrations are urged to make all practicable efforts to avoid the implementation of new fixed-service stations in these bands. S5.362AIn the United States, in the bands 1555–1559 MHz and 1656.5–1660.5 MHz, the aeronautical mobile-satellite (R) service (AMS(R)S) shall have priority access and immediate availability, by pre-emption if necessary, over all other mobile-satellite communications operating within a network. Mobile-satellite systems shall not cause unacceptable interference to, or claim protection from, AMS(R)S communications with priority 1 to 6 in Article S44. Account shall be taken of the priority of safety-related communications in the other mobile-satellite services. S5.374Mobile earth stations in the mobile-satellite service operating in the bands 1631.5–1634.5 MHz and 1656.5–1660 MHz shall not cause harmful interference to the stations in the fixed service operating in the countries listed in No. S5.359.

S5.375The use of the band 1645.5–1646.5 MHz by the mobile-satellite service (Earth-to-space) and for inter-satellite links is limited to distress and safety communications (see Article S31). S5.376Transmissions in the band 1646.5–1656.5 MHz from aircraft stations in the aeronautical mobile (R) service directly to terrestrial aeronautical stations, or between aircraft stations, are also authorized when such transmissions are used to extend or supplement the aircraft-to-satellite links. S5.376AMobile earth stations operating in the band 1660.0–1660.5 MHz shall not cause harmful interference to stations in the radio astronomy service.

ICAO POLICY Recover exclusive allocation of the bands 1 545-1 555 MHz and 1646.5-1646 MHz to AMS(R)S No change to S5.357A and Resolution 222 (WRC-2000) Participate and support the studies under Resolution 222 on the feasibility and practicality of priotirazation and real-time preemptive access between different networks. Retain S5.357, S5.357A, S5.375, S5.376 and S5.362A Monitor and review experimental and trial applications of generic-type operations with the objective of assessing their suitability for aeronautical safety services Support action for the deletion of the use of the bands 1545-1559 MHz and 646.5-1656.5 MHz by the fixed service (S5.355 and S5.359 refer) Support studies in ITU-R Study Group 8 on the sharing between fixed services and AMS(R)S in the bands 1545-1555 MHz and 1646.5-1656.5 MHz (S5.355 and S5.359 refer) Support the studies in ITU-R SG8 on the provision of distress and safety satellite services in the 1.5/1.6 MHz mobile satellite bands

AVIATION USE: These frequencies are used for air-ground communications and, in the FANS scenarios, are expected to replace HF voice over oceanic/remote areas. In continental airspace, satellite communications, may be used as a supplement to VHF. The system supports voice and data for ATC or ADS purposes. SARPs were adopted by ICAO in 1995.

Also included in the allocation table shown above are the mobile-satellite bands 1544–1545 MHz and 1645.5–1646.5 MHz which are to be used for any mobile service for distress and safety communications only.

AMS(R)S services will be provided by commercial service providers for both the space segment and the ground segment.   The connection to ATC centres.would normally be made by landline from the ground earth station.

COMMENTARY: The use of satellites for communications (and navigation) was recommended as official ICAO policy by the Tenth Air Navigation Conference (Montreal, 5 to 20 September 1991), as part of the future CNS/ATM systems recommended by FANS. The Tenth Air Navigation Conference discussions comprehensively covered all aspects of the subject. The ICAO Council endorsed the FANS recommendations at the twentieth meeting of its 134th Session on 29/31 October 1991. The prime use would be in oceanic and continental low density airspace. The system supports voice and data, the latter being a support element for ADS.

At the above-mentioned conference, the role of ICAO in satellite communications with aircraft was explored [Report of the Tenth Air Navigation Conference (1991) (Doc 9583), Agenda Item 8 refers], and was seen to be basically that of a facilitator and coordinator. The complexities of the institutional and legal arrangements and interfaces between the concerned parties, such as air traffic service provider, space system provider and ground system provider, were addressed in Agenda Item 4 of the same conference. Appendix A to Agenda Item 4 sets out guidelines and recommen-dations for study on these aspects.

Frequency requirements for AMS(R)S have been discussed in ICAO at a number of worldwide meetings such as divisional-type meetings, FMSG, FANS and AMCP. A definitive analysis was discussed under Agenda Item 1, paragraph 1.2.4 of the COM/MET/OPS/90 Meeting and Appendices A, B and C. Paragraph 6.1.4 and Table 13 of Appendix B indicate the best estimates for AMS(R)S up to the year 2010.

The COM/MET/OPS/90 also addressed the question of sharing and concluded that fixed spectrum partitioning was acceptable, but other forms required further study. The discussion appears in paragraphs 1.2.4 and 6.2 of Appendix B to the Report on Item 1.

Sharing and associated aspects such as generic allocations to mobile satellite services were discussed at the Special Communications/Operations Divisional Meeting (1995) (SP COM/OPS/95), and no service merging was acceptable pending further investigation to ensure that safety and regularity of flight would not be compromised (see Section 7-III, paragraph 7-III.3.1.2 — Service merging — of this handbook). Exclusive frequencies for AMS(R)S communications remain a firm ICAO policy as the ideal assurance that frequencies will be guaranteed. Other arrangements, such as multi-national agreements, which provide for the exclusive nature of AMS(R)S, are however not excluded.

Generic Allocations  /Access to Frequencies

Until 1997 the ITU allocation to the AMS(R)S were exclusive and world  wide in accordance with the definition at S1. 36, and the rules at Chapter SVIII for Aeronautical Mobile Services.  The exclusive condition ensured that ICAO SARPS could be applied and the system operators would provide a service with the required integrity and reliability.  Frequencies for mobile satellite use were under intensive demand for other mobile applications, which led to  a focusing of attention on the relatively unused AMS(R)S allocation.

The ITU WRC-97 discussed, at great length, the introduction of a generic allocation to the mobile satellite service which replaced the exclusive allocations to the aeronautical, land and maritime mobile satellite services, noting the dissenting views of the international civil aviation (see Section 7-III, paragraph 7-III.3.1.3 of this handbook) and maritime communities.  Frequencies in a generic allocation may be used for providing service to any class of mobile user, land sea or air, and may carry any type of communication  -   safety, public correspondence , voice or data.   Against the  stated policies of ICAO and IMO, the introduction of generic allocations was approved, together with a new footnote S5.357A intending to provide a guarantee  of future frequency access for aeronautical safety services. With  this new generic allocation to the mobile satellite service, aircraft have to share the  10 MHz in the bands 1545–1555 MHz and 1646.5–1656.5 MHz with non-aeronautical systems and services.

Footnote S5.357A - inserted at WRC-97 - is the mechanism intended by radio regulatory authorities to compensate for the loss of the exclusive 10 MHz of spectrum to the AMS(R)S and to assure access in the future. It  relied on cooperation between administrations and satellite system operators and by itself  had no apparent regulatory force. , In a situation where there are no spare frequencies for aeronautical use in the bands quoted in the footnote, with some used for other (non-aeronautical) mobile satellite systems, expansion of aeronautical use is only possible by a release of frequencies from a non-aeronautical user. In effect there was no guarantee that such release could be effected. Two important features of the footnote are that it addresses only the 10 MHz of spectrum allocated to the AMS(R)S prior to WARC-92  (as quoted in the footnote) )and that the priorities  o are Categories 1 to 6 of Article S44 of the Radio Regulations  These are identical to  Annex 10, Volume II, Chapter 5, 5.1.8 (see 7-III.3.8 of this handbook). This excludes Public Correspondence,  a category r which covers passenger and airline administrative communications.

The aviation concern on this point led - at WRC-2000 - to Resolution 222 (WRC-2000). Resolves 3 of the resolution states that Administrations shall ensure that MSS operators yield capacity to accommodate AMS(R)S requirements, either through the coordination process described below or through prioritization and real-time pre-emptive access, where feasible. if necessary by  yielding capacity by MSS operators, or alternately by the incorporation, where feasible, of prioritization and pre-emption. To give this Resolution a positive regulatory force a linked reference has been placed in footnote S5.357A, which under present ITU rules gives it the same status as a Radio Regulation.  This regulatory formula, whilst not fully meeting the ICAO policy calling for a recovery of the exclusive allocation to the AMS(R)S, is still a considerable improvement on the original.

The current practice of the application of S5.375A is that all satellite service providers planning to operate in the bands 1525-1559 MHz and 1626.6-1660.5 MHz register the use of the whole band with the ITU. With this registration, the obligations of the Radio Regulations to internationally coordinate the frequency assignments are satisfied. However, the actual allotment of portions of this spectrum to satellite systems operators is taking place under the auspices of a Memorandum of Understanding between the concerned satellite operators and relevant Administrations. On a yearly basis, using actual and predicted traffic characteristics, satellite operators are provided with spectrum, satisfying their needs obvious as long as these can be accommodated in the available spectrum. The results of these yearly consultations are not available in the public domain. ICAO is not invited to become a party in these discussions nor informed about the results. The frequency coordination and assignment process has been factually taken outside the traditional ITU frequency planning and coordination process. The secrecy around the results of the activities under the Memorandum of Understanding does not give ICAO or the aviation community the possibility to assess if the aeronautical spectrum requirements will be met, in particular in the longer term. Furthermore, the process under the memorandum of understanding does not provide for measures if not longer supported by Administrations or satellite system operators. This creates serious concern about the practical ability make to available for aeronautical communications, when required, frequency spectrum which under the memorandum of understanding has already been allotted to a particular satellite system operator,

Spectrum Requirements for Satellite Communications

The amount of spectrum required for civil aviation has been a subject of study since the first allocation of 15 MHz in both directions for safety communications only was made.   Later, with the realization that safety communications alone could not justify a satellite system with dedicated frequencies, and to meet airline needs, the scope was increased to include public correspondence.   Later Conferences reduced this allocation, finally concluding on the present 10 MHz quoted in footnote S5.357A.   The generic allocation permits public correspondence, subject to the priority terms for Categories 1 to 6 of Article S.44 as quoted in the footnote.

The most recent estimates (for air traffic control requirements only). and approved as ICAO policy, are :

10.8 Mhz up to 2010 and 18 MHz beyond 2010.

The present ICAO policy statement recognizes that the anticipated growth pattern  may be slower than predicted, and as a consequence accepts a lower capacity requirement with guarantees on priority access and absence of harmful interference.  This is in line with present ITU policy, which no longer accepts unused spectrum, or ineffective spectrum use.

Studies on AMS(R)S using Generic Allocations

The introduction of the new generic type allocations in 1997 has not recognized the serious reservations which are still held by international civil aviation on the compatibility of the requirements of AMS(R)S with other non-aeronautical mobile satellite services and, in particular, with the necessary compliance with ICAO SARPs and with the other requirements for integrity and reliability of communications. At the time of WRC-97, no confirmed and agreed studies or results from operational trials had been reviewed in an international forum which could provide the assurances of  satisfactory operations of AMSS and of meeting the stringent performance requirements defined by ICAO in the SARPs.A full discussion of the various aspects of using the generic allocation is at Attachment D to Agenda Item 1 of the Report of the AMCP/6 Meeting held in March 1999.

Specific  doubts remain on many points, including the important point of the practicability of operating a priority system between independent and possibly competing networks, and the very important aspect of the long-term guarantee that sufficient frequencies would remain available for aviation safety communications (these and other important points had been addressed in the ICAO submission to WRC-97). Completion of these studies and discussion of the results within ICAO must, therefore, be considered as a necessary prerequisite of international approval for generic type allocations and systems.

Studies under ITU Resolution No. 218 (WRC-97) (suppressed at WRC-2000), have been ongoing in ITU-R WP8D and will continue until at least WRC-2003 under Resolution 222 (WRC-2000).  Results of studies to date has indicated that pre-emption is technically feasible within a single network. One system (Inmarsat) already employs a pre-emption technique on the AES terminals on the frequencies employed for AMS(R)S.  It separates aeronautical safety communications from aeronautical public correspondence since the system was designed for exclusive AMS(R)S services. Extension to all terminals within a network also appears feasible, on condition that all terminals be fitted with the control facilities needed to exercise the pre-emption from the ground control point. It may be noted that the economics of meeting these requirements may act as a deterrent to the operation of a mixed service network. WP8D has also identified all of the features of the terminals and the network which are necessary for this pre-emption and interoperability capability (see CPM-2000 Report). No material has yet been presented which  to demonstrated practical possibility of pre-emption between different networks.

ICAO is also considering the feasibility of introducing more frequency efficient methods  without affecting the performance requirements for AMS(R)S. Early results of this work are reported at Agenda Item 2 of the AMCP/6.  In addition this work addresses the possibility of the use of non-geostationary satellites (NGSO. implemented in other frequency bands (see, for example, the band 1 610 - 1 626.5 MHz). However, these are expected not to become available in the near future

It may be noted that the Annex 10 SARPs differentiate the frequencies between 1544 and 1645.5 MHz in the following manner:

Standard: Annex 10, Volume III, Part I, Chapter 4, 4.2.1.2.1 and 4.2.1.3.1, 1544–1555 MHz and 1645.5–1656.5 MHz, respectively.

Recommended Practice: Annex 10, Volume III, Part I, Chapter 4, 4.2.1.2.2 and 4.2.1.3.2, 1555–1559 MHz and 1656.5–1660.5 MHz, respectively.

Recommended Practice: Annex 10, Volume III, Part I, Chapter 4, 4.2.1.2.3 and 4.2.1.3.3, 1525–1544 MHz and 1626.5–1645.5 MHz, respectively.

The order of priority of communications in aeronautical mobile and aero-nautical mobile-satellite services,  laid down in  Article S.44, are reproduced  in Section 7-III.3.8.2 of this handbook.

ITU-R Recommendations

Mobile satellite communications receive considerable attention from the ITU-R, which has formulated a number of recommendations (see Technical Information below). Some have been initiated by aeronautical services through the work and Recommendations of the AMSSP and AMCP.

Further studies on a possible merging of services in this band shall take into account the aspects on merging raised in paragraph 6.3 of Appendix B to Agenda Item 7 of the Report of the SP COM/OPS/95 Divisional Meeting (see Section 7-III.3.1.2, of this handbook).

TECHNICAL AND OTHER INFORMATION

Band: 1544–1545 MHz and 1645.5–1646.5 MHz

Service: Mobile satellite

Aviation use: Distress and safety communications (satellite EPIRBs)

Annex 10

SARPs: None

Frequency plan: None

Planning criteria: None

RTCA MOPS:

Eurocae MPS:

ARINC characteristic:

ITU Res/Rec: Radio Regulations: Article N38/Appendix S15

ITU-R:

CCIR:

Other material:

Band: 1545–1555 MHz and 1646.5–1656.5 MHz

Service: AMS(R)S

Aviation use: Satellite communications

Annex 10

SARPs: Annex 10, Volume III, Part I, Chapter 4

Frequency plan: Prepared by space segment provider

Channelization:

Planning criteria:

RTCA MOPS: DO-210 MOPS for aeronautical mobile-satellite service (1996)

Eurocae MPS:

ARINC characteristic: 741 P1 (aircraft installation) 741 P2 (satellite design) 741 P4 (specification and description language)

ITU Res/Rec

	Res. No. 44 (Mob-87): Compatibility of equipment used in the mobile-satellite service

	Res. No. 208 (Mob-87): Suppressed.

	Res. No. 218 (WRC-97): Suppresses

	Rec. No. 405:

Res. No. 222 (WRC-2000) relating to the use of the bands 1525 - 1559 MHz and 1626.5 - 1660.5 MHz by the mobile satellite service

ITU-R:

	ITU-RM.8281: Definition of availability for communication circuits in the mobile satellite service

	ITU-RM1037: Bit error performance objectives for the AMS(R)S radio links

	ITUR.M1089: Technical considerations for the coordination of mobile-satellite systems supporting the AMS(R)S

Other material: AMCP/5 Report

This page deliberately left blank.

Band: 1559–1626.5 MHz

Service: Aeronautical radionavigation/radionavigation

satellite/mobile-satellite (GNSS)

Allocation:

MHz 1559–1626.5

| Allocation to Services |
| --- |
| Region 1 | Region 2 | Region 3 |
| 1559–1610 | AERONAUTICAL RADIONAVIGATION RADIONAVIGATION-SATELLITE (space-to-Earth)(space-space) S5.329A S5.341 S5.362B S5.362C S5.363 |
| 1610–1610.6 | 1610–1610.6 | 1610–1610.6 |
| MOBILE-SATELLITE (Earth-to-space) S5.351A | MOBILE-SATELLITE (Earth-to-space) S5.351A | MOBILE-SATELLITE (Earth-to-space) S5.351A |
| AERONAUTICAL RADIONAVIGATION | AERONAUTICAL RADIONAVIGATION | AERONAUTICAL RADIONAVIGATION |
|  | RADIODETERMINATION-SATELLITE (Earth-to-space) | Radiodetermination-satellite (Earth-to-space) |
| S5.341 S5.355 S5.359 S5.363 S5.364 S5.366 S5.367 S5.368 S5.369 S5.371 S5.372 | S5.341 S5.364 S5.366 S5.367 S5.368 S5.370 S5.372 | S5.341 S5.355 S5.359 S5.364 S5.366 S5.367 S5.368 S5.369 S5.372 |
| 1610.6–1613.8 | 1610.6–1613.8 | 1610.6–1613.8 |
| MOBILE-SATELLITE (Earth-to-space) S5.351A | MOBILE-SATELLITE (Earth-to-space) S5.351A | MOBILE-SATELLITE (Earth-to-space) S5.351A |
| RADIO ASTRONOMY | RADIO ASTRONOMY | AERONAUTICAL RADIONAVIGATION |
| AERONAUTICAL RADIONAVIGATION | AERONAUTICAL RADIONAVIGATION | Radiodetermination-satellite (Earth-to-space) |
|  | RADIODETERMINATION- SATELLITE (Earth-to-space) |  |
| S5.149 S5.341 S5.355 S5.359 S5.363 S5.364 S5.366 S5.367 S5.368 S5.369 S5.371 S5.372 | S5.149 S5.341 S5.364 S5.366 S5.367 S5.368 S5.370 S5.372 | S5.149 S5.341 S5.355 S5.359 S5.364 S5.366 S5.367 S5.368 S5.369 S5.372 |
| 1613.8–1626.5 | 1613.8–1626.5 | 1613.8–1626.5 |
| MOBILE-SATELLITE (Earth-to-space) S5.351A | MOBILE-SATELLITE (Earth-to-space) S5.351A | MOBILE-SATELLITE (Earth-to-space) S5.351A |
| AERONAUTICAL RADIONAVIGATION | AERONAUTICAL RADIONAVIGATION | AERONAUTICAL RADIONAVIGATION |
| Mobile-satellite (space-to-Earth) | RADIODETERMINATION- SATELLITE (Earth-to-space) Mobile-satellite (space-to-Earth) | Radiodetermination-satellite (Earth-to-space) Mobile-satellite (space-to-Earth) |
| S5.341 S5.355 S5.359 S5.363 S5.364 S5.365 S5.366 S5.367 S5.368 S5.369 S5.371 S5.372 | S5.341 S5.364 S5.365 S5.366 S5.367 S5.368 S5.370 S5.372 | S5.341 S5.355 S5.359 S5.364 S5.365 S5.366 S5.367 S5.368 S5.369 S5.372 |

Footnotes: S5.351A For the use of the bands 1525-1544 MHz, 1545-1559 MHz, 1610-1626.5 MHz,1626.5-1645.5 MHz, 1646.5-1660.5 MHz, 1980-2010 MHz, 2170-2200 MHz, 2483.5-2500 MHz, 2500-2520 MHz, and 2670-2690 MHz by the mobile-satellite service, see Resolution 212 (Rev WRC-97) and 225 (WRC-2000)] S5.149In making assignments to stations of other services to which the bands: ..... 1610.6–1613.8 MHz * ..... are allocated (*indicates radio astronomy use for spectral line observations), administrations are urged to take all practicable steps to protect the radio astronomy service from harmful interference. Emissions from spaceborne or airborne stations can be particularly serious sources of interference to the radio astronomy service (see Nos. S4.5 and S4.6 and Article S29). S5.329A Use of systems in the radionavigation satellite service (space-space) operating in the bands 1215-1300 MHz and 1559-1610 MHz is not intended to provide safety service applicatiuons, and shall not impose any additional constraints on other systems or services operating in accordance with the Table of Frequency allocations. S5.341In the bands 1400–1727 MHz, 101–120 GHz and 197–220 GHz, passive research is being conducted by some countries in a programme for the search for intentional emissions of extraterrestrial origin. S5.355Additional allocation: Bahrain, Bangladesh, Congo, Egypt, Eritrea, , Iraq, Israel, Jordan, Kuwait, Lebanon, Malta, Morocco, Qatar, Syria, Somalia, Sudan, , Chad, Togo and Yemen , the bands 1540–1645.5 MHz and 1646.5–1660 MHz are also allocated to the fixed service on a secondary basis.

S5.362CAdditional allocation: In Bahrain, Bangladesh, Congo, Egypt, , Eritrea, the Islamic Republic of Iran, Iraq, Israel, Jordan, Kuwait, Lebanon, Malta, Morocco, , Syria, Somalia, Sudan, Togo, and Yemen , the band 1559-1610 MHz is also allocated to the fixed service on a secondary basis until 1 January 2015, at which time the allocation shall no longer be valid. Administrations are urged to take all practicable steps to protect the radionavigation-satellite service and not authorize new frequency assignments in this band S5.359Additional allocations: in Germany, Saudi Arabia, Armenia, Austria, Azerbaijan, Belarus, Benin, Bosnia, Bulgaria, Cameroon, Spain, France, Gabon, Georgia, Greece, Guinea, Guinea-Bissau, Hungary, Jordan, Kazakhstan, Kuwait, Latvia, Lebanon, Libya, Lithunia, Mali,Morocco Mauritania, Moldova, Mongolia, Nigeria, Uganda, Uzbekistan, Pakistan, Poland, Syria, Kyrgyzstan, the Democratic People's Republic of Korea, Romania, the Russian,Federation, Senegal, Swaziland, Tajikistan, Tunisia, Tanzania, Turkmenistan, and Ukraine, the bands 1550– 1559 MHz, 1610-1645.5 MHz and 1646.5–1660 MHz are also allocated to the fixed service on a primary basis. Administrations are urged to make all practicable efforts to avoid the implementation of new fixed-service stations in these bands. S5.362CAdditional allocations: The band 1559-1610 MHz is also allocated to the fixed service on a primary basis until 1January 2005 in Germany, Armenia, Azerbaijan, Belarus, Benin, Bosnia, Bulgaria, Spain, France, Gabon, Georgia, Greece, Guinea, Guinea-Bissau, Hungary, Kazakhstan, Latvia, Lithuania, Moldova, Mongolia, Nigeria, Uganda, Uzbekistan, Pakistan, Poland, Kyrgyzstan, the Democratic People's Republic of Korea, Romania, the Russian Federation, Senegal, Swaziland, Tajikistan, Tanzania, Turkmenistan, and Ukraine, and until 1 January 2010 in Saudi Arabia, Cameroon, Jordan, Kuwait, Lebanon, Libya, Mali, Morocco,Mauritania, Syria,and Tunisia. After these dates the fixed service may continue tooperate on a secondary basis until 1 January 2015, at which time this allopcation shall no longer be valid. Administrations are urged to take all practicable steps to protect the radionavigation-satellite service and the radionavigation service and not authorize new frequency assignments to fixed service systems in this band. S5.363Alternative allocation: In Sweden, the band 1590–1626.5 MHz is allocated to the aeronautical radionavigation service on a primary basis. S5.364The use of the band 1610–1626.5 MHz by the mobile-satellite service (Earth-to-space) and by the radiodetermination-satellite service (Earth-to-space) is subject to coordination under Resolution 46 (Rev. WRC-95)/No. S9.11A). A mobile earth station operating in either of the services in this band shall not produce a peak e.i.r.p. density in excess of -15 dB (W/4 kHz ) in the part of the band used by systems operating in accordance with the provisions of No. S5.366 (to which No. S4.10 applies), unless otherwise agreed by the affected administrations. In the part of the band where such systems are not operating, the mean e.i.r.p. density of a mobile earth station shall not exceed -3 dB (W/4 kHz). Stations of the mobile-satellite service shall not claim protection from stations in the aeronautical radionavigation service, stations operating in accordance with the provisions of No. S5.366 and stations in the fixed service operating in accordance with the provisions of No. S5.359. Administrations responsible for the coordination of mobile-satellite networks shall make all practicable efforts to ensure protection of stations operating in accordance with the provisions of No. S5.366. S5.365The use of the band 1613.8–1626.5 MHz by the mobile-satellite service (space-to-Earth) is subject to coordination under Resolution 46 (Rev. WRC-95)/No. S9.11A). S5.366The band 1610–1626.5 MHz is reserved on a worldwide basis for the use and development of airborne electronic aids to air navigation and any directly associated ground-based or satellite-borne facilities. Such satellite use is a subject to agreement obtained under No. S9.21. S5.367Additional allocation: the bands 1610–1626.5 MHz, 5000– 5150 MHz are also allocated to the aeronautical mobile-satellite (R) service on a primary basis, subject to agreement obtained under No. S9.21. S5.368With respect to the radiodetermination-satellite and mobile-satellite services the provisions of No. S4.10 do not apply in the band 1610– 1626.5 MHz, with the exception of the aeronautical radionavigation-satellite service. S5.369Different category of service: in Angola, Australia, Burundi, China, Côte d'Ivoire, Eritrea, Ethiopia, India, the Islamic Republic of Iran, Israel, Jordan, Lebanon, Liberia, Libya, Madagascar, Mali, Pakistan, Papua New Guinea, Syria, Senegal, Sudan, Swaziland, Togo,Zaire and Zambia, the allocation of the band 1610–1626.5 MHz to the radiodetermination-satellite service (Earth-to-space) is on a primary basis (see No. S5.33) subject to agreement obtained under No. S9.21 from countries not listed in this provision.

S5.370Different category of service: in Venezuela, the allocation to the radiodetermination-satellite service in the band 1610–1626.5 MHz (Earth-to-space) is on a secondary basis. S5.371Additional allocation: in Region 1, the bands 1610–1626.5 MHz (Earth-to-space) and 2483.5–2500 MHz (space-to-Earth) are also allocated to the radiodetermination-satellite service on a secondary basis, subject to agreement obtained under No. S9.21. S5.372Harmful interference shall not be caused to stations of the radio astronomy service using the band 1610.6–1613.8 MHz by stations of the radiodetermination-satellite and mobile-satellite services. (No. S29.13 applies.)

ICAO  POLICY

- .

- No change to the allocation to the radionavigation satellite service in the band 1559-1610 MHz.

- No new allocations to be made in the band 1559-1610 MHz.

- No change to S5.364, S5.365, S5.366, S5.367 and S5.368.



- Delete S5.362B and S5.362C on the grounds that the allocation to the fixed services is not compatible with the safe operation of ICAO GNSS services

- Delete  S5.363..

.

- Support the establishment of maximum permitted levels of spurious emissions in the band 1559– 1610 MHz  to ensure protection of ICAO GNSS on a global basis.

- Support studies in ITU-R which provide a sound technical basis for the operation and protection of ICAO GNSS

AVIATION USE: The bands at 1559 to 1626.5 MHz have been  allocated to  aeronautical Radionavigation and radionaivgation-satellite for many years.    Over recent  years,  a number of additions have been made to it, including that for the radionavigation satellite and radiodetermination satellite, and more recently (WRC-92), the mobile-satellite service (Earth-to-space) in the bands above 1610 MHz. The prime civil aviation interest is now in    the band 1559-1610 MHz  which will support the main frequency components of both GPS and Glonass.   A component of the European proposed system (Galileo) is expected to also operate in this band. :  Specific details of the use of the band are given below

1559–1610 MHz: The radionavigation satellite (space-to-Earth) allocation of 51 MHz is the  main allocation available for GNSS. Other bands identified to support this main component and to provide a more robust system with the possibility of compensation for ionospheric delay  are at 1164-1215 MHz (GPS and Galileo)  and 5000-5030 MHz (Galileo). In accord with the CNS/ATM concept, GNSS is foreseen to provide the basis for most civil aviation radionavigation requirements in the future. Present use of the band  includes the standard positioning service of the GPS system (GPS-SPS) as well as GLONASS.  Later, with the planning and implementation of Galileo this further system will be added to the band on frequencies which do not conflict with the other users.

1610–1626.5 MHz: The GLONASS radionavigation satellite system currently uses the lower part of this band. Future planning envisages a transfer to frequencies in the 1 559–1 610 MHz band (the sharing of the current band by GLONASS with the MSS service, and the radio astronomy service, creates problems which ultimately limit the aviation use). It is currently planned that GLONASS, after 2005, will operate below 1 610 MHz (1 598–1 605 MHz) (see Figure 7-2). GLONASS, in the standard mode, as part of the ICAO GNSS, will operate below 1605 MHz.

Figure 7-2.  Phased frequency shift of GLONASS carrier frequencies

COMMENTARY:

Band 1610–1626.5 MHz

The primary allocation to the aeronautical radionavigation service in the band 1 610–  1 626.5 MHz was the first aeronautical allocation to have a mobile satellite service allocation added in a sharing arrangement. The MSS service is primary in the Earth-to-space direction in all three ITU Regions and secondary in the space-to-Earth direction in Region 2. Under Footnote S5.364, the peak e.i.r.p. is limited to -15dB (W/4kHz) unless otherwise agreed between concerned administrations and in certain parts of the band to -3dB(W\4kHz). There have been no sharing studies carried out for these services in this band and, effectively, the MSS has now assumed control of the frequencies.

NGSO MSS is intended to provide a world wide service of voice and data for commercial purposes to all classes of mobile user, including personal handset users. The Earth-to-space direction for a mobile satellite service is the path between the mobile transmitting terminals, many of which will be hand-held devices, and the satellite. The potential for interference to aeronautical  GPS and GLONASS receivers by hand-held devices operating in the Earth-to-space direction  is hence high, particularly for mobile terminals operating on the lower frequencies in the band and especially in the vicinity of airports. This has led to the necessary development of ITU-R Recommendations limiting the level of unwanted emissions from these terminals into the GNSS band (see Commentary for that band below). Studies of this continue in ITU-R.

Footnote S5.367 allows AMS(R)S services to operate in the band subject to RR No. S9.21, which requires coordination with other administrations before a registration in the MIFR can be made. The AMS(R)S is an additional service by footnote provision and attracts primary status in both directions of transmission. Annex 10 SARPs do not apply for systems operating in this band.  It should be noted that  the  mobile satellite service (MSS) designation includes the aeronautical mobile satellite service (AMSS) and, therefore, permits the service to be used by aircraft, but the service providers would not have the obligation to  comply with Annex 10 require-ments. .

As in the GNSS band at 1559–1610 MHz, the fixed service is allowed to operate under the two Footnotes S5.355 and S5.359. This use conflicts with all of the satellite services in the band and is undesirable.

The use of the  the band 1610.6–1613.8 MHz for aeronautical purposes is also constrained by sharing with the radio astronomy allocation, which has primary status. Footnote S5.149 limits airborne use of this portion of the band.  In practical terms the band is of limited use for aviation services, and this is partcularly the case for aviation systems and services of international standard status.

Part of the standard accuracy mode of the GLONASS radionavigation satellite system presently operates in the lower 5.5 MHz (1610–1615.5 MHz, excluding the frequencies 1610.6 to 1613.8 MHz) but is planned to be transferred below 1 610 MHz by the year 2005 in two steps:

a)	between 1998 and 2005 thirteen carrier frequencies will be used between the frequencies 1598.0625 MHz–1609.3125 MHz; and

Note.— Carrier frequency 1609.3125 MHz will be used in exceptional cases.

b)	after 2005 twelve carrier frequencies will be used between 1598.0625 MHz and 1605.3750 MHz.

Note.— Carrier frequency 1604.8125 MHz and 1605.3750 MHz will only be used for technical purposes and when the satellite is over Russian territory.

Footnote S5.366 reserving the band 1610–1626.5 MHz for aeronautical purposes needs to be maintained.

Note.— In the civil (narrow band) mode the bandwidth is 0.5 MHz ; in the wide-band mode, the bandwidth is 5 MHz.

The primary allocation to the radiodetermination service in Region 2, and in Region 1 under footnote S5.371 and, on a secondary basis in Region 3, was made to accommodate a position-fixing service for general use, which was originally proposed for use by aviation. This service is only implemented to a limited extent and has never been recognized internationally as an approved service for aviation purposes. Footnote S5.364 requires coordination of this service with the MSS under the terms of Resolution 46.

Band 1559–1610 MHz

This 51 MHz band is now firmly established as the main allocation base for those radionavigation satellite services (RNSS), which are available for general use. (There are other RNSS systems which operate only  for special purposes or for national defense purposes)   These systems, (GPS, GLONASS and later Galileo) share the band without overlap of frequencies.  Typically an RNSS service will require some 12- 15 MHz or so of spectrum depending on the system's chipping rate and the accuracy requirement.  Signal levels at the Earths surface tend to be low demanding an interference free environment.  To combat the effects of atmospheric delay, and to provide a system with increased resilience to interference, it is becoming common practice to also transmit a component in other frequency bands (see for example commentary for DME band at 960-1215 MHz).

WRC-2000 added a (Space to Space) service to the (Space-to-Earth) allocation on a "no constraint to existing services* basis (see S5.329A).   This use is for the many operators of space services of all kinds who utilize the GPS system as a source of accurate timing, or for position fixing.  This regularizes a practice which has existed for many years but gives the service no rights over the main class of GNSS user and other allocations.

Global Navigation Satellite System (GNSS)

GNSS has been identified by the FANS Committee as a replacement for many of the existing terrestrial systems and is a main component of the CNS/ATM concept.  The specification for the ICAO Global Navigation Satellite System (GNSS), have the characteristics and safety features for use in civil aviation presently recognizes the GPS and GLONASS systems. The required characteristics for GNSS are incorporated in SARPS.  This forms the basis for satellite navigation as envisaged in the CNS/ATM concept, and provide service for both en-route, and for airport approach and landing.  The operational and technical features of this use are  described and explained in the ICAO Document  Guidelines for the Introduction and Operational use of the Global Navigation Satellite System (Circular 267)

Proposals for second generation RNSS are appearing having time scales of implementation from 2009 onwards. Notably are the addition of a new GPS frequency in the DME band, and a European civil operated system (Galileo)  planning to use this band, and possibly also the 1164-1215 MHz, 1260-1300 MHz, and 5010-5030 MHz bands.  WRC-2000 has regularized these proposals with suitable allocations, together with Resolutions calling for study of protection requirements for existing services.  Study by ICAO GNSSP is necessary to determine the extent to which these new systems can qualify for incorporation in the formula for GNSS

Protection of GNSS signals from Harmful Interference

The protection of GNSS signals from harmful interference is of major concern to aviation.  GNSS signal levels at the aircraft receiver are of very low level (in the order of minus 160 dBW) and, despite receiver signal processing having high interference rejection properties, the system is vulnerable to other in-band signals, and to spurious signals from non aviation systems operating in adjacent bands.  Additionally the placement of the GNSS antenna on the aircraft and its signal interfaces with other on-board radio systems require extreme care and careful design to ensure a system, which delivers the required accuracy, on a continuous basis. The characteristics and protection of GNSS is addressed in a number of ITU-R Recommendations (see below) and specific studies have been made, of the compatibility of GNSS with other systems to determine whether sharing is safe.  In respect of the total radio environment in which GPS must operate, the aggregate sum of all interferences is of major importance.  For this reason aviation has pressed for the inclusion of a safety margin factor in all assessments for individual interfering systems.  ICAO policy supports a factor of 6 to 10 dB for this feature. General details of some of the interference scenarios already identified, are given below:

Sharing with Fixed Services

,

The band 1559–1610 MHz is also shared with the fixed service under S5.362B an S5.362C  in a large number (72) of countries. ICAO’s concerns on this use have been expressed at a number of ITU Conferences. . This use by the fixed service, which is confined to parts of Europe and the Middle East, is well established and of long standing. Studies presented to ITU-WP8D have indicated the need for a separation between the fixed service location and the GNSS reception point of line of sight. This effectively makes GNSS unusable over a major part of Europe and the Middle East.   Pressure from ICAO culminated at WRC-2000 in an acceptance by most administrations that these fixed services should be ceased.  Footnote S5.362B and S5.362C were agreed at this Conference to place a final date of 2015 for the removal of all of these services. In some countries they remain as a primary service until 2005, then become secondary until the final date .In a small number of countries the reversion to secondary date is 2010. Whilst this result is an achievement the approved ICAO policy is to continue to apply pressure for further improvement.  Both primary and secondary fixed services present a threat, so that cessation of operation is important.

Hand held Devices in Band 1610-1626.5 MHz and Mobile Terminals in band 1626.5-1660.5 MHz.

Problems with high levels of spurious emissions from hand-held mobile satellite devices operating in the band 1610–1626.5 MHz have appeared and are the subject of European Telecommunication Standards Institute (ETSI) European Standards and ITU-R Recommendations.  This work resulted in the approval of ITU-R Recommendation M.1343 and the adoption of Standards by ETSI, both of which recognize the ICAO requirements on the level of protection to be given to GNSS. Further work on the protection in the band 1 605–1 610 MHz  on a similar set of regulations for the spurious emissions from mobile earth stations operating in the band 1626.5–1660.5 MHz has ben completed and resulted in ITU-R Recommendation XXXXXX..

Proposal for an allocation to MSS in band 1559-1567 MHz

A proposal to WRC-97 to allocate the frequency band between 1559 MHz and 1567 MHz to the mobile satellite service in the space-to-Earth direction, - strongly opposed by aviation interests -   was eventually not adopted by that  Conference. The proposal was referred   through  Resolution 220 (WRC-97) to the ITU-R for further study. The results of this study indicated  that sharing is not feasible  and were included in the CPM Report to WRC-2000.   WRC-2000 has accepted this resul , and Resolutions 226 and 227 of that Conference,  which address the question of additional spectrum for mobile satellite services in the bands between 1 and 3 GHz,  specifically exclude the band 1559-1610 MHz in the search. .

Other interferences to GPS

Recent evidence has reported potential interference from other sources, such as the harmonics of  TV services operating in bands between 500 and 800 MHz. Study of these is ongoing within the GNSSP.   An RTCA Committee  (RTCA DO-235) has also made a detailed study of these potentially interfering sources.

TECHNICAL AND OTHER INFORMATION

Band: 1559–1626.5 MHz

Service: Radionavigation satellite/aeronautical radionavigation

Aviation use: GNSS

Annex 10

SARPs:  In course of finalizationt

Frequency plan: GPS; GLONASS

Channelization: None

Planning criteria: None

ICAO Guidance  :  Circular 267  :  Guidelines for the introduction and Operational use of GNSS

RTCA MOPS:

	DO-208; MOPS for airborne supplemental navigation equipment using GPS (1991)

	DO-228; MOPS for GNSS airborne antenna equipment (1995)

Eurocae MPS:

ARINC characteristic: 743 (GPS), 743A (GPS/GLONASS)

ITU Res/Rec: Resolution 220 (WRC-97): Studies to consider the feasibility of using a portion of the band 1 559–1 610 MHz by the Mobile Satellite Service (space-to-Earth)

ITU-R Rec:

	ITU-RM 823: Technical characteristics for differential transmissions for GNSS from maritime radio beacons in the frequency band 283.6–315 MHz in Region 1 and 285–325 MHz in Regions 2 and 3.

	ITU-RM 1088: Considerations for sharing with systems of other services operating in the bands allocated to the radionavigation satellite service.

CCIR:

Other material:

	GNSS Panel; Reports

	RTCA DO-235 Assessment of Radio Frequency Interference Relevant to GNSS (1997).

PROTECTION OF GNSS IN BAND 1559–1610 MHz

Band 1559–1610 MHz

The 51 MHz radio navigation satellite band at 1559–1610 MHz supports the operation of the GNSS which is expected to become the future all-purpose radio navigation system for aviation operations. GPS and GLONASS, presently in operation, have been identified as the initial components of the systems that will be used, possibly with ground augmentation. Both systems are also available for all purposes where a position fixing facility is required. This includes all mobile navigation needs for land, sea or air, survey, mineral exploitation, search and rescue, etc.

Very stringent integrity and reliability standards, and other performance characteristics , have been developed by the ICAO GNSS Panel (see  SARPs for GNSS and ICAO Circular 267 — Guidelines for the Introduction and Operational Use of GNSS). Chapter 4 of Circular 267 gives a GNSS system overview and describes the two current candidate systems, GPS and GLONASS. Chapter 5 deals with interference in a general manner. Both systems operate using multiple orbiting satellites (up to 24 in number) at around 20 000 km above the Earth’s surface. Each satellite transmits exact orbital parameters (ephemeris data) with its corresponding highly accurate (atomic source) timing signal. Ground receivers solve four simultaneous equations for at least three sets of position data using the receivers’ integral accurate time source to obtain a two-dimensional position. A minimum of four satellites is required to provide a three-dimensional position. The two systems use different methods of modulation and transmission, with GPS using pseudo-random coding transmitted on the same frequency and GLONASS  using frequency division on discrete frequency for individual satellites.

Brief spectrum details of the occupation of the 1559–1610 MHz frequency band, present and expected, are shown in Figure 7-2. The details of the two systems presently in operation are:

GPS:

the centre frequency is 1 575.42 MHz. The occupied bandwidth is dependent on the type of receiver, and its tracking process C/A code requires plus or minus [4 MHz] and P code plus or minus [12 MHz].

GLONASS:

in its final configuration (expected in 2005), GLONASS will operate on 12 frequencies spaced at 0.5625 MHz in the band between 1598.0625– 1605.3750. This implies that even in the precision accuracy signal, all GLONASS spectrum requirements will not be met below 1 610 MHz.

GNSS augmentation:

proposals have been made for augmentation systems to improve GNSS integrity, which may operate in the lower end of the 1559 - 1610 MHz band. Protection requirements are tentative but early indications are that they would be similar to the systems already in use.

Aircraft receiving system protection

The performance requirements for the aircraft receiving system in regard to the projection from interference are contained in:

RTCA DO-229: Min Operational Performance Standards for GPS/WAAS Airborne 	Equipment (Jan. 1996);

RTCA  DO-228: Min Operational Performance Standards for GPS/WAAS Airborne 	Antenna Equipment (Jan. 1996).

The document RTCA DO-235 Assessment of Radio Frequency Interference Relevant to GNSS (1997) addresses the specifics of the interference situation. These documents may be taken to be the definitive texts produced by aviation experts and should be used as basic material in all protection calculations.

The protection requirements for aircraft receivers, as contained in RTCA DO-229, Appendix C, are:

Wide-band signals:minus 115 dBm/MHz

Narrow-band signals:minus 120.5 dBm/MHz

Wide-band signals are 1 MHz and wider, and narrow-band are nominally less than 700 kHz.

Sharing and protection from other radio services

Fixed Links

No published characteristics are available for the fixed links operated under footnotes S5.362B and S5.362C by the countries  included in the footnotes . Information from other work in connection with these fixed links indicates typical systems with characteristics as follows:

Frequency:	Anywhere in band 1400–1660 MHz at bandwidth of 600 kHz

Output Power:	1.2 W

Antenna Gain:	up to 22dB

Front/Back:	16 dB

Side Lobe Att:	9 dB min

With these characteristics, unacceptable interference to GNSS services could exist at distances of 400 Kms and greater to an aircraft receiver in the main lobe of the fixed link transmitter. Ground station GNSS monitors used for augmentation may be affected within 80 km. The numbers, locations and operating frequencies of these equipments are only known to the licensing national administrations. National coordination with authorities in the countries concerned is necessary to establish the sharing possibilities on an individual site basis.

These links have the potential to inhibit GNSS operations over a wide area. The problem has been recognized internationally, and WRC-2000 is expected to discuss solutions. ICAO Policy (Section 1559–1626.5 MHz of this handbook) supports the removal of the GNSS band at 1559–1610 MHz from both footnotes.

Other ITU-R documentation:

- Recommendation ITU-R M.1088: Considerations for sharing with systems of services operating in the bands allocated to the radionavigation satellite service.

- Recommendation ITU-R M.1317: Considerations for sharing between systems of other services operating in bands allocated to the radionavigation satellite service and aeronautical radionavigation services and the global navigation satellite system GLONASS.

- Recommendation ITU-R M.1318: Interference protection evaluation model for the radionavigation satellite service in the 1 559 to 1 610 MHz band.

- Recommendation ITU-R M.1343 : Essential technical requirements of mobile earth stations for global non-geostationary mobile satellite service systems in the bands 1–3 GHz.

ICAO Studies

The ICAO GNSS Panel has prepared material on the protection of GNSS to be used as ICAO input documentation to ITU-R and other discussions on this subject. This material contains the protection requirements for all GNSS and support systems that are expected to be utilized for aviation purposes.

The protection requirements for GNSS systems as stated by the GNSS Panel are:

- Minus 137 dBW/m2/MHz (wide-band signals)

- Minus 148 dBW/m2/Hz (narrow-band signals)

Protection of GNSS from the spurious emissions of Mobile Earth Stations (MES)

Mobile satellite terminals in the bands from 1 to 3 GHz

The band 1 610–1 626.5 MHz is allocated for use by these mobile satellite  terminals for transmissions fin the Earth-to-space direction to satellites in non-geostationary orbits (NGSO). The mobile terminals may either be fixed to a vehicle or other mobile unit, or be hand-held. The systems presently proposed may be either of CDMA (wide-band) or of FDMA (narrow-band) type. These systems generate unwanted  emissions which can interfere with GNSS services in the band 1 559–1 610 MHz.

GSO mobile satellite systems operating in other bands between 1 and 3 GHz, and particularly the Earth-to-space band at 1 660–1 660.5 MHz, also have potential for interference. The latter band is that also used by AMS(R)S for transmissions from the aircraft (i.e. from an AES) to the satellite. For this situation, special measures have to be applied by aircraft systems designers to maintain the AMS(R)S signal level at the GNSS antenna below the agreed protection value.

Any of these mobile terminals may be used in the vicinity of airports, which creates the need for an international agreement to control the manufacture and use of, and the cross-border controls relating to, such terminals. The importance of this international aspect is caused by the global nature of these systems. The Global Mobile Personal Communications by Satellite (GMPCS) MOU, developed jointly by ITU and the World Telecommunications Policy Forum 1996, has been raised for signature by all participating countries as an agreement addressing the import and control of mobile satellite equipment.

NGSO MES terminals

Recommendation ITU-R M.1343: Essential technical requirements of mobile earth stations for global non-geostationary mobile satellite systems in the bands 1 to 3 GHz.

The purpose of this recommendation, approved in 1997, is to provide a common technical basis for the following purposes:

to establish type approval requirements for MES terminals;

to facilitate the licensing of MES terminal operations;

to facilitate the development of mutual recognition arrangements of type approvals of MES terminals;

to facilitate the development of mutual recognition arrangements to facilitate the circulation and the use of MES terminals

GSO MES terminals

Draft new ITU-R Recommendation: Essential technical requirements of land mobile earth stations for global GSO MSS systems providing voice and/or data communi-cations in the bands 1 to 3 GHz.

This recommendation has been developed from a European initiative which was approved by the ITU-R Radiocommunications Sector.

The data for the carrier on condition only have been extracted. For the carrier off condition and all other relevant data, reference should be made to the Recommendation. The subject is complex and the information presented here is for general guidance only.

The limits relate to the level of unwanted emissions at the output of the MES in the frequency bands quoted. The first column is for terminals with antenna gain less than 8 dBi and e.i.r.p. less than 15 dBW. The measurement bandwidth is 1 MHz unless indicated otherwise.

Frequency range	e.i.r.p. limit	e.i.r.p. limit

(MHz)		(dBW)			(dBW)

1 559–1 600	-70	-70

1 600–1 605	-70	-70

1 605–1 612.5	-70 to -58.5(1)	(2)

Notes:

(1) — Linear interpolation in dBW versus frequency.

(2) — Linearly interpreted from -70 dBW in 1 MHz at 1 605 MHz to -46dBW at 1 610 at 1 610 MHz. Special conditions are applicable to GLONASS protection (see Recommendation).

This page deliberately left blank.

Band: 2700–3300 MHz

Service: Aeronautical radionavigation/radionavigation/radio

location (surveillance radar)

Allocation:

MHz 2700–3300

| Allocation to Services |
| --- |
| Region 1 | Region 2 | Region 3 |
| 2700–2900 | AERONAUTICAL RADIONAVIGATION S5.337 Radiolocation S5.423 S5.424 |
| 2900–3100 | RADIONAVIGATION S5.426 Radiolocation S5.425 S5.427 |
| 3100–3300 | RADIOLOCATION S5.149 S5.333 S5.428 |  |

Footnotes: S5.149In making assignments to stations of other services to which the bands: ..... 3260–3267 MHz * ..... are allocated (*indicates radio astronomy use for spectral line observations), administrations are urged to take all practicable steps to protect the radio astronomy service from harmful interference. Emissions from spaceborne or airborne stations can be particularly serious sources of interference to the radio astronomy service (see Nos. S4.5 and S4.6 and Article S29). S5.333In the bands 1215–1300 MHz, 3100–3300 MHz, 5250–5350 MHz, 8550–8650 MHz, 9500–9800 MHz and 13.4–14 GHz, radiolocation stations installed on spacecraft may also be employed for the earth exploration-satellite and space research services on a secondary basis. S5.337The use of the bands 1300–1350 MHz, 2700–2900 MHz and 9000– 9200 MHz by the aeronautical radionavigation service is restricted to ground-based radars and to associated airborne transponders which transmit only on frequencies in these bands and only when actuated by radars operating in the same band. S5.423In the band 2700–2900 MHz, ground-based radars used for meteorological purposes are authorized to operate on a basis of equality with stations of the aeronautical radionavigation service.

S5.424Additional allocation: in Canada, the band 2850–2900 MHz is also allocated to the maritime radionavigation service, on a primary basis, for use by shore-based radars. S5.425 In the band 2 900-3 100 MHz, the use of the shipborne interrogator-transponder system (SIT) shall be confined to the sub-band 2 930 -2 950 MHz. S5.426The use of the band 2900–3100 MHz by the aeronautical radionavigation service is limited to ground-based radars. S5.427In the bands 2900–3100 MHz and 9300–9500 MHz, the response from radar transponders shall not be capable of being confused with the response from radar beacons (racons) and shall not cause interference to ship or aeronautical radars in the radionavigation service, having regard, however, to No. S4.9 of these Regulations. S5.428Additional allocation: in , Azerbaijan, Bulgaria, Cuba, , Kyrgyzstan, Mongolia Romania, and Turkmenistan , the band 3100– 3300 MHz is also allocated to the radionavigation service on a primary basis.

ICAO  POLICY

- No change to the frequency allocations to the aeronautical radionavigation service in these bands

- No change to S5.333, S5.423, S5.426, and S5.426.

- Oppose any allocation to the mobile services which would endanger the operation of important radar services.

- Insist that any sharing studies carried out encompass the total technical and operational aspects of radar use, including possible derogation of the safety case for the service.

- Oppose any proposal which places undue or unreasonable economic, penalty on radar systems presently in use.

- Support an upgrading of the radiolocation service to a primary status on a non-interference basis

AVIATION USE: These bands are extensively used for primary surveillance radar (10 cm) for medium-range, en-route surveillance, and for terminal area and approach monitoring. The bands are also used by other radionavigation services (particularly maritime) and radiolocation as well as radars for national purposes on a shared basis. Airborne use is prohibited under the Footnotes S5.337 and S5.426.  Civil aviation radars tend to be concentrated in the 2700-2900 MHz, although the use of 2900-3400 MHz is increasing.  The major users in the 2900-3400 MHz are radionavigation radars for maritime purposes, and radiolocation radars for national defense purposes.

Ten-cm radar technologies and practices date from the 1940s and   modern versions  employ the latest radar techniques for plot extraction and display on formatted synthetic displays.  Frequency diversity and pulse compression techniques are used to extract weak echoes from interference and to improve range resolution. Multiple frequency operation, commonly using two to four frequencies separated by 60-100 MHz, is necessary and requires careful frequency planning and separation of stations. More stable solid state transmitter frequency control is leading to a more effective use of spectrum than older magnetron systems, although the latter systems still have many years of useful life. .

COMMENTARY: Item 1 of the report of the Communications/Meteorology/Operations Divisional Meeting (1990) (Doc 9566) (see Attachment 4 to Appendix B to Item 1) reported considerable use of 2700–2900 MHz for surveillance purposes worldwide. Table 1 indicates over 1200 radars reported in response to an ICAO survey. Some use by meteorological radar is also reported.

The proposed ICAO position at paragraph 4 (page 1B-35) of the above-mentioned report is that no change is made to the allocation at 2700–2900 MHz, or adjacent bands. This position recognizes the considerable investment made in equipment, their suitability for the surveillance role and the long useful life. Replacement systems will be required to prove their operational benefit over a long period of time.

While it is possible that SSR, GNSS and ADS will take over some of the functions of en-route surveillance, it is premature to derive a timescale for a reduction in the numbers of radars or the use of these bands. The airport use is likely to remain for many years and well beyond 2010.

S-band marine (shipborne) radar are concentrated at 3050 ±30 MHz.

Proposals for other allocations in the band 2700–2900 MHz

To locate spectrum for the ITU IMT2000 — the new global terrestrial/satellite multi-purpose communications service — attention has been focussed by radio regulators and  mobile systems providers on these radar bands with a view to determining possible sharing with, or release of, spectrum allocated to the radar services systems. At the outset, sharing does not seem possible, since there appears to be a high probability of intolerable interference to both services. For example, strobing on radar displays and high-power pulse interference to mobile receivers are considered as highly probable, and unacceptable, risks.   A further problem is that the IMT-2000 spectrum requirement appears to be for overflow purposes in high demand urban areas, which is the same location requirement as that for airport radar.

The precise use of the bands 2700–2900 MHz has been initially reviewed by ITU-R WP8/B in 1999. Early research indicates that air traffic radars tend to be concentrated in the 2700–2900 MHz band, but this is not yet considered as a conclusive result. Any suggestion of compressing the bands into a smaller spectrum segment must be carefully examined to determine whether there is sufficient capacity and what are the economics of such refarming   .

Any decision on changes to the allocations in these bands, whether by reduction or by sharing, can only be taken after a full examination of present and future use. Present indications are that these radars will continue well beyond the year 2000 — 2025 has been mentioned — and may increase as airport congestion becomes an even greater problem than it is at the present time. Most use of 10 cm radars is at airports, and these are installed following a national decision to  provide an independent surveillance support to the air traffic services at the airport. Increase in airport movements and congestion on runways, now becoming common at many major airports necessitates the provision of the more effective monitoring of the airspace.   Primary radar has the benefit that it does not require the carriage of equipment in the aircraft and ensures comprehensive  monitoring of all aircraft in the airspace.

The situation post WRC-2000 is that even though the Conference made no reference to the use of this band for IMT-2000, intensive studies are continuing in Europe to establish the possibility of an allocation to non-aeronautical users in this band. These studies include co-frequency and off-frequency sharing, and the efficient use of the band by radars. All sharing with mobile users is viewed with extreme concern due to the difficulty of tracing sources of interference, as well as the roaming and largely uncontrolled character of mobile use. Transfer to the bands above 2900 MHz, also used for radar for mainly national defense purposes is also an option proposed by the IMT-2000 community. Transfer to these bands will lead to economic penalties which many aviation authorities can not accept, and make planning in the new band very difficult taking in to account its present use,

The firm ICAO policy is to insist on a full and comprehensive study programme, including not only the technical parameters for a compatible  and safe operation of radar, but also the operational implications of sharing frequencies with a use - such as that by mobile users - which is not amenable to effective control.

Studies in ITU-R

Intensive study is being carried out by ITU-R WP8B to document the characteristics and protection requirements of radars operating in these bands. There is difficulty in carrying out a comprehensive review of this kind because of the confidential nature of those systems used in national defense roles.  Further, present ITU-R work has concentrated on PPI type display radars, often of a type used in maritime operations, and less work has been carried out on the modern plot extracted type systems now in extensive use in civil aviation.

Early results indicate that co- frequency sharing is not practicable or feasible, requiring an impracticable large geographic separation between radar stations and other users.  Refinement and extrapolation to define the separation required at offset frequencies is expected to continue in the future. Agreements on propagation models, and on protection ratios, also require study and documentation.

The documented ITU-R work on this subject includes the following:

Rec.

Rec.

Rec.

TECHNICAL AND OTHER INFORMATION

Band: 2700 - 3300 MHz

Service: Aeronautical radionavigation/radionavigation

Aviation use: Primary surveillance radar, surveillance radar element (SRE)

of precision approach radar (PAR) medium-range systems,

ground-based weather radar.

Annex 10

SARPs: Annex 10, Volume I, paragraph 3.2.4

Frequency plan: None

Planning criteria: None

RTCA MOPS: None

Eurocae MPS: None

ARINC characteristic: None

ITU Res/Rec:

ITU-R Rec: ITU-R.M 629: Use for the RN service of the frequency bands

2900–3100 MHz, 5470–5650 MHz, 9200–9300 MHz, 9300–9500 MHz	and 9500–9800 MHz

CCIR:

Other material:

Band: 4200–4400 MHz

Service: Aeronautical radionavigation (radio altimeter)

Allocation:

MHz 4200–4400

| Allocation to Services |
| --- |
| Region 1 | Region 2 | Region 3 |
| 4200–4400 | AERONAUTICAL RADIONAVIGATION S5.438 S5.437 S5.439 S5.440 |

Footnotes: S5.437Additional allocation: in Germany and Norway, the band 4200– 4210 MHz is also allocated to the fixed service on a secondary basis. S5.438Use of the band 4200–4400 MHz by the aeronautical radio-navigation service is reserved exclusively for radio altimeters installed on board aircraft and for the associated transponders on the ground. However, passive sensing in the earth exploration-satellite and space research services may be authorized in this band on a secondary basis (no protection is provided by the radio altimeters). S5.439Additional allocation: in , the Islamic Republic of Iran and Libya, the band 4200–4400 MHz is also allocated to the fixed service on a secondary basis. S5.440The standard frequency and time signal-satellite service may be authorized to use the frequency 4202 MHz for space-to-Earth transmissions and the frequency 6427 MHz for Earth-to-space transmissions. Such transmissions shall be confined within the limits of ±2 MHz of these frequencies, subject to agreement obtained under No S9.21.

ICAO POLICY No change to the allocation to the radionavigation service in the light of the continuing requirement for radio altimeters to operate in this band and the results of ITU-R studies indicate that 200 MHz is required to meet the stringent operational requirements for integrity and accuracy for radio altimeters No change to S5.438 which could constrain the operation of radio altimeters. Delete S5.439

AVIATION USE: The band is used exclusively for airborne radio altimeters (see Footnote S5.438), which have a vital task in automated landing for flare guidance, and as the sensor component in ground proximity warning systems. Considerable studies have been made to identify the need for a 200 MHz wide-band for this system (see CCIR Report BL8, Dusseldorf 1990). These studies show that the full band is required to meet the accuracy and integrity requirements of radio altimeters. These radio altimeters are operational during all phases of flight.

COMMENTARY: It was recognized that accuracy requirements in 1990 might be achieved in less than 200 MHz. However, it now appears that future requirements may require more than the current 200 MHz.

Upgrading of Earth exploration satellite service ) (EES)

A proposal has been made to   upgrade the earth exploration satellite service (EES ) to the band. S5.438  permits this on a secondary basis. Protection of the radio altimeter use is a prime consideration which cannot be infringed, either by other transmissions, or by a restriction in the present scope for radio altimeter use. Any increase in the status of this service should only be accompanied by suitable provisions to continue the present capability and protection for radio altimeters.

TECHNICAL AND OTHER INFORMATION

Band: 4200 MHz–4400 MHz

Service: Aeronautical radionavigation

Aviation use: Radio altimeters

Annex 10

SARPs: None

Frequency plan: None

Planning criteria:  None

RTCA MOPS:

DO-155 (Airborne low range radar altimeters (1974))

DO-161A (Airborne ground proximity warning system (1976))

Eurocae MPS:

ARINC characteristic: 594 (GPWS), 707

ITU Res/Rec:

Rec. No. 606 (Mob-87): The possibility of reducing the band 4200– 4400 MHz used by radio altimeters in the aeronautical radionavigation

service

ITU-R Rec:

Report [BL/8] (Dusseldorf 1990)

Question 94/8: Bandwidth required for radio altimeter

ITU-R:

Other material:

PROTECTION ASPECTS OF RADIO ALTIMETERS

IN BAND 4 200 - 4 400 MHz

General

The frequency band at 4 200 to 4 400 MHz has been allocated to the aeronautical radionavigation service (ARNS) and is reserved exclusively for radio altimeters by footnote S5.438. The radio altimeter, in one of its main applications, performs the highly important task of providing flare guidance in the last stages of automated approach to land. Equally critical is its use as an input to Ground Proximity Warning Systems in aircraft.

For these applications, a good interference rejection performance is essential. Integrity standards of the order of one failure in 1019 operations are not uncommon. The use of a wide frequency band is an essential feature in effective designs to achieve high orders of interference rejection and freedom from disruptive effects due to the high levels of pollution of the radio environment which exists around most big cities.

Studies have determined the necessity for the retention of the existing 200 MHz of spectrum to meet the exacting requirements of high accuracy with good all-round performance.

ITU-R Studies

CCIR Report 1186 discusses the technical background to meeting the operational performance required for modern conditions. It concludes that:

“The whole of the band 4 200 to 4 400 MHz currently allocated is required up to at least the year 2015.”

In coming to this conclusion, Report 1186 reviews the accuracy requirements and the design features to meet those requirements as laid down in MOPS and MASPS. The relationship between frequency excursion and accuracy is particularly noted. Typical performance requirements are contained in ARINC Doc 707-1 Section 3.7 as follows:

- Accuracy: Within 1.5 ft., or 2 per cent if greater, in the range 20 to 2 500 ft.

- Output noise: 0.25 ft.

- Output Resolution: 0.125 ft.

Band: 5000–5250 MHz

Service: Aeronautical radionavigation (MLS)

Allocation:

MHz 5000–5250

| Allocation to Services |
| --- |
| Region 1 | Region 2 | Region 3 |
| 5 000–5 150 | AERONAUTICAL RADIONAVIGATION S5.367 S5.443A S5.443BS5.444 S5.444A |
| 5 150–5 250 | AERONAUTICAL RADIONAVIGATION FIXED-SATELLITE SERVICE S5.447A (Earth-to-space) S5.446 S5.447 S5.447B S5.447C |

Footnotes: S5.367Additional allocation: the bands 1610–1626.5 MHz, 5000– 5150 MHz are also allocated to the aeronautical mobile-satellite (R) service on a primary basis, subject to agreement obtained under No. S9.21. S5.444The band 5030–5150 MHz is to be used for the operation of the international standard system (microwave landing system) for precision approach and landing. The requirements of this system shall take precedence over other uses of this band. For the use of this band, No. S5.444A and Resolution 114 (WRC-95) apply. S5.444AAdditional allocation: The band 5091–5150 MHz is also allocated to the fixed-satellite service (Earth-to-space) on a primary basis. This allocation is limited to feeder links of non-geostationary mobile-satellite systems and is subject to coordination under Resolution 46 (Rev. WRC-95) No. S9.11A. In the band 5091–5150 MHz, the following conditions also apply: — prior to 1 January 2010, the use of the band 5091–5150 MHz by feeder links of non-geostationary-satellite systems in the mobile- satellite service shall be made in accordance with Resolution 114 (WRC-95);

— prior to 1 January 2010, the requirements of existing and planned international standard systems for the aeronautical radionavigation service which cannot be met in the 5000–5091 MHz band shall take precedence over other uses of this band; — after 1 January 2008, no new assignments shall be made to stations providing feeder links of non-geostationary mobile-satellite systems; — after 1 January 2010, the fixed-satellite service will become secondary to the aeronautical radionavigation service. S5.443A Additional Allocation : The band 5000-5010 MHz is also allocated to the radionavigation-satellite service (Eath-to-space) on a primary basis. See Resolution 603 (WRC-2000). S5.443B Additional Allocation : The band 5010-5030 is also allocated to the radionavigatio-satellite service (space-to- Earth)(space-to-space) on a primary basis. In order not to cause harmful interference to the microwave landing system operating above 5030 MHz, the aggregate power flux density produced at the Earths surface in the band 5030-5150 MHz by all the space stations within any radionavigation-satellite service system (space-to-Earth) operating in the band 5010-5030 MHz shall not exceed -124.5 dB (W/m2) in any 150 kHz band. In order not to cause harmful interference to the radio astronomy service in the band 4990-5000 MHz, the aggregate power flux density produced in the 4990-5000MHz band by all the space stations within any RNSS (space-to-Earth) system operating in the band 5010-5030 MHz band shall not exceed the provisional value of -171 dB(W/m2) in a 10 MHz band at any radio astronomy site for more than 2 % of the time. For the use of this band Resolution 604 (WRC-2000) applies. S5.446Additional allocation: in the countries listed in Nos. S5.369 and S5.400, the band 5150–5216 MHz is also allocated to the radiodetermination-satellite service (space-to-Earth) on a primary basis, subject to agreement obtained under No. S9.21. In Region 2, the band is also allocated to the radiodetermination-satellite service (space-to-Earth) on a primary basis. In Regions 1 and 3, except those countries listed in Nos. S5.369 and S5.400, the band is also allocated to the radiodetermination-satellite service (space-to-Earth) on a secondary basis. The use by the radiodetermination-satellite service is limited to feeder links in conjunction with the radiodetermination-satellite service operating in the bands 1610–1626.5 MHz and/or 2483.5– 2500 MHz. The total power flux-density at the Earth's surface shall in no case exceed -159 dBW/m2 in any 4 kHz band for all angles of arrival. S5.447Additional allocation: in Germany, Austria, Belgium, Denmark, Estonia, Spain, Finland, France, Greece, Israel, Italy, Japan, Jordan, Lebanon, Liechtenstein, Luxembourg, Malta, Morocco, Norway, Pakistan, Netherlands, Portugal, Syria, the United Kingdom, Sweden, Switzerland and Tunisia, the band 5150– 5250 MHz is also allocated to the mobile service, on a primary basis, subject to agreement obtained under No. S9.21. S5.447AThe allocation to the fixed-satellite service (Earth-to-space) is limited to feeder links of non-geostationary-satellite systems in the mobile-satellite service and is subject to coordination under Resolution 46 (Rev. WRC-95)/No. S9.11A. S5.447BAdditional allocation: The band 5150–5216 MHz is also allocated to the fixed-satellite service (space-to-Earth) on a primary basis. This allocation is limited to feeder links of non-geostationary-satellite systems in the mobile-satellite service and is subject to provisions of Resolution 46 (Rev. WRC-95)/No. S9.11A. The power flux-density at the Earth's surface produced by space stations of the fixed-satellite service operating in the space-to-Earth direction in the band 5150–5216 MHz shall in no case exceed -164 dB (W/m2) in any 4 kHz band for all angles of arrival.

S5.447C Administrations responsible for fixed-satellite service networks in the band 5150–5250 MHz operated under Nos. S5.447A and S5.447B shall coordinate on an equal basis in accordance with Resolution 46 (Rev. WRC-95)/No. S9.11A with administrations responsible for non-geosta-tionary-satellite networks operated under No. S5.446 and brought into use prior to 17 November 1995. Satellite networks operated under No. S5.446 brought into use after 17 November 1995 shall not claim protection from, and shall not cause harmful interference to, stations of the fixed-satellite service operated under Nos. S5.447A and S5.447B.

ICAO  POLICY

- The allocation table, as amended by WRC-95 to be maintained without change until the review by ICAO of the use of the band 5091-5150 MHz as required by ITU Resolution No. 114 (WRC-95), is completed

- This review should include a statement on, firstly, the immediate use of the band by civil aviation and, secondly, the longer-term expectations for 2010 and after. The total ARNS requirement, of which MLS may only be a part, is required by Resolution No. 114 (WRC-95) and must be considered.

- .

- Apply the methodology contained in ITU-R Recommendation S.1342 in the coordination of MLS with FSS earth stations in the band 5091–5150 MHz.Apply, in support to the studies under Recsolution 603 the same methodology to unwanted emission from RNSS earth station operating in the band 5000 - 5010 MHz.

- Do not oppose the deletion of the allocation to the Aeronautical Radionavigation Service in the band 5150-5250 MHz on the grounds that the operation of other services in this band now precludes the safe use of this band for aeronautical purposes.

- Delete the allocation to the aeronautical mobile satellite (R) service in S5.367.

AVIATION USE: The band 5000–5250 MHz was allocated to the ARNS service in 1947, in anticipation of a future microwave landing system as a replacement for ILS, and for other radionavigation uses for which the band would be particularly suited.   At that time it was estimated that 250 MHz of spectrum was required to support a microwave landing system, and some of the later candidate systems occupied the full 250 MHz   Footnote S5.367 was added to allow use of the band for AMS(R)S as an option which could be taken up at a later date. Following the decision by ICAO, in 1978, to adopt the time reference scanning beam MLS as the future international standard system, footnote  No. S5.444 was added by WARC-79 giving precedence to this system over all other uses.  The scanning beam system required 60 MHz for the initial channel plan, with the possibility of needing a further 60 MHz later.

Annex 10, Volume I, Chapter 3, 3.11.4.1.1 was amended to include   the channelling requirement for MLS fo 200 channels based on capacity studies made by the AWOP. The channeling plan for 200 channels, spaced 300 kHz apart between 5030 and 5090.7 MHz, including the pairing with DME, is at Table A in Annex 10, Volume I paragraph xxx.

One ICAO region (EUR) has prepared a regional frequency assignment and implementation plan for MLS based on possible use at airports  in the region in the years ahead. In this work, it was noted that the band 5030–5091 MHz could only support a proportion of the foreseeable regional requirements if MLS were to become the standard for all non-visual needs. The current lack of any plan for implemen tation of MLS in other Regions

The longer-term requirement for aids to precision approach to support all weather operations has been discussed at the Special Communications/Operations Divisional Meeting (1995) (SP COM/OPS/95) under Agenda Item 3. Recommendation 3/4 identifies  some of the options for precision approach, and Attachment C to Item 3 provides a statement of the possible MLS implementation sequence. Under Item 5 (Appendix A), a strategy for the introduction of non-visual aids was developed and incorporated in Annex 10. Appendix B to Item 5 outlines the ICAO regional considerations for MLS, which includes a progression to MLS for CAT II and III requirements if GNSS is not available at the time of the ILS replacement.

It should be noted that the total ARNS use of this band will also include systems for national requirements, civil or military, as well as those for international civil aviation purposes.

The non- aeronautical uses (for mobile services and for fixed-satellite services) of the band 5091 - 5250 MHz, allowed by Footnotes S5.444A, S5.446, S5.447, S5.447A, S5.447B and S5.447C  should also be noted.

COMMENTARY:

This important radionavigation frequency band has, in recent years, been the subject of close attention by other ITU radio services seeking worldwide exclusive spectrum,. The very long delay in implementing the new ICAO standard system (MLS),, and the prospect  of  GNSS offering equivalent capability, has accelerated this attention and has led to  new allocations to non-aeronautical radionavigation uses for the frequencies in the band 5150-5250 MHz, and the band 5091–5150 MHz .    These were adopted by ITU Conferences in 1987, 1992 and 1995. The changes to  the 5091-5150  MHz band by the addition of the fixed-satellite service  for the provision for feeder links for NGSO satellites in the mobile satellite service are eventually  lead to a complete reappraisal by the ITU of the future aviation requirement  for these bands.   For this purpose  WRC-95 Resolution No. 114 requests study by ITU-R and a report to WRC-2001.  (now WRC-2003)

The present situation is that the FSS allocation is a primary one in the band 5150–5216 MHz for the space-to-Earthdirection (with a pfd limitation of -164 dBW/m2/4 kHz ) (see Footnote S5.447B), and for the Earth-to-space direction (subject to S5.447A) the FSS is primary also in the band 5091–5150 MHz for Earth-to-space links (with a foreseen reversion to secondary in 2010).   Before 2010, MLS requirements which cannot be met in 5030–5091 MHz band will have precedence in the band 5091–5150 MHz over other uses (see Footnote S5.444A) which  could require the closure of  the FSS feeder link stations. However, this situation will be reviewed at WRC-2003. In the absence of aviation requirements for using this band, it may be permanently re-allocated to non-aeronautical services.

FSS Earth station implementation i has commenced  in some areas and  includes the use of the band 5091–5150 MHz. Such implementation is  being coordinated with aviation authorities (using the procedures of Resolution 46 (Rev. WRC-95)/No. S9.11A), and further  in accordance with the terms of Resolution No. 114. Resolves 2 of that Resolution requires administrations to ensure that these stations shall not cause harmful interference to the ARNS. Coordination with the aeronautical Radionavigation service using the technical provision of ITU-R Recommendation S1342 is therefore required.  In effect, FSS Earth stations which have been coordinated, agreed, and implemented  will compete for spectrum with any later MLS frequency assignment plan that makes use of he band 5091-5150 MHz . This may create a first-come, first-served situation whereby the first  service  implemented acquires control of the band. Since there is unlikely to be any MLS use of the 5091–5150 MHz band in the early years of MLS implementation ahead, this can lead to a loss, partial or whole, of the band for ARNS use until the year 2010, and possibly after that date as well.

The frequency band  between 5150 and 5250 MHz is shared on a joint primary basis between the ARNS and the FSS. The latter use is specifically for feeder links for NGSO-mobile satellites (see S5.447A) in the Earth-to-space direction. Footnote S5.447B also allocates the band 5150–5216 MHz to the FSS in the space-to-Earth direction subject to a PFD limitation and to agreement under Resolution 46 (Rev. WRC-95)/No. S9.11A. In addition, under S5.447 the band from 5150-5250 MHz is in use in 26 countries for the mobile service with primary status. More countries may be added to this list in the future as the use of the systems operating in this band proliferates. In practical terms this spectrum between 5150-5250 MHz can no longer support any international standard ARNS system. Furthermore, the maintenance of the allocation in the Table of Allocations provides a false picture of the spectrum available to aviation.  Accordingly, deletion of the ARNS allocation in this band should not be opposed. Limited country or region use can be accommodated by suitable footnotes.

The radiodetermination satellite service (space-to-Earth) is allocated in the band 5150–5216 MHz in Region 2 on a primary basis, and on a secondary basis in Regions 1 and 3 with a PFD limitation of -159 dBW/m2/4 kHz, except some countries (see Footnote S5.446). This radiodetermination system also uses three other frequency bands (see Footnote S5.446) and has a PFD limitation of -159 dBW/m2/4 kHz. No identification of a need for international aviation support has yet appeared for this system despite its ten year existence.

The band 5000 - 5150 MHz is also allocated to the aeronautical mobile satellite service on a primary basis under the provisions of S5.367. There are no plans to accommodate this service in this band and the allocation could be removed.

Developments at  WRC-2000

Addition of the  radionavigation satellite service (RNSS) in the band 5000-5030 MHz

The search for  spectrum for new RNSS (space-to-Earth of 20 MHz and Earth-to-space of 10 MHz) has focused attention on this band. This band was particularly considered to be required for the European Galileo system. There are benefits in the use of these higher frequencies, such as a lower ionospheric delay — often reduced by a factor of 6 or more compared to the 1GHz or 1.5 GHz band — smaller antenna dimensions and higher tracking accuracies without augmentation. The main disadvantage is that of the need for higher powers in the satellites due to RF propagation losses.

ITU-R WP8D has analysed the use of various segments  of the band 5000-5030 MHz (see Attachment 18 of the Report of 6th Meeting of WP8D) and noted, in particular, the requirement to protect the radio astronomy allocation in the band below 5000 MHz which would entail a guard band of around 10 MHz to be provided from 5000–5010 MHz.

However, WRC-2000 approved  the new footnote S5.443A for the RNSS in band 5000-5010 MHz in the Earth-to-space direction, and S5.443B for the RNSS in the band 5010-5030 MHz in the space-to-Earth direction,  The latter footnote imposes  PFD limitations on the space transmissions of the RNSS  to protect MLS in the band 5030 - 5150 MHz and the Radioastronomy in the band below 5000 MHz. The addition of this RNSS allocation was not opposed by civil aviation. However, in the interest of protecting MLS, Resolution 603 (WRC-200) was agreed which calls for study of the necessary technical, operational, and regulatory measures necessary for the protection of MLS from the spurious emissions of the RNSS . For protection of MLS from unwanted emissions from  RNSS Earth stations in the 5000-5010 MHz band the preferred technical measure is likely to establish  a minimum separation distance between these and MLS facilities, in the same way as applies to the operation of the FSS service in the 5091-5150 MHz under ITU-R Rec.S.1342.

Review of Spectrum Requirement for MLS

The Fixed Satellite Service was introduced in the band 5091-5150 MHz by WRC95 with primary status, with the condition that MLS would take precedence (see S5.444A) if it was necessary to expand from the main MLS band at 5030-5091 MHz into the band 5091 - 5150 MHz. In the year 2010 the FSS would revert to a secondary status under the provisions of S5.444A. WRC-95 also adopted Resolution114 calling for a review of the ARNS requirements in the band by 2001. The assumption is that the FSS anticipates a more permanent use of these frequencies beyond the year 2009. WRC-2000 reviewed the issue again and agreed to agenda item (1.4) for WRC-2003 in order to consider the results of the studies required under Resolution 114, and to review the allocation to all services in this band on the basis of these studies. Retention of the band will clearly be dependent on satisfying WRC-2003 that there is a need for more spectrum for MLS  to satisfy requirements that cannot be accommodated in the band 5030 - 5091 MHz.

The ICAO has commenced a review of the future requirements for MLS This entails a sequential process of collection of projected MLS requirements and locations, and a planning exercise to determine the spectrum requirement.

Outlook for the Future

The failure to use the MLS frequency band effectively has focused the attention of other services on aeronautical spectrum not in use and has led to the present situation where the original 250 MHz which was available for aeronautical services has been considerably reduced, and the remaining part of the original band is now also under challenge to aviation to show the need for its retention. Present ITU policies support this procedure as a means of satisfying the demands stated by expanding services, particularly those for mobile services. Aviation can expect this process to continue in the future with a consequential loss of expansion possibilities and a limitation on the future spectrum available to aviation radio services. It is important that positive actions are taken to prepare firm statements of intent in order to secure good, workable and adequate spectrum for the future as aviation continues to expand.

ITU-R Studies

The studies required under Resolution 114 have been completed, and  ITU-R Recommendation  S,1342 has now been approved by the  ITU Radiocommunications Assembly.   This Recommendation provides the basis to establish geographic separation distances for the siting of FSS Earth stations to protect MLS assignments in the band 5030–5090 MHz from interference from FSS Earth stations in the band 5091–5150 MHz. Further changes to this recommendation are not supported. (See section on protection requirements below.)

TECHNICAL AND OTHER INFORMATION

Band: 5000–5250 MHz

Service: Aeronautical radionavigation

Aviation use: MLS

Annex 10

SARPs: Annex 10, Volume I, Chapter 3, 3.11

Frequency plan: Annex 10, Volume I, Table A

Planning criteria:

Annex 10, Volume V, Chapter 4, 4.4

Annex 10, Volume I, Attachment G, Section 9

RTCA MOPS: D0-177; MOPS for MLS airborne receiving equipment (1986)

Eurocae MPS:

ARINC characteristic: 727

ITU Res/Rec: Rec. No. 607 (Mob-87): Future requirements of the band

5000–5250 MHz for the aeronautical radionavigation service

ITU-R Rec:

Question 95/8 — Sharing between ARN and mobile service

ITU-R S.1342   Method for determining coordination distances, in the 5 GHz band, between the international standard microwave landing system in the aeronautical radionavigation service and non-geostationary mobile satellite service stations providing feeder uplink services.

CCIR:

Other material: RTCA DO-226 guidance material for evolving airborne precision area navigation equipment with emphasis on MLS.

MLS COORDINATION WITH MSS IN BAND 5090 to 5150 MHz

Protection requirements for MLS (coordination with MSS Earth stations)

General

The band 5000–5250 MHz is allocated to the aeronautical radionavigation service (ARNS). Footnote S5.444 gives precedence in the band  5030–5150 MHz to the international standard system (microwave landing system) for precision approach and landing. Footnote S5.444A allocates on a joint primary basis the band 5091– 5150 MHz to the fixed satellite service (for mobile satellite feeder links) in the Earth-to-space direction until the year 2010. This allocation  was made by ITU WRC-95. Resolution No. 114 calling for studies of the compatibility between  these two services was approved .

The compatibility studies under Resolution 114 were carried out by ITU-R SG4A, which primarily deals with fixed satellite systems, and it was found appropriate for the results of the work obtained in SG 4A to be examined by the ICAO AWOP/16 held in 1997. AWOP/16 proposed numerous amendments, most of which were  later adopted at the radiocommunications Assembly in 1997.

ITU-R Recommendations

The method for the determination of coordination distances between Earth stations in the mobile satellite service (feeder links) in the band 5091–5150 MHz and MLS in the band 5030–5090 MHz which has been agreed in ITU-R is contained inITU-R Rec. No. [S.1342] on the Method for determining coordination distances, in the 5 GHz band, between the International Standard Microwave Landing System (MLS) in the Aeronautical Radionavigation Service (ARNS) and non-geostationary mobile satellite service stations providing feeder uplink services.

This Recommendation addresses only the protection of MLS in the band 5030– 5090 MHz. This band is displayed at Table A of Annex 10, Volume I, which specifies 200 channels for MLS installations. The Recommendation recognizes that the sharing between MLS in the band 5091–5150 MHz and the FSS in the band 5091–5250 MHz, and other new ARNS in the band 5030 and 5250 MHz and FSS in the band 5091 and 5250 MHz remains to be studied. The band 5091–5150 MHz is required to satisfy future long-term requirements.

AWOP/16 has concluded that co-frequency sharing between the fixed satellite service and MLS is not feasible.

Band: 5350–5470 MHz

Service: Aeronautical radionavigation (airborne weather radar)

Allocation:

MHz 5350–5470

| Allocation to Services |
| --- |
| Region 1 | Region 2 | Region 3 |
| 5350–5460 | AERONAUTICAL RADIONAVIGATION S5.449 EARTH EXPLORATION-SATELLITE (active) Radiolocation S5.448B |
| 5 460–5 470 | RADIONAVIGATION S5.449 Radiolocation |

Footnotes: S5.448BThe earth exploration-satellite (active) service operating in the band 5350–5460 MHz shall not cause harmful interference to, or constrain the use and development of, the aeronautical radionavigation service. S5.449The use of the band 5350–5470 MHz by the aeronautical radionavigation service is limited to airborne radars and associated airborne beacons.

ICAO POLICY These bands are used extensively, particularly for airborne weather radar, and are needed for the foreseeable future. No changes should be made which would restrict this aeronautical use. Support an upgrading of the radiolocation service to a primary status on a non-interference basis

AVIATION USE: A prime use of the band 5350–5470 MHz is for airborne weather radar, which is in conformity with Footnote S5.449.

COMMENTARY: The use of the band 5350–5470 MHz for airborne weather radar (a mandatory carriage item in many countries) is well established and has existed for many years. Annex 6, Part I, Chapter 6, 6.11 recommends equipage for aircraft operating in areas with potentially hazardous weather conditions. The ICAO policy (Appendix C to the Report of the Communications/Operations (COM/OPS) Divisional Meeting (1985) (Doc 9464) refers) is to retain the allocation without changes. While airborne weather radars also use the band 9 300–9 500 MHz, there remains a substantial preference also for the lower frequency band since this band is very suitable for detecting clear air turbulence. One of the usages of airborne weather radar is to avoid penetration of aircraft in hazardous weather.

The band 5350–5470 MHz is used on larger aircraft, which permit the installation of larger antennas. In this band, RF waves penetrate dense moisture better than in the higher frequency bands. Many aircraft are equipped with this system.

The Communications/Meteorology/Operations (COM/MET/OPS) Divisional Meeting (1990) (Doc 9566) (Appendix A to the Report on Agenda Item 1 (page 1A-4) refers) reports the emergence of radar for wind shear detection for the band 5600–5650 MHz which would be an admissible use under Footnote S5.452.

There is every reason to support the continued retention of the band 5350– 5470 MHz, and adjacent bands, without change.

WRC-97 added the Earth Exploration Service on a primary basis, with the condition not to cause interference to, or restrict the development of, the ARNS. Resolution COM 5-4 (WRC-97) was agreed calling for ITU-R studies.

WRC-2003 will under agenda item 1.5 consider, inter alia, the upgrading of the radiolocation service to a primary status in these bands. There are no objections against such upgrading which must include provision to protect the aeronautical Radionavigation service from interference.

TECHNICAL AND OTHER INFORMATION

Band: 5350–5470 MHz

Service: Aeronautical radionavigation

Aviation use: Airborne weather radar

Annex 10

SARPs: Annex 6, Part 1, Chapter 6, 6.11

Frequency plan: None

Channelization: None

Planning criteria:  None

RTCA MOPS: D0-173 MOPS for airborne weather radar and

ground mapping pulsed radars (1985)

Eurocae MPS:

ARINC characteristic: No. 708

ITU Res/Rec: ITU Resolution COM 5-4 (WRC-97): Use of the

Frequency Band 5350–5460 MHz by Space borne Active Sensors.

ITU-R:

Other material: DO-220 MOPS for airborne weather radar with

forward-looking wind shear detection capability (1993/1995)

This page deliberately left blank.

Band: 8750–8850 MHz

Service: Aeronautical radionavigation/radiolocation (airborne Doppler radar)

Allocation:

MHz 8750–8850

| Allocation to Services |
| --- |
| Region 1 | Region 2 | Region 3 |
| 8750–8850 RADIOLOCATION | AERONAUTICAL RADIONAVIGATION S5.470 S5.471 |

Footnotes: S5.470The use of the band 8750–8850 MHz by the aeronautical radionavigation service is limited to airborne Doppler navigation aids on a centre frequency of 8800 MHz. S5.471Additional allocation: in Algeria, Germany, Bahrain, Belgium, China, the United Arab Emirates, France, Greece, Indonesia, the Islamic Republic of Iran, Libya, the Netherlands, Qatar and Sudan, the bands 8825–8850 MHz and 9000–9200 MHz are also allocated to the maritime radionavigation service, on a primary basis, for use by shore-based radars only.

ICAO POLICY  No change since the requirement is a continuing one.  No change to S5.470.

AVIATION USE: Footnote S5.470.

Doppler navigation systems are  widely used for specialized applications such as identification of ground speed and flight track control.

COMMENTARY: The ICAO policy is a continuing one of no change to the allocation, as expressed in the Report of the Communications/Operations (COM/OPS) Divisional Meeting (1985) (Doc 9464), page 8C-11. Hence  the current allocation to the aeronautical Radionavigation service in this band must be retained.

TECHNICAL AND OTHER INFORMATION

Band: 8750–8850 MHz

Service: Aeronautical radionavigation/radiolocation

Aviation use: Airborne Doppler radar

Annex 10

SARPs: None

Frequency plan: None

Channelization: None

Planning criteria:  None

RTCA MOPS:

DO-220 MOPS for Airborne Weather Radar with Forward-Looking Windshear Detection Capability (1993)

Eurocae MPS:

ARINC characteristic:

ITU Res/Rec:

ITU-R:

Other material:

Band: 9000–9500 MHz

Service: Aeronautical radionavigation / radionavigation

(precision approach radar)

Allocation:

MHz 9000–9500

| Allocation to Services |
| --- |
| Region 1 | Region 2 | Region 3 |
| 9 000–9 200 | AERONAUTICAL RADIONAVIGATION S5.337 Radiolocation S5.471 |
| 9 200–9 300 | RADIOLOCATION MARITIME RADIONAVIGATION S5.472 S5.473 S5.474 |
| 9 300–9 500 | RADIONAVIGATION S5.476 Radiolocation S5.427 S5.474 S5.475 |

Footnotes: S5.337The use of the bands 1300–1350 MHz, 2700–2900 MHz and 9000–9200 MHz by the aeronautical radionavigation service is restricted to ground-based radars and to associated airborne transponders which transmit only on frequencies in these bands and only when actuated by radars operating in the same band. S5.427 In the bands 2900–3100 MHz and 9300–9500 MHz, the response from radar transponders shall not be capable of being confused with the response from radar beacons (racons) and shall not cause interference to ship or aeronautical radars in the radionavigation service, having regard, however, to No. S4.9 of these Regulations.

S5.471Additional allocation: in Algeria, Germany, Bahrain, Belgium, China, the United Arab Emirates, France, Greece, Indonesia, the Islamic Republic of Iran, Libya, the Netherlands, Qatar and Sudan, the bands 8825–8850 MHz and 9000–9200 MHz are also allocated to the maritime radionavigation service, on a primary basis, for use by shore-based radars only. S5.472In the bands 8850–9000 MHz and 9200–9225 MHz, the maritime radionavigation service is limited to shore-based radars. S5.473Additional allocation: in Armenia, Austria, Azerbaijan, Belarus, Bulgaria, the Czech Republic, Cuba, Georgia, Hungary, , Kyrgyzstan, Moldova, Mongolia, Poland, Romania, the Russian Federation, , Slovakia, Tajikistan, Turkmenistan, Ukraine and Uzbekistan, the bands 8850–9000 MHz and 9200–9300 MHz are also allocated to the radionavigation service on a primary basis. S5.474In the band 9200–9500 MHz, search and rescue transponders (SART) may be used, having due regard to the appropriate ITU-R Recommen-dation (see also Article S31). S5.475The use of the band 9300–9500 MHz by the aeronautical radionavigation service is limited to airborne weather radars and ground-based radars. In addition, ground-based radar beacons in the aeronautical radionavigation service are permitted in the band 9300–9320 MHz on condition that harmful interference is not caused to the maritime radionavigation service. In the band 9300–9500 MHz, ground-based radars used for meteorological purposes have priority over other radiolocation devices. S5.476In the band 9300–9320 MHz in the radionavigation service, the use of shipborne radars, other than those existing on 1 January 1976, is not permitted until 1 January 2001.

ICAO POLICY  No changes to the allocations that can adversely affect aviation use.  No change to S5.337, S5.427, S5.474, S5.475.

AVIATION USE:

These 3 cm radar bands are used extensively for  aeronautical, maritime (land-based and ship-borne), and by national defence radar systems. They cater for essentially shorter range surveillance and precision functions up to 50 km range. In aviation, they find considerable application in precision monitoring and approach functions, and in airborne weather radar  systems (AWR) where their shorter wavelength is very suitable for the detection of storm clouds. In this latter role, the frequency band 9345–9375 MHz has been coordinated with other users within ITU-R as the agreed aeronautical airborne frequencies for this purpose. This band provides for a narrower beam than the airborne weather radars operating at 5.3 GHz  and, therefore, provide a better resolution and less ground clutter. Although the 5 GHz band is generally preferred, 70 per cent of aircraft use weather radar operating in this band.   One of the uses of airborne weather radar is to give warning of hazardous weather. In many countries the carriage of AWR is a mandatory requirement.  This band is also used for surface detection radar. Some national uses employ transportable and mobile systems for national defense purposes.

The sharing of the bands with maritime coast and shipborne radar requires care and the application of modern technology to alleviate interaction effects. Footnote S5.475 draws attention to this sharing but does not alter the principle that both services have equal access rights. It should be noted that airborne weather radars are categorized for aeronautical navigation, i.e. storm warning and avoidance in accordance with the definition in S1.10, while meteorological radars for observation and recordings are in the category radiolocation (see last sentence in Footnote S5.475).

COMMENTARY:

The ICAO policy for these radar bands is based upon the requirement that these radars are likely to remain in service for many years into the future.,  Sharing with maritime radars is very manageble and practical because of the different geographical usage, and coordination between the two services is good. Sharing with other services in the areas of important operational use is not feasible.

Studies are under way on a possible upgrading of the radiolocation service to primary status.

TECHNICAL AND OTHER INFORMATION

Band: 9000–9500 MHz

Service: Aeronautical radionavigation/radionavigation

Aviation use: Primary radar 3 cm short-range applications including

precision approach. Airfield surface detection equipment (ASDE)

Annex 10

SARPs: Annex 10, Volume I, Chapter 3, 3.2

Frequency plan: None

Channelization: None

Planning criteria: None

RTCA MOPS:

Eurocae MPS:

ARINC characteristic: 708 (AWR)

ITU Res/Rec:

ITU-R:

ITU-R M.629: Use for the radionavigation service of the radio frequency bands 2900–3100 MHz, 5470–5650 MHz, 9200–9300 MHz, 9300–9500 MHz and 9500–9800 MHz

Other material:

Band: 13.25–13.4 GHz

Service: Aeronautical radionavigation (airborne Doppler radar)

Allocation:

GHz 13.25–13.4

| Allocation to Services |
| --- |
| Region 1 | Region 2 | Region 3 |
| 13.25–13.4 AERONAUTICAL RADIONAVIGATION S5.497 |
|  | S5.498, S5.499 |

Footnotes: S5.497The use of the band 13.25–13.4 GHz by the aeronautical radionavigation service is limited to Doppler navigation aids. S5.498The band 13.25–13.4 GHz may also be used in the space research service (Earth-to-space) on a secondary basis, subject to agreement obtained under No. S9.21. S5.499Additional allocation: in Bangladesh, India and Pakistan, the band 13.25–14 GHz is also allocated to the fixed service on a primary basis.

ICAO POLICY  No change to the allocations as there is a continuing aeronautical requirement for this band.  No change to S5.497.

AVIATION USE:

Footnote S5.497 limits the use to Doppler navigation aids, which will continue to be used.

COMMENTARY:

The Communications Divisional Meeting (1978) (COM/78) and the Communications/Operations (COM/OPS) Divisional Meeting (1985) (Doc 9464) (Appendix C to the Report on Agenda Item 8 refers) both confirmed the need to retain this allocation. This requirement has been confirmed in 1997.

TECHNICAL AND OTHER INFORMATION

Band: 13.25–13.4 GHz

Service: Aeronautical radionavigation

Aviation use: Airborne Doppler radar

Annex 10

SARPs: None

Frequency plan: None

Channelization: None

Planning criteria: None

RTCA MOPS: DO-173, DO-220, DO-158

Eurocae MPS:

ARINC characteristic:

ITU Res/Rec:

ITU-R: ITU-RM.496.3: Limits of power flux density of radionavigation transmitters to protect to protect space station receivers in the fixed-satellite service in the 14 GHz band

Other material:

Band: 15.4 - 15.7 GHz

Service: Aeronautical radionavigation (ASDE/other systems)

Allocation:

GHz 15.4–16.6

| Allocation to Services |
| --- |
| Region 1 | Region 2 | Region 3 |
| 15.4–15.43 | AERONAUTICAL RADIONAVIGATION S5.511D |
| 15.43–15.63 | FIXED-SATELLITE (space-to-Earth) (Earth-to-space) S5.511A AERONAUTICAL RADIONAVIGATION S5.511C |
| 15.63–15.7 | AERONAUTICAL RADIONAVIGATION S5.511D |

Footnotes: S5.511A The band 15.43-15.63 GHz is also allocated to the fixed satellite service (space-to-Earth) on a primary basis. Use of the band 15.43-15.63 GHz by the fixed satellite service (space-to-Earth and Earth-to-space) is limited to feeder links of non-geostationary systems in the mobile-satellite service, subject to coordination under No. S9.11A. The use of the frequency band 15.43-15.63 GHz by the fixed satellite service (space-to-Earth) is limited to feeder links of non geostationary systems in the mobile-satellite service for which advance publication information has been received by the Bureau prior to 2 June 2000. In the space-to-Earth direction, the minimum earth station elevation angle above and gain towards the local horizontal plane and the minimum coordination distances to protect an earth station from harmful interference shall be in accordance with Recommendation ITU-R S.1341. In order to protect the radio astronomy service in the band 15.35-15.4 GHz, the aggregate power flux density radiated in the 15.35-15.4 GHz band by all the space stations within any feeder link of a non-geostationary system in the mobile satellite service (space-to-Earth) operating in the 15.43-15.63 GHz band shall not exceed the level of - 156 dB(W/m2) in a 50 MHz bandwidth, into any radio astronomy observatory site for more than 2% of the time. S5.511CStations operating in the aeronautical radionavigation service shall limit the effective e.i.r.p. in accordance with Recommendation ITU-R S.1340. The minimum coordination distance required to protect the aeronautical

radionavigation stations (No. S4.10 applies) from harmful interference from feeder-link earth stations and the maximum e.i.r.p. transmitted towards the local horizontal plane by a feeder-link earth station shall be in accordance with Recommendation ITU-R S.1340. S5.511DFixed-satellite service systems for which complete information for advance publication has been received by the Bureau by 21 November 1997 may operate in the bands 15.4–15.43 GHz and 15.63–15.7 GHz in the space-to-Earth direction and 15.63–15.65 GHz in the Earth-to-space direction. In the bands 15.4–15.43 GHz and 15.65–15.7 GHz, emissions from a non-geostationary space station shall not exceed the power flux-density limits at the Earth's surface of -146 dB(W/m2/MHz) for all angles of arrival. In the band 15.63–15.65 GHz, where an administration plans emissions from a non-geostationary space station that exceed -146 dB(W/m2/MHz) for any angle of arrival, it shall coordinate under Resolution 46 (Rev. WRC-97)/No. S9.11A with the affected administrations. Stations in the fixed-satellite service operating in the band 15.63–15.65 GHz in the Earth-to-space direction shall not cause harmful interference to stations in the aeronautical radionavigation service (No. S4.10 applies). S5.512Additional allocation: in Algeria, Angola, Saudi Arabia, Austria, Bahrain, Bangladesh, Bosnia and Herzegovina, Brunei Darussalam, Cameroon, Congo, Costa Rica, Egypt, El Salvador, the United Arab Emirates, Finland, Guatemala, India, Indonesia, the Islamic Republic of Iran, Jordan, Kuwait, Libya, Malaysia, Morocco, Mozambique, Nepal, Nicaragua, Oman, Pakistan, Qatar, Singapore, Slovenia, Somalia, Sudan, Swaziland,Tanzania, Chad, Yemen and Yugoslavia, the band 15.7–17.3 GHz is also allocated to the fixed and mobile services on a primary basis. S5.513Additional allocation: in Israel, the band 15.7–17.3 GHz is also allocated to the fixed and mobile services on a primary basis. These services shall not claim protection from or cause harmful interference to services operating in accordance with the Table in countries other than those included in No. S5.512.

ICAO POLICY No change to the allocation to the Aeronautical Radionavigation Service. These bands are preferred bands for ASDE radar, and extensive use of these systems are expected as airport congestion increases and saturation occurs at many major airports in high density locations in the future. This band must be protected for present and future use of these systems.

Systems using radar measurement of height and distance also use this band and are expected to be used by smaller aircraft, helicopters, and other aircraft for safe landing at secondary landing areas. These also require protection and the capability for ongoing use.

The addition of the fixed-satellite service as a primary allocation must not prejudice these important aviation applications. (ITU-R Recommendations S.1340 and S1341 refer) Account needs also to be taken of other expected developments in technological aeronautical applications to which this band is particularly suited.

. No further adverse change to the restrictions imposed on the aeronautical use of this band through footnotes S5.511A, S5.511C and S5.511D. .

AVIATION USE OF THE BAND 15.43–15.  63 GHZ:

This 20 mm band is in use for a variety of civil and military systems, using conventional radionavigation and radar techniques.   An important civil use of this band is for  airport surface detection equipment (ASDE) for the operational function of control of ground movement at airports, an expanding requirement as congestion at airports spreads and saturates ground manoeuvring areas. Predictions made in Europe, for example, indicate a growing problem with surface movements, already affecting a number of major hubs, with saturation occurring at all major West European airports before the year 2010. ASDE radar is one preferred solution, and equipment operating in this frequency band, which offers a good compromise between antenna size and propagation characteristics, is presently in use at several main international airports. Typically, in Region 2, the band 15.6–16.6 GHz is used for ASDE radar.

Another civil use is that of height and obstruction measurement using radar techniques. This use is presently limited for general application to smaller aircraft operating into secondary and temporary landing areas. A forecast expansion in this use for specialized civil (as well as military) use has been predicted.

Both of these civil uses are on-going for the foreseeable future.

This band is also available for use by civil or military radionavigation systems implemented for national purposes. The band offers the possibility for compact airborne systems which are light in weight and which have small antenna dimensions. High definition radar and precision landing systems are some examples of applications.

COMMENTARY:

Discussions and agreements at ITU Conferences

WRC-95 discussed and agreed an allocation in the band 15.4-15.7 GHz for the fixed satellite service (FSS) for feeder links to non-GSO mobile satellites.  The decision was made without a full knowledge of the use made of the band by the ARNS. To and clear any compatibility problem Resolutions 116 and 117 were adopted calling for further study.  These studies were undertaken  by ITU-R WP4/1 - dealing mostly with the fixed satellite service - and identified a much more extensive use of the band than had originally been envisaged at CPM-95 and WRC-95.  A range of applications, covering both airborne and ground systems,  both for civil and for military aviation.purposes was identified.   Sharing criteria were developed and  are now  fully documented in ITU-R Recommendations S.1340 and S.1341.   These recommendations also recommend a partitioning of the band in 3 sections , which now appears in the Table of Allocations.  Primarily this was to give added protection to the radio astronomy service in the band below 15.4 GHz, and because both a the bottom 300 kHz and the top 700 kHz were too restrictive to be exploited by the FSS   The FSS allocation is for both Earth-to-space and space -to- Earth..

WRC-97 reviewed the results of studies and adopted the partitioning of the band, and modified Footnotes S5.511A and S5.511D to provide a framework of control on the FSS to protect other services. Footnote S5.511B, which prohibited airborne use in the 15.45-15.65 GHz section was deleted in line with the agreed ICAO policies. Footnote S5.511C is a restriction placed on the ARNS to limit the interference to FSS earth stations, and to impose a coordination distance on the FSS for the protection of the ARNS stations.WRC-97 also adopted Resolution 123 calling for studies of the protection required for the radio astronomy service, which was reviewed at WRC-2000 who made further changes to the footnotes to make the control more effective. Resolution 123 was was deleted by WRC-2000

The allocation of the fixed-satellite service  to this band  has the potential to significantly affect the flexible use by aviation systems.   At the WRC-95 the FSS requirement was stated as for a "small number of stations". Despite the failure of one mobile satellite operator (at least) to proceed with an implementation to use the band, aviation has continued to meet a determined resistance within ITU to limit the allocation to a more realistic level.  Country or regional footnote would be such an appropriate limitation measure.

The sequence of events, which has taken place in the discussions on this band, are indicative of the present intense pressures to find spectrum for the new NGSO services. Towards this purpose, the normal ITU processes of “study then allocate” have been reversed. The experience gained is that it is considerably more difficult to remove an unjustified allocation once agreed at a WRC than it is to allocate in the first place. While a moderate amount of sharing with downlink space services is technically possible in this band, as determined by the ITU-R work, constraining the present use of this band by aviation, and future exploitation of the allocation by aeronautical services and systems is not a satisfactory situation.

ARNS Protection and Planning Implications

The ITU-R   Recommendations quoted above have identified and calculated the sharing criteria necessary for the protection of all of the present ARNS systems known to use the band. These indicate, among other criteria, the need for coordination distances of between 310 km (landing and airborne radar measurement systems) and 600 km for general purpose airborne radar, referenced to the areas of operation. Coordination with the location of ground Earth stations prior to implementation is necessary to assess the potential for interference. These limitations and those of the PFD in the space-to-Earth direction create a situation of difficulty in terms of the siting of the FSS Earth station. Concern is expressed on the practicalities to maintain an exclusion zone around FSS station for aircraft equipped with these systems.

The results of the sharing studies (see below) to protect the aeronautical radio-navigation services, which included ASDE and a radar altimeter, have been found unduly restrictive to the FSS — for example, very large dish sizes at earth stations were necessary, and the distance separations from navigation facilities were large. The use of this band by the FSS appears to be minimal, and a worldwide allocation to the FSS is hence an inefficient deployment of scarce spectrum. Limited use in only a few countries in the future should be accommodated by footnote. A footnote allocation is reasonable since the ITU-R Recommendation on sharing can be used as an effective criterion for coordination between countries.

In FSS terms, this band is a supplementary band for feeder link operation for possible use as a back-up or spill-over from the main FSS feeder link bands at 19 and 29 GHz. Resolution No. 117, recognizing (b), indicates only a small number of stations, and ITU discussions show a limited interest among FSS operators, possibly only one country in North America and one in Europe Provided that the ARNS service has a flexible use of the band, based on an agreed set of clear and safe technical sharing conditions, there is a manageable sharing situation. As a service to be shared with ARNS, the FSS service is likely to be disciplined in its operations, highly stable in its implementation and technical characteristics and hence be preferred as a sharing partner if sharing is necessary.

The Future Outlook for the Band

The considerations above are the main elements in defining the aeronautical position on this matter. The band is in intensive use and will remain so.  The short wavelength of operation permits the deployment of systems on the ground with a minimum of interference planning provided there is control within the agencies wishing to employ them. Likewise airborne use is highly practical and economical. The pressures on the spectrum are such that all worldwide exclusive bands above 1 GHz are very suitable for satellite services, and existing users, such as the ARNS, will continue to receive pressures to share, or vacate, especially in the situation where there is a perception of less than full use.  This is a highly useful band for the exploitation of compact airborne radar and radio altimeter systems for use in civil aviation which needs to be preserved for possible future implementation.  The ICAO policy is based on these principles and is to apply pressure to preserve the future use.

TECHNICAL AND OTHER INFORMATION

Band: 15.4–16.6 GHz

Service: Aeronautical radionavigation/radiolocation

Aviation use: Primary radar particularly airport surface detection equipment (ASDE)

Annex 10

SARPs: None

Frequency plan: None

Channelization: None

Planning criteria: None

RTCA MOPS:

Eurocae MPS:

ARINC characteristic:

ITU Res/Rec:

	Resolution 719 (WRC-95): Urgent studies required in preparation for the 1997 World Radiocommunication Conference; Annex to Resolution 719.

	Resolution 123 (WRC-97): Feasibility of implementing feeder links of non-geostationary satellite networks in the mobile-satellite service in the band 15.43–15.63 GHz (space-to-Earth) while taking into account the protection of the radio astronomy service, the earth exploration-satellite (passive) service and the space research (passive) service in the band 15.35–15.4 GHz.

ITU-R:

	Res 116: Allocation of frequencies to the fixed satellite service (space-to-Earth) in the band 15.4–15.7 GHz for feeder links of non-geostationary satellite networks in the mobile-satellite service

	Res 117: Allocation of frequencies to the fixed satellite service (Earth-to-space) in the band 15.45–15.65 GHz for use by feeder links of non-geostationary satellite networks operating in the mobile satellite service.

	ITU-R S.1340  Sharing between feeder links for the mobile-satellite service and the aeronautical radionavigation service in the Earth-to-space direction in the band 15.4–15.7 GHz.

	ITU-R  S.1341  Sharing between feeder links for the mobile-satellite service and the aeronautical radionavigation service in the space-to-Earth direction in the band 15.4–15.7 GHz and the protection of the radio astronomy service in the band 15.35–15.4 GHz.

SHARING IN THE BAND 15.4–15.7 GHz

General

The part of the band at 15.43–15.63 GHz of the aeronautical radionavigation band 15.4–15.7 GHz is shared with the fixed satellite service, an allocation which was made by WRC-95, and later amended by WRC-97 (see RR S5.511 A). The FSS use is restricted to feeder links for non-geostationary satellites in the mobile satellite service. The conditions of use are covered by the footnotes S5.511A and S5.511C, which place restrictions on both services as part of the protection requirements.

ITU-R studies have shown:

Aeronautical utilization of band

The band is utilized by the ARNS for a variety of systems:

- Airport surface detection equipment (ASDE): radar systems used at civil airports for the control of surface movement;

- Radar sensing and measurement system (RSMS): sensing systems used in small aircraft and helicopters for height and other low-range measurement;

- Airfield landing system (ALS): a transportable landing system used for temporary airfields;

- Multi purpose radar (MPR): an airborne surveillance radar.

Descriptions of these systems are given in Annex A of the ITU-R Recommendations S.1340 and S.1341 (see below).

ITU-R Recommendations

(i)  Rec. ITU-R S.1340: Sharing between the ARNS and MSS Feeder Links in the Earth-to-space direction.

This recommendation contains the following limitations:

—	Limits the emissions from ALS and MPR at graded angles of shoot (paragraph 2.1);

—	Limits horizontal emission by Earth Stations to 54 dB(W/MHz);

—	Restricts RSMS to band 15.43 to 15.63 GHz;

—	Establishes coordination distances for the protection of ALS and MPR;

—	Urges the limit of 42 dBW on all ARNS stations.

(ii)  Rec. ITU-R S.1341: Sharing between Feeder Links for MSS and the ARNS and the RAS in the space-to-Earth direction

This recommendation contains the following limitations:

—	Limits the PFD of the FSS at the Earth’s surface for various angles of arrival (paragraph 2.1);

—	Establishes coordination distances for ALS and MPR (paragraph 5);

—	Limits Earth stations to operate above 5 degrees;

—	Makes provision for the protection of the radio astronomy service in the band 15.35 to 15.4 GHz.

Band: 24.25–24.65 GHz

Service: Radionavigation (ASDE)

Allocation:

GHz 24.25–24.65

| Allocation to Services |
| --- |
| Region 1 | Region 2 | Region 3 |
| 24.25–24. 45 FIXED | 24.25–24.45 RADIONAVIGATION | 24.25–24.45 RADIONAVIGATION FIXED MOBILE |
| 24.45–24.65 FIXED INTER-SATELLITE | 24.45–24.65 INTER-SATELLITE RADIONAVIGATION S5.533 | 24.45–24.65 FIXED INTER-SATELLITE MOBILE RADIONAVIGATION S5.333 |

Footnote: S5.533The inter-satellite service shall not claim protection from harmful interference from airport surface detection equipment stations of the radionavigation service.

ICAO POLICY No change to the radionavigation allocations in Region 2 and Region 3.

AVIATION USE: These bands supplement the 15.4–15.7 GHz band for airfield surface detection equipment (ASDE). The higher frequency provides greater target resolution although performance in precipitation, such as rain and fog mainly, is inferior. Footnote S5.538 should be noted.

COMMENTARY: In 1997 the need to retain this allocation was reconfirmed. The ASDE requirement assumes greater priority with increasing airport congestion.

TECHNICAL AND OTHER INFORMATION

Band: 24.25–24.65 GHz

Service: Radionavigation

Aviation use: Primary radar: airfield surface detection equipment

Annex 10

SARPs: None

Frequency plan: None

Channelization: None

Planning criteria: None

RTCA MOPS:

Eurocae MPS:

ARINC characteristic:

ITU Res/Rec:

ITU-R:

Other material:

Band: 31.8–33.4 GHz

Service: Radionavigation (ASDE)

Allocation:

GHz 31.8–33.4

| Allocation to Services |
| --- |
| Region 1 | Region 2 | Region 3 |
| 31.8–32 | RADIONAVIGATION FIXED S5.547A SPACE RESEARCH (deep space) (space-to-Earth) S5.547 S5.547B S5.548 |
| 32–32.3 | FIXED S.547A INTER-SATELLITE RADIONAVIGATION SPACE RESEARCH (deep space) (space-to-Earth) S5.547 S5.547C S5.548 |
| 32.3–33 | FIXED S5.547A INTER-SATELLITE RADIONAVIGATION S5.547 S5.547D S5.548 |
| 33–33.4 | FIXED S5.547A RADIONAVIGATION S5.547 S5.547E |

Footnotes: S5.547 The bands 31.8-33.4 GHz, 51.4-52.6 GHz, 55.78-59 GHz and 64-66 GHz by the Fixed Service are available for high-density applications in the fixed service (see Resolutions 75 (WRC-2000) and 79 (WRC-2000).. Administrations should take this into account when considering regulatory provisions in relation to these services. Because of the potential deployment of high-density applications in the fixed-satellite service in the bands 39.5-40 GHz and 40.5-42 GHz, administrations should further take into account potential constraints to high -density applications in the fixed service, as appropriate (see Resolution 84 (WRC-2000) S5.547A Administrations should take practical measures to minimize the potential interference between stations in the fixed service and airborne stations in the radionavigation service in the 31.8-33.4 GHz band, taking into account the operational needs of the airborne radar systems. S5.547B Additional Allocation : in the United States, the band 31.8-32 GHz is allocated to the radionavigation and space research (deep space) (space-to-Earth)services on a primary basis. S5.547C Additional Allocation: in the United States, the band 32 -32.3 GHz is allocated to the inter-satellite, radionavigation and space research (deep space) (space-to-Earth) services on a primary basis S5.547D Additional Allocation : in the United States, the band 32.3 -33 GHz is allocated to the inter-satellite and radionavigation services on a primary basis S5.547E Additional Allocation : in the United States, the band 33 -33.4 GHz is allocated to the radionavigation services on a primary basis S5.548In designing systems for the inter-satellite and radionavigation services in the band 32–33 GHz, and for the space research service (deep space) in the band 31.8–32.3 GHz, administrations shall take all necessary measures to prevent harmful interference between these services, bearing in mind the safety aspects of the radionavigation service (see Recommen-dation 707).

ICAO POLICY No change to the radionavigation allocations, noting in particular the airborne use of these bands for precision approach radar.

AVIATION USE: Use of the band for ground movement radar detection equipment is reported.

COMMENTARY: The Communications Divisional Meeting (1978) (Doc 9239) (Appendix C to the report on Agenda Item 3 refers) reported some use of these bands for ASDE and for airborne precision approach mapping radar.

TECHNICAL AND OTHER INFORMATION

Band: 31.8–33.4 GHz

Service: Radionavigation

Aviation use: Airfield surface detection equipment

Annex 10

SARPs: None

Frequency plan: None

Channelization: None

Planning criteria: None

RTCA MOPS:

Eurocae MPS:

ARINC characteristic:

ITU Res/Rec:

Rec. No. 707 (WARC-79): Relating to the use of the frequency band 32–33 GHz shared between the inter-satellite service and the radionavigation service.

ITU-R:

Other material:

— — — — — — —