AMCP WGF/6 WP/31

Draft compilation of replies to State Letter E 3/5-00/101

Presented by the Secretary

Note.— All references are to State letter E 3/5-00/101 unless indicated otherwise.

REFERENCE:		General comments

STATES’ AND INTERNATIONAL ORGANIZATIONS, COMMENTS

Australia

Responsibility for determining Australia’s position to be taken to the WRC-2003 lies with the Minister for Communications, Information Technology and the Arts, Senator the Hon Richard Alston. However, the development of Australia's position involves extensive consultation with all stakeholders, including the civil aviation community. Representatives from this Department, Airservices Australia, Qantas and Ansett are participating on the International Radiocommunications Advisory Committee (IRAC) developing Australia's position for WRC-2003. Furthermore, recognizing the importance of these ITU World Conferences to aviation, Airservices Australia has participated in past WRCs and I am advised that a representative from Airservices Australia will be on Australia's delegation to WRC-2003.

We support the strategy for establishing and promoting the ICAO position as outlined in para 2 of your letter. In this process we would strongly emphasize the importance of ICAO participation in regional preparatory meetings such as the Asia Pacific Telecommunity Preparatory Groups (APGs) under the auspices of the Asia Pacific Telecommunity (APT). At these meetings expert ICAO representation can be very effective in winning the support of other administrations which are still undecided.

Mexico

(Note.—See appropriate partial language version of this AN-WP for original text.)

Specifically with regard to bands “L” and “S” used for the Primary Radars, we agree with ICAO’s position in the sense to protect these frequencies for civil aviation.  It should also be considered the protection of frequencies used by the Secondary Radar.

Our posture must be to protect and guarantee the frequency bands that, on a primary basis, are assigned at worldwide level to the mobile aeronautical service, as well as to support the assignment on a primary basis of the aeronautical frequency bands found at a secondary basis.

New Zealand

The ICAO Secretariat and the Aeronautical Mobile Communications Panel are to be commended for the early development of the initial ICAO position on those ITU WRC-2003 agenda items of critical concern to international civil aviation.

The work of the New Zealand Radiocommunications Sector, in which the Civil Aviation Authority is an active participant, has continued without a break since the successful conclusion of WRC-2000. A strategy for the development of the New Zealand position for WRC-2003 has been developed and Conference Preparatory Groups established.

The availability of the international civil aviation position has greatly facilitated the early presentation of that position to the New Zealand Radio Sector thus bringing aviation’s concerns to the forefront right from the outset of the development of the New Zealand position for WRC-2003.

EUROCONTROL

The Agenda for the ITU-WRC 2003, scheduled for mid 2003, is contained in Resolution GT Plen-2/3 of WRC-2000. It contains 36 items dealing with changes to the 1TU Radio Regulations, of which 17 have some impact on aviation radio services. Of these six are of major concern with the potential to affect adversely the civil aviation capability to meet its requirements in the years ahead. One item included in the agenda provides for GNSS augmentation systems. In summary the important Agenda Items and the affected aviation radio services are:

1.1 Use of aero bands by other services;

1.4 MILS in the band 5091-5150 MHz;

1.14 Interference to HF air ground comms.;

1.15 New satellite nav systems in aero bands;

1.22 IMT-2000 in aero radar bands;

1.28 GNSS augmentation in VOR band;

7.2 Agenda for WRC-2006

The views of the European civil aviation organizations were discussed at the EUROCONTROL Spectrum Protection Group (SPG) Meeting held in December 2000. These views, supplemented later as further discussions and events took place, have resulted in the EUROCONTROL position with respect to the items for which it was felt appropriate to consider all the necessary elements. These comments form the EUROCONTROL response to the ICAO State Letter E-3/5-00/101 and are developed in paragraph 2 below.

With regard to the items 1.3, 1.5, 1.6, 1.8, 1.9, 1.11, 1.16, 1.17, 1.20, and 1.22, in view of the partial information currently available, the initial EUROCONTROL view is supportive to the ICAO position pending further investigations.

Note: these items are not reproduced within this document.

It is intended to supplement this document as further discussions and events will take place, regionally and worldwide.

IATA

Having taken commendably early steps to define the ICAO aviation position, an early comprehensive and active program to generate support amongst national policy makers is essential.  Timing should be tied to the development of national and regional positions and not to be left until such positions have been formally adopted.  Encouragement to governments at the highest level to support aviation input to national positions is required.  Harmonisation of aviation initiatives amongst influential aviation aforementioned bodies is strongly urged.

IFALPA

IFALPA fully supports the ICAO position for ITU WRC-2003.  We believe that the radio frequency spectrum and frequency bands allocated to aeronautical radio services are safety critical in nature.  The Aviation growth will require additional radio frequency spectrum to preserve at least the safety levels of the present day supported by new data/digital technology.  Any harmful interference of non-aeronautical radio services to aeronautical safety systems at any stage of the aircraft flight profile could have catastrophic results permanently endangering lives and property.

IFALPA believes that any attempt to share the frequency spectrum with non-aeronautical services (fixed or ground mobile) should be avoided.  Any changes of the present protected bands with the already identified potential of harmful interference, should be immediately notified to aviation technical experts.  This would ensure that the required safety measures are established or adapted for example: increase separation standards, particularly in RVSM airspace, or adapt the design of terminal and or route airspace.  It may also be necessary to suspend introduction of new technology based on systems using a shared frequency spectrum or band until enough research has been undertaken to ensure that safety requirements are maintained.

REFERENCE:	Attachment A, page A-2, paragraph 2.1

STATES’ AND INTERNATIONAL ORGANIZATIONS, COMMENTS

IATA

The inclusion of a reference to a CNS/ATM systems implementation and operation in ICAO policy provides a better overall consistency with respect to the radio spectrum policy.  However the 1994 “space based concept” has increasingly changed to a hybrid terrestrial-space based concept and therefore we would suggest to consider deletion of the 1994 reference in favour of the latest version of the ICAO global transition plan, as developed by ALLPIRG.

REFERENCE:	Attachment A, page A-2, paragraph 2.2

STATES’ AND INTERNATIONAL ORGANIZATIONS’ COMMENTS

IATA

IATA fully supports this requirement and strongly urges that before another services can share a band with aeronautical radio services the same rigorous prior analysis and testing should be applied as for airworthiness certification.

REFERENCE:	Attachment A, page A-2, paragraph 2.3

STATES’ AND INTERNATIONAL ORGANIZATIONS’ COMMENTS

IATA

This general statement is understood to relate to the reference made in Paragraph 2.1.  IATA proposes deletion of this paragraph from the ICAO ITU WRC-2003 position as it is not directly related to the Conference.  Notwithstanding such possible deletion there is an urgent need for aviation to look over the horizon beyond CNS/ATM implementation.  It is evident that in the future reliance on communication, navigation and surveillance will be much greater than presently foreseen for the planned CNS/ATM systems and consequently the aviation requirements for radio spectrum will increase.

REFERENCE:	Attachment A, pages A-4 to A-6 , WRC-2003 Agenda Item 1.1

STATES’ AND INTERNATIONAL ORGANIZATIONS’ COMMENTS

Kenya

We [...] further intend to delete Kenya's country footnote in S5.70 since none of our Radio Non Directional Beacons operate below 255 kHz.

Lithuania

From the ICAO proposals in the item 1.1* the Lithuanian interests are directly reflected in the remark S5.359A of the 1TU Radio Regulations mentioned in the c) part of the agenda.

We have a preliminary anticipation that the Lithuanian Telecommunication Authority will give a proposal to delete the remark.

Zimbabwe

Zimbabwe supports the deletion of the following footnotes:

a)	S5.181, S5.197 and S5.259

b)	S5.203 and no change to S5.203A

c)	S5.355A and S5.35A9 to be effective from year 2005 at the latest

d)	S5.439

e)	No change to footnote S5.444A

f)	Support the policy of linked reference in respect of RR S34.1 for ELTs

g)	Support deletion of footnotes S5.203A WRC 2006

h)	Support inclusion of results of studies in accordance with Resolution 222 (WRC 2000).

EUROCONTROL

The initial EUROCONTROL view is supportive to the ICAO position:

Based on the expected good co-operation between civil and military, the fixed services in the band 1559-1610 MHz should be removed by 2010. At least in one European State, there are unauthorised transmissions from fixed services (including military fixed services) to the GNSS band 1559 - 1610 MHz. National representatives of concerned States are encouraged to act vis-à-vis their Post and Telecommunication administrations to remove these unauthorised transmissions. It is necessary to obtain an agreement within each State between the military and civil as in many States military frequencies are not registered.

There is a need to provide evidence of unauthorised transmission in 1559-1610 MHz before presenting this issue to ITU.

REFERENCE:	Attachment A, page A-7, WRC-2003 Agenda Item 1.3

STATES’ AND INTERNATIONAL ORGANIZATIONS’ COMMENTS

IATA

IATA is in principle against the use of aeronautical frequencies for disaster communications.  As aviation bands are routinely used for safety service their use cannot be interrupted in case of a disaster.

REFERENCE:	Attachment A, pages A-8 to A-9 , WRC-2003 Agenda Item 1.4

STATES’ AND INTERNATIONAL ORGANIZATIONS’ COMMENTS

Australia

Australia has no current plans to introduce microwave landing systems (MLS) in the band 5 091-5 150 MHz. Consequently it would be difficult for the aviation community here to argue that the MSS/FSS operators in Australia should not have this band allocated to the FSS on a primary basis.

Brazil

With respect to the item 1.4, Brazil has no problem supporting it, considering we are not interested to have MLS systems being part of our infrastructure network.

Denmark

In co-operation with EUROCONTROL, the ICAO EANPG is currently reviewing the MLS requirements in Europe. The ICAO EANPG FMG has planned, with the support of EUROCONTROL, to use the revised MLS requirement to elaborate new MLS frequency plans.

EUROCONTROL is investigating the feasibility of introducing an aeronautical communication system in the 5GHz band adapting mobile technology based on CDMA access. It could be envisaged to move some part of the VHF services (in airport for example) to the 5GHz band.

The need to review the aeronautical spectrum requirements for this band and to obtain operational advise on the designated operational coverage for MLS system to be used for frequency planning purpose is urgent.

No decision on the future of the ARNS allocation in the band 5091-5150 MHz should be taken until the ICAO review of future use(s) has been completed and approved. Interference from services in adjacent bands is also an essential part of this decision.

Switzerland

We expect that the results of the studies concerning Agenda Item 1.4 show that the retention of the allocation of the band 5 091-5 150 MHz to the aeronautical radionavigation service can not be justified with requirements for MLS assignments. It is reasonable to assume that the band 5 030-5 091 MHz will provide enough spectrum for MLS. This is a direct consequence of the adoption of the “Strategy for introduction and application of non-visual aids to approach and landing” by ICAO in 1995.

EUROCONTROL

With regard to MLS, the ICAO Annex 10 contains a 200 channels' plan from 5031.0 to 5090.7 MHz and a provision for additional requirement in the band 5030.4 to 5150.0 MHz.

The ICAO Annex 10 defines a coverage for the azimuth direction: horizontally 22.5 NM from the MLS station, vertically 20 000 ft. The volume defined by these values is used for elaborating the frequency plan.

The European Region is a prime area for examination, with possibly the highest expected deployment. The European Region of ICAO had prepared a frequency plan for the band 5031.0 -5090.7 MHz, which had necessitated an adjustment of the Annex 10 height requirement from 20,000 feet to 10,000 feet in order to include the European requirement foreseen at that time.

Implementation of MLS has been relatively slow, and has not yet met the expectations at the time the system was originally agreed.

The ICAO European Air Navigation Planning Group (EANPG) together with EUROCONTROL are currently reviewing the MLS requirements in Europe. The Frequency Management Group (FMG) of the EANPG, with the support of EUROCONTROL, has planned to use the revised MILS requirements to elaborate a new MLS frequencies plan.

EUROCONTROL is investigating the feasibility of introducing an aeronautical communication system in the 5GHz band adapting mobile technology based on Code Division Multiple Access (CDMA). It could be envisaged to move some part of the VHF services (in airport for example) to the 5 GHz band.

The need to review the aeronautical spectrum requirements for this band and to obtain operational advise on the designated operational coverage for MLS system to be used for frequency planning purpose is urgent.

Taking into account the timeframe for the preparations for WRC-2003, the SPG Meeting recalled that a decision on deploying aviation system in the band 5091-5150 MHz has to be taken by mid-2001 at the latest.

No decision on the future of the Aeronautical Radio Navigation Service (ARNS) allocation in the band 5091-5150 MHz should be taken until the ICAO review of future use(s) has been completed and approved. Interference from services in adjacent bands is also an essential part of this decision.

IATA

IATA appreciates and will support the ICAO proposed procedure to establish the MLS spectrum requirement with the caveat that the global flexibility offered by the introduction of the three alternatives for precision approach and landing (as per Annex 10) is not compromised before GNSS Cat III installations are certified.

REFERENCE:	Attachment A, page A-11, WRC-2003 Agenda Item 1.6

STATES’ AND INTERNATIONAL ORGANIZATIONS’ COMMENTS

United Kingdom

The United Kingdom has no problem with the ICAO position, the one exception is with Agenda Item 1.6 and the ICAO position “not to oppose the deletion of the allocation to the aeronautical radionavigation service in the band 5 150 - 5 250....”. While this statement may be correct the United Kingdom is not convinced a full assessment has been made as to whether we should delete this allocation or indeed whether we should seek an allocation to another aeronautical services such as communications in the quoted frequency band.

IATA

IATA agrees that for ITU WRC-2003 there is no justification to maintain this allocation.  However, it is not the aeronautical allocation that is on the Agenda but the protection of feeder links.  To satisfy future expected increases in aviation spectrum requirements every attempt should be made to maintain the present allocation.

REFERENCE:	Attachment A, page A-15, WRC-2003 Agenda Item 1.14

STATES’ AND INTERNATIONAL ORGANIZATIONS’ COMMENTS

Australia

In view of the vast areas involved over land and sea and the difficult nature of the terrain in the Asia Pacific region we do not subscribe to the view that interference of HF aeronautical communications from the multitude of illegal transient operators can be effectively contained by regulatory means as suggested in the Discussion section of the ICAO Attachment. We contend that whilst there is a need for regulatory control, this problem will not be solved in this region without a technical solution to mitigate interference. Of course this solution will need to be cost effective and have little or no cost impact on aircraft fit. We are, however, pleased that the ICAO has recognized this as a problem and is supportive of measures to combat it.

Denmark

Resolution 347 (WRC-00) requests to review WRC-03 the frequency arrangements in the maritime MF and HF bands considering new adaptive and digital technologies.

The results of WRC-03 are intended to be used at WRC-06 (Agenda 2.5) to find additional allocation to the broadcast service in the HF band, “normally” excluding aeronautical service.

The risk to be prevented is that WRC-03 extends the review from maritime to aeronautical band as broadcasters may need important spectrum capacity for their digital programmes and therefore to modify WRC-06 agenda 2.5 to consider also aviation allocations.

Support any measures which tighten the provisions related to the removal of interference to HF air ground communications.

Oppose any review of the Allotment Plan in Appendix S.29 on the basis that the frequency bands concerned are already suffering congestion and insufficient frequencies for international operations.

Ireland

Resolution 347 of WRC 2000 requests a review at WRC 2003 of the Frequency layout in the MF and HF Bands, taking account of new technologies (Digital). The danger in the future is that the aeronautical bands will be targeted for digital programmes. We would therefore oppose any review of the Allotment Plan due to the bands already congested and that there is not sufficient spectrum for International Operations.

EUROCONTROL

Resolution 347 (WRC-00) requests to review at WRC-03 the frequency arrangements in the maritime MF and HF bands considering new adaptive and digital technologies.

The results of WRC-03 are intended to be used at WRC-06 (Agenda 2.5) to find additional allocation to the broadcast service in the HF band, "normally' excluding civil aviation aeronautical services' allocations .

The risk to prevent is that WRC-03 extend the review from maritime to aeronautical band as broadcasters may need important spectrum capacity for their digital programmes and therefore to modify WRC-06 agenda 2.5 to consider also civil aviation allocations

It is necessary to support any measures which tighten the provisions related to the removal of interference to HF air ground communications. Also, it is necessary to oppose any review of the Allotment Plan in Appendix S.29 on the basis that the frequency bands concerned are already suffering congestion and insufficient frequencies for international operations.

IATA

IATA fully supports regulatory measures to protect HF communication against harmful interference.  Such regulatory measures should form the basis for consideration of possible new techniques.

REFERENCE:	Attachment A, pages A-16 to A-17, WRC-2003 Agenda Item 1.15

STATES’ AND INTERNATIONAL ORGANIZATIONS’ COMMENTS

Australia

Whilst we agree and support the ICAO position in regard to the introduction of RNSS (down link) allocations in the I GHz bands we note that no mention has been made of the allocation also made at WRC 2000 in the 5 GHz band (5 010 - 5 030 MHz). Studies under Resolution 604 calling for protection of the Radio Astronomy Service (RAS) in the band 4 990 to 5 030 MHz from the newlv allocated Radionavigations Satellite Service in the band 5 010 to 5 030 MHz are currently underway in ITU-R WP 8D. The outcomes of these studies are to be considered by WRC-2003. Is there any particular reason for this omission?

Denmark

Aviation has supported the allocation to the RNSS made by WRC-2000 on the conditional basis that ARNS services, existing and future, are fully protected.

ARNS services require protection since they are currently the prime radio navigation support and the standard ICAO system for en-route navigation in high-density continental airspace. In these areas there is no scope for re-assignment of frequencies. Europe has some of the most intensive use of this band in the world with many DME as well as Tacan.

The aggregate pfd limit must be defined in order to protect the current and future use of this band by the total ARNS systems i.e. ACAS, DME, Tacan, and SSR.

Band 1215-1300 MHz

When WRC-2000 allocated the frequency band 1260 – 1300 MHz to the radio navigation satellite service (RNSS) in the space-to-earth direction already occupied by 23 cm primary surveillance radar, the conference recognised the importance of those radar systems and the need for adequate protection. The RNSS signal in 1260-1300 MHz band is not foreseen to be used for aeronautical operation. Most of the radar systems are in operation as main sensors for air traffic management systems.

WRC-2000 developed the resolution 606, tasking the ITU-R sector to conduct for WRC 2003 as a matter of urgency the appropriate technical, operational and regulatory studies to ensure that the operation of radio satellite navigation service in the band 1215 – 1300 MHz will not cause harmful interference to radar stations.

Germany

It is proposed to include TACAN and SSR in the list of aeronautical systems, which needs to be protected from RNSS transmissions in the band 1 164 -1 215 MHz.

Ireland

Band 1164 –1215 Mhz.

ARNS services require protection, and Europe has dense population of DME. The PFD limit must be defined for protection of the future usage of ARNS… ACAS, TACAN,  SSR  as well as DME.

Band  1215-1300 Mhz.

WRC 2000 tasked the ITU-R to conduct for WRC 2003 the necessary studies to ensure that RNSS  in this band will not cause interference to Radar stations. ITU-R and CEPT are presently examining two methods for determining the potential for Interference to radar systems from RNSS. We would support the method based on Eurocontrol SPG 13 WP 14.

Switzerland

Our understanding of provision S5.328A and Resolution 605 (WRC-2000) is that protection is not limited to DME facilities already in operation. The aeronautical community should not accept any formal constraints on the future use of the band 1 164-1 215 MHz for DMEs. We have identified additional DME requirements for which further assignments may have to be made in the band 1 164-1 215 MHz.

EUROCONTROL

Band 1164-1215 MHz

Aviation has supported the allocation to the Radio Navigation Satellite Service (RNSS) made by WRC-2000, on the conditional basis that ARNS services, existing and future, are fully protected.

ARNS services require protection since they constitute, currently, the prime radio navigation support, and the standard ICAO system for en-route navigation in high density continental airspace. In these areas there is no scope for re-assignment of frequencies. Europe experiences one of the most intensive use of this band in the world with many DME as well as TACANs.

The aggregate power flux density (pfd) limit must be defined in order to protect the current and future use of this band by the total ARNS systems i.e. ACAS, DME, TACAN, and SSR.

Band 1215-1300 MHz

When WRC-2000 allocated the frequency band 1260 - 1300 MHz to the RNSS in the space-to-earth direction, already occupied by the 23 cm primary surveillance radar, the Conference recognised the importance of these radar systems and the need for adequate protection. The RNSS signal in 1260-1300 MHz band is not foreseen to be used for aeronautical operation. Most of the radar systems are in operation as main sensors for air traffic management systems.

WRC-2000 developed the resolution 606, tasking the ITU-R sector to conduct, in preparation for WRC 2003, as a matter of urgency, the appropriate technical, operational and regulatory studies, in order to ensure that the operation of RNSS in the band 1215 - 1300 MHz will not cause any harmful interference to radar stations.

ITU-R and the European Conference of Posts and Telecommunications Administrations (CEPT) is currently considering two procedures for determining the potential for interference to radar receivers from emissions of RNSS space stations.

One method is based on the assumption that operational experience in the band 1215 - 1260 MHz has shown that sharing between existing radio navigation-satellite systems and radar is feasible. And so, the pfd limit produced by existing radio satellite navigation systems should be applied also for future RNSS systems.

Another method is based on the definition of an interference threshold for radar receivers. This interference threshold can than be used to develop an aggregate pfd limit to be imposed on RNSS systems operating on a co-frequency basis.

The first method based on operational experience does not take into account future developments of RNSS systems like increasing number of satellites in the orbit constellation, different signal structure or increased signal power to be transmitted from the space stations. The SPG Meeting concluded, therefore, that this methodology is not appropriate to develop pfd limits for the protection of radar stations from harmful interference.

The second method based on an interference threshold of radar receivers of I/N=-6 dB as given in Recommendation ITU-R M.1461 delivers a pfd limit of -176.6 dBW/(m2.MHz) which might prohibit the implementation of a new radio navigation-satellite system in the band 1215-1300 MHz. Moreover, existing RNSS systems, operating on a co-primary basis in portions of the band 1215-1260 MHz, radiate 40 dB higher pfd limits.

Further actions are needed to verify the protection limits for existing and planned radar receivers, and to obtain operational confirmation or advise on the second method and on the radio parameters (antenna gain, I/N ratio...).

REFERENCE:	Attachment A, page A-23, WRC-2003 Agenda Item 1.28

STATES’ AND INTERNATIONAL ORGANIZATIONS’ COMMENTS

Brazil

Regarding page A-40 of the Attachment, related to agenda item 1, with respect to the item 1.28 and according to suggested amendments to the ITU Radio Regulations, Brazil suggests altering the wording of proposed Note S5.CCC to read as follows:

“The band 108-117.975 MHz is also allocated to the Aeronautical Mobile (R) Service and limited for the transmission of ground based signals that provide supplemental navigational data for the radio navigation satellite service, by ICAO standardized systemsair navigation and ICAO standardized control data systems”.

Denmark

It is essential for European aviation to find allocation for the use of GNSS augmentation systems.

VDL mode 4 is foreseen for ADS and possibly for communications application. There is an opportunity to initiate appropriate radio regulatory provisions for the introduction of VDL Mode 4.

In Europe, the VHF congestion on communications application is critical and some sectors cannot be opened due to frequencies shortage. There is an opportunity to raise awareness and discuss this matter in order to get support to overcome the situation.

Germany

The proposed ICAO position is satisfying the request for the introduction of GBAS/GRAS stations in the band 108 -117.975 MHz. It is suggested to extend this WRC agenda item to develop appropriate radio regulatory provisions for the introduction of VDL Mode 4 in this frequency band.

Greece

Regarding WRC-2003 agenda item 1.28, we have noted that recent studies (for instance GNSSP WP/53) indicate that the introduction of ground based augmentation systems (GBAS) in the band 108-117.975 MHz will imply constraints on the operation of conventional navaids in this band. Taking into account the shortage of frequencies in the same band in Europe and in Greece in particular, and that the conventional (VOR/ILS) navaids will continue to be used heavily in the foreseeable future, we support the following position vis a vis the aforementioned agenda item:

No objection to an allocation permitting the use of the band 108 - 117.975 MHz for the transmission of ICAO standard GNSS augmentation systems, on condition that no harmful interference is caused to the stations of the aeronautical radionavigation service operating in this band and that no restrictions are incurred to the deployment of such stations. Furthermore, conformity with ITU-R Recommendation IS-1009 regarding compatibility with the FM broadcast services in the band 87.5 -108 MHz should be ensured.

Ireland

It is important for  GNSS augmentation systems to be allocated spectrum. It is now envisaged that VDL Mode 4 be used for ADS, with possibility of communications applications.  In Europe, however, congestion on the bands 108-117.975 Mhz is critical. This has been alleviated temporarily by the introduction of 8.33 Khz channel spacing in the Core area. Further investigation and discussion is needed so as the best position is arrived at for the Aviation Interest.

Spain

(Note.—See appropriate partial language version of this AN-WP for original text.)

We consider that the proposal should not be limited only to navigation data since we understand that some frequencies of that band will be required shortly for the transmission of data related to the surveillance systems which are presently standardized or which are planned to be standardized immediately by ICAO.  (In this respect, of special importance are the surveillance systems related to VDL-4.)

In summary, one should ensure that the band 108-117.975 MHz can be used for the transmission of navigation and surveillance signals related to the corresponding systems standardized by ICAO.

Sweden

In order to allow maximum freedom for aviation needs, Sweden proposes the following change of Agenda Item 1.28 S5.CCC.

S5.CCC	The band 108-117.975 is also allocated to the Aeronautical Mobile (R) Service and limited for the transmission of ground-based signals that provide supplemental navigational data for the radio navigation satellite service, by ICAO standardized data link systems.

Switzerland

ITU-R Recommendation IS.1009-1 must be amended with criteria for compatibility assessments between GBAS and FM broadcast services in the band 87.5-108 MHz. GBAS/FM compatibility is not included in its present version.

“ICAO Position:	Support an allocation permitting the use of the band 108 - 117.975 MHz for the transmission of ICAO standard GNSS augmentation systems.

Ensure conformity with ITU-R Recommendation IS.1009 regarding compatibility with the FM broadcast services in the band 87.5 - 108 MHz. Amend ITU-R Recommendation IS.1009.”

EUROCONTROL

Due to the emergence of new technologies to be used in future by civil aviation (such as GNSS augmentation, VDL Mode 4, etc), and which could support multiple aviation services (Navigation, Communication, Surveillance), it is proposed to adopt right now a more flexible approach for the use of this part of the band, preventing the re-opening of a similar debate in future ITU meetings.

The objective is to evolve towards the following proposal:

To permit the use of the band 108 - 117.975 MHz for the transmission of signal according to the ICAO standardized systems.

However, detailed studies will be needed to identify spectrum requirements for proposed aeronautical systems to enable effective sharing of the band.

IATA

The ICAO position to the WRC-2003 only addresses the need to accommodate the GNSS augmentation in the 108 - 117.95 MHz.  IATA considers this draft ICAO position rather restrictive and does not reflect the ongoing trend to replace navigation services in the ITU definition, and surveillance services such as ADS-B data communication.  Accommodation of new technologies within existing regulations remain the root cause of inconclusive discussions within the aviation community.

IATA proposes to change the draft ICAO position as follows:

“Support an allocation permitting the use of the band 108-137 MHz for the use of ICAO standardized data link services.”

REFERENCE:	Attachment A, page A-24, WRC-2003 Agenda Item 1.31

STATES’ AND INTERNATIONAL ORGANIZATIONS’ COMMENTS

EUROCONTROL

The initial EUROCONTROL view is supportive to the ICAO position. It is noted that the GNSS band at 1559 -1610 MHz has been specifically excluded from the search for new mobile satellite spectrum.

REFERENCE:	Attachment A, page A-26, WRC-2003 Agenda Item 7.2

STATES’ AND INTERNATIONAL ORGANIZATIONS’ COMMENTS

Denmark

This item is an opportunity to address aviation radio spectrum requirements.

In addition to the examples given by ICAO, to support the inclusion in the agenda of WRC-2006 of items addressing

•	the shortage of aeronautical frequencies in some radio bands and some regions,

•	the need to find frequencies for aeronautical systems that may be introduced in the medium and longer term.

Ireland

This agenda item affords the opportunity to address Aviation Radio Spectrum requirements in general, i.e .

•	Need to find spectrum for aeronautical future medium/longterm systems.

•	Shortage of aeronautical frequencies at present in some bands and regions.

EUROCONTROL

This item is an opportunity to address aviation radio spectrum requirements.

In addition to the examples given by ICAO, it is proposed to support the inclusion in the agenda of WRC-2006 of items addressing:

-	the shortage of aeronautical frequencies in some radio bands and some regions; and

-	the need to find frequencies for aeronautical systems that may be introduced in the medium and longer term.

Further discussion is needed to consolidate the aviation position.

REFERENCE:		Attachment A, page A-31

STATES’ AND INTERNATIONAL ORGANIZATIONS’ COMMENTS

Brazil

Regarding page A-31 agenda items 3,4,5, 6 and 7.1, Brazil is conducting studies in view of analysing their impact on the Brazilian Administration and will manifest its position as soon as possible and in an appropriate manner.