|  | INTERNATIONAL TELECOMMUNICATION UNION | AMCP WF7/WP12 |
| --- | --- | --- |
|  | RADIOCOMMUNICATION STUDY GROUPS | Document 8D/TEMP/137-E 30 October 2001 English only |

Source:		Attachment 15 to Document 8D/140(Rev.1)

Working Party 8D
(Drafting Group 8D2b)

DRAFT REVISION TO WORK PLAN for

Determination of feasibility and practicability of prioritization and real-time pre-emptive access 
between different networks of MSS in the
bands 1 545-1 555 MHz and 1 646.5-1 656.5 MHz

# 1	Introduction

Working Party 8D considered Documents 8D/79 and 8D/88 on the feasibility and practicality of real-time pre-emptive access between different networks of MSS in the bands 1 545-1 555 MHz and 1 646.5-1 656.5 MHz.

Document 8D/79 (Attachment 1) was submitted to stimulate discussions and contributions on the feasibility and practicality of prioritization and real-time pre-emptive access for AMS(R)S, in the MSS generic allocation in frequency ranges 1 525-1 559 MHz and 1 626.5-1 660.5 MHz, in accordance with Resolution 222 (WRC-2000).

The document was considered as being useful to help administrations to focus on this issue, which must receive renewed attention. The pressing need to act diligently on the resolution of this issue comes from the fact that agenda item 3.2 of WRC-05/06 calls for a review of the studies made in accordance with Resolution 222 and that the spectrum allocated in this portion of the spectrum to the MSS and AMS(R)S is becoming congested.

Attachment 1 is also considered as a useful base to develop a work plan toward the resolution of this issue.

# 2	Steps for the work plan

(	Completion of revision of Recommendation ITU-R M.1089.

(	Definition of the terms "immediate availability" and "real-time pre-emptive access".

(	Identification of scenarios where real-time pre-emption would be applied.

(	Investigation of potential methodologies and mechanisms to accommodate prioritization and call pre-emption processes (e.g. spectrum reserve pool).

(	Determination of feasibility and further development of technical and operational factors relating to the interface architecture between MSS systems operating in the frequency band of interest.

Attachment 2 is a working document toward a preliminary draft new Recommendation that was contained in the report of the tenth meeting of ITU-R Working Party 8D.

The work plan has been developed to focus on the study requested by Resolution 222. Contributions are urgently invited to complete the work as soon as possible.

Attachment 3 is a contribution towards identification of scenarios where real-time pre-emption would be required.

____________

Attachment 1:	Document 8D/79 (not attached)

Attachment 2:	Attachment 18 of Document 8D/61 (not attached)

Attachment 3:	Contribution towards identification of scenarios where real-time pre-emption would be required (Doc. 8D/TEMP/aaa).