]SCRSP/WG-A

IP/A/

Agenda item-

Apr.2001

SURVEILLANCE AND CONFLICT RESOLUTION SYSTEMS PANEL (SCRSP)

AIRBORNE COLLISION AVOIDANCE SYSTEMS

WORKING GROUP-A

(Rio de Janeiro, Apr.9-13, 2001)

Electro-Magnetic Interference Report from Passenger-Carried

Portable Electronic Devices

Presented by Hajime Yoshimura (JCAB)

Prepared by Hajime Yoshimura (JCAB), Norio Yamamoto (ENRI)

SUMMARY Operators of commercial airplanes have reported numerous cases of passenger- carried portable electronic devices affecting airplane systems during flight. These devices have been suspected of causing such anomalous events as autopilot disconnect, erratic flight deck indications, audio noise etc. This paper presents the summary of electromagnetic interference report of passenger-carried portable electronic devices in Japan.

1. Introduction

Operators of commercial airplanes have reported numerous cases of passenger- carried portable electronic devices (PED) affecting airplane systems during flight. These devices including cell phones, laptop computer, digital video camera, compact-disc player and electronic games have been suspected of causing such anomalous events as autopilot disconnect, erratic flight deck indications, audio noise etc. Japan Civil Aviation Bureau (JCAB) has noticed that devices suspected of causing these anomalies be turned off during critical stages of flight (takeoff and landing). JCAB also notices prohibiting the use of devices that intentionally transmit electromagnetic signals, such as cell phones, during all phases of flight and making operators responsible for governing the use of portable electric devices on their own airplanes.

2. Electro-Magnetic Interference Report

JCAB has collected reports from commercial operators and investigated correlation between PED and airplane system anomalies.

2.1 Correlation between PED operation and airplane anomaly

The total number of EMI reports from operators is 41 reports for 8 years since 1993 (Figure 1). We officially require operators to submit reports with PEDs suspected as the causes. Figure 2 shows EMI report categories. The majority of these reports, 27 events, were events where PED interference was suspected. There are 8 events with seemingly some apparent correlation between PED operation and the airplane anomaly (the problem disappeared when the PED was turned off, either immediately or shortly after), 1 event deemed to have a strong correlation (the problem disappeared when the PED was turned off, returned when PED use resumed, and disappeared when the PED was turned off again) and 4 events which were later found failures in airplane system at repair shop.

2.2. PED

Reports of cell phones is remarkably numerous (Figure 3). The regulation which make cell phones turned off during all phase of flight is not thoroughly observed.

2.3 Airplane Systems

Figure 4 shows Airplane systems received electro-magnetic interference and the number of reports.

2.4 Example of EMI report

Some example cases are included to illustrate the variety of potential PED events.

October 2000, B737

Passenger cell phones were reported to cause autopilot system disconnected during cruise. The airplane was cruising at 27000ft when L-NAV and V-NAV mode was suddenly disengaged. Both modes could be engaged after a while. It was reported that two passengers were using cell phones in the aft cabin. No system failures were found at the repair shop after landing.

February 2000, DC-9

A passenger laptop computer was reported to cause false alarm on the alarm system during cruise at 33000ft. Horizon alarm in the comparator was turned on while the laptop computer was used in the cabin. After the computer was turned off, the alarm was cleared. However, while the laptop computer was then allowed to use for a few minutes, the anomaly happened again.

December 1999, A320

A passenger cell phone was also reported to cause noises in communication system during climb from 29000ft to 33000ft. Buzz sound occurred in VHF communication receivers intermittently. A passenger cell phone was discovered to turn on and was receiving a call from a ground cell phone station. After the cell phone turned off, the noise disappeared.

November 2000, B767

A passenger cell phone was reported to cause anomaly on a traffic collision avoidance system (TCAS) during cruise at 32700ft. Resolution Advisory (RA) was issued for a target at flight level 33600. Though the airplane descended 1000ft below in accordance with RA, the target symbol was still in the same position on the TCAS display. The pilot shifted a transponder from left to right and then the target disappeared. The ATC reported there was no traffic around the airplane. A cell phone was used in the cabin.

2.5 Flight Phase

EMI events occurred in all Flight phases (Figure 5). The most frequently subjected flight phase is cruising. JCAB conducted an experiment to measure electromagnetic environment in the cabin during flight. It was found that calls from ground cell phone stations can readily reach in the cabin even during cruise and a passenger cell phone can respond to the call and transmit electromagnetic signal.

3. Consideration

Many cases of EMI have been reported over the years, with PEDs suspected as the cause, but almost impossible to duplicate these events after landing. Many EMI events are transient and there are no precise devices to record electromagnetic level and exact time when these events occur. However, the result of our experiment shows a possibility that PEDs are suspected of interfering airplane systems because some PEDs radiate electromagnetic waves over the accepted susceptibility level of airplane systems, prescribed in RTCA DO160-D “Environmental Conditions and test Procedures for Airborne Equipment”. JCAB maintain collecting EMI reports from operators and investigating the correlation between PEDs and airplane systems anomalies hereafter.

4. Contact

Hajime Yoshimura

Chief of Avionics section, Airworthiness division, Civil Aviation Bureau

Tel: +81-3-5253-8735 Fax: +81-3-5253-1661

E-mail: yoshimura-h2iv@mlit.go.jp