### AMCP WGF9/WP22

Source:

# Date:  3rd December 2002

Subject: Agenda Item 7.2; Future Conference Agenda Items

Origin: UK

Proposal:    Agenda Item for WRC-2007:

2.YY		to consider spectrum requirements for ensuring the safe control of the flight of Unmanned Air Vehicles (UAVs) including High Altitude Platforms

Background/Reason:

The use of Unmanned Air Vehicles (UAVs) in the past has been limited, with a vast majority of flights being carried out by the military.  One reason for the limited number of flights has been the heavy restrictions placed on where and when these flights can take place due to concerns over the ability of UAVs to integrate safetly with  other manned aircraft.

With advances in technology the size, payload and performance of UAVs has increased significantly.  This has brought with it a commercial realisation of the potential uses for UAVs, including High Altitude Platforms for IMT2000, that the number of flights by civil UAVs is likely to dramatically increase.

To facilitate UAV operations,  Civil Aviation Authorities will need to introduce  rules and regulations governing the use of UAVs.  One fundamental requirement for the introduction of these rules and regulations will be that command and control over the flight profile of a UAV can be maintained in all circumstances.  As part of this requirement there will be a need to identify suitable spectrum within which such command and control links can operate and for which sufficient secure protection is afforded.

Radio Services concerned:

To be determined, however it may require a new service definition

Indication of possible difficulties:

- Identifying the amount and type of spectrum required

- Identification of the protection requirements required

- The identification of suitable spectrum

Previous/on-going studies on the issue:

- No known studies

| Studies to be carried out by: | with participation of: |
| --- | --- |
| European administrations with EUROCONTROL and ICAO Europe support | ICAO other regions |

ITU-R Study Groups concerned:

Initially SG8, with a likelihood for liaison statements to other groups

ITU Resource Implications, financial Indications

Most of the studies will be conducted initially within Aviation

Preliminary CPG Position:

## Position of other Regional Bodies/Administrations

This request has been coordinated with EUROCONTROL and ICAO (AMCP/WG F)

ECP: Yes  /  No                                     Multicountry Proposal:  Yes / No

Remarks:

Proposal for an new agenda Item for WRC-2007