AMCP WGF9/WP32

Information Paper

on the

PLANNED GBAS AND VDL4 DEPLOYMENT IN EUROPE

SUMMARY

Aviation is at a transition point experiencing various changes and challenges .  For example, the ability to expand on existing systems for conventional VHF radionavigation and communication facilities is getting increasingly hard as there is little or no provision, particularly in core Europe where the spectrum is saturated.

In addition, for Radionavigation, there is a growing acknowledgement of the use of satellite navigation systems.

Aviation has outlined a strategy for Air Traffic Management (Air Traffic management Programme – Description of activities published by Eurocontrol May 2002). In the Strategy, it describes planned provisions in the 2000 to 2015 timeframe to cater for the technology changes within Communications, Radionavigation and Surveillance.

The short to medium term solution to cater for developing new concepts in Communications, Radionavigation and Surveillance, is seeing a growing requirement to move to data links and short messaging services for some of the standard functions. By using a ‘communication system’ to convey ‘radionavigation information’ or to provide ‘surveillance function’. (Both GBAS and VDL mode 4 are perfect examples of this) many functions can be carried out more optimally (both from an operations and efficiency of spectrum perspective) than over the traditional voice channel ATC techniques. Adoption of such a strategy would thus in turn relieve some the congestion in the VHF navigation and communication band and buy more time till the implementation of a longer term solution is required.

Eurocontrol has a roadmap for making some of the new services available (see attached.

It should be noted that the implementation of this roadmap requires   a regulatory provision being in place at the end of the next conference (WRC 2003) to enable the use of VDL mode 4 in the VHF Radio navigation band. (Note: GBAS is not related with the roadmap which we forwarded to you. Therefore, separate arguments should be provided for it, based on e.g. the plans of other programmes and domains)

Eurocontrol strongly supports making the necessary regulatory provisions in ITU WRC 2003 to enable the introduction of GBAS (see note above) and VDL mode 4 in the timeframe described in the attached roadmap.

THE ROADMAP

Package 1 consists of

- Ground Surveillance applications

- Airborne Surveillance applications (including Airborne Traffic situation awareness and spacing applications)

Package 2 is proposed to include:

- Enhanced Ground Surveillance/Airborne Surveillance applications from Package I

- Airborne separation applications etc.