|  | International Civil Aviation Organization WORKING PAPER | ACP-WGI12/WP-0x 04/30/10 |
| --- | --- | --- |

AERONAUTICAL COMMUNICATIONS PANEL (ACP)

TWELVETH MEETING OF THE WORKING GROUP I

Paris, France 19 – 21 May 2010

| Agenda Item x: | Maintenance of ICAO Doc 9896 |
| --- | --- |

Reservation for FANS applications over IPS for ICAO Doc 9896

(Presented by Rob Morgenstern, MITRE)

SUMMARY

This working paper proposes updates for edition 2 of ICAO Doc 9896 to reserve an Application Technology Type field entry for FANS applications over IPS for interoperability purposes.

ACTION

The working group is invited to consider the changes for incorporation into Edition 2 of Document 9896.

INTRODUCTION

The FAA Data Communications program is fielding Segment 1 capabilities for the 2013-2018 timeframe.  This capability includes FANS and ATN capabilities.  The FAA plans to utilize the ICAO Doc 9896 dialog service to communicate from their end application systems to an intermediate device which will translate to ATN or FANS as appropriate.  This simplifies end system implementation and eases the transition to an eventual IPS networking capability for air/ground.

discussion

The following changes to Doc 9896 are proposed to support the conveyance of FANS applications utilizing the ICAO Doc 9896 Dialog Service.

Amendment Proposal

| Title: | FANS application support |
| --- | --- |
| AP working paper number and date | I12/WPx 19 May 2010 |
| Document(s) Affected: | Manual on VDL Mode 2 Technical Specifications |
| Document Version: | Doc 9896 |
| Sections of Documents Affected: | Part II, Section 2.2 |
| Coordinator: | Robert Morgenstern |
| Coordinator's Address: | 7515 Colshire Drive, M/S N660 McLean, VA 22102 USA |
| Coordinator's Phone: | +1 703 983 7846 |
| Coordinator's Fax: | +1 703 983 1367 |
| Coordinator's E-mail Address: | rmorgens@mitre.org |
| Category: | NEW CAPABILITY |
| Problem description: | Allocates an available entry in the Application Technology Type field to support FANS applications over IPS for interoperability purposes. |
| Background: | Most aircraft using VDL2 are using AOA. This defines the method in the standard, so as to ensure interoperability. |
| Backwards compatibility: | YES |
| Amendment Proposal: | See below. |
| WG-M Status: | SUBMITTED 5/19/10 |

2.2.5.4.3.2	The Application Technology Type shall reserve a value of b011 to indicate “FANS/IPS DS” and have a format of (3 bits / internal / optional).

ACTION BY THE MEETING

The ACP WG-I is invited to proposed changes to ICAO Doc 9896 for Edition 2.