|  |  | ACP WG-I/15 MEETING REPORT 30 May 2012 |
| --- | --- | --- |

AERONAUTICAL COMMUNICATIONS PANEL (ACP)

WG I – Internet Protocol Suite – 15th Meeting

Bucharest, Romania, 28th - 30th May  2012

Report of ACP WGI-15 Meeting

Presented by the Secretary and Rapporteur

Table of Contents

1.	AGENDA ITEM 1: MEETING ORGANIZATIONAL ISSUES	3

2.	AGENDA ITEM 2: APPROVAL OF THE AGENDA AND REVIEW OF WG-I/13        MEETING REPORT.	3

3.	AGENDA ITEM 3: REVIEW OF ACTION ITEMS	3

4.	AGENDA ITEM 7.3: SWIM – General Discussion	4

5.	AGENDA ITEM 5: REGIONAL IP IMPLEMENTATIONS	5

6.	AGENDA ITEM 7.2:  ENTERPRISE SECURITY	6

7.	AGENDA ITEM 6:  IPS IMPEMENTATION GUIDANCE DEVELOPMENT	6

8.	AGENDA ITEM 4 – IPV6 IMPLEMENTATION PAPERS (MOBILE AND FIXED)	7

9.	AGENDA ITEM 7.3: SWIM – CONOPS OVERVIEW	9

10.	AGENDA ITEM 6.3 – SECURITY: AIR-GROUND SECURITY STANDARD  -     PROPOSED APPROACH	9

11.	AGENDA ITEM 7.1: AN CONF 12 PREPARATION	10

12.	AGENDA ITEM 10; NEXT MEETING	10

13.	APPENDIX A - ACP WGI AGENDA	11

14.	APPENDIX C LIST OF ATTENDEES	12

15.	APPENDIX D – TABLE OF ACTION ITEMS AND OUTCOMES	13

Note: This report follows the chronological order in which agenda items were discussed.

# AGENDA ITEM 1: MEETING ORGANIZATIONAL ISSUES

1.1	The meeting was opened by the Rapporteur, Liviu Popescu who proceeded to thank ROMATSA for hosting the meeting and explained the general arrangements for the meeting. In the initial discussion is was explained that although Item 7.3 (SWIM) would be dealt with the following day, it was agreed to open a general discussion on SWIM on the first day, due to the availability of attendees who would not be available later in the week.

# AGENDA ITEM 2: APPROVAL OF THE AGENDA AND REVIEW OF WG-I/13 MEETING REPORT.

2.1	A draft agenda coordinated by the Rapporteur with key members of the WG was presented and accepted by the meeting.  The agenda is in Appendix A of this report.

2.2	The meeting then proceeded to allocated WPs and IPs to agenda items. The attached agenda was updated to show these allocations.

# AGENDA ITEM 3: REVIEW OF ACTION ITEMS

3.1	Action Items were reviewed with the following outcome:

3.2	ACTION WG-I/13-08: ICAO Secretariat will work to obtain IPV6 address blocks for the Regions. Status – Remains Open

3.3	ACTION WG-I/14-01: Secretary to Refer Action Item 13-07 to WG-M and Part 2B to read Part 4B. Status – Closed.

3.4	ACTION WG-I/14-02 Secretary to modify Doc 9896 Rev 19 to include the proposed modifications to ED-137 given in WPs 6 and 7 explaining that these requirements are limited to the FAA.  This is expected to be ready for approval for publication as Edition 2 within two weeks. Status – Closed  (NOTE: This has been replaced by a new action item 15-1).

3.5	ACTION WG-I/14-03: Secretary to take appendices A and B from Section 5 of the report of the Working Group of the Whole and make these stand-alone documents. These are to be clearly identified and placed in the general repository of the ACP web-site. Status – Closed.

3.6	ACTION WG-I/14-04 Secretariat draft State Letter asking for (i) support from personnel with IPS skills and (ii) an extension to the schedule for the work programme based on the various reasons given above. In order to be effective State Letter must ask for experts to be nominated by name with details of expertise. Agenda Item 6 of this report provides more details. Status – To remain Open.

3.7	ACTION WG-I/14-05 ICAO to develop a justification for a /16 address block and make an application to ARIN or IANA based on expediency.  Agenda Item 6 of this report provides more details. Status – To remain Open.

3.8 	ACTION WG-I/14-06:  Hoang Tranh to draft guidance material for Doc 9896 on IPV4-IPV6 transition. Status – To remain  Open.

3.9 	ACTION WG-I/14-07:  Robert Witzen to draft a paper for the ACP WGW recommending a SARPS amendment changing the OSI Protocols to recommendations. Status – required amendment has been approved by the Air Navigation Commission, State Letter in preparation. This item can be Closed.

3.10	ACTION WG-I/14-08:  ICAO to apply for new TLD and draft appropriate guidance material on the allocation of lower level domain names. Status – to remain Open.

3.11	ACTION WG-I/14-09:  Secretary to capture some justifications (for the formation of a task force on SWIM) on paper and circulate to WG-I members. Once done, the Secretary to prepare a paper seeking the ACP WGW to request the ANC to approve the formation of a Task Force. Further information on this subject is given in Agenda Item 7.3 of this report. Status – to remain Open.

3.12	All action items related to global IPS resources management  (14-05, 14-08) to remain open pending outcome of the efforts to obtain support via the AN Conf 12 on securing  resources for ICAO to proceed with the administration of the key resources of ATN/IPS.

SWIM action (14-09) requires guidance from ACP on which will be the best way to address SWIM infrastructure work items. One of the options would be to extend the scope of WGI as per paragraph 4.1 below.

3.13     The meeting then proceeded to deal with papers related to Action Item 14-2. This was due to the fact that progress had overtaken the need for action item 14-2, as special provisions to support FAA requirements had been incorporated into industry standards and so did not need special treatment in the ICAO guidance material. WPs 4 and 5 provided suggested text for Document 9896 which was accepted by the meeting. This resulted in the following action item:

ACTION ITEM 15-1: Secretary to make efforts to have changes given in WPs 4 and 5 into Edition 2 of Doc. 9896. If not successful then these changes shall be used to produce Edition 3 of Doc. 9896. Secretary to report to WG-I on this within two weeks.

ACTION ITEM 15-2: Secretary to make details of Annex 10 amendment available to WG-I.

# AGENDA ITEM 7.3: SWIM – General Discussion

4.1	This item began with a general discussion on WG-I’s attention to SWIM so far, which was to consider the ACP’s potential role in SWIM standardization. In the ensuing discussion a number of key points were raised:

- How do we migrate to SWIM

- How to ensure upward compatibility with existing ACP developments

- Implementation guidance development for current deployed systems migration (e.g. AMHS, EUROCONTROL Surveillance Data Distribution System) in the context of SWIM.

- SWIM is a global effort. Consequently it is essential to maintain the appropriate standardization in ICAO

- There are various System Oriented Architecture (SOA) standards and it should be ICAO’s role to determine which should be adopted for global use.

- Management of the Security of SWIM

4.2	At meeting 14, it was agreed that a task force should be formed to evaluate SWIM and determine the ACP’s role. This resulted in ACTION ITEM 14-9, which remains open. On this subject, Jacky Pouzet (EUROCONTROL) mentioned that airline and airports personnel should participate in this. The Secretary responded that proposals of this nature should be made at the AN Conf 12. This resulted in the following action item:

ACTION ITEM 15-3: Brent Phillips to look into FAA intentions to deal with SWIM at the AN Conf 12.

4.3	Vid Patel then raise the question as to the nature and quantity of data to be exchanged between administrations. This is an important consideration as it will greatly influence the standardization task.

4.4	In the ensuing discussion it was agreed that the ACP should be proactive in this regard and approach States in order to obtain support for SWIM standards development. This resulted in the following action item:

ACTION ITEM 15-4: Secretary to draft State letter seeking support for SWIM activities.

4.5	Jacky Pouzet pointed out that with the performance-based approach now taken with standards development, ACP has been able to complete tasks in a very short time, ie: VOIP and AEROMacs, hence the work on SWIM could be completed in a reasonable time. It was proposed that ACP should launch the initiative by organizing a workshop.

# AGENDA ITEM 5: REGIONAL IP IMPLEMENTATIONS

5.1	Cosmin Dumitrescu presented IP2 describing ROMATSA’s experience in pioneering the use of IP for ATM communications. In this a number of points were made:

- Use of COTS equipment with capabilities is recommended to continuously inspect and monitor traffic through Inspection and Firewall modules.

- Determining and then monitoring traffic pattern baselines is necessary to ensure that the network is functioning correctly and that no traffic anomalies have occurred.

- It was necessary to develop monitoring software in-house as COTS products did not meet their requirements.

- Applying the most effective routing protocols is key for ensuring High performance convergence time of the whole network ( 1 sec).

- Strict Management of Multicast is needed to prevent “storms” and “ flooding”.

- Satellite back-up (VSAT) is implemented for business continuity of critical applications ( e.g. A-G VoIP )

# AGENDA ITEM 7.2:  ENTERPRISE SECURITY

6.1	Vic Patel, FAA presented NAS Information System Security (NEISS) and provided an overview high level description of the NEISS capabilities.   The NEISS emphasis is enterprise security and is designed to complement, not replace, end-system security. There will be cyber security capabilities and controls that must still be implemented by individual NAS systems.

6.2	The presentation addressed the following:

- Plans to implement a NAS Security Architecture that is based on Enterprise or “Common” Controls rather than the current system-by-system control

- Plans that all NAS and NextGen Programs interface to and use the Common Controls to gain the mitigation benefits

- The five Common Controls that comprise NEISS

6.3	The presentation covered aviation Changing Environment Increases, Cyber Security Risks to the NAS and Potential Impacts to NAS, the Threat, and The Challenge.  The presentation addressed why NAS Enterprise Information System Security (ISS) Architecture is needed.  This discussion covered the following:

- Growing and evolving cyber security threats

- Evolution to support and enable NextGen

- Security is based around individual systems

- What Architecture will provide

- Benefits

  - Five fundamental capabilities each with a specific security purpose were discussed.

- The External Boundary Protection (EBP) capability is designed to keep malware from entering the secured NAS and to limit the effects of distributed denial of service attacks within the secured NAS.

- 2.	The Internal Policy Enforcement (IPE) capability inhibits the spread of any cyber damage within the secured NAS.

- The Incident Detection and Response (IDR) capability detects cyber- compromised systems within the secured NAS and provides a response based on the type of intrusion.

3.	The Certified Software Management (CSM) capability ensures that malware does not enter the NAS via the software supply chain.

4.	The Identity and Key Management (IKM) capability provides an identity Verification system for all components within the NAS (human or machine) that participates in data transfers. Such verification is a crucial tool used by the previous four capabilities.

5.	Governance and Policy for NEISS Establishing policy, procedures, roles and responsibilities for implementing the NAS Enterprise Information System Security (NEISS) Architecture was discussed.  The discussion also covered Challenges and Implementation Alternatives

# AGENDA ITEM 6:  IPS IMPEMENTATION GUIDANCE DEVELOPMENT

7.1	The Secretary presented IP05 which provided details of an informal group dealing with cyber-security known as the Joint Coordination Group (JCG). The purpose of this was to:

- outline the involvement of the JCG with the ICAO Aviation Security (AVSEC) Group and

- explain how the ACP could exploit the JCG interest in Network Security to lobby States to recommend at AN Conf 12 that ICAO provide the resources needed by the ACP to complete its work on IPS guidance and implementation. This includes funding (to obtain an address block and domain names) and personnel with the required skill set.

7.2	As the JCG proposes the establishment of a task force to coordinate cyber-security, various members of WG-I expressed strong concern that:

- ACP WGI/M groups are already dealing with these subjects

- the task force will duplicate the work of the ACP and

- there was a risk of invalidating the work of the ACP thus far if different standards were selected.

7.3	On the latter point, the Secretary explained that he would provide the JCG with an inventory of the work done by the ACP on network security thus far and advise them that this would serve as a baseline for future requirements.

7.4	Some members expressed the view that the benefit of this approach was not clear and was competing with previously agreed WGI action 14-04. This led to the following action item:

ACTION ITEM 15-5: Secretary to develop short explanation of the approach to be used with the JCG to obtain additional resources to assist the ACP with the development of IPS guidance material. This shall be pursued in parallel with the actions agreed at WG-I/14. This shall be distributed to members of WG-I within two weeks.

# AGENDA ITEM 4 – IPV6 IMPLEMENTATION PAPERS (MOBILE AND FIXED)

8.1	Surveillance Data Distribution Systems

Johannes De Haan of EUROCONTROL presented IP03 on the IP platform used to support the distribution of surveillance data by EUROCONTROL. The key aspect of this was not the distribution of data as such but the security provided by the system. Some salient point from the paper were;

- The system also covers datalink distribution.

- It also support SOA services such as Publish/Subscribe and Request/Reply.

- It provides stateless and stateful security as needed.

- Acts as a gateway between different national systems, ie: IPV6 vs IPV4, multicast vs unicast.

  - As mentioned security is a key function of the system however it was pointed out that the surveillance data itself is not protected as it has such a short lifetime. The security provides protection for the system management software and hardens the system against intrusions, through spoofing and other techniques. It was pointed out that the system protects against a set of threats from the BSI threat catalogue. These were chosen based on their relevance to the surveillance environment.

  - When the Surveillance Data Distribution System (SDDS) development project started, it became apparent that a lot of functions in this system were similar with other message communication systems (air-ground data link, meteo services and AMHS). This resulted in the a platform architecture that not only can be used for surveillance data, but practically any IP based message communication system. The domain specific applications are integrated in the form of plug-ins.

  - The layered structure of the platform allows re-use of components without or with very limited adaptations. This will reduce development, validation and certification cost and improve harmonisation. In addition to this, the use of open protocols at the infrastructure side (SNMP for monitoring and control and XML for configuration) ensures easy integration in the centre infrastructures.

  - The platform is fully Service Oriented, supporting publish/subscribe as well as request/reply mechanisms. This ensures SWIM compatibility.Currently the software and documents are available free of charge only to EUROCONTROL member states and organisations. The release outside of the EUROCONTROL area is under investigation. All aviation stakeholders are invited to submit ideas and requests for the development of new plug-ins.

8.6	In response to the questions that followed the presentation it was clarified that:

- SDDS was developed independently from PENS. It can use any IP infrastructure. First tests of SDDS sending surveillance data via PENS are scheduled in the beginning of June 2012

- SDDS security assessment was guided by a document from the German Federal Agency for IT System Security BSI. NIST - 53 could be used for the SDDS. It is expected that the BSI and NIST security assessment specifications are very similar in scope and approach.

- The security assessment was done by a group of ANSP representatives in the context of the EUROCONTROL Surveillance Distribution Requirements Group (SDDR-G). The outcome was a document that was used by the main SDDS contractor to do the security assessment. The assessment was reviewed by the EUROCONTROL project team.

- In relation with continuous security monitoring SDDS has a requirement that requires that every breach of the security requirements has to be reported to the user. All security relevant components (switches, routers and servers) will send a trap to the operator position if a security breach is detected. The SDDS release policy foresees the delivery of security related patches on a quarterly basis.

- IPv4-IPv6 transition was one of the main objectives for the SDDS. It can act as a gateway between IPv4 and IPv6 domains.

- Practically any message based IP communication can be handled by the SDDS by developing a domain specific plug-in. The API for the plug-in development is open. Multiple plug-ins can run on a single server, but give the relatively low cost of hardware it is recommended to use separate servers for each plug-in especially if performance is important

# AGENDA ITEM 7.3: SWIM – CONOPS OVERVIEW

9.1	 Marc Brochard - EUROCONTROL presented the state of play of System Wide Information Management (SWIM) development and early adoption in Europe. This information was supported by an Information paper which was already presented at the last AFSG meeting (Paris - April 2012). The Group noted that an initial SWIM Concept of Operation (ConOps) was produced by SESAR programme. This provides a clear definition of SWIM Building Blocks.

9.2	The Group noted that implementation of SWIM wouldn’t be a big-bang replacement of the existing ATM environment, but rather an evolutionary process based on a gradual transition towards a service oriented ATM system. It was noted that the move towards SWIM implementation can start by implementing AIXM and WXXM and being Service Oriented Architecture compliant (by developing services).

9.3	The Group noted that SWIM was one of the cornerstones of the ICAO ASBU programme to be presented and discussed at the 12th AN Conf in November 2012. The Group agreed that following the outcomes of the 12th AN Conf, further refinement and consolidation of the regional documentation would be required. The Secretary would keep the Group informed about these developments and provide a comprehensive report on the outcomes of the 12th AN Conf to the next meeting.

9.4	Following the presentation, questions were raised on the first SWIM application considered, on the ICAO activities related to SWIM A-G and on the PENS capabilities to support SWIM applications. It was explained that SWIM currently started with MET and Flight Information Domain related applications. Standardisation at ICAO level will be required. The A-G component of SWIM is being considered however no standards are available now. PENS already deploys EAD and Network Management   (CFMU) applications and will support future SWIM evolutions

# AGENDA ITEM 6.3 – SECURITY: AIR-GROUND SECURITY STANDARD  - PROPOSED APPROACH

10.1	Vid Patel presented WP06 intended for WG-M#19 to the meeting as this was of interest to the group. This paper outlined the Secure Dialogue Service which will be proposed as the security solution for the ATN using OSI. Some key advantages of this approach are as follows:

- The solution will facilitate the implementation of Security over  OSI and is consistent with IPS security requirements.

- It resides between the upper layers and the application thus eliminating the need for security provisions in the application or layers of the communication stack.

- Its implementation is optional thus providing backward compatibility with existing implementations ( e.g. Link 2000+)

10.2	This approach was well regarded by the meeting. It was further pointed out that the changes to Doc 9880 were expected to be completed by the end of this year and validation to be completed by mid-2013.

# AGENDA ITEM 7.1: AN CONF 12 PREPARATION

11.1 	The Secretary provided a presentation on the Aviation System Block Upgrades, the supporting Roadmaps and the fourth edition of the Global Air Navigation Plan. The following is a summary of the presentation:

- The block upgrades and roadmaps were developed by a broad group including

Representatives from NextGen and SESAR, airlines, airframe manufacturers, industry-standards bodies and other industry groups.

- The resulting block upgrades and component modules went through a three stage review by the global civil aviation community.

- The modules represent operational improvements which will be available for implementation at milestones separated by five years.

- Many of the modules provide a phased implementation of an operational capability.

- The block milestone dates represent the time that all provisions (technology, procedures, regulatory approvals, business case etc. ) will be in place to allow implementation to take place.

- Implementation of modules is not mandatory but shall be determined based on a needed performance improvement.

- The roadmap technologies which support the block upgrade modules as well as legacy technologies which have a general application.

- The next edition of the Global Air Navigation Plan (GANP) will be based on the Block Upgrades and supporting roadmaps. The (GANP) will have guidelines to allow the PIRGS to maintain and update their regional air navigation plans.

- The FASID will exist in electronic (on-line) form and will be updated via a Performance Framework Form which has been updated to accommodated the ASBU modules.

- Implementation by the Regions will be monitored and published each year in a Global Air Navigation Report.

# AGENDA ITEM 10; NEXT MEETING

It was tentatively agreed that the next meeting would take place during the week beginning January 21st, 2013. This remains tentative until agreed by WG-M. This is necessary as the two meetings are held consecutively. The tentative meeting location will be ICAO Headquarters in Montreal unless another organisation is willing to host the meeting and also fund travel for ICAO Secretariat staff.

POST-MEETING NOTE: It was decided at WG-M that the consecutive WG-M/WG-I meetings would be held over Jan 23-30 with WG-I meeting from Jan 28-30.

# APPENDIX A - ACP WGI AGENDA

AERONAUTICAL COMMUNICATION PANEL

FIFTEENTH MEETING OF WORKING GROUP - I

Bucharest, Romania 28 – 30 May 2012

Proposed Agenda

WG-I Proposed Agenda:

- Meeting Organisational Issues

- Approval of the Agenda & Review of WG-I/14 Meeting Report

- Review of Action Items and Items for Follow-Up.

- IPv6 implementation papers (Mobile and Fixed)

- Regional IP implementations (need input from ICAO regional secretariats)

- IPS implementation guidance development

  - IPv6 Addressing

  - IPV4- IPV6 transition

  - Security - Air-Ground Security Standard – Proposed approach

  - DNS Naming

- Any Other Business

  - ANC-12 Preparation Discussion

    - Roadmaps and Supporting IP

  - Enterprise Security Capabilities

  - SWIM

- Next meeting

# APPENDIX C LIST OF ATTENDEES

ACP WGI-14 – Montreal, Canada: 18th – 20th July 2011

LIST OF ATTENDEES

| NAME | ORGANIZATION NAME | E-MAIL |
| --- | --- | --- |
| Liviu Popescu | EUROCONTROL Rapporteur | liviu.popescu@eurocontrol.int |
| Maiolla, Vaughn | ICAO Panel Secretary | vmaiolla@icao.int |
| Cosmin Dumitrescu | ROMATSA | cosmin.dumitrescu@romatsa.ro |
| Brent Phillips | FAA | Brent.phillips@faa.gov |
| Attayde Frauche | DECEA (Brazil) |  |
| Jacky Pouzet | EUROCONTROL | jacky.pouzet@eurocontrol.int |
| Jean-Marc Vacher |  |  |
| Pierre |  |  |
| Vic Patel | FAA | Vidyut.patel@faa.gov |
| Stephane Tamelet | AIRBUS |  |
| Johannes De Haan | EUROCONTROL |  |
| Marc Brochard (remote only) | EUROCONTROL |  |
| Mike Olive | Honeywell | Mike.olive@honeywell.com |

# APPENDIX D – TABLE OF ACTION ITEMS AND OUTCOMES

| Action Item | Description | Status |
| --- | --- | --- |
| 13-8 | ICAO Secretariat will work to obtain IPV6 address blocks for the Regions. | OPEN – In progress. |
| 14-4: | Secretariat draft State Letter asking for (i) support from personnel with IPS skills and (ii) an extension to the schedule for the work programe based on the various reasons given above. In order to be effective State Letter must ask for experts to be nominated by name with details of expertise. | Secretary |
| 14-5: | ICAO to develop a justification for a /16 address block and make an application to ARIN or IANA based on expediency. | Secretary |
| 14-6: | Hoang Tranh to draft guidance material for Doc 9896 on IPV4-IPV6 transition. | Hoang Tranh |
| 14- 8: | ICAO to apply for new TLD and draft appropriate guidance material on the allocation of lower level domain names. | ICAO |
| 14-9: | Secretary to capture some justifications on paper and circulate to WG-I members. Once done, the Secretary to prepare a paper seeking the ACP WGW to request the ANC to approve the formation of a Task Force. | Secretary |
| 15-01: | Secretary to make efforts to have changes given in WPs 4 and 5 into Edition 2 of Doc. 9896. If not successful then these changes shall be used to produce Edition 3 of Doc. 9896. Secretary to report to WG-I on this within two weeks. | Secretary |
| 15-02: | Secretary to make details of Annex 10 amendment available to WG-I. | Secretary |
| 15-03: | Brent Phillips to look into FAA intentions to deal with SWIM at the AN Conf 12. | Brent Phillips |
| 15-04: | Secretary to draft State letter seeking support for SWIM activities. | Secretary |
| 15-05: | Secretary to develop short explanation of the approach to be used with the JCG to obtain additional resources to assist the ACP with the development of IPS guidance material. This shall be pursued in parallel with the actions agreed at WG-I/14. This shall be distributed to members of WG-I within two weeks. | Secretary |

Items for Follow-Up at WG-I/14

| Item | Description | Status |
| --- | --- | --- |
| 14-1: | WG-I to consider architecture for DNS Network and Security. | On-going |
| 14-2: | ACP to consider the development of a suitable architecture to support SWIM. (This is subject to resolution of SWIM related actions from WG-I/15) | On-going |
| 15-1: | Information from ROMATSA on IP network implementation and management covered in IP02 under Agenda Item 5 to be taken into account when developing guidance material on ATN/IPS implementation | On-going |
| 15-2 | Information from EUROCONTROL in SDDS given in IP03 under agenda item 4 5 to be taken into account when developing guidance material on ATN/IPS implementation | On-going |

# Text boxes

Summary

This document is the ACP WGI-15 Meeting Report.