ICAO

Aeronautical Telecommunication Network (ATN)

Manual for the ATN using IPS Standards and Protocols (Doc 9896)

Prepared by: ICAO ACP WG-I

August 25, 2008

Version 14b

FOREWORD

This document defines the requisite data communications protocols and services to be used for implementing the International Civil Aviation Organization (ICAO) Aeronautical Telecommunications Network (ATN) using the Internet Protocol Suite (IPS). The material in this document is to be considered in conjunction with the relevant Standards and Recommended Practices (SARPs) as contained in Annex 10, Volume III, Part I Chapter 3.

Editorial practices in this document.

The detailed technical specifications in this document that include the operative verb “shall” are essential to be implemented to secure proper operation of the ATN.

The detailed technical specifications in this document that include the operative verb “should” are recommended for implementation in the ATN.  However, particular implementations may not require this specification to be implemented.

The detailed technical specifications in this document that include the operative verb “may” are optional. The use or non use of optional items shall not prevent interoperability between ATN/IPS nodes.

The Manual for the ATN using IPS Standards and Protocols is divided into the following parts:

Part I – Detailed Technical Specifications

This section contains general description of Internet Protocol Suite (IPS) communications including information on user requirements.  Information on institutional guidelines to IPS services and the Standards and Recommended Practices (SARPS).

Part II – IPS Applications

This section contains general description of IPS applications, possible implementations of IPS DS and examples of  IPS applications being supported by ICAO Annex 10 material.

Part III – Guidance Material

This section contains guidance material on IPS communications including information on potential operational benefits, architectures, IPS addressing plan, AS numbering plan and general information on IPS implementation.

ICAO

Aeronautical Telecommunication Network (ATN)

Manual for the ATN using IPS Standards and Protocols (Doc 9896)

Part I

Detailed Technical Specifications

PART 1 TABLE of contents

1.0 INTRODUCTION	1

1.1 General Overview	1

2.0 REQUIREMENTS	3

2.1 ATN/IPS ADMINISTRATION	3

2.1.1 The ATN/IPS	3

2.1.2 Administrative Domains	3

2.2 PHYSICAL LAYER & LINK LAYER REQUIREMENTS	3

2.3 NETWORK LAYER REQUIREMENTS	3

2.3.1 IPv6 Networking	3

2.3.2 Network Addressing	4

2.3.3 Inter-Domain Routing	4

2.3.4 Error Detection and Reporting	5

2.3.5 Quality of Service (QoS)	5

2.4 TRANSPORT LAYER REQUIREMENTS	6

2.4.1	End to End Services	6

2.4.2	Support Services	6

2.4.3 Transmission Control Protocol (TCP)	6

2.4.4 User Datagram Protocol (UDP)	6

2.5 SECURITY	6

2.5.1  Ground-Ground  Security	6

2.5.1.1  Ground-Ground IPsec/IKEv2	6

2.5.2 Air-Ground Security	7

2.5.2.1  Air-Ground Access Network Security	7

2.5.2.2  Air-Ground IPsec/IKEv2	7

2.5.2.3  Air-Ground Transport Layer Security	8

2.5.2.4  Air-Ground Application Layer Security	8

TABLE of Figures

Figure 1 – IPS Architecture in the ATN	1

# 1.0 INTRODUCTION

## 1.1 General Overview

This manual contains the minimum communication protocols and services that will enable implementation of an ICAO Aeronautical Telecommunication Network (ATN) based on the Internet Protocol Suite (IPS) utilizing Internet Protocol version 6 (IPv6).

Implementation of IPv4 in ground networks, for transition to IPv6 ground networks (or as a permanent network) is a local issue, and is not addressed in this manual.  IPv6 is to be implemented in air-ground networks.  The scope of this manual is on interoperability across administrative domains in the ATN/IPS internetwork, although the material in this manual can also be used within an Administrative Domain.

The IPS in the ATN architecture is illustrated in Figure 1.

Figure 1 – IPS Architecture in the ATN

In accordance with Annex 10, Volume III, Part I, paragraph [3.3.3] implementation of the ATN/IPS, including the protocols and services included in this manual, will take place on the basis of regional air navigation agreements between ICAO contracting States.  Regional planning and implementation groups (PIRG’s) are coordinating such agreements.

# 2.0 REQUIREMENTS

## 2.1 ATN/IPS ADMINISTRATION

### 2.1.1 The ATN/IPS

2.1.1.1	The ATN/IPS internetwork consists of IPS nodes and networks operating in a multinational environment.  The ATN/IPS internetwork is capable of supporting Air Traffic Service Communication (ATSC) as well as Aeronautical Industry Service Communication (AINSC), such as Aeronautical Administrative Communications (AAC), Aeronautical Passenger Communication (APC) and Aeronautical Operational Communications (AOC).

2.1.1.2 In this manual an IPS node is a device that implements IPv6. There are two types of IPS nodes in the ATN.

- An IPS Router is an IPS node that forwards Internet Protocol (IP) packets not explicitly addressed to itself.

- An IPS host is an IPS node that is not a router.

### 2.1.2 Administrative Domains

2.1.2.1	From an administrative perspective, the ATN/IPS internetwork consists of a number of interconnected Administrative Domains (AD).  An Administrative Domain can be an individual State, a group of States (e.g., an ICAO Region), an Air Communications Service Provider (ACSP),  an Air Navigation Service Provider (ANSP), or other organizational enty that manages ATN/IPS network resources and services.

2.1.2.2	Each Administrative Domain participating in the ATN/IPS internetwork shall operate one or more IPS routers which execute the inter-domain routing protocol specified in this manual.

2.1.2.3 From a routing perspective, inter-domain routing protocols are used to exchange routing information between Autonomous Systems (AS), where an AS is a connected group of one or more IP prefixes.  The routing information exchanged includes IP address prefixes of differing lengths depending on the type of AD. For example, an IP address prefix exchanged between ICAO regions may have a shorter length than an IP address prefix exchanged between individual states within a particular region.

2.1.2.4 Administrative Domains shall coordinate their policy for carrying transit traffic with peer Administrative Domains.

2.1.2.5 IP layer mobility in the ATN/IPS is based on IPv6 mobility standards. Mobile IPv6 permits mobile nodes (MN) (i.e., aircraft in the ATN/IPS) to communicate transparently with correspondent nodes (CN) (i.e., ground automation systems in the ATN/IPS) while moving within or across Air-Ground Access Networks.

2.1.2.6 A Mobility Service Provider in the ATN/IPS is a service provider that provides Mobile IPv6 service (i.e., Home Agents), within the ATN/IPS.  An MSP in the ATN/IPS is an instance of an AD which may be an ACSP, ANSP, Airline, Airport Authority, government or other aviation organization.

## 2.2 PHYSICAL LAYER & LINK LAYER REQUIREMENTS

2.2.1	The specification of the physical and link layer characteristics for a node is local to the interfacing nodes.

2.2.2 IPS nodes should implement the RObust Header Commpression Framework (

ROHC) as specified in RFC 4995.

2.2.3  IF ROHC is supported, then the following ROHC profiles should be supported as applicable:

a.  the ROHC profile for TCP/IP specified in RFC 4996

b.  the ROHC profile for RTP/UDP/ESP specified in RFC 3095

c.  the IP-Only ROHC profile specified in RFC 4843

d.  the ROHC over PPP profile specified in RFC 3241

## 2.3 NETWORK LAYER REQUIREMENTS

### 2.3.1 IPv6 Internetworking and Mobility

2.3.1.1 IPS nodes in the ATN shall implement IPv6 as specified in RFC-2460.

2.3.1.2 IPS nodes shall implement IPv6 Maximum Transmission Unit (MTU) path discovery as specified in RFC-1981.

Commentor’s note:  Max Ehammer has noted the following; “This protocol might introduce unnecessary delays, especially for larger packets and might was (precioius wireless) bandwidth.  Therefore, I would suggest to set the IPv6 maximum MTU to 1280 octets.  This is the value each link (which transports IPv6) has to support.  I guess ATN application data packets are rearely larger than this value.  Of course in the gorund-ground network it’s a different story”  The WG may address this in the next meeting.

2.3.1.3 IPS nodes shall set the flow label field to zero, since it is not used in the ATN.

2.3.1.4 IPS mobile nodes shall implement Mobile IPv6 as specified in RFC-3775.

2.3.1.5 IPS home agents shall implement Mobile IPv6 as specified in RFC 3775.

Commentors note:  This is more than was previously agreed to; however, it follows from the introduction of an MSP as an administrative entity.  The WG can decide to leave in or delete)

2.3.1.6 IPS mobile nodes and home agents may implement extensions to Mobile IPv6 to enable support for network mobility as specified in RFC 3963.

2.3.1.7 IPS correspondent nodes that implement Mobile IPv6 route optimization shall allow route optimization to be administratively enabled or disabled with the default being disabled.

Note.- Mobile IPv6 route optimization is not mandated by this specification as new solutions are expected as a result of IETF chartered work which includes aviation requirements.

### 2.3.2 Network Addressing

2.3.2.1	IPS nodes shall implement IP Version 6 Addressing Architecture as specified in RFC-4291.

2.3.2.2	IPS nodes shall use globally scoped IPv6 addresses when communicating over the ATN/IPS.

2.3.2.3	Administrative Domains shall obtain IPv6 address prefix assignments from their local internet registry or regional internet registry.

2.3.2.4 MSPs shall obtain an /32 IPv6 address prefix assignment for the exclusive use of IPS mobile nodes.

2.3.2.5 MSP’s should use the following IPv6 address structure, for aircraft assignments.

Note 1: Under this structure each aircraft constitutes a /56 IPv6 end site, which is based on the ICAO 24 bit aircraft address, as defined in Annex 10 vol 3, appendix to chapter 9.

Note 2: An aircraft may have different subnets for different services (ATS, AOC, AAC,  etc.) or may have different MSPs for different services.

2.3.2.4 Mobility Service Providers (MSPs), shall advertise their /32 aggregate prefix to the ATN/IPS.

### 2.3.3 Inter-Domain Routing

2.3.3.1 IPS routers which support inter-domain dynamic routing shall implement the Border Gateway Protocol (BGP4) as specified in RFC-4271.

2.3.3.2 IPS routers which support inter-domain dynamic routing shall implement the BGP-4 Multiprotocol Extensions as specified in RFC-2858.

2.3.3.3 Administrative Domains shall obtain AS numbers for ATN/IPS routers that implement BGP-4.

2.3.3.4 AD domains that use a private ASN shall follow the AS numbering plan described in Part 3 of this document.

Note: ADs that require additional private AS numbers should coordinate through ICAO.

2.3.3.4	IPS routers which support inter-domain dynamic routing should authenticate routing information exchanged between them.

Note 1.— Inter-domain routing protocols are used to exchange routing information between autonomous systems(AS).  The routing information exchanged includes IP address prefixes of differing lengths. For example, an IP address prefix exchanged between ICAO regions will have a shorter length than an IP address prefix exchanged between individual states within a particular region.

Note 2.— For routing purposes, an Autonomous System has a unique identifier called an AS number.

Note 3.— The routing protocol within an Autonomous System is a local matter determined by the managing organization.

### 2.3.4 Error Detection and Reporting

2.3.4.1 IPS nodes shall implement Internet Control Message Protocol (ICMPv6) as specified in RFC-4443.

### 2.3.5 Quality of Service (QoS)

2.3.5.1	AD shall provide the required class of service to support the operational requirements.

2.3.5.1.1 Administrative domains shall make use of Differentiated Services as specified in RFC2475 as a means to provide Quality of Service (QoS) to ATN/IPS applications and services.

2.3.5.1.2 AD supporting Voice over IP services shall assign those services to the Expedited Forwarding (EF) Per-Hop Behavior (PHB) as specified by RFC3246.

2.3.5.1.3 AD shall assign ATN application traffic to the Assured Forwarding (AF) Per hop Behavior (PHB) as specified by RFC2597.

Note 1:  This provision is applicable to applications as defined in Annex 10.

Note 2: Assured forwarding allows the ATN/IPS operator to provide assurance of delivery as long as the traffic does not exceed the subscribed rate. Excess traffic has a higher probability of being dropped if congestion occurs.

2.3.5.1.4 Any measures of priority applied to the AF classes shall be based on the ATN mapping of priorities defined in Annex 10, Volume III, Part I, Table 1.

## 2.3.6 IPv4 to IPv6 Transition

2.3.7.1 Administrative Domains should use the dual IP layer mechanism as described in RFC 4213.

## Note 1. -- This provision ensures that ATN/IPS hosts also support IPv4 for backwards compatibility with  local IPv4 applications

## 2.4 TRANSPORT LAYER REQUIREMENTS

### 2.4.1	End to End Services

2.4.1.1	The transport layer provides end-to-end service between IPS hosts.

### 2.4.2	Support Services

2.4.2.1	The transport layer supports the following types of services: Connection-Oriented (CO), invoking TCP or Connection-Less (CL), invoking UDP

### 2.4.3 Transmission Control Protocol (TCP)

2.4.3.1	IPS hosts shall implement Transmission Control Protocol (TCP) as specified in RFC-793.

2.4.3.2	IPS hosts may implement TCP Extensions for High Performance as specified in RFC-1323.

2.4.3.3 IPS hosts may implement RFC-2488 when operating over satellite links.

### 2.4.4 User Datagram Protocol (UDP)

2.4.4.1	IPS hosts shall implement User Datagram Protocol as specified in RFC-768.

## 2.5 SECURITY

2.5.1 This section contains provisions for ground-ground and air-ground security in the ATN/IPS.  The IPS node provisions in this section are mandatory to implement but their actual use is to be based on a system threat and vulnerability analysis.

### 2.5.2 Ground-Ground Security

2.5.2.1 Network layer security in the ground-ground ATN/IPS internetwork is implemented using Internet Protocol security (IPsec) and the Internet Key Exchange (IKEv2) protocol.

#### 2.5.2.1 Ground-Ground IPsec/IKEv2

2.5.2.1.1 IPS nodes in the ground-ground environment shall implement the Security Architecture for the Internet Protocol as specified in RFC 4301

2.5.2.1.2. IPS nodes in the ground-ground environment shall implement the IP Encapsulating Security Payload (ESP) protocol as specified in RFC 4303.

2.5.2.1.3 IPS nodes in the ground-ground environment may implement the IP Authentication Header (AH) protocol as specified in RFC 4302.

2.5.2.1.4 IPS nodes in the ground-ground environment shall implement the Internet Key Exchange (IKEv2) protocol as specified in RFC 4306.

2.5.2.1.5 IPS nodes in the ground-ground environment shall implement the Cryptographic Algorithm Implementation Requirements for the Encapsulating Security Payload (ESP) and Authentication Header (AH) as specified in RFC 4835.

2.5.2.1.6 IPS nodes in the ground-ground environment shall implement the Null Encryption Algorithm  as specified in RFC 4305, but not the Null Authentication Algorithm.

Note - ESP encryption is optional, but authentication is always performed.

2.5.2.1.7 IPS nodes in the ground-ground environment shall implement the Cryptographic Algorithms for Use in the Internet Key Exchange Version 2 (IKEv2) required algorithms for key exchange as specified in RFC 4307.

\

2.5.2.1.8  IPS nodes in the ground-ground environment which use digital signatures for authentication shall use the Internet X.509 Public Key Infrastructure Certificate and Certificate Revocation List (CRL) Profile as specified in RFC 5280.

2.5.2.1.9  IPS nodes in the ground-ground environment which use digital signatures for authentication shall use the Internet X.509 Public Key Infrastructure Certificate Policy and Certificate Practices Framework as specified in RFC 3647.

### 2.5.3 Air-Ground Security

#### 2.5.3.1 Air-Ground Access Network Security

2.5.3.1.1 IPS mobile nodes shall implement the security provisions of the access network, to enable access network security.

Note. – For example, the WiMAX, 3GPP, and 3GPP2 access networks have authentication and authorization provisions.

#### 2.5.3.2 Air-Ground IPsec/IKEv2

2.5.3.2.1 IPS nodes in the air-ground environment shall implement the Security Architecture for the Internet Protocol as specified in RFC 4301.

2.5.3.2.2 IPS nodes in the air-ground environment shall implement the IP Encapsulating Security Payload (ESP) protocol as specified in RFC 4303.

2.5.3.2.3 IPS nodes in the air-ground environment shall implement ESP with the following transforms:

- AUTH_HMAC_SHA2_256-128 as the integrity algorithm for ESP authentication as specified in RFC 4868,

- AES-GCM with an 8 octet ICV and with a key length attribute of 128 for ESP encryption with authentication as specified in RFC 4106 if encryption is supported

2.5.3.2.4    IPS nodes in the air-ground environment shall implement the Internet Key Exchange (IKEv2) Protocol as specified in RFC 4306.

2.5.3.2.5   IPS nodes in the air-ground environment shall implement IKEv2 with the following transforms:

- PRF_HMAC_SHA_256 as the pseudo-random function as specified in RFC 4868.

- 233-bit random ECP group for Diffie-Hellman Key Exchange values as specified in RFC 4753.

- ECDSA with SHA-256 on the P-256 curve as the authentication method as specified in RFC 4754.

- AES CBC with 128-bit keys as the IKEv2 encryption transform as specified in RFC 3602.

- HMAC-SHA-256-128 as the IKEv2 integrity transform as specified in RFC 4868.

2.5.3.2.6  IPS nodes in the air-ground environment shall use the Internet X.509 Public Key Infrastructure Certificate and Certificate Revocation List (CRL) Profile as specified in RFC 5280.

2.5.3.2.7  IPS nodes in the air-ground environment shall use the Internet X.509 Public Key Infrastructure Certificate Policy and Certificate Practices Framework as specified in RFC 3647.

Note. –  The Air Transport Association (ATA) Digital Security Working Group (DSWG) has developed a Certificate Policy (ATA Specification 42) for use in the aviation community. ATA Specification 42 includes certificate and CRL profiles that are suitable for aeronautical applications and interoperability with an aerospace industry PKI bridge.  These profiles provide greater specificity than, but do not conflict with, RFC 5280.

2.5.3.2.8 IPS nodes in the air-ground environment, shall implement Mobile IPv6 Operation with IKEv2 and the Revised IPsec Architecture as specified in RFC 4877.

#### 2.5.3.3 Air-Ground Transport Layer Security

2.5.3.3.1 IPS mobile nodes and correspondent nodes may implement the Transport Layer Security (TLS) protocol as specified in RFC 4346.

2.5.3.3.2 IPS mobile nodes and correspondent nodes shall implement the Cipher Suite TLS_ECDH_ECDSA_WITH_AES_128_CBC_SHA as specified in RFC 4492 when making use of TLS.

#### 2.5.3.4 Air-Ground Application Layer Security

2.5.3.4.1 IPS mobile nodes and correspondent nodes may implement application layer security at the IPS Dialogue Service Boundary.

2.5.3.4.2 IPS mobile nodes and correspondent nodes shall append an HMAC keyed message authentication code as specified in RFC 2104 using SHA-256 as the cryptographic hash function when application layer security is used.

2.5.3.4.3 A HMAC tag truncated to 32 bits shall be computed over the User Data concatenated with a 32-bit send sequence number for replay protection when application layer security is used.

2.5.3.4.2 IKEv2 shall be used for key establishment as specified in section 2.6.2.2 when application layer security is used.

ICAO

Aeronautical Telecommunication Network (ATN)

Manual for the ATN using IPS Standards and Protocols (Doc 9896)

Part II

IPS Applications

Part II Table of Contents

1.0 INTRODUCTION	3

1.2 Objective	3

2.0 Legacy ATN Applications	3

2.1 Legacy ATN/OSI Applications, using IPS	3

2.1.1 Support for CPDLC	3

2.1.2 Support for CM	3

2.1.3 Air-Ground Applications over ATN IPS	4

2.1.4 Parameters of the ATNPKT	5

2.2 Ground-Ground Applications	6

2.2.1 ATSMHS	6

2.2.2 AIDC	6

2.2.3 Voice over Internet Protocol (VoIP)	6

2.2.3.1 Standards and Protocols	7

2.2.3.1.1 H323	7

2.2.3.1.1.1 Multimedia	1

2.2.3.1.1.2 Data Transfer	1

2.2.3.1.1.3 Signalling	1

2.2.3.1.2 MGCP/MEGACO	2

3.0 Application Services	4

3.1 IPS DS	4

3.1.1 Services and Primitives	5

3.1.2 Protocol	6

3.1.3 Packet Format	7

3.1.4 ATNPKT Version	8

3.1.5 DS Primitive	8

3.1.6 Content Type	8

3.1.7 Content Version	9

3.1.8 Called Peer ID	9

3.1.9 Calling Peer ID	9

3.1.10 Security Requirements	9

3.1.11 Reject Source	9

3.1.12 Result	9

3.1.13 Application Technology Type	9

3.1.14 User Data Length	10

3.1.15 User Data	10

3.1.16 Multiple Application Instantiations	10

3.2 OLDI	11

3.3 FMTP	11

3.3.1 Testing OLDI/FMTP	12

# 1.0 INTRODUCTION

### 1.2 Objective

Add text

# 2.0 Legacy ATN Applications

Note . – Legacy ATN applications are defined in Doc 9705 and/or Doc 9880. The ATN applications described in Doc 9705/9880 specify the use of the ATN/OSI layers for lower layer communications, termed the Internet Communication Services. This section indicates how those applications interface with the ATN/IPS.

## 2.1 Legacy ATN/OSI Applications, using IPS

Note 1. – In order to accommodate legacy ATN/OSI air-ground applications over the IPS, the following IP header definition is used.  Parameters from the ATN/OSI Dialogue Service (DS) will be mapped as detailed in the sections below.  This mapping supersedes the ULCS specification of ICAO Doc 9705 and Doc 9880.

Note 2. – Either TCP or UDP may be used with the ATNPKT header format.

### 2.1.1 Support for CPDLC

IPS hosts that support the ATN/OSI Controller-Pilot Data Link (CPDLC), Automatic Dependent Surveillance (ADS) and Flight Information Services (FIS) applications shall comply to Doc 9705 or Doc 9880.

### 2.1.2 Support for CM

IPS hosts that support the ATN/OSI Context Management (CM) application shall comply to Doc 9880.

Note 1. – This is in order to allow passing the new IPS addressing information contained in the updated CM application ASN.1

### 2.1.3 Air-Ground Applications over ATN IPS

To operate the air-ground applications over ATN IPS, IPS hosts shall make use of the ATNPKT header format as defined in 1.

Figure 1.  ATNPKT Format

### 2.1.4 Parameters of the ATNPKT

The parameters of the ATNPKT header shall be mapped to the application DS parameters as shown in the following tables.

Note. – This parameter mapping applies for both sending and receiving application data to/from peer IPS systems.

| D-START |
| --- |
| Parameter | TCP/UDP/IP/ATNPKT parameter | Comments |
| Called Peer ID | ATNPKT Called Peer ID | This is the 24 bit address/ICAO facility designator. It may comprise part of the IPv6 address. This would be padded with preceding zeros. |
| Called Sys ID | TCP/UDP Destination Port number | Port designation TBD |
| Called Presentation Address | Recipient’s IPv6 address |  |
| Calling Peer ID | ATNPKT Calling Peer ID | This is the 24 bit address/ICAO facility designator. It may comprise part of the IPv6 address. This would be padded with preceding zeros. |
| Calling Sys ID | TCP/UDP Source Port number | Port designation TBD |
| Calling Presentation Address | Originator’s IPv6 address |  |
| DS-User Version number | ATNPKT Content Version |  |
| Security Requirements | ATNPKT Security Requirements | Possible mappings: 00 – No security 01 – Sec dlg key mngt 02 – Sec dlg 03 – Reserved |
| Quality of Service | IPS Class of Service |  |
| Result | ATNPKT Result | Possible mappings: 00 – accepted 01 – rejected (permanent) 02 – rejected (transient) |
| Reject Source | ATNPKT Reject Source | Possible mappings: 00 – DS-user 01 – DS-provider |
| User Data | ATNPKT User Data |  |

| D-DATA |
| --- |
| Parameter | TCP/UDP/IP/ATNPKT parameter | Comments |
| User Data | ATNPKT User Data |  |

| D-END |
| --- |
| Parameter | TCP/UDP/IP/ATNPKT parameter | Comments |
| Result | ATNPKT Result | Possible mappings: 00 – accepted 01 – rejected (permanent) 02 – rejected (transient) |
| User Data | ATNPKT User Data |  |

| D-ABORT |
| --- |
| Parameter | TCP/UDP/IP/ATNPKT parameter | Comments |
| Originator | Originator’s IPv6 address |  |
| User Data | ATNPKT User Data |  |

| D-P-ABORT |
| --- |
| Parameter | TCP/UDP/IP/ATNPKT parameter | Comments |
| (no data) |

| D-UNIT-DATA |
| --- |
| Parameter | TCP/UDP/IP/ATNPKT parameter | Comments |
| Called Peer ID | ATNPKT Called Peer ID | This is the 24 bit address/ICAO facility designator. It may comprise part of the IPv6 address. This would be padded with preceding zeros. |
| Called Sys ID | TCP/UDP Destination Port number | Port designation TBD |
| Called Presentation Address | Recipient’s IPv6 address |  |
| Calling Peer ID | ATNPKT Calling Peer ID | This is the 24 bit address/ICAO facility designator. It may comprise part of the IPv6 address. This would be padded with preceding zeros. |
| Calling Sys ID | TCP/UDP Source Port number | Port designation TBD |
| Calling Presentation Address | Originator’s IPv6 address |  |
| DS-User Version number | ATNPKT Content Version |  |
| Security Requirements | ATNPKT Security Requirements | Possible mappings: 00 – No security 01 – Sec dlg key mngt 02 – Sec dlg 03 – Reserved |
| Quality of Service | IPS Class of Service |  |
| User Data | ATNPKT User Data |  |

Note. – State tables for the new IPS DS are given in Error! Reference source not found., including those for UDP.  The state table is split into different sections, including actions upon receiving DS primitives from the ATN application, actions upon receiving TCP control bits, and actions upon receiving data contained in UDP packets.

Table 1.  IPS DS State Tables

|  | State -> | NULL | Connection Pending | Data Transfer | Connection Closing |
| --- | --- | --- | --- | --- | --- |
| Event Source | Event |  |  |  |  |
| From ATN App |  |  |  |  |  |
|  | D-START Req | - create ATNPKT, setting DS primitive to D-START Ind - Perform TCP CONNECT/SYN or - Perform UDP data send - enter Connection Pending |  |  |  |
|  | D-START Rsp |  | - create ATNPKT, setting DS primitive type to D-START Cnf - Perform TCP ACK - enter Data Transfer |  |  |
|  | D-UNIT-DATA Req | - create ATNPKT, setting DS primitive to D-UNIT-DATA Ind - Perform TCP CONNECT/SYN or - Perform UDP data send - Remain in NULL |  |  |  |
|  | D-DATA Req |  |  | - create ATNPKT, setting DS primitive type to D-DATA Ind - Send data - Remain in Data Transfer |  |
|  | D-END Req |  |  | - create ATNPKT, setting DS primitive type to D-End Cnf - Perform TCP CLOSE/FIN - enter Connection Closing |  |
|  | D-ABORT Req |  |  | - create ATNPKT, setting DS primitive type to D-End Cnf - Perform TCP CLOSE/FIN - enter Connection Closing |  |
| From TCP |  |  |  |  |  |
|  | SYN/SYN+ACK Received, ATNPKT DS Primitive type is D-START Ind |  | - Create D-START Ind DS primitive and give to application - Send TCP ACK - Remain in Connection Pending state |  |  |
|  | SYN/SYN+ACK Received, ATNPKT DS Primitive type is D-UNIT-DATA Ind |  | - Create D-UNIT-DATA Ind DS primitive and give to application - Send TCP ACK - Send TCP CLOSE/FIN - Enter Connection Closing state |  |  |
|  | ACK Received, ATNPKT DS Primitive type is D-START Cnf |  | - Create D-START Cnf DS primitive and give to application - Enter Data Transfer State |  |  |
|  | Data received, ATNPKT DS Primitive Type is D-DATA Ind |  |  | - Create D-DATA Ind DS Primitive and give to application - Remain in Data Transfer state |  |
|  | CLOSE/FIN received, ATNPKT Primitive Type is D-END Ind |  |  | - Create D-END Ind DS Primitive and give to application - Send TCP FIN/ACK - Enter NULL state |  |
|  | CLOSE/FIN received, ATNPKT Primitive Type is D-ABORT Ind |  |  | - Create D-ABORT Ind DS Primitive and give to application - Send TCP FIN/ACK - Enter NULL state |  |
|  | CLOSE/FIN received, ATNPKT Primitive Type is D-P-ABORT Ind |  |  | - Create D-P-ABORT Ind DS Primitive and give to application - Send TCP FIN/ACK - Enter NULL state |  |
|  | RST received, ATNPKT Primitive Type is D-ABORT Ind |  | - Create D-ABORT Ind DS Primitive and give to application - Send TCP FIN/ACK - Enter NULL state |  | - Create D-ABORT Ind DS Primitive and give to application - Send TCP FIN/ACK - Enter NULL state |
|  | RST received, ATNPKT Primitive Type is D-P-ABORT Ind |  | - Create D-P-ABORT Ind DS Primitive and give to application - Send TCP FIN/ACK - Enter NULL state |  | - Create D-P-ABORT Ind DS Primitive and give to application - Send TCP FIN/ACK - Enter NULL state |
| From UDP |  |  |  |  |  |
|  | ATNPKT header with D-START Ind | - Create D-START Ind DS Primitive and give to application - Enter the Connection Pending state |  |  |  |
|  | ATNPKT header with D-START Cnf |  | - Create D-START Cnf DS Primitive and give to application - Enter the Data Transfer state |  |  |
|  | ATNPKT with D-UNIT-DATA Ind | - Create D-UNIT-DATA Ind DS Primitive and give to application - Remain in the NULL state |  |  |  |
|  | ATNPKT with D-DATA Ind |  |  | - Create D-DATA Ind DS Primitive and give to application - Remain in the Data Transfer state |  |
|  | ATNPKT with D-END Ind |  |  | - Create D-END Ind DS Primitive and give to application - Enter the NULL state |  |
|  | ATNPKT with D-ABORT Ind |  | - Create D-ABORT Ind DS Primitive and give to application - Enter the NULL state | - Create D-ABORT Ind DS Primitive and give to application - Enter the NULL state | - Create D-ABORT Ind DS Primitive and give to application - Enter the NULL state |
|  | ATNPKT with D-P-ABORT Ind |  | - Create D-P-ABORT Ind DS Primitive and give to application - Enter the NULL state | - Create D-P-ABORT Ind DS Primitive and give to application - Enter the NULL state | - Create D-P-ABORT Ind DS Primitive and give to application - Enter the NULL state |

## 2.2 Ground-Ground Applications

### 2.2.1 ATSMHS

Note. –  The ATS Message Handling Services (ATSMHS) application aims at providing generic message services over the Aeronautical Telecommunication Network (ATN).

2.2.1.1 IPS hosts that support the ATSMHS application shall comply to Doc 9705 Edition 3 with the exception of clause 3.1.2.2.2.1.2 ("Use of Transport Service").

2.2.1.2 To operate ATSMHS over ATN IPS, IPS hosts shall:

a) make use of RFC-2126 to directly provide TCP/IPv6 interface; or,

b) make use of RFC-1006 to provide a TCP/IPv4 interface combined with IPv4/IPv6 protocol translation device(s).

### 2.2.2 AIDC

### AIDC has not been implemented over OSI as specified in Document 9880. Regions have deployed alternative solutions meeting AIDC operational requirements as specified in Document 9694. This section describes regional implementations of AIDC over IPv6, thereby enabling AIDC operational services over the ATN/IPS

### Note 1. – The AIDC application exchanges information between ATS Units (ATSUs) for the support of critical Air Traffic Control (ATC) functions, such as notification of flights approaching a Flight Information Region (FIR) boundary, coordination of boundary conditions and transfer of control and communications authority.

### Note 2. – The AIDC application as specified in DOC 9880 is considered too complex to easily map to an IPS environment.

### 2.1.2.1 IPS hosts in the ATN that support the AIDC application exchanges may make use of the equivalent operational application described in the EUROCONTROL Specifications for On-Line Data Interchange (OLDI).

### 2.1.2.2 IPS hosts in the ATN that support the OLDI application shall make use of EUROCONTROL Specifications for the Flight Message Transfer Protocol to operate the application over TCP/IPv6.

### 2.2.3 Voice over Internet Protocol (VoIP)

The key advantages associated with the use of a packet network for the transmission of digitized voice are:

- Bandwidth allocation efficiency

- Ability to use modern voice compression methods

- Associate economics with shared network use

- Reduce costs

- Enhanced reliability of packet networks

- Ability to use multiple logical connections over a single physical circuit.

#### 2.2.3.1 Standards and Protocols

There are two standardized frame works for implementing VoIP, H.323 and SIP.  Although both protocols may be used for VoIP applications, the original focus of each protocol is different.  The focus of H.323 has been to handle voice and multimedia calls, including supplementary services, while SIP was designed as a generic transaction protocol for session initiation not bound to any specific media (e.g., audio or video).  Details of relevant protocols are described in the following subsection:

##### 2.2.3.1.1 H323

As shown in Figure 8.1, H.323 operates in the application layer to support multimedia, data and signalling protocols. Also  depicted in Figure 2 are the various protocols used to convey multimedia traffic over TCP/UDP/IP networks.

Multimedia                             Data Transfer                Signalling

Figure 2 H.323 Core Architecture

###### 2.2.3.1.1.1 Multimedia

This group of protocols converts between analog (e.g., voice) and digital signals, which are fed into, or picked from, the UDP/IP network. Some of these protocols include:

- Audio codecs – These compress digital voice for low bandwidth transmission, and decompress digital voice received from the network for feeding to the user audio device (e.g., speaker, headphone).

- Video codecs – These compress digital video for constrained bandwidth, and decompress digital video received from the network for feeding to the user video device.

- RTP (Real-Time Transport Protocol) and RTP Control Protocol (RTCP) – These are control protocols for the payloads fed into the network. RTP regulates the end-to-end delivery of audio and video in real time over IP networks.  RTCP regulates the control services in multimedia transmissions, and monitors the quality of its distribution, including synchronization of receivers.

###### 2.2.3.1.1.2 Data Transfer

This class of protocols provides real-time, multi-point data communications and application services over IP networks (e.g., collaborative decision making with video, voice, and data exchange).  Data transfers between generic applications and the IP network are processed by the T.120 protocol, which can operate over various transports, including PSTN and ISDN.

T.130 is a protocol still under development for controlling audiovisual sessions for real-time multimedia conferencing, and ensure high QoS.

###### 2.2.3.1.1.3 Signalling

- H.225.0 call signalling is used to set up connections and exchange call signalling between H.323 endpoints (terminals and gateways), which are transported as real-time data and carried over the TCP/UDP/IP network.  H.225.0 uses Q.931 for call setup and teardown.

- H.245 control signalling is used to exchange end-to-end messages between H.323 endpoints.  The control messages are carried over H.245 logical control channels, which are relayed between conference session endpoints.

- H.235 provides security services within the H.323 framework, such as authentication, encryption, integrity and no-repudiation.

H.450.1 deals with the procedures and signalling protocol between H.323 entities for the control of supplementary services.  Other protocols within the H.450 series (i.e. H.450.2-12) provide specific supplementary services (e.g., call transfer, call hold, call waiting, call priority).

##### 2.2.3.1.2 MGCP/MEGACO

Shown in Figure 3 is the SIP Protocol Suite. SIP is an application layer control protocol that provides advanced signalling and control functionality for large range multimedia communications.  SIP is an alternative to H.323, which establishes, modifies, and terminates multimedia sessions, which can be used for IP telephony.  SIP is an important component in the context of other protocols to enable complete multimedia architecture, as shown in Figure 4.  These include RTP for real time data transport and QoS assurance, RTSP for controlling streaming media, MEGACO for controlling gateways to the PSTN, Figure 8.3, and SDP for describing multimedia sessions.  These sessions include Internet multimedia conferences, Internet telephone calls, and multimedia distribution over TCP/UDP/IPv4, or IPv6, as shown in Figure 5.

Figure 3 SIP Protocol Suite

# 3.0 Application Services

## 3.1 IPS DS

This section describes a replacement for the ULCS Dialogue Service (DS) interface to the upper layers, called the IPS DS.  The legacy DS served as an interface between the dialogue service and the upper layers (session down) via the control function.  The IPS DS does not have an interface to the session layer; instead it is mapped to TCP primitives in a fashion similar to RFC1006 for TP0 over TCP/IP.  This is depicted in Figure 6.  One of the differences is that for the IPS DS, there is no transport-transport interface.  It is an upper layer to transport interface, i.e. a service above TCP/UDP.  While conceptually similar, the upper layers will be interfacing with transport services instead of network services.

Figure 6.  Updated Upper Layers Diagram

When an application such as CM interfaces with the ULCS, it does so via the dialog service.  The DS is defined as a number of primitives with parameters that allow the applications to establish and manage connections and exchange data with peer applications.  In order to minimize impacts on the applications, the IPS DS intends to keep the DS interface to the applications the same as the legacy DS, and changing the lower level mapping to transport parameters.  This is done by identifying the services and primitives used in the DS and mapping those to the TCP events, actions, and data types.

For UDP, the data types are similar (and simpler), but there is no notion of the states that TCP has.  While it would be usable by legacy ATN applications, the use of UDP does not allow guaranteed delivery, and packets may go missing or be duplicated.  But UDP would be usable for applications that acknowledge its limitations, or want to take advantage of its broadcast nature.  It should be noted that the applications were developed with a reliable transport service in mind; therefore the use of UDP would need to be further explored to determine impacts of lost/duplicate packets on the application state machines.

The ATN OSI-type applications are divided into two main sets of functions:  the Application Service Element (ASE) which is part of the larger Application Entity (AE), and the user function.  The two main interfaces are the user interface (between the application user and the ASE) and the dialogue service interface (between the ASE and the supporting communication layers).  From an IP perspective, the ASE provides the part of the application that maintains protocol checking and is responsible for delivering the required functionality as specified in the standards.  The user function is how data is given to and received from the application.

### 3.1.1 Services and Primitives

The current DS primitives used by the ATN applications are given in the following table:

| Service | Description |
| --- | --- |
| D-START | This is a confirmed service used to establish the binding between the communicating DS-Users. |
| D-DATA | This unconfirmed service is used by a DS-User to send a message from the DS-User to the peer DS-User. |
| D-END | This is a confirmed service used to provide the orderly unbinding between the communicating DS-Users, such that any data in transit between the partners is delivered before the unbinding takes effect. |
| D-ABORT | This unconfirmed service can be invoked to abort the relationship between the communicating DS-Users. Any data in transit between them may be lost. |
| D-P-ABORT | This unconfirmed service is used to indicate to the DS-User that the dialogue service provider has aborted the relationship with the peer DS-User. Any data in transit between them may be lost. |
| D-UNIT-DATA | This unconfirmed service is used to send a single data item from one peer DS-User to another. Any problem in delivering the data item to the recipient will not be signaled to the originator. |

In order to provide the transport services, the following TCP services are mapped to the corresponding dialog services.  The protocol of TCP provides the following services:

| Event | Description |
| --- | --- |
| Connected | Open succeeded (either ACTIVE or PASSIVE) |
| Connect fails | ACTIVE open fails |
| Data ready | Data can be read from the connection |
| Error | The connection has encountered and error and is now closed |
| Closed | An orderly disconnection has started |

| Action | Description |
| --- | --- |
| Listen on port | PASSIVE open on the given port |
| Open port | ACTIVE open on the given port |
| Read data | Data is read from the connection |
| Send data | Data is sent on the connection |
| Close | The connection is closed (pending data is sent) |

### 3.1.2 Protocol

The mapping between the TCP states and the dialog service primitives is given in the following table.

| Dialog Service | TCP |
| --- | --- |
| Connection Establishment |
| D-START Req | Open starts |
| D-START Ind | Listen (PASSIVE open) starts |
| D-START Rsp | Listen completes |
| D-START Cnf | Open (ACTIVE open) finish |
| D-UNIT-DATA Req | Open completes |
| D-UNIT-DATA Ind | Listen (PASSIVE open) starts and finishes |
| Data Transfer |
| D-DATA Req | Send data |
| D-DATA Ind | Data ready followed by read data |
| Connection Release |
| D-END Req | Close |
| D-END Ind | Connection closes |
| D-ABORT Req | Abort |
| D-ABORT Ind | Connection closes |
| D-P-ABORT Ind | Connection closes |

The use of UDP is not as straight-forward.  The D-UNIT-DATA is connectionless, so that parameter would easily map to UDP.  However, for other dialogue service primitives, since UDP is stateless and connectionless, there is not an inherent mapping as there is for TCP.  Also, there is no concept of a connection so aborts have relevance only to the application level.  In order to indicate the dialogue service primitive using UDP, it would seem that a data element should be added to explicitly indicate which dialogue service is being invoked.  This is further addressed in the Packet Format section below.

### 3.1.3 Packet Format

TCP is inherently different from TP4 in that it’s a streaming protocol and not a packet protocol.  The TCP packet format would be used as defined in RFC 793.  UDP may also be used.  The UDP header is simpler, and doesn’t allow for synchronization, ordering or streaming.  It is proposed that the same packet format be used for both TCP and UDP.

In general, the use of the TCP/UDP for the DS lends itself well for the DS parameters.  In order to accommodate all of the parameters necessary, a new TCP packet header format is proposed.  This header takes into account all of the data that is currently exchanged via the existing DS primitives, and maps those that do no map directly onto TCP, UDP or IP parameters into a packet format.

As previously mentioned, use of UDP may require additional data to indicate the type of dialogue service that is being invoked (e.g. D-START Req, D-END Req, etc).  The IPS DS would then need to put in the requisite values depending on the service.  If the packet format is common with TCP, the service type parameter could be optional since it can be discerned by the corresponding TCP states.  Another option is to have separate header formats for UDP and TCP, mapping D-UNIT-DATA to only UDP and all other to TCP.

Additionally, other parameters that may need further investigation to see if they are needed, and if so, the best way to indicate them.  Some of these parameters will become more evident as IPv6 architectures mature.  These parameters include the Called/Calling Peer ID, Called/Calling Sys ID, Security Requirements, and Quality of Service (QoS).

It should be noted that the Quality of Service parameters currently used by the ATN are not indicated to the peer; they are intended to be used by the transport and lower layers in order to provide the requested performance.  Therefore, it seems likely that these parameters will be passed as is done currently for legacy ATN applications, and that the IPS will need to takes those passed values into account when performing the corresponding QoS services.

The provisional ATN Packet (ATNPKT) format is shown in Error! Reference source not found..

Figure 7.  ATNPKT Format

The fields of the ATNPKT are described in the following subsections.

### 3.1.4 ATNPKT Version

The version of the ATNPKT header.  Initially set to 1, this will be rolled to account for any subsequent modifications to the basic ATNPKT format.

### 3.1.5 DS Primitive

The type of DS primitive that this packet is meant to carry.  This would be required for UDP in order to allow state processing.  The field would be provisionally optional for TCP.  The exact format is TBD, but a possible way forward would be to set D-START Req to 0, D-START Ind to 1, etc.  Note also that the application does not provide this parameter; it is filled in by the IPS DS.

### 3.1.6 Content Type

The type of application data carried.  This is an additional field that does not map explicitly to a current usage of the DS.  However, from an application point of view, it would be trivial to include since the various services are explicitly called (e.g. a CM-logon is only used for CM).  It is proposed that these values follow the OID references for the ASE types as given in the current Doc 9705 Subvolume 9, e.g. ADS is 0, CM is 1, CPDLC is 2, ATIS is 3, etc.

### 3.1.7 Content Version

This is the version number of the application information carried in the content.  It would normally be mapped to the application’s version number.

### 3.1.8 Called Peer ID

This is the 24 bit address of the aircraft or the ICAO facility to which the data is being sent.  This field may not be necessary depending on the IP architecture chosen (i.e. if that information is contained within the IP address itself).  If it is not, this field would be used to exchange that information.

### 3.1.9 Calling Peer ID

This is the 24 bit address of the aircraft or the ICAO facility from which the data is being sent.  As with the Called Peer ID, this information may be included as part of the IP address itself.  If not, an additional field would need to be used to explicitly carry the information.

### 3.1.10 Security Requirements

The Security Requirements is another parameter that may not be necessary.  It will be used to convey the current different levels of security, which are No Security, Secured Dialogue Supporting Key Management, Secured Dialogue, and Reserved.  Note that 4 bits are notionally reserved.

### 3.1.11 Reject Source

The Reject Source is used to indicate which level issued a rejection for a particular service.  For the ATN applications, this is either the DS-user or the DS-provider.  To indicate this information 2 bits are notionally reserved.

### 3.1.12 Result

The Result parameter is used by the ATN applications to determine whether or not a dialogue is to be kept open as well as whether there was a problem with the transaction.  The values are accepted, rejected (permanent) and rejected (transient).  The range of values is notionally indicated with 2 bits.

### 3.1.13 Application Technology Type

The Application Technology Type identifies the genre of application information that is carried.  Other legacy applications besides legacy ATN may also take advantage of the IPS infrastructure, e.g. FANS-1/A, ACARS, etc.  An added indicator may assist with routing on the ground and aircraft by indicating if the encapsulated data type.  This notionally represented by 8 bits.

### 3.1.14 User Data Length

This is a 16 bit field indicating the length of the user data.  It is assumed that 16 bits will be sufficient; however, if need be it can be increased.

### 3.1.15 User Data

This is the encoded data from the ATN applications.

### 3.1.16 Multiple Application Instantiations

Normally running more than one application instance between end systems is not done for most applications, particularly for applications such as CPDLC that are dependent on proper pairing of messages with their respective responses.  However, there may be times when more than one of the same application needs to be run between end systems.  Also, normally there is a one to one correlation between end systems.  For cases where multiple instances are running between the same end systems, this also holds true; however for this case an association cannot be limited to an end-system pair, it must be further identified by connection.

For TCP connections, this is easily doable.  Each connection will have a separate state machine, and end systems may be run in a socket server configuration.  This means they listen on a particular socket, and if a connect request is received local conditions are checked (e.g. connection number limit, connection initiator rules, etc) and if ok the socket is accepted and passed to a child process.  That child process manages all of the concurrent application state stables.  Care must be taken so that data available to the multiple sockets is not overwritten inadvertently, but these are normal concerns with any type of threaded system.

For UDP connections, handling multiple instances is not as easily performed since there is no concept of a connection.  While the source of UDP packets can be discerned, there is currently no field in the ATNPKT header that allows for an instance identifier.  If added, this would allow the ATNPKT header to identify explicitly which instance of an application is sending the data.  Separate state machines can then be used for each different instance identifier received.  For TCP, this parameter’s use would be optional or not used.

## 3.2 OLDI

On-Line Data Interchange (OLDI) combined with the Flight Message Transfer Protocol (FMTP) is a means to enable AIDC operational requirements for the co-ordination and transfer of aircraft between adjacent air traffic control units.

The relationship between AIDC and OLDI messages is described in the Appendix of ICAO Document 9694, Part VI, Chapter 1.

The OLDI specification does not mandate the implementation of OLDI messages but specifies the requirements that need to be met when implementing such facilities. If OLDI messages are implemented as the result of regulatory provisions, or based on bilateral agreement between Air Traffic Control Units, then the requirements outlined as mandatory in this specification for those messages become mandatory for implementation. This is required in order to meet the purpose of the messages and to ensure interoperability between systems.

The co-ordination procedure requires that systems identify whether or not transfers are in accordance with Letters of Agreements (LoAs).

The process which checks such compliance is referred to in the OLDI Specification as "the filter". The database used for the filter will include the following, if required:

- agreed co-ordination points;

- eligible (or ineligible) flight levels which may also be associated with the co-ordination points;

- aerodromes of departure;

- destinations;

- agreed direct routes ;

- time and/or distance limits prior to the COP, after which any co-ordination message is considered non-standard;

- any other conditions, as bilaterally agreed.

All items in this list may be combined to define more complex conditions.

The format of the messages (ICAO PANS/RAC 4444 or EUROCONTROL ADEXP) to be transmitted and received has to be agreed bilaterally.

The address of the ATS units providing the services has to be agreed and has to be different from the addresses of the other units to which the ATS units are already connected or planned to be connected. The ATS unit addresses are part of the OLDI message.

## 3.3 FMTP

The Flight Message Transfer Protocol is a communications stack based on TCP/IPv6. FMTP is a state machine that handles connection establishment and session management. Each FMTP system requires to be assigned with an identification value that is to be exchanged during connection establishment. The identification values have to be bilaterally agreed and must be different from the values of the other units to which the ATS units are already connected or planned to be connected.

The FMTP specification assumes the transfer of ASCII characters but implementations of the protocol may wish to extend this support to other character sets or binary transfers. Further guidance material on FMTP is available from EUROCONTROL at the following website http://www.eurocontrol.int/communications/public/standard_page/com_network.html

### 3.3.1 Testing OLDI/FMTP

EUROCONTROL has developed a test tool named ETIC to validate OLDI/FMTP implementations and build test scenarios. The tool can be made available to FMTP implementation projects upon request. Request for further information on ETIC can be addressed to etic@eurocontrol.int.

ICAO

Aeronautical Telecommunication Network (ATN)

Manual for the ATN using IPS Standards and Protocols (Doc 9896)

Part III

Guidance Material Section

TABLE OF CONTENTS

1.0 Introduction	4

1.1  Background	5

1.2  Reference Document	5

1.3  Abbreviations	5

2.0 General Guidance	5

2.1  ATN Policy	6

2.1.1 Transit Traffic	6

2.2 Transition between IPv4 and IPv6	6

2.3 Network Transition Mechanisms	7

2.3.1 Tunnelling	8

2.3.2 Dual Stack	8

2.3.3 Translation	9

2.3.4 Combining of the Mechanisms	9

3.0 PROTOCOL Stack	10

3.1	10

3.2	10

3.3 Physical and Link Layer Guidance	10

3.4 Network Layer	10

3.4.1 Address Plan	10

3.4.2 Application interface to the network layer	10

3.4.3 Inter-domain routing	10

3.4.4 Multicast	12

3.5 Transport Layer	13

3.5.1 Transmission Control Protocol	14

3.5.2   User Datagram Protocol (UDP)	14

3.5.3 Transport Layer Addressing	15

3.5.4 Application Interface to the Transport Layer	15

3.5.5 Congestion Avoidance	15

3.5.6 Error Detection and Recovery	16

3.5.7 Performance Enhancing Proxies (PEPs)	16

4.0 Security Guidance	17

4.1 MOBILE IPv6	17

4.2 Enhancements to MIPv6	18

4.3 Proxy Mobile IPv6	19

APPENDIX A – REFERENCE DOCUMENTS	20

APPENDIX B – ABBREVIATIONS/DEFINITIONS	1

APPENDIX C – AS Numbering Plan	4

List of Tables

Table 4-1 AS Numbering Plan	Error! Bookmark not defined.

Table 6-1 DS Primitives	Error! Bookmark not defined.

Table 6-2 Dialog Services	Error! Bookmark not defined.

Table 6-3 Mapping between TCP states and Dialog Service Primitives	Error! Bookmark not defined.

List of Figures

Figure 1.1 Protocol Reference Model	4

Figure 4.1 SSM Multicast IPv6 address with global scopeIPv6	13

Figure 6-1  Upper Layers Diagram	Error! Bookmark not defined.

Figure 6-2  ATNPKT Format	Error! Bookmark not defined.

Figure 8.1 H.323 Core Architecture	7

Figure 8.2 SIP Protocol Suite	2

Figure 8-3 VoIP Interface to PSTN via MEGACO	3

Figure 8-4 VoIP with SIP	3

FOREWORD

The material contained in this document supplements the Standards and Recommended Practices (SARPs) and the Manual for Detailed Technical Specifications.  This document is to be used to assist in the deployment of IPS systems of the Aeronautical Telecommunication Network (ATN)  as defined in Annex 10 — Aeronautical Telecommunications, Volume III — Communication Systems and Part I — Digital Data Communication Systems and the Manual on Detailed Technical Specification for the IPS ATN Doc 9896.

1.0 Introduction

The Aeronautical Telecommunication Network Internet Protocol Suite (ATN IPS) Guidance Document contains information to assist member states in the deployment of an IPS network for their state infrastructure to support the delivery of ICAO Air Traffic Management (ATM) services. The following minimum core services should be provided by ATN/IPS:IP network services, and Global information exchange.

These core services enable ATN IPS applications to provide voice and data services with the appropriate priority and security over a network with the required quality and class of service.

The protocols discussed in this document are referred to based on the open system interconnect reference model (OSI).  However, since IPS uses only 4 layers the mapping is not consistent with the reference model.  Figure 1.1 depicts the OSI reference model and the relationship between the ISO ATN and the IPS protocols.

Figure 1.1 Protocol Reference Model

1.1  Background

The ICAO/ATN has established with the specific goals of providing a commercial off the shelf global ATM services. Currently, ATN services can be provided using the ISO based ICAO protocols as documented is ICAO Standards 9705/9880. This document along with the ICAO ATN/IPS Standard 9896 [1] is an additional technical approach for networking, and will enable member state to have an additional resource for providing ATM services.

## 1.2  Reference Document

ICAO Document 9705 Manual of Technical Provisions for the ATN

ICAO Document 9880 Manual of Technical Provisions for the ATN

ICAO Document 9694 Manual of Air Traffic Services Data Link Applications

## 1.3  Abbreviations

ATN  		Aeronautical Telecommunications Network

ATM		Air Traffic Management

BGP		Border Gateway Protocol

IPS		Internet Protocol Suite

ICAO		International Civil Aviation Organization

IPv4		Internet Protocol Version 4

IPv6		Internet Protocol Version 6

ISO		International Organization for Standardization

MOA		Memorandum of Agreement

2.0 General Guidance

This section contains general guidance information about the implementation of IPS for ATN services. This document only discusses IPS based services for detailed information on ISO standards based ATN services refer to document 9705/9880.

The current recommendation of ICAO is to deploy IPv6 protocols and services but that does not preclude a member state network from supporting or deploying IPv4 services.  However, these services must remain transparent from the IPv6 portion of the network.  All transaction over the ICAO ATN must be done using ICAO standards 9705/9880 or 9896.

This document focuses on the network, transport and application services; physical and link services are to be negotiated on a service need basis by the implementing state.

ATN Administration

The administration of the ATN shall be performed by the member state and the their appointed service provider.  However, that does not preclude agreements between member states that form a federation in the interest of providing ATM services.

## 2.1  ATN Policy

The purpose of this section is to define the operating polices for the ATN.

### 2.1.1 Transit Traffic

The ATN IPS manual does not specify which routes are to be advertised between ATN IPS routers nor basic traffic management policies for a dynamically routed environment.

ATN IPS routers will exchange information about their internal network prefixes with its immediate neighbor routers but may also forward routing information about other network prefixes learned from other BGP neighbors.

As a result, traffic between two Administrative Domains may be relayed by a number of intermediate Administrative Domains. Such traffic being carried on behalf of two others is termed transit traffic.

All Administrative Domains that participate to the ATN IPS must ensure the proper handling of transit traffic on the following basis:

- An Administrative Domain will not advertise a network prefix if it is not prepared to accept incoming traffic to that network prefix destination;

- When establishing the interconnections between two Administrative domains a charging mechanism may be agreed to in order to recover costs;

- Administrative Domains that relay transit traffic will ensure that the associated security and QoS policies of the traffic is maintained

## 2.2 Transition between IPv4 and IPv6

Current ground communications are generally handled through appropriate protocol profiles that are based on IPv4. For technical, economical and strategic reasons, transition to IPv6 will be made gradually and appropriate transition path need to be defined:

RFC 4213 - Basic Transition Mechanisms for IPv6 Hosts and Routers

This RFC discusses dual stack approaches as well as tunnelling IPv6 traffic through existing IPv4 networks. The three main interoperability cases are as follows:

- IPv6 nodes that require to communicate over an IPv4 sub network

- IPv4 nodes that require to communicate over an IPv6 sub network

- An IPv4 node that requires to communicate with an IPv6 node

Case 1 can be resolved by relying on common IPv6 over IPv4 tunnels. Although this does create additional overhead it would allow early deployment of ATN/IPS applications.

Case 2 could be resolved by relying on IPv4 over IPv6 tunnels. If the two autonomous IPv4 domains overlap in terms of routing and addressing; interoperability may not be achieved.  A dual stack approach is recommended to ensure that ATN systems can natively interface over the ATN/IPS without having to resort to such tunnelling techniques which may not be appropriate.

Case 3 can be the result of legacy applications that have not been updated to IPv6 or no longer maintained. In the ATN context, this issue needs to be considered as some application vendors (e.g. AMHS) do not have a dual stack solution and only support IPv4 profiles. This case can be handled through the use of network address translation from IPv4 to IPv6:

RFC 2766 - Network Address Translation - Protocol Translation (NAT-PT)

The benefit of NAT-PT and other similar mechanisms allow an IPv4-only system to behave as an IPv6 system and communicate over the ATN/IPS.

All ATN/IPS systems are recommended to adopt a dual stack approach in order to ensure native inter-working over the ATN/IPS and local IPv4 environments without having to rely on the use of external tunnelling or translation devices.

## 2.3 Network Transition Mechanisms

IPv6 has been adopted by the IETF and the internet authorities to cope with the ever increasing growth rate of the global internet. IPv6 solves many of the technical problems associated with IPv4, in particular the limited IPv4 address space.

The global implementation of IPv6 has already begun. It is the building block of the next generation internet which will enable a flexible means to roll-out new technologies and services. For this reason, the ATN IPS is based on IPv6 to take immediate advantage of new commercial off-the-shelf products and technologies.

The implementation of the ATN IPS will be gradual over a significant period of time. Many organizations will be required to go through multiple steps to ensure that ATN IPS end-systems and routers are integrated into their existing environment in particular for those that have deployed legacy ATN/OSI CLNP (primarily over Ethernet or “X.25”) and IPv4 systems.

Three transitions mechanisms can assist organisations deploying the ATN IPS in a heterogeneous environment:

- Tunnelling: one protocol being encapsulated in another

- Dual stack: an environment in which multiple protocols operate simultaneously

- Translation: the conversion from one protocol to another

An in-depth description of the first two mechanisms can be found in RFC4213 (Basic Transition Mechanisms for IPv6 Hosts and Routers). The applicability of above three mechanisms to the ATN IPS are further described.

### 2.3.1 Tunnelling

IPv6 has been specified to operate over a variety of lower layer interfaces such as Frame Relay, ATM, HDLC, PPP and LAN technologies. Tunneling implies that a given protocol is encapsulated into another, meaning that IPv6 would be encapsulated into another functionally equivalent network protocol. With regard to the ATN IPS, the key benefit of this mechanism would be for aeronautical organizations that already operate IPv4 networks to allow the ATN IPS hosts and routers communicate between each other over such an underlying IPv4 network. Furthermore, if the interconnecting infrastructure between two ATN IPS administrative domains is limited to IPv4, this mechanism can be applied.

It is recalled that IPv6 cannot operate over X.25; an IPv6 tunnel over IPv4 can be in turn tunneled over an X.25 network. A specific tunneling mechanism termed IP SNDCF is defined for ATN/OSI applications, it is to be noted that this enables interoperability between ATN/OSI applications over an IP network but does not enable interoperability with ATN/IPS applications.

Tunnelling mechanisms lead to an increase of protocol overhead and the segregation of the two routed domains creates additional network management e.g. an IPv6 routed domain over an underlying IPv4 routed domain that needs to be managed in terms of QoS, security, and route optimization. In addition, this mechanism only foresees interoperability between ATN IPS systems as it does not enable interoperability between ATN OSI systems nor other IPv4 systems within the organization. Nevertheless, it may provide an effective way to enable the ATN IPS within and between two administrative domains.

The tunneling mechanism is best suited to resolve lower layer communication issues between ATN IPS IPv6 hosts and routers but does not provide interoperability with non-compliant ATN IPS systems.

### 2.3.2 Dual Stack

The dual stack mechanism implies that an implementation handles more than one communications protocol for a given application or function. Within the internet domain a significant number of communication applications have been dual stacked e.g. HTTP, FTP, SSH, DNS, SMTP etc. by supporting both IPv4 and IPv6 protocols. However, in the context of the ATN IPS the purpose of dual stacking is to resolve similar yet different issues.

The concept of dual stacking is ideally suited for systems that need to support ATN applications for both OSI and IPS. In such environments, the applications are designed in an abstract fashion to be independent of the lower layers, in other words they are unaware which lower layer communications protocol (OSI or IP) is being used to communicate with their peer. X.400 vendors have taken this approach to support both OSI and IP environments avoiding the need to develop complex ad-hoc lower layer communication gateways. Usually such implementations rely on some form of directory or lookup table associating a high-level address with a specific communications protocol address.

The concept of dual stack can be extended to multiple stack. ATN AMHS manufacturers usually support operation over multiple protocols such as OSI, TCP/IP and X.25 .

The dual stack mechanism is best suited to provide the maximum level of interoperability with peers while reducing the complexity of lower layer communication protocol gateways and additional single points of failure. It is ideally suited for applications such as AMHS whereby some systems have already been implemented on the basis of OSI and others on TCP/IP. A dual stack approach can be a valid for air-ground datalink ground systems to support CPDLC over multiple datalink services such as ATN OSI and ATN IPS.

### 2.3.3 Translation

Translation mechanisms imply the conversion from one protocol to another. This mechanism can be interpreted as a lower layer communications gateway between two protocols that share a high degree of commonality. Several translators have been developed in the context of the transition from IPv4 to IPv6 as both versions share a number of common features.

Within the overall transition from IPv4 to IPv6, it was envisaged that some systems may be only capable of communicating with IPv4 and others with IPv6. Considering global internet scalability issues and the fact that most internet applications and systems have become dual stacked, the need for translators has declined.

However, translators may play an important short-term role in the case of the ATN IPS. For example, although existing AMHS systems operate on dual stack operating systems, none of them have upgraded their application code to make use of IPv6. In other words, RFC1006 is supported but not RFC2126. In such particular cases and in view of the limited number of systems, the deployment of translators provides a short-term measure for such systems to comply with the ATN IPS and inter-work with RFC2126 enabled systems.

IPv4/IPv6 translators increase the complexity of the IP infrastructure and its management. A dual stack approach is to be preferred but in specific cases translators may be the only short-term measure to provide compliance with the ATN IPS.

### 2.3.4 Combining of the Mechanisms

As the ATN IPS implementation will be gradual it is understandable that a combination of the above three mechanisms will be applied.

Specific combinations of the above mechanisms can be deployed to better fit within the environment of the administrative domain environment.

3.0 PROTOCOL Stack

## 3.1 Text

## 3.2 text

## 3.3 Physical and Link Layer Guidance

Physical and link layer issues will be determined by the required service and member state connections.  The physical and link layer issues will be on service need basis and should be contained in a memorandum of agreement (MOA).

## 3.4 Network Layer

The IPS ATN addressing is performed using IPv6, which uses 128 bits long address block versus 32 bits in IPv4.

### 3.4.1 Address Plan

TBD.

### 3.4.2 Application interface to the network layer

Although applications generally interface to the communication service at the transport layer, it is sometime necessary to transmit and receive datagrams at the network level. This is granted by some socket API extensions specified in:

RFC 3542 - Advanced Sockets Application Program Interface (API) for IPv6

### 3.4.3 Inter-domain routing

This section discusses inter-domain routing that will enable member state networks to interconnect while maintaining state or federation autonomy.  The protocol to be used shall be the border gateway protocol (BGP).

#### 3.4.3.1 AS numbering plan

AS numbers need to be assigned and configured in ATN/IPS routers to announce their autonomous systems within the routed domain. The AS numbering plan is presented in Appendix C.

#### 3.4.3.2 ATN/IPS Router Ids

In order to establish BGP between two neighbours, each BGP peer must define a router id. If two routers make use of the same router-id value, BGP cannot be established. As the router id is a 32 bit field, it is usually on the IPv4 address of the router.

As ATN IPS routers may not have Ipv4 interfaces a scheme needs to be recommended. Although global uniqueness of these values is not a pre-requisite, to ease implementation of the ATN IPS the following scheme is recommended (based on draft-dupont-durand-idr-ipv6-bgp-routerid-01.txt):

4 bits set to one,

16 bits set to the AS number (a global AS number plan is part of this Document)

12 bits manually allocated within the domain. (allows for 4096 different router IDs in each routing domain)

##### 3.4.3.2.1 Routing Advertisement

ATN IPS routers should advertise network prefixes based on consistent prefix lengths or aggregate route prefixes;

##### 3.4.3.2.2 Traffic type segregation

BGP-4 does not natively allow setting up different set of routes for different traffic to the same destination.  ATN IPS requirement on traffic type segregation may be fulfilled by appropriate provisions in the ATN addressing plan: if the ATN address incorporates an indication of the traffic type, BGP-4 will transparently flood segregated route information for the various traffics.

##### 3.4.3.2.3 Differentiated Service

Differentiated Service (RFC 2474) provides a mean for specifying and implementing QOS handling consistently in IPS network. This specification is made on a per node basis, specifying behaviour of individual nodes concerning QOS (Per Hop behaviour).

The general framework / current practices is depicted in details in:

RFC 2475 - Architecture for Differentiated Services

##### 3.4.3.2.4 Traffic Priority

Historically, network layer priority was selected explicitly by the sending application through the TOS field. Although Differentiated Service (RFC 2474) preserves the IP precedence semantic of the TOS field, this approach is now deprecated. This is partly because the IP precedence has been superseded by the Per-Hop-Behaviour strategy inside Differentiated service, but also because network administrators usually don’t trust QOS specification coming from the application.

ATN application traffics can be identified / prioritised according to the destination port of data grams when they enter the network:

- This provides transparent and safe identification of traffics, because the destination port is always a trusted information (otherwise the traffic will never reach its destination).

- But this requires specification of a distinct port for every ATN application (proliferation of ports would unnecessarily complexity administration of routers, and incurs their performance).

- During transit in the IPS network, corresponding data grams could be marked using the Differentiated Service field, in respect to the practices indicated in RFC 2475.

### 3.4.4 Multicast

The need to send the same information to multiple receivers is one of the main requirements of surveillance data distribution. This requirement can be supported by the Internet Protocol versions 4 and 6 (IPv4 and Ipv6 respectively) multicast services. Other networking techniques that achieve the same multicast objective are not further considered within the scope of this document.

A limited number of European States have deployed national Ipv4 multicast services for surveillance data distribution. However, the limited range of the Ipv4 multicast address space inhibits the deployment of scalable service within

In recent years, significant technical progress has been made in the field of IP multicast, namely source specific multicast (SSM). Contrary to existing deployments on the basis of PIM-SM (Protocol Independent Multicast—Sparse Mode), SSM provides added simplicity and resiliency to the routing of IP multicast traffic and is ideally suited for surveillance needs.

At present, there are no gateways to allow interworking between Ipv4 and Ipv6 multicast implementations.

#### 3.4.4.1 Planned European Deployments

As early as 2001, Eurocontrol and its Member States identified the need to introduce IPv6 for inter-ANSP data exchanges (which are typically cross-border) for both unicast and multicast network services.

Indeed, surveillance data flows that cross national borders are required to use the IPv6 protocol due to the architecture of the trans-national backbone network. Surveillance data flows that remain inside national borders use either IPv4 or IPv6 depending on the architecture of the national network infrastructure.

As source specific multicast (SSM) is particularly suited to inter-ANSP data exchanges, it use over IPv6 is recommended in a Eurocontrol guideline entitled “EUROCONTROL GUIDELINES FOR IMPLEMENTATION SUPPORT (EGIS) Part 5: COMMUNICATION & NAVIGATION SPECIFICATIONS, Chapter 12, SURVEILLANCE DISTRIBUTION OVER IP MULTICAST PROFILE REQUIREMENT LIST (PRL)”. Eurocontrol will indicate the URL of the above document once it is on-line.

Furthermore it is recommended that all surveillance data transmitters or receivers that are intended to send or receive data beyond the local domain, ie across national borders, should be IPv6-compliant as depicted in Figure 4-1.

The surveillance data is delivered using the source specific multicast (SSM) service. A data channel is defined by the combination of destination multicast address and source unicast address, and contains a single surveillance data flow.

Figure 4.1 SSM Multicast IPv6 address with global scopeIPv6

|   8    |  4 |  4 |   8    |    8   |       64       |    32    |

+--------+----+----+--------+--------+----------------+----------+

|11111111|0011|1110|00000000|00000000| 000……………………000 | group ID |

+--------+----+----+--------+--------+----------------+----------+

- The IPv6 multicast group ID shall be in the range 0x8000000 to 0xFFFFFFFF allowed for dynamic assignment by a host, as specified in  RFC 3307 section 4.3 and RFC 4607 section 1.

- The resulting available IPv6 SSM address range is FF3E::8000:0/97 (FF3E:0:0:0:0:0:8000:0 / 97).

- Assuming the appropriate access to the service, to receive a SSM (source specific multicast) stream one requires the following three parameters:

1. Source-address (unicast address)

2. Multicast address (as indicated by the source application)

3. Port (default is 8600 for ASTERIX surveillance data in Europe)

## 3.5 Transport Layer

The transport layer protocols are used to provide reliable or unreliable communication services over the ATN. There are two mandatory transport protocols, TCP and UDP.  TCP is used to provide reliable transport services and UDP is used to provide best effort service.  Other transport protocols may be used but can not affect ATN communications or services.

### 3.5.1 Transmission Control Protocol

The Internet Protocol (IP) works by exchanging groups of information called packets. Packets are short sequences of bytes consisting of a header and a body. The header describes the packet's routing information, which routers on the Internet use to pass the packet along in the right direction until it arrives at its final destination. The body contains the application information. TCP is optimized for accurate delivery rather than timely delivery, TCP sometimes incurs long delays while waiting for out-of-order messages or retransmissions of lost messages, and it is not particularly suitable for real-time applications like Voice over IP. Real time applications will require protocols like the Real-time Transport Protocol (RTP) running over the User Datagram Protocol (UDP).

TCP is a reliable stream delivery service that guarantees to deliver a stream of data sent from one host to another without duplication or losing data. Since packet transfer is not reliable, a technique known as positive acknowledgment with retransmission, is used to guarantee reliability of packet transfers. This fundamental technique requires the receiver to respond with an acknowledgment message as it receives the data. The sender keeps a record of each packet it sends, and waits for acknowledgment before sending the next packet. The sender also keeps a timer from when the packet was sent, and retransmits a packet if the timer expires. The timer is needed in case a packet becomes lost or corrupt.

In the event of congestion, the IP can discard packets, and, for efficiency reasons, two consecutive packets on the internet can take different routes to the destination. Then, the packets can arrive at the destination in the wrong order.

The TCP software libraries use the IP and provides a simpler interface to applications by hiding most of the underlying packet structures, rearranging out-of-order packets, minimizing network congestion, and re-transmitting discarded packets. Thus, TCP very significantly simplifies the task of writing network applications.

TCP provides a connection-oriented service with a reliable semantic. It operates above the network layer which does not necessarily detect and report all errors (e.g. corruption, misrouting). For this purpose, it provides:

- Error detection based on a checksum covering the transport header and payload as well as some vital network layer information.

- Recovery from error based on retransmission of erroneous or lost packets.

TCP is also designed for to detect and manage end-to-end network congestion and maximum user data segment sizes. This is essential for operation over heterogeneous sub networks with some low bandwidth / high latency trunks, such as the actual ATN Air/Ground sub networks.

### 3.5.2   User Datagram Protocol (UDP)

UDP provides a connectionless service with limited error detection and no recovery, nor congestion management mechanisms. It is naturally dedicated for light data exchanges, where undetected occasional loss or corruption of packets is acceptable, and when simplicity of use is a goal.

### 3.5.3 Transport Layer Addressing

Transport layer addressing relies on port numbers (16 bits integer values) that are associated with source and destinations endpoints to identify separate data streams.

Ports are classified in three categories with associated range of values:

- Well-known ports are those from 0 through 1023 and are assigned by IANA. On most systems these ports can only be used by system (or root) processes or by programs executed by privileged users. Such pre-defined well-known port numbers associated to distinct TCP and/or UDP applications, makes them visible (“well-known”) to client applications without specific knowledge / configuration.

- Registered ports are those from 1024 through 49151 and are registered by IANA following user request. Essentially such ports play the same role as well-known ports but for less critical or widespread applications. The use of such ports does not require specific privileges.

- Dynamic and/or private ports are those from 49152 through 65535. They may be used freely by applications.

Port assignment is obtained on request to IANA. An up-to-date image of the port registry is available at:

http://www.iana.org/assignments/port-numbers

This assignment plan is compulsory over the public Internet. It should be made applicable to ATN IPS (at least concerning well-known ports) in order to avoid conflicts between standard IPS applications (that may be used in ATN IPS environment) and ATN applications.

ATN/IPS hosts will require to support the following port numbers:

- tcp 102 for ATSMHS

- tcp 8500 for FMTP

### 3.5.4 Application Interface to the Transport Layer

The application interface to the TCP and UDP transport layers is provided consistently on a wide range of platform/operating systems according to the specification made in:

RFC 3493 - Basic Socket Interface Extensions for IPv6

This RFC extends the socket interface (originally developed by the Berkeley University for supporting IPv4 in their BSD Unix distribution) to IPv6.

### 3.5.5 Congestion Avoidance

In order to adapt to variables conditions for draining traffic in sub networks, TCP implements basically 4 mechanisms: slow-start, congestion-avoidance, fast-retransmit and fast-recovery. These are specified in:

RFC 2581 - TCP Congestion Control

The two first mechanisms aim at preventing important loss of packets when congestion occurs, while the two others attempt to shorten the delay for retransmitting the lost packets. These mechanisms are implemented independently in every end system, they don’t completely avoid loss of packets.

In the case of low bandwidth sub networks (e.g. ATN Air/Ground sub networks), TCP applications may make use of the Explicit Congestion Notification mechanism will more likely provide a significant benefit. It is specified by:

RFC 3168 - The Addition of Explicit Congestion Notification (ECN) to IP

This feature anticipates congestion, significantly reducing packet loss. However, it impacts the transport and network layers, and requires participation of a significant number of routers in the networks (preferentially, the routers at the edge of low speeds / high latency sub networks).

### 3.5.6 Error Detection and Recovery

TCP error detection relies on lack of timely received acknowledgement. Recovery is performed through retransmission of (supposed) lost packets.

Loss of a large numbers of packets in a short period of time may heavily incur the TCP connection throughput (hence performance). This may become critical for high latency sub networks (e.g. ATN Air/Ground sub networks).

Supports of TCP selective acknowledge option may mitigate this problem by allowing selective retransmission of lost packets only (instead of the whole sequence from the first to the last packet lost).  This option is specified in:

RFC 2018 - TCP Selective Acknowledgment Options

### 3.5.7 Performance Enhancing Proxies (PEPs)

Performance Enhancing Proxies (PEPs) are often employed to improve severely degraded TCP performance caused by different link characteristics in heterogeneous environments, e.g. in wireless or satellite environments that are common in aeronautical communications. Transport layer or application layer PEPs are applied to adapt the TCP parameters to the different link characteristics.

RFC3135 “Performance Enhancing Proxies Intended to Mitigate Link-Related Degradations” is a survey of PEP performance enhancement techniques, and describes some of the implications of using Performance Enhancing Proxies. Most implications of using PEPs result from the fact that the end-to-end semantics of connections are usually broken. In particular, PEPs disable the use of end-to-end IPsec encryption and have implications on mobility and handoff procedures.

4.0 Security Guidance

This section contains guidance for the optional ground-ground and air-ground security in the ATN/IPS.

Note. - Support for security is to be based on a system threat and vulnerability analysis and is not mandatory for implementation.

## 4.1 MOBILE IPv6

This manual specifies that the IP mobility solution for the ATN/IPS is Mobile IPv6 (MIPv6) as specified in RFC 3775.  With Mobile IP a mobile node (MN) has two addresses: a home address (HoA), which is a permanent address, and a dynamic care-of address (CoA), which changes as the mobile node changes its point of attachment.  The fundamental technique of Mobile IP is forwarding. A correspondent node (CN), which is any peer node with which a mobile node is communicating, sends packets to the home agent (HA) of the mobile node.  The CN reaches the HA through normal IP routing.  Upon receipt of a packet from the CN,  the HA will forward these packets to the MN at its current CoA.  The HA simply tunnels the original packet in another packet with its own source address and a destination address of the current CoA. This is possible because of the Mobile IP protocol whereby the MN sends “binding update” messages to the HA whenever its point of attachment changes.  The binding update associates the mobile nodes HoA with its current CoA.  The HA maintains a Binding Cash that stores the current CoA of the MN.  In the reverse direction, the MN could simply send packets directly to the CN using normal IP routing.  However, this results in triangular routing and depending on the relative location of the HA, there can be a situation where the path in one direction (e.g. CN to HA to MN) is significantly longer than the path in the reverse direction (e.g., MN to CA).  A further consideration in this case occurs if the MN uses its home address as a source address.  The problem here is that many networks perform ingress filtering of incoming packets and will not accept packets that are topologically incorrect. This would be the case with packets from the MN because they actually originate from the care-of-address but the source address in the IP packet is the home address.  Because of these issues, MIPv6 allows the MN to follow the same path back to the CN via the HA using bidirectional tunneling whereby in addition to the HA tunneling packets to the MN, the MN reverse tunnels packets to the HA.  The HA will decapsulate a tunneled IP packet and forward it to the CN.  With bidirectional tunneling the CN is not required to support Mobile IP.

Bidirectional tunneling solves the problems of triangular routing and ingress filtering; however, there still can be suboptimal routing since the path from the MN to the CN via the HA may be relatively long in cases where the MN and CN are in close proximity.  With MIPv6 the situation where the path through the HA is longer than a direct path to the CN may be addressed using a technique called route optimization.  With route optimization the MN sends binding updates to both the HA and the CN.  In this case the MN and CN can communicate directly and adapt to changes in the MN’s CoA. RFC 3775 defines the procedures for route optimization.  It requires that the MN initiate the return routability procedure.  This procedure provides the CN with some reasonable assurance that the MN is addressable at its claimed care-of address and its home address.

Binding update messages to the HA or CN must be secured.  The essential requirements for Mobile IPv6 security are specified in the base Mobile IPv6 specification, [RFC 3775].  This ATN/IPS manual also requires support for “Mobile IPv6 Operation with IKEv2 and the revised IPsec Architecture” [RFC 4877].  RFC 4877 specifies the use of IPsec under the latest version of IPsec Architecture [RFC 4301] and describes how IPsec can be used with version 2 of the Internet Key Agreement protocol IKEv2 [RFC 4306].

## 4.2 Enhancements to MIPv6

When a mobile node (MN) changes its point of attachment to the network, the changes may cause delay, packet loss, and generally result in overhead traffic on the network.

One technology developed to address these issues is “Heirarchical Mobile IPv6 (HMIPv6)” [RFC 4140].  RFC 4140 introduces extensions to Mobile IPv6 and IPv6 Neighbor Discovery to allow for local mobility handling.  HMIPv6 reduces the amount of signaling between a MN, its CNs, and its HA.  HMIPv6 introduces the concept of the Mobility Anchor Point (MAP).  A MAP is essentially a local home agent for a mobile node.  A mobile node entering a MAP domain (i.e., a visited access network) will receive Router Advertisements containing information about one or more local MAPs. The MN can bind its current location, i.e., its On-link Care-of Address (LCoA), with an address on the MAP's subnet, called a Regional Care-of Address (RCoA).  Acting as a local HA, the MAP will receive all packets on behalf of the mobile node it is serving and will encapsulate and forward them directly to the mobile node's current address.  If the mobile node changes its current address within a local MAP domain (LCoA), it only needs to register the new address with the MAP.  The RCoA does not change as long as the MN moves within a MAP domain.  RFC 4140 notes that the use of the MAP does not assume that a permanent HA is present, that is, a MN need not have a permanent HoA or HA in order to be HMIPv6-aware or use the features of HMIPv6.  HMIPv6-aware mobile nodes can use their RCoA as the source address without using a Home Address option.  In this way, the RCoA can be used as an identifier address for upper layers.  Using this feature, the mobile node will be seen by the correspondent node as a fixed node while moving within a MAP domain. This usage of the RCoA does not have the cost of Mobile IPv6 (i.e., no bindings or home address options are sent back to the HA), but still provides local mobility management to the mobile nodes with near-optimal routing. Although such use of RCoA does not provide global mobility.

A further enhancement to MIPv6 is “Fast Handovers for Mobile IPv6 (FMIPv6)” [RFC 4068].  FMIPv6 attempts to reduce the chance of packet loss through low latency handoffs. FMIPv6 attempts to optimize handovers by obtaining information for a new access router before disconnecting from the previous access router.  Access routers request information from other access routers to acquire neighborhood information that will facilitate handover.  Once the new access router is selected a tunnel is established between the old and new router.  The previous Care-of Address (pCoA) is bound to a new Care-of Address (nCoA) so that data may be tunneled from the previous Access Router to the new Access Router during handover.  Combining HMIPv6 and FMIPv6 would contribute to improved MIPv6 performance but this comes at the cost of increased complexity.

In addition the the HMIPv6 and FMIPv6 enhancements, there is ongoing analysis in the IRTF to define enhancements to MIPv6 route optimization.  RFC 4651 presents a taxonomy and analysis of enhancements to MIPv6 route optimization.  This document notes that the two reachability tests of the return routability procedure can lead to a handoff delay unacceptable for many real-time or interactive applications, that the security that the return-routability procedure guarantees might not be sufficientvfor security-sensitive applications, and periodically refreshing a registration at a correspondent node implies a hidden signaling overhead.  RFC 4651 concludes that although IPv6 deployment is yet far away from becoming widespread, the sooner efficient route optimization will be available the more likely that it will in the end be ubiquitously supported.

## 4.3 Proxy Mobile IPv6

Although this manual specifies MIPv6 as the baseline for network-based mobility, access network service providers may optionally provide network-based mobility using for example Proxy Mobile IPv6 (PMIPv6).  Network-based mobility is another approach to solving the IP mobility challenge.  It is possible to support mobility for IPv6 nodes without host involvement by extending Mobile IPv6 [RFC-3775] signaling messages between a network node and a home agent.  This approach to supporting mobility does not require the mobile node to be involved in the exchange of signaling messages between itself and the home agent.  A proxy mobility agent in the network performs the signaling with the home agent and does the mobility management on behalf of the mobile node attached to the network.  The core functional entities for PMIPv6 are the Local Mobility Anchor (LMA) and the Mobile Access Gateway (MAG).  The local mobility anchor is responsible for maintaining the mobile node's reachability state and is the topological anchor point for the mobile node's home network prefix(es).  The mobile access gateway is the entity that performs the mobility management on behalf of a mobile node and it resides on the access link where the mobile node is anchored.  The mobile access gateway is responsible for detecting the mobile node's movements to and from the access link and for initiating binding registrations to the mobile node's local mobility anchor.

An access network which supports network mobility would be agnostic to the capability in the IPv6 stack of the nodes which it serves.  IP mobility for nodes which have mobile IP client functionality in the IPv6 stack as well as those nodes which do not, would be supported by enabling Proxy Mobile IPv6 protocol functionality in the network.  The advantages of PMIPv6 are reuse of home agent functionality and the messages/format used in  mobility signaling and common home agent would serve as the mobility agent for all types of IPv6 nodes.  PMIPv6 like HMIPv6 is a local mobility management approach which further reduces the air-ground signalling overhead.  Using PMIPv6 would also facilitate use of an AAA infrastructure for network access control since this function may be performed by the MAG.

# APPENDIX A – REFERENCE DOCUMENTS

IETF STANDARDS AND PROTOCOLS

The following documents are available publicly at http://www.ietf.org and form part of this manual to the extent specified herein. In the event of conflict between the documents referenced herein and the contents of this manual, the provisions of this manual shall take precedence.

Request for Comments (RFCs)

netlmm-mn-ar-if

Network-based Localized Mobility Management Interface between Mobile Node and Mobility Access Gateway, May 2007

RFC-768	User Datagram Protocol, August 1980

RFC-793	Transmission Control Protocol (TCP), September 1981

RFC-1006	ISO Transport Service on top of TCP, May 1987

RFC-1323	TCP Extensions for High Performance May 1992

RFC-1981	Path Maximum Transmission Unit (MTU) Discovery for IP Version 6, August 1996

RFC-2126	ISO Transport Service on top of TCP, March 1997

RFC-2460	Internet Protocol, Version 6 (IPv6) Specification, December 1998

RFC-2474	Differential Services Field, December 1998

RFC-2488	Enhancing TCP over Satellite Channels, January 1999

RFC-2858	Border Gateway Protocol (BGP4) Multiprotocol Extensions June 2000

RFC-3775	Mobility Support in IPv6,  June 2004

RFC-4271	A Border Gateway Protocol 4 (BGP-4), January 2006

RFC-4291	IP Version 6 Addressing Architecture, February 2006

RFC-4301	Security Architecture for the Internet Protocol, December, 2005

RFC-4302	Internet Protocol (IP) Authentication Header, December 2005

RFC-4303	IP Encapsulating Security Payload (ESP), December 2005RFC-4305	Cryptographic Algorithm Implementation Requirements for Encapsulating Security Payload (ESP) and Authentication Header (AH) – (NB proposed standard, obsoletes RFC-2402, RFC-2406), December 2005

RFC-4306	Internet Key Exchange (IKEv2) Protocol, December 2005

RFC-4307	Cryptographic Algorithms for Use in the Internet Key Exchange Version 2 (IKEv2), December 2005

RFC-4443	Internet Control Message Protocol (ICMPv6) for the Internet Protocol Version 6 (IPv6) Specification, March 2006

RFC-4492	Elliptic Curve Cryptography (ECC) Cipher Suites for Transport Layer Security, May 2006

RFC 4555	IKEv2 Mobility and Multihoming Protocol (MOBIKE),  June 2006

RFC 4830	Problem Statement for Network-Based Localized Mobility Management (NETLMM), April 2007

RFC 4831	Goals for Network-Based Localized Mobility Management (NETLMM), April 2007

RELEVANT ICAO PUBLICATIONS

In the event of a conflict between the manual and the provisions in Annex 10, the provisions of Annex 10 shall take precedence.

ICAO Annex 2 Rules of the Air

ICAO Annex 3 Meteorological Service for International Air Navigation

ICAO Annex 10 Aeronautical Telecommunications – Volume III, Part I – Digital Data Communication Systems

ICAO Annex 11 Air Traffic Services

ICAO Doc. 9705-AN/956 Edition 3, Manual of Technical Provisions for the ATN, 2002

ICAO Doc. 9739 Edition 1, Comprehensive ATN Manual (CAMAL), 2000

ICAO Doc. 4444 Procedures for Air Navigation Services – Air Traffic Management 14th Edition, 2001

ICAO Doc. 9694 Manual of Air Traffic Services Data Link Applications

ICAO Doc. 9880 Detailed Technical Specifications for the Aeronautical Telecommunication Network (ATN) using ISO/OSI protocols

EUROCONTROL SPECIFICATIONS

The following documents are available publicly at http://www.eurocontrol.int/ses and form part of this manual to the extent specified herein. In the event of conflict between the documents referenced herein and the contents of this manual, the provisions of this manual shall take precedence.

EUROCONTROL-SPEC-0100	EUROCONTROL Specifications of Interoperability and Performance Requirements for the Flight Message Transfer Protocol (FMTP), Edition 2.0, June 2007

EUROCONTROL-SPEC-0106	EUROCONTROL Specifications for On-Line Data Interchange (OLDI), Edition 4.0, October 2007

# APPENDIX B – ABBREVIATIONS/DEFINITIONS

The acronyms used in this manual are defined as follows:

AAC		Aeronautical Administrative Communications

AOC		Aeronautical Operational Communications

AS		Autonomous System

AD		Administrative Domain

AH		Authentication Header

AIDC		ATS Interfacility Data Communications

AINSC	Aeronautical Industry Service Communication

AN		Access Network

ATSMHS	ATS Message Handling Services

ATN		Aeronautical Telecommunication Network

ATC		Air Traffic Control

ATS		Air Traffic Services

ATSU		ATS Unit

ATSC		Air Traffic Services Communication

BGP		Border Gateway Protocol

CL		Connection-less

CN		Correspondent Node

CO		Connection-oriented

ECC		Elliptic Curve Cryptography (ECC)ECP		Encryption Control Protocol

ESP		Encapsulating Security Protocol

FIR		Flight Information Region

FMTP		Flight Message Transfer Protocol

G-G		Ground- to- Ground

HC		Handover Control

H-MM		Host-based Mobility Management

IANA		Internet Assigned Numbers Authority

ICAO		International Civil Aviation Organization

ICMP		Internet Control Message Protocol

IETF		Internet Engineering Task Force

IKEv2		Internet Key Exchange (version2)

IP		Internet Protocol

IPS		Internet Protocol Suite

IPsec		IP Security

IPv6		Internet Protocol version 6

ISO		International Organization for Standardization

LAN		Local Area Network

LM		Location Management

MM		Mobility Management

MN		Mobile Node

MTU		Maximum Transmission Unit

N-MM		Network-based Mobility Management

OLDI		On-Line Data Interchange

OSI		Open System Interconnection

QoS		Quality of Service

RFC		Request for Comments

TCP		Transmission Control Protocol

TLS		Transport Layer Security

SARPs		Standards and Recommended Practices

SPI		Security Parameter Index

UDP		User Datagram Protocol

WAN		Wide Area Network

DEFINITIONS

Definitions are consistent with IETF terminology.

Access Network

A network that is characterized by a specific access technology.

Administrative Domain

An administrative entity in the ATN/IPS.  An Administrative Domain can be an individual State, a group of States, an Aeronautical Industry Organization (e.g., an Air-Ground Service Provider), or an Air Navigation Service Provider (ANSP) that manages ATN/IPS network resources and services.  From a routing perspective, an Administrative Domain includes one or more Autonomous Systems.

ATN/IPS Internetwork

The ATN/IPS internetwork consists of IPS nodes and networks operating in a multinational environment.

Autonomous System

A connected group of one or more IP prefixes, run by one or more network operators, which has a single, clearly defined routing policy.

Global Mobility

Global Mobility is mobility across access networks.

Handover Control

The handover control (HC) function is used to provide the ‘session continuity’ for the ‘on-going’ session of the mobile node.

Host	A host is a node that is not a router.  A host is a computer connected to the ATN/IPS that provides end users with services.

Host-based Mobility Management

A mobility management scheme in which MM signaling is performed by the mobile node.

IPS Mobile node

an IPS node that uses the services of one or more MSPs.

Local Mobility

Local Mobility is network layer mobility within an access network.

Location Management

The location management (LM) function is used to keep track of the movement of a mobile node and to locate the mobile node for data delivery.

Mobility Service Provider (MSP)

is a service provider that provides Mobile IPv6 service (i.e. Home Agents), within the ATN/IPS. A MSP is an instance of an AD which may be an ACSP, ANSP, airline, airport authority, government organization, etc.

Network-based Mobility Management

A mobility management scheme in which the MM signaling is performed by the network entities on behalf of the mobile node.

Node		A device that implements IPv6

Router	A router is an node that forwards Internet Protocol (IP) packets not explicitly addressed to itself.   A router manages the relaying and routing of data while in transit from an originating end system to a destination end system.

Inter-Domain Routing (Exterior Routing Protocol)

Protocols for exchanging routing information between Autonomous Systems.  They may in some cases be used between routers within an AS, but they primarily deal with exchanging information between Autonomous Systems.

Intra-Domain Routing (Interior Routing Protocol)

Protocols for exchanging routing information between routers within an AS.

# APPENDIX C – AS Numbering Plan

| ICAO Region | Country/Organisation/Location | ASN |  | ICAO Region | Country/Org./Loc. | ASN |
| --- | --- | --- | --- | --- | --- | --- |
| MID | Afghanistan | 64512 |  | EUR/NAT | Ireland | 64688 |
| APAC | American Samoa | 64513 |  | EUR/NAT | Italy | 64692 |
| ESAF | Angola | 64514 |  | EUR/NAT | Kazakhstan | 64696 |
| NACC | Anguilla I. (U.K.) | 64515 |  | EUR/NAT | Kyrgyzstan | 64700 |
| NACC | Antigua and Barbuda | 64516 |  | EUR/NAT | Latvia | 64704 |
| SAM | Argentina | 64517 |  | EUR/NAT | Liechtenstein | 64706 |
| NACC | Aruba (Netherlands) | 64518 |  | EUR/NAT | Lithuania | 64708 |
| WACAF | Ascension and St Helena Is. (U.K.) | 64519 |  | EUR/NAT | Luxembourg | 64712 |
| APAC | Australia | 64520 |  | EUR/NAT | The former Yugoslav Republic of Macedonia | 64716 |
| NACC | Bahamas | 64521 |  | EUR/NAT | Malta | 64720 |
| APAC | Bangladesh | 64522 |  | EUR/NAT | Monaco | 64724 |
| NACC | Barbados | 64523 |  | EUR/NAT | Montenegro | 64725 |
| NACC | Belize | 64524 |  | EUR/NAT | Morocco | 64726 |
| WACAF | Benin | 64525 |  | EUR/NAT | Netherlands | 64728 |
| NACC | Bermuda (U.K.) | 64526 |  | EUR/NAT | Norway | 64732 |
| APAC | Bhutan | 64527 |  | EUR/NAT | Poland | 64736 |
| SAM | Bolivarian Republic of Venezuela | 64528 |  | EUR/NAT | Portugal | 64740 |
| SAM | Bolivia | 64529 |  | EUR/NAT | Republic of Moldova | 64744 |
| ESAF | Botswana | 64530 |  | EUR/NAT | Romania | 64748 |
| SAM | Brazil | 64531 |  | EUR/NAT | Serbia | 64752 |
| ESAF | British Indian Ocean Territory | 64532 |  | EUR/NAT | Russian Federation | 64756 |
| APAC | Brunei Darussalam | 64533 |  | EUR/NAT | San Marino | 64758 |
| WACAF | Burkina Faso | 64534 |  | EUR/NAT | Slovak Republic | 64760 |
| ESAF | Burundi | 64535 |  | EUR/NAT | Slovenia | 64764 |
| APAC | Cambodia | 64536 |  | EUR/NAT | Spain | 64768 |
| WACAF | Cameroon | 64537 |  | EUR/NAT | Sweden | 64772 |
| NACC | Canada | 64538 |  | EUR/NAT | Tajikistan | 64776 |
| WACAF | Cape Verde | 64539 |  | EUR/NAT | Switzerland | 64780 |
| NACC | Cayman Is. (U.K.) | 64540 |  | EUR/NAT | The Holy See | 64781 |
| WACAF | Central African Republic | 64541 |  | EUR/NAT | Tunisia | 64782 |
| WACAF | Chad | 64542 |  | EUR/NAT | Turkey | 64784 |
| SAM | Chile | 64543 |  | EUR/NAT | Turkmenistan | 64788 |
| APAC | China | 64544 |  | EUR/NAT | Ukraine | 64792 |
| SAM | Colombia | 64545 |  | EUR/NAT | United Kingdom | 64796 |
| WACAF | Congo | 64546 |  | EUR/NAT | Uzbekistan | 64800 |
| APAC | Cook Islands | 64547 |  | EUR/NAT | Regional - Benelux/Germany | 65108 |
| NACC | Costa Rica | 64548 |  | EUR/NAT | Regional - Central Europe | 65112 |
| WACAF | Côte d'Ivoire | 64549 |  | EUR/NAT | EUROCONTROL | 65208 |
| NACC | Cuba | 64550 |  | EUR/NAT | EUROCONTROL | 65212 |
| APAC | Democratic People's Republic of Korea | 64551 |  | EUR/NAT | EUROCONTROL | 65216 |
| WACAF | Democratic Republic of the Congo | 64552 |  | EUR/NAT | EUROCONTROL | 65220 |
| APAC | Democratic Republic of Timor-Leste | 64553 |  | EUR/NAT | EUROCONTROL | 65224 |
| ESAF | Djibouti | 64554 |  | EUR/NAT | EUROCONTROL | 65228 |
| NACC | Dominica | 64555 |  | EUR/NAT | EUROCONTROL | 65232 |
| NACC | Dominican Republic | 64556 |  | EUR/NAT | EUROCONTROL | 65236 |
| APAC | Easter Island (Chile) | 64557 |  | WACAF | Mauritania | 65237 |
| SAM | Ecuador | 64558 |  | ESAF | Mauritius | 65238 |
| MID | Egypt | 64559 |  | NACC | Mexico | 65239 |
| NACC | El Salvador | 64560 |  | APAC | Micronesia, Federated States of | 65240 |
| WACAF | Equatorial Guinea | 64561 |  | APAC | Midway Is. (U.S.) | 65241 |
| ESAF | Eritrea | 64562 |  | APAC | Mongolia | 65242 |
| ESAF | Ethiopia | 64563 |  | NACC | Montserrat I. (U.K.) | 65243 |
| SAM | Falklands Is. (U.K.) | 64564 |  | ESAF | Mozambique | 65244 |
| NACC | French Antilles (?) | 64565 |  | APAC | Myanmar | 65245 |
| WACAF | Gabon | 64566 |  | ESAF | Namibia | 65246 |
| WACAF | Gambia | 64567 |  | APAC | Nauru | 65247 |
| WACAF | Ghana | 64568 |  | APAC | Nepal | 65248 |
| NACC | Grenada | 64569 |  | NACC | Netherlands Antilles | 65249 |
| APAC | Guam (U.S.) ? | 64570 |  | APAC | New Caledonia | 65250 |
| NACC | Guatemala | 64571 |  | APAC | New Zealand | 65251 |
| WACAF | Guinea | 64572 |  | NACC | Nicaragua | 65252 |
| WACAF | Guinea-Bissau | 64573 |  | WACAF | Niger | 65253 |
| SAM | Guyana | 64574 |  | WACAF | Nigeria | 65254 |
| SAM | Guyane Francaise | 64575 |  | APAC | Niue Island (New Zealand) | 65255 |
| NACC | Haiti | 64576 |  | MID | Oman | 65256 |
| SAM | Honduras | 64577 |  | MID | Pakistan | 65257 |
| APAC | Hong Kong Special Administrative Region of China | 64578 |  | APAC | Palau | 65258 |
| APAC | Iles Wallis Et Futuna (France) | 64579 |  |  | Palestinian Territory, occupied | 65259 |
| APAC | India | 64580 |  | APAC | Palmyra Is. (U.S.) | 65260 |
| APAC | Indonesia | 64581 |  | SAM | Panama | 65261 |
| MID | Iran, Islamic Republic of | 64582 |  | APAC | Papua New Guinea | 65262 |
| MID | Iraq | 64583 |  | SAM | Paraguay | 65263 |
| MID | Israel | 64584 |  | SAM | Peru | 65264 |
| NACC | Jamaica | 64585 |  | APAC | Philippines | 65265 |
| APAC | Japan | 64586 |  | APAC | Pitcairn Island (U.K.) | 65266 |
| APAC | Johnston I. (U.S.) | 64587 |  | APAC | Polynesie Francaise | 65267 |
| MID | Jordan | 64588 |  | NACC | Puerto Rico | 65268 |
| ESAF | Kenya | 64589 |  | MID | Qatar | 65269 |
| MID | Kingdom of Bahrain | 64590 |  | APAC | Republic of Korea | 65270 |
| APAC | Kingman Reef (U.S.) ? | 64591 |  | APAC | Republic of the Fiji Islands | 65271 |
| APAC | Kiribati | 64592 |  | ESAF | Rwanda | 65272 |
| MID | Kuwait | 64593 |  | NACC | Saint Kitts and Nevis | 65273 |
| ESAF | La Reunion (France) | 64594 |  | NACC | Saint Lucia | 65274 |
| APAC | Lao People's Democratic Republic | 64595 |  | NACC | Saint Vincent and the Grenadines | 65275 |
| MID | Lebanon | 64596 |  | APAC | Samoa | 65276 |
| ESAF | Lesotho | 64597 |  | WACAF | Sao Tome and Principe | 65277 |
| WACAF | Liberia | 64598 |  | MID | Saudi Arabia | 65278 |
| MID | Libyan Arab Jamahiriya | 64599 |  | WACAF | Senegal | 65279 |
| APAC | Macao Special Administrative Region of China | 64600 |  | ESAF | Seychelles | 65280 |
| ESAF | Madagascar | 64601 |  | WACAF | Sierra Leone | 65281 |
| ESAF | Malawi | 64602 |  | APAC | Singapore | 65282 |
| APAC | Malaysia | 64603 |  | APAC | Solomon Islands | 65283 |
| APAC | Maldives | 64604 |  | ESAF | Somali Republic | 65284 |
| WACAF | Mali | 64605 |  | ESAF | South Africa | 65285 |
| APAC | Mariana Is. (U.S.) | 64606 |  | APAC | Sri Lanka | 65286 |
| APAC | Marshall Islands | 64607 |  | MID | Sudan | 65287 |
| EUR/NAT | Albania | 64608 |  | SAM | Suriname | 65288 |
| EUR/NAT | Algeria | 64609 |  | ESAF | Swaziland | 65289 |
| EUR/NAT | Andorra | 64610 |  | MID | Syrian Arab Republic | 65290 |
| EUR/NAT | Armenia | 64612 |  | APAC | Thailand | 65291 |
| EUR/NAT | Austria | 64616 |  | WACAF | Togo | 65292 |
| EUR/NAT | Republic of Azerbaijan | 64620 |  | APAC | Tonga | 65293 |
| EUR/NAT | Belarus | 64624 |  | NACC | Trinidad And Tobago | 65294 |
| EUR/NAT | Belgium | 64628 |  | NACC | Turks And Caicos Islands (U.K.) | 65295 |
| EUR/NAT | Bosnia and Herzegovina | 64632 |  | APAC | Tuvalu | 65296 |
| EUR/NAT | Bulgaria | 64636 |  | ESAF | Uganda | 65297 |
| EUR/NAT | Croatia | 64640 |  | ESAF | Union of the Comoros | 65298 |
| MID | Cyprus | 64644 |  | MID | United Arab Emirates | 65299 |
| EUR/NAT | Czech Republic | 64648 |  | ESAF | United Republic of Tanzania | 65300 |
| EUR/NAT | Denmark | 64652 |  | NACC | United States of America | 65301 |
| EUR/NAT | Estonia | 64656 |  | SAM | Uruguay | 65302 |
| EUR/NAT | Finland | 64660 |  | APAC | Vanuatu | 65303 |
| EUR/NAT | France | 64664 |  | APAC | Viet Nam | 65304 |
| EUR/NAT | Georgia | 64668 |  | NACC | Virgin Islands (U.K.) | 65305 |
| EUR/NAT | Germany | 64672 |  | NACC | Virgin Islands (U.S.) | 65306 |
|  | Gibraltar | 64674 |  | APAC | Wake I. (U.S.) | 65307 |
| EUR/NAT | Greece | 64676 |  |  | Western Sahara | 65308 |
|  | Greenland | 64678 |  | MID | Yemen | 65309 |
| EUR/NAT | Hungary | 64680 |  | ESAF | Zambia | 65310 |
| EUR/NAT | Iceland | 64684 |  | ESAF | Zimbabwe | 65311 |

# Text boxes

Video

Codecs

H.261

H.263

H.450.1 Series

(Supplementary Services)

IP (Internet Protocol) v4 or v6

TCP (Transfer Control Protocol)

UDP (User Datagram Protocol)

H.235 (Security)

H.245

(Control

Signalling)

H.225.0

RAS

Q.931

(Call Signalling)

T.120

(Real Time)

T.130

(Audio- Visual

Control)

RTP

RTCP

(Real Time TransportControl Protocol)

Audio

Codecs

G.711

G.728

G.729

IPS

IPS DS

ATN-App ASE

Application User