|  |  | ACP-WG-I-08/WP-xx 25 August 2008 |
| --- | --- | --- |

AERONAUTICAL COMMUNICATIONS PANEL (ACP)

WG I – Internet Protocol Suite

IPS Manual and Guidance Air-Ground Application Sections

Prepared by:

Greg Saccone

Christophe Grassaud

Pierre Vabre

Eivan Cerasi

ICAO

Aeronautical Telecommunication Network (ATN)

Manual for the ATN using IPS Standards and Protocols (Doc 9896)

Part II

IPS Applications

Part II Table of Contents

To be updated…..

# INTRODUCTION

## Objective

The legacy DS served as an interface between the dialogue service and the upper layers (session down) via the control function.  In order to minimize the impacts to the legacy ATN applications, a new dialogue service that allows the legacy ATN applications to operate over the ATN IPS is introduced.  This section specifies a replacement for the ULCS Dialogue Service (DS) interface to the upper layers, called the IPS DS.

The IPS DS does not have an interface to the session layer; instead it is mapped to TCP/UDP primitives in a fashion similar to RFC1006 for TP0 over TCP/IP.  This is depicted in Figure 1.1-1.  One of the differences is that for the IPS DS, there is no transport-transport interface.  It is an upper layer to transport interface, i.e. a service above TCP/UDP.  While conceptually similar, the upper layers will be interfacing with transport services instead of network services.

Figure 1.1-1.  ATN IPS Upper Layers Diagram

## Legacy ATN/OSI Applications, using IPS

Note 1 . – Legacy ATN applications are defined in Doc 9705 and/or Doc 9880. The ATN applications described in Doc 9705/9880 specify the use of the ATN/OSI layers for lower layer communications, termed the Internet Communication Services. This section indicates how those applications interface with the ATN/IPS.

Note 2. – In order to accommodate legacy ATN/OSI air-ground applications over the IPS, the following IPS Dialogue Service (DS) definition is used.  Parameters from the ATN/OSI DS will be mapped as detailed in the sections below.  This mapping supersedes the ULCS specification of ICAO Doc 9705 and Doc 9880.

Note 3. – The ATNPKT header format defined below describes a dedicated format designed to accommodate the passing of legacy ATN application data over the ATN IPS.  Either TCP or UDP may be used with the ATNPKT header format.

### CPDLC, ADS and FIS

#### IPS hosts that support the ATN/OSI Controller-Pilot Data Link (CPDLC), Automatic Dependent Surveillance (ADS) and Flight Information Services (FIS) applications shall comply with Doc 9705 or Doc 9880.

### CM

#### IPS hosts that support the ATN/OSI Context Management (CM) application shall comply with Doc 9880.

Note 1. – This is in order to allow passing the new IPS addressing information contained in the updated CM application ASN.1

### ATN IPS Dialogue Service Description

#### Scope of Dialogue Service

### Service Primitives

Note. – In order to retain commonality with the ULCS dialogue service primitives described in Doc 9880, the IPS DS uses the same primitive names.

#### Implementations which claim to support the DS functionality shall exhibit the behaviour defined by the service primitives in Table Table 0-1.

Table 1.2-1.  Summary of Dialogue Service Primitives

| Service | Description |
| --- | --- |
| D-START | This is a confirmed service used to establish the binding between the communicating DS-Users. |
| D-DATA | This unconfirmed service is used by a DS-User to send a message from that DS-User to the peer DS-User. |
| D-END | This is a confirmed service used to provide the orderly unbinding between the communicating DS-Users, such that any data in transit between the partners is delivered before the unbinding takes effect. |
| D-ABORT | This unconfirmed service can be invoked to abort the relationship between the communicating DS-Users. Any data in transit between them may be lost. |
| D-P-ABORT | This unconfirmed service is used to indicate to the DS-User that the dialogue service provider has aborted the relationship with the peer DS-User. Any data in transit between the communicating DS-Users may be lost. |
| D-UNIT-DATA | This unconfirmed service is used to send a single data item from one peer DS-User to another. Any problem in delivering the data item to the recipient will not be signalled to the originator. This service is specified in 2.7. |

Table 1.2-2.  Parameters of the Dialogue Service Primitives

| Service | Parameters |
| --- | --- |
| D-START | Called Peer ID Called Sys-ID Called Presentation Address Calling Peer ID Calling Sys-ID Calling Presentation Address DS-User Version Number Security Requirements Quality-of-Service Result Reject Source User Data |
| D-DATA | User Data |
| D-END | Result User Data |
| D-ABORT | Originator User Data |
| D-P-ABORT | (no parameters) |

Note. – The parameters of the dialogue service primitives are mapped to either the IP header, a field of the transport protocol header, or as transport data in the ATNPKT format defined in 1.3.5.2.

### Dialogue Service Definition

#### Sequence of Primitives

##### Implementations which claim to support the DS functionality shall exhibit behaviour allowing two communicating DS-Users to:

a)	establish a dialogue;

b)	exchange user data;

c)	terminate a dialogue in an orderly or abnormal fashion; and

d)	be informed of DS abnormal dialogue termination due to the underlying communications failure;

consistent with the appropriate use of the corresponding service primitives.

##### Either DS-User may send data at any time after the initial D-START exchange, by using the D-DATA service.  Under normal circumstances, a dialogue is released by a DS-User invoking the D-END service.  A dialogue is abnormally released with the D-ABORT service.  If the underlying service provider abnormally releases the dialogue, the DS-Users which are aware of the dialogue will be notified with the D-P-ABORT service.

##### For the purposes of this service definition, it is only valid for the DS-User to issue and be prepared to receive primitives for one Dialogue according to the permitted sequences of DS primitives shown in Table 1.3-3, where intersections marked “Y” show possible primitives which may occur after the primitive in the column heading.

Table 1.2-3.  Sequence of DS primitives for one Dialogue at one DS-User

| The DS primitive -> | D-START | D-DATA | D-END | D-ABORT | D-P-ABORT |
| --- | --- | --- | --- | --- | --- |
| May be followed by the DS primitive Y | req | cnf | ind | rsp | req | ind | req | cnf | ind | rsp | req | ind | ind |
| 1 D-START req |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 2 D-START cnf (accepted) | Y |  |  |  |  |  |  |  |  |  |  |  |  |
| 3 D-START ind |  |  |  |  |  |  |  | Y |  | Y | Y | Y | Y |
| 4 D-START rsp (accepted) |  |  | Y |  |  |  |  |  |  |  |  |  |  |
| 5 D-DATA req |  | Y |  | Y | Y | Y |  |  | Y |  |  |  |  |
| 6 D-DATA ind |  | Y |  | Y | Y | Y | Y |  |  |  |  |  |  |
| 7 D-END req |  | Y |  | Y | Y | Y |  |  |  |  |  |  |  |
| 8 D-END cnf (accepted) |  |  |  |  |  |  | Y |  |  |  |  |  |  |
| 9 D-END ind |  | Y |  | Y | Y | Y |  |  |  |  |  |  |  |
| 10 D-END rsp (accepted) |  |  |  |  |  |  |  |  | Y |  |  |  |  |
| 11 D-ABORT req | Y | Y | Y | Y | Y | Y | Y |  | Y |  |  |  |  |
| 12 D-ABORT ind | Y | Y | Y | Y | Y | Y | Y |  | Y |  |  |  |  |
| 13 D-P-ABORT ind | Y | Y | Y | Y | Y | Y | Y |  | Y |  |  |  |  |

#### ATNPKT Format

The purpose of the ATNPKT is to convey information between peer DS-Users during the processing of a DS primitive.  It is carried in the data part of the transport protocol (either TCP or UDP).  It is used to convey parameters of the service primitives that cannot be mapped to existing IP or transport header fields. The ATNPKT will also convey information to allow the Dialogue Service protocol function (e.g. the type of DS primitive).

In order to provide the most efficient use of bandwith, a variable length format is used which depends on the processed DS primitive in order to optimize the amount of bytes being transferred. This is an important issue when operating over narrow band or costly air ground communication links.

The ATNPKT format is split in two parts:

- a fixed part containing parameters that are present regardless of the DS primitive, and

- a variable part containing optional fields.

In order to handle optional parameters, the presence of the ATNPKT fields will be indicated by a bit field included in the fixed part ('Presence Flag'). Their position in the variable part will be determined by their position in the bit field. Their representation will depend on their characteristics; the ones with a variable length will be represented in LV format (i.e. Length + Value), for the others only the value will be required.  The ATNPKT format is shown in Figure 1.3-1.

Figure 1.3-1.  ATNPKT Format

#### ATNKPKT Fields

##### Each of the ATNPKT fields is described below using the following conventions:

- the field characteristics are given between brackets ( <bits> /<provider> / <usage> )

- the <bits> field is the length of the value field (not including the length itself),

- the <provider> field indicates if the value is provided by the DS-User as primitive parameter (external) or assigned by the DS-Provider itself (internal),

- the <usage> field indicates whether or not the DS-User may omit to provide a value for the corresponding primitive parameter (optional vs. mandatory).

#### Fixed Part of ATNPKT

##### ATNPKT Version:

Note. – The ATNPKT version indicates the version of the ATNPKT header currently being used.

###### The ATNPKT version shall be set to 1 for the present specification and have a format of (4 bits / internal / mandatory).

Note 1.  – The ATNPKT version will be rolled to account for any subsequent modifications to the packet format.

Note 2.  – Reserving 4 bits will give provision for up to 15 versions; this is considered to be more than enough provided that the future applications are not supposed to use the Dialogue Service; rather, they will be developed directly on top of the transport layer.

Note 3.  – This field is not exposed at the DS-User's level; it will be set by the DS-Provider.

##### DS Primitive (4 bits / internal / mandatory):

Note. – The DS Primitive field is set by the DS-Provider to indicate the type of DS primitive that the packet meant to carry.

###### The DS Primitive field shall take one of the values specified below and have a format of (4 bits / internal / mandatory):

| Value | Assigned DS Primitive |
| --- | --- |
| 1 | D-START |
| 2 | D-STARTCNF |
| 3 | D-END |
| 4 | D-ENDCNF |
| 5 | D-DATA |
| 6 | D-ABORT |
| 7 | D-UNIT-DATA |
| 8 | D-ACK |
| 9 | D-KEEPALIVE |

Note 1. – Reserving 4 bits will give provision for up to 16 protocol elements, allowing up to 7 additional primitives to be defined.

Note 2. – The D-P-ABORT is not listed, as it is not sent end-to-end.  Upon receipt of an abnormal event or expiration of an inactivity timer, the D-P-ABORT indication will be given to the DS-User.

##### Application Technology Type

Note. – The Application Technology Type identifies the type of application information that is being carried. Other legacy applications besides legacy ATN may also take advantage of the IPS infrastructure, e.g. FANS-1/A, ACARS, etc.

###### The Application Technology Type shall be set to a value of b000 to indicate “ATN IPS DS” and have a format of (3 bits / internal / optional).

Note. – Additional values to be defined are outside the scope of this manual.

##### More

Note. – The More bit will be used as more indicator for segmentation and reassembly of datagrams, and is part of the reliability mechanisms further described in 1.3.

###### The more bit shall take a value of 0 to indicate a single or last segment or a value of 1 to indicate the first or intermediate segment and have a format of (1 bit / internal / optional).

##### Presence Field

Note.  The Presence Field is a series of bits that indicate whether or not particular fields are present the in the ATNPKT format being exchanged.

###### The Presence Field shall use a bit value of 0 to indicate the absence of an optional field or a bit value of 1 to indicate the presence of an optional field, and have a format of (12 bits / internal / mandatory).

###### The optional field details shall comply with Table 1.3-4.

Table 1.2-4.  Presence Field Details

| Bit | Optional field | Size (in bits) | Format | Description |
| --- | --- | --- | --- | --- |
| 0 | Source ID | 16 | V | DS connection identifier of the sender |
| 1 | Destination ID | 16 | V | DS connection identifier of the recipient |
| 2 | Sequence numbers | 8 | V | Sequence numbers (Ns, Nr) |
| 3 | Inactivity time | 8 | V | Inactivity timer value of the sender (in minutes) |
| 4 | Called Peer ID | 24 to 64 (+8) | LV (1) | Called Peer ID (provided by the local DS-User) |
| 5 | Calling Peer ID | 24 to 64 (+8) | LV (1) | Calling Peer ID (provided by the local DS-User) |
| 6 | Content Version | 8 | V | Version of the application data caried |
| 7 | Security Indicator | 8 | V | Security requirements: 0 – No security (default value) 1 – Secured dialogue supporting key management 2 – Secured dialogue 3…255 – Reserved |
| 8 | Quality of Service | 8 | V | ATSC Routing Class: 0 – No traffic type policy preference 1 – "A" 5 – "E" 2 – "B" 6 – "F" 3 – "C" 7 – "G" 4 – "D" 8 – "H" 9…255 – Reserved |
| 9 | Result | 8 | V | Result of a request to initiate or terminate a dialogue: 0 – accepted (default value) 1 – Rejected transient 2 – Rejected permanent 3…255 – Reserved |
| 10 | Originator | 8 | V | Originator of the abort: 0 – user (default value) 1 – provider 2…255 – Reserved |
| 11 | User Data | UDP : 0 to 8192 (+16) TCP: Variable size (+16) | LV (2) | User Data (provided by the local DS User) |

Note 1. – The additional bits required for the length part of LV parameters is

indicated between brackets in the above table.

Note 2. – An optional field is present in the variable part when the corresponding bit is on in the presence field and has one of the following formats:

- V = value

- LV (1) = length (1 byte) + value

- LV (2) = length (2 bytes) + value

#### Variable Parts of ATNPKT

Note. – The variable parts of the ATNPKT will be provided on an as needed basis depending on the DS primitive being exchanged and the current state of the application using the IPS DS.

##### The position of an optional field in the variable part of the ATNPKT shall match the relative position of its corresponding bit in the 'Presence Flag' (i.e. options are in the same order as the presence flag).

##### Source ID

Note. – The Source ID identifies the DS connection at sender side. This field is used as part of the reliability mechanisms described in 1.3.

###### The Source ID shall be present in the D-START and D-STARTCNF primitives, and also when D-ABORT is transmitted after D-START and before D-STARTCNF is received and have a format of (16 bits / internal / optional).

##### Destination ID

Note.  – The Destination ID identifies the connection at recipient side. This field is used as part of the reliability mechanisms described in 1.3.

###### The Destination ID shall be present in the D-STARTCNF, D-DATA, D-END, D-ENDCNF, D-ABORT, D-ACK and D-KEEPALIVE primitives and have a format of (16 bits / internal / optional).

##### Sequence Numbers

Note. – The Sequence Numbers field contains the sequence numbers to be included in the ATNPKT. This mechanism is used to detect the loss and the duplication of UDP datagrams; it allows piggybacked (i.e. D-DATA with additional semantic of D-ACK) or explicit acknowledgement (D-ACK).  This field is part of the reliability mechanisms described in 1.3.

###### The Sequence Numbers field shall be present in all DS primitives over UDP and have the format (8 bits / internal / mandatory) as detailed in Figure 1.3-2 below:

Figure 1.3-2.  Sequence Number Format

N(S) - [0…15] - sequence number of the ATNPKT sent.

N(R) - [0…15] - expected sequence number of the next ATNPKT to be received.

Note – For D-ACK and D-KEEPALIVE, only the N(R) is meaningful on transmission.

###### When using Sequence Numbers with D-ACK and D-KEEPALIVE over UDP, the current value of the send sequence number for N(S) may be used without subsequently incrementing it after transmission.

##### Inactivity Time

Note. – The Inactivity Time indicates the value (in minutes) of the inactivity timer at sender side. This field is used as part of the reliability mechanisms described in 1.3.

###### The Inactivity Time shall be optionally present in the D-START and D-STARTCNF Primitives and have the format (8 bits / internal / optional).

###### When this parameter is not provided by the DS-User, the default value of 4 minutes shall be used as inactivity timer by the source DS-Provider.

##### Called Peer ID

Note. – The Called Peer ID identifies the intended peer DS-User.

###### The Called Peer ID shall be either a 24 bit ICAO Aircraft Identifier or a 3 – 8 character ICAO Facility Designation and have the format (24 to 64 bits / external / optional).

##### Calling Peer ID

Note. – The Calling Peer ID identifies the initiating peer DS-User.

###### The Calling Peer ID shall be either a 24 bit ICAO Aircraft Identifier or a 3 – 8 character ICAO Facility Designation and have the format (24 to 64 bits / external / optional).

##### Content Version

Note. – The Content Version field is used to indicate the application’s version number.

###### The Content Version shall be the version of the ASN.1 syntax used for the User Data field and have the format (8 bits / external / optional).

##### Security Indicator

Note 1. – The Security Indicator parameter is used to convey the level of security to be applied to the dialogue.  In Doc9705/ 9880, this field is referred as 'Security Requirements'; it is renamed here as 'requirement' is not really appropriate in this case.  It is really an indication from the local DS-user on the kind of security procedure to setup.

###### The Security Indicator parameter shall take one of the following values and have a format of (8 bits / external / optional):

| Value | Security Level |
| --- | --- |
| 0 | No security (default value) |
| 1 | Secured dialogue supporting key management |
| 2 | Secured dialogue |
| 3 – 255 | Reserved |

Note. – The omission of this parameter by the DS-User is equivalent to the default value.

##### Quality of Service

Note. – The Quality of Service is used to convey the quality of service (when provided by the DS-User) as a value corresponding to ATSC Routing Class.  The Quality of Service may also be used for other types of QoS the mapping to be applied as specified below.

###### The Quality of Service shall have a format of (8 bits / external / optional) and take a value of either:

- The DS-User-provided ATSC Routing class as below:

| Value | ATSC Routing Class Description |
| --- | --- |
| 0 | No traffic type policy preference |
| 1 | “A” |
| 2 | “B” |
| 3 | “C” |
| 4 | “D” |
| 5 | “E” |
| 6 | “F” |
| 7 | “G” |
| 8 | “H” |
| 9 – 255 | Reserved |

- The Residual Error Rate (RER) as defined below:

| Value | RER Level |
| --- | --- |
| 0 | Low |
| 1 | Medium |
| 2 | High |

- Priority as defined in <<<Ref to Table in CoS section>>> with a mapping to the Differentiated Service field of RFC2474, mapped to the ‘Traffic Class’ for IPv6 with the QoS parameter mapped to the class selector codepoint as below:

| Bits 0 – 2 of the Differentiated Services Codepoint | Corresponding Application |
| --- | --- |
| 111 | Reserved for IP traffic routing (network control) |
| 110 | Reserved for IP traffic routing (internetwork control) |
| 101 | Reserved for higher priority applications |
| 100 | CDPLC, ADS |
| 011 | FIS |
| 010 | CM |
| 001 | Unused |
| 000 | Unused |

###### When using UDP and RER, the UDP checksum may be activated for low or medium RER values and not activate for a high RER value.

##### Result

Note. – The Result is set by the destination DS-User in order to indicate whether or not the requested dialogue initiation or termination completed successfully.

###### The Result shall have the format of (8 bits / external / mandatory) and take one of the values below:

| Value | Definition |
| --- | --- |
| 0 | Accepted |
| 1 | Rejected (transient) |
| 2 | Rejected (permanent) |
| 3 – 255 | Reserved |

##### Originator

Note. – The Originator indicates the source of a D-ABORT.

###### The Originator shall have the format of (8 bit / external / optional) and take of the values below:

| Value | Definition |
| --- | --- |
| 0 | User (default) |
| 1 | Provider |
| 2 – 255 | Reserved |

Note. – When this parameter is not provided by the DS-User the default value shall be assumed.

##### User Data

Note. – The User Data contains the PER encoded application data.

###### The User Data shall have the format of (UDP: 0 to 8192, TCP: variable size / external / optional).

#### IPS DS Parameter Mapping

Note. – The intent of the IPS DS is to present an identical interface to the legacy applications of the ULCS as specified in Doc 9880.  As such, the parameters of the IPS DS are identical to those of the ULCS.  However, there is a different mapping of the contents of those parameters.  These modified mappings are summarized in Table 1.3-5  below and detailed for each primitive in Table 1.3-6.

Table 1.2-5.  IPS DS - ULCS DS Parameter Mapping

| DS Parameter Visible to the DS-User | IP Header | Transport Protocol Header | ATNPKT (See 1.3.5.2) | Comment |
| --- | --- | --- | --- | --- |
| Called Peer ID |  |  | Called Peer ID | This can be an ICAO 24 bit aircraft address or an ICAO Facility Designator (4 to 8 characters) |
| Called Sys-ID |  | Destination Port Number |  | This is a “well-known” port number assigned to each ATN application |
| Called Presentation Address | Destination IP Address |  |  | IP address of the recipient ATN application |
| Calling Peer ID |  |  | Calling Peer ID | This can be an ICAO 24 bit aircraft address or an ICAO Facility Designator (4 to 8 characters) |
| Calling Sys-ID |  | Source Port Number |  | Using TCP, this port number is dynamically assigned by the transport protocol stack on the client side. With UDP, this port number has a static value, which is supposed to the same as the destination port number. |
| Calling Presentation Address | Source IP Address |  |  | IP address of the originator of the ATN application |
| DS-User Version Number |  |  | Content Version | This is the application’s version number |
| Security Requirements |  |  | Security Requirements | 00 – No security 01 – Secured dialogue Supporting Key Management 02 – Secured Dialogue 03 – Reserved |
| Quality of Service |  |  | <<<Quality of Service>>> | This parameter is to be transported only when provided as ‘ATSC Routing Class’; otherwise it will be used by the source DS-Provider |
| Result |  |  | Result | 00 – Accepted 01 – Rejected (permanent) 02 – Rejected (transient) |
| Reject Source |  |  |  | 00 – the remote DS-User 01 – the local DS-Provider Provided locally in the Confirmation primitive only; not transferred end-end |
| Originator |  |  | Originator | 0 – User 1 – Provider (default) 2-255 – Reserved |
| User Data |  |  | User Data | This is the PER encoded data provided by the application |

##### The inclusion of optional ATNPKT parameters for each DS protocol message shall comply with Table 1.3-6:

Table 1.2-6.  ATNPKT Parameters for DS Protocol Messages

| ATNPKT Parameter  | Protocol message  | D-START | D-STARTCNF | D-DATA | D-UNIT-DATA | D-END | D-ENDCNF | D-ABORT | D-ACK | D-KEEPALIVE |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Fixed part |  |  |  |  |  |  |  |  |  |
| ATNPKT Version | M | M | M | M | M | M | M | M | M |
| DS Primitive | M | M | M | M | M | M | M | M | M |
| Application Technology Type | M | M | M | M | M | M | M | M | M |
| More | O | O | O |  | O | O |  |  |  |
| Presence Flag | M | M | M | M | M | M | M | M | M |
| Variable part |  |  |  |  |  |  |  |  |  |
| Source ID | M (4) | M (4) |  |  |  |  | (1) |  |  |
| Destination ID |  | M (4) | M (4) |  | M (4) | M (4) | M (2) | M | M |
| Sequence Numbers | M (4) | M (4) | M (4) | M | M (4) | M (4) | M | M | M |
| Inactivity Time | O (3) | O (3) |  |  |  |  |  |  |  |
| Called Peer ID | O (3) |  |  | O |  |  |  |  |  |
| Calling Peer ID | O (3) |  |  | O |  |  |  |  |  |
| Content Version | O (3) | O (3) |  | O |  |  |  |  |  |
| Security Indicator | O (3) | O (3) |  | O |  |  |  |  |  |
| Quality Of Service | O (3) |  |  |  |  |  |  |  |  |
| Result |  | M (3) |  |  |  | M (3) |  |  |  |
| Originator |  |  |  |  |  |  | O |  |  |
| User Data | O (4) | O (4) | M (4) | M | O (4) | O (4) | O |  |  |

(O = optional, M = mandatory, empty = precluded to use)

(1) Source ID is present if D-ABORT is sent after D-START and before D-STARTCNF is received

(2) Destination ID is absent if D-ABORT is sent after D-START and before D-STARTCNF is received.

(3) For segmented messages this parameter is present only in the first segment.

(4) For segmented messages this parameter is present in all the segments

#### Dialogue Service Primitives

Note. – In order to provide the services identified in 1.3.4, the primitives listed in Table 1.3-7 are used.  Each primitive may be either directly exposed to the DS-User (request/response primitives) or reported to the DS-User by the DS-Provider (indication/confirmation primitives).

Table 1.2-7.  Dialogue Service Primitive Details

| Interface Primitive | Dialogue Service Description | DS-User | DS-Provider |
| --- | --- | --- | --- |
| D-START req | Request to initiate a Dialogue with a peer DS-User | ( |  |
| D-START ind | Inform a local DS-User that a peer DS-User requested for a Dialogue initiation |  | ( |
| D-START rsp | Complete a pending Dialogue initiation with either a positive or a negative response | ( |  |
| D-START cnf | Inform a local DS-User that the peer DS-User completed the pending Dialogue initiation with either a positive or a negative response |  | ( |
| D-UNIT-DATA req | Send a datagram from the local DS-User to a peer DS-User (the end-to-end delivery of the datagram is not guaranteed) | ( |  |
| D-UNIT-DATA ind | Inform a local DS-User that a datagram is received from a peer DS-User |  | ( |
| D-DATA req | Send a datagram from the local DS-User to a peer DS-User over an established Dialogue | ( |  |
| D-DATA ind | Inform a local DS-User that a datagram is received from a peer DS-User over an established Dialogue |  | ( |
| D-END req | Request to terminate a Dialogue with a peer DS-User | ( |  |
| D-END ind | Inform a local DS-User that a peer DS-User requested for a Dialogue termination |  | ( |
| D-END rsp | Complete a pending Dialogue termination with either a positive or a negative response | ( |  |
| D-END cnf | Inform a local DS-User that the peer DS-User completed the pending Dialogue termination with either a positive or a negative response |  | ( |
| D-ABORT req | Request to abort a Dialogue with a peer DS-User | ( |  |
| D-ABORT ind | Inform a local DS-User that the peer DS-User requested to abort the Dialogue |  | ( |
| D-P-ABORT ind | Dialogue aborted by the DS-Provider |  | ( |

#### Dialogue Service Time-Sequence Diagrams

Note. – The sections below illustrate the Dialogue Service protocol exchanges between source and destination DS-Providers, including the ATNPKT user data part.

##### D-START service

Figure 1.3-3.  D-START Service

##### D-DATA service

Note. - Figure 1.3-4 shows the D-DATA service over a TCP connection.  Due to the nature of the connection, an ACK is not required.  Figure 1.3-5 shows the D-DATA service over UDP.  In order to provide explicit acknowledgment of the receipt of the UDP packet, a D-ACK is returned by the receiver of the D-DATA ATNPKT.

Figure 1.3-4.  D-DATA Service (TCP)

Figure 1.3-5.  D-DATA Service (UDP)

##### D-END service

Figure 1.3-6.  D-END Service

##### D-ABORT service

Figure 1.3-7.  D-ABORT Service

##### D-P-ABORT service

Note. – There is no ATNPKT format defined for the D-P-ABORT service, as it is a local indication to the DS-User only.

Figure 1.3-8.  D-P-ABORT Service

##### D-UNIT-DATA service

Note. - Figure 1.3-9 shows the D-DATA service over a TCP connection.  Due to the nature of the connection, an ACK is not required.  Figure 1.3-10 shows the D-DATA service over UDP.  In order to provide explicit acknowledgment of the receipt of the UDP packet, a D-ACK is returned by the receiver of the D-DATA ATNPKT.

Figure 1.3-9.  D-UNIT-DATA Service (TCP)

Figure 1.3-10.  D-UNIT-DATA Service (UDP)

##### D-ACK service

Figure 1.3-11.  D-ACK Service

##### D-KEEPALIVE service

Figure 1.3-12.  D-KEEPALIVE Service

## Transport Layer

### Overview

#### The IPS DS has been designed to allow a user selection of either TCP or UDP for the transport protocol.  For simplicity, port-related operations are not considered as primitives.

#### The transport layer primitives are given in Table 1.4-1.

Table 1.3-1.  Transport Layer Primitives Used in the IPS DS

|  | Transport Layer |  |  |
| --- | --- | --- | --- |
| Interface Primitive | Description | TCP | UDP |
| OPEN | Connection establishment (referred as 'active' on initiator side, 'passive' on the other side) | ( |  |
| CLOSE | Connection termination (referred as 'active' on initiator side, 'passive' on the other side) | ( |  |
| RECEIVE | Receive transport level datagram | ( | ( |
| SEND | Send transport level datagram | ( | ( |

#### Table 1.4-2 gives the mapping to be applied between the Dialogue Service and the Transport Layer primitives.

Table 1.3-2.  Transport Layer - IPS DS Service Mapping

| Dialogue Service | Transport Layer |  |
| --- | --- | --- |
| Service | Interface Primitive | Interface Primitive | User Data | Protocol |
| Initialisation |  |  |
|  |  | OPEN (passive) |  | TCP |
| Dialogue Establishment |  |  |
| D-START | D-START req | OPEN (active) |  | TCP |
|  |  | SEND | D-START | TCP, UDP |
|  | D-START ind | RECEIVE | D-START |  |
|  | D-START rsp | SEND | D-STARTCNF |  |
|  | D-START cnf | RECEIVE | D-STARTCNF |  |
| Connectionless Data Exchange |  |  |
| D-UNIT-DATA | D-UNIT-DATA req | SEND | D-UNITDATA | UDP |
|  | D-UNIT-DATA ind | RECEIVE | D-UNITDATA |  |
| Connected-mode Data Exchange |  |  |
| D-DATA | D-DATA req | SEND | D-DATA | TCP, UDP |
|  | D-DATA ind | RECEIVE | D-DATA |  |
| Orderly Dialogue Termination (user initiated) |  |  |
| D-END | D-END req | SEND | D-END | TCP, UDP |
|  | D-END ind | RECEIVE | D-END |  |
|  | D-END rsp | SEND | D-ENDCNF |  |
|  |  | CLOSE (passive) |  | TCP |
|  | D-END cnf | RECEIVE | D-ENDCNF | TCP, UDP |
|  |  | CLOSE (active) |  | TCP |
| Forced Dialogue Termination (user initiated) |  |  |
| D-ABORT | D-ABORT req | SEND | D-ABORT | TCP, UDP |
|  |  | CLOSE (active) |  | TCP |
|  | D-ABORT ind | RECEIVE | D-ABORT | TCP, UDP |
|  |  | CLOSE (passive) |  | TCP |
| Error-related Dialogue Termination (provider initiated) |  |  |
| D-P-ABORT | D-P-ABORT ind | RECEIVE / SEND (failure) |  | TCP, UDP |
|  |  | Unexpected CLOSE (passive) |  | TCP |

### Providing Dialogue Service over UDP

Note 1. – In general, TCP should be the preferred transport protocol used to convey Dialogue Service primitives, because it provides reliable delivery of data, or notification failure. Additionally, TCP provides a connection- oriented service, making it more suitable for applications where internal states might be mapped to TCP connection.

Note 2. – UDP is mostly employed for applications requiring broadcast or multicast, but it might also be used for simple "request-reply" applications provided that some reliability is added at highest levels. UDP is not reliable enough to guarantee the end-to-end delivery of the datagrams. For this reason, additional mechanisms are implemented to pass over the UDP limitations; basically the truncation, the loss, or the duplication of UDP datagrams.  These mechanisms are specified in the following sections.

#### In order to add some reliability when acting over UDP, the DS-Provider shall implement the mechanisms as described in Table 1.3-3:

Table 1.3-3.  IPS DS UDP Reliability Mechanisms

| Provide ‘dialog connection’ over UDP -identification of connections - connection timeout - termination timeout | M O O |
| --- | --- |
| Detect the loss of UDP datagrams using one-to-one acknowledgments (on a per connection basis) - retransmission timer + max retry count - explicit ack nowledgment -piggy-back ed ack nowledgment (max delay before ack ) | M M O |
| Detect long-lived unpaired connections -inactivity timer + k eep alive | M |
| Handle UDP datagrams truncation - datagram segmentation / reassembly | M |

(O = optional, M = mandatory)

### Connection-ids

#### A pair of connection-ids, the Source ID and Destination ID, shall be assigned during the connection phase (D-START / D-STARTCNF) by every participating DS peer and used over any subsequent exchanges.

Note 1. – DS connection identification above UDP will be handled by the assignment of this pair of connection-ids.

Note 2. – The 2 byte size for these identifiers was chosen because this will allow the DS-Provider to associate a particular semantic to the dialogue-id assigned on its side (without interference with the involved peer DS-User). In such a case, the identifier might be an index in a context table, making it implicitly unique, but also allowing the receiving DS-Provider to find out the context without having to use multiple search criteria and parsing the whole table of contexts.

#### The Source ID and Destination ID shall be conveyed in the variable part of the ATNPKT based on DS primitives as described in Table 1.3-4:

Table 1.3-4.  Source ID and Destination ID Usage

| DS Primitive field | Source ID | Destination ID |
| --- | --- | --- |
| D-START | M | Identifier given by the DS-Provider who initiates the dialogue; it will allow him to find out the dialogue context during the whole dialogue duration. | - | Unassigned at this time |
| D-STARTCNF | M | Identifier given by the DS-Provider who accepts the dialogue; it will allow him to find out the dialogue context during the whole dialogue duration. | M | Identifier of the DS-Provider who initiated the dialogue. |
| D-DATA | - | No need to transport it since it would be meaningless for the destination DS-Provider. | M | Identifier of the peer DS-Provider. |
| D-END | - | No need to transport it since it would be meaningless for the destination DS-Provider. | M | Identifier of the peer DS-Provider. |
| D-ENDCNF | - | No need to transport it since it would be meaningless for the destination DS-Provider. | M | Identifier of the peer DS-Provider. |
| D-ABORT before D-STARTCNF | M | Identifier given by the DS-Provider who initiated the dialogue. | - | Unknown for now. |
| D-ABORT other cases | - | No need to transport it since it would be meaningless for the destination DS-Provider | M | Identifier of the peer DS-Provider. |

(O = optional, M = mandatory)

### Detecting Lost Datagrams

Note 1. – The loss of UDP datagrams is detected through a one-to-one acknowledgment mechanism, on a per DS connection basis: i.e. one data packet sent, one acknowledgement to be received before more data can be sent again.

Note 2. – The acknowledgment may be piggy-backed with a dialogue message in the reverse direction for the same dialogue; this will be possible for instance with confirmed primitives.

#### If the receiver has no message to send for the same dialogue (i.e. the service is unconfirmed), the receiving user shall use an explicit acknowledgment by sending an ATNPKT with no data and with a specific value (D-ACK) as 'DS Primitive'.

Note 1. – For acknowledgment purpose, the 'Sequence Numbers' field of the ATNPKT variable part will be used.

Note 2. – This sequence number is required to avoid delivering duplicated data to the peer DS-user following retransmission (i.e. if a D-ACK has been lost), and in more exceptional circumstances, when UDP datagrams are swapped by the network

#### The DS-Provider shall associate an incremental sequence number to outgoing ATNPKTs, conversely remember the sequence number of the last ATNPKT received from the peer DS-Provider in order to acknowledge it in a subsequent sending.

#### Both outgoing and incoming sequence numbers shall be respectively carried by the N(S) and N(R) subfields of the 'Sequence Numbers'.

Note 1. – N(S) corresponds to the current sequence number of the ATNPKT sent; N(R) is the next sequence number expected as N(S) from the remote DS-Provider (in his next sending).

Note 2. – Using sequence numbers will allow the DS-Provider to detect missing or duplicated ATNPKTs. In our specific case, there is at most one ATNPKT not acknowledged; for this reason there will be no grouped acknowledgments and there is no need to implement a selective reject mechanism.

Note 3. – The lack of reception of an acknowledgment will timely entail a retransmission; an excessive number of retransmission will break the DS connection.  The values of these parameters are detailed in Table 1.3-5.

### Connection Timeout

Note. – In order to avoid long lived unpaired DS connections, a simple mechanism for detecting inactivity is implemented. Both ends of the DS connection will transmit a keepalive packet on 'keepalive timer' expiration during the whole duration of the connection; this timer will then be restarted by the sender each time it sends data on the connection (to avoid unnecessary keepalive transmission).

#### A keepalive (an ATNPKT with no data and with a value of D-KEEPALIVE as 'DS Primitive') shall be sent at each expiry of the local keepalive transmission timer.

#### The keepalive transmission timer may be set to 1/3 of the inactivity timer of the peer DS-Provider, or 1/3 of the default inactivity timer.

Note. – The lack of reception of either data or keepalive for an interval of time corresponding to the inactivity time will break the DS connection.  The parameter value for this time is detailed in Table 1.3-5.

#### The optional ATNPKT field ‘Inactivity Time’ may be used at dialogue initialization time (i.e. in D-START and D-STARTCNF) so that each DS-Provider can adjust its keepalive transmission timer.

Note. – Absence of the parameter indicates uses of the default value.

### “More” Indicator

Note. – Most of the ATN applications messages do not exceeding 1000 bytes. Additionally the suggested value of 1024 bytes does not exceed the IP payload (1500 bytes) in the Ethernet frame (1518 bytes).

#### A D-DATA with a user data part exceeding 1024 bytes shall be segmented using the 'MORE' bit reserved in the ATNPKT fixed part.

Note. – Upon receipt of a D-DATA with the more bit set, the receiving side is responsible for ordering and segmenting the data.

### DS-Provider Parameters

#### The values specified in Table 1.3-5 shall be applied to the identified DS-Provider parameters:

Table 1.3-5.  DS-Provider Parameters

| Parameter | Min | Max | Default |
| --- | --- | --- | --- |
| Delay before retransmission | 1 sec | 60 sec | 15 sec |
| Max number of transmissions | 1 | 10 | 3 |
| Inactivity time | 3 min | 15 min | 4 min |

## IPS Dialogue Service State Tables

### IPS Dialogue Service TCP State Tables

Table 1.4-1.  IPS DS State Table for TCP

| Events State ( ( | D-IDLE | D-CONNECTED | D-START-SENT | D-START-RECEIVED | D-TRANSFER | D-END-SENT | D-END-RECEIVED | D-WAIT-CLOSE |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| During initialisation phase | - OPEN (passive) |  |  |  |  |  |  |  |
| DS-User events | D-START req | - OPEN (active) - Map D-START req to D-START - SEND (D-START) - Enter D-START-SENT state |  |  |  |  |  |  |  |
|  | D-START rsp |  |  |  | - Map D-START cnf to D-STARTCNF - SEND (D-STARTCNF) - In case of positive response : - Start tinact - Enter D-TRANSFER state - Otherw ise : -Enter D-WAIT-CLOSE state |  |  |  |  |
|  | D-DATA req |  |  |  |  | - Map D-DATA req to D-DATA - SEND (D-DATA) |  |  |  |
|  | D-END req |  |  |  |  | - Cancel tinact - Map D-END req to D-END - SEND (D-END) - Enter D-END-SENT state |  |  |  |
|  | D-END rsp |  |  |  |  |  |  | - Map D-END rsp to D-ENDCNF - SEND (D-ENDCNF) -In case of positive response : -Enter D-WAIT-CLOSE state - Otherw ise : - Start tinact - Enter D-TRANSFER state |  |
|  | D-ABORT req |  |  | - Map D-ABORT req to D-ABORT - SEND (D-ABORT) - Enter D-WAIT-CLOSE state | - Map D-ABORT req to D-ABORT - SEND (D-ABORT) - Enter D-WAIT-CLOSE state | - Cancel tinact - Map D-ABORT req to D-ABORT - SEND (D-ABORT) - Enter D-WAIT-CLOSE state | - Map D-ABORT req to D-ABORT - SEND (D-ABORT) - Enter D-WAIT-CLOSE state | - Map D-ABORT req to D-ABORT - SEND (D-ABORT) - Enter D-WAIT-CLOSE state |  |
| TCP events | OPEN (passive) completed | - Enter D-CONNECTED state |  |  |  |  |  |  |  |
|  | RECEIVE (D-START) |  | - Map D-START to D-START ind - Report D-START ind to DS-User - Enter D-START-RECEIVED state |  |  |  |  |  |  |
|  | RECEIVE (D-STARTCNF) |  |  | - Map D-STARTCNF to D-START cnf - Report D-START cnf to DS-User - In case of positive response : - Start tinact - Enter D-TRANSFER state - Otherw ise : - CLOSE (active) -Enter D-IDLE state |  |  |  |  |  |
|  | RECEIVE (D-DATA) |  |  |  |  | - Reset tinact - Map D-DATA to D-DATA ind - Report D-DATA ind to DS-User |  |  |  |
|  | RECEIVE (D-END) |  |  |  |  | - Cancel tinact - Map D-END to D-END ind - Report D-END ind to DS-User - Enter D-END-RECEIVED state |  |  |  |
|  | RECEIVE (D-ENDCNF) |  |  |  |  |  | - Map D-ENDCNF to D-END cnf - Report D-END cnf to DS-User - In case of positive response : - CLOSE (active) - Enter D-IDLE state - Otherw ise : - Start tinact - Enter D-TRANSFER state |  |  |
| TCP events | RECEIVE (D-ABORT) |  |  |  | - Map D-ABORT to D-ABORT ind -Report D-ABORT ind to DS-User - CLOSE (active) -Enter D-IDLE state | - Cancel tinact - Map D-ABORT to D-ABORT ind - Report D-ABORT ind to DS-User - CLOSE (active) - Enter D-IDLE state | - Map D-ABORT to D-ABORT ind - Report D-ABORT ind to DS-User - CLOSE (active) - Enter D-IDLE state | - Map D-ABORT to D-ABORT ind - Report D-ABORT ind to DS-User - CLOSE (active) - Enter D-IDLE state |  |
|  | CLOSE (passive) |  | - CLOSE (active) - Enter D-IDLE state | - Report D-P-ABORT ind to DS-User - CLOSE (active) -Enter D-IDLE state | - Report D-P-ABORT ind to DS-User - CLOSE (active) -Enter D-IDLE state | - Cancel tinact - Report D-P-ABORT ind to DS-User - CLOSE (active) - Enter D-IDLE state | - Report D-P-ABORT ind to DS-User - CLOSE (active) - Enter D-IDLE state | - Report D-P-ABORT ind to DS-User - CLOSE (active) - Enter D-IDLE state | - CLOSE (active) - Enter D-IDLE state |
| DS-Provider events | tinact expires |  |  |  |  | - Report D-P-ABORT ind to DS-User - Enter D-IDLE state |  |  |  |

### IPS Dialogue Service UDP State Tables

Table 1.4-2.  IPS DS State Table for UDP

| Events State ( ( | D-IDLE | D-START-SENT | D-START-RECEIVED | D-TRANSFER | D-END-SENT | D-END-RECEIVED |
| --- | --- | --- | --- | --- | --- | --- |
| DS-User events | D-START req | -Map D-START req to D-START - SEND (D-START) - Start tconnect - Enter D-START-SENT state |  |  |  |  |  |
|  | D-START rsp |  |  | - Map D-START cnf to D-STARTCNF - SEND (D-STARTCNF) -In case of positive response : - Start tinact -Enter D-TRANSFER state - Otherw ise : -Enter D-IDLE state |  |  |  |
|  | D-DATA req |  |  |  | - Map D-DATA req to D-DATA - SEND (D-DATA) |  |  |
|  | D-END req |  |  |  | - Cancel tinact -Map D-END req to D-END - SEND (D-END) - start tterm - Enter D-END-SENT state |  |  |
|  | D-END rsp |  |  |  |  |  | -Map D-END rsp to D-ENDCNF - SEND (D-ENDCNF) - In case of positive response : - Enter D-IDLE state - Otherw ise : - Start tinact - Enter D-TRANSFER state |
|  | D-ABORT req |  | - Cancel tconnect -Map D-ABORT req to D-ABORT - SEND (D-ABORT) - Enter D-IDLE state | - Map D-ABORT req to D-ABORT - SEND (D-ABORT) - Enter D-IDLE state | - Cancel tinact - Map D-ABORT req to D-ABORT - SEND (D-ABORT) - Enter D-IDLE state | - Cancel tterm - Map D-ABORT req to D-ABORT - SEND (D-ABORT) - Enter D-IDLE state | - Map D-ABORT req to D-ABORT - SEND (D-ABORT) - Enter D-IDLE state |
| UDP events | RECEIVE (D-START) | -Map D-START to D-START ind - Report D-START ind to DS-User - Enter D-START-RECEIVED state |  |  |  |  |  |
|  | RECEIVE (D-STARTCNF) |  | - Cancel tconnect -Map D-STARTCNF to D-START cnf - Report D-START cnf to DS-User -In case of positive response : -Start tinact - Enter D-TRANSFER state - Otherw ise : - Enter D-IDLE state |  |  |  |  |
|  | RECEIVE (D-DATA) |  |  |  | - Reset tinact - Map D-DATA to D-DATA ind - Report D-DATA ind to DS-User |  |  |
|  | RECEIVE (D-END) |  |  |  | - Cancel tinact -Map D-END to D-END ind - Report D-END ind to DS-User - Enter D-END-RECEIVED state |  |  |
|  | RECEIVE (D-ENDCNF) |  |  |  |  | - Cancel tterm -Map D-ENDCNF to D-END cnf - Report D-END cnf to DS-User - In case of positive response : - Enter D-IDLE state - Otherw ise : - Start tinact - Enter D-TRANSFER state |  |
|  | RECEIVE (D-ABORT) |  |  | - Map D-ABORT to D-ABORT ind - Report D-ABORT ind to DS-User - Enter D-IDLE state | - Cancel tinact - Map D-ABORT to D-ABORT ind - Report D-ABORT ind to DS-User - Enter D-IDLE state | - Cancel tterm - Map D-ABORT to D-ABORT ind - Report D-ABORT ind to DS-User - Enter D-IDLE state | - Map D-ABORT to D-ABORT ind - Report D-ABORT ind to DS-User - Enter D-IDLE state |
| D S events | tconnect expires |  | - Report D-P-ABORT ind to DS-User - Enter D-IDLE state |  |  |  |  |
|  | tinact expires |  |  |  | - Report D-P-ABORT ind to DS-User - Enter D-IDLE state |  |  |
|  | tterm expires |  |  |  |  | -Report D-P-ABORT ind to DS-User - Enter D-IDLE state |  |

# Comments

If this is to be broken out in section 3 of Part II, the entire section can be moved

Not sure how this is done; is this leftover from before when the format changed?  Suggest removing…

Left out IPv4 since the tech manual doesn’t reference it

# Text boxes

Summary

This paper presents initial sections to be inserted into the draft ICAO Doc 9896.

IPS

IPS DS

ATN-App ASE

Application User