ICAO

Aeronautical Telecommunication Network (ATN)

Manual for the ATN using IPS Standards and Protocols (Doc 9896)

September 17, 2008

Version 15

FOREWORD

This document defines the data communications protocols and services to be used for implementing the International Civil Aviation Organization (ICAO) Aeronautical Telecommunications Network (ATN) using the Internet Protocol Suite (IPS). The material in this document is to be considered in conjunction with the relevant Standards and Recommended Practices (SARPs) as contained in Annex 10, Volume III, and Part I Chapter 3.

Editorial practices in this document.

The detailed technical specifications in this document that include the operative verb “shall” are essential to be implemented to secure proper operation of the ATN.

The detailed technical specifications in this document that include the operative verb “should” are recommended for implementation in the ATN.  However, particular implementations may not require this specification to be implemented.

The detailed technical specifications in this document that include the operative verb “may” are optional. The use or non use of optional items shall not prevent interoperability between ATN/IPS nodes.

The Manual for the ATN using IPS Standards and Protocols is divided into the following parts:

Part I – Detailed Technical Specifications

This section contains a general description of Internet Protocol Suite (IPS).  It covers the network, transport and security requirements for the ATN/IPS.

Part II – Application Support

This section contains a description of applications supported by the ATN/IPS.  It includes convergence mechanisms and application services that allow the operation of legacy ATN/OSI applications over the ATN/IPS transport layer.

Part III – Guidance

This section contains guidance material on IPS communications including information on architectures, and general information to support IPS implementation.

ICAO

Aeronautical Telecommunication Network (ATN)

Manual for the ATN using IPS Standards and Protocols (Doc 9896)

Part I

Detailed Technical Specifications

PART 1 TABLE of contents

1.0 INTRODUCTION	2

1.1 General Overview	2

2.0 REQUIREMENTS	4

2.1 ATN/IPS ADMINISTRATION	4

2.1.1 The ATN/IPS	4

2.1.2 ATN/IPS Mobility	4

2.2 LINK LAYER REQUIREMENTS	5

2.3 internet LAYER REQUIREMENTS	5

2.3.1 General IPv6 Internetworking	5

2.3.2 Mobile IPv6	5

2.3.3 Network Addressing	5

2.3.4 Inter-Domain Routing	6

2.3.5 Error Detection and Reporting	7

2.3.6 Quality of Service (QoS)	7

2.3.7 IP Version Transition	7

2.4 TRANSPORT LAYER REQUIREMENTS	8

2.4.1 Transmission Control Protocol (TCP)	8

2.4.2 User Datagram Protocol (UDP)	8

2.5 SECURITY REQUIREMENTS	8

2.5.1 Ground-Ground Security	8

2.5.1.1 Ground-Ground IPsec/IKEv2	8

2.5.2 Air-Ground Security	9

2.5.2.1 Air-Ground Access Network Security	9

2.5.2.2 Air-Ground IPsec/IKEv2	9

2.5.2.3 Air-Ground Transport Layer Security	10

2.5.2.4 Air-Ground Application Layer Security	11

2.6 Performance	11

# 1.0 INTRODUCTION

## 1.1 General Overview

This manual contains the minimum communication protocols and services that will enable implementation of an ICAO Aeronautical Telecommunication Network (ATN) based on the Internet Protocol Suite (IPS), referred to as the ATN/IPS. The scope of this manual is on interoperability across Administrative Domains in the ATN/IPS internetwork, although the material in this manual may also be used within an Administrative Domain.  In accordance with Annex 10, Volume III, Part I, paragraph [3.3.3] implementation of the ATN/IPS, including the protocols and services included in this manual, will take place on the basis of regional air navigation agreements between ICAO contracting States.  Regional planning and implementation groups (PIRG’s) coordinate such agreements.

The ATN/IPS protocol architecture is illustrated in Figure 1.  The ATN/IPS has adopted the same four layer model as defined in Internet Society (ISOC) internet standard STD003.

Note.- STD003 is a combination of  Internet Engineering Task Force (IETF) RFC1122 and RFC1123.

Figure 1 – ATN/IPS Protocol Architecture

This model has four abstraction layers called the Link Layer, the Internet or IP Layer, the Transport Layer and the Application Layer.

As depicted in Figure 1, this manual does not adopt any specific link layer protocol as this is a local or bi-lateral issue which does not affect overall interoperability.

This manual adopts the Internet Protocol version 6 (IPv6) for fundamental internet layer interoperability. Implementation of IPv4 in ground networks, for transition to IPv6 (or as a permanent network) is not addressed in this manual.  IPv6 is to be implemented in air-ground networks. The Border Gateway Protocol 4 with extensions (BGP4+) is adopted for inter-domain routing.

The Transmission Control Protocol (TCP) and User Datagram Protocol (UDP) are adopted for connection-oriented and connectionless service at the transport layer.

Part II of this manual includes convergence mechanisms and application services that allow the operation of legacy ATN/OSI applications over the ATN/IPS transport layer.

# 2.0 REQUIREMENTS

## 2.1 ATN/IPS ADMINISTRATION

### 2.1.1 The ATN/IPS

2.1.1.1	The ATN/IPS internetwork consists of IPS nodes and networks operating in a multinational environment in support of Air Traffic Service Communication (ATSC) as well as Aeronautical Industry Service Communication (AINSC), such as Aeronautical Administrative Communications (AAC) and Aeronautical Operational Communications (AOC).

2.1.1.2 In this manual an IPS node is a device that implements IPv6. There are two types of IPS nodes.

- An IPS router is an IPS node that forwards Internet Protocol (IP) packets not explicitly addressed to itself.

- An IPS host is an IPS node that is not a router.

2.1.1.3	From an administrative perspective, the ATN/IPS internetwork consists of a number of interconnected Administrative Domains.  An Administrative Domain can be an individual State, a group of States (e.g., an ICAO Region), an Air Communications Service Provider (ACSP), an Air Navigation Service Provider (ANSP), or any other organizational entity that manages ATN/IPS network resources and services.

2.1.1.4	Each Administrative Domain participating in the ATN/IPS internetwork shall operate one or more IPS routers which execute the inter-domain routing protocol specified in this manual.

2.1.1.5 From a routing perspective, inter-domain routing protocols are used to exchange routing information between Autonomous Systems (AS), where an AS is a connected group of one or more IP prefixes.  The routing information exchanged includes IP address prefixes of differing lengths. For example, an IP address prefix exchanged between ICAO regions may have a shorter length than an IP address prefix exchanged between individual States within a particular region.

2.1.1.6 Administrative Domains should coordinate their policy for carrying transit traffic with their counter parts.

### 2.1.2 ATN/IPS Mobility

2.1.2.1 ATN/IPS mobility is based on IPv6 mobility standards, operated by Mobility Service Providers (MSP).

Note - A MSP in the ATN/IPS is an instance of an AD which may be an Air Communications Service Provider (ACSP), Air Navigation Service Provider (ANSP), Airline, Airport Authority, government or other aviation organization.

2.1.2.2 ATN/IPS Mobility Service Providers (MSP) shall operate one or more home agents (HA).

## 2.2 LINK LAYER REQUIREMENTS

2.2.1	The specification of the link layer characteristics for a node is a local issue.

## 2.3 internet LAYER REQUIREMENTS

### 2.3.1 General IPv6 Internetworking

2.3.1.1 IPS nodes shall implement IPv6 as specified in RFC 2460.

2.3.1.2 IPS nodes shall implement IPv6 Maximum Transmission Unit (MTU) path discovery as specified in RFC 1981.

2.3.1.3 IPS nodes shall set the flow label field of the IPv6 header to zero, as it is not used in the ATN.

### 2.3.2 Mobile IPv6

2.3.2.1 IPS mobile nodes shall implement Mobile IPv6 as specified in RFC 3775.

Note- RFC 3775 is expected to be updated by the IETF, which is preparing RFC 3775bis.

2.3.2.2 IPS home agents shall implement Mobile IPv6 as specified in RFC 3775.

2.3.2.3 IPS mobile nodes and home agents may implement extensions to Mobile IPv6 to enable support for network mobility as specified in RFC 3963.

2.3.2.4 IPS correspondent nodes that implement Mobile IPv6 route optimization shall allow route optimization to be administratively enabled or disabled with the default being disabled.

Note.- Mobile IPv6 route optimization is not mandated by this specification as new solutions are expected as a result of IETF chartered work which includes aviation requirements.

### 2.3.3 Network Addressing

2.3.3.1 IPS nodes shall implement IP Version 6 Addressing Architecture as specified in RFC 4291.

2.3.3.2 IPS nodes shall use globally scoped IPv6 addresses when communicating over the ATN/IPS.

2.3.3.3 Administrative Domains shall obtain IPv6 address prefix assignments from their Local Internet Registry (LIR) or Regional Internet Registry (RIR).

2.3.3.4 MSPs shall obtain a /32 IPv6 address prefix assignment for the exclusive use of IPS Mobile Nodes or mobile networks,

2.3.3.5 MSPs should use the following IPv6 address structure, for aircraft assignments.

Note-1 .— Under this structure each aircraft constitutes a /56 IPv6 end site, which is based on the ICAO 24 bit aircraft address, as defined in Annex 10 vol 3, appendix to chapter 9.

Note-2. —   An aircraft may have different subnets for different services (ATS, AOC, AAC,  etc.) as a means to enable mobile networks supported by a mobile router or may have different MSPs for different services.

2.3.3.6 Mobility Service Providers (MSPs), shall advertise their /32 aggregate prefix to the ATN/IPS.

### 2.3.4 Inter-Domain Routing

Note 1.— Inter-domain routing protocols are used to exchange routing information among ASs.

Note 2.— For routing purposes, an AS has a unique identifier called an AS number (ASN).

Note 3. — A single Administrative Domain may be responsible for the management of several ASs.

Note 4.— The routing protocol within an AS is a local matter determined by the managing organization.

2.3.4.1 IPS routers which support inter-domain dynamic routing shall implement the Border Gateway Protocol (BGP-4) as specified in RFC 4271.

2.3.4.2 IPS routers which support inter-domain dynamic routing shall implement the BGP-4 Multiprotocol Extensions as specified in RFC 2858.

2.3.4.3 Administrative Domains shall use AS numbers for ATN/IPS routers that implement BGP-4.

2.3.4.4 Administrative Domains that use private AS numbers shall follow the AS numbering plan described in Part I of this document.

Note. — Administrative Domains that require additional private AS numbers should coordinate through ICAO.

2.3.4.5 IPS routers which support inter-domain dynamic routing should authenticate routing information exchanges as specified in RFC 2385.

### 2.3.5 Error Detection and Reporting

2.3.5.1 IPS nodes shall implement Internet Control Message Protocol (ICMPv6) as specified in RFC 4443.

### 2.3.6 Quality of Service (QoS)

2.3.6.1 Administrative Domains shall enable the required ATN/IPS class of service to meet the operational and application requirements.

2.3.6.2 Administrative Domains shall make use of Differentiated Services as specified in RFC 2475 as a means to provide Quality of Service (QoS) to ATN/IPS applications and services.

2.3.6.3 Administrative Domains supporting Voice over IP services shall assign those services to the Expedited Forwarding (EF) Per-Hop Behavior (PHB) as specified by RFC 3246.

2.3.6.4 Administrative Domains shall assign ATN application traffic to the Assured Forwarding (AF) PHB as specified by RFC 2597.

Note 1. - This provision is applicable to applications as defined in Annex 10.

Note 2. - Assured forwarding allows the ATN/IPS operator to provide assurance of delivery as long as the traffic does not exceed the subscribed rate. Excess traffic has a higher probability of being dropped if congestion occurs.

2.3.6.5  Administrative Domains applying  measures of priority  to the AF classes shall assign relative measures based on the ATN mapping of priorities defined in Annex 10, Volume III, Part I, Table 1.

### 2.3.7 IP Version Transition

2.3.7.1 Administrative Domains should use the dual IP layer mechanism for IPv6 to IPv4 compatibility as described in RFC 4213.

Note - This provision ensures that ATN/IPS hosts also support IPv4 for backwards compatibility with local IPv4 applications.

## 2.4 TRANSPORT LAYER REQUIREMENTS

### 2.4.1 Transmission Control Protocol (TCP)

2.4.1.1 IPS nodes shall implement the Transmission Control Protocol (TCP) as specified in RFC 793.

2.4.1.2 IPS nodes may implement TCP Extensions for High Performance as specified in RFC 1323.

### 2.4.2 User Datagram Protocol (UDP)

2.4.2.1 IPS hosts shall implement User Datagram Protocol as specified in RFC 768.

## 2.5 SECURITY REQUIREMENTS

Note: This section contains provisions for ground-ground and air-ground security in the ATN/IPS.  Certain provisions in this section are mandatory to implement but optional to use. Their actual use is to be based on a system threat and vulnerability analysis.

### 2.5.1 Ground-Ground Security

Note: IP layer security in the ground-ground ATN/IPS internetwork is implemented using Internet Protocol security (IPsec) and the Internet Key Exchange (IKEv2) protocol.

### 2.5.1.1 Ground-Ground IPsec/IKEv2

2.5.1.1.1 IPS nodes in the ground-ground environment shall implement the Security Architecture for the Internet Protocol as specified in RFC 4301.

2.5.1.1.2. IPS nodes in the ground-ground environment shall implement the IP Encapsulating Security Payload (ESP) protocol as specified in RFC 4303.

2.5.1.1.3 IPS nodes in the ground-ground environment may implement the IP Authentication Header (AH) protocol as specified in RFC 4302.

2.5.1.1.4 IPS nodes in the ground-ground environment shall implement the Internet Key Exchange (IKEv2) Protocol as specified in RFC 4306.

2.5.1.1.5 IPS nodes in the ground-ground environment shall implement the Cryptographic Algorithm Implementation Requirements for the Encapsulating Security Payload (ESP) and Authentication Header (AH) if AH is implemented as specified in RFC 4305.

2.5.1.1.6 IPS nodes in the ground-ground environment shall implement the Null Encryption Algorithm as specified in RFC4305, but not the Null Authentication Algorithm, when establishing IPsec security associations.

2.5.1.1.7 IPS nodes in the ground-ground environment shall implement the Cryptographic Algorithms for Use in the Internet Key Exchange Version 2 (IKEv2) required algorithms for key exchange as specified in RFC4307.

2.5.1.1.8 IPS nodes in the ground-ground environment should use the Internet X.509 Public Key Infrastructure Certificate and Certificate Revocation List (CRL) Profile as specified in RFC 5280, when digital signatures are used as the IKEv2 authentication method.

2.5.1.1.9 IPS nodes in the ground-ground environment should use the Internet X.509 Public Key Infrastructure Certificate Policy and Certificate Practices Framework as specified in RFC 3647, when digital signatures are used as the IKEv2 authentication method.

### 2.5.2 Air-Ground Security

### 2.5.2.1 Air-Ground Access Network Security

2.5.2.1.1 IPS mobile nodes shall implement the security provisions of the access network, to enable access network security.

Note. – For example, the WiMAX, 3GPP, and 3GPP2 access networks have authentication and authorization provisions.

### 2.5.2.2 Air-Ground IPsec/IKEv2

2.5.2.2.1 IPS nodes in the air-ground environment shall implement the Security Architecture for the Internet Protocol as specified in RFC4301.

2.5.2.2.2 IPS nodes in the air-ground environment shall implement the IP Encapsulating Security Payload (ESP) protocol as specified in RFC 4303.

2.5.2.2.3 IPS nodes in the air-ground environment shall implement AUTH_HMAC_SHA2_256-128 as the integrity algorithm for ESP authentication as specified in RFC 4868, when establishing IPsec security associations.

2.5.2.2.4 IPS nodes in the air-ground environment which implement encryption shall implement AES-GCM with an 8 octet ICV and with a key length attribute of 128 bits for ESP encryption and authentication as specified in RFC 4106.

2.5.2.2.5    IPS nodes in the air-ground environment shall implement the Internet Key Exchange (IKEv2) Protocol as specified in RFC 4306.

2.5.2.2.6   IPS nodes in the air-ground environment shall implement IKEv2 with the following transforms:

- PRF_HMAC_SHA_256 as the pseudo-random function as specified in RFC 4868.

- 256-bit random ECP group for Diffie-Hellman Key Exchange values as specified in RFC 4753.

- ECDSA with SHA-256 on the P-256 curve as the authentication method as specified in RFC 4754.

- AES CBC with 128-bit keys as the IKEv2 encryption transform as specified in RFC 3602.

- HMAC_SHA_256-128 as the IKEv2 integrity transform as specified in RFC 4868.

2.5.2.2.7 IPS nodes in the air-ground environment should use the Internet X.509 Public Key Infrastructure Certificate and Certificate Revocation List (CRL) Profile as specified in RFC 5280, when digital signatures are used as the IKEv2 authentication method.

2.5.2.2.8 IPS nodes in the air-ground environment should use the Internet X.509 Public Key Infrastructure Certificate Policy and Certificate Practices Framework as specified in RFC 3647, when digital signatures are used as the IKEv2 authentication method.

Note. – The Air Transport Association (ATA) Digital Security Working Group (DSWG) has developed a Certificate Policy (ATA Specification 42) for use in the aviation community. ATA Specification 42 includes certificate and CRL profiles that are suitable for aeronautical applications and interoperability with an aerospace industry PKI bridge.  These profiles provide greater specificity than, but do not conflict with, RFC 5280.

2.5.2.2.9 IPS nodes in the air-ground environment, shall implement Mobile IPv6 Operation with IKEv2 and the Revised IPsec Architecture as specified in RFC 4877.

### 2.5.2.3 Air-Ground Transport Layer Security

2.5.2.3.1 IPS mobile nodes and correspondent nodes may implement the Transport Layer Security (TLS) protocol as specified in RFC 4346.

2.5.2.3.2 IPS mobile nodes and correspondent nodes shall implement the Cipher Suite TLS_ECDH_ECDSA_WITH_AES_128_CBC_SHA as specified in RFC 4492 when making use of TLS.

### 2.5.2.4 Air-Ground Application Layer Security

2.5.2.4.1 IPS mobile nodes and correspondent nodes may implement application layer security at the IPS Dialogue Service Boundary, as described in Part II.

2.5.2.4.2 IPS mobile nodes and correspondent nodes shall append an HMAC keyed message authentication code as specified in RFC 2104 using SHA-256 as the cryptographic hash function when application layer security is used.

2.5.2.4.3 A HMAC tag truncated to 32 bits shall be computed over the User Data concatenated with a 32-bit send sequence number for replay protection when application layer security is used.

2.5.2.4.4 IKEv2 shall be used for key establishment as specified in section 2.5.2.2 when application layer security is used.

## 2.6 Performance

2.6.1 IPS nodes may implement RFC 2488 in order to improve performance over satellite links.

2.6.2 IPS nodes may implement the RObust Header Compression Framework (ROHC) as specified in RFC 4995 in order to optimize bandwidth utilization.

2.6.3 If ROHC is supported, then the following ROHC profiles shall be supported as applicable:

a. the ROHC profile for TCP/IP specified in RFC 4996

b. the ROHC profile for RTP/UDP/ESP specified in RFC 3095

c. the IP-Only ROHC profile specified in RFC 4843

d. the ROHC over PPP profile specified in RFC 3241

# APPENDIX A – AS Numbering Plan

Note: This numbering plan covers ICAO Contracting and Non-Contracting States, and Territories.

| ICAO Region | Country/Organisation/Location | ASN |  | ICAO Region | Country/Org./Loc. | ASN |
| --- | --- | --- | --- | --- | --- | --- |
| MID | Afghanistan | 64512 |  | EUR/NAT | Ireland | 64688 |
| APAC | American Samoa | 64513 |  | EUR/NAT | Italy | 64692 |
| ESAF | Angola | 64514 |  | EUR/NAT | Kazakhstan | 64696 |
| NACC | Anguilla I. (U.K.) | 64515 |  | EUR/NAT | Kyrgyzstan | 64700 |
| NACC | Antigua and Barbuda | 64516 |  | EUR/NAT | Latvia | 64704 |
| SAM | Argentina | 64517 |  | EUR/NAT | Liechtenstein | 64706 |
| NACC | Aruba (Netherlands) | 64518 |  | EUR/NAT | Lithuania | 64708 |
| WACAF | Ascension and St Helena Is. (U.K.) | 64519 |  | EUR/NAT | Luxembourg | 64712 |
| APAC | Australia | 64520 |  | EUR/NAT | The former Yugoslav Republic of Macedonia | 64716 |
| NACC | Bahamas | 64521 |  | EUR/NAT | Malta | 64720 |
| APAC | Bangladesh | 64522 |  | EUR/NAT | Monaco | 64728 |
| NACC | Barbados | 64523 |  | EUR/NAT | Montenegro | 64820 |
| NACC | Belize | 64524 |  | EUR/NAT | Morocco | 64824 |
| WACAF | Benin | 64525 |  | EUR/NAT | Netherlands | 64732 |
| NACC | Bermuda (U.K.) | 64526 |  | EUR/NAT | Norway | 64736 |
| APAC | Bhutan | 64527 |  | EUR/NAT | Poland | 64740 |
| SAM | Bolivarian Republic of Venezuela | 64528 |  | EUR/NAT | Portugal | 64744 |
| SAM | Bolivia | 64529 |  | EUR/NAT | Republic of Moldova | 64724 |
| ESAF | Botswana | 64530 |  | EUR/NAT | Romania | 64748 |
| SAM | Brazil | 64531 |  | EUR/NAT | Serbia | 64756 |
| ESAF | British Indian Ocean Territory | 64532 |  | EUR/NAT | Russian Federation | 64752 |
| APAC | Brunei Darussalam | 64533 |  | EUR/NAT | San Marino | 64828 |
| WACAF | Burkina Faso | 64534 |  | EUR/NAT | Slovak Republic | 64760 |
| ESAF | Burundi | 64535 |  | EUR/NAT | Slovenia | 64764 |
| APAC | Cambodia | 64536 |  | EUR/NAT | Spain | 64768 |
| WACAF | Cameroon | 64537 |  | EUR/NAT | Sweden | 64772 |
| NACC | Canada | 64538 |  | EUR/NAT | Tajikistan | 64776 |
| WACAF | Cape Verde | 64539 |  | EUR/NAT | Switzerland | 64780 |
| NACC | Cayman Is. (U.K.) | 64540 |  | EUR/NAT | The Holy See | 64782 |
| WACAF | Central African Republic | 64541 |  | EUR/NAT | Tunisia | 64832 |
| WACAF | Chad | 64542 |  | EUR/NAT | Turkey | 64784 |
| SAM | Chile | 64543 |  | EUR/NAT | Turkmenistan | 64788 |
| APAC | China | 64544 |  | EUR/NAT | Ukraine | 64792 |
| SAM | Colombia | 64545 |  | EUR/NAT | United Kingdom | 64796 |
| WACAF | Congo | 64546 |  | EUR/NAT | Uzbekistan | 64800 |
| APAC | Cook Islands | 64547 |  | EUR/NAT | Regional - Germany | 65108 |
| NACC | Costa Rica | 64548 |  | EUR/NAT | Regional - Europe | 65112 |
| WACAF | Côte d'Ivoire | 64549 |  | EUR/NAT | EUROCONTROL | 65208 |
| NACC | Cuba | 64550 |  | EUR/NAT | EUROCONTROL | 65212 |
| APAC | Democratic People's Republic of Korea | 64551 |  | EUR/NAT | EUROCONTROL | 65216 |
| WACAF | Democratic Republic of the Congo | 64552 |  | EUR/NAT | EUROCONTROL | 65220 |
| APAC | Democratic Republic of Timor-Leste | 64553 |  | EUR/NAT | EUROCONTROL | 65224 |
| ESAF | Djibouti | 64554 |  | EUR/NAT | EUROCONTROL | 65228 |
| NACC | Dominica | 64555 |  | EUR/NAT | EUROCONTROL | 65232 |
| NACC | Dominican Republic | 64556 |  | EUR/NAT | EUROCONTROL | 65236 |
| APAC | Easter Island (Chile) | 64557 |  | WACAF | Mauritania | 65237 |
| SAM | Ecuador | 64558 |  | ESAF | Mauritius | 65238 |
| MID | Egypt | 64559 |  | NACC | Mexico | 65239 |
| NACC | El Salvador | 64560 |  | APAC | Micronesia, Federated States of | 65240 |
| WACAF | Equatorial Guinea | 64561 |  | APAC | Midway Is. (U.S.) | 65241 |
| ESAF | Eritrea | 64562 |  | APAC | Mongolia | 65242 |
| ESAF | Ethiopia | 64563 |  | NACC | Montserrat I. (U.K.) | 65243 |
| SAM | Falklands Is. (U.K.) | 64564 |  | ESAF | Mozambique | 65244 |
| NACC | French Antilles (?) | 64565 |  | APAC | Myanmar | 65245 |
| WACAF | Gabon | 64566 |  | ESAF | Namibia | 65246 |
| WACAF | Gambia | 64567 |  | APAC | Nauru | 65247 |
| WACAF | Ghana | 64568 |  | APAC | Nepal | 65248 |
| NACC | Grenada | 64569 |  | NACC | Netherlands Antilles | 65249 |
| APAC | Guam (U.S.) ? | 64570 |  | APAC | New Caledonia | 65250 |
| NACC | Guatemala | 64571 |  | APAC | New Zealand | 65251 |
| WACAF | Guinea | 64572 |  | NACC | Nicaragua | 65252 |
| WACAF | Guinea-Bissau | 64573 |  | WACAF | Niger | 65253 |
| SAM | Guyana | 64574 |  | WACAF | Nigeria | 65254 |
| SAM | Guyane Francaise | 64575 |  | APAC | Niue Island (New Zealand) | 65255 |
| NACC | Haiti | 64576 |  | MID | Oman | 65256 |
| SAM | Honduras | 64577 |  | MID | Pakistan | 65257 |
| APAC | Hong Kong Special Administrative Region of China | 64578 |  | APAC | Palau | 65258 |
| APAC | Iles Wallis Et Futuna (France) | 64579 |  |  | Palestinian Territory, occupied | 65259 |
| APAC | India | 64580 |  | APAC | Palmyra Is. (U.S.) | 65260 |
| APAC | Indonesia | 64581 |  | SAM | Panama | 65261 |
| MID | Iran, Islamic Republic of | 64582 |  | APAC | Papua New Guinea | 65262 |
| MID | Iraq | 64583 |  | SAM | Paraguay | 65263 |
| MID | Israel | 64584 |  | SAM | Peru | 65264 |
| NACC | Jamaica | 64585 |  | APAC | Philippines | 65265 |
| APAC | Japan | 64586 |  | APAC | Pitcairn Island (U.K.) | 65266 |
| APAC | Johnston I. (U.S.) | 64587 |  | APAC | Polynesie Francaise | 65267 |
| MID | Jordan | 64588 |  | NACC | Puerto Rico | 65268 |
| ESAF | Kenya | 64589 |  | MID | Qatar | 65269 |
| MID | Kingdom of Bahrain | 64590 |  | APAC | Republic of Korea | 65270 |
| APAC | Kingman Reef (U.S.) ? | 64591 |  | APAC | Republic of the Fiji Islands | 65271 |
| APAC | Kiribati | 64592 |  | ESAF | Rwanda | 65272 |
| MID | Kuwait | 64593 |  | NACC | Saint Kitts and Nevis | 65273 |
| ESAF | La Reunion (France) | 64594 |  | NACC | Saint Lucia | 65274 |
| APAC | Lao People's Democratic Republic | 64595 |  | NACC | Saint Vincent and the Grenadines | 65275 |
| MID | Lebanon | 64596 |  | APAC | Samoa | 65276 |
| ESAF | Lesotho | 64597 |  | WACAF | Sao Tome and Principe | 65277 |
| WACAF | Liberia | 64598 |  | MID | Saudi Arabia | 65278 |
| MID | Libyan Arab Jamahiriya | 64599 |  | WACAF | Senegal | 65279 |
| APAC | Macao Special Administrative Region of China | 64600 |  | ESAF | Seychelles | 65280 |
| ESAF | Madagascar | 64601 |  | WACAF | Sierra Leone | 65281 |
| ESAF | Malawi | 64602 |  | APAC | Singapore | 65282 |
| APAC | Malaysia | 64603 |  | APAC | Solomon Islands | 65283 |
| APAC | Maldives | 64604 |  | ESAF | Somali Republic | 65284 |
| WACAF | Mali | 64605 |  | ESAF | South Africa | 65285 |
| APAC | Mariana Is. (U.S.) | 64606 |  | APAC | Sri Lanka | 65286 |
| APAC | Marshall Islands | 64607 |  | MID | Sudan | 65287 |
| EUR/NAT | Albania | 64608 |  | SAM | Suriname | 65288 |
| EUR/NAT | Algeria | 64804 |  | ESAF | Swaziland | 65289 |
| EUR/NAT | Andorra | 64808 |  | MID | Syrian Arab Republic | 65290 |
| EUR/NAT | Armenia | 64612 |  | APAC | Thailand | 65291 |
| EUR/NAT | Austria | 64616 |  | WACAF | Togo | 65292 |
| EUR/NAT | Republic of Azerbaijan | 64620 |  | APAC | Tonga | 65293 |
| EUR/NAT | Belarus | 64624 |  | NACC | Trinidad And Tobago | 65294 |
| EUR/NAT | Belgium | 64628 |  | NACC | Turks And Caicos Islands (U.K.) | 65295 |
| EUR/NAT | Bosnia and Herzegovina | 64632 |  | APAC | Tuvalu | 65296 |
| EUR/NAT | Bulgaria | 64636 |  | ESAF | Uganda | 65297 |
| EUR/NAT | Croatia | 64640 |  | ESAF | Union of the Comoros | 65298 |
| MID | Cyprus | 64644 |  | MID | United Arab Emirates | 65299 |
| EUR/NAT | Czech Republic | 64648 |  | ESAF | United Republic of Tanzania | 65300 |
| EUR/NAT | Denmark | 64652 |  | NACC | United States of America | 65301 |
| EUR/NAT | Estonia | 64656 |  | SAM | Uruguay | 65302 |
| EUR/NAT | Finland | 64660 |  | APAC | Vanuatu | 65303 |
| EUR/NAT | France | 64664 |  | APAC | Viet Nam | 65304 |
| EUR/NAT | Georgia | 64668 |  | NACC | Virgin Islands (U.K.) | 65305 |
| EUR/NAT | Germany | 64672 |  | NACC | Virgin Islands (U.S.) | 65306 |
| EUR/NAT | Gibraltar | 64812 |  | APAC | Wake I. (U.S.) | 65307 |
| EUR/NAT | Greece | 64676 |  |  | Western Sahara | 65308 |
| EUR/NAT | Greenland | 64816 |  | MID | Yemen | 65309 |
| EUR/NAT | Hungary | 64680 |  | ESAF | Zambia | 65310 |
| EUR/NAT | Iceland | 64684 |  | ESAF | Zimbabwe | 65311 |

ICAO

Aeronautical Telecommunication Network (ATN)

Manual for the ATN using IPS Standards and Protocols (Doc 9896)

Part II

IPS Applications

Part II Table of Contents

1.0 INTRODUCTION 	3

1.1 Objective 	3

2.0 LEGACY ATN APPLICATIONS 	3

2.1 Ground Applications 	3

2.1.1 ATSMHS 	3

2.1.2 AIDC	 3

2.2 air-ground applications 	4

2.2.1 Legacy Dialogue Service 	4

2.2.2 CPDLC, ADS and FIS 	5

2.2.3 CM 	5

2.2.4 ATN IPS Dialogue Service Primitives 	5

2.2.5 Dialogue Service Definition 	6

2.3 Transport Layer 	23

2.3.1Overview 	23

2.3.2 Providing Dialogue Service over UDP 	24

2.3.3 Connection-ids 	25

2.3.4 Detecting Lost Datagrams 	26

2.3.5 Connection Timeout 	27

2.3.6 “More” Indicator 	27

2.3.7 DS-Provider Parameters 	27

2.4 IPS Dialogue Service State Tables 	29

2.4.1 IPS Dialogue Service TCP State Tables 	29

2.4.2 IPS Dialogue Service UDP State Tables 	31

# 1.0 INTRODUCTION

## 1.1 Objective

Note. – This part indicates how legacy ATN applications can make use of the ATN/IPS.

# 2.0 LEGACY ATN APPLICATIONS

Note. – Legacy ATN applications are defined in Doc 9705 and/or Doc 9880. The ATN applications described in Doc 9705/9880 specify the use of the ATN/OSI layers for lower layer communications, termed the Internet Communication Services. This section indicates how those applications make use of the ATN/IPS with minimal impacts on the applications themselves.

## 2.1 Ground Applications

### 2.1.1 ATSMHS

Note. –  The ATS Message Handling Services (ATSMHS) application aims at providing generic message services over the Aeronautical Telecommunication Network (ATN).

2.1.1.1 IPS hosts that support the ATSMHS application shall comply with Doc 9705 Edition 3 with the exception of clause 3.1.2.2.2.1.2 ("Use of Transport Service").

2.1.1.2 To operate ATSMHS over ATN IPS, IPS hosts shall:

a) make use of RFC-2126 to directly provide TCP/IPv6 interface; or,

b) make use of RFC-1006 to provide a TCP/IPv4 interface combined with IPv4/IPv6 protocol translation device(s).

### 2.1.2 AIDC

Note 1. – The AIDC application exchanges information between ATS Units (ATSUs) for support of critical Air Traffic Control (ATC) functions, such as notification of flights approaching a Flight Information Region (FIR) boundary, coordination of boundary conditions and transfer of control and communications authority.

Note 2. – AIDC is considered too complex to easily map to an IPS environment.

2.1.2.1 IPS hosts in the ATN that support the AIDC application exchanges may make use of the equivalent operational application described in the EUROCONTROL Specifications for On-Line Data Interchange (OLDI).

2.1.2.2 IPS hosts in the ATN that support the OLDI application shall make use of EUROCONTROL Specifications for the Flight Message Transfer Protocol to operate the application over TCP/IPv6.

## 2.2 air-ground applications

### 2.2.1 Legacy Dialogue Service

2.2.1.1The legacy Dialogue Service (DS) served as an interface between the dialogue service and the upper layers (session down) via the control function.  In order to minimize the impacts to the legacy ATN applications, a new dialogue service that allows the legacy ATN applications to operate over the ATN IPS is introduced.  This section specifies a replacement for the ULCS Dialogue Service (DS) interface to the upper layers, called the IPS DS.

2.2.1.2 The IPS DS does not have an interface to the session layer; instead it is mapped to TCP/UDP primitives in a fashion similar to RFC1006 for TP0 over TCP/IP.  This is depicted in Error! Reference source not found..  One of the differences is that for the IPS DS, there is no transport-transport interface.  It is an upper layer to transport interface, i.e. a service above TCP/UDP.  While conceptually similar, the upper layers will be interfacing with transport services instead of network services.

Figure 0-1.  ATN IPS Upper Layers Diagram

2.2.1.3 In order to accommodate legacy ATN/OSI air-ground applications over the IPS, the following IPS Dialogue Service (DS) definition is used.  Parameters from the ATN/OSI DS will be mapped as detailed in the sections below.  This mapping supersedes the ULCS specification of ICAO Doc 9705 and Doc 9880.

2.2.1.4 The ATNPKT header format defined below describes a dedicated format designed to accommodate the passing of legacy ATN application data over the ATN IPS.  Either TCP or UDP may be used with the ATNPKT header format.

### 2.2.2 CPDLC, ADS and FIS

2.2.2.1 IPS hosts that support the ATN/OSI Controller-Pilot Data Link (CPDLC), Automatic Dependent Surveillance (ADS) and Flight Information Services (FIS) applications shall comply with Doc 9705 or Doc 9880.

### 2.2.3 CM

2.2.3.1 IPS hosts that support the ATN/OSI Context Management (CM) application shall comply with Doc 9880.

Note 1. – This is in order to allow passing the new IPS addressing information contained in the updated CM application ASN.1.

Note 2. – The CM application is also known as the Data Link Initiation Capability (DLIC) service.

### 2.2.4 ATN IPS Dialogue Service Primitives

Note. – In order to retain commonality with the ULCS dialogue service primitives described in Doc 9880, the IPS DS uses the same primitive names.

2.2.4.1 Implementations which claim to support the DS functionality shall exhibit the behaviour defined by the service primitives in Table Table 0-1.

Table 0-1.  Summary of Dialogue Service Primitives

| Service | Description |
| --- | --- |
| D-START | This is a confirmed service used to establish the binding between the communicating DS-Users. |
| D-DATA | This unconfirmed service is used by a DS-User to send a message from that DS-User to the peer DS-User. |
| D-END | This is a confirmed service used to provide the orderly unbinding between the communicating DS-Users, such that any data in transit between the partners is delivered before the unbinding takes effect. |
| D-ABORT | This unconfirmed service can be invoked to abort the relationship between the communicating DS-Users. Any data in transit between them may be lost. |
| D-P-ABORT | This unconfirmed service is used to indicate to the DS-User that the dialogue service provider has aborted the relationship with the peer DS-User. Any data in transit between the communicating DS-Users may be lost. |
| D-UNIT-DATA | This unconfirmed service is used to send a single data item from one peer DS-User to another. Any problem in delivering the data item to the recipient will not be signalled to the originator. This service is specified in 2.7. |

Table 0-2.  Parameters of the Dialogue Service Primitives

| Service | Parameters |
| --- | --- |
| D-START | Called Peer ID Called Sys-ID Called Presentation Address Calling Peer ID Calling Sys-ID Calling Presentation Address DS-User Version Number Security Requirements Quality-of-Service Result Reject Source User Data |
| D-DATA | User Data |
| D-END | Result User Data |
| D-ABORT | Originator User Data |
| D-P-ABORT | (no parameters) |

Note. – The parameters of the dialogue service primitives are mapped to either the IP header, a field of the transport protocol header, or as transport data in the ATNPKT format defined in 2.2.4.2.

### 2.2.5 Dialogue Service Definition

#### 2.2.5.1 Sequence of Primitives

2.2.5.1.1 Implementations which claim to support the DS functionality shall exhibit behaviour allowing two communicating DS-Users to:

a)	establish a dialogue;

b)	exchange user data;

c)	terminate a dialogue in an orderly or abnormal fashion; and

d)	be informed of DS abnormal dialogue termination due to the underlying communications failure;

e)	be consistent with the appropriate use of the corresponding service primitives.

2.2.5.1.2 Either DS-User may send data at any time after the initial D-START exchange, by using the D-DATA service.  Under normal circumstances, a dialogue is released by a DS-User invoking the D-END service.  A dialogue is abnormally released with the D-ABORT service.  If the underlying service provider abnormally releases the dialogue, the DS-Users which are aware of the dialogue will be notified with the D-P-ABORT service.

2.2.5.1.3 For the purposes of this service definition, it is only valid for the DS-User to issue and be prepared to receive primitives for one Dialogue according to the permitted sequences of DS primitives shown in Table 0-3, where intersections marked “Y” show possible primitives which may occur after the primitive in the column heading.

Table 0-3.  Sequence of DS primitives for one Dialogue at one DS-User

| The DS primitive -> | D-START | D-DATA | D-END | D-ABORT | D-P-ABORT |
| --- | --- | --- | --- | --- | --- |
| May be followed by the DS primitive Y | req | cnf | ind | rsp | req | ind | req | cnf | ind | rsp | req | ind | ind |
| 1 D-START req |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 2 D-START cnf (accepted) | Y |  |  |  |  |  |  |  |  |  |  |  |  |
| 3 D-START ind |  |  |  |  |  |  |  | Y |  | Y | Y | Y | Y |
| 4 D-START rsp (accepted) |  |  | Y |  |  |  |  |  |  |  |  |  |  |
| 5 D-DATA req |  | Y |  | Y | Y | Y |  |  | Y |  |  |  |  |
| 6 D-DATA ind |  | Y |  | Y | Y | Y | Y |  |  |  |  |  |  |
| 7 D-END req |  | Y |  | Y | Y | Y |  |  |  |  |  |  |  |
| 8 D-END cnf (accepted) |  |  |  |  |  |  | Y |  |  |  |  |  |  |
| 9 D-END ind |  | Y |  | Y | Y | Y |  |  |  |  |  |  |  |
| 10 D-END rsp (accepted) |  |  |  |  |  |  |  |  | Y |  |  |  |  |
| 11 D-ABORT req | Y | Y | Y | Y | Y | Y | Y |  | Y |  |  |  |  |
| 12 D-ABORT ind | Y | Y | Y | Y | Y | Y | Y |  | Y |  |  |  |  |
| 13 D-P-ABORT ind | Y | Y | Y | Y | Y | Y | Y |  | Y |  |  |  |  |

#### 2.2.5.2 ATNPKT Format

The purpose of the ATNPKT is to convey information between peer DS-Users during the processing of a DS primitive.  It is carried in the data part of the transport protocol (either TCP or UDP).  It is used to convey parameters of the service primitives that cannot be mapped to existing IP or transport header fields. The ATNPKT will also convey information to allow the Dialogue Service protocol function (e.g. the type of DS primitive).

In order to provide the most efficient use of bandwith, a variable length format is used which depends on the processed DS primitive in order to optimize the amount of bytes being transferred. This is an important issue when operating over narrow band or costly air ground communication links.

The ATNPKT format is split in two parts:

- a fixed part containing parameters that are present regardless of the DS primitive, and

- a variable part containing optional fields.

In order to handle optional parameters, the presence of the ATNPKT fields will be indicated by a bit field included in the fixed part ('Presence Flag'). Their position in the variable part will be determined by their position in the bit field. Their representation will depend on their characteristics; the ones with a variable length will be represented in LV format (i.e. Length + Value), for the others only the value will be required.  The ATNPKT format is shown in Figure 0-2.

Figure 0-2.  ATNPKT Format

#### 2.2.5.3 ATNKPKT Fields

2.2.5.3.1 Each of the ATNPKT fields is described below using the following conventions:

- the field characteristics are given between brackets ( <bits> /<provider> / <usage> )

- the <bits> field is the length of the value field (not including the length itself),

- the <provider> field indicates if the value is provided by the DS-User as primitive parameter (external) or assigned by the DS-Provider itself (internal),

- the <usage> field indicates whether or not the DS-User may omit to provide a value for the corresponding primitive parameter (optional vs. mandatory).

#### 2.2.5.4 Fixed Part of ATNPKT

2.2.5.4.1 ATNPKT Version:

Note. – The ATNPKT version indicates the version of the ATNPKT header currently being used.

2.2.5.4.1.1 The ATNPKT version shall be set to 1 for the present specification and have a format of (4 bits / internal / mandatory).

Note 1.  – The ATNPKT version will be rolled to account for any subsequent modifications to the packet format.

Note 2.  – Reserving 4 bits will give provision for up to 15 versions; this is considered to be more than enough provided that the future applications are not supposed to use the Dialogue Service; rather, they will be developed directly on top of the transport layer.

Note 3.  – This field is not exposed at the DS-User's level; it will be set by the DS-Provider.

2.2.5.4.2 DS Primitive (4 bits / internal / mandatory):

Note. – The DS Primitive field is set by the DS-Provider to indicate the type of DS primitive that the packet meant to carry.

2.2.5.4.2.1 The DS Primitive field shall take one of the values specified below and have a format of (4 bits / internal / mandatory):

| Value | Assigned DS Primitive |
| --- | --- |
| 1 | D-START |
| 2 | D-STARTCNF |
| 3 | D-END |
| 4 | D-ENDCNF |
| 5 | D-DATA |
| 6 | D-ABORT |
| 7 | D-UNIT-DATA |
| 8 | D-ACK |
| 9 | D-KEEPALIVE |

Note 1. – Reserving 4 bits will give provision for up to 16 protocol elements, allowing up to 7 additional primitives to be defined.

Note 2. – The D-P-ABORT is not listed, as it is not sent end-to-end.  Upon receipt of an abnormal event or expiration of an inactivity timer, the D-P-ABORT indication will be given to the DS-User.

##### 2.2.5.4.3 Application Technology Type

Note. – The Application Technology Type identifies the type of application information that is being carried. Other legacy applications besides legacy ATN may also take advantage of the IPS infrastructure, e.g. FANS-1/A, ACARS, etc.

2.2.5.4.3.1 The Application Technology Type shall be set to a value of b000 to indicate “ATN IPS DS” and have a format of (3 bits / internal / optional).

Note. – Additional values to be defined are outside the scope of this manual.

##### 2.2.5.4.4 More

Note. – The More bit will be used as more indicator for segmentation and reassembly of datagrams, and is part of the reliability mechanisms further described in 0.

2.2.5.4.4.1 The more bit shall take a value of 0 to indicate a single or last segment or a value of 1 to indicate the first or intermediate segment and have a format of (1 bit / internal / optional).

#### 2.2.5.4.5 Presence Field

Note.  The Presence Field is a series of bits that indicate whether or not particular fields are present the in the ATNPKT format being exchanged.

2.2.5.4.5.1 The Presence Field shall use a bit value of 0 to indicate the absence of an optional field or a bit value of 1 to indicate the presence of an optional field, and have a format of (12 bits / internal / mandatory).

2.2.5.4.5.2 The optional field details shall comply with Table 0-4.

Table 0-4.  Presence Field Details

| Bit | Optional field | Size (in bits) | Format | Description |
| --- | --- | --- | --- | --- |
| 0 | Source ID | 16 | V | DS connection identifier of the sender |
| 1 | Destination ID | 16 | V | DS connection identifier of the recipient |
| 2 | Sequence numbers | 8 | V | Sequence numbers (Ns, Nr) |
| 3 | Inactivity time | 8 | V | Inactivity timer value of the sender (in minutes) |
| 4 | Called Peer ID | 24 to 64 (+8) | LV (1) | Called Peer ID (provided by the local DS-User) |
| 5 | Calling Peer ID | 24 to 64 (+8) | LV (1) | Calling Peer ID (provided by the local DS-User) |
| 6 | Content Version | 8 | V | Version of the application data carried |
| 7 | Security Indicator | 8 | V | Security requirements: 0 – No security (default value) 1 – Secured dialogue supporting key management 2 – Secured dialogue 3…255 – Reserved |
| 8 | Quality of Service | 8 | V | ATSC Routing Class: 0 – No traffic type policy preference 1 – "A" 5 – "E" 2 – "B" 6 – "F" 3 – "C" 7 – "G" 4 – "D" 8 – "H" 9…255 – Reserved |
| 9 | Result | 8 | V | Result of a request to initiate or terminate a dialogue: 0 – accepted (default value) 1 – Rejected transient 2 – Rejected permanent 3…255 – Reserved |
| 10 | Originator | 8 | V | Originator of the abort: 0 – user (default value) 1 – provider 2…255 – Reserved |
| 11 | User Data | UDP : 0 to 8192 (+16) TCP: Variable size (+16) | LV (2) | User Data (provided by the local DS User) |

Note 1. – The additional bits required for the length part of LV parameters is

indicated between brackets in the above table.

Note 2. – An optional field is present in the variable part when the corresponding bit is on in the presence field and has one of the following formats:

- V = value

- LV (1) = length (1 byte) + value

- LV (2) = length (2 bytes) + value

#### 2.2.5.5 Variable Parts of ATNPKT

Note. – The variable parts of the ATNPKT will be provided on an as needed basis depending on the DS primitive being exchanged and the current state of the application using the IPS DS.

2.2.5.5.1 The position of an optional field in the variable part of the ATNPKT shall match the relative position of its corresponding bit in the 'Presence Flag' (i.e. options are in the same order as the presence flag).

2.2.5.5.2 Source ID

Note. – The Source ID identifies the DS connection at sender side. This field is used as part of the reliability mechanisms described in 0.

2.2.5.5.2.1 The Source ID shall be present in the D-START and D-STARTCNF primitives, and also when D-ABORT is transmitted after D-START and before D-STARTCNF is received and have a format of (16 bits / internal / optional).

2.2.5.5.3 Destination ID

Note.  – The Destination ID identifies the connection at recipient side. This field is used as part of the reliability mechanisms described in 0.

2.2.5.5.3.1 The Destination ID shall be present in the D-STARTCNF, D-DATA, D-END, D-ENDCNF, D-ABORT, D-ACK and D-KEEPALIVE primitives and have a format of (16 bits / internal / optional).

2.2.5.5.4 Sequence Numbers

Note. – The Sequence Numbers field contains the sequence numbers to be included in the ATNPKT. This mechanism is used to detect the loss and the duplication of UDP datagrams; it allows implicit (i.e.  the service confirmation) or explicit acknowledgement (D-ACK).  This field is part of the reliability mechanisms described in 0.

2.2.5.5.4.1 The Sequence Numbers field shall be present in all DS primitives over UDP and have the format (8 bits / internal / mandatory) as detailed in Figure 0-3 below:

Figure 0-3.  Sequence Number Format

N(S) - [0…15] - sequence number of the ATNPKT sent.

N(R) - [0…15] - expected sequence number of the next ATNPKT to be received.

Note – For D-ACK and D-KEEPALIVE, only the N(R) is meaningful on transmission.

2.2.5.5.4.2 When using Sequence Numbers with D-ACK and D-KEEPALIVE over UDP, the current value of the send sequence number for N(S) may be used without subsequently incrementing it after transmission.

2.2.5.5.5 Inactivity Time

Note. – The Inactivity Time indicates the value (in minutes) of the inactivity timer at sender side. This field is used as part of the reliability mechanisms described in 0.

2.2.5.5.5.1The Inactivity Time shall be optionally present in the D-START and D-STARTCNF Primitives and have the format (8 bits / internal / optional).

2.2.5.5.5.2 When this parameter is not provided by the DS-User, the default value of 4 minutes shall be used as inactivity timer by the source DS-Provider.

2.2.5.5.6 Called Peer ID

Note. – The Called Peer ID identifies the intended peer DS-User.

2.2.5.5.6.1 The Called Peer ID shall be either a 24 bit ICAO Aircraft Identifier or a 3 – 8 character ICAO Facility Designation and have the format (24 to 64 bits / external / optional).

2.2.5.5.7 Calling Peer ID

Note. – The Calling Peer ID identifies the initiating peer DS-User.

2.2.5.5.7.1 The Calling Peer ID shall be either a 24 bit ICAO Aircraft Identifier or a 3 – 8 character ICAO Facility Designation and have the format (24 to 64 bits / external / optional).

2.2.5.5.8 Content Version

Note. – The Content Version field is used to indicate the application’s version number.

2.2.5.5.8.1 The Content Version shall be the version of the ASN.1 syntax used for the User Data field and have the format (8 bits / external / optional).

2.2.5.5.9 Security Indicator

Note 1. – The Security Indicator parameter is used to convey the level of security to be applied to the dialogue.  In Doc9705/ 9880, this field is referred as 'Security Requirements'; it is renamed here as 'requirement' is not really appropriate in this case.  It is really an indication from the local DS-user on the kind of security procedure to setup.

2.2.5.5.9.1 The Security Indicator parameter shall take one of the following values and have a format of (8 bits / external / optional):

| Value | Security Level |
| --- | --- |
| 0 | No security (default value) |
| 1 | Secured dialogue supporting key management |
| 2 | Secured dialogue |
| 3 – 255 | Reserved |

Note. – The omission of this parameter by the DS-User is equivalent to the default value.

2.2.5.5.10 Quality of Service

Note. – The Quality of Service is used to convey the quality of service (when provided by the DS-User) as a value corresponding to ATSC Routing Class.  The Quality of Service may also be used for other types of QoS the mapping to be applied as specified below.

2.2.5.5.10.1 The Quality of Service shall have a format of (8 bits / external / optional) and take  values of:

- The DS-User-provided ATSC Routing class as below:

| Value | ATSC Routing Class Description |
| --- | --- |
| 0 | No traffic type policy preference |
| 1 | “A” |
| 2 | “B” |
| 3 | “C” |
| 4 | “D” |
| 5 | “E” |
| 6 | “F” |
| 7 | “G” |
| 8 | “H” |
| 9 – 255 | Reserved |

- The Residual Error Rate (RER) as defined below:

| Value | RER Level |
| --- | --- |
| 0 | Low |
| 1 | Medium |
| 2 | High |

- Priority as defined in 2.3.6 of Part I of this document may be implemented by mapping the Differentiated Service field of RFC2474 to the ‘Traffic Class’ for IPv6 as the class selector codepoint as below:

| Bits 0 – 2 of the Differentiated Services Codepoint | Corresponding Application |
| --- | --- |
| 111 | Reserved for IP traffic routing (network control) |
| 110 | Reserved for IP traffic routing (internetwork control) |
| 101 | Reserved for higher priority applications |
| 100 | CDPLC, ADS |
| 011 | FIS |
| 010 | CM |
| 001 | Unused |
| 000 | Unused |

Note. – The priority is normally set by the network layer, so it is not necessary for the application to provide it.  The network layer can discern the priority by the port number being used, and set the differentiated service field accordingly.  It should also be noted that the network manager may remark the packet regardless of what the application indicates depending on the local differentiated service definitions.

2.2.5.5.10.2 The TCP and UDP checksum may be activated for low or medium RER values and not activated for a high RER value.

Note. – The TCP and UDP checksums are activated by default.

2.2.5.5.11 Result

Note. – The Result is set by the destination DS-User in order to indicate whether or not the requested dialogue initiation or termination completed successfully.

2.2.5.5.11.1 The Result shall have the format of (8 bits / external / mandatory) and take one of the values below:

| Value | Definition |
| --- | --- |
| 0 | Accepted |
| 1 | Rejected (transient) |
| 2 | Rejected (permanent) |
| 3 – 255 | Reserved |

2.2.5.5.12 Originator

Note. – The Originator indicates the source of a D-ABORT.

2.2.5.5.12.1 The Originator shall have the format of (8 bit / external / optional) and take of the values below:

| Value | Definition |
| --- | --- |
| 0 | User (default) |
| 1 | Provider |
| 2 – 255 | Reserved |

Note. – When this parameter is not provided by the DS-User the default value shall be assumed.

2.2.5.5.13User Data

Note. – The User Data contains the PER encoded application data.

2.2.5.5.13.1 The User Data shall have the format of (UDP: 0 to 8192, TCP: variable size / external / optional).

#### 2.2.5.6 IPS DS Parameter Mapping

Note. – The intent of the IPS DS is to present an identical interface to the legacy applications of the ULCS as specified in Doc 9880.  As such, the parameters of the IPS DS are identical to those of the ULCS.  However, there is a different mapping of the contents of those parameters.  These modified mappings are summarized in Table 0-5  below and detailed for each primitive in Table 0-6.

Table 0-5.  IPS DS - ULCS DS Parameter Mapping

| DS Parameter Visible to the DS-User | IP Header | Transport Protocol Header | ATNPKT (See 0) | Comment |
| --- | --- | --- | --- | --- |
| Called Peer ID |  |  | Called Peer ID | This can be an ICAO 24 bit aircraft address or an ICAO Facility Designator (4 to 8 characters) |
| Called Sys-ID |  | Destination Port Number |  | This is a “well-known” port number assigned to each ATN application |
| Called Presentation Address | Destination IP Address |  |  | IP address of the recipient ATN application |
| Calling Peer ID |  |  | Calling Peer ID | This can be an ICAO 24 bit aircraft address or an ICAO Facility Designator (4 to 8 characters) |
| Calling Sys-ID |  | Source Port Number |  | Using TCP, this port number is dynamically assigned by the transport protocol stack on the client side. With UDP, this port number has a static value, which is supposed to the same as the destination port number. |
| Calling Presentation Address | Source IP Address |  |  | IP address of the originator of the ATN application |
| DS-User Version Number |  |  | Content Version | This is the application’s version number |
| Security Requirements |  |  | Security Requirements | 00 – No security 01 – Secured dialogue Supporting Key Management 02 – Secured Dialogue 03 – Reserved |
| Quality of Service |  |  | Quality of Service | This parameter is to be transported only when provided as ‘ATSC Routing Class’; the RER and Priority are not indicated end-to-end but are optionally indicated to the IPS DS and used locally |
| Result |  |  | Result | 00 – Accepted 01 – Rejected (permanent) 02 – Rejected (transient) |
| Reject Source |  |  |  | 00 – the remote DS-User 01 – the local DS-Provider Provided locally in the Confirmation primitive only; not transferred end-end |
| Originator |  |  | Originator | 0 – User 1 – Provider (default) 2-255 – Reserved |
| User Data |  |  | User Data | This is the PER encoded data provided by the application |

2.2.5.6.1 The inclusion of optional ATNPKT parameters for each DS protocol message shall comply with Table 0-6:

Table 0-6.  ATNPKT Parameters for DS Protocol Messages

| ATNPKT Parameter  | Protocol message  | D-START | D-STARTCNF | D-DATA | D-UNIT-DATA | D-END | D-ENDCNF | D-ABORT | D-ACK | D-KEEPALIVE |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Fixed part |  |  |  |  |  |  |  |  |  |
| ATNPKT Version | M | M | M | M | M | M | M | M | M |
| DS Primitive | M | M | M | M | M | M | M | M | M |
| Application Technology Type | M | M | M | M | M | M | M | M | M |
| More | O | O | O |  | O | O |  |  |  |
| Presence Flag | M | M | M | M | M | M | M | M | M |
| Variable part |  |  |  |  |  |  |  |  |  |
| Source ID | M (4) | M (4) |  |  |  |  | (1) |  |  |
| Destination ID |  | M (4) | M (4) |  | M (4) | M (4) | M (2) | M | M |
| Sequence Numbers | M (4) | M (4) | M (4) | M | M (4) | M (4) | M | M | M |
| Inactivity Time | O (3) | O (3) |  |  |  |  |  |  |  |
| Called Peer ID | O (3) |  |  | O |  |  |  |  |  |
| Calling Peer ID | O (3) |  |  | O |  |  |  |  |  |
| Content Version | O (3) | O (3) |  | O |  |  |  |  |  |
| Security Indicator | O (3) | O (3) |  | O |  |  |  |  |  |
| Quality Of Service | O (3) |  |  |  |  |  |  |  |  |
| Result |  | M (3) |  |  |  | M (3) |  |  |  |
| Originator |  |  |  |  |  |  | O |  |  |
| User Data | O (4) | O (4) | M (4) | M | O (4) | O (4) | O |  |  |

(O = optional, M = mandatory, empty = precluded to use)

(1) Source ID is present if D-ABORT is sent after D-START and before D-STARTCNF is received

(2) Destination ID is absent if D-ABORT is sent after D-START and before D-STARTCNF is received.

(3) For segmented messages this parameter is present only in the first segment.

(4) For segmented messages this parameter is present in all the segments

#### 2.2.5.7 Dialogue Service Primitives

Note. – In order to provide the services identified in 0, the primitives listed in Table 0-7 are used.  Each primitive may be either directly exposed to the DS-User (request/response primitives) or reported to the DS-User by the DS-Provider (indication/confirmation primitives).

Table 0-7.  Dialogue Service Primitive Details

| Interface Primitive | Dialogue Service Description | DS-User | DS-Provider |
| --- | --- | --- | --- |
| D-START req | Request to initiate a Dialogue with a peer DS-User | ( |  |
| D-START ind | Inform a local DS-User that a peer DS-User requested for a Dialogue initiation |  | ( |
| D-START rsp | Complete a pending Dialogue initiation with either a positive or a negative response | ( |  |
| D-START cnf | Inform a local DS-User that the peer DS-User completed the pending Dialogue initiation with either a positive or a negative response |  | ( |
| D-UNIT-DATA req | Send a datagram from the local DS-User to a peer DS-User (the end-to-end delivery of the datagram is not guaranteed) | ( |  |
| D-UNIT-DATA ind | Inform a local DS-User that a datagram is received from a peer DS-User |  | ( |
| D-DATA req | Send a datagram from the local DS-User to a peer DS-User over an established Dialogue | ( |  |
| D-DATA ind | Inform a local DS-User that a datagram is received from a peer DS-User over an established Dialogue |  | ( |
| D-END req | Request to terminate a Dialogue with a peer DS-User | ( |  |
| D-END ind | Inform a local DS-User that a peer DS-User requested for a Dialogue termination |  | ( |
| D-END rsp | Complete a pending Dialogue termination with either a positive or a negative response | ( |  |
| D-END cnf | Inform a local DS-User that the peer DS-User completed the pending Dialogue termination with either a positive or a negative response |  | ( |
| D-ABORT req | Request to abort a Dialogue with a peer DS-User | ( |  |
| D-ABORT ind | Inform a local DS-User that the peer DS-User requested to abort the Dialogue |  | ( |
| D-P-ABORT ind | Dialogue aborted by the DS-Provider |  | ( |

#### 2.2.5.8 Dialogue Service Time-Sequence Diagrams

Note. – The sections below illustrate the Dialogue Service protocol exchanges between source and destination DS-Providers, including the ATNPKT user data part.

2.2.5.8.1 D-START service

Figure 0-4.  D-START Service

2.2.5.8.2 D-DATA service

Note. - Figure 0-5 shows the D-DATA service over a TCP connection.  Due to the nature of the connection, an ACK is not required.  Figure 0-6 shows the D-DATA service over UDP.  In order to provide explicit acknowledgment of the receipt of the UDP packet, a D-ACK is returned by the receiver of the D-DATA ATNPKT.

Figure 0-5.  D-DATA Service (TCP)

Figure 0-6.  D-DATA Service (UDP)

2.2.5.8.3D-END service

Figure 0-7.  D-END Service

2.2.5.8.4 D-ABORT service

Figure 0-8.  D-ABORT Service

2.2.5.8.5 D-P-ABORT service

Note. – There is no ATNPKT format defined for the D-P-ABORT service, as it is a local indication to the DS-User only.

Figure 0-9.  D-P-ABORT Service

2.2.5.8.6 D-UNIT-DATA service

Note. - Figure 0-10 shows the D-DATA service over a TCP connection.  Due to the nature of the connection, an ACK is not required.  Figure 0-11 shows the D-DATA service over UDP.  In order to provide explicit acknowledgment of the receipt of the UDP packet, a D-ACK is returned by the receiver of the D-DATA ATNPKT.

Figure 0-10.  D-UNIT-DATA Service (TCP)

Figure 0-11.  D-UNIT-DATA Service (UDP)

2.2.5.8.7 D-ACK service

Figure 0-12.  D-ACK Service

2.2.5.8.8 D-KEEPALIVE service

Figure 0-13.  D-KEEPALIVE Service

## 2.3 Transport Layer

### 2.3.1Overview

2.3.1.1 The IPS DS has been designed to allow a user selection of either TCP or UDP for the transport protocol.  For simplicity, port-related operations are not considered as primitives.

2.3.1.2 The transport layer primitives are given in Table 0-1.

Table 0-1.  Transport Layer Primitives Used in the IPS DS

|  | Transport Layer |  |  |
| --- | --- | --- | --- |
| Interface Primitive | Description | TCP | UDP |
| OPEN | Connection establishment (referred as 'active' on initiator side, 'passive' on the other side) | ( |  |
| CLOSE | Connection termination (referred as 'active' on initiator side, 'passive' on the other side) | ( |  |
| RECEIVE | Receive transport level datagram | ( | ( |
| SEND | Send transport level datagram | ( | ( |

2.3.1.3 Table 0-2 gives the mapping to be applied between the Dialogue Service and the Transport Layer primitives.

Table 0-2.  Transport Layer - IPS DS Service Mapping

| Dialogue Service | Transport Layer |  |
| --- | --- | --- |
| Service | Interface Primitive | Interface Primitive | User Data | Protocol |
| Initialisation |  |  |
|  |  | OPEN (passive) |  | TCP |
| Dialogue Establishment |  |  |
| D-START | D-START req | OPEN (active) |  | TCP |
|  |  | SEND | D-START | TCP, UDP |
|  | D-START ind | RECEIVE | D-START |  |
|  | D-START rsp | SEND | D-STARTCNF |  |
|  | D-START cnf | RECEIVE | D-STARTCNF |  |
| Connectionless Data Exchange |  |  |
| D-UNIT-DATA | D-UNIT-DATA req | SEND | D-UNITDATA | UDP |
|  | D-UNIT-DATA ind | RECEIVE | D-UNITDATA |  |
| Connected-mode Data Exchange |  |  |
| D-DATA | D-DATA req | SEND | D-DATA | TCP, UDP |
|  | D-DATA ind | RECEIVE | D-DATA |  |
| Orderly Dialogue Termination (user initiated) |  |  |
| D-END | D-END req | SEND | D-END | TCP, UDP |
|  | D-END ind | RECEIVE | D-END |  |
|  | D-END rsp | SEND | D-ENDCNF |  |
|  |  | CLOSE (passive) |  | TCP |
|  | D-END cnf | RECEIVE | D-ENDCNF | TCP, UDP |
|  |  | CLOSE (active) |  | TCP |
| Forced Dialogue Termination (user initiated) |  |  |
| D-ABORT | D-ABORT req | SEND | D-ABORT | TCP, UDP |
|  |  | CLOSE (active) |  | TCP |
|  | D-ABORT ind | RECEIVE | D-ABORT | TCP, UDP |
|  |  | CLOSE (passive) |  | TCP |
| Error-related Dialogue Termination (provider initiated) |  |  |
| D-P-ABORT | D-P-ABORT ind | RECEIVE / SEND (failure) |  | TCP, UDP |
|  |  | Unexpected CLOSE (passive) |  | TCP |

### 2.3.2 Providing Dialogue Service over UDP

Note. – UDP is mostly employed for applications requiring broadcast or multicast, but it might also be used for simple "request-reply" applications provided that some reliability is added at the  highest levels. UDP by itself  is not reliable enough to guarantee the end-to-end delivery of the datagrams. For this reason, additional mechanisms are implemented to address UDP limitations; basically the truncation, loss, or duplication of UDP datagrams.  These mechanisms are specified in the following sections.

2.3.2.1 In order to add some reliability when acting over UDP, the DS-Provider shall implement the mechanisms as described in Table 0-3:

Table 0-3.  IPS DS UDP Reliability Mechanisms

| Provide ‘dialog connection’ over UDP -identification of connections - connection timeout - termination timeout | M O O |
| --- | --- |
| Detect the loss of UDP datagrams using one-to-one acknowledgments (on a per connection basis) - retransmission timer + max retry count - explicit ack nowledgment -piggy-back ed ack nowledgment (max delay before ack ) | M M O |
| Detect long-lived unpaired connections -inactivity timer + k eep alive | M |
| Handle UDP datagrams truncation - datagram segmentation / reassembly | M |

(O = optional, M = mandatory)

### 2.3.3 Connection-ids

2.3.3.1 A pair of connection-ids, the Source ID and Destination ID, shall be assigned during the connection phase (D-START / D-STARTCNF) by every participating DS peer and used over any subsequent exchanges.

Note 1. – DS connection identification above UDP will be handled by the assignment of this pair of connection-ids.

Note 2. – The 2 byte size for these identifiers was chosen because this will allow the DS-Provider to associate a particular semantic to the dialogue-id assigned on its side (without interference with the involved peer DS-User). In such a case, the identifier might be an index in a context table, making it implicitly unique, but also allowing the receiving DS-Provider to find out the context without having to use multiple search criteria and parsing the whole table of contexts.

2.3.3.2 The Source ID and Destination ID shall be conveyed in the variable part of the ATNPKT based on DS primitives as described in Table 0-4:

Table 0-4.  Source ID and Destination ID Usage

| DS Primitive field | Source ID | Destination ID |
| --- | --- | --- |
| D-START | M | Identifier given by the DS-Provider who initiates the dialogue; it will allow him to find out the dialogue context during the whole dialogue duration. | - | Unassigned at this time |
| D-STARTCNF | M | Identifier given by the DS-Provider who accepts the dialogue; it will allow him to find out the dialogue context during the whole dialogue duration. | M | Identifier of the DS-Provider who initiated the dialogue. |
| D-DATA | - | No need to transport it since it would be meaningless for the destination DS-Provider. | M | Identifier of the peer DS-Provider. |
| D-END | - | No need to transport it since it would be meaningless for the destination DS-Provider. | M | Identifier of the peer DS-Provider. |
| D-ENDCNF | - | No need to transport it since it would be meaningless for the destination DS-Provider. | M | Identifier of the peer DS-Provider. |
| D-ABORT before D-STARTCNF | M | Identifier given by the DS-Provider who initiated the dialogue. | - | Unknown for now. |
| D-ABORT other cases | - | No need to transport it since it would be meaningless for the destination DS-Provider | M | Identifier of the peer DS-Provider. |

(O = optional, M = mandatory)

### 2.3.4 Detecting Lost Datagrams

Note 1. – The loss of UDP datagrams is detected through a one-to-one acknowledgment mechanism, on a per DS connection basis: i.e. one data packet sent, one acknowledgement to be received before more data can be sent again.

Note 2. – The acknowledgment may be piggy-backed with a dialogue message in the reverse direction for the same dialogue; this will be possible for instance with confirmed primitives.

2.3.4.1 If the receiver has no message to send for the same dialogue (i.e. the service is unconfirmed), the receiving user shall use an explicit acknowledgment by sending an ATNPKT with no data and with a specific value (D-ACK) as 'DS Primitive'.

Note 1. – For acknowledgment purpose, the 'Sequence Numbers' field of the ATNPKT variable part will be used.

Note 2. – This sequence number is required to avoid delivering duplicated data to the peer DS-user following retransmission (i.e. if a D-ACK has been lost), and in more exceptional circumstances, when UDP datagrams are swapped by the network

2.3.4.2 The DS-Provider shall associate an incremental sequence number to outgoing ATNPKTs, conversely remember the sequence number of the last ATNPKT received from the peer DS-Provider in order to acknowledge it in a subsequent sending.

2.3.4.3 Both outgoing and incoming sequence numbers shall be respectively carried by the N(S) and N(R) subfields of the 'Sequence Numbers'.

Note 1. – N(S) corresponds to the current sequence number of the ATNPKT sent; N(R) is the next sequence number expected as N(S) from the remote DS-Provider (in his next sending).

Note 2. – Using sequence numbers will allow the DS-Provider to detect missing or duplicated ATNPKTs. In our specific case, there is at most one ATNPKT not acknowledged; for this reason there will be no grouped acknowledgments and there is no need to implement a selective reject mechanism.

Note 3. – The lack of reception of an acknowledgment will timely entail a retransmission; an excessive number of retransmission will break the DS connection.  The values of these parameters are detailed in Table 0-5.

### 2.3.5 Connection Timeout

Note. – In order to avoid long lived unpaired DS connections, a simple mechanism for detecting inactivity is implemented. Both ends of the DS connection will transmit a keepalive packet on 'keepalive timer' expiration during the whole duration of the connection; this timer will then be restarted by the sender each time it sends data on the connection (to avoid unnecessary keepalive transmission).

2.3.5.1 A keepalive (an ATNPKT with no data and with a value of D-KEEPALIVE as 'DS Primitive') shall be sent at each expiry of the local keepalive transmission timer.

2.3.5.2 The keepalive transmission timer may be set to 1/3 of the inactivity timer of the peer DS-Provider, or 1/3 of the default inactivity timer.

Note. – The lack of reception of either data or keepalive for an interval of time corresponding to the inactivity time will break the DS connection.  The parameter value for this time is detailed in Table 0-5.

2.3.5.3 The optional ATNPKT field ‘Inactivity Time’ may be used at dialogue initialization time (i.e. in D-START and D-STARTCNF) so that each DS-Provider can adjust its keepalive transmission timer.

Note. – Absence of the parameter indicates uses of the default value.

### 2.3.6 “More” Indicator

Note. – Most of the ATN applications messages do not exceeding 1000 bytes. Additionally the suggested value of 1024 bytes does not exceed the IP payload (1500 bytes) in the Ethernet frame (1518 bytes).

2.3.6.1 A D-DATA with a user data part exceeding 1024 bytes shall be segmented using the 'MORE' bit reserved in the ATNPKT fixed part.

Note. – Upon receipt of a D-DATA with the more bit set, the receiving side is responsible for ordering and segmenting the data.

### 2.3.7 DS-Provider Parameters

2.3.7.1 The values specified in Table 0-5 shall be applied to the identified DS-Provider parameters:

Table 0-5.  DS-Provider Parameters

| Parameter | Min | Max | Default |
| --- | --- | --- | --- |
| Delay before retransmission | 1 sec | 60 sec | 15 sec |
| Max number of transmissions | 1 | 10 | 3 |
| Inactivity time | 3 min | 15 min | 4 min |

## 2.4 IPS Dialogue Service State Tables

### 2.4.1 IPS Dialogue Service TCP State Tables

Table 0-1.  IPS DS State Table for TCP

| Events State ( ( | D-IDLE | D-CONNECTED | D-START-SENT | D-START-RECEIVED | D-TRANSFER | D-END-SENT | D-END-RECEIVED | D-WAIT-CLOSE |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| During initialisation phase | - OPEN (passive) |  |  |  |  |  |  |  |
| DS-User events | D-START req | - OPEN (active) - Map D-START req to D-START - SEND (D-START) - Enter D-START-SENT state |  |  |  |  |  |  |  |
|  | D-START rsp |  |  |  | - Map D-START cnf to D-STARTCNF - SEND (D-STARTCNF) - In case of positive response : - Start tinact - Enter D-TRANSFER state - Otherw ise : -Enter D-WAIT-CLOSE state |  |  |  |  |
|  | D-DATA req |  |  |  |  | - Map D-DATA req to D-DATA - SEND (D-DATA) |  |  |  |
|  | D-END req |  |  |  |  | - Cancel tinact - Map D-END req to D-END - SEND (D-END) - Enter D-END-SENT state |  |  |  |
|  | D-END rsp |  |  |  |  |  |  | - Map D-END rsp to D-ENDCNF - SEND (D-ENDCNF) -In case of positive response : -Enter D-WAIT-CLOSE state - Otherw ise : - Start tinact - Enter D-TRANSFER state |  |
|  | D-ABORT req |  |  | - Map D-ABORT req to D-ABORT - SEND (D-ABORT) - Enter D-WAIT-CLOSE state | - Map D-ABORT req to D-ABORT - SEND (D-ABORT) - Enter D-WAIT-CLOSE state | - Cancel tinact - Map D-ABORT req to D-ABORT - SEND (D-ABORT) - Enter D-WAIT-CLOSE state | - Map D-ABORT req to D-ABORT - SEND (D-ABORT) - Enter D-WAIT-CLOSE state | - Map D-ABORT req to D-ABORT - SEND (D-ABORT) - Enter D-WAIT-CLOSE state |  |
| TCP events | OPEN (passive) completed | - Enter D-CONNECTED state |  |  |  |  |  |  |  |
|  | RECEIVE (D-START) |  | - Map D-START to D-START ind - Report D-START ind to DS-User - Enter D-START-RECEIVED state |  |  |  |  |  |  |
|  | RECEIVE (D-STARTCNF) |  |  | - Map D-STARTCNF to D-START cnf - Report D-START cnf to DS-User - In case of positive response : - Start tinact - Enter D-TRANSFER state - Otherw ise : - CLOSE (active) -Enter D-IDLE state |  |  |  |  |  |
|  | RECEIVE (D-DATA) |  |  |  |  | - Reset tinact - Map D-DATA to D-DATA ind - Report D-DATA ind to DS-User |  |  |  |
|  | RECEIVE (D-END) |  |  |  |  | - Cancel tinact - Map D-END to D-END ind - Report D-END ind to DS-User - Enter D-END-RECEIVED state |  |  |  |
|  | RECEIVE (D-ENDCNF) |  |  |  |  |  | - Map D-ENDCNF to D-END cnf - Report D-END cnf to DS-User - In case of positive response : - CLOSE (active) - Enter D-IDLE state - Otherw ise : - Start tinact - Enter D-TRANSFER state |  |  |
| TCP events | RECEIVE (D-ABORT) |  |  |  | - Map D-ABORT to D-ABORT ind -Report D-ABORT ind to DS-User - CLOSE (active) -Enter D-IDLE state | - Cancel tinact - Map D-ABORT to D-ABORT ind - Report D-ABORT ind to DS-User - CLOSE (active) - Enter D-IDLE state | - Map D-ABORT to D-ABORT ind - Report D-ABORT ind to DS-User - CLOSE (active) - Enter D-IDLE state | - Map D-ABORT to D-ABORT ind - Report D-ABORT ind to DS-User - CLOSE (active) - Enter D-IDLE state |  |
|  | CLOSE (passive) |  | - CLOSE (active) - Enter D-IDLE state | - Report D-P-ABORT ind to DS-User - CLOSE (active) -Enter D-IDLE state | - Report D-P-ABORT ind to DS-User - CLOSE (active) -Enter D-IDLE state | - Cancel tinact - Report D-P-ABORT ind to DS-User - CLOSE (active) - Enter D-IDLE state | - Report D-P-ABORT ind to DS-User - CLOSE (active) - Enter D-IDLE state | - Report D-P-ABORT ind to DS-User - CLOSE (active) - Enter D-IDLE state | - CLOSE (active) - Enter D-IDLE state |
| DS-Provider events | tinact expires |  |  |  |  | - Report D-P-ABORT ind to DS-User - Enter D-IDLE state |  |  |  |

### 2.4.2 IPS Dialogue Service UDP State Tables

Table 0-2.  IPS DS State Table for UDP

| Events State ( ( | D-IDLE | D-START-SENT | D-START-RECEIVED | D-TRANSFER | D-END-SENT | D-END-RECEIVED |
| --- | --- | --- | --- | --- | --- | --- |
| DS-User events | D-START req | -Map D-START req to D-START - SEND (D-START) - Start tconnect - Enter D-START-SENT state |  |  |  |  |  |
|  | D-START rsp |  |  | - Map D-START cnf to D-STARTCNF - SEND (D-STARTCNF) -In case of positive response : - Start tinact -Enter D-TRANSFER state - Otherw ise : -Enter D-IDLE state |  |  |  |
|  | D-DATA req |  |  |  | - Map D-DATA req to D-DATA - SEND (D-DATA) |  |  |
|  | D-END req |  |  |  | - Cancel tinact -Map D-END req to D-END - SEND (D-END) - start tterm - Enter D-END-SENT state |  |  |
|  | D-END rsp |  |  |  |  |  | -Map D-END rsp to D-ENDCNF - SEND (D-ENDCNF) - In case of positive response : - Enter D-IDLE state - Otherw ise : - Start tinact - Enter D-TRANSFER state |
|  | D-ABORT req |  | - Cancel tconnect -Map D-ABORT req to D-ABORT - SEND (D-ABORT) - Enter D-IDLE state | - Map D-ABORT req to D-ABORT - SEND (D-ABORT) - Enter D-IDLE state | - Cancel tinact - Map D-ABORT req to D-ABORT - SEND (D-ABORT) - Enter D-IDLE state | - Cancel tterm - Map D-ABORT req to D-ABORT - SEND (D-ABORT) - Enter D-IDLE state | - Map D-ABORT req to D-ABORT - SEND (D-ABORT) - Enter D-IDLE state |
| UDP events | RECEIVE (D-START) | -Map D-START to D-START ind - Report D-START ind to DS-User - Enter D-START-RECEIVED state |  |  |  |  |  |
|  | RECEIVE (D-STARTCNF) |  | - Cancel tconnect -Map D-STARTCNF to D-START cnf - Report D-START cnf to DS-User -In case of positive response : -Start tinact - Enter D-TRANSFER state - Otherw ise : - Enter D-IDLE state |  |  |  |  |
|  | RECEIVE (D-DATA) |  |  |  | - Reset tinact - Map D-DATA to D-DATA ind - Report D-DATA ind to DS-User |  |  |
|  | RECEIVE (D-END) |  |  |  | - Cancel tinact -Map D-END to D-END ind - Report D-END ind to DS-User - Enter D-END-RECEIVED state |  |  |
|  | RECEIVE (D-ENDCNF) |  |  |  |  | - Cancel tterm -Map D-ENDCNF to D-END cnf - Report D-END cnf to DS-User - In case of positive response : - Enter D-IDLE state - Otherw ise : - Start tinact - Enter D-TRANSFER state |  |
|  | RECEIVE (D-ABORT) |  |  | - Map D-ABORT to D-ABORT ind - Report D-ABORT ind to DS-User - Enter D-IDLE state | - Cancel tinact - Map D-ABORT to D-ABORT ind - Report D-ABORT ind to DS-User - Enter D-IDLE state | - Cancel tterm - Map D-ABORT to D-ABORT ind - Report D-ABORT ind to DS-User - Enter D-IDLE state | - Map D-ABORT to D-ABORT ind - Report D-ABORT ind to DS-User - Enter D-IDLE state |
| D S events | tconnect expires |  | - Report D-P-ABORT ind to DS-User - Enter D-IDLE state |  |  |  |  |
|  | tinact expires |  |  |  | - Report D-P-ABORT ind to DS-User - Enter D-IDLE state |  |  |
|  | tterm expires |  |  |  |  | -Report D-P-ABORT ind to DS-User - Enter D-IDLE state |  |

ICAO

Aeronautical Telecommunication Network (ATN)

Manual for the ATN using IPS Standards and Protocols (Doc 9896)

Part III

Guidance Material Section

TABLE OF CONTENTS

1.0 Introduction	4

1.1  Background	5

1.2  Reference Document	5

1.3  Abbreviations	5

2.0 General Guidance	5

2.1 The ATN/IPS	6

2.1.1  The ATN/IPS Internetwork	6

2.1.2 Coordination of Policies Among Administrative Domains	7

2.1.3 ATN/IPS Internetworking with Mobility	8

2.2 Transition between IPv4 and IPv6	9

2.3 Network Transition Mechanisms	10

2.3.1 Tunnelling	11

2.3.2 Dual Stack	11

2.3.3 Translation	12

2.3.4 Combining of the Mechanisms	12

3.0 PROTOCOL Stack	13

3.1 Physical and Link Layer Guidance	13

3.2 Network Layer	13

3.2.1 Address Plan	13

3.2.2 Application interface to the network layer	13

3.2.3 Inter-domain routing	13

3.2.4 Multicast	15

3.3 Transport Layer	16

3.3.1 Transmission Control Protocol	16

3.3.2   User Datagram Protocol (UDP)	17

3.3.3 Transport Layer Addressing	17

3.3.4 Application Interface to the Transport Layer	18

3.3.5 Congestion Avoidance	18

3.3.6 Error Detection and Recovery	18

3.3.7 Performance Enhancing Proxies (PEPs)	19

4.0  MOBILITY GUIDANCE	19

4.1  MOBILE IPv6	19

4.1.1  MIPv6 Bidirectional Tunneling	20

4.1.2  MIPv6 Route Optimization	20

4.2 Enhancements to MIPv6	21

4.2.1  Heirarchical Mobile IPv6 (HMIPv6)	21

4.2.2  Fast Handovers for Mobile IPv6 (FMIPv6)	22

4.2.3 Proxy Mobile IPv6 (PMIPv6)	22

4.2.4 Network Mobility (NEMO)	22

5.0  SECURITY GUIDANCE	23

5.1 Requirments for Implementation	23

5.2 Ground-Ground Security	23

5.2.1 Ground-Ground IPsec	23

5.2.2 Ground-Ground IKEv2	24

5.2.3 Alternatives to IPsec/IKEv2 for Ground-Ground Security	24

5.3 Air-Ground Security	24

5.3.1 Air-Ground IPsec	24

5.3.2 Air-Ground IKEv2	25

5.3.3  Securing Air-Ground End-to-End Communications	26

5.3.4  Securing Access Network and Mobile IP Signalling	29

5.3.5 Public Key Infrastructure Profile and Certificate Policy	30

5.3.6 General Guidance for Implementation of Security	30

6.0 Voice over Internet Protocol (VoIP)	31

6.1 Standards and Protocols	31

6.1.1 H323	32

6.1.2 MGCP/MEGACO	2

7.0 IPS Implementations	1

7.1 OLDI	1

7.2 FMTP	1

7.2.1 Testing OLDI/FMTP	2

APPENDIX A – REFERENCE DOCUMENTS	3

APPENDIX B – ABBREVIATIONS/DEFINITIONS	1

FOREWORD

The material contained in this document supplements the Standards and Recommended Practices (SARPs) and the Manual for Detailed Technical Specifications.  This document is to be used to assist in the deployment of IPS systems of the Aeronautical Telecommunication Network (ATN)  as defined in Annex 10 — Aeronautical Telecommunications, Volume III — Communication Systems and Part I — Digital Data Communication Systems and the Manual on Detailed Technical Specification for the IPS ATN Doc 9896.

# 1.0 Introduction

The Aeronautical Telecommunication Network Internet Protocol Suite (ATN IPS) Guidance Document contains information to assist member states in the deployment of an IPS network for their state infrastructure to support the delivery of ICAO Air Traffic Management (ATM) services. The following minimum core services should be provided by ATN/IPS:IP network services, and Global information exchange.

These core services enable ATN IPS applications to provide voice and data services with the appropriate priority and security over a network with the required quality and class of service.

The protocols discussed in this document are referred to based on the open system interconnect reference model (OSI).  However, since IPS uses only 4 layers the mapping is not consistent with the reference model.  Figure 1.1 depicts the OSI reference model and the relationship between the ISO ATN and the IPS protocols.

Figure 1.1 Protocol Reference Model

1.1 Background

The ICAO/ATN has established with the specific goals of providing a commercial off the shelf global ATM services. Currently, ATN services can be provided using the ISO based ICAO protocols as documented is ICAO Standards 9705/9880. This document along with the ICAO ATN/IPS Standard 9896 [1] is an additional technical approach for networking, and will enable member state to have an additional resource for providing ATM services.

## 1.2 Reference Document

ICAO Document 9705 Manual of Technical Provisions for the ATN

ICAO Document 9880 Manual of Technical Provisions for the ATN

ICAO Document 9694 Manual of Air Traffic Services Data Link Applications

## 1.3 Abbreviations

ATN  		Aeronautical Telecommunications Network

ATM		Air Traffic Management

BGP		Border Gateway Protocol

IPS		Internet Protocol Suite

ICAO		International Civil Aviation Organization

IPv4		Internet Protocol Version 4

IPv6		Internet Protocol Version 6

ISO		International Organization for Standardization

MOA		Memorandum of Agreement

# 2.0 General Guidance

This section contains general guidance information about the implementation of IPS for ATN services. This document only discusses IPS based services for detailed information on ISO standards based ATN services refer to document 9705/9880.

The current recommendation of ICAO is to deploy IPv6 protocols and services but that does not preclude a member state network from supporting or deploying IPv4 services.  However, these services must remain transparent from the IPv6 portion of the network.  All transaction over the ICAO ATN must be done using ICAO standards 9705/9880 or 9896.

This document focuses on the network, transport and application services; physical and link services are to be negotiated on a service need basis by the implementing state.

ATN Administration

The administration of the ATN shall be performed by the member state and the their appointed service provider.  However, that does not preclude agreements between member states that form a federation in the interest of providing ATM services.

## 2.1 The ATN/IPS

### 2.1.1 The ATN/IPS Internetwork

The ATN/IPS Internetwork is specifically and exclusively intended to provide data communicattions services to air traffic service (ATS) provider organizations and aircraft operating agencies supporting the following types of communications traffic:

- ATS Communication (ATSC).  Communication related to air traffic services including air traffic control, aeronautical and meteorological information, position reporting and services related to safety and regularity of flight. This communication involves one or more air traffic service administrations.

- Aeronautical Administrative Communication (AAC). Communication used by aeronautical operating agencies related to the business aspects of operating their flights and transport services. This communication is used for a variety of purposes, such as flight and ground transportation, bookings, deployment of crew and aircraft or any other logistical purposes that maintain or enhance the efficiency of over-all flight operation.

- Aeronautical Operational Control (AOC). Communication required for the exercise of authority over the initiation, continuation, diversion or termination of flight for safety, regularity and efficiency reasons.

In order to support these communications types, this manual specifies a set of technical and administrative requirements on the entities which constitute the ATN/IPS.  See Figure 2.1-1.

Technical requirements in this manual are levied against an IPS router, an IPS host, or an IPS node when the requirement applies to both.  This manual adopts the RFC 2460 definition of an IPS node as a device that implements IPv6 and distinguishes between an IPS router as a node that forwards IP packets not addressed to itself and an IPS host as a node that is not a router.

Administrative requirements in this manual are levied against Administrataive Domains. An Administrative Domain is an organizational entity and can be an individual State, a group of States (e.g., an ICAO Region or a regional organization such as EURO-CONTROL), an Air Communications Service Provider (ACSP),  an Air Navigation Service Provider (ANSP), or other organizational enty that manages ATN/IPS network resources and services.

The primary requirement is that each Administrative Domain participating in the ATN/IPS internetwork must operate one or more IPS routers which execute an inter-domain routing protocol called the Border Gate Protocol.  This is essentially so that the ATN/IPS can be formed across the various Administrative Domains whereby any IPS host can reach any other IPS host in the ATN/IPS internetwork.

Figure 2.1-1 – The ATN/IPS Internetwork

An inter-domain routing protocol is used to exchange routing information among Autonomous Systems.  An Autonomous System is defined in RFC 1930 to be a connected group of one or more IP prefixes run by one or more network operators which has has a single and clearly defined routing policy.  From this definition we see two distinct entities: one is the AS as a group of IP prefixes and the other is the network operators, i.e., the Administrative Domains. This distinction is meaninful in the Internet since it permits multiple organizations (i.e., Administrative Domains) to run BGP to an Internet Service Provider (ISP) which in turn connects each of these organizations to the Internet.  This manual does not preclude using ISPs in this fashion; however, as noted above, requirements are levied directly on the Administrative Domains.

### 2.1.2 Coordination of Policies Among Administrative Domains

IPS routers will exchange information about their internal network prefixes with their immediate neighbour routers but may also forward routing information about other network prefixes learned from other BGP neighbours.  As a result, traffic between two Administrative Domains may be relayed by an number of intermediate Administrative Domains. Such traffic being carried on behalf of two others is termed transit traffic.

This manual does not specify which routes are to be advertised between IPS routers nor basic traffic management policies for a dynamically routed environment.  Administrataive Domains however are required to coordinate their policy for carring transit traffic with peer Administrative Domains.  Administrative Domains that  participate in the ATN/IPS should ensure the proper handling of transit traffic on the following basis:

- An Administrative Domain should not advertise a network prefix if it is not prepared to accept incoming traffic to that network prefix destination;

- When establishing the interconnections between two Administrative domains a charging mechanism may be agreed to support implicit corresponding transit policy;

- Administrative Domains that relay transit traffic should ensure that the associated security and QoS policies of the traffic is maintained

### 2.1.3 ATN/IPS Internetworking with Mobility

The fixed or ground-ground ATN/IPS described in section 2.1.1 may be extended to support mobility, that is, it may be extended to support air-ground communications.  This is accomplished through the use of Mobile IPv6, the IETFs general mobility solution.  Mobile IPv6 permits mobile nodes (MN) (i.e., aircraft in the ATN/IPS) to communicate transparently with correspondent nodes (CN) (i.e., ground automation systems in the ATN/IPS) while moving within or accross air-ground networks. An Administrative Domain in the ATN/IPS which offers Mobile IPv6 service is called a Mobility Service Provider (MSP).  Thus the ATN/IPS is extended to support mobility through the addition of MSPs providing mobility service to mobile nodes.  Figure 2.1-2 depicts the ATN/IPS with a Mobility Service Provider.  As is shown in this figure in order to provide mobilty service, the MSP must operate one or more home agents.  The home agent provides a key role in that on one side it provides location management to keep track of the movement of a mobile node and to locate the mobile node for data delivery, while on the other side it operates as an inter-domain router providing connectivity to the rest of the ATN/IPS.  (Note that this is a logical view.  Different physical configurations are possible in actual implementations.)

Figure 2.1-2 shows the minimal configuration, e.g., for ATSC, where the MSP might be an ACSP.  However, this is not the only possible configuration.  An ANSP may choose become its own MSP and obtain access service from an ACSP.  To support AOC and AAC an Airline may likewise become an MSP.  Similarly, an Airport Authority may decide to become a MSP and offer service to the ATN/IPS.  In this case IP layer mobility service may be offered along with or in addition to link layer mobility.  As noted in section 2.1.1, the ATN/IPS is intended to support ATSC, AAC, and AOC.  However, the mobility approach may be used by other aviation organization organizations.  These organizations may become MSPs and support other types of communications such as Airline Passenger Communications (APC).  In this case an enhanced form of Mobile IP service called Network Mobility (NEMO) may be offered.

## 2.2 Transition between IPv4 and IPv6

Current ground communications are generally handled through appropriate protocol profiles that are based on IPv4. For technical, economical and strategic reasons, transition to IPv6 will be made gradually and appropriate transition path need to be defined:

RFC 4213 - Basic Transition Mechanisms for IPv6 Hosts and Routers

This RFC discusses dual stack approaches as well as tunnelling IPv6 traffic through existing IPv4 networks. The three main interoperability cases are as follows:

- IPv6 nodes that require to communicate over an IPv4 sub network

- IPv4 nodes that require to communicate over an IPv6 sub network

- An IPv4 node that requires to communicate with an IPv6 node

Case 1 can be resolved by relying on common IPv6 over IPv4 tunnels. Although this does create additional overhead it would allow early deployment of ATN/IPS applications.

Case 2 could be resolved by relying on IPv4 over IPv6 tunnels. If the two autonomous IPv4 domains overlap in terms of routing and addressing; interoperability may not be achieved.  A dual stack approach is recommended to ensure that ATN systems can natively interface over the ATN/IPS without having to resort to such tunnelling techniques which may not be appropriate.

Case 3 can be the result of legacy applications that have not been updated to IPv6 or no longer maintained. In the ATN context, this issue needs to be considered as some application vendors (e.g. AMHS) do not have a dual stack solution and only support IPv4 profiles. This case can be handled through the use of network address translation from IPv4 to IPv6:

RFC 2766 - Network Address Translation - Protocol Translation (NAT-PT)

The benefit of NAT-PT and other similar mechanisms allow an IPv4-only system to behave as an IPv6 system and communicate over the ATN/IPS.

All ATN/IPS systems are recommended to adopt a dual stack approach in order to ensure native inter-working over the ATN/IPS and local IPv4 environments without having to rely on the use of external tunnelling or translation devices.

## 2.3 Network Transition Mechanisms

IPv6 has been adopted by the IETF and the internet authorities to cope with the ever increasing growth rate of the global internet. IPv6 solves many of the technical problems associated with IPv4, in particular the limited IPv4 address space.

The global implementation of IPv6 has already begun. It is the building block of the next generation internet which will enable a flexible means to roll-out new technologies and services. For this reason, the ATN IPS is based on IPv6 to take immediate advantage of new commercial off-the-shelf products and technologies.

The implementation of the ATN IPS will be gradual over a significant period of time. Many organizations will be required to go through multiple steps to ensure that ATN IPS end-systems and routers are integrated into their existing environment in particular for those that have deployed legacy ATN/OSI CLNP (primarily over Ethernet or “X.25”) and IPv4 systems.

Three transitions mechanisms can assist organisations deploying the ATN IPS in a heterogeneous environment:

- Tunnelling: one protocol being encapsulated in another

- Dual stack: an environment in which multiple protocols operate simultaneously

- Translation: the conversion from one protocol to another

An in-depth description of the first two mechanisms can be found in RFC4213 (Basic Transition Mechanisms for IPv6 Hosts and Routers). The applicability of above three mechanisms to the ATN IPS are further described.

### 2.3.1 Tunnelling

IPv6 has been specified to operate over a variety of lower layer interfaces such as Frame Relay, ATM, HDLC, PPP and LAN technologies. Tunneling implies that a given protocol is encapsulated into another, meaning that IPv6 would be encapsulated into another functionally equivalent network protocol. With regard to the ATN IPS, the key benefit of this mechanism would be for aeronautical organizations that already operate IPv4 networks to allow the ATN IPS hosts and routers communicate between each other over such an underlying IPv4 network. Furthermore, if the interconnecting infrastructure between two ATN IPS administrative domains is limited to IPv4, this mechanism can be applied.

It is recalled that IPv6 cannot operate over X.25; an IPv6 tunnel over IPv4 can be in turn tunneled over an X.25 network. A specific tunneling mechanism termed IP SNDCF is defined for ATN/OSI applications, it is to be noted that this enables interoperability between ATN/OSI applications over an IP network but does not enable interoperability with ATN/IPS applications.

Tunnelling mechanisms lead to an increase of protocol overhead and the segregation of the two routed domains creates additional network management e.g. an IPv6 routed domain over an underlying IPv4 routed domain that needs to be managed in terms of QoS, security, and route optimization. In addition, this mechanism only foresees interoperability between ATN IPS systems as it does not enable interoperability between ATN OSI systems nor other IPv4 systems within the organization. Nevertheless, it may provide an effective way to enable the ATN IPS within and between two administrative domains.

The tunneling mechanism is best suited to resolve lower layer communication issues between ATN IPS IPv6 hosts and routers but does not provide interoperability with non-compliant ATN IPS systems.

### 2.3.2 Dual Stack

The dual stack mechanism implies that an implementation handles more than one communications protocol for a given application or function. Within the internet domain a significant number of communication applications have been dual stacked e.g. HTTP, FTP, SSH, DNS, SMTP etc. by supporting both IPv4 and IPv6 protocols. However, in the context of the ATN IPS the purpose of dual stacking is to resolve similar yet different issues.

The concept of dual stacking is ideally suited for systems that need to support ATN applications for both OSI and IPS. In such environments, the applications are designed in an abstract fashion to be independent of the lower layers, in other words they are unaware which lower layer communications protocol (OSI or IP) is being used to communicate with their peer. X.400 vendors have taken this approach to support both OSI and IP environments avoiding the need to develop complex ad-hoc lower layer communication gateways. Usually such implementations rely on some form of directory or lookup table associating a high-level address with a specific communications protocol address.

The concept of dual stack can be extended to multiple stack. ATN AMHS manufacturers usually support operation over multiple protocols such as OSI, TCP/IP and X.25 .

The dual stack mechanism is best suited to provide the maximum level of interoperability with peers while reducing the complexity of lower layer communication protocol gateways and additional single points of failure. It is ideally suited for applications such as AMHS whereby some systems have already been implemented on the basis of OSI and others on TCP/IP. A dual stack approach can be a valid for air-ground datalink ground systems to support CPDLC over multiple datalink services such as ATN OSI and ATN IPS.

### 2.3.3 Translation

Translation mechanisms imply the conversion from one protocol to another. This mechanism can be interpreted as a lower layer communications gateway between two protocols that share a high degree of commonality. Several translators have been developed in the context of the transition from IPv4 to IPv6 as both versions share a number of common features.

Within the overall transition from IPv4 to IPv6, it was envisaged that some systems may be only capable of communicating with IPv4 and others with IPv6. Considering global internet scalability issues and the fact that most internet applications and systems have become dual stacked, the need for translators has declined.

However, translators may play an important short-term role in the case of the ATN IPS. For example, although existing AMHS systems operate on dual stack operating systems, none of them have upgraded their application code to make use of IPv6. In other words, RFC1006 is supported but not RFC2126. In such particular cases and in view of the limited number of systems, the deployment of translators provides a short-term measure for such systems to comply with the ATN IPS and inter-work with RFC2126 enabled systems.

IPv4/IPv6 translators increase the complexity of the IP infrastructure and its management. A dual stack approach is to be preferred but in specific cases translators may be the only short-term measure to provide compliance with the ATN IPS.

### 2.3.4 Combining of the Mechanisms

As the ATN IPS implementation will be gradual it is understandable that a combination of the above three mechanisms will be applied.

Specific combinations of the above mechanisms can be deployed to better fit within the environment of the administrative domain environment.

# 3.0 PROTOCOL Stack

## 3.1 Physical and Link Layer Guidance

Physical and link layer issues will be determined by the required service and member state connections.  The physical and link layer issues will be on service need basis and should be contained in a memorandum of agreement (MOA).

## 3.2 Network Layer

The IPS ATN addressing is performed using IPv6, which uses 128 bits long address block versus 32 bits in IPv4.

### 3.2.1 Address Plan

TBD.

### 3.2.2 Application interface to the network layer

Although applications generally interface to the communication service at the transport layer, it is sometime necessary to transmit and receive datagrams at the network level. This is granted by some socket API extensions specified in:

RFC 3542 - Advanced Sockets Application Program Interface (API) for IPv6

### 3.2.3 Inter-domain routing

This section discusses inter-domain routing that will enable member state networks to interconnect while maintaining state or federation autonomy.  The protocol to be used shall be the border gateway protocol (BGP).

#### 3.2.3.1 AS numbering plan

AS numbers need to be assigned and configured in ATN/IPS routers to announce their autonomous systems within the routed domain. The AS numbering plan is presented in Appendix C.

#### 3.2.3.2 ATN/IPS Router Ids

In order to establish BGP between two neighbours, each BGP peer must define a router id. If two routers make use of the same router-id value, BGP cannot be established. As the router id is a 32 bit field, it is usually on the IPv4 address of the router.

As ATN IPS routers may not have Ipv4 interfaces a scheme needs to be recommended. Although global uniqueness of these values is not a pre-requisite, to ease implementation of the ATN IPS the following scheme is recommended (based on draft-dupont-durand-idr-ipv6-bgp-routerid-01.txt):

4 bits set to one,

16 bits set to the AS number (a global AS number plan is part of this Document)

12 bits manually allocated within the domain. (allows for 4096 different router IDs in each routing domain)

##### 3.2.3.2.1 Routing Advertisement

ATN IPS routers should advertise network prefixes based on consistent prefix lengths or aggregate route prefixes;

##### 3.2.3.2.2 Traffic type segregation

BGP-4 does not natively allow setting up different set of routes for different traffic to the same destination.  ATN IPS requirement on traffic type segregation may be fulfilled by appropriate provisions in the ATN addressing plan: if the ATN address incorporates an indication of the traffic type, BGP-4 will transparently flood segregated route information for the various traffics.

##### 3.2.3.2.3 Differentiated Service

Differentiated Service (RFC 2474) provides a mean for specifying and implementing QOS handling consistently in IPS network. This specification is made on a per node basis, specifying behaviour of individual nodes concerning QOS (Per Hop behaviour).

The general framework / current practices is depicted in details in:

RFC 2475 - Architecture for Differentiated Services

##### 3.2.3.2.4 Traffic Priority

Historically, network layer priority was selected explicitly by the sending application through the TOS field. Although Differentiated Service (RFC 2474) preserves the IP precedence semantic of the TOS field, this approach is now deprecated. This is partly because the IP precedence has been superseded by the Per-Hop-Behaviour strategy inside Differentiated service, but also because network administrators usually don’t trust QOS specification coming from the application.

ATN application traffics can be identified / prioritised according to the destination port of data grams when they enter the network:

- This provides transparent and safe identification of traffics, because the destination port is always a trusted information (otherwise the traffic will never reach its destination).

- But this requires specification of a distinct port for every ATN application (proliferation of ports would unnecessarily complexity administration of routers, and incurs their performance).

- During transit in the IPS network, corresponding data grams could be marked using the Differentiated Service field, in respect to the practices indicated in RFC 2475.

### 3.2.4 Multicast

The need to send the same information to multiple receivers is one of the main requirements of surveillance data distribution. This requirement can be supported by the Internet Protocol versions 4 and 6 (IPv4 and Ipv6 respectively) multicast services. Other networking techniques that achieve the same multicast objective are not further considered within the scope of this document.

A limited number of European States have deployed national Ipv4 multicast services for surveillance data distribution. However, the limited range of the Ipv4 multicast address space inhibits the deployment of scalable service within

In recent years, significant technical progress has been made in the field of IP multicast, namely source specific multicast (SSM). Contrary to existing deployments on the basis of PIM-SM (Protocol Independent Multicast—Sparse Mode), SSM provides added simplicity and resiliency to the routing of IP multicast traffic and is ideally suited for surveillance needs.

At present, there are no gateways to allow interworking between Ipv4 and Ipv6 multicast implementations.

#### 3.2.4.1 Planned European Deployments

As early as 2001, Eurocontrol and its Member States identified the need to introduce IPv6 for inter-ANSP data exchanges (which are typically cross-border) for both unicast and multicast network services.

Indeed, surveillance data flows that cross national borders are required to use the IPv6 protocol due to the architecture of the trans-national backbone network. Surveillance data flows that remain inside national borders use either IPv4 or IPv6 depending on the architecture of the national network infrastructure.

As source specific multicast (SSM) is particularly suited to inter-ANSP data exchanges, it use over IPv6 is recommended in a Eurocontrol guideline entitled “EUROCONTROL GUIDELINES FOR IMPLEMENTATION SUPPORT (EGIS) Part 5: COMMUNICATION & NAVIGATION SPECIFICATIONS, Chapter 12, SURVEILLANCE DISTRIBUTION OVER IP MULTICAST PROFILE REQUIREMENT LIST (PRL)”. Eurocontrol will indicate the URL of the above document once it is on-line.

Furthermore it is recommended that all surveillance data transmitters or receivers that are intended to send or receive data beyond the local domain, ie across national borders, should be IPv6-compliant as depicted in Figure 4-1.

The surveillance data is delivered using the source specific multicast (SSM) service. A data channel is defined by the combination of destination multicast address and source unicast address, and contains a single surveillance data flow.

Figure 4.1 SSM Multicast IPv6 address with global scopeIPv6

|   8    |  4 |  4 |   8    |    8   |       64       |    32    |

+--------+----+----+--------+--------+----------------+----------+

|11111111|0011|1110|00000000|00000000| 000……………………000 | group ID |

+--------+----+----+--------+--------+----------------+----------+

- The IPv6 multicast group ID shall be in the range 0x8000000 to 0xFFFFFFFF allowed for dynamic assignment by a host, as specified in  RFC 3307 section 4.3 and RFC 4607 section 1.

- The resulting available IPv6 SSM address range is FF3E::8000:0/97 (FF3E:0:0:0:0:0:8000:0 / 97).

- Assuming the appropriate access to the service, to receive a SSM (source specific multicast) stream one requires the following three parameters:

1. Source-address (unicast address)

2. Multicast address (as indicated by the source application)

3. Port (default is 8600 for ASTERIX surveillance data in Europe)

## 3.3 Transport Layer

The transport layer protocols are used to provide reliable or unreliable communication services over the ATN. There are two mandatory transport protocols, TCP and UDP.  TCP is used to provide reliable transport services and UDP is used to provide best effort service.  Other transport protocols may be used but can not affect ATN communications or services.

### 3.3.1 Transmission Control Protocol

The Internet Protocol (IP) works by exchanging groups of information called packets. Packets are short sequences of bytes consisting of a header and a body. The header describes the packet's routing information, which routers on the Internet use to pass the packet along in the right direction until it arrives at its final destination. The body contains the application information. TCP is optimized for accurate delivery rather than timely delivery, TCP sometimes incurs long delays while waiting for out-of-order messages or retransmissions of lost messages, and it is not particularly suitable for real-time applications like Voice over IP. Real time applications will require protocols like the Real-time Transport Protocol (RTP) running over the User Datagram Protocol (UDP).

TCP is a reliable stream delivery service that guarantees to deliver a stream of data sent from one host to another without duplication or losing data. Since packet transfer is not reliable, a technique known as positive acknowledgment with retransmission, is used to guarantee reliability of packet transfers. This fundamental technique requires the receiver to respond with an acknowledgment message as it receives the data. The sender keeps a record of each packet it sends, and waits for acknowledgment before sending the next packet. The sender also keeps a timer from when the packet was sent, and retransmits a packet if the timer expires. The timer is needed in case a packet becomes lost or corrupt.

In the event of congestion, the IP can discard packets, and, for efficiency reasons, two consecutive packets on the internet can take different routes to the destination. Then, the packets can arrive at the destination in the wrong order.

The TCP software libraries use the IP and provides a simpler interface to applications by hiding most of the underlying packet structures, rearranging out-of-order packets, minimizing network congestion, and re-transmitting discarded packets. Thus, TCP very significantly simplifies the task of writing network applications.

TCP provides a connection-oriented service with a reliable semantic. It operates above the network layer which does not necessarily detect and report all errors (e.g. corruption, misrouting). For this purpose, it provides:

- Error detection based on a checksum covering the transport header and payload as well as some vital network layer information.

- Recovery from error based on retransmission of erroneous or lost packets.

TCP is also designed for to detect and manage end-to-end network congestion and maximum user data segment sizes. This is essential for operation over heterogeneous sub networks with some low bandwidth / high latency trunks, such as the actual ATN Air/Ground sub networks.

### 3.3.2   User Datagram Protocol (UDP)

UDP provides a connectionless service with limited error detection and no recovery, nor congestion management mechanisms. It is naturally dedicated for light data exchanges, where undetected occasional loss or corruption of packets is acceptable, and when simplicity of use is a goal.

### 3.3.3 Transport Layer Addressing

Transport layer addressing relies on port numbers (16 bits integer values) that are associated with source and destinations endpoints to identify separate data streams.

Ports are classified in three categories with associated range of values:

- Well-known ports are those from 0 through 1023 and are assigned by IANA. On most systems these ports can only be used by system (or root) processes or by programs executed by privileged users. Such pre-defined well-known port numbers associated to distinct TCP and/or UDP applications, makes them visible (“well-known”) to client applications without specific knowledge / configuration.

- Registered ports are those from 1024 through 49151 and are registered by IANA following user request. Essentially such ports play the same role as well-known ports but for less critical or widespread applications. The use of such ports does not require specific privileges.

- Dynamic and/or private ports are those from 49152 through 65535. They may be used freely by applications.

Port assignment is obtained on request to IANA. An up-to-date image of the port registry is available at:

http://www.iana.org/assignments/port-numbers

This assignment plan is compulsory over the public Internet. It should be made applicable to ATN IPS (at least concerning well-known ports) in order to avoid conflicts between standard IPS applications (that may be used in ATN IPS environment) and ATN applications.

ATN/IPS hosts will require to support the following port numbers:

- tcp 102 for ATSMHS

- tcp 8500 for FMTP

### 3.3.4 Application Interface to the Transport Layer

The application interface to the TCP and UDP transport layers is provided consistently on a wide range of platform/operating systems according to the specification made in:

RFC 3493 - Basic Socket Interface Extensions for IPv6

This RFC extends the socket interface (originally developed by the Berkeley University for supporting IPv4 in their BSD Unix distribution) to IPv6.

### 3.3.5 Congestion Avoidance

In order to adapt to variables conditions for draining traffic in sub networks, TCP implements basically 4 mechanisms: slow-start, congestion-avoidance, fast-retransmit and fast-recovery. These are specified in:

RFC 2581 - TCP Congestion Control

The two first mechanisms aim at preventing important loss of packets when congestion occurs, while the two others attempt to shorten the delay for retransmitting the lost packets. These mechanisms are implemented independently in every end system, they don’t completely avoid loss of packets.

In the case of low bandwidth sub networks (e.g. ATN Air/Ground sub networks), TCP applications may make use of the Explicit Congestion Notification mechanism will more likely provide a significant benefit. It is specified by:

RFC 3168 - The Addition of Explicit Congestion Notification (ECN) to IP

This feature anticipates congestion, significantly reducing packet loss. However, it impacts the transport and network layers, and requires participation of a significant number of routers in the networks (preferentially, the routers at the edge of low speeds / high latency sub networks).

### 3.3.6 Error Detection and Recovery

TCP error detection relies on lack of timely received acknowledgement. Recovery is performed through retransmission of (supposed) lost packets.

Loss of a large numbers of packets in a short period of time may heavily incur the TCP connection throughput (hence performance). This may become critical for high latency sub networks (e.g. ATN Air/Ground sub networks).

Supports of TCP selective acknowledge option may mitigate this problem by allowing selective retransmission of lost packets only (instead of the whole sequence from the first to the last packet lost).  This option is specified in:

RFC 2018 - TCP Selective Acknowledgment Options

### 3.3.7 Performance Enhancing Proxies (PEPs)

Performance Enhancing Proxies (PEPs) are often employed to improve severely degraded TCP performance caused by different link characteristics in heterogeneous environments, e.g. in wireless or satellite environments that are common in aeronautical communications. Transport layer or application layer PEPs are applied to adapt the TCP parameters to the different link characteristics.

RFC3135 “Performance Enhancing Proxies Intended to Mitigate Link-Related Degradations” is a survey of PEP performance enhancement techniques, and describes some of the implications of using Performance Enhancing Proxies. Most implications of using PEPs result from the fact that the end-to-end semantics of connections are usually broken. In particular, PEPs disable the use of end-to-end IPsec encryption and have implications on mobility and handoff procedures.

# 4.0 MOBILITY GUIDANCE

## 4.1 MOBILE IPv6

This manual specifies that the IP mobility solution for the ATN/IPS is Mobile IPv6 (MIPv6) as specified in RFC 3775.  With Mobile IP a mobile node (MN) has two addresses: a home address (HoA), which is a permanent address, and a dynamic care-of address (CoA), which changes as the mobile node changes its point of attachment.  See figure 4.1-1 The fundamental technique of Mobile IP is forwarding. A correspondent node (CN), which is any peer node with which a mobile node is communicating, sends packets to the home agent (HA) of the mobile node.  The CN reaches the HA through normal IP routing.  Upon receipt of a packet from the CN,  the HA will forward these packets to the MN at its current CoA.  The HA simply tunnels the original packet in another packet with its own source address and a destination address of the current CoA. This is possible because of the Mobile IP protocol whereby the MN sends “binding update” messages to the HA whenever its point of attachment changes.  The binding update associates the mobile nodes HoA with its current CoA.  The HA maintains a Binding Cash that stores the current CoA of the MN.

Figure 4.1-1:  Mobile IP

### 4.1.1 MIPv6 Bidirectional Tunneling

In the reverse direction, the MN could simply send packets directly to the CN using normal IP routing.  However, this results in triangular routing and depending on the relative location of the HA, there can be a situation where the path in one direction (e.g. CN to HA to MN) is significantly longer than the path in the reverse direction (e.g., MN to CN).  A further consideration in this case occurs if theMN uses its home address as a source address.  The problem here is that many networks perform ingress filtering of incoming packets and will not accept packets that are topologically incorrect. This would be the case with packets from the MN because they actually originate from the care-of-address but the source address in the IP packet is the home address.  Because of these issues, MIPv6 allows the MN to follow the same path back to the CN via the HA using bidirectional tunneling whereby in addition to the HA tunneling packets to the MN, the MN reverse tunnels packets to the HA.  The HA will decapsulate a tunneled IP packet and forward it to the CN.  With bidirectional tunneling the CN is not required to support Mobile IP.

### 4.1.2 MIPv6 Route Optimization

Bidirectional tunneling solves the problems of triangular routing and ingress filtering; however, there still can be suboptimal routing since the path from the MN to the CN via the HA may be relatively long even when the MN and CN are in close proximity.  With MIPv6 the situation where the path through the HA is longer than a direct path to the CN may be addressed using a technique called route optimization.  With route optimization the MN sends binding updates to both the HA and the CN.  In this case the MN and CN can communicate directly and adapt to changes in the MN’s CoA. RFC 3775 defines the procedures for route optimization.  It requires that the MN initiate the return routability procedure.  This procedure provides the CN with some reasonable assurance that the MN is addressable at its claimed care-of address and its home address.

It is generally acknowledged that there are drawbacks to route optimization. RFC 4651 presents a taxonomy and analysis of enhancements to MIPv6 route optimization.  This document notes that the two reachability tests of the return routability procedure can lead to a handoff delay unacceptable for many real-time or interactive applications, that the security that the return-routability procedure guarantees might not be sufficient for security-sensitive applications, and periodically refreshing a registration at a correspondent node implies a hidden signaling overhead.  Because of the overhead and delay associated with the return routability procedure and because at least for ATSC it is expected that the CN and HN will be in relative close proximity, this manual requires that IPS CNs that implement Mobile IPv6 route optimization allow route optimization to be administratively enabled or disabled with the default being disabled. New solutions to route optimization are expected as a result of IETF chartered work in the Mobility Extensions for IPv6 (MEXT) working group which includes avaiation-specific requirements.

## 4.2 Enhancements to MIPv6

When a mobile node (MN) changes its point of attachment to the network, the changes may cause delay, packet loss, and generally result in overhead traffic on the network.

### 4.2.1 Heirarchical Mobile IPv6 (HMIPv6)

One technology developed to address these issues is “Heirarchical Mobile IPv6 (HMIPv6)” [RFC 4140].  RFC 4140 introduces extensions to Mobile IPv6 and IPv6 Neighbor Discovery to allow for local mobility handling.  HMIPv6 reduces the amount of signaling between a MN, its CNs, and its HA.  HMIPv6 introduces the concept of the Mobility Anchor Point (MAP).  A MAP is essentially a local home agent for a mobile node.  A mobile node entering a MAP domain (i.e., a visited access network) will receive Router Advertisements containing information about one or more local MAPs. The MN can bind its current location, i.e., its On-link Care-of Address (LCoA), with an address on the MAP's subnet, called a Regional Care-of Address (RCoA).  Acting as a local HA, the MAP will receive all packets on behalf of the mobile node it is serving and will encapsulate and forward them directly to the mobile node's current address.  If the mobile node changes its current address within a local MAP domain (LCoA), it only needs to register the new address with the MAP.  The RCoA does not change as long as the MN moves within a MAP domain.  RFC 4140 notes that the use of the MAP does not assume that a permanent HA is present, that is, a MN need not have a permanent HoA or HA in order to be HMIPv6-aware or use the features of HMIPv6.  HMIPv6-aware mobile nodes can use their RCoA as the source address without using a Home Address option.  In this way, the RCoA can be used as an identifier address for upper layers.  Using this feature, the mobile node will be seen by the correspondent node as a fixed node while moving within a MAP domain. This usage of the RCoA does not have the cost of Mobile IPv6 (i.e., no bindings or home address options are sent back to the HA), but still provides local mobility management to the mobile nodes with near-optimal routing. Although such use of RCoA does not provide global mobility.

### 4.2.2 Fast Handovers for Mobile IPv6 (FMIPv6)

A further enhancement to MIPv6 is “Fast Handovers for Mobile IPv6 (FMIPv6)” [RFC 4068].  FMIPv6 attempts to reduce the chance of packet loss through low latency handoffs. FMIPv6 attempts to optimize handovers by obtaining information for a new access router before disconnecting from the previous access router.  Access routers request information from other access routers to acquire neighborhood information that will facilitate handover.  Once the new access router is selected a tunnel is established between the old and new router.  The previous Care-of Address (pCoA) is bound to a new Care-of Address (nCoA) so that data may be tunneled from the previous Access Router to the new Access Router during handover.  Combining HMIPv6 and FMIPv6 would contribute to improved MIPv6 performance but this comes at the cost of increased complexity.

### 4.2.3 Proxy Mobile IPv6 (PMIPv6)

In MIPv6 as described above the MN updates the HA with binding updates messages.  This mode of operation is called node-based mobility management.  A complimentary approach is for access network service providers to provide network-based mobility management using  Proxy Mobile IPv6 (PMIPv6).    .  This approach to supporting mobility does not require the mobile node to be involved in the exchange of signaling messages between itself and the home agent to potentially optimize the access network service provision.  A proxy mobility agent in the network performs the signaling with the home agent and does the mobility management on behalf of the mobile node attached to the network.  The core functional entities for PMIPv6 are the Local Mobility Anchor (LMA) and the Mobile Access Gateway (MAG).  The local mobility anchor is responsible for maintaining the mobile node's reachability state and is the topological anchor point for the mobile node's home network prefix(es).  The mobile access gateway is the entity that performs the mobility management on behalf of a mobile node and it resides on the access link where the mobile node is anchored.  The mobile access gateway is responsible for detecting the mobile node's movements to and from the access link and for initiating binding registrations to the mobile node's local mobility anchor.  An access network which supports network-based mobility would be agnostic to the capability in the IPv6 stack of the nodes which it serves.  IP mobility for nodes which have mobile IP client functionality in the IPv6 stack as well as those nodes which do not, would be supported by enabling Proxy Mobile IPv6 protocol functionality in the network.  The advantages of PMIPv6 are reuse of home agent functionality and the messages/format used in  mobility signaling and common home agent would serve as the mobility agent for all types of IPv6 nodes.  PMIPv6 like HMIPv6 is a local mobility management approach which further reduces the air-ground signalling overhead.

### 4.2.4 Network Mobility (NEMO)

Mobile IPv6 supports movement of an individual network node.  However, there are scenarios in which it would be necessary to support movement of an entire network in the ATN/IPS.  One case is for APC where is would be wasteful of bandwidth to have mobility signalling for every individual passenger.  Another case may when there is a common airborne router supporting multiple traffic types provided proper security issues can be addressed.  The extension to Mobile IPv6 which supports these scenarios is called Network Mobility (NEMO).  This manual lists NEMO in accordance with RFC 3963 as an option for implementation.  The NEMO operational model introduces a new entity called a Mobile Network Node (MNN) which is any node in the network that moves as a unit.  It can be a host moving with other MNNs or a Mobile Router.  The Mobile Router operates like any Mobile IP host on the egress interface (to a fixed access router).  The Mobile Router also negotiates a prefix list with the home agent.  The home agent uses this list to forward packets arriving for the MNNs that share the common prefix to the Mobile Router.  On the ingress interface (to the mobile network) the Mobile Router adversises will advertise one or more prefixes to the MNNs.  Although on the surface NEMO appears to be a straight-forward extension to Mobile IP there are are several considerations that are still being investigated in IETF working groups.  These issues include how to do NEMO route optimization and several considerations with prefix delegation and management.

# 5.0 SECURITY GUIDANCE

This section of the Manual for the ATN using IPS Standards and Protocols contains a description of the rational for the requirements in section 2.5 of Part I of the manual with background information when additional clarification is warranted and general guidance for implementation of security.

## 5.1 Requirments for Implementation

This ATN/IPS Manual contains certain security provisions that are required to implement.  The requirement to implement security is intended to be consistent with the Security Architecture for IPv6, which requires that all IPv6 implementations comply with the requirements of RFC 4301.  Although all ATN/IPS nodes are required to implement Internet Protocol security (IPsec) and the Internet Key Exchange (IKEv2) protocol, the actual use of these provisions is to be based on a system threat and vulnerability analysis.

## 5.2 Ground-Ground Security

### 5.2.1 Ground-Ground IPsec

The baseline for ground-ground security is to require network layer security in the ATN/IPS internetwork implemented using IPsec.  IPsec creates a boundary between unprotected and protected interfaces.  IPsec is typically used to form a Virtual Private Network (VPN) among gateways (NIST 800-77).  A gateway may be a router or another security device such as a firewall.  In this context other security devices are considered to be ATN/IPS nodes.  The gateway-to-gateway model protects communications among ATN/IPS networks between regions or between states or organizations in a particular region.  IPsec may also be used in a host-to-gateway environment, typically to allow hosts on an unsecure network to gain access to protected resources.  IPsec may also be used in a host-to-host environment where end-to-end protection of applications is provided.

To achieve interoperability across the ATN/IPS internetwork, this manual specifies support for the IPsec security architecture, the Encapsulating Security Payload (ESP)  protocol and a common set of cryptographic algorithms.  The architecture is as specified in RFC 4301.  ESP is as specified in RFC 4303 and the cryptographic algorithms which may be used are specified in RFC 4835.  This ATN/IPS manual further specifies that ESP encryption is optional but authentication is always performed.

This manual specifies that ATN/IPS nodes in the ground-ground environment may implement the IP Authentication Header (AH) protocol as specified in RFC-4302.  This is in recognition that while AH may exist in certain products, it’s use in IPsec has been downgraded.  RFC 4301 states, “Support for AH has been downgraded to MAY because experience has shown that there are very few contexts in which ESP cannot provide the requisite security services.  Note that ESP can be used to provide only integrity, without confidentiality, making it comparable to AH in most contexts”.

### 5.2.2 Ground-Ground IKEv2

The IPsec architecture [RFC 4301] specifies support for both manual and automated key management. As the ATN/IPS evolves use of manual key management will not scale well.  Therefore this manual specifies that nodes in the ground-ground environment shall implement the Internet Key Exchange (IKEv2) Protocol as specified in RFC-4306 for automated key management.  IKEv2 is the latest version of this protocol.  The IKEv2 specification is less complicated than the first version of the protocol which should contribute to better interoperability among different implementations.

As is the case for ESP, the IKEv2 protocol requires a set of mandatory-to-implement algorithms for interoperability.  This manual requires that nodes in the ground-ground environment implement the Cryptographic Algorithms specified in RFC-4307.

### 5.2.3 Alternatives to IPsec/IKEv2 for Ground-Ground Security

Alternatives to network security may be appropriate in certain operating environments.  Alternatives to IPsec may be applied at the Data Link, Transport, or Applicaiton Layer.   NIST SP 800-77 describes the main alternatives, characterizes the alternatives in terms or strangths and weaknesses, and identifies potential cases where they may be used as alternatives to IPsec.

## 5.3 Air-Ground Security

### 5.3.1 Air-Ground IPsec

Similar to the ground-ground environment, to achieve interoperability in the air-ground environment this manual specifies that ATN/IPS nodes support the IPsec security architecture and the Encapsulating Security Payload (ESP)  protocol.    As in the ground case, the architecture is as specified in RFC 4301 and ESP is as specified in RFC 4305.  However rather than implement all of the the cryptographic algorithms which are identified in RFC 4305,  specific default algorithms are identified for  authentication  and for encryption and authentication together..  This is in consideration of bandwidth-limited air-ground links and so as not to have unused code in the avionics platform.

The authentication algorithm selected for use when confidentiality is not also selected is AUTH_HMAC_SHA2_256-128 as specified in RFC 4868.  This algorithm uses a 256-bit key to compute a HMAC tag using the SHA-256 hash function.  The tag is truncated to 128 bits.   The same algorithm is used for integrity in IKEv2 as described below.

If ESP encryption is used, this manual specifies that the Advanced Encryption Standard (AES) be used in Galois/Counter Mode (GCM).  AES-GCM is used with an 8 octet Integrity Check Value (ICV) and with a key length attribute of 128 as specified in RFC 4106.  AES-GCM is a “combined mode” algorithm which offers both confidentiality and authentication in a single operation.  Combined mode algorithms offer efficiency gains when compared with sequentially applying encryption and then authentication.  When AES-GCM is used the ICV consists solely of the AES-GCM Authentication Tag and a separate HMAC tag is not applied.

### 5.3.2 Air-Ground IKEv2

Because manual key management is not practical in the air-ground environment, this manual requires that ATN/IPS nodes implement the Internet Key Exchange (IKEv2) Protocol as specified in RFC 4306. As is the case of ESP in consideration of bandwidth limitations and so that there will not be unused code in the avioncs platform, this manual specifies a set of default algorithms for use in IKEv2.  The selection of transforms is intended to be compatible with the selections of the ATA DSWG and AEEC DSEC working groups to the extent possible; however, this manual only uses transforms that have been registered with IANA.  Five transforms are used by IKEv2.

- There is a pseudo-random function (PRF) which is used in IKEv2 for generation of keying material and for authentication of the IKE security association.  This manual requires the use of PRF_HMAC_SHA_256 as specified in RFC 4868 as the PRF.

- IKEv2 uses the Diffie-Hellman key exchange protocol to derive a shared secret value used by the communicating peers.  The Diffie-Hellman calculation involves computing a discrete logarithm using either finite field or elliptic curve arithmentic. When elliptic curve cryptography is used, the conventional choices are to use either prime characteristic or binary curves.   This manual selectes a prime characteristic curve and requires the use of the 233-bit random ECP group as specified in RFC 4753.

- When public key certificates are used in IKEv2 for entity authentication certain data must be signed in the IKEv2 exchange.  This manual requires that signing be performed using the Elliptic Curve Digital Signature Algorithim (ECDSA) using SHA-256 as the hash algorithm on the 256-bit prime characteristic curve as specified in RFC 4754.

- The authentication exchange of IKEv2 has a payload that is encrypted and integrity protected.  This manual specifies that AES CBC with 128-bit keys as specified in RFC 3602 be used as the IKEv2 encryption transform.

- This manual specifies that the encrypted payload be integrity protected using HMAC-SHA-256-128 as specified in RFC 4868.

The above suite of algorithms together with the use of AES-GCM for ESP encryption is the “Suite-B-GCM-128” set specified in RFC 4869.  This suite is expected to be available as a Commerical-Off-The-Shelf implementation and should provide adequate cryptographic strength beyond 2030.  See NIST SP 800-57 for additional guidance on cryptographic algorithm and key size selection.

The use of IKEv2, while offering the advantage of COTS availabilty and flexibility in signalling algorithms, authentication mechanisms, and other parameters,  will result in more overhead than might otherwise be incurred in a custom aviation-specific solution.  IKEv2 requires at least 4 messages to be exchanged to establish a session key for air-ground communications.  In addition, the encryption algorithms in IKEv2 and ESP result in message expansion.   While this expansion may be negligible for large messages, it will represent a more significant percentage for small messages.  While this is a significant consideration for bandwidth-constrained datalinks, it is expected to be less of an issue when there is a high-speed datalink approved for safety services.

### 5.3.3 Securing Air-Ground End-to-End Communications

Figure 5.3.3-1 depicts the options for securing end-to-end communications in the ATN/IPS air-ground environment.  IKEv2 and ESP of IPsec are required to be implemented.  This manual also defines options for TLS and for IKEv2 with Application-level security.  In all cases this manual defines a default set of cryptographic algorithms.

Figure 5.3.3-1 – Options for Air-Ground End-to-End Security

#### 5.3.3.1 Air-Ground End-to-End Network Layer Security

As desribed in sections 5.3.1 and 5.3.2, for air-ground end-to-end network layer security this manual requires that ESP be implemented along with IKEv2 for key establishment.  Figure 5.3.3-1 depicts the CN interfacing to a PKI Certificate Server.  The interface method is considered a local matter.  This may be an LDAP interface to a database of X.509 Certificates and Certificate Revocation Lists (CRLs) or another certificate management protocol.  As noted above a “Suite-B” set of algorithms as specified in RFC 4869 is being used for ESP and IKEv2.  The US National Security Agency Suite B Certificate and CRL Profile identifies the Certificate Management Messages over CMS protocol as specified in RFC 2797 as the preferred protocol.  The acutal authentication method used in an Administrative Domain is a local matter and will depend on the application.  IKEv2 permits pre-shared keys or Digital Certificates to be used with Digital Certificates considered to be a stronger method.  It would be possible to use pre-shared keys in the downlink direction and to use Digital Certificates in the uplink direction.  Since there is no practical way for the MN to independently check a CRL, short-lived certificates could be used in the uplink direction.  In the downlink direction if Digital Certificates are used it is recommended that rather than the MN sending an actual cettificate, the MN should use the IKEv2 “Hash and URL” method.  With method the MN sends the URL of a PKI certificate server where the CN can retrieve its certificate.  Section  5.3.5 contains more guidance on PKI profiles and certificate policy.  This section has described using certificates for authentication when strong authentication is required.  This is the preferred approach in the end-to-end environment even though it would be possible to use IKEv2 and the Extensible Authentication Protocol (ESP) with an authentication, authorization, and accounting (AAA) infrastructure as will be described for access networks and mobility service providers.  It is expected that PKI bridge concept being developed by the  that the Air Transport Association (ATA) Digital Security Working Group (DSWG) will facilitate operating a PKI on a global basis.  Under the PKI bridge each Administrative Domain may certify to a central bridge rather than each Administrative Domain cross-certifying with every othr Administrative Domain.

#### 5.3.3.2 Air-Ground End-to-End Transport Layer Security

This manual permits ATN/IPS mobile nodes and correspondent nodes to implement the Transport Layer Security (TLS) protocol as specified in RFC 4346.  This will permit applications that already use TLS to operate in the ATN/IPS air-ground environment. If TLS is used, then the following cipher suite as defined in RFC 4492 is required:

TLS_ECDH_ECDSA_WITH_AES_128_CBC_SHA

This cipher suite is for:

- The Transport Layer Security (TLS) protocol.  Version 1.0 or 1.1 may be be used

- Elliptic Curve Diffie Hellman (ECDH) key agreement

- Elliptic Curve Digital Signature Algorithm (ECDSA) for client authentication

- The Advanced Encyption Standard (AES) with 128 block size in Cipher Block Chaining (CBC) mode for confidentiality

- The Secure Hash Algorithm (SHA) version 1 for integrity (i.e., for HMAC)

This cipher suite is selected because it has aglorithms in common with those identified for air-ground IPsec and and IKEv2.  Note that this cipher suite a required implementation for servers and one of the suites that clients may implement to be compliant with RFC 4492.

#### 5.3.3.3 Air-Ground End-to-End Application Layer Security

This manual permits ATN/IPS mobile nodes and correspondent nodes to implement application layer security at the IPS Dialogue Service Boundary. This alternative is intended to be for legacy ATN applications which may already implement application layer security in the ATN/OSI environment.  In this case mobile nodes and corresondent nodes shall append an HMAC-SHA-256 keyed message authentication code to application messages.  HMAC-SHA-256 is already required for ESP and IKEv2 so there is essentially no additional cryptography for this option.  The HMAC tag truncated to 32 bits is computed over the User Data concatenated with a send sequence number for replay protection.  Since IKEv2 is required in any case, if application layer security is used for air-ground security, IKEv2 is again used for key establishment.

### 5.3.4 Securing Access Network and Mobile IP Signaling

Figure 5.3.4-1 depicts options for securing Access Service Provider (ASP) or Mobility Service Provider (MSP) signalling.  The distinction between an ASP and MSP has become useful in IETF working groups examining the use of AAA back end infrastructures for mobility security.  According to RFC 4640 an ASP is a network operator that provides direct IP packet forwarding to and from the end host.  An MSP is a service provider that provides Mobile IPv6 service.  In the figure the AAA-NA service is used for network access and the AAA-MIP server is used for access to Mobile IP service.

Figure 5.3.4-1 – ASP or MSP Security

#### 5.3.4.1 Securing Mobile IP Signaling

Consistent with RFC 3775 this manual requires that IPsec be used specifically for protection of Mobile IP signaling in conformance to RFC 4877.  RFC 4877 is an update to RFC 3776 and describes how IKEv2 is to be used for automated key management.  RFC 4877 in particular describes how IKEv2 with EAP as the authentication method may be used.  When extensible authentication is used in IKEv2 there is an additional exchange after the IKE_SA_INIT and IKE_SA_AUTH exchanges.  In this case the MN will not include an authentication payload in the IKE_SA_AUTH exchange but rather will include an EAP payload in the next message.  The HA then interacts with the AAA-MIP server to complete the authentication exchange and if successful completes the IKEv2 exchange.

#### 5.3.4.2 Air-Ground Access Network Security

This ATN/IPS Manual requires that mobile nodes implement the security provisions of the accces network.  The security provisions of an access network are those associated with access control to the network itself and are typically implemented using an AAA infrastructure.

The IETF mobility working groups and other standards development organizations have recognized that although Mobile IPv6 and Proxy Mobile IPv6 were originally designed without integration with an AAA infrastructure, it may be more efficient to authenticate users using credentials stored at the AAA server.  Furthermore, use of an AAA infrastructure may facilitate other bootstrapping functions such as dynamic configuration of other parameters such as the home address and home agent address in order to accomplish mobility registration.    EAP between the MN and Authenticator may operate over the access network link level protocol or in conjunction with IKEv2 as described for securing Mobile IP signaling. EAP between the Authenticator and AAA server operates over RADIUS [RFC 2865] or DIAMETER [RFC 3588].

### 5.3.5 Public Key Infrastructure Profile and Certificate Policy

This manual requires that ATN/IPS nodes use the Internet X.509 Public Key Infrastructure Certificate and Certificate Revocation List (CRL) Profile as specified in RFC 5280 and the Internet X.509 Public Key Infrastructure Certificate Policy and Certificate Practices Framework as specified in RFC 3647.  This manual notes that the Air Transport Association (ATA) Digital Security Working Group (DSWG) has developed a Certificate Policy (ATA Specification 42) for use in the Aviation community.  ATA Specification 42 includes certificate and CRL profiles that are suitable for aeronautical applications.  These profiles provide greater specificity than, but do not conflict with, RFC 5280.  The ATA Specification 42 profiles are interoperable with an aerospace industry PKI bridge.  Interoperablity with an operational aerospace and defense PKI bridge will provide the opportunity to leverage existing infrastructure rather than develop an infrastructure unique to the ATN/IPS and will more readily achieve interoperability and policy uniformity in a multi-national, multi-organizational aerospace and defense environment.

### 5.3.6 General Guidance for Implementation of Security

Many government agencies have developed additional guidance and profiles for implementing security.  In the US the the NIST 800 series of recommendations is an example  of general security implementation guidance covering a broad range of topics.

In the IETF there have been many Internet Drafts dealing with security.  Two informational RFCs of particular interest are RFC 4942 AND RFC 4864.  RFC 4942 gives an overview of security issues associated with IPv6.  The issues are grouped into three general categories: issues due to the IPv6 protocol itself; issues due to transition mechanisms; and issues due to IPv6 deployment.  RFC 4864 notes that Network Address Translation (NAT) is not required in IPv6 and describes how Local Network Protection (LNP) mechanisms can provide the security benefits associated with NAT.  In particular, RFC 4864 describes how the IPv6 tools for Privacy Addresses, Unique Local Addresses, DHCPv6 Prefix Delegation, and Untraceable IPv6 Addresses may be used to provide the perceived security benefits of NAT including the following: Gateway between the Internet and an Internal Network; Simple Security (derived from stateful packet inspection); User/Application Tracking; Privacy and Topology Hiding; Independent Control of Addressing in a Private Network; Global Address Pool Conservation; and Multihoming and Renumbering.  RFC 4864 describes the addition benefits of native IPv6 and universal unique addressing including the following:  Universal Any-to-Any Connectivity, Auto-Configuration, Native Multicast Services, Increased Security Protection, Mobility and Merging Networks.

# 6.0 Voice over Internet Protocol (VoIP)

The key advantages associated with the use of a packet network for the transmission of digitized voice are:

- Bandwidth allocation efficiency

- Ability to use modern voice compression methods

- Associate economics with shared network use

- Reduce costs

- Enhanced reliability of packet networks

- Ability to use multiple logical connections over a single physical circuit.

## 6.1 Standards and Protocols

There are two standardized frame works for implementing VoIP, H.323 and SIP.  Although both protocols may be used for VoIP applications, the original focus of each protocol is different.  The focus of H.323 has been to handle voice and multimedia calls, including supplementary services, while SIP was designed as a generic transaction protocol for session initiation not bound to any specific media (e.g., audio or video).  Details of relevant protocols are described in the following subsection:

### 6.1.1 H323

As shown in Figure 8.1, H.323 operates in the application layer to support multimedia, data and signaling protocols. Also depicted in Figure 2 are the various protocols used to convey multimedia traffic over TCP/UDP/IP networks.

Multimedia                             Data Transfer                Signalling

Figure 2 H.323 Core Architecture

#### 6.1.1.1 Multimedia

This group of protocols converts between analog (e.g., voice) and digital signals, which are fed into, or picked from, the UDP/IP network. Some of these protocols include:

- Audio codecs – These compress digital voice for low bandwidth transmission, and decompress digital voice received from the network for feeding to the user audio device (e.g., speaker, headphone).

- Video codecs – These compress digital video for constrained bandwidth, and decompress digital video received from the network for feeding to the user video device.

- RTP (Real-Time Transport Protocol) and RTP Control Protocol (RTCP) – These are control protocols for the payloads fed into the network. RTP regulates the end-to-end delivery of audio and video in real time over IP networks.  RTCP regulates the control services in multimedia transmissions, and monitors the quality of its distribution, including synchronization of receivers.

#### 6.1.1.2 Data Transfer

This class of protocols provides real-time, multi-point data communications and application services over IP networks (e.g., collaborative decision making with video, voice, and data exchange).  Data transfers between generic applications and the IP network are processed by the T.120 protocol, which can operate over various transports, including PSTN and ISDN.

T.130 is a protocol still under development for controlling audiovisual sessions for real-time multimedia conferencing, and ensure high QoS.

#### 6.1.1.3 Signalling

- H.225.0 call signaling is used to set up connections and exchange call signalling between H.323 endpoints (terminals and gateways), which are transported as real-time data and carried over the TCP/UDP/IP network.  H.225.0 uses Q.931 for call setup and teardown.

- H.245 control signaling is used to exchange end-to-end messages between H.323 endpoints.  The control messages are carried over H.245 logical control channels, which are relayed between conference session endpoints.

- H.235 provides security services within the H.323 framework, such as authentication, encryption, integrity and no-repudiation.

H.450.1 deals with the procedures and signalling protocol between H.323 entities for the control of supplementary services.  Other protocols within the H.450 series (i.e. H.450.2-12) provide specific supplementary services (e.g., call transfer, call hold, call waiting, call priority).

### 6.1.2 MGCP/MEGACO

Shown in Figure 3 is the SIP Protocol Suite. SIP is an application layer control protocol that provides advanced signalling and control functionality for large range multimedia communications.  SIP is an alternative to H.323, which establishes, modifies, and terminates multimedia sessions, which can be used for IP telephony.  SIP is an important component in the context of other protocols to enable complete multimedia architecture, as shown in Figure 4.  These include RTP for real time data transport and QoS assurance, RTSP for controlling streaming media, MEGACO for controlling gateways to the PSTN, Figure 8.3, and SDP for describing multimedia sessions.  These sessions include Internet multimedia conferences, Internet telephone calls, and multimedia distribution over TCP/UDP/IPv4, or IPv6, as shown in Figure 5.

Figure 3 SIP Protocol Suite

# 7.0 IPS Implementations

## 7.1 OLDI

On-Line Data Interchange (OLDI) combined with the Flight Message Transfer Protocol (FMTP) is a means to enable AIDC operational requirements for the co-ordination and transfer of aircraft between adjacent air traffic control units.

The relationship between AIDC and OLDI messages is described in the Appendix of ICAO Document 9694, Part VI, Chapter 1.

The OLDI specification does not mandate the implementation of OLDI messages but specifies the requirements that need to be met when implementing such facilities. If OLDI messages are implemented as the result of regulatory provisions, or based on bilateral agreement between Air Traffic Control Units, then the requirements outlined as mandatory in this specification for those messages become mandatory for implementation. This is required in order to meet the purpose of the messages and to ensure interoperability between systems.

The co-ordination procedure requires that systems identify whether or not transfers are in accordance with Letters of Agreements (LoAs).

The process which checks such compliance is referred to in the OLDI Specification as "the filter". The database used for the filter will include the following, if required:

- agreed co-ordination points;

- eligible (or ineligible) flight levels which may also be associated with the co-ordination points;

- aerodromes of departure;

- destinations;

- agreed direct routes ;

- time and/or distance limits prior to the COP, after which any co-ordination message is considered non-standard;

- any other conditions, as bilaterally agreed.

All items in this list may be combined to define more complex conditions.

The format of the messages (ICAO PANS/RAC 4444 or EUROCONTROL ADEXP) to be transmitted and received has to be agreed bilaterally.

The address of the ATS units providing the services has to be agreed and has to be different from the addresses of the other units to which the ATS units are already connected or planned to be connected. The ATS unit addresses are part of the OLDI message.

## 7.2 FMTP

The Flight Message Transfer Protocol is a communications stack based on TCP/IPv6. FMTP is a state machine that handles connection establishment and session management. Each FMTP system requires to be assigned with an identification value that is to be exchanged during connection establishment. The identification values have to be bilaterally agreed and must be different from the values of the other units to which the ATS units are already connected or planned to be connected.

The FMTP specification assumes the transfer of ASCII characters but implementations of the protocol may wish to extend this support to other character sets or binary transfers. Further guidance material on FMTP is available from EUROCONTROL at the following website http://www.eurocontrol.int/communications/public/standard_page/com_network.html

### 7.2.1 Testing OLDI/FMTP

EUROCONTROL has developed a test tool named ETIC to validate OLDI/FMTP implementations and build test scenarios. The tool can be made available to FMTP implementation projects upon request. Request for further information on ETIC can be addressed to etic@eurocontrol.int.

# APPENDIX A – REFERENCE DOCUMENTS

IETF STANDARDS AND PROTOCOLS

The following documents are available publicly at http://www.ietf.org and form part of this manual to the extent specified herein. In the event of conflict between the documents referenced herein and the contents of this manual, the provisions of this manual shall take precedence.

Request for Comments (RFCs)

netlmm-mn-ar-if

Network-based Localized Mobility Management Interface between Mobile Node and Mobility Access Gateway, May 2007

RFC-768	User Datagram Protocol, August 1980

RFC-793	Transmission Control Protocol (TCP), September 1981

RFC-1006	ISO Transport Service on top of TCP, May 1987

RFC-1323	TCP Extensions for High Performance May 1992

RFC-1981	Path Maximum Transmission Unit (MTU) Discovery for IP Version 6, August 1996

RFC-2126	ISO Transport Service on top of TCP, March 1997

RFC-2460	Internet Protocol, Version 6 (IPv6) Specification, December 1998

RFC-2474	Differential Services Field, December 1998

RFC-2488	Enhancing TCP over Satellite Channels, January 1999

RFC-2858	Border Gateway Protocol (BGP4) Multiprotocol Extensions June 2000

RFC-3775	Mobility Support in IPv6,  June 2004

RFC-4271	A Border Gateway Protocol 4 (BGP-4), January 2006

RFC-4291	IP Version 6 Addressing Architecture, February 2006

RFC-4301	Security Architecture for the Internet Protocol, December, 2005

RFC-4302	Internet Protocol (IP) Authentication Header, December 2005

RFC-4303	IP Encapsulating Security Payload (ESP), December 2005RFC-4305	Cryptographic Algorithm Implementation Requirements for Encapsulating Security Payload (ESP) and Authentication Header (AH) – (NB proposed standard, obsoletes RFC-2402, RFC-2406), December 2005

RFC-4306	Internet Key Exchange (IKEv2) Protocol, December 2005

RFC-4307	Cryptographic Algorithms for Use in the Internet Key Exchange Version 2 (IKEv2), December 2005

RFC-4443	Internet Control Message Protocol (ICMPv6) for the Internet Protocol Version 6 (IPv6) Specification, March 2006

RFC-4492	Elliptic Curve Cryptography (ECC) Cipher Suites for Transport Layer Security, May 2006

RFC 4555	IKEv2 Mobility and Multihoming Protocol (MOBIKE),  June 2006

RFC 4830	Problem Statement for Network-Based Localized Mobility Management (NETLMM), April 2007

RFC 4831	Goals for Network-Based Localized Mobility Management (NETLMM), April 2007

RELEVANT ICAO PUBLICATIONS

In the event of a conflict between the manual and the provisions in Annex 10, the provisions of Annex 10 shall take precedence.

ICAO Annex 2 Rules of the Air

ICAO Annex 3 Meteorological Service for International Air Navigation

ICAO Annex 10 Aeronautical Telecommunications – Volume III, Part I – Digital Data Communication Systems

ICAO Annex 11 Air Traffic Services

ICAO Doc. 9705-AN/956 Edition 3, Manual of Technical Provisions for the ATN, 2002

ICAO Doc. 9739 Edition 1, Comprehensive ATN Manual (CAMAL), 2000

ICAO Doc. 4444 Procedures for Air Navigation Services – Air Traffic Management 14th Edition, 2001

ICAO Doc. 9694 Manual of Air Traffic Services Data Link Applications

ICAO Doc. 9880 Detailed Technical Specifications for the Aeronautical Telecommunication Network (ATN) using ISO/OSI protocols

EUROCONTROL SPECIFICATIONS

The following documents are available publicly at http://www.eurocontrol.int/ses and form part of this manual to the extent specified herein. In the event of conflict between the documents referenced herein and the contents of this manual, the provisions of this manual shall take precedence.

EUROCONTROL-SPEC-0100	EUROCONTROL Specifications of Interoperability and Performance Requirements for the Flight Message Transfer Protocol (FMTP), Edition 2.0, June 2007

EUROCONTROL-SPEC-0106	EUROCONTROL Specifications for On-Line Data Interchange (OLDI), Edition 4.0, October 2007

# APPENDIX B – ABBREVIATIONS/DEFINITIONS

The acronyms used in this manual are defined as follows:

AAC		Aeronautical Administrative Communications

AOC		Aeronautical Operational Communications

AS		Autonomous System

AD		Administrative Domain

AH		Authentication Header

AIDC		ATS Interfacility Data Communications

AINSC	Aeronautical Industry Service Communication

AN		Access Network

ATSMHS	ATS Message Handling Services

ATN		Aeronautical Telecommunication Network

ATC		Air Traffic Control

ATS		Air Traffic Services

ATSU		ATS Unit

ATSC		Air Traffic Services Communication

BGP		Border Gateway Protocol

CL		Connection-less

CN		Correspondent Node

CO		Connection-oriented

ECC		Elliptic Curve Cryptography (ECC)ECP Encryption Control Protocol

ESP		Encapsulating Security Protocol

FIR		Flight Information Region

FMTP		Flight Message Transfer Protocol

G-G		Ground- to- Ground

HC		Handover Control

H-MM		Host-based Mobility Management

IANA		Internet Assigned Numbers Authority

ICAO		International Civil Aviation Organization

ICMP		Internet Control Message Protocol

IETF		Internet Engineering Task Force

IKEv2		Internet Key Exchange (version2)

IP		Internet Protocol

IPS		Internet Protocol Suite

IPsec		IP Security

IPv6		Internet Protocol version 6

ISO		International Organization for Standardization

LAN		Local Area Network

LM		Location Management

MM		Mobility Management

MN		Mobile Node

MTU		Maximum Transmission Unit

N-MM		Network-based Mobility Management

OLDI		On-Line Data Interchange

OSI		Open System Interconnection

QoS		Quality of Service

RFC		Request for Comments

TCP		Transmission Control Protocol

TLS		Transport Layer Security

SARPs		Standards and Recommended Practices

SPI		Security Parameter Index

UDP		User Datagram Protocol

WAN		Wide Area Network

DEFINITIONS

Definitions are consistent with IETF terminology.

Access Network

A network that is characterized by a specific access technology.

Administrative Domain

An administrative entity in the ATN/IPS.  An Administrative Domain can be an individual State, a group of States, an Aeronautical Industry Organization (e.g., an Air-Ground Service Provider), or an Air Navigation Service Provider (ANSP) that manages ATN/IPS network resources and services.  From a routing perspective, an Administrative Domain includes one or more Autonomous Systems.

ATN/IPS Internetwork

The ATN/IPS internetwork consists of IPS nodes and networks operating in a multinational environment.

Autonomous System

A connected group of one or more IP prefixes, run by one or more network operators, which has a single, clearly defined routing policy.

Global Mobility

Global Mobility is mobility across access networks.

Handover Control

The handover control (HC) function is used to provide the ‘session continuity’ for the ‘on-going’ session of the mobile node.

Host	A host is a node that is not a router.  A host is a computer connected to the ATN/IPS that provides end users with services.

Host-based Mobility Management

A mobility management scheme in which MM signaling is performed by the mobile node.

IPS Mobile node

an IPS node that uses the services of one or more MSPs.

Local Mobility

Local Mobility is network layer mobility within an access network.

Location Management

The location management (LM) function is used to keep track of the movement of a mobile node and to locate the mobile node for data delivery.

Mobility Service Provider (MSP)

is a service provider that provides Mobile IPv6 service (i.e. Home Agents), within the ATN/IPS. A MSP is an instance of an AD which may be an ACSP, ANSP, airline, airport authority, government organization, etc.

Network-based Mobility Management

A mobility management scheme in which the MM signaling is performed by the network entities on behalf of the mobile node.

Node		A device that implements IPv6

Router	A router is an node that forwards Internet Protocol (IP) packets not explicitly addressed to itself.   A router manages the relaying and routing of data while in transit from an originating end system to a destination end system.

Inter-Domain Routing (Exterior Routing Protocol)

Protocols for exchanging routing information between Autonomous Systems.  They may in some cases be used between routers within an AS, but they primarily deal with exchanging information between Autonomous Systems.

Intra-Domain Routing (Interior Routing Protocol)

Protocols for exchanging routing information between routers within an AS.

# Text boxes

T.120

(Real Time)

T.130

(Audio- Visual

Control)

RTP

RTCP

(Real Time TransportControl Protocol)

Audio

Codecs

G.711

G.728

G.729

Video

Codecs

H.261

H.263

H.450.1 Series

(Supplementary Services)

IP (Internet Protocol) v4 or v6

TCP (Transfer Control Protocol)

UDP (User Datagram Protocol)

H.235 (Security)

H.245

(Control

Signalling)

H.225.0

RAS

Q.931

(Call Signalling)

Application User

ATN-App ASE

IPS DS

IPS