AMCP/WG-M/1/WP 7

AERONAUTICAL MOBILE COMMUNICATIONS PANEL (AMCP)

Working Group M Meeting

Malmo, Sweden

12-19 December, 2000

Proposed Defect Report

| Title: | Bit Ordering |
| --- | --- |
| Reference Number: | M-3-001 |
| Document(s) Affected: | Manual on VDL Mode 3 Technical Specifications |
| Document Version: | AMCP/7 Report |
| Date Submitted: | 14/11/00 |
| Submitter Name: | Robert Morgenstern |
| Submitter Address: | 1820 Dolley Madison Blvd, M/S W387 McLean, VA 22102 USA |
| Submitter Phone: | +1 703 883 7846 |
| Submitter Fax: | +1 703 883 1367 |
| Submitter Email Address: | rmorgens@mitre.org |
| Sections Affected: | B.1.2, B.2.11, Fig B-13, Fig B-14 |
| Severity: | CRITICAL |
| Proposed Defect: | Incompatible bit ordering between Tech Manual and Implementation Aspects documents |
| Recommended Resolution: | Bit ordering should be as defined in the Implementation Aspects due to simpler implementation and more existing implementations. See attached for specific changes to TM. |
| Status: | PROPOSED |
| History: | 12/12/00 - Received by WG-M |

The following modifications are needed in the Manual on VDL Mode 3 Technical Specifications to resolve conflicts in bit order between documents.

Modify B.1.2 as follows:

B.1.2  Bit Ordering

Bit fields in this Appendix shall be encoded such that the most significant bit is in the first bit transmitted (shown as the lowest bit number position in the figures).  For binary data listed in tables, the left-most bit shall be considered the most significant bit.  For fields that are split over a number of octets the most significant portion shall be sent in the lower numbered octets.

Modify B.2.11 as follows to correct the reference:

B.2.11  Acknowledgement message

The Acknowledgement message shown in Figure B-10, is used by the aircraft to acknowledge a V/D (data) burst sequence.

Modify Figure B-13 and B-14 as follows:

|  | first bit transmitted | Bit Number |
| --- | --- | --- |
| Octet No. | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 |
| 1 | Message ID = 0XX | Local User ID |
| 2 | Local User ID (cont.) | EOM |  |

Figure B-13.  V/D (Voice) Burst Header Segment

|  | first bit transmitted | Bit Number |
| --- | --- | --- |
| Octet No. | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 |
| 1 | Message ID = 1XX | Ground Station Code | Segment Number |
| 2 | Segment Number | Spare | EOM |  |  |  |  |

Figure B-14.  V/D (Data) Burst Header Segment