AMCP/WG-M/1/WP 8

AERONAUTICAL MOBILE COMMUNICATIONS PANEL (AMCP)

Working Group M Meeting

Malmo, Sweden

12-19 December, 2000

Proposed Defect Report

| Title: | MASPS Alignment |
| --- | --- |
| Reference Number: | M-3-003 |
| Document(s) Affected: | Manual on VDL Mode 3 Technical Specifications |
| Document Version: | 4.0 |
| Date Submitted: | 21/11/00 |
| Submitter Name: | Robert Morgenstern |
| Submitter Address: | 1820 Dolley Madison Blvd, M/S W387 McLean, VA 22102 USA |
| Submitter Phone: | +1 703 883 7846 |
| Submitter Fax: | +1 703 883 1367 |
| Submitter Email Address: | rmorgens@mitre.org |
| Sections Affected: | Various |
| Severity: | CRITICAL |
| Proposed Defect: | Updating Tech Manual with latest changes to VDL Mode 3 MASPS before publication |
| Recommended Resolution: | See attached for specific changes to TM. Bit Ordering submitted as separate PDR. |
| Status: | PROPOSED |
| History: | 12/12/00 - Received by WG-M |

5.5.1.1.1	     Recommendation.(  The VDL Mode 3 user should be made aware of a "step-on" condition, i.e. the condition resulting from two VDL Mode 3 users on the same channel attempting to gain access to the channel close enough in time resulting in neither party achieving access.

5.5.1.2    Channel occupancy.  Channel occupancy shall be considered the amount of time spent on the channel per access event.

For data operation, an access event shall consist of no more than 15 consecutive V/D (data) burst opportunities.  For downlink data transmission, an access event shall be the result of a single Reservation Request.

For voice operation, an access event shall not be limited to a fixed number of V/D (voice) burst opportunities.  However, voice operation shall honor the voice signaling information issued in the M uplink burst.  An access event shall correspond with each push-to-talk (PTT) assertion.  The maximum duration of a single aircraft radio PTT event shall be limited to 35 seconds.  The PTT event shall be automatically terminated and the user being terminated shall be alerted to the termination.

5.5.2.1.5   External time reference interface.  The VDL Mode 3 ground stations shall have the option to synchronize their station TDMA system timing clocks to a common absolute time standard.  This external time source shall provide a timing strobe once per second on the second and a means to identify epoch boundaries.  For purposes of providing epoch strobes, the external time source shall be aligned to UTC on 6 January 1980.

5.5.2.4    System configurations.  The VDL Mode 3 shall recognize and support the set of system configurations identified in Table 5-47.

Note 1.( All the configurations except 3T are called non-3T configurations .

Note 2.( See the Implementation Aspects for the applications and descriptions of each System Configuration.

5.5.2.5    Media access control cycle

Media access shall be based on a MAC cycle of 240 ms (two consecutive TDMA frames, denoted even and odd frames, Figure 5-3a).

Note. ( MAC cycles for each System Configuration are shown in the Implementation Aspects.

5.5.2.5.1    Logical burst access channels.  For all configurations (except 3T, 3S and 2S1X), VDL Mode 3 shall grant media access individually for each of up to 8 separate LBACs numbered 1-8.  A description of each LBAC for these cases (other than 3T, 3S and 2S1X) shall be as given by Table 5-48.  For the 3T configuration, VDL Mode 3 shall grant media access individually for each of up to 18 separate Logical Burst Access Channels (LBACs) numbered 1-18.  A description for each LBAC for the 3T configuration shall be as given by Table 5-50.  For the 3S configuration, VDL Mode 3 shall grant media access individually for each of up to 10 separate LBACs numbered 1-10. A description for each LBAC for the 3S configuration shall be as given by Table 5-51a.  For the 2S1X, VDL Mode 3 shall grant media access individually for each of up to 7 separate LBACs numbered 1-7.  A description for each LBAC for the 2S1X configuration shall be as given by Table 5-51b.

Note.( MAC cycles for each System Configuration are shown labeled with each LBAC in the Implementation Aspects for VDL Mode 3.

5.5.2.5.2    Burst access timing.  The System Configuration code provided in the M uplink burst (Appendix B, Section B.2.1) shall be used by the aircraft VDL in conjunction with the timing reference point  to establish proper burst timing.  For all configurations (except 3T, 3S and 2S1X), LBACs shall be established according to Table 5-49; for the 3T configuration, LBACs shall be established according to Table 5-50;  for 3S configuration, LBACs shall be established according to Table 5-51a; and for 2S1X configuration, LBACs shall be established according to Table 5-51b.   The timing reference point (TRP) shall be established per Section 5.5.4.1. The relative timings among the TRPs of different user groups for the various system configurations are shown in Table 5-51c.

5.5.3.1    Parameter t (truncation).  This parameter shall be the number of MAC cycles which can elapse in normal timing state 1 (TS1) while not receiving a primary time reference (defined in Section 5.5.4.1.1) without requiring transmitted V/D (voice) bursts to be truncated.

Note:  This parameter is determined by the symbol clock stability of the aircraft VDL and represents the number of MAC cycles prior to accumulating a timing drift of (1 symbol periods.

5.5.3.1.1   Validity Window.  Due to the 1 symbol period accuracy assumed for the aircraft radio timing, the aircraft radio shall establish a validity window also equal to ( 1 symbol period.  A timing beacon shall be considered valid, i.e., acceptable for timing, if it is received within the validity window with respect to the previous beacon’s timing reference.

5.5.3.3    Parameter NM1 (maximum retry). The parameter NM1 shall represent the maximum number of retransmissions of a random access Reservation Request message.

5.5.3.7    Parameter WR (reservation request retransmission delay). The parameter WR shall specify the number of MAC cycles that an aircraft radio shall wait before attempting a Reservation Request message retransmission.

5.5.4   Description of procedures

Media access shall observe the procedures described in this section in addition to observing the timing structure limitations of Section 5.5.2.1.

5.5.4.1    Timing acquisition and maintenance

5.5.4.1.1    Primary timing reference.  The aircraft VDL shall derive its primary timing from the received M uplink burst (LBAC 11 for 3T configuration, either LBAC 5, 7, or 9 for 3S configuration, either LBAC 4 or 6 for 2S1X, and LBAC 5 for other configurations) associated with its assigned user group and Ground Station Code.  The timing reference point shall be established based on the center of the first received symbol of the synchronization sequence at the antenna port of the M uplink burst associated with the user group assigned.  VDL media access opportunities for transmitted bursts shall be set relative to this reference in terms of transmitted symbol periods as shown in Tables 5-49, 5-50, and 5-51.

Note 1. ( To remain in the normal timing state (TS1), an aircraft VDL should maintain its primary timing to within (1 symbol period of the correct time based on the position of the aircraft relative to the ground station.  This timing tolerance is the basis for developing the timing state transition rules of Sections 5.5.4.1.4 and 5.5.4.1.5.  Refer to Section 5.5.3.1 for this timing accuracy requirement.

Note 2.  The relative timings among the TRPs of the different user groups are as shown in Table 5-51c.

5.5.4.1.2    Alternate timing reference.  When required by the procedures of Section 5.5.4.1.3 through Section 5.5.4.1.5, the aircraft VDL shall derive Alternate timing in truncate timing state 2 (TS2) from alternate timing sources (ATSs).  ATSs are poll responses (except in the 3T configuration)  associated with the user group or another user group (if available) and M uplink bursts in slots other than the one controlling the aircraft radio’s user group received during that MAC cycle.  This alternate timing shall be derived based on the first received symbol of the synchronization sequence of the received poll responses or uplink M bursts.   The aircraft VDL shall accept timing from ATSs if they obey the following rule:

Tr < Ta + 0.04  ( CTC2  ( Ts

where Ta is the expected time of an ATS as determined by the aircraft radio’s clock, Tr is the actual time of arrival of the ATS with respect to the aircraft radio’s clock, Ts is the symbol period, and CTC2 is the current value of the CTC2 counter (defined in Section 5.5.4.1.3).  If CTC2 is greater than 800, all ATS time updates shall be accepted.  If the time is updated, CTC2 is reset to 0.

5.5.4.1.3   Coast timing counters.  The aircraft VDL shall maintain Coast Timing Counter 1 (CTC1), Coast Timing Counter 2 (CTC2), and Coast Timing Counter 3 (CTC3) in order to determine the timing state for each MAC cycle. CTC1, CTC2, and CTC3 shall be maintained per Table 5-54. The maximum value that each of the three CTC counters is allowed to increment to shall be 1023.  Once a CTC counter reaches 1023, that CTC counter shall be held at that value indefinitely until reset is required in accordance with the rules stated in Table 5-54.

5.5.4.1.6   Dummy poll responses.  When an aircraft radio receives an uplink M channel message with value 61 or 62 (Section B.2.1.4) in the Aircraft ID (Poll) field, indicating that the ground station does not support discrete addressing, an aircraft radio shall transmit dummy Poll Responses in downlink M slots reserved for Poll Response.  The format of a dummy Poll Response shall be identical to a regular Poll Response.  Dummy Poll Responses shall not be processed by the controlling ground station.  The MAC cycle in which to transmit the dummy Poll Responses shall be chosen by the following algorithm:

Immediately after net initialization, after determining that the uplink Beacon contains Aircraft ID = 61 or 62, divide all further MAC cycles into groups of 25.  Within each group, choose one MAC cycle at random from 1 to 25 in which to transmit a dummy Poll Response.  Continue to transmit dummy Poll Responses for as long as the aircraft radio remains in timing state TS1.

Note 1. ( For the voice-only configurations: 4V, 3V, 3S and 2S1X, polling may not be implemented and a ground radio in one of these configurations may not support polling.  In order to support the transmission of an Alternate Timing Reference in these configurations (see Section 5.5.4.1.2), aircraft radios must transmit “Dummy Poll Response” messages since they are never actually polled.

Note 2. ( Analysis and simulation have shown that, unless the number of aircraft radios is extremely large, the probability that at least one MAC cycle out of 25 contains one and only one dummy Poll Response is very close to 1.

Note 3. ( The LBACs available for dummy Poll Responses include LBAC 1 for configurations 4V, 3V, 3S, and 2S1X, irrespective of whichever LBAC is associated with the time slot the aircraft radio is currently connected to.

5.5.4.3.1    Polling. When directed by the ground LME the ground MAC sublayer shall transmit a Poll Request message. The aircraft MAC sublayer shall deliver a received Poll Request message to the aircraft LME. Upon receiving a Poll Response from the aircraft LME, the aircraft MAC sublayer shall stop the Reservation Request retransmission using the random access M-channel until a new request is generated.  The aircraft station shall respond to a poll by the ground station by transmitting a Reservation Request message in LBAC 2, 3, or 4 for 3T configuration, and LBAC 1 for other configurations in the MAC cycle immediately following the poll.  This opportunity to request a reservation shall be consistent with the procedures of Section 5.5.4.4.3.3.3.  If no reservation is needed by the aircraft VDL, the Number of Slots Requested field and the Voice Request field shall be set to zero.

The ground MAC sublayer shall deliver a received Poll Response message to the ground LME.  The ground station shall respond to a Reservation Request message contained in a Poll Response using the procedures identified in Sections 5.5.4.4.3.3.1 and 5.5.4.4.3.3.3.  No response shall be sent by the ground station if the number of slots in the reservation field is zero.

5.5.4.4.1    Segmentation function.  The MAC sublayer shall perform segmentation of the user message longer than one data burst, as received from the upper layer, to support data burst transmission.  The segmentation function shall observe the following procedures:

Each segment, except the last, shall occupy an entire data burst and shall set the EOM field of the Header segment to 0.  Each segment of the user message shall include the Segment Number in the Segment Number field of the Header segment of each V/D (data) burst.  The Segment Number shall begin with 1 for the first segment and shall be incremented by 1 for subsequent segments.  The final segment of the user message shall set the EOM field to 1 to indicate to the peer MAC entity that the user message is completed.  A Segment Number of 0 is reserved.

All downlink segments of the user message shall occupy only the time slots indicated in the Reservation Response field of the M uplink (Normal Message) burst (Section B.2.2 of Appendix B) and shall be transmitted in consecutive burst opportunities.

Any missing or corrupted segments shall result in discarding of the entire user message.

Note. ( The Maximum user message size is established by the maximum DLS frame group size assuring containment within a maximum of 15 V/D (data) bursts (Section 5.6.3.2).

5.5.4.4.2.1    Acknowledgement protocol. Upon receipt of an ACK frame from the local DLS sublayer, an Acknowledgement message shall be transmitted in the M burst downlink subchannel associated with the same slot one MAC cycle after the receipt of the last burst of the message being acknowledged, as illustrated in Figure 5-4. The downlink ACK frame shall not be transmitted in a V/D (data) burst.  The peer MAC sublayer shall restore the ACK frame and forward it to the local DLS sublayer.

5.5.4.4.3.2   Assemble message for MAC data transfer.  Every MAC cycle, the MAC sublayer shall determine if the transmit queue manager has traffic to be transmitted.  The existence of traffic in the transmit queue manager shall cause the MAC sublayer to initiate the data transfer procedure described in Sections 5.5.4.4.3.3 through 5.5.4.4.3.6 below.

5.5.4.4.3.3.2	Reservation request acknowledgement.  Upon receipt of a valid Reservation Request, the ground station shall respond with a Reservation Response message. This message shall be either a reservation or a Reservation Request Acknowledgement (RACK).

A Reservation Response message with slot assignment shall be sent to convey the actual slot assignment to the requester.  A Reservation Response message with RACK shall be sent to the requester if the ground station is unable to honor the request due to unavailability of the time slots.  The Reservation Response message with RACK shall not be sent in response to a Poll Response that cannot be immediately granted.

If the aircraft is scheduled to be polled before a Reservation Response message (with either slot assignment or RACK) can be generated, the ground station shall send the Poll Request to the aircraft as scheduled, wait for the Poll Response, and send a Reservation Response or no response, as required.

Upon receiving a Reservation Response message with RACK, the aircraft radio shall stop retransmitting the pending request, but shall continue to respond to Poll Request with a Poll Response (see Section 5.5.4.4.3.3.3).

Note 1.( The Reservation Request Acknowledgement message is a special Reservation Response message (described in Section B.2.2.1) with value 00012  in the Reserved Slot.

Note 2.(  RACK  is not a proper ground station response to a Poll Response message except to the first Poll Response during net entry.

5.5.4.4.3.3.3	Reservation via poll response. Aircraft shall be allowed to use the Poll Response to reaffirm, to modify, or to cancel the outstanding request, or to replace the outstanding request with a new request.  The new Reservation Request shall have no limitation on the number of time slots requested, other than that the maximum of V/D (data) bursts requested is consistent with the value of parameter N1 (see Section 5.6.3.2).  Upon receiving a Poll Response, the ground station shall automatically replace the outstanding request with the new request.  If a Poll Response for the new request is received with no slots requested, the ground station shall automatically cancel the outstanding request.  If the Poll Response is not received, the ground station shall cancel the outstanding request.  The aircraft shall wait for the next poll opportunity to retransmit the request or transmit a new request.

The rules described in Section 5.5.4.4.3.3.1 on sending a new reservation request after the aircraft has received a Reservation Response message with slot assignment for the outstanding request shall apply when the outstanding request is via Poll Response.

5.5.4.4.3.6    Acknowledgement protocol. Acknowledgements of downlink transmissions sent by the ground station shall be processed by the aircraft DLS to indicate completion of downlink data transfer.

5.5.4.5  MAC data frame transmission. After each transmission that requires acknowledgement, the MAC sublayer shall maintain a retransmission timer T1 for each destination.  This timer is the time that the MAC sublayer shall wait for an acknowledgement prior to a new transmission.  Timeout of the T1 timer shall result in a request to the DLS for a new frame group. This implies that the VDL shall replace the retransmission of the outstanding frame group with the transmission of a new frame group, if the new frame group has higher priority frames. The number of successive T1 timer expirations to a specific destination shall not exceed N2 times.  The LME shall be informed when the successive T1 timer expirations exceeds N2 times, signaling it to terminate the link to that destination.  The N2 counter shall be reset upon the successful acknowledgement of the message.

The maximum transmission delay for an uplink ACK for a VDL Mode 3 ground station shall not exceed T_ack, where T_ack is in MAC cycles.  The delay associated with transmitting an uplink ACK is defined from the time the last V/D (data) burst is received to the time that the ACK transmission begins.  If the ground station is unable to transmit the ACK within T_ack after the receipt of the last downlink V/D (data) burst, it shall not transmit the ACK.  For aircraft stations, the specific downlink M channel for ACK transmission is defined in Section 5.6.5.2.

The MAC data frame transmission system parameters T1, T_ack, and N2 shall be as defined in Table 5-56.

Note.( Upon T1 timer expiration and depending upon the message priorities of the current message queues, the new frame group generated by the DLS sublayer to be sent to the MAC sublayer for transmission may not include the previously transmitted acknowledged frames, which are associated with event of the T1 timer expiration.

5.6.1.3    Data transfer.  Data shall be transferred in the information fields of VDL INFO and CTRL frames.  One and only one subnetwork packet shall be contained in an INFO frame.

5.6.2.3.2    Priority. The priority subfield supplies the priority of the frame for processing. This subfield shall be only included for Data frames.  The 16 levels of priority supported by the ATN for the CLNP subnetwork interface are grouped into four VDL Mode 3 frame priority categories which shall be encoded in the 2-bit priority field per Table 5-57.  The VDL PLP subnetwork interface groups the 16 ATN priority levels down to only two priority levels, high or low, which are mapped into the same 2-bit priority field also designated in Table 5-57.  CTRL_CMD, CTRL_RSP, and ACK frames are always management priority and shall assume a priority of 3, hence they do not need this information encoded in the frame header.  The priority field shall be encoded such that bit 7 of Figure 5-6 is the most significant bit.

5.6.2.4.1    Ground subnetwork address subfield.  The ground subnetwork address subfield shall contain a 6-bit number, unique with respect to adjacent facilities, used to identify the ground subnetwork entity used to communicate with the aircraft user.  The binary value of 000000 shall be reserved to indicate ‘Unknown Subnetwork Address’.  This is used during the connection establishment phase when an aircraft DLS may not yet know the appropriate subnetwork address to use.

5.6.3    Data link service system parameters

The parameters needed by the DLS sublayer shall be as listed in Table 5-58 and detailed in Sections 5.6.3.1 through 5.6.3.2.

5.6.3.1    Timer T3 (link initialization time).  Timer T3 shall be the time that a data link entity waits for a CTRL_RSP frame before retransmitting a CTRL_CMD frame.  Timer T3 shall be started upon transmission of a CTRL_CMD frame.

5.6.3.2    Parameter N1 (Maximum frame group size). The N1 parameter indicates the maximum frame group size in octets. The value of parameter N1 includes all DLS frame headers of its component frames.  The maximum INFO frame that a station can accept shall be limited by the parameter N1 minus 6 octets for the DLS frame header.

5.6.4.3.1.2	Recommendation for Frame Grouping. (  To reduce the number of media accesses, as new information frames arrive at the transmission queue, they should be checked for priorities and grouped in their order of arrival with existing frames of the same priorities into a single MAC sublayer access event.

Note.( Grouping is the inclusion of more than one frame within a single media access event.

5.6.4.3.3   Transmission acknowledgement/retransmission.  The DLS shall not send a new frame group to the MAC sublayer until an acknowledgement frame has been received for the previous acknowledged frame group or upon expiration of the T1 timer.  When the T1 timer expires, the DLS shall provide the MAC sublayer with a new frame group, based on the current priority queuing, for transmission.

Note.( The Media Access Control sublayer is responsible for the determination of when to retransmit the message.  The DLS must remain involved in the retransmission procedure as the MAC sublayer cannot acknowledge correct receipt of a message until the DLS declares the message to have passed the FCS test.

5.7.1 Services

The LME sublayer shall provide link establishment and release services between local DLS and remote DLS.  It shall deliver link status information to the subnetwork dependent convergent function (SNDCF), DLS, and voice unit.

5.7.2.1.1    Net Initialization.  Before the link establishment procedure, the aircraft VDL shall initialize to initial timing state 0 (TS0) and set parameters CTC1, CTC2, and CTC3 to max(f-50, t).  The first part of the link establishment procedure shall be the acquisition of the M uplink burst (LBAC 11 for 3T configuration, LBAC 5, 7, or 9 for 3S configuration, LBAC 4 or 6 for 2S1X, and LBAC 5 for other configurations) associated with the specified user group identifier.  Upon receipt of 2 consecutive M uplink bursts containing the identical information  (i.e., System Configuration, Squelch Window, Slot ID, and Ground Station Code) in bits 5-8 of octet 2 and all of octet 3 of the uplink burst, the LME shall declare the net initialized and shall establish the net operating parameters based on the static information contained in bits 5-8 of octet 2 and all of octet 3.  Configurations 3S and 2S1X shall be considered initialized when at least one of the wide area coverage slots provide 2 consecutive M uplink bursts containing the same information in bits 5-8 of octet 2 and all of octet 3.  Upon net initialization, the aircraft VDL shall transition from TS0 to TS1.

If the aircraft VDL is unable to enter TS1, it shall search for ATSs to determine the number of slots in its net and enter TS2.  If CTC3 equals parameter f before the aircraft VDL enters TS2, it shall enter TS3.  Prior to net initialization, voice access shall be inhibited.

Note. ( Net Initialization is a prerequisite for the next step of Net Entry, however with Net Initialization, dedicated voice circuits (Section 8) can be supported.

5.7.2.1.2    Net Entry. The net entry procedure shall begin with the aircraft station transmitting a Net Entry Request message following a successful net initialization.  The transmission of the Net Entry Request message and the subsequent retransmission, if enabled, shall follow the procedures described in Appendix D. The Net Entry retransmission shall continue until a Net Entry Response message is received or the number of retransmissions reaches NL1.  After NL1 retries (Table 5-60a), the SN-SME shall be notified.  If a Net Entry Response message is received, the aircraft station shall transmit a Poll Response message in the next MAC cycle.  If the Net Entry Response message is of type "previous link preserved," the aircraft TL3 timer (Table 5-60a) shall be stopped.

Note.( All configurations that offer one or more data circuit(s) must support net entry (3V1D, 2V2D, 2V1D, 3T).  The voice only configurations (3V, 4V, 3S and 2S1X) may support net entry if discrete addressing is enabled by the ground user.

Upon receiving a Net Entry Request message, the ground shall check the aircraft ICAO number.  If this number has been assigned a Local ID and the TL3 timer has not been started, the ground shall transmit the Net Entry Response message of type “previous link preserved.”  When the Poll Response message is received by the ground station, the ground station shall respond by sending a Reservation Response message to the entering aircraft during the next MAC cycle.  This message shall be either a reservation or a RACK if data slots were requested or a “no reservation” message if no data slots were requested.

If the aircraft ICAO number has not been assigned a Local ID, the ground shall assign the next available Local User ID to the requesting aircraft and the pending disconnect link table shall be examined.  If the aircraft ICAO number is found in the table, the link status shall be reinstated, the TL3 timer shall be stopped, and the link port address shall be changed to the new radio station port address.  The ground shall transmit the Net Entry Response message of type "previous link preserved."  When the Poll Response message is received by the ground station, the ground station shall respond by sending a Reservation Response message to the entering aircraft during the next MAC cycle.  This message shall be either a reservation or a RACK if data slots were requested or a “no reservation” message if no data slots were requested.

If the aircraft ICAO number is not found in the table and a Local ID has been assigned, the ground shall transmit the Net Entry Response message of type "no previous link."  When the Poll Response message is received by the ground station, the ground station shall respond by sending a Reservation Response message to the entering aircraft during the next MAC cycle.  This message shall be either a reservation or a RACK if data slots were requested or a “no reservation” message if no data slots were requested.  It shall also form a join event message, as required by the supported network stack, and deliver it to all ground routers which are directly connected to the local ground network interface (GNI).

If there are already 60 aircraft in the net when the Net Entry Request message is received, the ground LME shall respond with a Net Entry Response message with the local identifier field set to 0 indicating that the net is currently full. The aircraft shall then use a Local ID of 61 to indicate that it has not entered the net, when communicating with the ground station and other aircraft.

If a duplicate Net Entry Request message is received it shall be discarded.

If the requesting aircraft does not receive a Reservation message from the ground in the next MAC cycle after transmitting the Poll Response message, it shall restart the net entry procedure.

Note 1. ( The GNI provides a connection management function across multiple ground stations such that the same subnetwork connections are maintained with aircraft served by those ground stations.  A description of the GNI function is provided in the Implementation Aspects for VDL Mode 3.

Note 2. – A Net Entry Request message is considered to be a duplicate if a ground station receives a retransmitted Net Entry Request while it is still processing a previously received Net Entry Request from the same aircraft.

Note 3. – Aircraft receiving a “Net Full” indication in the Net Entry Response message are expected to operate in a limited manner until the pilot manually directs the LME to re-initiate the Net Entry Process.

5.7.2.1.3  Initial link negotiation.  Following Net Entry, the aircraft LME shall initiate the link negotiation phase of link establishment to configure the link.  The configuration shall be negotiated using Exchange Identifiers (XIDs) specified in Table 5-59a according to the procedures described in the subsections below.   The parameters negotiated shall be in effect for the duration of the connection.  If the link is preserved between ground stations, then the parameter states are maintained as well, subject to later negotiation.

### 5.7.2.1.3.2  General ground response.  If the ground LME receives the CTRL_CMD_LE frame, it shall confirm link configuration by sending a CTRL_RSP_LE frame containing the parameters from the CTRL_CMD_LE frame that are accepted as well as any that are modified from those included.

5.7.2.1.3.4.2	Unacceptable parameters.  If the parameters in the CTRL_RSP_LE from the ground LME are not acceptable to the aircraft LME, then the aircraft LME shall notify the MAC to send a Leaving Net M burst to terminate the link, and then reset to an Aircraft Identifier of 61 to indicate the lack of discrete-addressed services.

5.7.2.2		Slot selection (configurations 3S and 2S1X).  Configurations 3S and 2S1X shall employ a slot selection algorithm in the aircraft receiver which will choose the best slot to use for the processing of uplink Management frames and the forwarding of any uplink V/D (voice) frames to the voice unit.  Slot selection shall be achieved by applying the selection algorithm to the M uplink bursts of all slots received during one or a number of MAC cycles.

In the downlink direction, the aircraft radio shall always transmit in slot A.  For this reason, the aircraft radio need not apply a slot selection algorithm in order to receive downlink V/D(voice) frames.

Note.( Details of selection algorithms that could be used by the aircraft radio are described in the Implementation Aspects for VDL Mode 3.

5.7.2.3	Link Modification

## 5.7.2.3.1  Description of LME procedures.  The aircraft and ground LMEs shall use the CTRL_CMD and CTRL_RSP frame types listed in Table 5-59b and the procedures described in the text below to maintain a reliable connection between the aircraft and ground system.   The parameters negotiated shall be in effect for the duration of the link connection.

5.7.2.3.2.2.2  	General Aircraft Response. The aircraft LME shall not respond to broadcast CTRL_CMD_LPM frames.

Note.( As there is no acknowledgement to broadcast CTRL frames, the ground station operator may transmit the frames multiple times to increase the likelihood of correct reception.

5.7.2.6.1    Explicit Link Release.  The aircraft LME shall acknowledge receipt of Next Net information only after receiving the same Next Net message in two consecutive cycles. The procedures for Next Net message transmission, Next Net Acknowledgement, and Next Net retransmission shall be per Section 5.5.4.3.3.

When the aircraft LME determines that a net handoff is required, the LME shall generate a Leaving Net message and command the MAC sublayer to transmit the Leaving Net message to the ground station and TL3 timer shall be started.  When TL3 expires, the link shall be changed to disconnect status, and a leave event message, as required by the supported network stack, shall be formed and delivered to the aircraft router.

Note. ( The aircraft LME could take action to execute a net handoff as a result of three possible prior activities: 1) pilot manually selects new channel and takes actions to execute transfer; 2) a Next Net Command message is uplinked and the pilot takes action to execute the transfer; and 3) the aircraft LME autonomously executes a net handoff (system configuration 3T only) per Section 5.5.4.6.

After the Leaving Net message is received, the ground shall start TL3 timer, change link status to pending, stop polling the aircraft, and make the Local User ID assigned to the aircraft available for reassignment.  When the TL3 expires, the link shall be changed to disconnect status, and a leave event message, as required by the supported network stack, shall be formed and delivered to the ground router(s).

5.7.2.6.2    Implicit Link Release.  When the aircraft LME determines that the poll request is not received from the ground over TL4 MAC cycles (Table 5-60a), the aircraft LME shall start the TL3 timer and execute the net entry procedure described in Section 5.7.2.1.2.

When the ground LME determines that an aircraft does not respond to the poll requests exceeding the NL2 times (Table 5-60a), the ground LME shall change the link status to disconnect state, and inform the subnetwork layer-system management entity (SN-SME) and the DLS.  A leave event message, as required by the supported network stack, shall be formed and delivered to the associated ground router(s).

5.7.3.2.3    Timer TL3 (disconnect delay timer). Timer TL3 defines the time interval that the LME shall wait before the link is changed to disconnect state, and a Leave Event message, as required by the supported network stack, is sent to the local router.

Note.( Used by the LME to support link redirection across multiple ground stations.

5.7.3.2.4    Timer TL4 (polling interval). Timer TL4 shall represent the maximum number of elapsed MAC cycles between receipt of two consecutive polls.  Timer TL4 shall be started upon receipt of a poll.  Upon expiration of this timer the upper layers shall be notified.

5.7.3.3  Exchange Identity (XID) Parameter Format

The user data field of CTRL_CMD and CTRL_RSP frames shall be encoded as defined in ISO8885 and shall only include the parameters described in Sections 5.7.3.3.1 through 5.7.3.3.5.  The CTRL frame containing the XID parameters shall be delivered using the V/D (data) burst.  The following order is implied within the parameters:

- Bit order in each parameter value shall be indicated by subscript numbers.  Bit 1 shall indicate the least significant bit.

- Bits shall be transmitted octet by octet, starting with the parameter ID, and within each octet, the rightmost bit (as shown in the tables) shall be transmitted first.

Note. ( XID parameters are extracted from the DLS sublayer CTRL frames and sent to the LME.

5.7.3.3.4.1.3    Network initialization parameter.   The network initialization parameter defines the network support which the avionics VDL Mode 3 installation can perform.  It is used to pass any necessary information to initialize the subnetwork protocol or any compression.  Table 5-66a defines the format of this parameter set.  The length field shall contain the number of networks present.  For each network, a length field shall indicate the number of subparameters.  If no subparameters are needed for a network, then that network’s length field shall indicate zero.

Note 1.( As many networks as applicable can appear, as defined in Table 5-66b.

Note 2.( It is assumed that the ground system will support all options and the aircraft system will support at least one.

A Network Type value of zero indicates that the VDL Mode 3 system is carrying ISO8208 packets which shall be transferred to an ATN ISO8208 data communication equipment (DCE) at the remote end.  The ISO8208 packets shall be compressed using the VDL Mode 3 PLP Compression as defined in Section 6.7.2.1.  A Network Type value of one indicates that the VDL Mode 3 system is carrying ATN CLNP packets which shall be transferred to an ATN-conformant CLNP service at the remote end.  The CLNP packets shall be compressed using the VDL Mode 3 compression as defined in Section 6.7.2.2.  A Network Type value of two indicates that: (1) The VDL Mode 3 system is carrying ISO8208 packets which shall be transferred to an ATN ISO8208 DCE at the remote end; and (2) No compression is performed.  Similarly, a Network Type value of three indicates that the VDL Mode 3 system is carrying ATN CLNP packets which shall be transferred to an ATN-conformant CLNP service at the remote end with no compression. A Network Type Value of four indicates that no (sub)network protocol shall be used.  Data shall be sent to the remote end unmodified with no (sub)network operands.

Note 3.( The ATN designation tells the VDL Mode 3 system to support any ATN-specific requirements.  For example, ATN join and leave events will be generated when network types of 0, 1, 2, or 3 are sent from the aircraft to the ground.

Note 4. ( An indication of ‘No Compression’ in this parameter only indicates that the VDL Mode 3 subnetwork performs no compression.  This does not indicate or prohibit any compression by the network or higher layers.

Note 5. ( The ground station will support all Network Types

Note 6. —The use of the raw interface requires that the largest packet received with the addition of the payload and DLS frame header be a maximum of 930 bytes as no segmentation of the data is possible.

5.7.3.3.4.3.1     NM1 (maximum retry) parameter.  The value of NM1 (used by aircraft) shall be encoded as an unsigned 8-bit integer per Table 5-71.

5.7.3.3.5.44.3.13	MbB_Operations_Permitted.  The MbB_Operations_Permitted parameter shall be encoded as an unsigned 8-bit integer per Table 5-83. There shall be two permissible values. The encoding of 01 hex shall correspond to the logical value of TRUE.  The encoding of 00 hex shall correspond to the logical value of FALSE.

6.7.2    Compression signaling

For each network packet transferred, an indication that the packet is compressed or not compressed shall exist. The Type Specific Information Field located in the Payload octet shall be reserved for this purpose. A value of all zeros (0000 binary) shall be reserved to indicate that no compression information is present, i.e. the data is not compressed.  Additional values for the Type Specific Information Field are possible and are dependent on the compression scheme employed. These values shall be defined with the compression documentation, as necessary.

6.7.3.2.3  Aircraft MbB-operation.  Once the aircraft has determined that it is participating in MbB operations for a particular GNIp-group, the following shall occur.

- The aircraft shall delay the generation of a Leave Event Message for the former_GNIp until one of the following events takes place:

  - Aircraft_TMbB seconds pass after the beginning of participation in MbB operations.

  - A new MbB parameter set is received via an XID transfer that contains an operative_GNIP identifier not matching the stored former_GNIP.

  - The MbB_Operations_Permitted parameter value is FALSE as a result of the uplink of a new MbB parameter set.

- Each subnetwork packet received from the local ATN router shall be encapsulated in a frame, as defined in Section 5.6.2.1. The Ground Subnetwork Address field in the DLS sublayer frame header shall be set to the next hop link address value accompanying the packet received from the ATN router.

- If CLNP compression is occurring, the aircraft CLNP compression utility shall be provided the ground subnetwork address for each packet. This is done to assure the uniqueness of the index number for each GNIP and to restrict compression restart operation on reception of a restart packet to the indices associated with the originating GNIp.

Note.( Each packet forwarded to the VDL Mode 3 avionics system by the local ATN router will contain the next hop destination address to use. The next hop destination defines the ground subnetwork address field in each VDL Mode 3 frame, and is known as a result of the router interface procedures described in Section 6.7.3.2, Note 1.  In this way established and newly required end-system communications will use the path corresponding to the former_GNIP. IDRP initialization will occur using the path corresponding to the operative_GNIP. Once IDRP has initialized, both former and operative GNIP paths will be used until the Aircraft_TMbB timer expires and the former_GNIP path is withdrawn.

6.7.3.3.1	  Determining MbB applicability on the ground.  The operative_GNIp is that GNIp through which communications is actively occurring, i.e., the aircraft has presently entered the net of a GNI within the GNIp-group. Whenever:  (1) an aircraft begins the link establishment protocol, as per Sections 5.7.2.1 and 6.7.3, (2) the operative_GNIP has sent a Net Entry Response of type “no previous link”, as per Section 5.7.2.1.2, and (3) a CTRL_CMD_LE has been received, the operative_GNIP shall examine the downlinked former_GNIp XID parameter of the CTRL_CMD_LE frame.  If the parameter value matches a GNIP identifier on the MbB-list, the operative_GNIP will set the MbB_Operations_Permitted parameter to TRUE. Otherwise this parameter’s value is FALSE. The MbB parameter set, as defined in Section 6.7.3.1, is then uplinked according to the XID procedures defined in Section 5.7.2.3.1. All subsequent XID parameter exchanges occurring with any GNI that is a member of the GNIp-group shall contain the MbB parameter set.

7.2.1  Introduction

The VDL Mode 3 mobile shall support the raw interface and one or more of the other defined SNDCFs. The first type of SNDCF is ISO 8208 based and corresponds to that described in the ATN SARPs for mobile SNDCF. Procedures for this SNDCF are defined in Section 7.2.2. The second type of SNDCF, denoted frame-based SNDCF, shall use the procedures defined in Section 7.2.3.

Note.— The SNDCF is termed frame-based because it uses the VDL Mode 3 frames without the need for an additional protocol (viz. ISO 8208 SNDCF) to transfer network packets. The VDL Mode 3 achieves independence from the network protocol by identifying the payload of each frame. Upon receipt of a frame, the payload field is examined and control is passed to the protocol identified.

7.2.3.2.2	 Payload Identification.

When ATN connectivity is in effect the VDL Mode 3 frame-based SNDCF shall be capable of transferring all types of CLNP and ISH packets. When transferring CLNP or ISH packets the procedures of Section 6.7.1 shall be used to identify each frame payload.

7.2.3.2.3	Disposition of CLNP and ISH Packets.

When ATN connectivity has been specified during the net entry procedures, all CLNP and ISH network packets received by the SNDCF from its remote peer(s) shall be transferred to the local ATN router.

7.2.3.2.4  ISH Packets.

ES-IS or IS-IS packets presented to the VDL Mode 3 system shall be transferred as broadcast or unicast packets as signaled by the ATN router.

7.2.3.2.5	 CLNP Compression.

Compression of CLNP packets within the frame-based SNDCF shall be supported. Compression of CLNP packets shall be performed whenever ATN connectivity is specified and shall be performed according to the procedures defined in Appendix F. Compression shall be performed on both broadcast and unicast packets. The use of compression shall be signaled during net entry, using the procedures described in Section 5.7.3.3.4.1.3.

8.2.1  Speech encoding algorithm

The Voice Unit shall incorporate and default to the Advanced Multiband Excitation (AMBE) vocoder algorithm, version AMBE-ATC-10, from Digital Voice Systems, Incorporated (DVSI), or equivalent vocoder, for speech compression unless commanded otherwise.

Note 1. - The AMBE algorithm is subject to patents.  See SARPs, Annex 10, Vol. III Part 1 Chapter 6 for more details.

Note 2. – The FEC parity bits are included in the 4800 bps transmission rate.

Comment - The algorithm must use a voice frame size compatible with the TDMA frame of 120 ms.

Table 5-55.  Conditions for Voice Media Access (Aircraft VDL)

|  | Voice Signal Field* Encoding |
| --- | --- |
| Timing State | Ground Access | Occupied | Voice Channel Idle |
| Initial TS0** | No Access | No Access | No Access |
| Normal TS1 | No Access | Access permitted if access granted in previous MAC cycle | Access |
| Truncate TS2** (non-3T) | Access | Access | Access |
| Transition** (3T only) | No access | No access | No access |
| Free Running TS3** | Access | Access | Access |

*Defined in Appendix B, Section B.2.1.3.

** The aircraft VDL does not receive Voice Signal Field Encoding information in these cases.

Table 5-56   MAC Data Frame Transmission System Parameters

| Symbol | Parameter Name | Minimum | Maximum | Mode 3 Default | Increment |
| --- | --- | --- | --- | --- | --- |
| T1 (MAC cycles) | Delay before retransmission (ground) | 1 | 40 | 2 | 1 |
|  | Delay before retransmission (aircraft) | 2 | 40 | 10 | 1 |
| T_ack (MAC cycles) | Maximum delay allowable for ACK (ground only) | 1 | 40 | 9 | 1 |
| N2 | Maximum number of successive T1 timer expirations | 1 | 20 | 3* | 1 |

* For T1 (ground) = 2 and T1 (aircraft) = 10.

Table 5-59a.  XID Parameters

|  |  | Air initiated Link establishment | Link connection rejection |
| --- | --- | --- | --- |
|  | Source | Aircraft | New ground Station | Any station |
|  | Destination | Proposed ground station | Aircraft | Any station |
| XID parameters | GI | PI | CTRL_CMD_LE | CTRL_RSP_LE | CTRL_RSP_LCR CTRL_CMD_LCR |
| Public parameters (8885:1993:Mode 3) |  |  |  |  |  |
| Parameter set ID | 80h | 01h | N/A | O | N/A |
| N1-downlink | 80h | 05h | N/A | O | N/A |
| N1-uplink | 80h | 06h | N/A | O | N/A |
| Counter N2 | 80h | 0Ah | N/A | O | N/A |
| Timer T1 | 80h | 09h | N/A | O | N/A |
| T-ack | 80h | 08h | N/A | O | N/A |
| Private parameters (V) |  |  |  |  |  |
| Parameter set ID | F0h | 00h | O | O | M |
| SQP | F0h | 02h | O | O | N/A |
| LCR cause | F0h | 06h | N/A | N/A | M |
| Modulation support | F0h | 81h | O | N/A | N/A |
| Private parameters (W) |  |  |  |  |  |
| Parameter set ID | F0h | 00h | M | M | O |
| Algorithm version number | F0h | 01h | O | O | O |
| Network initialization | F0h | 02h | M | M | N/A |
| Connection check | F0h | 03h | N/A | N/A | N/A |
| Version | F0h | 04h | O | O | O |
| Authentication | F0h | 05h | O | O | O |
| NM1 | F0h | 42h | N/A | O | N/A |
| RR | F0h | 43h | N/A | O | N/A |
| WR | F0h | 44h | N/A | O | N/A |
| RE | F0h | 46h | N/A | O | N/A |
| RL | F0h | 47h | N/A | O | N/A |
| Timer T3 | F0h | 48h | N/A | O | N/A |
| NL1 | F0h | 49h | N/A | O | N/A |
| Timer TL3 | F0h | 4Ah | N/A | O | N/A |
| Timer TL4 | F0h | 4Bh | N/A | O | N/A |
| WE | F0h | 4Ch | N/A | O | N/A |
| Operative_GNIp | F0h | 4Fh | O | O | N/A |
| Aircraft_TMbB | F0h | 50h | O | O | N/A |
| MbB_Operations_Permitted | F0h | 51h | O | O | N/A |
| CT1 | F0h | 52h | O | O | O |
| Timer CT2 | F0h | 53h | O | O | O |
| Timer CT3 | F0h | 54h | O | O | O |
| GDTE | F0h | 55h | N/A | O | N/A |
| VER | F0h | 56h | O | O | O |
| M-BIT | F0h | 57h | O | O | O |
| Expedited recovery | F0h | 80h | O | N/A | N/A |
| t | F0h | 81h | O | N/A | N/A |
| f | F0h | 82h | O | N/A | N/A |
| Former_GNIp | F0h | 83h | O | O | N/A |
| ADSA | F0h | 84h | O | N/A | N/A |
| Counter NL2 | F0h | C1h | N/A | O | N/A |

Key for Table 5-59a above:

Abbreviations used:

GI	= ISO 8885 Group Identifier

PI	= ISO 8885 Parameter Identifier

M	= Mandatory

O	= Optional

N/A	= Not applicable

h	= hexadecimal

Table 5-59b. XID Parameters

|  |  | Addressed link parameter modification | Broadcast link parameter modification |
| --- | --- | --- | --- |
|  | Source | Current ground station | Aircraft | Current ground station |
|  | Destination | Aircraft | Current ground Station | Aircraft |
| XID parameters | GI | PI | CTRL_CMD_LPM | CTRL_RSP_LPM | CTRL_CMD_LPM (GSIF) |
| Public parameters (8885:1993:Mode3) |  |  |  |  |  |
| Parameter set ID | 80h | 01h | O | N/A | O |
| N1-downlink | 80h | 05h | O | N/A | O |
| N1-uplink | 80h | 06h | O | N/A | O |
| Counter N2 | 80h | 0Ah | O | N/A | O |
| Timer T1 | 80h | 09h | O | N/A | O |
| T-ack | 80h | 08h | N/A | 0 | N/A |
| Private parameters (V) |  |  |  |  |  |
| Parameter set ID | F0h | 00h | O | O | O |
| SQP | F0h | 02h | O | O | O |
| LCR cause | F0h | 06h | N/A | N/A | N/A |
| Modulation support | F0h | 81h | N/A | N/A | N/A |
| Private parameters (W) |  |  |  |  |  |
| Parameter set ID | F0h | 00h | O | O | O |
| Algorithm version number | F0h | 01h | O | N/A | O |
| Network initialization | F0h | 02h | O | O | O |
| Connection check | F0h | 03h | O | O | O |
| Version | F0h | 04h | N/A | N/A | O |
| Authentication | F0h | 05h | O | O | O |
| NM1 | F0h | 42h | O | N/A | O |
| RR | F0h | 43h | O | N/A | O |
| WR | F0h | 44h | O | N/A | O |
| RE | F0h | 46h | O | N/A | O |
| RL | F0h | 47h | O | N/A | O |
| Timer T3 | F0h | 48h | O | N/A | O |
| NL1 | F0h | 49h | O | N/A | O |
| Timer TL3 | F0h | 4Ah | O | N/A | O |
| Timer TL4 | F0h | 4Bh | O | N/A | O |
| WE | F0h | 4Ch | O | N/A | O |
| Operative_GNIp | F0h | 4Fh | O | O | O |
| Aircraft_TMbB | F0h | 50h | O | O | O |
| MbB_Operations_Permitted | F0h | 51h | O | O | O |
| CT1 | F0h | 52h | O | O | O |
| Timer CT2 | F0h | 53h | O | O | O |
| Timer CT3 | F0h | 54h | O | O | O |
| GDTE | F0h | 55h | O | N/A | O |
| VER | F0h | 56h | N/A | N/A | O |
| M-BIT | F0h | 57h | O | O | O |
| Expedited recovery | F0h | 80h | N/A | N/A | N/A |
| t | F0h | 81h | O | N/A | O |
| f | F0h | 82h | O | N/A | O |
| Former_GNIp | F0h | 83h | O | O | O |
| ADSA | F0h | 84h | N/A | O | N/A |
| Counter NL2 | F0h | C1h | O | N/A | O |

Key for Table 5-59b above:

Abbreviations used:

GI	= ISO 8885 Group Identifier

PI	= ISO 8885 Parameter Identifier

M	= Mandatory

O	= Optional

N/A	= Not applicable

h	= hexadecimal

| Table 5-60a. LME System Parameters |
| --- |
| Symbol | Parameter Name | Minimum | Maximum | Mode 3 Default | Increment |
| WE | Net Entry Request Delay (MAC cycle) | 1 | 256 | See Table 5-60b | 1 |
| NL1 (air) | Maximum net entry request retry | 1 | 128 | 20 | 1 |
| NL2 (gnd) | Polling reply counter | 1 | 255 | 3 | 1 |
| TL3 | Disconnect delay timer | 5 s | 30 s | 10 s | 1 s |
| TL4 (air) | Polling interval (MAC cycles) | 1 | 300 | 120 | 1 |

Table 5-60b. WE Parameter Default Values

|  |  | System Configuration |
| --- | --- | --- |
| Symbol | Parameter Name | 4V | 3V1D | 2V2D | 3T | 3V | 2V1D | 3S | 2S1X |
| WE | Net Entry Request Delay (MAC cycle) | 1 | 2 | 2 | 2 | 1 | 2 | 1 | 1 |

Table 5-65b.  Vocoder Algorithm Version Encoding

| Bit # | Algorithm Version |
| --- | --- |
| 1 | AMBE-ATC-10 or equivalent vocoder |
| 2 | Not currently specified |
| 3 | Not currently specified |
| 4 | Not currently specified |
| 5 | Not currently specified |
| 6 | Not currently specified |
| 7 | Not currently specified |
| 8 | Not currently specified |

Table 5-66b.  Network Type Values

| Network Type | Protocol |
| --- | --- |
| 0000 0000 | ATN/ISO8208/VDL Mode 3 PLP Compression |
| 0000 0001 | ATN/ISO8473/ISO9542/VDL Mode 3 CLNP Compression |
| 0000 0010 | ATN/ISO8208 (No Subnetwork Compression) |
| 0000 0011 | ATN/ISO8473/ISO9542 (No Subnetwork Compression) |
| 0000 0100 | Raw/VDL |
| 0000 0101 to 1111 1111 | Reserved |

| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Type-specific Info | Type |

| BIT | PROTOCOL |
| --- | --- |
| 0000 | ISO8208 |
| 0001 | ISO8473/ISO9542 |
| 0010 | Raw |
| 0011 - 1111 | Reserved |

Figure 6-1.    Payload octet

B.2.1.3  Voice signal.  The Voice Signal field is used by the ground station to maintain a degree of control over the voice channel.  The valid codes are listed in Table B-3 below.

Table B-3.  Voice Signal Codes

| Code | Description |
| --- | --- |
| 00 | Ground access (clears mobiles off) |
| 01 | Occupied |
| 10 | Voice channel idle |
| 11 | Spare |

B.2.2.1  Reservation response.  Each Reservation Response field contains three subfields as follows:

- Group ID (2 bits):  The Group ID is coded identically as the Slot ID (Section B.2.1.5).  In this case it is used in conjunction with the Aircraft ID (listed below) to uniquely identify the aircraft across all user groups supported on the frequency by the ground station.

Note.( The Group ID and the Aircraft ID fields are collectively referred to as the Local User ID.

- Aircraft ID (6 bits):  Section B.2.1.4 defines the valid codes.  When the Reservation Response field is not used, the value of 0 shall be used in the Aircraft ID field.

- Reserved Slot (4 bits):  This subfield indicates the slot for which V/D (data) burst access has been scheduled to begin.  This subfield is coded as indicated below:

Table B-6  Reserved Slot Subfield Encoding

| Code | Description |
| --- | --- |
| 0000 | No Reservation Information |
| 0001 | RACK |
| 0010 | Spare |
| 0011 | Spare |
| 0100 | Data Reservation (start in even B-slot) |
| 0101 | Data Reservation (start in odd B-slot) |
| 0110 | Data Reservation (start in even B-slot, skip D) |
| 0111 | Data Reservation (start in odd B-slot, skip D) |
| 1000 | Data Reservation (start in even C-slot) |
| 1001 | Data Reservation (start in odd C-slot) |
| 1010 | Data Reservation (start in even C-slot, skip D) |
| 1011 | Data Reservation (start in odd C-slot, skip D) |
| 1100 | Data Reservation (start in even D-slot) |
| 1101 | Data Reservation (start in odd D-slot) |
| 1110 | Voice Reservation (start in even D-slot) |
| 1111 | Voice Reservation (start in odd D-slot) |

Note:  For non-3T configurations, use only the codes with the third bit set to 0.  For system configuration 2V2D, allowable values are 0000, 0001, 1000, 1001, 1100, and 1101.  For system configuration 3V1D, allowable values are 0000, 0001, 1100, and 1101.  For system configuration 2V1D, allowable values are 0000, 0001, 1000, and 1001.

B.2.10.3  Voice request.  The Voice Request field is a 2 bit field.  The valid codes are listed as follow:

Table B-8  Voice Request Field

| Code | Description |
| --- | --- |
| 00 | No request |
| 01 | Request routine access |
| 10 | Request priority access |
| 11 | Spare |

The most significant bit shall be sent in octet 2 while the least significant bit shall be sent in octet 3, as shown in Figure B-9.

Appendix D - Random Access Downlink M Burst Selection Algorithms for Aircraft Radio

Retransmission

Step 5.  If a valid response is not received by LBACy in MAC cycle Z + Wn, where Z and Wn are defined in Step 4, the Net Entry or Reservation Request message shall be retransmitted by repeating the above procedures beginning in Step 2.

Note 1.— The available LBACs depend on process type (Net Entry, Reservation Request, or Leave Net) and configuration.  LBACs scheduled for Poll Responses and downlink ACKs are removed from the lists.  The initial list includes all downlink M burst LBACs available to the relevant net.

Note 2.— Steps 4 and 5 are not applicable to Leaving Net since a Leaving Net message requires no reply.

Note 3.— Failure to detect a downlink V/D (data) burst with an EOM indication may cause a aircraft VDL to transmit in an uplink RA M channel, which has been reserved for downlink ACK for another aircraft and corrupt the downlink ACK transmission.  Duplicate messages will occur as a result.

E.2.1.1  General.   The interface between the XNI DCE and ATN Router DTE(s) shall conform to the ISO 8208 packet layer protocol.  Accordingly, the XNI shall contain an ISO 8208 DCE.

Note.(   The ATN router contains a DTE.

E.2.2.2  Mobile DTE Address

The mobile DTE address shall have a total length of 10 BCD digits, as follows:

X0 X1 X2 X3 X4 X5 X6 X7 X8 X9	(X0 shall be the most significant digit)

The digits X0 to X7 shall contain the ICAO 24 bit aircraft address coded in BCD. The digits X8 X9 received as XID parameter ADSA (Section E.10.1) shall identify a sub-address for a specific DTE onboard an aircraft.  This sub-address shall be in the range of 0 through 15.  The following sub-address assignments shall be used:

00		ATN router

01 to 15		Unassigned

E.4.1  State transitions

The DCE shall operate as a state machine with the states as identified in Table E.4-1.  Upon entering a state, the DCE shall perform the actions specified in Table E.6-1.  If a state transition is specified, the actions taken shall be as specified in Tables E.11-1 through Table E.11-10.

E.5.1.3  Processing of M-Bit sequences

Note.(   M-bit processing is used for the orderly sequencing of reformatted DATA Packets.

E.5.2.1.1.1  General.  Reception by the ANI internetworking process of an ISO 8208 CALL REQUEST Packet from the local DCE shall result in the generation of a corresponding VDL Mode 3 CALL REQUEST by the ANI Packet as specified in Table E.5-1:

Table E.5-1:  VDL Mode 3 Call Request packet

| MSB | Bit Number | LSB |
| --- | --- | --- |
| Octet | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
| 1 | DP | VP | SP | ST | FILL |
| 2 | P | FILL | SN |
| 3 | CH | AM |
| 4 | AG |
| 5 | FS | FILL |
| 6 + n | FDv |

In formatting the VDL Mode 3 packet the information shall be derived as follows.

E.5.2.1.1.3  VDL Supervisory Packet (VSP) packet type (VP).  This field shall be set to 1.

E.5.2.1.1.10  Address, ground (AG).  This address shall be the ground DTE address in the range of 0 to 255.  The address is obtained as part of the link initialization procedure as defined in Section E.10.2.

E.5.2.1.2.1  General.  Reception by the GNI internetworking process of a VDL Mode 3 CALL REQUEST by ADLP Packet from the GDCE shall result in the generation of a corresponding ISO 8208 CALL REQUEST Packet to the local DCE.  The translation from the VDL Mode 3 packet to the ISO 8208 packet shall be the reverse of the processing specified in Section E.5.2.1.1 with the exceptions as specified in the following paragraph.

E.5.2.2.1.1  General.  Reception by the GNI internetworking process of an ISO 8208 CALL REQUEST Packet from the local DCE shall result in the generation of a corresponding VDL Mode 3 CALL REQUEST by GNI Packet(s) as specified in Table E.5-2.

Table E.5-2:  VDL Mode 3 CALL REQUEST Packet

| MSB | Bit Number | LSB |
| --- | --- | --- |
| Octet | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
| 1 | DP | VP | SP | ST | FILL |
| 2 | P | FILL | SN |
| 3 | FILL | TC | AM |
| 4 | AG |
| 5 | FS | FILL |
| 6 + n | FDv |

Fields shown in the packet format and not specified in the following paragraphs shall be set as specified in E.5.2.1.

E.5.2.2.1.6  Temporary channel number field (TC).  This field shall be used to distinguish multiple call request from a GNI.  The ANI internetworking process, upon receipt of a temporary channel number, shall assign a channel number from those presently in the Ready State, p1.

E.5.2.2.2.1  General.  Reception by the ANI internetworking process of a VDL Mode 3 CALL REQUEST by GNI Packet from the ADCE shall result in the generation of a corresponding ISO 8208 CALL REQUEST Packet to the local DCE.  The translation from the VDL Mode 3 packet to the ISO 8208 packet shall be the reverse of the processing defined in E.5.2.2.1 with the exceptions as specified in the following paragraph.

E.5.2.3.1.1  General.  Reception by the ANI Internetworking process of an ISO 8208 CALL ACCEPT Packet from the local DCE shall result in the generation of a corresponding VDL Mode 3 CALL ACCEPT by ANI Packet as specified in Table E.5-3.

Table E.5-3:  VDL Mode 3 CALL ACCEPT Packet

| MSB | Bit Number | LSB |
| --- | --- | --- |
| Octet | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
| 1 | DP | VP | SP | ST | FILL |
| 2 | TC | SN |
| 3 | CH | AM |
| 4 | AG |
| 5 + n | FDv |

Fields shown in the packet format and not specified in the following paragraphs shall be set as specified in E.5.2.1

E.5.2.3.2.1  General.  Reception by the GNI Internetworking process of a VDL Mode 3 CALL ACCEPT by ANI Packet from the GDCE shall result in the generation of a corresponding ISO 8208 CALL ACCEPT Packet to the local DCE.  The translation from the VDL Mode 3 packet to the ISO 8208 packet shall be the reverse of the processing defined in the following paragraph.

E.5.2.4.1.1  General.  Reception by the GNI Internetworking Process of an ISO 8208 CALL ACCEPT Packet from the local DCE shall result in the generation of a corresponding VDL Mode 3 CALL ACCEPT by GNI Packet as specified in Table E.5-4.

Table E.5-4:  VDL Mode 3 CALL ACCEPT Packet

| MSB | Bit Number | LSB |
| --- | --- | --- |
| Octet | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
| 1 | DP | VP | SP | ST | FILL |
| 2 | FILL | SN |
| 3 | CH | AM |
| 4 | AG |
| 5 + n | FDv |

Fields shown in the packet format and not specified in the following paragraphs shall be set as specified in E.5.2.1

E.5.2.4.2.1  General.  Reception by the ANI internetworking Process of a VDL Mode 3 CALL ACCEPT by GNI Packet from the ADCE shall result in the generation of a corresponding ISO 8208 CALL ACCEPT Packet to the local DCE.  The translation from the VDL Mode 3 packet to the ISO 8208 packet shall be the reverse of the processing defined in E.5.2.4.1 with the exceptions as specified in the following paragraph.

E.5.2.5.1.1  General. Reception by the ANI Intertworking Process of an ISO 8208 CLEAR REQUEST Packet from the local DCE shall result in the generation of a corresponding VDL Mode 3 CLEAR REQUEST by ANI Packet as specified in Table E.5-5

Table E.5-5:  VDL Mode 3 CLEAR REQUEST Packet

| MSB | Bit Number | LSB |
| --- | --- | --- |
| Octet | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
| 1 | DP | VP | SP | ST | FILL |
| 2 | TC | SN |
| 3 | CH | AM |
| 4 | AG |
| 5 | CC |
| 6 | DC |
| 7 + n | FDv |

Fields shown in the packet format and not specified in the following paragraphs shall be set as specified in E.5.2.1 and E.5.2.2.

E.5.2.5.2.1  General.  Reception by the GNI Internetworking Process of a VDL Mode 3 CLEAR REQUEST by ANI Packet from the local GDCE shall result in the generation of a corresponding ISO 8208 CLEAR REQUEST Packet to the local DCE.  The translation from the VDL Mode 3 packet to the ISO 8208 packet shall be the reverse of the processing defined in E.5.2.5.1.

E.5.2.6.1.1  General.  Reception by the GNI internetworking process of an ISO 8208 CLEAR REQUEST Packet from the local DCE shall result in the generation of a corresponding VDL Mode 3 CLEAR REQUEST by GNI Packet as specified in Table E.5-6.

Table E.5-6:  VDL Mode 3 CLEAR REQUEST Packet

| MSB | Bit Number | LSB |
| --- | --- | --- |
| Octet | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
| 1 | DP | VP | SP | ST | FILL |
| 2 | TC | SN |
| 3 | CH | AM |
| 4 | AG |
| 5 | CC |
| 6 | DC |
| 7 + n | FDv |

Fields shown in the packet format and not specified in the following paragraphs shall be set as specified in E.5.2.1 and E.5.2.2.

E.5.2.6.2.1  General.  Reception by the ANI Intenetworking Process of a VDL Mode 3 CLEAR REQUEST by GNI Packet from the local ADCE shall result in the generation of a corresponding ISO 8208 CLEAR REQUEST Packet to the local DCE.  The translation from the VDL Mode 3 packet to the ISO 8208 packet shall be the reverse of processing defined in E.5.2.6.1.

E.5.2.7.1.1  General.  Reception by the XNI internetworking process of ISO 8208 DATA Packet(s) from the local DCE shall result in the generation of corresponding VDL Mode 3 DATA Packet(s) as specified in Table E.5-7.

Table E.5-7:  VDL Mode 3 DATA Packet

| MSB | Bit Number | LSB |
| --- | --- | --- |
| Octet | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
| 1 | DP | M | SN |
| 2 | PS | PR |
| 3 | CH | FILL |
| 4 + n | DATAv |

E.5.2.7.1.2  Data packet type (DP).  This field shall be set to 1.

E.5.2.7.1.3  M field (M). A value of ONE shall indicate that the packet is part of an M-bit sequence with more packets in the sequence to follow.  A value of ZERO shall indicate that the sequence ends with this packet.  The appropriate value shall be placed in the M-bit Field of the VDL Mode 3 Packet.

E.5.2.7.2  Translation into ISO 8208 packets.  Reception by the XNI Internetworking Process of VDL Mode 3 DATA Packets from the local XDCE shall result in the generation of corresponding ISO 8208 DATA Packet(s) to the local DCE.  The translation from VDL Mode 3 packet(s) to the ISO 8208 packet(s) shall be the reverse of the processing defined in E.5.2.7.1.

E.5.2.8.1.1  General.  Reception by the XNI Internetworking Process of an ISO 8208 INTERRUPT Packet from the local DCE shall result in the generation of a corresponding VDL Mode 3 INTERRUPT Packet as specified in Table E.5-8.

Table E.5-8:  VDL Mode 3 INTERRUPT Packet

| MSB | Bit Number | LSB |
| --- | --- | --- |
| Octet | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
| 1 | DP | VP | SP | ST | FILL |
| 2 | FILL | SN |
| 3 | CH | FILL |
| 4+n | UDv |

Fields shown in the packet format and not specified in the following paragraphs shall be set as specified in E.5.2.1.

E.5.2.8.2  Translation into ISO 8208 packets.  Reception by the XNI Internetworking process of a VDL Mode 3 INTERRUPT Packet from the local XDCE shall result in the generation of a corresponding ISO 8208 INTERRUPT Packet to the local DCE.   The translation from the VDL Mode 3 packet to the ISO 8208 packet shall be the reverse of the processing defined in E.5.2.8.1.

E.5.2.9.1.1  General.  Reception by the XNI Internetworking Process of an ISO 8208 INTERRUPT CONFIRMATION Packet from the local DCE shall result in the generation of a corresponding VDL Mode 3 INTERRUPT CONFIRMATION Packet as specified in Table E.5-9.

Table E.5-9:  VDL Mode 3 INTERRUPT Packet

| MSB | Bit Number | LSB |
| --- | --- | --- |
| Octet | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
| 1 | DP | VP | SP | ST | SS |
| 2 | FILL | SN |
| 3 | CH | FILL |

Fields shown in the packet format and not specified in the following paragraphs shall be set as specified in E.5.2.1.

E.5.2.9.2  Translation into ISO 8208 packets.  Reception by the XNI Internetworking process of a VDL Mode 3 INTERRUPT CONFIRMATION Packet from the local XDCE shall result in the generation of a corresponding ISO 8208 INTERRUPT CONFIRMATION Packet to the local DCE.   The translation from the VDL Mode 3 packet to the ISO 8208 packet shall be the reverse of the processing defined in E.5.2.9.1.

E.5.2.10.1.1  General.  Reception by the XNI Internetworking Process of an ISO 8208 RESET REQUEST Packet from the local DCE shall result in the generation of a corresponding VDL Mode 3 RESET REQUEST Packet as specified in Table E.5-10.

Table E.5-10:  VDL Mode 3 RESET REQUEST Packet

| MSB | Bit Number | LSB |
| --- | --- | --- |
| Octet | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
| 1 | DP | VP | SP | ST | FILL |
| 2 | FILL | SN |
| 3 | CH | FILL |
| 4 | RC |
| 5 | DC |

Fields shown in the packet format and not specified in the following paragraphs shall be set as specified in E.5.2.1.

E.5.2.10.2  Translation into ISO 8208 packets.  Reception by the XNI Internetworking process of a VDL Mode 3 RESET REQUEST Packet from the local XDCE shall result in the generation of a corresponding ISO 8208 RESET REQUEST Packet to the local DCE.   The translation from the VDL Mode 3 packet to the ISO 8208 packet shall be the reverse of the processing defined in E.5.2.10.1.

E.5.3.1.1  General.  The VDL Mode 3 RECEIVE READY Packet arriving from the XNI is not related to the control of the DTE/DCE interface and shall not cause the generation of an ISO 8208 packet.  The format of this packet shall be as specified in Table E.5-11.

Table E.5-11:  VDL Mode 3 RECEIVE READY Packet

| MSB | Bit Number | LSB |
| --- | --- | --- |
| Octet | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
| 1 | DP | VP | SP | ST | FILL |
| 2 | FILL | SN |
| 3 | CH | PR |

Fields shown in the packet format and not specified in the following paragraphs shall be set as specified in E.5.2.1.  The packet shall be processed as specified in E.6.5.

E.5.3.2.1  General.  The VDL Mode 3 RECEIVE NOT READY Packet arriving from the XNI is not related to the control of the DTE/DCE interface and shall not cause the generation of an ISO 8208 packet.  The format of this packet shall be as specified in Table E.5-12.

Table E.5-12:  VDL Mode 3 RECEIVE NOT READY Packet

| MSB | Bit Number | LSB |
| --- | --- | --- |
| Octet | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
| 1 | DP | VP | SP | ST | FILL |
| 2 | FILL | SN |
| 3 | CH | PR |

Fields shown in the packet format and not specified in the following paragraphs shall be set as specified in E.5.2.1.  The packet shall be processed as specified in E.6.6.

E.5.3.3.1  General. The format of this packet shall be as specified in Table E.5-13.

Table E.5-13:  VDL Mode 3 CLEAR CONFIRMATION Packet

| MSB | Bit Number | LSB |
| --- | --- | --- |
| Octet | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
| 1 | DP | VP | SP | ST | FILL |
| 2 | TC | SN |
| 3 | CH | AM |
| 4 | AG |

Fields shown in the packet format and not specified in the following paragraphs shall be set as specified in E.5.2.1 and E.5.2.5.  The packet shall be processed as specified in E.6.3.

E.5.3.4.1  General. The format of this packet shall be as specified in Table E.5-14.

Table E.5-14:  VDL Mode 3 RESET CONFIRMATION Packet

| MSB | Bit Number | LSB |
| --- | --- | --- |
| Octet | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
| 1 | DP | VP | SP | ST | FILL |
| 2 | FILL | SN |
| 3 | CH | FILL |

Fields shown in the packet format and not specified in the following paragraphs shall be set as specified in E.5.2.1.  The packet shall be processed as specified in E.6.7.

E.5.3.5.1  General. The format of this packet shall be as specified in Table E.5-15.

Table E.5-15:  VDL Mode 3 REJECT Packet

| MSB | Bit Number | LSB |
| --- | --- | --- |
| Octet | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
| 1 | DP | VP | SP | ST | SS |
| 2 | FILL | SN |
| 3 | CH | PR |

Fields shown in the packet format and not specified in the following paragraphs shall be set as specified in E.5.2.1.  The packet shall be processed as specified in E.6.8.

E.6.4.4.5  Next in sequence, within the window.  When the sequence number (PS) of the packet received is next in sequence and within the window, the XDCE shall accept this packet.  Receipt of a packet shall be considered an error if it contains a sequence number (PS)

- outside the window, or

- out of sequence, or

- not equal to zero for the first data packet after entering Flow control Ready state

E.7.2.1  Multiplexing header.   The header for the multiplexed packets

shall be as specified in Table E-7.1.

Table E.7-1:  Multiplexing Header Packet Structure

| MSB | Bit Number | LSB |
| --- | --- | --- |
| Octet | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
| 1 | DP | VP | SP | ST | FILL |

Where,

Data packet type (DP) = 0

VSP Packet type (VP) = 1

Supervisory packet (SP) = 3

Supervisory type (ST) = 2

E.8.1  Ground subnetwork address – DTE address correlation

The ANI shall construct and manage a VDL Mode 3 Ground Subnetwork Address – DTE cross reference table whose entries are the VDL Mode 3 data link Ground Subnetwork Address and the ground DTE address associated with the ground ATN router.  This table is used to maintain the connection context to associate link layer PDUs with the appropriate SVC, as well as providing a means to maintain a connection through an old SVC while establishing a new SVC during handoff.  Each entry of the cross reference table shall consist of the 6 bit Ground Subnetwork Address and the 8 bit binary representation of the Ground DTE.

Table E.10-1 ADSA Parameter

Parameter ID			1 0 0 0	0 1 0 0	ADSA parameter

Parameter Length			0 0 0 0	0 0 0 1

Parameter Value			v8v7v6v5	v4v3v2v1

Table E.10-2 GDTE Parameter

Parameter ID			0 1 0 1	0 1 0 1	GDTE parameter

Parameter Length			0 0 0 0	0 0 0 1

Parameter Value			v8v7v6v5	v4v3v2v1

Table E.10-3 VER Parameter

Parameter ID			0 1 0 1	0 1 1 0	VER parameter

Parameter Length			0 0 0 0	0 0 0 1

Parameter Value			v8v7v6v5	v4v3v2v1

Table E.10-4 MBIT Parameter

Parameter ID		0 1 0 1		0 1 1 1	M-BIT parameter

Parameter Length		0 0 0 0		0 0 1 0

Parameter Value		v16v15v14v13	v12v11v10v09

V08v07v06v05	v04v03v02v01

F.1.1.8  Bit field.  The Bit Field, as well as the Q bit of Section F.1.1.3, shall be as defined in Figure F-4.

| Bit | Meaning (Present == 1) |
| --- | --- |
| Q | QOS Options Present |
| S | SP flag of CLNP Header - Data Unit Identifier Present |
| E | Compliment of CLNP Error Flag (ER) flag |
| M | More Segments (MS) bit of CLNP Header |
| T | Sequence vs. Transit Delay Bit (from QOS Option) |
| H | Lifetime Field present (Hop Count) |
| O | Segment Offset Present |
| L | Total Length field present |
| D | Type of PDU (Error = 1, Data = 0) |

##### Figure  F-4.  Bit Field Definitions

F.1.1.11  Segment Offset.  The Segment Offset shall be sent whenever the Segmentation Permitted (SP) bit is set and the Segment Offset is greater than zero. The presence of the Segment Offset field shall be indicated by the O bit.

F.1.2.3  Restart Packets  On reception of a restart packet all index numbers that have been assigned by the receiving entity, and the information referenced by the index numbers, (e.g., NSAP pair) shall be deleted. For a ground VDL Mode 3 installation deletion shall be restricted to the index information associated with the aircraft originating the restart packet.

Note.(  A compressor has two sets of index numbers. Those assigned by the compressor and those assigned by its peer. Reception of a restart packet only applies to the index numbers used for decompressing, i.e., the index numbers assigned by the remote peer.

F.2   Compression rules

Note.(  The following compression and decompression rules are for both the air and ground VDL Mode 3 equipment.  It is assumed that both require broadcast compression (although the usefulness of aircraft VDL Mode 3 broadcasting has yet to be determined).

- If the CLNP version field is not 1, the packet shall be sent as TYPE_CLNP.

- If the CLNP packet is of any type other than Data or Error, the packet shall be sent as TYPE_CLNP.

Note.(  It has now been determined that this packet is suitable for compression.

- If the NSAP pair has not been associated with an index number, the CLNP packet shall be sent as TYPE_UNCOMPRESSED_CLNP.

- If the link is simplex, the packet is not TYPE_MULTICAST, and the last CT1 (System Parameter) packets for this index/pair association have been sent as compressed type, or CT2 (system parameter) seconds have passed since the last packet with this index number has been sent, the packet shall be sent as TYPE_UNCOMPRESSED_CLNP.

- If the security option is not coded as specified for ATN traffic, the CLNP packet shall be sent as TYPE_COMPRESSED_CLNP_LONG_WITH_OPTIONS.  The security and other non-compressed options shall be copied into the options portion of the compressed header.

- If the priority option is present with a value greater than 14, the CLNP packet shall be sent as TYPE_COMPRESSED_CLNP_LONG_WITH_OPTIONS.  The priority and other non-compressed options shall be copied into the options portion of the compressed header.

- If the CLNP packet SP bit is zero, the lifetime field has a value of greater than hexadecimal 1c on downlinks or is less than 5 on uplinks, the S/T bit is not set, the packet type is DT, the ER bit is non-zero, and no options are present other than security, QOS, Security, or Priority, the packet shall be sent as TYPE_COMPRESSED_SHORT.

Note 1.(  Many CLNP installations include the segment information fields even when the packet is unsegmented. It is thus necessary to check for this condition.

Note 2.(  At this point, the packet compression type must be long.

- If a CLNP option is present which is not QOS, security, priority, or padding, the packet shall be sent as TYPE_COMPRESSED_CLNP_LONG_WITH_OPTIONS. The options shall be copied into the options portion of the compressed header.

- Otherwise the packet shall be sent as TYPE_COMPRESSED_CLNP_LONG_NO_OPTIONS

- For the compressed long packets, the Lifetime field shall be included when its value is greater than 5, or less than hexadecimal 1d.  The DUI field shall be included when the packet is segmented.  The Segment Offset field shall be included when it is non-zero and the SP bit from the CLNP header is set.  The Total Length field shall be included if this is the first time this DUI is being compressed.  The Options fields that are not QOS, priority, security, or padding shall be included unmodified.  The T, M, and S fields shall be set to the corresponding values of the S/T, MS and SP values in the original packet. The E fields shall be set to the inverse (complement) of the ER value. The Discard Reason field shall be set if the packet is an Error PDU.

###### Table F-1 CT1 Parameter

Parameter ID	0  1  0  1       0  0  1  0	Multicast Packet Period

Parameter Length	0  0  0  0       0  0  0  1

Parameter Value	v8 v7 v6 v5     v4 v3 v2 v1

###### Table F-2 CT2 Timer

Parameter ID		0    1   0    1       0   0   1   1	Multicast Refresh Timer

Parameter Length		0    0   0    0       0   0   1   0

Parameter Value		v16 v15 v14 v13     v12 v11 v10 v9

v8  v7  v6   v5      v4  v3  v2  v1

###### Table F-3 CT3 Timer

Parameter ID		0    1   0    1       0   1    0   0	Index Idle Timer

Parameter Length		0    0   0    0       0   0    0   1

Parameter Value		v16 v15 v14 v13     v12 v11 v10 v9

v8  v7  v6   v5      v4  v3  v2  v1