AERONAUTICAL MOBILE COMMUNICATIONS PANEL (AMCP)

WORKING GROUP M, FIRST MEETING

Malmö, 12-19 December 2000

Agenda Item 8:	VDL Mode 4 Manual Progress and Configuration Control Procedures

VDL Mode 4 VSG Activites Since AMCP/7

(Presented by Larry Johnsson)

Summary This paper provides information about the changes introduced into the VDL Mode 4 Manual on Detailed Technical Specifications by the Validation Sub Group Since AMCP/7.

1.	INTRODUCTION

The following notes summarise the updates made to the VDL Mode 4 Manual on Detailed Technical Specifications since AMCP/7.  The changes have been discussed and approved by the VDL Mode 4 validation sub-group during two meetings.  The notes should be read in conjunction with a revision marked copy of the VDL Mode 4 Manual on Detailed Technical Specifications.  The baseline version (ie the one into which red-line changes have been made) is AMCP/7-WP/81.

VSG will deliver the VDL Mode 4 	Manual on Detailed Technical Specifications and the VDL Mode 4 Implementation Manual to the ICAO Secretariat together with this WP summarising the changes introduced.

2.	LIST OF CHANGES

1.1.3:  Definitions removed from SARPs have been added to this section of the TM.

1.1.3:  Tables have been updated with new parameters and symbols introduced as a result of changes elsewhere in the TM.

Table 1-3:  Specific reference to GFSK has been removed since GFSK is now the only modulation scheme supported by Mode 4

1.2.3.2/1.2.3.4:  Movement of one paragraph because it fits better in 1.2.3.4.

1.2.4/1.3.5/1.3.6.2.3:  Clarification of references to VDL SARPs

General: Correction of typos resulting from transcription to WordPerfect.

1.3.2:  Reference to missing figure in note removed. Introduced TCP change flag.

1.3.6.2.2.4: Addition of a recommendation that a mobile should avoid using slots reserved for transmission by the mobile on other channels

1.3.6.3.2:  Removal of requirement which has been superseded by conflict reservation procedures

1.3.6.6:  Addition of procedures to determine what to do if a mobile is required to transmit simultaneously on more than one channel. Editorial change of “required” to “requested”.

1.3.8: Small wording change to cut down the over use of “specific”

Table 1-18: Changed strange symbol to “not equal”.

1.3.14.2.3: Replaced “. Hence” with “and” in note.

1.3.16: Replaced “desired” with “specified” rate in note.

1.3.16.1/Table 1-39/1.3.16.3.2:  Removal of parameter nsr (all equations will now use nr only)

Table 1-35:  Changed reference to Table 1-27.  Clarification of what happens when nr = special and pr_flag = 0

1.3.16.1.2:  Text clarified

Table 1-37:  Removal of most significant bit of “off” subfield which was included in error

1.3.16.5.3: Removal of duplicate requirement (says virtually the same as the first sentence in the paragraph)

Table 1-40: Rotate the descriptions “block timeout (bt)” and “block repeat rate (br)” as they were placed in wrong table cells.

Table 1-41:  Incorrect use of field “dt” replaced by “bt”

Table 1-42: Added missing description “timeout (vt)”.

Table 1-45: Changed strange symbol to “greater than or equal to”.

1.3.17.9.2:  Change of incorrect use of V66 and V67 – usage switched over

1.3.20.1:  Clarification of general response procedures

1.4.1: Added a note.

1.4.2.2.1/Table 1-56: Clarification of RTS procedures and addition of ei field

Table 1-53: Replaced the word “linear” with “integer”.

Table 1-58: Small modification of T2 value

Table 1-66:  Clarification that CPR flag applies to all encoded positions in the burst including station current position and any TCP information included in burst

1.5.3.1/Table 1-70: Addition of new fields to control XID sequences

1.5.3.2:  Further clarification of content of compressed XID burst. Change “Ox” to hex.

Table 1-81:  Correction of parameter length

Table 1-84:  Tidy up table to be consistent with other XID parameter tables

Table 1-85:  Correction: 16 DOS messages can be accommodated. Changed strange symbol to “not equal”.

Table 1-92/1.5.6.3.1.5/Table 1-94: Introduction of CG1_reach to control exposure filter

1.5.6.3.1.8: New paragraph. The following paragraph renumbered to 1.5.3.1.9.

1.5.6.3.3.2 Clarification of text.

Table 1-94: Replaced “at least” med “less than”.

1.5.8.1/1.5.8.3/Table 1-101/1.5.8.4: Introduction of new requirements to specify general response to RTX

Section 2: Editorial updates.

Table  3-2/Table 3-8:  Introduction of two slot TCP.  Note that this has entailed splitting table 3-8 into two labelled a and b.

Table 3-11 and many other places in chapters 3 and 4:  Amendment of references to the CPR section (previously section 5 and now section 4). Corrected range values that were corrupted in the transfer process. Rplaced the word “linear” with “integer”.

Table 3-21:  Correction of sleep field length

3.7.2:  Addition of new channel management XID providing a flexible method of specifying reporting rates. This also required some changes to the autotune protocol in section 1.3.16.

Section 4:  Correction of references and a few formulae incorrectly transferred to WordPerfect document

3.	ACTIONS BY THE GROUP

The meeting is invited to note the information in this paper.

- END -