Amendment Proposal

| Title: Original: AMCP WG M/-WP29 | Bit Ordering |
| --- | --- |
| AP working paper number and date | M1/WP7 12 Dec 2000 |
| Document(s) Affected: | Manual on VDL Mode 3 Technical Specifications |
| Document Version: | AMCP/7 Report AI1 Appendix B |
| Sections of Documents Affected: | B.1.2, B.2.11, Fig B-13, Fig B-14 |
| Coordinator: | Robert Morgenstern |
| Coordinator's Address: | 1820 Dolley Madison Blvd, M/S W387 McLean, VA 22102 USA |
| Coordinator's Phone: | +1 703 883 7846 |
| Coordinator's Fax: | +1 703 883 1367 |
| Coordinator's E-mail Address: | rmorgens@mitre.org |
| Category: | CRITICAL |
| Problem description: | Incompatible bit ordering between Tech Manual, and Implementation Aspects documents and validation systems. Published MASPS document is also conflicted. |
| Background: | The definition of bit ordering was realized to be backwards after submission to AMCP/7. Validated by inspection and integration testing. |
| Backwards compatibility: | None. Critical change to prevent interoperability issues. |
| Amendment Proposal: | Bit ordering should be as defined in the Implementation Aspects due to simpler implementation and more existing implementations. See attached for specific changes to TM. |
| WG-M Status: | RESOLVED 15/12/00 |
|  | APPROVED |

The following modifications are needed in the Manual on VDL Mode 3 Technical Specifications to resolve conflicts in bit order between documents.

Modify B.1.2 as follows:

B.1.2  Bit Ordering

Bit fields in this Appendix shall be encoded such that the most significant bit is in the first bit transmitted (shown as the lowest bit number position in the figures).  For binary data listed in tables, the left-most bit shall be considered the most significant bit.  For fields that are split over a number of octets the most significant portion shall be sent in the lower numbered octets.

Modify B.2.11 as follows to correct the reference:

B.2.11  Acknowledgement message

The Acknowledgement message shown in Figure B-10, is used by the aircraft to acknowledge a V/D (data) burst sequence.

Modify Figure B-13 and B-14 as follows:

|  | first bit transmitted | Bit Number |
| --- | --- | --- |
| Octet No. | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 |
| 1 | Message ID = 0XX | Local User ID |
| 2 | Local User ID (cont.) | EOM |  |

Figure B-13.  V/D (Voice) Burst Header Segment

|  | first bit transmitted | Bit Number |
| --- | --- | --- |
| Octet No. | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 |
| 1 | Message ID = 1XX | Ground Station Code | Segment Number |
| 2 | Segment Number | Spare | EOM |  |  |  |  |

Figure B-14.  V/D (Data) Burst Header Segment