Amendment Proposal

| Title: Original: AMCP WG M/-WP35 | LREF |
| --- | --- |
| AP working paper number and date | M1/WP35 15 Dec 2000 |
| Document(s) Affected: | Manual on VDL Mode 3 Technical Specifications |
| Document Version: | AMCP/7 Report AI1 Appendix B |
| Sections of Documents Affected: | 5.7.3.3.4.1.3, 6.7.2.2, 7.2.3.2.5, Appendix F |
| Coordinator: | Robert Morgenstern |
| Coordinator's Address: | 1820 Dolley Madison Blvd, M/S W387 McLean, VA 22102 USA |
| Coordinator's Phone: | +1 703 883 7846 |
| Coordinator's Fax: | +1 703 883 1367 |
| Coordinator's E-mail Address: | rmorgens@mitre.org |
| Category: | BUG |
| Problem description: | ATNP has requested that we harmonize our CLNP header compression to the LREF standard documented in ICAO Doc 9705. Currently, their specification is such that we cannot reference it, as it requires ISO 8208 to operate. In a meeting of the ATNP Internet Draft Group, we came to an agreement that they would produce a version of the LREF documentation that could be referenced by a generic subnetwork. This has not yet occurred. When complete definition of the generic LREF, it will be analyzed for the appropriateness of referencing versus our current header compression scheme. |
| Background: | ATNP IDG and members of WG-M have met in the past to come to a common agreement for an efficient interface for the VDL Mode 3 subnetwork. It was agreed that it was desirable for the VDL Mode 3 to use the standard LREF header compression in place of a slightly modified version of it, that is currently specified in Appendix F. There are issues with the current LREF definition that tie its operation to the ISO 8208 protocol. To utilize the LREF compression for VDL Mode 3, it is necessary to have a generic definition of the LREF compression. For legacy/certification issues, ATNP needs to leave the current specifications unchanged. They have indicated that they will replicate the LREF requirements and generalize those requirements so that ANY subnetwork could reference it. Validation will be required to examine the impact of this change. |
| Backwards compatibility: | Needs to be resolved in a timely fashion to prevent interoperability problem for CLNP header compression. |
| Amendment Proposal: | Need to reference generic version of Doc 9705 Section 5.7.6.3 that ATNP will develop, if it is acceptable. Specific changes to TM pending. |
| WG-M Status: | OPEN (Pending input from ATNP) 15/12/00 |
|  | PENDING |