AMCP WGM1 - WP36

Table 2.  Format of Amendment Proposal (AP)

| Title:Original AMCP WGM/1 WP36 | VDL Mode 2 Technical Manual Amendments |
| --- | --- |
| AP working paper number and date: AP#1 | AMCP WG-M,WP22 , WP19, 12 DEC 00 |
| Document(s) affected: | Manual on VDL Mode 2 Technical Specifications, |
| Sections of Documents affected: | Table 6-52 (Table 6-3 in Technical Manual) |
| Coordinator: | Bassam Farroha |
| Coordinators address: | 2551 Riva Road, Annapolis Maryland, USA, 21401 |
| Coordinators Phone: | 410-266-2160 |
| Coordinators Fax: | 410-266-4040 |
| Coordinators e-mail address: | Bfarroha@arinc.com |
| Category: | MINOR |
| Problem description: | 8208 Timers T24 and T25 are excluded |
| Background: | These timers are described in ISO 8208. T24 and T25 can optionally be used for deadlock recovery, thus improving the robustness of the 8208 protocol. Optional use of these timers during implementation should be allowed . |
| Backwards compatibility: | There is no interoperability problem if one peer uses these timers and the other peer does not. |
| Amendment Proposal: | Add T24 and T25 timers to Table 6-52 (SARPS) (table 6-3 Technical Manual) designating them for “optional” use. Remove T24 from former exclusion Table 6-54 (SARPS) |
| WG-M status: | Open (need to submit suggested values) |
|  | Pending |

Table 6-1. Subnetwork layer service system parameters for VDL Mode 2

Symbol 	Name 				      Minimum Maximum 		Mode 2 standard

T20	RESTART REQUEST response timer 	1 s 	300 s 		180 s

T21 	CALL REQUEST response timer 	1 s 	300 s 		200 s

T22 	RESET REQUEST response timer 	1 s 	300 s 		180 s

T23 	CLEAR REQUEST response timer 	1 s 	300 s 		180 s

T24	Window Status Transmission Timer	1 s	300 s		TBD

T25	Window Rotation Timer			1 s	300 s		TBD

Table 6-3. Facilities not supported by VDL Mode 2

Facility 							ISO 8208 Section

Q-bit							 6.6

Non-receipt of window rotation information 		11.2

On line facility registration 				13.1

Extended packet seq. numbering 				13.2

D-bit modification 					13.3

Reject response timer (Timer T27) 			13.4.1

Incoming calls barred 					13.5

Outgoing calls barred 					13.6

One-way logical channel outgoing 			13.7

One-way logical channel incoming 			13.8

Default throughput classes assignment 			13.11

Throughput class negotiation 				13.13

Closed user group related facilities 			13.14

Bilateral closed user group related facilities 		13.15

Reverse charging 					13.18