AMCP WGM1 - WP38

Table 2.  Format of Amendment Proposal (AP)

| Title:Original: AMCP WGM/1 WP38 | VDL Mode 2 Technical Manual Amendments |
| --- | --- |
| AP working paper number and date:AP#3 | AMCP WG-M,WP22 , WP19, 12 DEC 00 |
| Document(s) affected: | Manual on VDL Mode 2 Technical Specifications, |
| Sections of Documents affected: | Table 6-11 (Table 5-6 in Technical Manual) |
| Coordinator: | Bassam Farroha |
| Coordinators address: | 2551 Riva Road, Annapolis Maryland, USA, 21401 |
| Coordinators Phone: | 410-266-2160 |
| Coordinators Fax: | 410-266-4040 |
| Coordinators e-mail address: | Bfarroha@arinc.com |
| Category: | EDITORIAL |
| Problem description: | HDLC Public Parameter ID has a value of 0 |
| Background: | The HDLC public parameter ID should be based on Spec. (ISO 8885, Table 1) |
| Backwards compatibility: | HDLC spec. defines a value of 1 for this parameter ID. |
| Amendment Proposal: | Change HDLC Public Parameter ID from 0 to1 |
| WG-M status: | RESOLVED |
|  | Approved |

Table 5-6. HDLC public parameter set identifier

Parameter ID 0 0 0 0 0 0 0 1 HDLC public

parameter set

Parameter length 0 0 0 0 1 0 0 1

Parameter value

0 	0 	1	 1 	1 	0 	 0	0	character `8'

0 	0 	1	 1 	1 	0	 0 	0 	character `8'

0 	0 	 l 	  l 	1	0	 0 	0 	character `8'

0 	0	1	 1	0	1	 0          1 	character `5'

0 	0 	1 	 1 	1 	0 	 1 	0	character `:'

0 	0 	1 	 1 	0 	0	 0	1 	character `1'

0 	0 	1 	 1 	1 	0 	 0 	1 	character `9'

0 	0 	1 	 1 	1 	0 	 0 	1	character `9'

0 	0 	1	 1	0 	0	 1 	1	character `3'