AMCP WGM1 - WP39

Table 2.  Format of Amendment Proposal (AP)

| Title: Original: AMCP WGM/1 WP39 | VDL Mode 2 Technical Manual Amendments |
| --- | --- |
| AP working paper number and date:AP#4 | AMCP WG-M,WP22 , WP19, 12 DEC 00 |
| Document(s) affected: | Manual on VDL Mode 2 Technical Specifications, |
| Sections of Documents affected: | Table 6.5.3.4.1 (SARPs) (Section 5.3.4.1 in Technical Manual) |
| Coordinator: | Bassam Farroha |
| Coordinators address: | 2551 Riva Road, Annapolis Maryland, USA, 21401 |
| Coordinators Phone: | 410-266-2160 |
| Coordinators Fax: | 410-266-4040 |
| Coordinators e-mail address: | Bfarroha@arinc.com |
| Category: | EDITORIAL |
| Problem description: | Timer calculation using parameter TD and there is no definition of TD, only the definition of TD99. |
| Background: | Appears to be a typographical error |
| Backwards compatibility: |  |
| Amendment Proposal: | Changer parameter TD to TD99 |
| WG-M status: | RESOLVED |
|  | Approved |

5.3.4 Data link service

system parameters for Mode 2

These parameters needed by the DLS sub-layer shall be as listed in Table 5-5 and detailed in 5.3.4.1 through

5.3.4.7. DLS parameters shall be set using XID frames.

5.3.4.1 Timer T1 (delay before retransmission). Timer T1 shall be set to the time that a DLE will wait

for an acknowledgement before retransmitting an INFO, RR (P=1), SREJ (P=1) or a FRMR frame.

The value of Timer T1 shall be computed by the following formula:

Timer T1 = T1min + 2TD99 + min(U(x),T1max)

where:

U(x) is a uniform random number generated between 0 and x;

x = T1mult* TD99 *T1exp retrans