AMCP WGM1 - WP42

Table 2.  Format of Amendment Proposal (AP)

| Title: Original: AMCP WGM/1 WP42 | VDL Mode 2 Technical Manual Amendments |
| --- | --- |
| AP working paper number and date:AP#7 | AMCP WG-M,WP22 , WP19, 12 DEC 00 |
| Document(s) affected: | Manual on VDL Mode 2 Technical Specifications, |
| Sections of Documents affected: | Section 6.6.3.2.4, (Section 6.3.2.4 in Technical Manual) |
| Coordinator: | Bassam Farroha |
| Coordinators address: | 2551 Riva Road, Annapolis Maryland, USA, 21401 |
| Coordinators Phone: | 410-266-2160 |
| Coordinators Fax: | 410-266-4040 |
| Coordinators e-mail address: | Bfarroha@arinc.com |
| Category: |  |
| Problem description: | Existing Text supports “Call Requests from the Ground”. |
| Background: | There are no Call requests from the ground. Refer to SARPs Section 6.6.6.3.2 (section 6.6.3.2 in Technical Manual) that ground can not initiate subnetwork connections. Also for resolution regarding expedited Ground Initiated HandOff, refer to ARINC 631-3 section 9.4.1.1 that modified this process to conform to the above Technical Manual explicit statement. |
| Backwards compatibility: |  |
| Amendment Proposal: | Delete references to “Call requests from the ground”. |
| WG-M status: | OPEN (requires further study. This proposal is not acceptable to ground service providers who are planning to support Ground Initiated Expedited Handoff for use in their system management) |
|  | Pending |

6.3.2.4 Ground network DTE addresses. If the ground LME indicates support of ground network DTE addresses during link establishment, it shall accept and process addresses which follow the format used in the ground network. All CALL REQUESTs from the ground shall use, as the Calling Address, the ground DTEs X.121 address.