AMCP WGM1 - WP44

Table 2.  Format of Amendment Proposal (AP)

| Title: Original: AMCP WGM/1 WP44 | VDL Mode 2 Technical Manual Amendments |
| --- | --- |
| AP working paper number and date:AP#9 | AMCP WG-M,WP22 , WP19, 12 DEC 00 |
| Document(s) affected: | Manual on VDL Mode 2 Technical Specifications, |
| Sections of Documents affected: | Section 6.5.4.4.12.3 (Section 5.4.4.12.3 in Technical Manual) |
| Coordinator: | Bassam Farroha |
| Coordinators address: | 2551 Riva Road, Annapolis Maryland, USA, 21401 |
| Coordinators Phone: | 410-266-2160 |
| Coordinators Fax: | 410-266-4040 |
| Coordinators e-mail address: | Bfarroha@arinc.com |
| Category: |  |
| Problem description: | Technical Manual does not define T3 Min as a timer but does use this timer. When to set this timer ? |
| Background: | The Technical Manual has text “If T3min expires, the responding LME shall include all responses… |
| Backwards compatibility: |  |
| Amendment Proposal: | Suggest adding the following text to SARPs Section 6.5.3.4 (Technical Manual section 5.3.4): “T3min is the acknowledgement delay for XID commands. Upon receiving an XID command, a station will transmit the XID response within the duration of timer T3min.” |
| WG-M status: | OPEN (requires further study) |
|  | Pending |

5.3.4.3 Timer T3 (link initialization time). T3min is the acknowledgement delay for XID commands. Upon receiving an XID command, a station will transmit the XID response within the duration of timer T3min.Timer T3 shall be set to the time that a DLE waits for an XID response before retransmitting an exchange identification command (XID_CMD). The period of Timer T3 shall be computed by using the same algorithm and parameters of Timer T1, except that T3min shall be separately negotiated. XID_CMDs (except for ground station information frames) shall be retransmitted using the procedures defined in 5.3.4.1.

Note 1.— There is one Timer T3 per a DLE.

Note 2.— T3min shall be greater than T1min to allow the responding entity time to co-ordinate the response and perform any additional initialization processing.