AMCP WGM1 - WP45

Table 2.  Format of Amendment Proposal (AP)

| Title: Original: AMCP WGM/1 WP45 | VDL Mode 2 Technical Manual Amendments |
| --- | --- |
| AP working paper number and date:AP#10 | AMCP WG-M,WP22 , WP19, 12 DEC 00 |
| Document(s) affected: | Manual on VDL Mode 2 Technical Specifications, |
| Sections of Documents affected: | Table 6-51a,b,c (Table 5-46 in Technical Manual) |
| Coordinator: | Bassam Farroha |
| Coordinators address: | 2551 Riva Road, Annapolis Maryland, USA, 21401 |
| Coordinators Phone: | 410-266-2160 |
| Coordinators Fax: | 410-266-4040 |
| Coordinators e-mail address: | Bfarroha@arinc.com |
| Category: |  |
| Problem description: | Public parameter set ID, Procedure class, and HDLC options are only mandatory on XID_CMD_LE and XID_RSP_LE, otherwise they are optional. |
| Background: | AEEC 631 makes these XID parameters mandatory to avoid possible interoperability problems. Take XID_CMD_HO and XID_RSP_HO as example, it cannot be assumed that the next ground station will support the same HDLC class and HDLC options as the current ground station. Therefore it is prudent to include these parameters in the negotiation to make sure both the aircraft and the ground support the same HDLC options and class. |
| Backwards compatibility: |  |
| Amendment Proposal: | Make the Public parameter set ID, Procedure class, and HDLC options mandatory in all XID |
| WG-M status: | OPEN (requires further study) |
|  | Pending |

Changes to be inserted into table 5.46b,c

(See printed version of AMCP WGM/1 WP45)