AMCP WGM1 - WP47

| Title:Original: AMCP WGM/1 WP47 | VDL Mode 2 Technical Manual Amendments |
| --- | --- |
| AP working paper number and date: AP#12 | AMCP WG-M,WP22 , WP19, 12 DEC 00 |
| Document(s) affected: | Manual on VDL Mode 2 Technical Specifications, |
| Sections of Documents affected: | Specific Requirements should be added to the VHF Management Entity (VME) section of the VDL SARPs or technical manual to support this capability. |
| Coordinator: | Damien Marce |
| Coordinators address: | Service Technique De La Navigation Aerienne, 1 AV. Du DR Maurice Grynfogel, BP1084-31035, Toulouse Cedex, France |
| Coordinators Phone: | (33) 562 14 59 24 |
| Coordinators Fax: | (33) 562 14 58 53 |
| Coordinators e-mail address: | Marce_damien@stna.dgac.fr |
| Category: |  |
| Problem description: | “Join” and “Leave” events not reported to ATN Router |
| Background: | The ATN routing process requires that the underlying sub-networks (e.g., VDL Mode 2) should report the availability status of peer ATN routing via the “join” and “leave” events. Currently, the VDL SARPs do not have this provision. The VHF ground stations broadcast the air/ground router availability information in the GSIF. Each GSIF contains ADM and optionally the ARS fields of the air/ground router NET that is reachable via that ground station. These NETs and the ground service provider ID’s should be forwarded to the ATN router IS-SME. The IS-SME is responsible for the selection of specific air/ground route based on owner preference and initiating subnetwork connection establishment. The GSIF needs to include a unique identification of each AGR to the airborne system. The a/c needs to be able to determine when handoff to a particular ground station within the domain of the same DSP will require transitioning to a different AGR. Thus simplifying the decision process and minimizing the possibility that the system will go NOCOMM. ARINC recommends the replacement of the components of the ATN NETs to include: Three Octets of the ADM Three Octets to be DSP defined to uniquely identify an AGR The new NETs should be used in the GSIF and other appropriate XID exchanges such a alternate ground station lists. Figure 5-40 shows a proposed ATN Router NET Parameter that includes the proposed fields. |
| Backwards compatibility: |  |
| Amendment Proposal: | See Attachment (Extract of WP-23, section 1.1 ARINC Response) |
| WG-M status: | OPEN (Pending further study) |
|  | Pending |

5.4.2.7.4 ATN router NETs parameter. This parameter defines a list of ATN air-ground routersidentified by the “administration identifier” (ADM) and optionally “administration region selector” (ARS) subfields of their network entity titles (NETs). It shall be encoded as per Table 5-40.

ATN NETs to include:

- Three Octets of the ADM

- Three Octets to be DSP defined to uniquely identify an AGR

Table 5-40. ATN router NETs parameter

| Parameter ID | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | ATN router NETs |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Parameter Length | n8 | n7 | n6 | n5 | n4 | n3 | n2 | n1 |  |
|  | a24 | a23 | a22 | a21 | a20 | a19 | a18 | a17 | ADM subfield |
|  | a16 | a15 | a14 | a13 | a12 | a11 | a10 | a9 |  |
|  | a8 | a7 | a6 | a5 | a4 | a3 | a2 | a1 |  |
|  | u24 | u23 | u22 | u21 | u20 | u19 | u18 | u17 | DSP Defined |
|  | u16 | u15 | u14 | u13 | u12 | u11 | u10 | u9 |  |
|  | u8 | u7 | u6 | u5 | u4 | u3 | u2 | u1 |  |