AMCP WGM1 - WP48

| Title:Original: AMCP WGM/1 WP48 | VDL Mode 2 Technical Manual Amendments |
| --- | --- |
| AP working paper number and date: AP#13 | AMCP WG-M,WP22 , WP19, 12 DEC 00 |
| Document(s) affected: | Manual on VDL Mode 2 Technical Specifications, |
| Sections of Documents affected: | General Modifications to Technical Manual |
| Coordinator: | Bassam Farroha |
| Coordinators address: | 2551 Riva Road, Annapolis Maryland, USA, 21401 |
| Coordinators Phone: | 410-266-2160 |
| Coordinators Fax: | 410-266-4040 |
| Coordinators e-mail address: | Bfarroha@arinc.com |
| Category: | TBD |
| Problem description: | Add requirement for VME to generate a handoff event to IS-SME |
| Background: | Although VDL Mode 2 subnetwork is based on ISO 8208 standard, it has unique requirements to address aircraft mobility. An enroute aircraft typically transitions through the line-of-sight coverage region of a VHF ground station within 10 to 15 minutes. This requires the VDL to reestablish air/ground connectivity seamlessly to reduce the RF overhead associated with the ATN route initiation. |
| Backwards compatibility: |  |
| Amendment Proposal: | As such the VME should generate a handoff event to the ATN IS-SME to artificially force a connection establishment without triggering the ES-IS and the IDRP routing protocols. Requirement should be added to provide this capability. |
| WG-M status: | OPEN (needs further study, additional wording will be submitted for review) |
|  | Pending |