AMCP WGM1 - WP50

| Title:Original: AMCP WGM/1 WP50 | VDL Mode 2 Technical Manual Amendments |
| --- | --- |
| AP working paper number and date: AP#15 | AMCP WG-M,WP22 , WP19, 12 DEC 00 |
| Document(s) affected: | Manual on VDL Mode 2 Technical Specifications, |
| Sections of Documents affected: | Section 6.5.4.3.1 of the VDL SARPs |
| Coordinator: | Bassam Farroha |
| Coordinators address: | 2551 Riva Road, Annapolis Maryland, USA, 21401 |
| Coordinators Phone: | 410-266-2160 |
| Coordinators Fax: | 410-266-4040 |
| Coordinators e-mail address: | Bfarroha@arinc.com |
| Category: | MINOR |
| Problem description: | The title of the TG1 timer specified in section 6.5.4.3.1 of the VDL SARPs appears to be incorrect. |
| Background: | TG1 is the minimum time an aircraft should dwell on a frequency to detect valid uplinks if it has no link established (condition (c) in section 6.5.4.3.1). If the aircraft has already received an uplink on that frequency, it may establish a new connection or continue searching (condition (a) or condition (b) in section 6.5.4.3.1). |
| Backwards compatibility: |  |
| Amendment Proposal: | The title “minimum frequency dwell time” is not appropriate for TG1. It is recommended that the word “minimum” be deleted. |
| WG-M status: | OPEN (needs more study and re-evaluation) |
|  | Pending |

5.4.3.1 Timer TG1 (minimum frequency dwell time). Timer TG1 shall be set to the minimum time (TG1) an aircraft LME dwells on a frequency while attempting to establish a link (in order to receive a valid uplink from at least one ground station). This timer shall be set by an aircraft LME (if it is not already running) when an aircraft tunes to a new frequency during a frequency search. It shall be cancelled when a valid uplink is received. On expiry of the timer the aircraft station shall: