AMCP WGM1 - WP52

| Title:Original: AMCP WGM/1 WP52 | VDL Mode 2 Technical Manual Amendments |
| --- | --- |
| AP working paper number and date: AP#17 | AMCP WG-M,WP22 , WP19, 12 DEC 00 |
| Document(s) affected: | Manual on VDL Mode 2 Technical Specifications, |
| Sections of Documents affected: | Section 6.6.6.3.1 and Section 6.6.6.1 |
| Coordinator: | Bassam Farroha |
| Coordinators address: | 2551 Riva Road, Annapolis Maryland, USA, 21401 |
| Coordinators Phone: | 410-266-2160 |
| Coordinators Fax: | 410-266-4040 |
| Coordinators e-mail address: | Bfarroha@arinc.com |
| Category: | MINOR |
| Problem description: | Remove requirement to initialize “aircraft DCE” in section 6.6.6.3.1 |
| Background: | The air/ground sub-network interface of VDL Mode 2 is DTE to DCE where the aircraft contains the DTE and the ground contains the DCE function (as per requirements specified in the VDL SARPs sections 6.6.1). Section 6.6.6.3.1 requires that the “aircraft DCE” be initialized on receipt of a valid XID_RSP_LE conflicts with section 6.6.6.1. |
| Backwards compatibility: | YES |
| Amendment Proposal: | It is recommended that the last sentence of section 6.6.6.3.1 be deleted as the airborne sub-network DTE entity will be initialized on receipt of a SN-Unitdata request from the SNDCF. |
| WG-M status: | RESOLVED |
|  | Approved |

6.6.3.1 Subnetwork entity initialization.  The ground DCE shall be initialized on receipt of a valid XID_CMD_LE.