AMCP WGM1 - WP64

| Title: Original: AMCP WGM/1 WP64 | VDL Mode 2 Technical Manual Amendments |
| --- | --- |
| AP working paper number and date: AP#19 | AMCP WG-M,WP22 , WP19, 12 DEC 00 |
| Document(s) affected: | Manual on VDL Mode 2 Technical Specifications, |
| Sections of Documents affected: | Section 6.3.2.3 of technical manual |
| Coordinator: | Bassam Farroha |
| Coordinators address: | 2551 Riva Road, Annapolis Maryland, USA, 21401 |
| Coordinators Phone: | 410-266-2160 |
| Coordinators Fax: | 410-266-4040 |
| Coordinators e-mail address: | Bfarroha@arinc.com |
| Category: | Clarification |
| Problem description: |  |
| Background: | Definition of the Router NET is ambiguous and does not agree with current implementation. |
| Backwards compatibility: |  |
| Amendment Proposal: | Text attached |
| WG-M status: | Open |
|  | Pending |

6.3.2.3 Ground DTE address. The VDL subnetwork-specific ground DTE addresses shall be the BCD encoding of the ADM, and optionally the ARS field (from the NET, as defined in the ATN Manual). It shall be sent in the Called Address Extension facility. Bit 8 of the first octet after the facility code shall be set to 1 and bit 7 shall be set to 0. The Called Address shall not be included when using VDL subnetwork-specific ground DTE addresses.

6.3.2.3.1 Since the VDL SARPs supports two addressing options at the subnetwork layer.  The default addressing is called VDL Specific DTE Addressing (VSDA) and should be supported by all VDL entities.  Optionally, VDL SARPs supports X.121 addressing.  The VSDA consists of six octets.  The first three octets of VSDA should be the same as the ATN Administration Domain Identifier (ADM) field as defined in the ATN SARPs.  The service provider assigns the second three octets of VSDA.  The service provider may use these three octets to uniquely address an air/ground router or may use them as a routing area identifier (same as the ATN ARS field specified in the ATN SARPs).  If the VSDA assigned by the DSP does not uniquely identify a specific air /ground router, then the ground system should support X.121 addressing option.