|  | International Civil Aviation Organization WORKING PAPER | ACP-WGM 10 WP-11 23/05/05 |
| --- | --- | --- |

AERONAUTICAL COMMUNICATIONS PANEL (ACP)

WORKING GROUP M-10

Montreal, Canada 23 – 26 May 2005

| Agenda Item 4: | Resolution of VDL Mode 3 amendment proposals |
| --- | --- |

(Presented by: Rob Morgenstern)

Amendment Proposal

| Title: | MASPS/MOPS Harmonization - Formats |
| --- | --- |
| AP working paper number and date | M9/WP15 5 Oct 2004 |
| Document(s) Affected: | Manual on VDL Mode 3 |
| Document Version: | ICAO Doc 9805 |
| Sections of Documents Affected: | Part I – Chapter 3 |
| Coordinator: | Robert Morgenstern |
| Coordinator's Address: | 7515 Colshire Drive, M/S N660 McLean, VA 22102 USA |
| Coordinator's Phone: | +1 703 883 7846 |
| Coordinator's Fax: | +1 703 883 1367 |
| Coordinator's E-mail Address: | rmorgens@mitre.org |
| Category: | MINOR |
| Problem description: | A number of issues were identified between MASPS RTCA DO-224A change 2 and the publication of the MOPS RTCA DO-271B. These issues include Multiple radio operation, addition of 1V3D/1V2D for surface operations, expanded addressing, support for diversity site group operations. |
| Background: | [Validation Details] During MOPS development, it was realized there was an issue when users might tune multiple radios into the same net. Also, operational issues were raised with some surface locations having upwards of 200 aircraft (Chicago O’Hare). Diversity site group issues were recognized during FAA ground system development. Validated by simulation and test. OpNet simulations used for data operation under load. MITRE, BCI/CIE, BAE, NEC, Rockwell-Collins and Honeywell equipment have been used in the testing. Rockwell-Collins and Honeywell equipment should likely be certified by the end of the calendar year. The R-C equipment will furthermore have an STC for equipage on 737-600/700/800. |
| Backwards compatibility: | There are interoperability issues for all system configurations but 4V and 3V1D due to the restructuring of the Message ID field for Poll Responses. Also, the Supported Options message is a new step in the Net Entry process. It should be noted that all known implementations comply with the proposed changes. |
| Amendment Proposal: | See attached for specific changes to Manual. |
| WG-M Status: | Proposed 5 Oct 04 Revised 19 Oct 04 Accepted 29 Oct 04 with modifications |

The following modifications are needed in the Manual on VDL Mode 3 Implementation Aspects to resolve protocol deficiencies and to harmonize the ICAO standards with the RTCA standards to which the avionics vendors have built and are certifying against.

CHAPTER 3.  FORMATS

3.3.5The meanings of the timing states of TS1, TS2 and TS3 were discussed briefly in 1.4.5 and will be discussed in detail in Chapter 8. Here it is sufficient to note that the normal state of VDL Mode 3 is TS1. The aircraft Local ID consists of a 2-bit prefix (Group ID) plus a 6-bit numerical suffix (Aircraft ID). The 6-bit numbers are used as follows:

| 0 | Reserved for ground station or indication that the net is full |
| --- | --- |
| 1–60 | Available for aircraft users |
| 61 | Discrete addressing not supported/Dummy address |
| 62 | spare |
| 63 | Broadcast |

3.4    M UPLINK FORMATS

3.4.1The M uplink messages consist of the synchronization sequence S2* and 96 bits. Of these, 48 are information bits, which are contained in four (24,12) Golay words. A message is created by assembling four separate words. There are six types of standard words listed below, along with their contents.

Beacon 1

| Message ID | 4 bits |
| --- | --- |
| Voice Signal | 2 bits |
| Aircraft ID (Poll) | 6 bits |

Beacon 2

| Configuration | 4 bits |
| --- | --- |
| Beacon ID | 2 bits |
| Ground Station Code | 3 bits |
| Squelch Window | 3 bits |

Reservation

| Local ID | 8 bits |
| --- | --- |
| Reserved Slot | 4 bits |

ICAO Address (2 words)

| ICAO Address | 24 bits |
| --- | --- |

Next Net 1

| Next Group ID | 2 bits |
| --- | --- |
| Next Frequency | 10 bits |

Next Net 2

| Next Net Type | 1 bit |
| --- | --- |
| Next Ground Station Code | 3 bits |
| Local ID | 8 bits |

Terminate Net

| Terminated Local ID | 8 bits |
| --- | --- |
| Spare | 4 bits |

Supported Options

| Options | 10 bits |
| --- | --- |
| Radio ID | 2 bits |

3.4.2    Beacon 1

3.4.2.1Every uplink M channel message begins with Beacon 1. The initial field of Beacon 1, the MID, identifies the type of information to follow. The first bit of all uplink MIDs is a 0. The remaining bits are described below:

| MID | 0000 | Normal Message |
| --- | --- | --- |
|  | 0001 | Net Entry Response 1: No previous link |
|  | 0010 | Net Entry Response 2: Previous link preserved |
|  | 0011 | Next Net Command |
|  | 0100 | Recovery |
|  | 0101 0110 0111 | Handoff Check Terminate Net Supported Options |
|  | 1000-1111 | Reserved for Downlink Messages |

Note.— There are two separate Net Entry Response messages. If the new ground station is unable to redirect the link from the previous ground station, MID = 0001 is used. If the new ground station can support redirection, MID = 0010 is used. The defined messages will be described more completely below.

3.4.2.3The final part of Beacon 1 is the Aircraft ID (Poll) field. This field is used to poll each of the members of a net in an orderly way. The Local ID suffix of the aircraft user to be polled is the 6-bit Aircraft ID field. For configurations 4V, 3V, 3V1D, the Group ID is the same as the Beacon ID in Beacon 2. For 3T, the Group ID is implied by the position of the Beacon 1 field in the uplink M channel burst. For 3S the Group ID is irrelevant and is arbitrarily set to A = 00. For the wide area coverage slots of 2S1X, the Group ID is also arbitrarily set to A = 00. For 1V3D and 1V2D, the Group ID provides 2-bit extension to the aircraft addressing for up to 240 users.  For 2V2D and 2V1D, each user group has 2 Group IDs available to provide up to 120 users in each net.  Polling is described in more detail in Chapter 4 on protocols.

3.4.3    Beacon 2

3.4.3.1Every uplink M channel message contains a Beacon 2 word that follows Beacon 1. Beacon 2 contains static information that is not expected to change from cycle to cycle. This information is required by radios entering a net. The first field, labelled Configuration, defines how the system is configured in the area covered by the ground transmitter. There can be up to 16 different configurations. Those that have been defined are as follows:

| Configuration | 0000 | 4V |
| --- | --- | --- |
|  | 0001 | 3S |
|  | 0010 | 3V1D |
|  | 0011 | 2V2D |
|  | 0100 | 3T |
|  | 0101 | 3V |
|  | 0110 | 2V1D |
|  | 0111 | 2S1X |
|  | 1000 1001 1010–1111 | 1V3D 1V2D Spare |

Note.— There can be different configurations associated with different ground stations at any given time. It is also possible to provide mixed configurations at a single ground site. For example, a single ground site could support a 2V2D net using slots A and C and two separate 4V nets using slots B and D.

3.4.3.2The field called Beacon ID is normally just the number of the slot in which the beacon is transmitted (A = 00, B = 01, C = 10, D = 11), except for 1V3D/1V2D where it is used for address extension up to 240 and 2V2D/2V1D where it is used to differentiate the 2 nets while doubling the address space to 120. The GSC is a 3-bit number described previously. The Squelch Window is a 3-bit number that is related to the physical size of the volume served by the ground station. More details on the Squelch Window will be found below.

3.4.4.3The exact meaning of the 4-bit Reserved Slot field is as follows:

| 0000 | No reservation information |
| --- | --- |
| 0001 | RACK (UDR Supported) |
| 0010 | RACK (UDR Not Supported) |
| 0011 | Spare |
| 0100 | Data reservation (start in even B slot) |
| 0101 | Data reservation (start in odd B slot) |
| 0110 | Data reservation (start in even B slot, skip D) |
| 0111 | Data reservation (start in odd B slot, skip D) |
| 1000 | Data reservation (start in even C slot) |
| 1001 | Data reservation (start in odd C slot) |
| 1010 | Data reservation (start in even C slot, skip D) |
| 1011 | Data reservation (start in odd C slot, skip D) |
| 1100 | Data reservation (start in even D slot) |
| 1101 | Data reservation (start in odd D slot) |
| 1110 | Voice reservation (start in even D slot) |
| 1111 | Voice reservation (start in odd D slot) |

Note.— For non-3T configurations, use only the codes with the third bit set to 0, except for 0010. For system configuration 2V2D, allowable values are 0000, 0001, 0010, 1000, 1001, 1100, and 1101. For system configuration 3V1D, allowable values are 0000, 0001, 0010, 1100, and 1101. For system configuration 2V1D, allowable values are 0000, 0001, 0010, 1000, and 1001. For configuration 1V3D the allowable values are 0000, 0001, 0010, 0100, 0101, 1000, 1001, 1100, and 1101. For configuration 1V2D the allowable values are 0000, 0001, 0010, 0100, 0101, 1000, and 1001.

.

3.4.7    Terminate net

Terminate Net is used by the ground station to reclaim a Local ID that has previously been assigned.  This is primarily intended to be used when the net is nearly full and the ground station recognizes that some airframes have multiple radios in the net and hence are occupying multiple local IDs.  By use of the Terminate Net message, the ground station can free up sufficient address space so that new aircraft entering the net can access discrete-addresses services.

3.4.8    Supported options

Supported Options is used to complete the net entry process and communicate whether certain options are actively being offered by the ground station.  Currently, the support for Urgent Downlink Request is the only defined option.  The second field of Supported Options is the Radio ID, which is used to differentiate different radio units on an airframe that may be tuned to the same net.  As the DLS sublayer does not have access to the Local ID, the radio ID, passed in the Address Type field of the DLS, along with the ICAO address in the Aircraft Station Address field allows for the unique addressing of the DLS frames, and ensures that aircraft operating multiple radios on the net do not self-jam.

3.4.9    Message types

3.4.9.1This section shows how the various types of uplink messages are constructed.

| Normal Message | (MID = 0000) |
| --- | --- |
| Beacon 1 | 12 bits |
| Beacon 2 | 12 bits |
| Reservation #1 | 12 bits |
| Reservation #2 | 12 bits |

| Net Entry Response | (MID = 0001 or 0010) |
| --- | --- |
| Beacon 1 | 12 bits |
| Beacon 2 | 12 bits |
| ICAO Address | 24 bits |

| Next Net | (MID = 0011) |
| --- | --- |
| Beacon 1 | 12 bits |
| Beacon 2 | 12 bits |
| Next Net 1 | 12 bits |
| Next Net 2 | 12 bits |

| Recovery | (MID = 0100) |
| --- | --- |
| Beacon 1 | 12 bits |
| Beacon 2 | 12 bits |
| Reservation #1 | 12 bits |
| Reservation #2 | 12 bits |
| Terminate Net Beacon 1 Beacon 2 Terminate Net Reservation | (MID = 0110) 12 bits 12 bits 12 bits 12 bits |

| Supported Options Beacon 1 Beacon 2 Reservation Supported Options | (MID = 0111) 12 bits 12 bits 12 bits 12 bits |
| --- | --- |

3.4.9.2The usage of the various uplink M channel message types will be explained in Chapter 4, Protocols.

3.5.3	The Poll Responses and Next Net ACKs consist of the synchronization sequence S2* and 48 bits. Of these 48 bits, 24 are information bits assembled as two (24, 12) Golay words. Included in each message is a 4-bit MID. To distinguish the Poll Responses and Next Net ACKs from the uplink M messages (which also use synchronization sequence S2*), the first bit of all such messages is a 1. The remaining bits are defined as follows:

| MID | 1000 | 4V/3V1D Configuration Poll Response (ALT) |
| --- | --- | --- |
|  | 1001 | 2V2D Configuration Poll Response (ALT) |
|  | 1010 | 1V3D Configuration Poll Response (ALT) |
|  | 1011 | 3T Configuration Poll Response |
|  | 1100 | 3V/3S/2S1X Configuration Poll Response (ALT) |
|  | 1101 | 2V1D Configuration Poll Response (ALT) |
|  | 1110 | 1V2D Configuration Poll Response (ALT) |
|  | 1111 | Next Net Acknowledgment |

Note.— Poll Responses are Alternate Timing Signals (ALT) except in the 3T configuration. The meaning of the designation ALT will be explained in Chapter 8.

3.5.5    Message types

3.5.5.1The various downlink messages are defined below.

| Poll Response (S2*: MID = 1000 - 1110) |
| --- |
| Reservation Request (S1: MID = 1000) |
|  | Message ID | 4 bits |
|  | Local ID | 8 bits |
|  | Ground Station Code | 3 bits |
|  | Voice Request | 2 bits |
|  | Number of Slots Required | 4 bits |
|  | Spare | 1 bit |
|  | Priority | 2 bits |

| Acknowledgment(S1: MID = 1001) |
| --- |
|  | Message ID | 4 bits |
|  | Local ID | 8 bits |
|  | Ground Station Code | 3 bits |
|  | Voice Request | 2 bits |
|  | Spare | 7 bits |

| Next Net ACK (S2*: MID = 1111) |
| --- |
| Leaving Net(S1: MID = 1010) |
|  | Message ID | 4 bits |
|  | Local ID | 8 bits |
|  | Ground Station Code | 3 bits |
|  | All zeros | 9 bits |

| Net Entry Request(S1*: No MID) |
| --- |
|  | ICAO Address | 24 bits |

Note.— Every downlink message (except the Net Entry Request message) contains a MID, a Local ID and a GSC.

3.6    MEDIA ACCESS CONTROL MESSAGE FORMAT SUMMARY

The various message formats described in this chapter are summarized in Tables 3-1, 3-2 and 3-3. (The numbers following the colons represent the number of information bits contained.)

Table 3-1. Burst format summary (M channel uplink)

| Type | Message ID | Sync |  |
| --- | --- | --- | --- |
| Normal Net Entry Response 1 Net Entry Response 2 Next Net Recovery Terminate Net Supported Options | 0000 0001 0010 0011 0100 0110 0111 | S2* S2* S2* S2* S2* S2* S2* | {Beacon 1: 12}{Beacon 2: 12}{Res: 12}{Res: 12} {Beacon 1: 12}{Beacon 2: 12}{ICAO Address: 24} {Beacon 1: 12}{Beacon 2: 12}{ICAO Address: 24} {Beacon 1: 12}{Beacon 2: 12}{Next Net 1: 12}{Next Net 2: 12} {Beacon 1: 12}{Beacon 2: 12}{Res: 12}{Res: 12} {Beacon 1: 12}{Beacon 2: 12}{Terminate: 12} {Res: 12} {Beacon 1: 12}{Beacon 2: 12}{Res: 12}{Opt: 12} |

{ } = Golay Codeword (two words in the case of ICAO address) {Beacon 1: 12} = {(Message ID: 4)(Voice Signal: 2)(Aircraft ID (Poll): 6)} {Beacon 2: 12} = {(Configuration: 4)(Beacon ID: 2)(Ground Station Code: 3)(Squelch Window: 3)} {Next Net 1: 12} = {(Next Group ID: 2)(Next Frequency: 10)} {Next Net 2: 12} = {(Next Net Type: 1)(Next Ground Station Code: 3)(Local ID: 8)} {Reservation: 12} = {(Local ID: 8)(Reserved Slot: 4)} {Terminate: 12} = {(Local ID: 8)(Spare: 4)} {Options: 12} = {(Options:10)(Radio ID: 2)}

Table 3-2. Burst format summary (M channel downlink)

| Type | Message ID | Sync |  |
| --- | --- | --- | --- |
| Res. Request Acknowledgment Leaving Net Poll Response Next Net ACK Net Entry Request | 1000 1001 1010 1000/1010/1100 1111 N/A | S1 S1 S1 S2* S2* S1* | {(Message ID:4)(Local ID: 8)}{(GSC: 3) (Voice Request: 2) (Number of Slots: 4) (Spare: 1)(Priority: 2)} {(Message ID:4)(Local ID: 8)}{(GSC: 3) (Voice Request: 2)(Spare: 7)} {(Message ID:4)(Local ID: 8)}{(GSC: 3)(All 0: 9)} {(Message ID:4)(Local ID: 8)}{(GSC: 3) (Voice Request: 2)(Number of Slots: 4) (Spare: 1)(Priority: 2)} {(Message ID:4)(Local ID: 8)}{(GSC: 3)(Spare: 9)} {ICAO Address: 24} |

3.7.2	The Address Type field indicates the direction of communication as well as indicating whether the address is a point-to-point address or a multicast address. The Address Type also conveys the Radio ID to differentiate multiple radios on a single airframe.  The field is encoded as follows:

| Address Type | 000 | Directed Ground-to-Air (Radio ID=0) |
| --- | --- | --- |
|  | 001 | Directed Air-to-Ground (Radio ID=0) |
|  | 010 | Directed Ground-to-Air (Radio ID=1) |
|  | 011 | Directed Air-to-Ground (Radio ID=1) |
|  | 100 | Directed Ground-to-Air (Radio ID=2) |
|  | 101 | Directed Air-to-Ground (Radio ID=2) |
|  | 110 | Reserved |
|  | 111 | Broadcast Ground-to-Air |

3.7.3	The Frame Type field indicates the use of the frame contents. It is encoded as follows:

| Encoding | Frame Type |
| --- | --- |
| p0p10 | Information (INFO), |
|  | where p0p1 represents the priority encoding |
| 001 | Control-Command (CTRL_CMD) |
| 011 | Control-Response (CTRL_RSP) |
| 101 | spare |
| 111 | Acknowledge (ACK) |

3.9.3    Raw interface

The raw interface is identified by a Network Type field of 2. The Compression Type (CT) field is always set to 0. Immediately following the payload byte is an 8-bit Initial Protocol Identifier (IPI), encoded per ISO 9577.  For an IPI of 0xFF, an 8-bit Extended Initial Protocol Identifier (EIPI) follows.  An EIPI of 0xFF is reserved to delineate ACARS networking over VDL Mode 3.  An EIPI of 0xFE is reserved to delineate FIS-B messaging consistent with RTCA DO-267A.  An EIPI of 0 is reserved to support Minimum Operational Performance Standards (MOPS) testing. This interface could also be used for a dedicated link, if so desired by a given State.

3.10    VOCODER FORMATTING

3.10.1    Bit Exact Algorithm

A proprietary vocoder algorithm developed by DVSI (Digital Voice Systems Incorporated) has been selected for use by the VDL Mode 3 system. DVSI has developed a fixed-point C implementation of the selected vocoder algorithm and a corresponding set of test vectors. The fixed-point C application will be ported by DVSI to processor-specific versions of code that can be delivered to implementers, or implementers can utilize the C reference for their own port.  Each manufacturer will then have to integrate the ported code into its product.  For certification purposes, implementers will wish to use the bit-exact fixed-point implementation available from DVSI.  This implementation provides repeatability of output necessary to satisfy certification of the implementation.

3.10.2    Bit Ordering

Implementers should be aware that the bit ordering specified in Part II, section 8.2.3.1 is nibblewise bit-reversed (every 4 bits reversed) from what DVSI indicates in their reference documentation.

3.10.3    Test Vectors

The DVSI part number for the test vectors and output results is 03-168-1229 rev 1.0 as of October 2003.

- END -