Amendment Proposal

| Title: | Allowed/Disallowed X25 options |
| --- | --- |
| AP working paper number and date | M13/WPx 18 Nov 2008 |
| Document(s) Affected: | Manual on VDL Mode 2 Technical Specifications |
| Document Version: | Doc 9776 |
| Sections of Documents Affected: | Table 6-1, 6-2, 6-3 |
| Coordinator: | Robert Morgenstern |
| Coordinator's Address: | 7515 Colshire Drive, M/S N660 McLean, VA 22102 USA |
| Coordinator's Phone: | +1 703 983 7846 |
| Coordinator's Fax: | +1 703 983 1367 |
| Coordinator's E-mail Address: | rmorgens@mitre.org |
| Category: | BUG |
| Problem description: | Elimination of T24 and T25. Addition of T27 |
| Background: | Cleaning up the removal of T24 and T25 timers |
| Backwards compatibility: | Implementations should have already removed these timers. Just cleaning up the documentation trail. |
| Amendment Proposal: | See below. |
| WG-M Status: | SUBMITTED 11/18/08 |

Table 6-1. Subnetwork layer service system parameters for VDL Mode 2

| Symbol | Name | Minimum | Maximum |  | Mode 2 standard |
| --- | --- | --- | --- | --- | --- |
| T20 | RESTART REQUEST response timer | 1 s | 300 s |  | 180 s |
| T21 | CALL REQUEST response timer | 1 s | 300 s |  | 200 s |
| T22 | RESET REQUEST response timer | 1 s | 300 s |  | 180 s |
| T23 | CLEAR REQUEST response timer | 1 s | 300 s |  | 180 s |
| T27 | REJECT response timer | 1 s | 300 s |  | 180 s |
| R20 | RESTART REQUEST retransmission count | 0 | 7 |  | 1 |
| R22 | RESET REQUEST retransmission count | 0 | 7 |  | 1 |
| R23 | CLEAR REQUEST retransmission count | 0 | 7 |  | 1 |
| R27 | REJECT retransmission count | 0 | 7 |  | 1 |
| P | Packet size | 128 octets | 2 048 octets |  | 1 024 octets |
| W | Transmit window size | 1 packet | 7 packets |  | 7 packets |
| A | Acknowledgment window size | 1 packet | 4 packets |  | 4 packets |
| LTC | Lowest two-way channel | 0 | 4 095 |  | 1 024 |
| HTC | Highest two-way channel | 0 | 4 095 |  | 3 071 |
| Note.— P, W, A values define defaults. Other parameter values are preset and not negotiated. The packet size (P) and window sizes (W, A) define defaults, and may be negotiated during call setup. |

Table 6-2. Facilities supported by the VDL Mode 2

| Facility | ISO 8208 Section |
| --- | --- |
| Packet retransmission | 13.4 |
| Reject response timer (T27 timer) | 13.4.1 |
| Nonstandard default packet sizes | 13.9 |
| Nonstandard default window sizes | 13.1 |
| Flow control parameter negotiation | 13.12 |
| Fast select | 13.16 |
| Fast select acceptance | 13.17 |
| Called line address modified notification | 13.26 |
| Called address extension | 14.2 |

Table 6-3. Facilities not supported by VDL Mode 2

| Facility | ISO 8208 Section |
| --- | --- |
| Q-bit | 6.6 |
| Non-receipt of window rotation information | 11.2 |
| Window status retransmission timer (T24) | 11.2.2 |
| On line facility registration | 13.1 |
| Extended packet seq. numbering | 13.2 |
| D-bit modification | 13.3 |
| Incoming calls barred | 13.5 |
| Outgoing calls barred | 13.6 |
| One-way logical channel outgoing | 13.7 |
| One-way logical channel incoming | 13.8 |
| Default throughput classes assignment | 13.11 |
| Throughput class negotiation | 13.13 |
| Closed user group related facilities | 13.14 |
| Bilateral closed user group related facilities | 13.15 |
| Reverse charging | 13.18 |
| Reverse charging acceptance | 13.19 |
| Local charging prevention | 13.20 |
| Network user identification | 13.21 |
| Charging information | 13.22 |
| RPOA selection | 13.23 |
| Hunt group | 13.24 |
| Call redirection | 13.25 |
| Call redirection notification | 13.27 |
| Transit delay selection and indication | 13.28 |
| Calling address extension | 14.1 |
| Minimum throughput class negotiation | 14.3 |
| End-to-end transit delay negotiation | 14.4 |
| Expedited data negotiation | 14.5 |

# Comments

This deletion approved by AMCP/8