ACP/WGM WP13

Amendment Proposal

| Title: | Options |
| --- | --- |
| AP working paper number and date | M13/WPx 18 Nov 2008 |
| Document(s) Affected: | Manual on VDL Mode 2 Technical Specifications |
| Document Version: | Doc 9776 |
| Sections of Documents Affected: | Table 5-46a,b,c |
| Coordinator: | Robert Morgenstern |
| Coordinator's Address: | 7515 Colshire Drive, M/S N660 McLean, VA 22102 USA |
| Coordinator's Phone: | +1 703 983 7846 |
| Coordinator's Fax: | +1 703 983 1367 |
| Coordinator's E-mail Address: | rmorgens@mitre.org |
| Category: | BUG |
| Problem description: | Conflict with standard and AEEC/current implementations on supported parameters. |
| Background: | The HDLC options and System mask parameters are now mandatory where applicable. There is also the addition of the Airport coverage parameter to support some of the multiple frequency solutions, as well as the aircraft location/destination airport. |
| Backwards compatibility: | Some older units may not support now mandatory parameters. |
| Amendment Proposal: | See below. |
| WG-M Status: | SUBMITTED 11/18/08 |

Table 5-46a). XID parameters

|  |  | GSIF | Air initiated link establishment | Link parameter modification |
| --- | --- | --- | --- | --- |
|  | Source address | Ground station | Aircraft | New ground station | Current ground station | Aircraft |
|  | Destination address | All aircraft | Proposed ground station | Aircraft | Aircraft | Current ground station |
| XID parameters | GI | PI | GSIF (P=0) | XID_CMD_LE (P=1) | XID_RSP_LE (F=1) | XID_CMD_LPM (P=1) | XID_RSP_LPM (F=1) |
| Public parameters |  |  |  |  |  |  |  |
| Parameter set ID | 80h | 01h | M | M | M | N/A | N/A |
| Procedure classes | 80h | 02h | M | M | M | N/A | N/A |
| HDLC options | 80h | 03h | M | M | M | N/A | N/A |
| N1-downlink | 80h | 05h | O | N/A | O | N/A | N/A |
| N1-uplink | 80h | 06h | O | N/A | O | N/A | N/A |
| k-downlink | 80h | 07h | O | N/A | O | N/A | N/A |
| k-uplink | 80h | 08h | O | N/A | O | N/A | N/A |
| Timer T1 _ downlink | 80h | 09h | O | N/A | O | N/A | N/A |
| Counter N2 | 80h | 0Ah | O | N/A | O | N/A | N/A |
| Timer T2 | 80h | 0Bh | O | N/A | O | N/A | N/A |
| Private parameters |  |  |  |  |  |  |  |
| Parameter set ID | F0h | 00h | M | M | M | M | M |
| Connection management | F0h | 01h | N/A | M | M | N/A | N/A |
| SQP | F0h | 02h | N/A | O | O | O | O |
| XID sequencing | F0h | 03h | N/A | M | M | M | M |
| AVLC specific options | F0h | 04h | M | M | M | N/A | N/A |
| Expedited SN connection | F0h | 05h | N/A | O | O | N/A | N/A |
| LCR cause | F0h | 06h | N/A | N/A | N/A | N/A | N/A |
| Modulation support | F0h | 81h | N/A | M | N/A | N/A | N/A |
| Alternate ground stations | F0h | 82h | N/A | O | O | N/A | N/A |
| Destination airport | F0h | 83h | N/A | M3 | N/A | N/A | N/A |
| Aircraft location | F0h | 84h | N/A | M3 | N/A | N/A | N/A |
| Autotune frequency | F0h | 40h | N/A | N/A | O | N/A | N/A |
| Repl. ground station | F0h | 41h | N/A | N/A | O | N/A | N/A |
| Timer T4 | F0h | 42h | O | N/A | O | O | N/A |
| MAC persistence | F0h | 43h | O | N/A | O | O | N/A |
| Counter M1 | F0h | 44h | O | N/A | O | O | N/A |
| Timer TM2 | F0h | 45h | O | N/A | O | O | N/A |
| Timer TG5 | F0h | 46h | O | N/A | O | O | N/A |
| Timer T3min | F0h | 47h | O | N/A | O | N/A | N/A |
| Address filter | F0h | 48h | N/A | N/A | N/A | N/A | N/A |
| Broadcast connection | Foh | 49h | N/A | N/A | N/A | N/A | N/A |
| Frequency support | F0h | C0h | O | N/A | O | N/A | N/A |
| Airport coverage | F0h | C1h | M1 | N/A | O2 | N/A | N/A |
| Nearest airport ID | F0h | C3h | M1 | N/A | O2 | N/A | N/A |
| ATN router NETs | F0h | C4h | M | N/A | M | N/A | N/A |
| System mask | F0h | C5h | M | N/A | M | N/A | N/A |
| TG3 | F0h | C6h | O | N/A | O | N/A | N/A |
| TG4 | F0h | C7h | O | N/A | O | N/A | N/A |
| Ground station location | F0h | C8h | M | N/A | O | N/A | N/A |
| GI = ISO 8885 Group identifier PI = ISO 8885 Parameter identifier M = Mandatory O = Optional N/A = Not applicable h = hexadecimal NOTES.— 1. In a GSIF XID frame it is mandatory to include either the Airport Coverage Indication parameter or the Nearest Airport Identifier parameter but not both (see 5.4.2.7.3). 2. Where the Airport Coverage Indication parameter and the Nearest Airport Identifier parameter are marked as optional, either parameter may be included in the frame or neither but not both. 3. Presence of this field is mandated only when valid data is available. In the absence of valid data, the parameter shall be omitted. |

Table 5-46b). XID parameters

|  |  | Ground initiated handoff | Air initiated handoff |
| --- | --- | --- | --- |
|  | Source address | Proposed ground station | Aircraft | Aircraft | New ground station |
|  | Destination address | Aircraft | New ground station | Proposed ground station | Aircraft |
| XID parameters | GI | PI | XID_CMD_HO (P=1) | XID_RSP_HO (F=1) | XID_CMD_HO (P=1) | XID_RSP_HO (F=1) |
| Public parameters |  |  |  |  |  |  |
| Parameter set ID | 80h | 01h | M | M | M | M |
| Procedure classes | 80h | 02h | M | M | M | M |
| HDLC options | 80h | 03h | M | M | M | M |
| N1-downlink | 80h | 05h | O | N/A | N/A | O |
| N1-uplink | 80h | 06h | O | N/A | N/A | O |
| k-downlink | 80h | 07h | O | N/A | N/A | O |
| k-uplink | 80h | 08h | O | N/A | N/A | O |
| Timer T1 - downlink | 80h | 09h | O | N/A | N/A | O |
| Counter N2 | 80h | 0Ah | O | N/A | N/A | O |
| Timer T2 | 80h | 0Bh | O | N/A | N/A | O |
| Private parameters |  |  |  |  |  |  |
| Parameter set ID | F0h | 00h | M | M | M | M |
| Connection management | F0h | 01h | M | M | M | M |
| SQP | F0h | 02h | O | O | O | O |
| XID sequencing | F0h | 03h | M | M | M | M |
| AVLC specific options | F0h | 04h | O | O | O | O |
| Expedited SN connection | F0h | 05h | X | X | O | O |
| LCR cause | F0h | 06h | N/A | N/A | N/A | N/A |
| Modulation support | F0h | 81h | N/A | N/A | N/A | N/A |
| Alternate ground stations | F0h | 82h | N/A | N/A | O | N/A |
| Destination airport | F0h | 83h | N/A | O | O | M3 |
| Aircraft location | F0h | 84h | N/A | O | O | M3 |
| Autotune frequency | F0h | 40h | N/A | N/A | N/A | O |
| Repl. ground station | F0h | 41h | O | N/A | N/A | O |
| Timer T4 | F0h | 42h | O | N/A | N/A | O |
| MAC persistence | F0h | 43h | O | N/A | N/A | O |
| Counter M1 | F0h | 44h | O | N/A | N/A | O |
| Timer TM2 | F0h | 45h | O | N/A | N/A | O |
| Timer TG5 | F0h | 46h | O | N/A | N/A | O |
| Timer T3min | F0h | 47h | O | N/A | N/A | O |
| Address filter | F0h | 48h | N/A | N/A | N/A | N/A |
| Broadcast connection | F0h | 49h | N/A | N/A | N/A | N/A |
| Frequency support | F0h | C0h | O | N/A | N/A | O |
| Airport coverage | F0h | C1h | O2 | N/A | N/A | O2 |
| Nearest airport ID | F0h | C3h | O2 | N/A | N/A | O2 |
| ATN router NETs | F0h | C4h | M | N/A | N/A | O |
| System mask | F0h | C5h | M | N/A | N/A | M |
| TG3 | F0h | C6h | O | N/A | N/A | O |
| TG4 | F0h | C7h | O | N/A | N/A | O |
| Ground station location | F0h | C8h | O | N/A | N/A | O |
| GI = ISO 8885 Group identifier PI = ISO 8885 Parameter identifier M = Mandatory O = Optional N/A = Not applicable h = hexadecimal NOTES.— 1. In a GSIF XID frame it is mandatory to include either the Airport Coverage Indication parameter or the Nearest Airport Identifier parameter but not both (see 5.4.2.7.3). 2. Where the Airport Coverage Indication parameter and the Nearest Airport Identifier parameter are marked as optional, either parameter may be included in the frame or neither but not both. 3. Presence of this field is mandated only when valid data is available. In the absence of valid data, the parameter shall be omitted. |

Table 5-46c). XID parameters

|  |  | Air requested handoff | Ground requested handoff | Ground requested broadcast | Link connection rejection |
| --- | --- | --- | --- | --- | --- |
|  | Source address | Aircraft | Current ground station | New ground station | Any station |
|  | Destination address | Current or proposed ground station | Aircraft | All aircraft | Any station |
| XID parameters | GI | PI | XID_CMD_HO (P=0 | XID_CMD_HO (P=0) | XID_CMD_HO (P=0) | XID_RSP_LCR XID_CMD_LCR |
| Public parameters |  |  |  |  |  |  |
| Parameter set ID | 80h | 01h | N/A | M | M | N/A |
| Procedure classes | 80h | 02h | N/A | M | M | N/A |
| HDLC options | 80h | 03h | N/A | M | M | N/A |
| N1-downlink | 80h | 05h | N/A | O | O | N/A |
| N1-uplink | 80h | 06h | N/A | O | O | N/A |
| k-downlink | 80h | 07h | N/A | O | O | N/A |
| k-uplink | 80h | 08h | N/A | O | O | N/A |
| Timer T1 - downlink | 80h | 09h | N/A | O | O | N/A |
| Counter N2 | 80h | 0Ah | N/A | O | O | N/A |
| Timer T2 | 80h | 0Bh | N/A | O | O | N/A |
| Private parameters |  |  |  |  |  |  |
| Parameter set ID | F0h | 00h | M | M | M | M |
| Connection management | F0h | 01h | M | M | M | M |
| SQP | F0h | 02h | N/A | N/A | N/A | N/A |
| XID sequencing | F0h | 03h | M | M | M | M |
| AVLC specific options | F0h | 04h | N/A | O | O | N/A |
| Expedited SN connection | F0h | 05h | N/A | N/A | N/A | N/A |
| LCR cause | F0h | 06h | N/A | N/A | N/A | M |
| Modulation support | F0h | 81h | N/A | N/A | N/A | N/A |
| Alternate ground stations | F0h | 82h | O | N/A | N/A | N/A |
| Destination airport | F0h | 83h | O | N/A | N/A | N/A |
| Aircraft location | F0h | 84h | O | N/A | N/A | N/A |
| Autotune frequency | F0h | 40h | N/A | O | N/A | N/A |
| Repl. ground station | F0h | 41h | N/A | O | N/A | N/A |
| Timer T4 | F0h | 42h | N/A | O | O | N/A |
| MAC persistence | F0h | 43h | N/A | O | O | N/A |
| Counter M1 | F0h | 44h | N/A | O | O | N/A |
| Timer TM2 | F0h | 45h | N/A | O | O | N/A |
| Timer TG5 | F0h | 46h | N/A | O | O | N/A |
| Timer T3min | F0h | 47h | N/A | O | O | N/A |
| Address filter | F0h | 48h | N/A | N/A | M | N/A |
| Broadcast connection | F0h | 49h | N/A | N/A | M | N/A |
| Private parameters |  |  |  |  |  |  |
| Frequency support | F0h | C0h | N/A | O | O | N/A |
| Airport coverage | F0h | C1h | N/A | N/A | O2 | N/A |
| Nearest airport ID | F0h | C3h | N/A | N/A | O2 | N/A |
| ATN router NETs | F0h | C4h | N/A | M | M | N/A |
| System mask | F0h | C5h | N/A | M | M | N/A |
| TG3 | F0h | C6h | N/A | O | O | N/A |
| TG4 | F0h | C7h | N/A | O | O | N/A |
| Ground station location | F0h | C8h | N/A | O | O | N/A |
| GI = ISO 8885 Group identifier PI = ISO 8885 Parameter identifier M = Mandatory O = Optional N/A = Not applicable h = hexadecimal NOTES.— 1. In a GSIF XID frame it is mandatory to include either the Airport Coverage Indication parameter or the Nearest Airport Identifier parameter but not both (see 5.4.2.7.3). 2. Where the Airport Coverage Indication parameter and the Nearest Airport Identifier parameter are marked as optional, either parameter may be included in the frame or neither but not both. |