Amendment Proposal

| Title: | Called Line Address Modification Notification |
| --- | --- |
| AP working paper number and date | M13/WPx 18 Nov 2008 |
| Document(s) Affected: | Manual on VDL Mode 2 Technical Specifications |
| Document Version: | Doc 9776 |
| Sections of Documents Affected: | 6.6.3 |
| Coordinator: | Robert Morgenstern |
| Coordinator's Address: | 7515 Colshire Drive, M/S N660 McLean, VA 22102 USA |
| Coordinator's Phone: | +1 703 983 7846 |
| Coordinator's Fax: | +1 703 983 1367 |
| Coordinator's E-mail Address: | rmorgens@mitre.org |
| Category: | BUG |
| Problem description: | Ensuring the aircraft uses the VSDA address in the call request packet |
| Background: | Service provider implementations are simplified if they can be assured of the inclusion of the VSDA in all CALL REQUEST packets. |
| Backwards compatibility: | Older implementations might have chosen to not include the VSDA in some scenarios. |
| Amendment Proposal: | See below. |
| WG-M Status: | SUBMITTED 11/18/08 |

Insert new:

6.6.3.4  Call Redirection for X.121-based Networks. Even if the ground network supports X.121 addressing, the aircraft shall generate the new Call Request with the VSDA address of the specific air-ground router in the address extension field of the Called Address Extension facility.  For JOIN and HANDOFF operations, the aircraft station shall always generate a Call Request using a VSDA address in the Called Address Extension facility

If the addressed air-ground router is not reachable from the ground station, the ground system shall redirect the call to a different air-ground router DTE and inform the aircraft about the call redirection using the Called Line Address Modification Notification (CLAMN) facility specified in Section 6.6.3.3.

Note. — A CLAMN facility can be used to modify the address for reasons other than redirection.

Call redirection shall only be used in case of faults related to the air-ground router.  The ground system shall only redirect a call to another address within the same routing domain (i.e., same Air-Ground Router).