Amendment Proposal

| Title: | Broadcast aircraft address |
| --- | --- |
| AP working paper number and date | M13/WPx 18 Nov 2008 |
| Document(s) Affected: | Manual on VDL Mode 2 Technical Specifications |
| Document Version: | Doc 9776 |
| Sections of Documents Affected: | 5.3.3.4 |
| Coordinator: | Robert Morgenstern |
| Coordinator's Address: | 7515 Colshire Drive, M/S N660 McLean, VA 22102 USA |
| Coordinator's Phone: | +1 703 983 7846 |
| Coordinator's Fax: | +1 703 983 1367 |
| Coordinator's E-mail Address: | rmorgens@mitre.org |
| Category: | BUG |
| Problem description: | An aircraft station configured with the ground broadcast address of all 1s can have a deleterious effect upon the system. A requirement is needed to minimize the risk of this occurring |
| Background: | During Link 2000 operations, aircraft have been detected that have been misconfigured by the operator to an all-1s address, which caused network issues with the system. |
| Backwards compatibility: | Not an issue, beyond older systems still being a risk. |
| Amendment Proposal: | See below. |
| WG-M Status: | SUBMITTED 11/18/08 |

Insert new:

5.3.3.4.2  Erroneous Transmission. The aircraft station shall not transmit VDL frames if the 24-bit ICAO aircraft address is configured with the all ones broadcast address.

5.3.3.4.3  Erroneous Reception. The ground station shall discard without response any received frames containing a 24-bit source address of all ones.