|  | International Civil Aviation Organization WORKING PAPER | ACP-WGN14/WP-04 02/06/09 |
| --- | --- | --- |

AERONAUTICAL COMMUNICATIONS PANEL (ACP)

FOURTEENTH MEETING OF WORKING GROUP - M

Brussels, Belgium 2 – 5 June 2009

| Agenda Item 4: | Maintenance of VDL Mode-2 Documents |
| --- | --- |

Amendment Proposal #1

(Presented by Robert Morgenstern

SUMMARY

Table attached

ACTION

Consider amendment

Amendment Proposal

| Title: | GRAIHO FSL |
| --- | --- |
| AP working paper number and date | M14/WPx 2 Jun 2009 |
| Document(s) Affected: | Manual on VDL Mode 2 Technical Specifications |
| Document Version: | Doc 9776 with AP-M13/WP13bis included |
| Sections of Documents Affected: | Table 5-46c |
| Coordinator: | Robert Morgenstern |
| Coordinator's Address: | 7515 Colshire Drive, M/S N660 McLean, VA 22102 USA |
| Coordinator's Phone: | +1 703 983 7846 |
| Coordinator's Fax: | +1 703 983 1367 |
| Coordinator's E-mail Address: | rmorgens@mitre.org |
| Category: | BUG |
| Problem description: | GRAIHO XID allows for Frequency Support XID yet prohibits associated Airport Coverage or Nearest Airport ID XID, which would be needed to identify the associated airport. |
| Background: | During implementation of recent AEEC 631-5 changes, one of the vendors recognized an inconsistency associated with Frequency Support List (FSL) with relation to the Ground Requested Air Initiated Hand off (GRAIHO) allowing the inclusion of the FSL parameter, but not either the Airport Coverage or Nearest Airport ID parameter, which go with the FSL with the recent standard updates. Upon discussion between the implementers at AEEC DLK, it was decided that allowing the FSL in a message requesting the aircraft go somewhere else seemed a waste a bandwidth. As such, it is proposed to remove the FSL from the GRAIHO XID. |
| Backwards compatibility: | Aircraft would be capable of processing an optional parameter that would not be sent. If the ground station is out of date, it might potentially include the message which might cause an aircraft to reject the XID, depending on the implementation. Ultimately, the GS would not likely add the parameter as it doesn’t have a means to identify the associated airport for the FSL-based handoff. |
| Amendment Proposal: | See below. |
| WG-M Status: | SUBMITTED 5/28/09 |

Table 5-46c). XID parameters

|  |  | Air requested handoff | Ground requested handoff | Ground requested broadcast | Link connection rejection |
| --- | --- | --- | --- | --- | --- |
|  | Source address | Aircraft | Current ground station | New ground station | Any station |
|  | Destination address | Current or proposed ground station | Aircraft | All aircraft | Any station |
| XID parameters | GI | PI | XID_CMD_HO (P=0 | XID_CMD_HO (P=0) | XID_CMD_HO (P=0) | XID_RSP_LCR XID_CMD_LCR |
| Public parameters |  |  |  |  |  |  |
| Parameter set ID | 80h | 01h | N/A | M | M | N/A |
| Procedure classes | 80h | 02h | N/A | M | M | N/A |
| HDLC options | 80h | 03h | N/A | M | M | N/A |
| N1-downlink | 80h | 05h | N/A | O | O | N/A |
| N1-uplink | 80h | 06h | N/A | O | O | N/A |
| k-downlink | 80h | 07h | N/A | O | O | N/A |
| k-uplink | 80h | 08h | N/A | O | O | N/A |
| Timer T1 - downlink | 80h | 09h | N/A | O | O | N/A |
| Counter N2 | 80h | 0Ah | N/A | O | O | N/A |
| Timer T2 | 80h | 0Bh | N/A | O | O | N/A |
| Private parameters |  |  |  |  |  |  |
| Parameter set ID | F0h | 00h | M | M | M | M |
| Connection management | F0h | 01h | M | M | M | M |
| SQP | F0h | 02h | N/A | N/A | N/A | N/A |
| XID sequencing | F0h | 03h | M | M | M | M |
| AVLC specific options | F0h | 04h | N/A | O | O | N/A |
| Expedited SN connection | F0h | 05h | N/A | N/A | N/A | N/A |
| LCR cause | F0h | 06h | N/A | N/A | N/A | M |
| Modulation support | F0h | 81h | N/A | N/A | N/A | N/A |
| Alternate ground stations | F0h | 82h | O | N/A | N/A | N/A |
| Destination airport | F0h | 83h | O | N/A | N/A | N/A |
| Aircraft location | F0h | 84h | O | N/A | N/A | N/A |
| Autotune frequency | F0h | 40h | N/A | O | N/A | N/A |
| Repl. ground station | F0h | 41h | N/A | O | N/A | N/A |
| Timer T4 | F0h | 42h | N/A | O | O | N/A |
| MAC persistence | F0h | 43h | N/A | O | O | N/A |
| Counter M1 | F0h | 44h | N/A | O | O | N/A |
| Timer TM2 | F0h | 45h | N/A | O | O | N/A |
| Timer TG5 | F0h | 46h | N/A | O | O | N/A |
| Timer T3min | F0h | 47h | N/A | O | O | N/A |
| Address filter | F0h | 48h | N/A | N/A | M | N/A |
| Broadcast connection | F0h | 49h | N/A | N/A | M | N/A |
| Private parameters |  |  |  |  |  |  |
| Frequency support | F0h | C0h | N/A | N/A | O | N/A |
| Airport coverage | F0h | C1h | N/A | N/A | O2 | N/A |
| Nearest airport ID | F0h | C3h | N/A | N/A | O2 | N/A |
| ATN router NETs | F0h | C4h | N/A | M | M | N/A |
| System mask | F0h | C5h | N/A | M | M | N/A |
| TG3 | F0h | C6h | N/A | O | O | N/A |
| TG4 | F0h | C7h | N/A | O | O | N/A |
| Ground station location | F0h | C8h | N/A | O | O | N/A |
| GI = ISO 8885 Group identifier PI = ISO 8885 Parameter identifier M = Mandatory O = Optional N/A = Not applicable h = hexadecimal NOTES.— 1. In a GSIF XID frame it is mandatory to include either the Airport Coverage Indication parameter or the Nearest Airport Identifier parameter but not both (see 5.4.2.7.3). 2. Where the Airport Coverage Indication parameter and the Nearest Airport Identifier parameter are marked as optional, either parameter may be included in the frame or neither but not both. |